Figures and programs included in this Sample Chapter:

Figures:

Figure 3-1. Organization of Screen Memory for Monochrome Display.
Figure 3-2 Organization of Color Screen Memory
Figure 3-3. Cartesian Coordinate System
Figure 3-4 Polar Coordinate System
Figure 3-5. Raster Coordinate System
Figure 3-6. Normalized Device Coordinate (NDC) System
Figure 3-7. The Mandelbrot Primitive
Figure 3-8. Mandelbrot Figure
Figure 3-9. ANother Segment of the Mandelbrot Boundary.





Programs:

Program 3-1. LINEDRAW.PRG
Program 3-2  STRING.BAS
Program 3-3. KALEIDO.BAS
Program 3-4. DRAGON.BAS
Program 3-5. MANDELBROT.BAS
Program 3-6. NEOWRITE.BAS
Program 3-7. NEOLOAD.BAS



Chapter 3

ST Graphics

During the late 1950s and early 1960s, the Massachusetts Institute 
of  Technoloy (MIT) was the center of the computer world, an 
academic community actively involved in the research and 
construction of supercomputer systems.
     In 1963, Ivan Sutherland, a young graduate student working on 
his doctoral dissertation at MIT, could often be seen working far 
into the night at the terminal of a giant mainframe computer.  He 
wasn't alone in his labors. Other students doing research on 
computers had to use the late-night hours, when the mainframes 
weren't being used for other purposes, for exploring the limits of 
this fledgling science of computers; the technology  for 
microcomputers  had not even been developed.
    Sutherland wrote and rewrote his lines of code.  After much 
revision, he was finally successful.  The monitor display cleared, 
and a green line appeared:  The first computer graphic, a straight 
line, had been produced by the giant mainframe.  Not much by 
today's standards, but this occasion marked the beginning of a 
whole new art form --computer graphics.
     This single straight line evolved into the Sketchpad line-
drawing  program.  Sutherland's early drawing program allowed the 
user to point at the screen with a light pen to sketch objects. 
This simple system was the predecessor of today's complex 
computer-assisted drawing (CAD) programs.
     A lot had to happen to computers, however, before 
sophisticated computer graphics could become a reality. For a 
while computers remained the expensive tools of government and 
universities. In 1965, IBM introduced the first mass-produced 
cathode ray tube (CRT), but the price was more than $100,000 for 
the CRT only.  This price tag made entry into computer graphics 
practically impossible for all but a few specialized users. In 
1968, Tektronics introduced the storage-tube CRT, which displayed 
a drawing by retaining the image until the user replaced it. This 
type of display eliminated the need for costly memory and hardware 
to store and display the image, but the selling price of $15,000 
still placed the CRT far beyond the means of most users.
   It wasn't until the late 1970s and early 1980s that the 
microcomputer industry exploded, and computer wars brought the 
price and power of the personal computer within the reach of the 
middle-income person.
     Soon, powerful graphics programs such as DEGAS and NEOchrome 
had introduced many people to this new art form, and some even 
discovered hidden talents. And now that computer art has become 
accessible to so many people, those people want to make the best 
possible use of its potential.
     In this chapter, we'll take you beyond DEGAS and NEOchrome, 
showing you how to develop and use the powerful graphics routines 
built into the ST. Previously, exploitation of these features was 
rather difficult. Most programmers resorted to C or assembly 
language programming when sophisticated graphics were required. 
GFA BASIC delivers the power to fully utilize the graphics 
potential of your ST. Stunning graphics are easily obtained using 
the GFA BASIC interpreter, while the GFA BASIC compiler allows you 
to develop arcade-quality games in BASIC, then execute the 
programs from the GEM Desktop with your program running at speeds 
rivaling those of assembly language.

Computer Graphics

     Computer graphics is a generic term which refers to any image 
created with a computer. This covers a wide range, from a simple 
line on a monitor, to intricate pictures developed with drawing 
programs, and more. Some computer scientists, for instance, are 
using computers to control lasers which produce holographic 
images. Perhaps the scene from Star Wars where C3PO and Chew-baka 
are playing a chesslike game with holographic images isn't even 
that far-fetched.
     The motion picture industry, in recent years, has used 
computer graphics extensively. The transformation of the Genesis 
planet in Star Trek II, The Wrath of Khan, was an effect produced 
with fractal graphics --one of the most fascinating areas of 
computer graphics (and one which we'll explore later in this 
chapter). Disney Studios merged real action with computer-
generated graphics in the movie TRON. The Last Starfighter has 25 
minutes of spectacular computer imagery, with each frame requiring 
dozens of algorithms and hundreds of intricate designs. In fact, 
such movies have contributed to the birth of a new industry 
devoted to enhancing computer-generated graphics technology, with 
one of the leaders in this new industry being Lucasfilm, a pioneer 
in special effects since the Star Wars trilogy.
     Although holographic imaging and Hollywood-type special 
effects are beyond the scope of this book, it will show you a 
fascinating world open to those who know the power of the ST.


Graphics Capabilities

Good graphics require a minimum of a high-resolution display and a 
large number of colors to work with. Some rumors are beginning to 
circulate about computers for homes and businesses with monitors 
capable of displaying up to one million --1000  X  1000 --pixels. 
Currently only dedicated graphics workstations, such as the Sun or 
the Cray II, offer such capabilities, and both of these are priced 
far beyond the home enthusiast's budget.  Although the ST doesn't 
have the capabilities of a dedicated graphics workstation, it is 
capable of displaying up to 256,000 pixels, for a fraction of the 
cost. Plus, the palette of 512 colors makes it ideal for producing 
colorful, exciting displays.
   In order to program graphics on the ST, it's necessary to 
understand a little about the way the screen is displayed. On the 
monochrome screen, each pixel (picture element) is represented by 
a single bit of memory.  Each bit will be either a 0 or a 1, 
indicating whether each pixel is off or on, respectively. Screen 
memory is organized so that the first byte represents the 8 
pixels, or dots, at the top left corner of the screen. Each 
succeeding byte represents the next 8 pixels in succession. Each 
screen line consists of 640 pixels, so the first 80 bytes (80 
times 8) represent the top row of the screen. Since there are 400 
lines of pixels vertically on the screen, a total of 256,000 bits 
are used to represent the monochrome screen. This means that 
32,000 bytes of screen memory are used to store the display.

Binary Decimal
 00    0
 01    1
 10    2
 11    3

Figure 3-1 Organization of Screen Memory for Monochrome Display.

    Color  screen  memory is organized in much  the  same  way  as 
monochrome screen memory, but instead of single bits representing 
single pixels, groups of bits are used to represent each pixel. In 
medium resolution, a pixel may be one of four colors. Two bits are 
used to create the four possible colors:
   The first byte of screen memory represents the first four 
pixels at the upper left corner of the screen. The two high-order 
bits specify the color in the first pixel, the next two bits 
represent the color in the second pixel, and so on. There are 640 
pixels per row; each row requires 160 bytes of memory. Since there 
are only 200 vertical rows of pixels, only 32,000 bytes of memory 
are necessary to store a screen.
   In low resolution, a pixel can be one of 16 colors, so four 
bits are required to represent a single pixel.

0000 = 0        1000 = 8
0001 = 1        1001 = 9
0010 = 2        1010 = 10
0011 = 3        1011 = 11
0100 = 4        1100 = 12
0101 = 5        1101 = 13
0110 = 6        1110 = 14
0111 = 7        1111 = 15

    Each  byte describes the color of only 2  pixels.  But  again, 
since there are only 320 pixels per line, and 200 vertical lines, 
only 32,000 bytes are required to represent a full screen.

Figure 3-2 Organization of Color Screen Memory

   As mentioned previously, the ST is capable of displaying 512 
colors, but only 16 colors may be displayed at one time (in low 
resolution). Each value stored in color memory corresponds to a 
hardware color register.
     In GFA BASIC, the command COLOR defines the color to be used 
by a graphics command. If you do not specify a color before a 
graphics command, either the default color or the color last used 
is selected. Usually, the default color is color 1, which has a 
default value of black, 0.

Graphics Programming Techniques

Entire  books  have  been  written about  the  various  phases  of 
computer graphics. Each section of this chapter could be dealt 
with in much greater detail. Instead, we're going to introduce 
you, quickly and painlessly, to graphics techniques, point you in 
the right direction, and then leave you to the excitement of 
discovery as you explore this world with your staunch ally, GFA 
BASIC.
   As with any voyage, some preliminary attention to detail must 
be undertaken. After all, to use the graphics commands, you must 
at least be able to tell the computer where you want the object 
you're drawing to appear.
     There are several coordinate systems in use, but the two most 
common are the Cartesian coordinate system and the polar 
coordinate system.
     In the Cartesian coordinate system, the two-dimensional plane 
is assigned two axes: the horizontal axis, usually labeled x, and 
the vertical axis, €usually labeled y. By convention, the positive 
direction of the x-axis is to the right, but the positive 
direction of the y-axis can be either up or down, depending on the 
application. In geometry and most other mathematical applications, 
the positive direction of the y-axis is up, but on most computer 
systems, the positive direction is down. Points in the plane are 
represented by ordered pairs (x,y), where x is the distance of the 
point from the y-axis and y is the distance of the point from the 
x-axis. The point (0,0) is called the origin because it is the 
point where the x and y axes intersect, the point from which all 
other points in the plane are located.
  The location of the origin is another disputed aspect of the 
Cartesian coordinate system. In geometry, the origin is 
traditionally located in the lower left corner of the display with 
the positive x and y axes extending toward the right and top of 
the display, respectively. However, on most computers, the origin 
is located in the upper left corner of the screen, because of the 
way the monitor draws the display. Another possible location for 
the origin is the center of the display. This orientation makes it 
easy to graph both negative as well as positive values -- 
something the other two systems ignore. Either of these locations 
is equally valid, and conversion from one orientation to the other 
is simple, so the choice of which system to use is usually left up 
to the user.


Figure 3-3. Cartesian Coordinate System



Figure 3-4 Polar Coordinate System


   The Cartesian coordinate system cooresponds closely with the 
real world, which makes it ideal for most applications, but in 
situations where rotation is necessary, the Cartesian coordinate 
system is difficult to use.    Two systems of referencing are in 
common use with computers: the normalized device coordinate (NDC) 
system, and the raster coordinate (RC) system

. The NDC system addresses the graphics display independent of the 
device's display size, while the RC system addresses the device in 
actual display units. The RC system is the system used on most 
microcomputers. With this system, the screen is divided into rows 
and columns of dots, or pixels. The pixels in the top row have a 
vertical, or y, coordinate of 0. The y coordinate increases as you 
move toward the bottom of the screen. The bottom row of the screen 
has a y coordinate value of 199 on a color system and 399 on a 
monochrome system. The leftmost column of pixels has a horizontal, 
or x, coordinate of 0.

     The x coordinate increases as you move toward the right edge 
of the display, where each pixel in the rightmost column has the 
value of 319 on color systems in low resolution and 639 in medium 
or high resolution.
               Figure 3-5. Raster Coordinate System



     The ST also supports the NDC system. It's difficult to write 
a single program that will work with the different types of 
devices, because almost every graphics output device has a 
different maximum horizontal and vertical resolution. That's where 
the NDC system becomes expedient.
   The NDC system offers the programmer a means by which graphics 
drawn on one computer screen or printer will look the same when 
drawn on other computer screens or printers of different 
resolutions. With the NDC system, all graphics output is sent to 
an imaginary device that is 32,768 pixels wide and 32,768 pixels 
high. These pixels are grouped differently from those under the RC 
system. The y axis begins with 0 at the bottom of the screen, and 
moves up to the top row of pixels numbering 32,767. As in the RC 
system, the x axis is numbered from left to right. The leftmost 
column of pixels is 0, and the rightmost column is 32,767.
   Two coordinate-referencing systems on one computer may seem 
difficult to grasp, but usually you'll only be dealing with the RC 
system in GFA BASIC. You should be aware of the NDC system, as it 
does have value with GDOS and some VDI functions.

Figure 3-6. Normalized Device Coordinate (NDC) System


Resolving a problem

     The ST may be configured in low resolution (320x200 pixels) 
and medium resolution (640x200 pixels) with a color monitor, or in 
high resolution (640x400 pixels) with a monochrome monitor. It's 
very easy to include a simple check for the resolution mode, then 
use program modules applicable for th resolution. It's even 
possible to affect a change of resolution from GFA BASIC by using 
an XBIOS function. At the very least, you should include a check 
in your program to determine which mode of resolution the computer 
is displaying. If necessary, you can then display an Alert box 
informing the user that the program requires a different 
resolution. Good programming practice dictates that your program 
be compatible with different systems, if possible. Especially with 
programs that use graphics, the effect you've labored to create 
will be lost if the proper mode of resolution isn't selected.
   XBIOS is a group of extended input/output functions which are 
available to the programmer. For more information about XBIOS 
routines, refer to Appendix F. GFA BASIC makes these functions 
available to you by using the same bindings as those used by 
programmers working in C. Refer to Appendix F for a list of the 
XBIOS functions and bindings.
   To check the resolution of a system, XBIOS 4, called getrez in 
most literature about the ST, can be used.

PROCEDURE check_rez
 '
 rez=XBIOS(4)
 '
RETURN

   This  procedure  will  return  the  screen  resolution  in  the 
variable, rez:

0 = low resolution (320x200, 16 colors)
1 = medium resolution (640x200, 4 colors)
2 = high resolution (640x400, monochrome)

   To change resolution modes, use the following procedure. Define 
rez  equal  to  the  value of the  desired  resolution  then  call 
set_rez. (Note: high resolution is only available with a 
monochrome monitor.)

PROCEDURE set_rez
 '
  dummy=XBIOS(5,L:-1,L:-1,W:rez)
 '
RETURN

   Switching from medium to low resolution will present no special 
problems.  However, when you force a switch from low resolution to 
medium resolution,  graphics commands will not appear on the right 
side of the screen. The operating system still assumes that values 
greater than 319 for X are off the screen.  Meanwhile all graphics 
with X coordinates less than 320,  will be shown, on the left side 
of  the  screen.  Using the PRINT command to display  text  should 
present no problem.

GFA BASIC Graphics Commands

   As the following list of graphics commands illustrates, GFA 
BASIC provides a powerful and easy to use programming enviornment. 
More information about these commands can be found in Chapter Two, 
GFA BASIC Commands and Functions or in Appendix A, Quick Reference 
GFA BASIC Glossary.


BITBLT
BOX
CIRCLE
CLEARW
CLOSEW
CLS
COLOR
DEFFILL
DEFLINE
DEFMARK
DEFMOUSE
DRAW
ELLIPSE
FILL
FULLW
GET
GRAPHMODE
HARDCOPY
HIDEM
INFOW
LINE
MOUSE
MOUSEX
MOUSEY
MOUSEK
OPENW
PBOX
PCIRCLE
PELLIPSE
PRBOX
PLOT
POINT
POLYLINE
POLYFILL
POLYMARK
PUT
RBOX
SETCOLOR
SGET
SHOWM
SPRITE
SPUT
TEXT
TITLEW
VSYNC


Graphics on a 2-dimensional surface

   The simplest of the graphic commands in GFA BASIC are the  line 
drawing commands. The simplest of these is the LINE command. 
Remember, the coordinates used by the LINE command and the other 
GFA BASIC graphics commands are in the Raster Coordinate (RC) 
System.

Figure  3-7.  Simple  graphic produced by Program  3-1  using  GFA 
BASIC.

   The following short program demonstrates the ease with which  a 
simple graphic screen can be developed using the LINE and BOX 
commands.
   GFA BASIC listings for this book have been produced by first 
selecting the dir item on the Editor's menu bar, then entering, 
DEFLIST 0, which causes all commands and function to be displayed 
(and printed LLIST) in all capitol letters. Variable names and 
names of procedures will be in lower case letters. 
Program  3-1 
LINEDRAW.PRG


' Simple Line Drawing Demo
'
LINE 0,100,150,100
LINE 500,100,640,100
BOX 150,50,500,150
LINE 325,25,150,50
LINE 325,25,500,50
BOX 295,80,355,150
BOX 175,90,255,130
LINE 215,90,215,130
LINE 175,110,255,110
BOX 390,90,470,130
LINE 430,90,430,130
LINE 390,110,470,110
'


   In order to make the screen a little more interesting, we'll 
use DEFFILL to select a pattern style and colors to be used by the 
FILL command. For more information about DEFFILL, or any other GFA 
BASIC command, refer to Chapter Two. 

DEFFILL 3
'
FILL 5,195
'
DEFFILL 1,3
FILL 330,30
'
DEFFILL 1,2
FILL 5,5
'
DEFFILL 2,2
FILL 155,55
'
DEFFILL 2,1
FILL 310,115


   The image produced will only flash on the screen, then 
disappear as the edit screen reappears when the program ends . We 
need to place GFA BASIC into a loop which repeats until we decide 
it's time to exit the loop (and the program) and send a signal to 
the interpretter. All that is needed is a REPEAT...UNTIL loop 
which will wait for any key to be pressed. When a key is pressed, 
the program ends.


'
REPEAT
UNTIL INKEY$<>""
END


   Generally, we'll be discussing each routine used in a program, 
rather than the individual commands used to obtain the desired 
result. If a more detailed explanation of a command or function is 
needed, refer to Chapter 2 or Appendix A.


String Art

Only a short step from line drawing is an interesting art form, 
String Art. String Art may be either a succession of points 
connected by lines, or a  sequence of lines drawn on the screen. 
Computer generated String Art may even take the form of lines 
dancing around the screen, as in this program. STRING.BAS will 
draw each screen and then wait for the user to press a key before 
continuing. The last screen prompts the user for a positive 
number. This number determines how many petals to draw on a rose.
   Originally we intended this part to work only with integers, 
but we discovered that some very interesting patterns develop if 
you enter compound numbers (numbers with a fractional part). Try 
several different values. STRING.BAS will display the rose for 
each and then wait for you to press a key. If you'd like to stop 
the drawing process to any time, press a key. When the drawing has 
stopped, pressing a key will prompt you for a new number. Enter 0 
to exit STRING.BAS. The LINE command is used to draw each of the 
screens.

Program 3-2. String Art

   The first thing String Art does is check the current screen 
resolution and set the global variables x_size and y_size to the 
width and height of the screen, respectively.


' What resolution is the ST in?
'   xbios(4) returns 0 if low ,  1 if medium,  and 2  if  high 
resolution
rez=XBIOS(4)
'
' set x_size to the width and y_size to the height of the screen
'
IF rez=0
 x_size=320
 y_size=200
ENDIF
IF rez=1
 x_size=640
 y_size=200
ENDIF
IF rez=2
 x_size=640
 y_size=400
ENDIF
'


   STRING.BAS is written so that each screen is drawn by a 
separate procedure; this makes it easy to delete some of the 
existing screens or add new ones of your own. After each screen is 
drawn, STRING.BAS waits for any key to be pressed before it clears 
the screen and draws the next screen.

GOSUB screen_1
GOSUB wait_key
CLS
GOSUB screen_4
GOSUB wait_key
CLS
GOSUB screen_2
GOSUB wait_key
CLS
GOSUB screen_3
GOSUB wait_key
CLS
GOSUB screen_5
'
END


   The rest of STRING.BAS consists of the procedures used in 
calculating or actually drawing the figures.


'
'
' PROCEDURE wait_key
'
'    This subroutine pauses the program until the user  presses  a 
key.
'
PROCEDURE wait_key
 REPEAT
 UNTIL inkey$<>""
RETURN              ! end of wait_key


   The following procedure converts the radius and theta values of 
polar coordinates to Cartesian coordinates. See the section on 
coordinate systems earlier in this chapter for details.


'
'
' PROCEDURE polar_to_rect
'
'   This procedure converts from the polar coordinate system to the
' rectangular coordinate system. Pass r (radius) and theta to
'  polar_to_rect  and  it will return the x and y  values  in  the GLOBAL
' VARIABLES x and y.
'
PROCEDURE polar_to_rect(r,theta)
 x=r*COS(theta)
 y=r*SIN(theta)
RETURN              ! end of polar_to_rect


   This routine is used to draw two of the screens in STRING.BAS, 
by calculating the values necessary for the end points of the line 
to trace a limacon. Procedure limacon is used in the procedures 
screen --1 and screen --2. The first parameter of limacon is the 
angle theta for which the radius is to be calculated. The next two 
parameters are constants which modify the shape of the limacon. 
You might find it interesting to play around with these constants.


'
'
' PROCEDURE limacon
'
'   This procedure returns the value of r (radius) necessary to draw
'  a limacon given the angle of theta and two scaling  factors,  m and n.
' NOTE: r is a GLOBAL VARIABLE.
'
PROCEDURE limacon(theta,m,n)
 r=m+n*COS(theta)
RETURN             ! end of limacon


   Procedure rose generates one of the prettiest patterns possible 
using polar coordinates. Its output is used in screen 5.


'
'
' PROCEDURE rose
'
'   This procedure returns the value of r (radius) necessary to 
draw
' a rose given the angle theta,  the number of leaves,  n,  and  a 
scaling
' factor m. n determines the number of leaves in the rose. If n is 
even,
' then the rose will have 2n petals;  if n is odd, there will be n 
leaves.
' NOTE: r is a GLOBAL VARIABLE.
'
PROCEDURE rose(theta,n,m)
 r=m*COS(n*theta)
RETURN             

  end of rose denominator is used in screen --5 to  determine  how 
much  of  the flower to draw.  The denominator  returned  by  this 
procedure  is  used to calculate the upper limit of  the  function 
before it is plotted.


'
'
' PROCEDURE denominator
'
'   This  routine returns the denominator of a number  with  a 
fractional component.  
'
PROCEDURE denominator(num)
 LOCAL k
 LOCAL a
 LOCAL b
 '
 k=1
 found=0
 a=num
 GOSUB denom(a)
 IF found=0
  a=num/SQR(2)
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num/SQR(3)
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num/SQR(5)
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num/PI
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num/PI^2
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num/EXP(1)
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num*PI
  k=PI
  GOSUB denom(a)
 ENDIF
 IF found=0
  a=num*PI^2
  k=PI^2
  GOSUB denom(a)
 ENDIF
 IF found=0
  k=1
 ENDIF
 '
 d=b*k
RETURN
'
'
' PROCEDURE denom
'
'   This routine actually calculates the denominator of the fraction.
'
PROCEDURE denom(a)
 LOCAL c
 LOCAL dun
 c=ABS(a)
 b=1
 REPEAT
  dun=0
  b=b/c
  c=(1/c)-INT(1/c)
  IF b>100000
   dun=1
  ENDIF
 UNTIL c<1.0E-06 OR dun<>0
 IF dun<>1
  b=INT(b)
  found=1
 ENDIF
RETURN


   The remaining five procedures actually draw the screens. Each 
of them is well documanted in the code so we won't go into detail 
on them.


'
'
' PROCEDURE screen_1
'
'   This procedure draws the first screen using the procedures,
' NOTE: the following variables are GLOBAL: rez, x_size, and y_size.
'
PROCEDURE screen_1
 LOCAL steps
 LOCAL y_scale    !y scaling factor
 LOCAL x_scale    !x scaling factor
 LOCAL l_limit    !lower limit of funtion
 LOCAL u_limit    !upper limit of function
 LOCAL x_inc     !x or theta increment
 IF rez=0
  steps=1000*PI
 ENDIF
 IF rez=1
  steps=2000*PI
 ENDIF
 IF rez=2
  steps=4000*PI
 ENDIF
 '
 y_scale=y_size/2
 l_limit=0
 u_limit=2*PI
 x_scale=x_size/2
 x_inc=x_scale/steps
 '
 FOR theta=l_limit TO u_limit STEP x_inc
  GOSUB limacon(theta,y_scale*3/4,y_scale*3/4)
  GOSUB polar_to_rect(r,theta)
  x1=x
  y1=y
  GOSUB limacon(theta,y_scale*3/4,-y_scale*3/4)
  GOSUB polar_to_rect(r,theta)
  x2=x
  y2=y
  IF rez<>1
   LINE x1+x_scale,y1+y_scale,x2+x_scale,y2+y_scale
  ELSE
   LINE x1*2+x_scale,y1+y_scale,x2*2+x_scale,y2+y_scale
  ENDIF
 NEXT theta
RETURN             ! end of screen_1
'
'
' PROCEDURE screen_2
'
'   This procedure draws the second screen using the procedures,
' NOTE: the following variables are GLOBAL: rez, x_size, and y_size.
'
PROCEDURE screen_2
 LOCAL steps
 LOCAL y_scale    !y scaling factor
 LOCAL x_scale    !x scaling factor
 LOCAL l_limit    !lower limit of funtion
 LOCAL u_limit    !upper limit of function
 LOCAL x_inc     !x or theta increment
 IF rez=0
  steps=250*PI
 ENDIF
 IF rez=1
  steps=500*PI
 ENDIF
 IF rez=2
  steps=1000*PI
 ENDIF
 '
 y_scale=y_size/2
 l_limit=0
 u_limit=2*PI
 x_scale=x_size/(u_limit-l_limit)
 x_inc=x_scale/steps
 ' ferp
 FOR theta=l_limit TO u_limit STEP x_inc
  GOSUB limacon(theta,y_scale*9/14,y_scale)
  GOSUB polar_to_rect(r,theta)
  x1=x
  y1=y
  GOSUB limacon(theta,y_scale*9/14,-y_scale)
  GOSUB polar_to_rect(r,theta)
  x2=x
  y2=y
  IF rez<>1
   LINE x2+x_size*15/16,y2+y_size/2,x1+x_size/16,y1+y_size/2
  ELSE
   LINE x2*2+x_size*15/16,y2+y_size/2,x1*2+x_size/16,y1+y_size/2
  ENDIF
 NEXT theta
RETURN             ! end of screen_2
'
'
' PROCEDURE screen_3
'
'   This procedure draws the third screen using the procedures,
' NOTE: the following variables are GLOBAL: rez, x_size, and y_size.
'
PROCEDURE screen_3
 LOCAL steps
 LOCAL y_scale    !y scaling factor
 LOCAL x_scale    !x scaling factor
 LOCAL l_limit    !lower limit of funtion
 LOCAL u_limit    !upper limit of function
 LOCAL x_inc     !x or theta increment
 IF rez=0
  steps=500*PI
 ENDIF
 IF rez=1
  steps=750*PI
 ENDIF
 IF rez=2
  steps=1000*PI
 ENDIF
 '
 y_scale=y_size/2
 l_limit=0
 u_limit=8*PI
 x_scale=x_size/2
 x_inc=x_scale/steps
 '
 FOR i=l_limit TO u_limit STEP x_inc
  x1=SIN(i)+1
  x2=SIN(i-3*PI/4)+1
  y1=COS(i*3/4)+1
  y2=COS((i-3*PI/4)*3/4)+1
  LINE x1*x_scale,y1*y_scale,x2*x_scale,y2*y_scale
  PAUSE 1
 NEXT i
RETURN             ! end of screen_3
'
'
' PROCEDURE screen_4
'
'   This procedure draws the fourth screen using the procedures,
' NOTE: the following variables are GLOBAL: rez, x_size, and y_size.
'
PROCEDURE screen_4
 LOCAL steps
 LOCAL y_scale    !y scaling factor
 LOCAL x_scale    !x scaling factor
 LOCAL l_limit    !lower limit of funtion
 LOCAL u_limit    !upper limit of function
 LOCAL x_inc     !x or theta increment
 IF rez=0
  steps=250*PI
 ENDIF
 IF rez=1
  steps=500*PI
 ENDIF
 IF rez=2
  steps=1000*PI
 ENDIF
 '
 y_scale=y_size/2
 l_limit=0
 u_limit=5*PI
 x_scale=x_size/2
 x_inc=x_scale/steps
 '
 FOR i=l_limit TO u_limit STEP x_inc
  x1=SIN(i)+1
  x2=SIN(i-3*PI/4)+1
  y1=COS(i*5/6)+1
  y2=COS((i-3*PI/4)*5/6)+1
  LINE x1*x_scale,y1*y_scale,x2*x_scale,y2*y_scale
  PAUSE 1
 NEXT i
RETURN             ! end of screen_4
'
'
' PROCEDURE screen_5
'
'   This procedure draws the fifth screen using the procedures,
' NOTE: the following variables are GLOBAL: rez, x_size, and y_size.
'
PROCEDURE screen_5
 LOCAL steps
 LOCAL y_scale    !y scaling factor
 LOCAL x_scale    !x scaling factor
 LOCAL l_limit    !lower limit of funtion
 LOCAL u_limit    !upper limit of function
 LOCAL x_inc     !x or theta increment
 IF rez=0
  steps=500*PI
 ENDIF
 IF rez=1
  steps=1000*PI
 ENDIF
 IF rez=2
  steps=4000*PI
 ENDIF
 '
 y_scale=y_size/2
 l_limit=0
 x_scale=x_size/2
 '
 PRINT "  This routine draws flowers with the"
 PRINT "number of petals that you specify."
 PRINT "If you enter an odd number, n, a flower"
 PRINT "with n petals will be drawn. If you"
 PRINT "enter an even number, n, a flower with"
 PRINT "2n petals will be drawn. Flowers with"
 PRINT "large numbers of petals look like"
 PRINT "filled-in circles, so keep your number"
 PRINT "small. You can stop the drawing at any"
 PRINT "by pressing a key. When the drawing has"
 PRINT "stopped, press any key to continue."
 PRINT
 REPEAT
  INPUT "Input a positive number (0 to quit) ";n
 UNTIL n>=0
 WHILE n>0
  CLS
  u_limit=1
  d=1
  IF INT(n)<>n
   found=0
   GOSUB denominator(n)
   u_limit=d
  ENDIF
  IF ODD(n*d) AND ODD(d)
   u_limit=PI*u_limit
  ELSE
   u_limit=2*PI*u_limit
  ENDIF
  steps=2000*PI*n
  x_inc=x_scale/steps
  theta=l_limit
  a$=""
  WHILE theta<=u_limit AND a$=""
   GOSUB rose(theta,n,y_scale)      ! rose returns r
   GOSUB polar_to_rect(r,theta)     ! polar returns x and y
   x1=x
   y1=y
   GOSUB rose(theta-PI/(3*n),n,y_scale)
   GOSUB polar_to_rect(r,theta-PI/(3*n))
   IF rez=1
    LINE x1*2+x_scale,y1+y_scale,x*2+x_scale,y+y_scale
   ELSE
    LINE x1+x_scale,y1+y_scale,x+x_scale,y+y_scale
   ENDIF
   theta=theta+x_inc
   a$=INKEY$
  WEND
  GOSUB wait_key
  PRINT "Previous Number = ";n;" (";n*d;"/";d;")"
  REPEAT
   INPUT "Input a positive integer (0 to quit) ";n
  UNTIL n>=0
 WEND
RETURN             ! end of screen_5


Kaleidoscope

   Here's a colorful demonstration program reminiscent of the Lava 
Lamps popular during the 1960s. You may have seen a version of ths 
program  running  on the Commodore Amiga,  or even  a  C  language 
version  on  th  ST.  KALEDIOSCOPE.BAS runs  from  the  GFA  BASIC 
interpretter.  This program also demonstrates the use of some  new 
graphic  commands.  Note  that "!" separates a  comment  from  the 
command on the same line.  Also, the ' mark is used in lines which 
contain only a comment.   In this program you'll see color spelled 
two ways; color and colour. Color is a GFA BASIC command which 
sets the color to be used by a graphics command, and the in-line 
Syntax checker will interpret it as such. Often to use a 
descriptive label or variable name, it's advantageous to 
deliberately mis-spell a word. Be sure to keep track of such mis-
spellings, and mis-spell the word the same way every time.

Program 3-3. KALEDIO.BAS

   Begin by reserving an area of memory to hold the alternate 
palette colors.   

DIM palette(15),pal(15),pal2(15)
'
shape=0          ! Initial shape is a circle.
HIDEM           ! Hide mouse
'
'
' Check for low resolution
'
IF XBIOS(4)<>0
 alrt$="KALEIDOSCOPE only works in|Low Res (320X200 Pixels)"
 ALERT 3,alrt$,1,"Oops!!",b
 END
ENDIF


    Next,  set  up  an alternate  color  palette.  Each  color  is 
represented by three hexadecimal numbers,  representing the  three 
color guns of an RGB (Red, Green, and Blue) monitor, ranging from 
0 for a gun which is turned off, to 7 for a gun at the highest 
output level. You can experiment with the numbers on the following 
table to observe the effects of different numbers on the display. 
(For more inforamtion about colors and the SETCOLOR command, refer 
to Chapter 2.)
   You can use the Control Panel desk accessory to get instant 
feedback on mixing colors. When you use it to mix colors using 
different levels of red, green, and blue, the panel displays these 
color levels as numbers from 0 to 7. The desktop, and the COntrol 
Panel, will change colors as you change the settings. It's best to 
write down the numbers displayed as you proceed, as it may become 
necessary to turn off your ST and reboot in order to restore a 
readable screen. Use these numbers as the hexadecimal values in 
the following table to install the colors in your color palette, 
as demonstrated below.


'
'
' Set up color table
'
pal2(0)=&H555
pal2(1)=&H700
pal2(2)=&H60
pal2(3)=&H7
pal2(4)=&H5
pal2(5)=&H520
pal2(6)=&H50
pal2(7)=&H505
pal2(8)=&H222
pal2(9)=&H77
pal2(10)=&H55
pal2(11)=&H707
pal2(12)=&H505
pal2(13)=&H550
pal2(14)=&H770
pal2(15)=&H555
'


   Now we'll display an Alert box containing the program title and 
a few pieces of necessary preliminary information. Usually, you 
won't want to use an Alert box for displaying anything except a 
warning, but in this case very little information is required. 
Notice that as you type in the text for the variable alrt$ the 
screen will scroll to the left. When you move to the next line, a 
dollar sign is displayed at the point where the text exceeds the 
80 character screen limit. This dollar sign signifies that more 
text exists on this line

.


'
' Display title box
'
alrt$="    Kaleidoscope|Left Button  Restarts|Right  Button 
Changes Shape|Both Buttons End Program|"
ALERT 1,alrt$,1,"Okay",b
'


   Since we plan to tamper with the color scheme, it would only be 
polite to provide a means to reset the colors when we end our 
program.


GOSUB save_palette    '
' Setcolor 0,5,5,5     ! Set background to gray.
'
GOSUB set_colour      ! Install new palette
'
start:           ! Here's the real starting point
'
GOSUB restore_palette   ! We want to restore colors for multiple runs
'              otherwise print might be hard to read.
CLS
'
' Do some more start up stuff.
'
PRINT AT(1,10);
INPUT "How many pixels/step (1 to 10)";stp$
IF stp$=""
 GOTO start
ENDIF
stp=VAL(stp$)
'
IF stp<1 OR stp>10  ! Check for valid range.
 GOTO start
ENDIF
'
minr=stp
CLS
FOR colour=1 TO 12
 DEFTEXT colour,17
 GOSUB title
NEXT colour
c=0


    The next few lines determine the starting point for the  first 
item to be drawn.


x=INT(RND(1)*320)
x1=x
y=INT(RND(1)*179)+20
y1=y
r=minr
dr=1
'
' Main program loop follows:
'
REPEAT
 '
 GOSUB new_x
 GOSUB new_y
 '
 DEFFILL c
 INC c
 IF c>15
  c=1
 ENDIF
 IF dr=1
  INC r
 ENDIF
 IF dr=0
  DEC r
 ENDIF
 IF r=20
  dr=0
 ENDIF
 IF r=minr
  dr=1
 ENDIF
 '
 


Now determine which shape,  circle or square to draw; then display 
that shape on the screen.



 IF shape=0
  PCIRCLE x,y,r
 ELSE
  PBOX x,y,x+r,y+r
 ENDIF
 '
 GOSUB change_colour
 '
 k=MOUSEK
UNTIL k<>0
'
' Left mouse button pressed?
'
IF k=1
 GOTO start
ENDIF
'
' Right Mouse button pressed?
'
IF k=2 AND shape=0
 shape=1        ! Change shape to rectangle
 GOTO start
ENDIF
'
IF k=2 AND shape=1
 shape=0        ! Change shape to circle
 GOTO start
ENDIF
'
PAUSE 35        ! System needs a sec or 2 here.
CLS
GOSUB restore_palette
SHOWM
END
'


   Now we need to find a new value for x.


'
PROCEDURE new_x
 '
 IF x1>=319
  SUB x,stp
 ELSE
  ADD x,stp
 ENDIF
 ADD x1,stp
 IF x1>=643
  x1=stp
  x=stp
 ENDIF
RETURN
'


   Next we need a new y value.


'
PROCEDURE new_y
 '
 IF y1>199
  SUB y,stp
 ELSE
  ADD y,stp
 ENDIF
 ADD y1,stp
 IF y1>375
  y1=28
  y=28
 ENDIF
RETURN
'


   The following procedure is a useful routine you'll see often in 
this  book.  It saves the palette as set up by the user  from  the 
Control Panel, so that the default colors may be restored when the 
program ends.


' Save Original Color Palette
'
PROCEDURE save_palette
 LOCAL i
 '
 FOR i=0 TO 15
  palette(i)=XBIOS(7,W:i,W:-1)
  pal(i)=palette(i)
 NEXT i
 '
RETURN
'
'


   Here's the procedure which restores the default color  palette. 
You'll see this one used again, too.


'
' Restore Original Color Palette
'
PROCEDURE restore_palette
 LOCAL i
 '
 FOR i=0 TO 15
  SETCOLOR i,palette(i)
 NEXT i
RETURN
'


     To give the illusion of constant movement on the screen, 
we're going to rotate the color palette. This procedure takes care 
of the rotation sequence.


PROCEDURE change_colour
 '
 temp=pal(1)
 FOR i=2 TO 15
  pal(i-1)=pal(i)
 NEXT i
 pal(15)=temp
 '
 FOR i=1 TO 15
  SETCOLOR i,pal(i)
 NEXT i
 FOR i=0 TO 15
  pal(i)=XBIOS(7,W:i,W:-1)
 NEXT i
RETURN
'


   Here is another routine to dazzle the beholder.  This procedure 
sets  up the title "Kaleidoscope" to alternate colors  with  color 
cycling.


PROCEDURE title
 IF colour=1
  TEXT 95,7,"K"
 ENDIF
 IF colour=2
  TEXT 105,7,"a"
 ENDIF
 IF colour=3
  TEXT 115,7,"l"
 ENDIF
 IF colour=4
  TEXT 125,7,"e"
 ENDIF
 IF colour=5
  TEXT 135,7,"i"
 ENDIF
 IF colour=6
  TEXT 145,7,"d"
 ENDIF
 IF colour=7
  TEXT 155,7,"o"
 ENDIF
 IF colour=8
  TEXT 165,7,"s"
 ENDIF
 IF colour=9
  TEXT 175,7,"c"
 ENDIF
 IF colour=10
  TEXT 185,7,"o"
 ENDIF
 IF colour=11
  TEXT 195,7,"p"
 ENDIF
 IF colour=12
  TEXT 205,7,"e"
 ENDIF
RETURN
'


   The set_color procedure is used to install our custom palette 
when the program intializes.


PROCEDURE set_colour
 FOR i=0 TO 15
  dummy=XBIOS(7,pal2(i))
 NEXT i
RETURN



The Dragon Plot

Fractals  have  been  receiving  a  great  deal  of  attention  in 
mathematics  and  computer  graphics.   They're  being  used   for 
everything from simulating random plant growth to generating 
realistic planetary landscapes in science fiction films.
     Understanding fractals may not be as exciting as seeing them 
in action, but some explanation should prove helpful to your 
programming. The word fractal €was coined by Benoit Mandelbrot, a 
pioneer in their study, to denote curves or surfaces having 
fractional dimension. The idea of fractional dimension can be 
illustrated as a straight curve (a line) which has only one- 
dimension, length. If the curve is infinitely long and curves in 
such a manner that it completely fills an area of the plane 
containing it, the curve can be considered two-dimensional. A 
curve partially filling an area has a fractional dimension between 
1 and 2.
   Many types of fractals are self-similar. This means that all 
portions of the fractal resemble each other. This occurs whenever 
the whole is an expansion of some basic building block. In the 
language of fractals, this basic building block is called the 
generator.
  The generator in the next program consists of a number of 
connected line segments.The curves plotted by this program are the 
result of starting with the generator and then repeatedly 
replacing each line segment, according to a defined rule. The 
number of cycles is limited by the screen resolution. Select too 
high a number of cycles, and the program will also slow down to a 
crawl. Eventually, the screen will be filled by the fractal 
generator, as portions are plotted off the screen as well.
  This simple program which begins our exploration of the world of 
fractals plots a particular type of fractal which Mandelbrot 
labeled a "dragon plot." This program illustrates a self-
contacting curve. A self-contacting curve touches, but does not 
cross, itself. The generator consists of two-line segments of 
equal length forming a right angle. During each cycle, the 
generator is substituted for each segment on alternating sides of 
the segments. (Even though GFA BASIC executes faster than most 
interpreted languages, it's still slow, and that's part of the 
fascination of the dragon plot --watching as your ST plots the 
figure, and noting the areas of similarity.
   DRAGON.BAS begins by asking you to enter an even number of 
cycles. When a plot is complete, pressing any key clears the 
screen and returns you to the starting prompt. Try starting out 
with two cycles, then four, then six, and so on.  As you add more 
cycles, more time is required to fill in the dragon.


Program 3-4. DRAGON.BAS


DIM sn(20)
in:
CLS
PRINT "Enter an even number of cycles (2-20)"
INPUT "or enter a zero to quit: ";nc$
nc=VAL(nc$)
IF nc=0
 END
ENDIF
IF nc<2 OR nc>20
 GOTO in
ENDIF
IF EVEN(nc)<>-1
 GOTO in
ENDIF
l=128
FOR c=2 TO nc STEP 2
 l=l/2
NEXT c
x=85
y=100
CLS
COLOR 3
PLOT x,y
FOR c=0 TO nc
 sn(c)=0
NEXT c
rot_seg:
d=0
FOR c=1 TO nc
 IF sn(c-1)=sn(c)
  d=d-1
  GOTO rotate_it
 ENDIF
 d=d+1
 rotate_it:
 IF d=-1
  d=7
 ENDIF
 IF d=8
  d=0
 ENDIF
NEXT c
IF d=0
 x=x+l+l
 GOTO seg
ENDIF
IF d=2
 y=y+l
 GOTO seg
ENDIF
IF d=4
 x=x-l-l
 GOTO seg
ENDIF
y=y-l
seg:
COLOR 3
DRAW TO x,y
sn(nc)=sn(nc)+1
FOR c=nc TO 1 STEP -1
 IF sn(c)<>2
  c=1
  GOTO next_seg
 ENDIF
 sn(c)=0
 sn(c-1)=sn(c-1)+1
 next_seg:
NEXT c
IF sn(0)=0
 GOTO rot_seg
ENDIF
PRINT AT(7,23);"Press any key to continue"
REPEAT
UNTIL INKEY$<>""
GOTO in



The Mandelbrot Set

     You can see fractals in nature in many places. The clouds, 
coastlines displayed in satellite photographs, and even a leaf 
will reveal fractals. We've seen one form of computer-generated 
fractals in Program 3-5, the dragon sweep. Now we'll explore one 
of the strangest and most beautiful areas of fractal geometry, the 
Mandelbrot set.
   The Mandelbrot set consists of complex numbers, numbers with a 
"real" and "imaginary" part. These terms, real and imaginary, have 
historical significance in mathematics, but are no longer 
relevant. A complex number takes the form of 6 + 3i; 6 is the real 
part of the number, and 3i represents the imaginary part (hence 
the i). Each complex number can be represented by a point on the 
two-dimensional plane.
   The Mandelbrot set is located at the center of a two-
dimensional sheet of numbers called the complex plane. When a 
specific operation is applied repeatedly to the numbers, the 
numbers outside the set retreat to infinity. The remaining numbers 
move about within the plane. Near the edge of the set, the numbers 
move about in a pattern which marks the beginning of the area of 
instability. This area is astonishingly beautiful, complex, 
infinitely variable, and yet somehow, strangely similiar.
   The unique factor in numbers within the Mandelbrot set is that 
values in the set never grow larger than 2 as the mathematical 
operation is performed on them. Points within the Mandelbrot set 
are represented in our program by black pixels. The colors of the 
other points are determined by counting the number of times each 
complex number is operated on before its value exceeds 2. This 
count is converted into a color.
   For more information on the theory of fractals, see The Fractal 
Geometry of Nature, by Benoit Mandelbrot.


Figure 3-8. The Mandelbrot Primitive

  Figure 3-8 shows a representation of the entire Mandelbrot set. 
You can reproduce this figure by running MANDELBROT.BAS, and 
selecting 100 iterations, an X Center of .75, and a Y Center of 0. 
Choose a range of 2 for viewing the complete image. Once you've 
become somewhat familiar with the general coordinates of the 
Mandelbrot set, try exploring the boundary area by selecting x and 
y coordinates located on the boundary, and then selecting smaller 
values for the range.   Program 3-5, MANDELBROT.BAS, was used to 
generate the image displayed in Figures 3-8, 3-9, and 3-10. Only a 
black-and-white representation was possible in the book, but the 
set generated by Program 3-5 is quite colorful.    Some other 
interesting areas to explore follow.

Figure 3-9. Mandelbrot Figure

Figure 3-10. Another Segment of the Mandelbrot Boundary.



X-Center   Y-Center    Range
  -1       0.32        0.3
  -1       0.2895      0.0005
  -0.97    0.276       0.0001


 
     In this program, we'll be introducing several new procedures 
which can be used in your own programs. We'll show you later how 
to merge these procedures into your programs.


Program 3-5. MANDELBROT.BAS


DIM palette(15),pal2(15)

   The mouse pointer will be in the way on the picture,  so  we'll 
just turn it off.


'
HIDEM
'


   We'll check to see which resolution is in use, then give a 
warning if the machine isn't in low resolution. This program will 
work in any resolution; it just looks best with 16 colors, so 
we'll allow it to continue if the user doesn't want to quit.


'
rez=XBIOS(4)
IF rez<>0
 alrt$="Fractals look best in|Low Resolution"
 ALERT 1,alrt$,1,"Continue|Quit",b
 IF b=2
  END
 ENDIF
ENDIF
'


    Next  we'll  establish default  values  for  different  screen 
resolutions.



IF rez=0
 screen_height=200      ! Low res screen 
 screen_width=320       
ENDIF
'
IF rez=1            ! Medium resolution screen
 screen_height=200
 screen_width=640
ENDIF
'
IF rez=2            ! High resolution screen
 screen_height=400
 screen_width=640
ENDIF
'
' Main Loop begins here
'


   We've used this routine before. It saves the palette so you can 
restore the original colors later. It's a good programming 
practice to clean up after yourself. If you change the palette, 
then exit to the GFA BASIC editor, you may find yourself stuck on 
a screen that is impossible to read.


GOSUB save_palette
'


   Here's the main loop which controls the program.


DO
 '
 GOSUB values
 IF rez=0
  GOSUB set_new_colors
 ENDIF
 GOSUB calculate
 IF rez=0
  GOSUB restore_palette
 ENDIF
 GOSUB display_it
 '
LOOP


   We'll put an END in here, but the program never really exits 
from the DO...LOOP. Other procedures are called and executed from 
procedures called by the DO...LOOP, but everything within this 
program actually occurs within this loop.


'
END
'


   display_it is a procedure which displays information about the 
calculations for this particular portion of the Mandelbrot set and 
offers some options which may be selected by pressing a key. 
Usually this procedure will be encountered after the calculations 
for displaying the fractal are complete.

PROCEDURE display_it
 '
 display:
 CLS
 PRINT AT(1,3);"Fractal Image"
 PRINT AT(1,5);count;" Iterations Calculated."
 seconds=INT((time_finish-time_start)/2)/100
 min=INT(seconds/60)
 IF min<=0
  min=0
 ENDIF
 seconds=ABS(INT((seconds MOD 60)*100)/100)
 PRINT AT(1,7);min;" Minutes and ";seconds;" Seconds required."
 PRINT AT(1,8);"Number of iterations: ";iteration_limit
 PRINT AT(1,10);"X Center: ";x_center
 PRINT AT(1,11);"Y Center: ";y_center
 PRINT AT(1,12);"Scaling factor: ";range
 PRINT AT(1,14);"Minimum real value (xmin): ";real_min
 PRINT AT(1,15);"Maximum real value (xmax): ";real_max
 PRINT AT(1,16);"Minimum imaginary value (ymin): ";imag_min
 PRINT AT(1,17);"Maximum Imaginary value (ymax): ";imag_max
 PRINT AT(1,19);"Press:"
 PRINT AT(5,20);"<V> to View Fractal"
 PRINT AT(5,21);"<P> to Plot new Fractal"
 PRINT AT(5,22);"<S> to Save .NEO file"
 PRINT AT(5,23);"<Q> to Quit"
 '


   key waits for the user to press a key. Then the key value is 
stored in a$, and evaluated, and the proper branch is taken. UPPER 
is a GFA BASIC command which converts any value in a$ to 
uppercase. For more information about any GFA BASIC commands, 
refer to Chapter 2.


 key:
 REPEAT
  a$=INKEY$
 UNTIL a$<>""
 '
 IF UPPER$(a$)="V"
  SGET screen2$
  IF rez=0
   GOSUB set_new_colors
  ENDIF
  SPUT screen1$
  REPEAT
  UNTIL INKEY$<>""
  GOSUB restore_palette
  SPUT screen2$
 ENDIF
 '
 IF UPPER$(a$)="P"
  GOTO finito
 ENDIF
 '
 IF UPPER$(a$)="Q"
  SHOWM
  CLS
  END
 ENDIF
 '
 IF UPPER$(a$)="S"
  '


   Here's a handy procedure that saves the screen into a 
NEOchrome-compatible file. Following this program, we'll give you 
a simple routine which can be merged with your programs, and show 
you how you can use this routine to load screens in your own 
programs. 

  IF rez<>0
   CLS
   ALRT$="Must be Low Res|for Neochrome files"
   ALERT 1,alrt$,1,"OKAY",b
  ENDIF
  GOTO not_neo
  '
  SGET screen2$
  default$="C:\*.NEO"
  FILESELECT default$,"",infile$
  CLS
  IF infile$=""           !equals "" if CANCEL selected
   GOTO not_neo
  ENDIF
  GOSUB set_new_colors
  SPUT screen1$
  OPEN "o",#1,infile$
  '
  ' First two bytes to zero
  '
  FOR i=0 TO 2
   OUT #1,0
   OUT #1,0
  NEXT i
  '
  ' Save color palette
  '
  FOR i=0 TO 15
   hi=INT(pal2(i)/256)
   lo=pal2(i)-256*hi
   OUT #1,hi
   OUT #1,lo
  NEXT i
  '
  ' Color cycling info (not needed)
  '
  FOR i=0 TO 89
   OUT #1,0
  NEXT i
  '
  ' Save screen info
  '
  BPUT #1,XBIOS(3),32000
  '
  CLOSE
  SPUT screen2$
  GOSUB restore_palette
  '
  not_neo:
  '
 ENDIF
 '
 GOTO display
 '
 finito:
' 
 RETURN
'


   values accepts input from the user for the values to be 
examined for the Mandelbrot boundaries.


PROCEDURE values
 '
 CLS
 INPUT "Number of iterations";iteration_limit
 INPUT "Center X";x_center
 INPUT "Center Y";y_center
 INPUT "Scale Range";range
 real_min=x_center-(range/2)
 real_max=x_center+(range/2)
 imag_max=y_center+((range/2)*0.77)
 imag_min=y_center-((range/2)*0.77)
 CLS
RETURN
'
    The next procedure does the real work.  The complex number  is 
evaluated as defined. Several arbitary values were selected for 
constants. You may find it interesting to change values, such as 
max_limit, to observe any changes in the figure plotted. 
time_start is used to calculate the time it took to complete the 
plot.
   Note that even though GFA BASIC is one of the fastest 
interpreters available, fractals can take a lot of time to plot. 
Most designs will take over an hour to complete. The closer the 
complex numbers are to the Mandelbrot set, the more calculations 
are required before the result exceeds 2. Therefore, more time is 
required.


PROCEDURE calculate
 '
 time_start=INT(TIMER)
 max_limit=100000000
 count=0
 real=(real_max-real_min)/(screen_width-1)
 imaginary=(imag_max-imag_min)/(screen_height-1)
 FOR y=0 TO screen_height
  FOR x=0 TO screen_width
   lreal=real_min+x*real
   limag=imag_min+y*imaginary
   re=lreal
   im=limag
   depth=0
   calc_loop:
   INC count
   x1=re^2
   y1=im^2
   im=2*re*im-limag
   re=x1-y1-lreal
   INC depth
   IF ((depth=iteration_limit) OR ((x1+y1)>max_limit))
    GOTO finished_yet
   ELSE
    GOTO calc_loop
   ENDIF
   finished_yet:
   IF (depth<iteration_limit)
    GOSUB draw_point
   ENDIF


   Since we can get stuck here waiting on the calculations for a 
long time, this will offer a way out and allow us a means to check 
on the time spent and calculations completed on this particular 
set of complex numbers.


   IF INKEY$<>""
    GOSUB break
   ENDIF
  NEXT x
 NEXT y
 '
 ' Save screen into screen1$
 '
 SGET screen1$
 '
 time_finish=INT(TIMER)     ! time of completion
 '
RETURN
'


   If a key is pressed, we must stop to evaluate it. We'll also 
display an interim screen with some interesting information. 

PROCEDURE break
 '
 SGET screen1$
 time_finish=INT(TIMER)
 IF rez=0
  GOSUB restore_palette
 ENDIF
 CLS
 PRINT AT(1,3);"Fractal Image"
 PRINT AT(1,5);count;" Iterations Calculated."
 seconds=INT((time_finish-time_start)/2)/100
 min=INT(seconds/60)
 IF min<=0
  min=0
 ENDIF
 seconds=ABS(INT((seconds MOD 60)*100)/100)
 PRINT AT(1,7);min;" Minutes and ";seconds;" Seconds required."
 PRINT AT(1,8);"Number of iterations: ";iteration_limit
 PRINT AT(1,10);"X Center: ";x_center
 PRINT AT(1,11);"Y Center: ";y_center
 PRINT AT(1,12);"Scaling factor: ";range
 PRINT AT(1,14);"Minimum real value (xmin): ";real_min
 PRINT AT(1,15);"Maximum real value (xmax): ";real_max
 PRINT AT(1,16);"Minimum imaginary value (ymin): ";imag_min
 PRINT AT(1,17);"Maximum Imaginary value (ymax): ";imag_max
 PRINT AT(1,19);"Press:"
 PRINT AT(5,20);"<C> to Continue Plot"
 PRINT AT(5,21);"<E> to Return to Main Menu"
 '
 keyit:
 REPEAT
  a$=INKEY$
 UNTIL a$<>""
 '
 IF UPPER$(a$)="E"
  x=screen_width
  y=screen_height
  SPUT screen1$
  GOTO finit
 ENDIF
 '
 IF UPPER$(a$)="C"
  IF rez=0
   GOSUB set_new_colors
  ENDIF
  SPUT screen1$
  GOTO finit
 ENDIF
 '
 GOTO keyit
 '
 finit:
RETURN

   The calculations are completed; now it's time to plot the 
point. Depth is equal to the number of iterations calculated on 
the number which represents the point. 

'
PROCEDURE draw_point
 '
 colour=depth MOD 16
 COLOR colour
 IF (depth>100)
  PLOT x,y
 ELSE
  GOSUB greater_than_two
 ENDIF
RETURN
'
PROCEDURE greater_than_two
 '
 IF depth MOD 2
  PLOT x,y
 ENDIF
RETURN
'


   set_new_colors changes the color palette by installing the 
colors we've selected into the hardware register for the palette.


PROCEDURE set_new_colors
 '
 ' Set up color table
 '
 pal2(0)=&H0
 pal2(1)=&H75
 pal2(2)=&H765
 pal2(3)=&H401
 pal2(4)=&H410
 pal2(5)=&H530
 pal2(6)=&H241
 pal2(7)=&H62
 pal2(8)=&H474
 pal2(9)=&H744
 pal2(10)=&H731
 pal2(11)=&H165
 pal2(12)=&H14
 pal2(13)=&H750
 pal2(14)=&H423
 pal2(15)=&H601
 '
 '
 FOR i=0 TO 15
  SETCOLOR i,pal2(i)
 NEXT i
RETURN
'


   We've seen the next two procedures before.

'
' Save Original Color Palette
'
PROCEDURE save_palette
 LOCAL i
 '
 '
 FOR i=0 TO 15
  palette(i)=XBIOS(7,W:i,W:-1)
 NEXT i
RETURN
'
'
'
' Restore Original Color Palette
'
PROCEDURE restore_palette
 LOCAL i
 '
 FOR i=0 TO 15
  SETCOLOR i,palette(i)
 NEXT i
RETURN






Saving a Screen in NEOchrome Format

Here's a simple little routine similar to the one used in 
MANDELBROT.BAS. This program can easily be merged with any of your 
programs.

Program 3-6. NEOWRITE.BAS

Procedure Save_neoscreen
'Reserve an area of memory for the alternate palette.

 '
 Dim Pal2(15)
 '
 Gosub Save_palette
 Hidem
 '
 Sget Screen1$
 '
 Rez=Xbios(4)
 If Rez<>0
  Cls
  Print ''Must be Low Resolution for Neochrome''
  Repeat
  Until Inkey$<>''''
  Cls
  Sput Screen1$
  Goto Not_neo
 Endif
 '
 Default$=''A:\*.NEO''
 Fileselect Default$,'''',Infile$
 Cls
 Sput Screen1$
 Open ''o'',#1,Infile$
 '
 ' First three words to zero
 '
 For I=0 To 2
  Out #1,0
  Out #1,0
 Next I
 '
 ' Save color palette
 '
 For I=0 To 15
  Hi=Int(Pal2(I)/256)
  Lo=Pal2(I)-256*Hi
  Out #1,Hi
  Out #1,Lo
 Next I
 '
 ' Color cycling info (not needed)
 '
 For I=0 To 89
  Out #1,0
 Next I
 '
 ' Save screen info
 '
 Bput #1,Xbios(3),32000
 '
 Close
 '
 Not_neo:
 '
Endif
'
'
Finito:
'
Return
'
' Save Original Color Palette
'
Procedure Save_palette
Local I
'
'
'
For I=0 To 15
 Pal2(I)=Xbios(7,W:I,W:-1)
Next I
Return
'


After you've saved a screen in a NEOchrome format,  you'll need  a 
routine to display the screen without loading NEOCHROME.PRG. 
Here's a routine to load any NEOchrome-format screen. With a minor 
alteration, you may load any screen into your programs without 
using the fileselector box.

Program 3-7. NEOLOAD.BAS



DIM palette(15),pal2(15)
'
GOSUB save_palette
'


     Here's the main loop. Use these procedures as applicable in 
your program to load .NEO files. Refer to the user's guide for 
DEGAS Elite for information on how to handle a DEGAS file. It's 
just as simple.


main:
'
GOSUB check_rez
GOSUB choose_pic
HIDEM
GOSUB load_colour
GOSUB install_colour
GOSUB show_pic
'
g$=''''
REPEAT
 g$=INKEY$
UNTIL g$<>''''
'
CLS
'
GOSUB restore_palette
'
IF UPPER$(g$)=''Q''
 END
ENDIF
'
SHOWM
GOTO main
'
'
PROCEDURE check_rez
 '
 rez=XBIOS(4)
 IF rez<>0
  alrt$=''NEOLOAD only works in|Low Resolution.''
  ALERT 3,alrt$,1,''Exit'',b
  END
 ENDIF
 '
RETURN
'
PROCEDURE choose_pic
 '


     The next section was included to allow you to select a 
NEOchrome-format file using the standard GEM file selector. If 
you'd like to load a predetermined file, omit this procedure and 
define Filename$ as the name of the desired program before calling 
Procedure Load_colour.


 '
 disk$=''*.NEO''
 FILESELECT disk$,'''',filename$
 IF filename$=''''
  END
 ENDIF
 '
RETURN
'
PROCEDURE load_colour
 '
 OPEN ''I'',#1,filename$
 temp$=INPUT$(38,#1)



The first six bytes of the file don't matter,  so we'll strip them 
off.


 colour$=MID$(temp$,7,32)
 CLOSE #1
 '


Next, we'll break down the two-byte color values into values which 
we can assign to our alternate palette, and install the colors.


 palnum=0
 count=0
 REPEAT
  hibyte=ASC(MID$(colour$,count,1))
  INC count
  lobyte=ASC(MID$(colour$,count,1))
  INC count
  pal2(palnum)=(hibyte*256)+lobyte
  INC palnum
 UNTIL palnum=15
 '
RETURN
'

The  following XBIOS routine changes the hardware pointer  to  the 
palette  to point to the variable Colour$.  Changing this  pointer 
installs the new palette.



PROCEDURE install_colour
 '
 VOID XBIOS(6,L:VARPTR(colour$))
 '
RETURN
'


  Here's a little trick for loading the picture. XBIOS (2) is an 
XBIOS function which returns the location of the physical screen. 
This will vary for 520s and 1040s. Actually, we're cheating a bit 
here. We know that the first 128 bytes of a NEOchrome file contain 
information we're not interested in (information concerning the 
resolution, which is never used, the color palette, and the color 
rotation ). What we'll do is ignore this information and begin 
loading the picture into an absolute memory location 128 bytes 
lower than the beginning of screen memory. This area isn't usually 
used for anything, and provides an easy way to strip off the 
unneeded bytes and load the picture image.


PROCEDURE show_pic
 '
 physbase=XBIOS(2)
 BLOAD filename$,physbase-128
 '
RETURN
'
' Save Original Color Palette
'
PROCEDURE save_palette
 '
 FOR i=0 TO 15
  palette(i)=XBIOS(7,W:i,W:-1)
 NEXT i
 '
RETURN
'
PROCEDURE restore_palette
 '
 FOR i=0 TO 15
  SETCOLOR i,palette(i)
 NEXT i
 '
RETURN



Great Graphics

     As you have seen from these simple examples, GFA BASIC makes 
graphics programming easy. It's not necessary to resort to PEEK's 
and POKE's to achieve the spectacular. This is only the starting 
point. As you continue to explore graphics with GFA BASIC, you'll 
be amazed at the power you can unleash as use the power of the 
68000 Microprocessor.
   In the next chapter, we'll introduce you to an even more 
impressive use of graphics -- Animation. Soon you'll be writing 
the games you dream about.

e you to  an  even  more 
impressive  use of graphics -- Ani