Atari ST Machine Specific Programming In Assembly

Chapter 7: An Adaptive Algorithm
     

Algorithmic Intelligence
  
     By saying to you now that I consider every item of 
software to be intelligent to at least some degree, I 
restrict the range of my future comments concerning any 
comparisons between the levels of intelligence of items of 
software to the extent that I will not be able to refer to 
one item as intelligent and another as being devoid of 
intelligence.  My comments would not be as restricted if 
there were a system of intelligent quotients for software, 
because then I would be able to assign an IQ to each item 
under discussion in order to specify its relative level of 
intelligence.
     I am not aware of the existence of such a system and I 
have no desire to develop one myself, at least not at this 
time.  Therefore, in order to differentiate between levels 
of software intelligence, I must use descriptive phrases 
such as smarter than or more intelligent than.  I place 
these limits on the terminology I permit myself to use in 
this chapter because I want to avoid extensive, 
nonproductive philosophical discussions of relative levels 
of intelligence.
     Most of the algorithms that I have discussed so far 
have been designed to perform their functions in an 
unsophisticated fashion, without much regard for external 
stimuli.  Notable exceptions are the custom traps which 
adjust their output based on the number of digits or the 
number of leading zeroes in a passed parameter and trap #8, 
which executes a wait for keypress algorithm only if the 
invoking process was not spawned by another.  To the degree 
that response to external stimuli is a measure of 
intelligence, those custom traps which adapt their output 
according to input are more intelligent than those which 
simply alter a memory location, such as does trap #0, or 
return a value, such as does trap #3.
     Much as I have declared custom traps which alter their 
output in response to their input to be the more intelligent 
in the paragraph above, I shall simply declare that an 
algorithm which can alter itself in response to external 
stimuli to be more intelligent than one which cannot do so.  
And, in order to reduce the length of descriptive phrases, I 
shall refer to such algorithms as adaptive algorithms.  In 
fact, I shall simply declare that the term adaptive applies 
to any algorithm which can alter itself in response to any 
stimuli, whether it be externally or internally generated.
     If you have read the suggested material in Christopher 
Evans' The Micro Millennium, I believe that you will grasp 
my line of reasoning and deduce that I am laying the 
foundation for a discussion of an item of software to which 
Mr. Evans' six major constituents of intelligence may be 
applied.  I am not concerned about adhering religiously to 
his definitions, nor do I wish to confirm or refute his 
conclusions.  My only concern is that you understand the 
discussions in this chapter, and I feel that I could not 
have found a better reference than his for your perusal.
     I am very aware of the hundreds, perhaps even 
thousands, of books which have been jammed on bookshelves in 
recent years simply because a number of people with nothing 
to say realized that money could be had if it was said in a 
book bearing the words Artificial Intelligence.  And if one 
of these books does actually contain useful information, I 
shall probably never know of it because I have vowed not to 
touch a book bearing those words on its front cover.  In 
fact, I would consider myself honored if you would now ink 
over those words in the sentence above and pretend that I 
never wrote them.
     I have recommended Mr. Evans' book because it is not at 
all like those others that are filled with buzz word 
gibberish copied from articles or other books filled with 
identical gibberish.  I have enjoyed the Evans book 
immensely, and I have just finished reading it for the third 
time, so as to have it freshly in mind as I write this 
chapter.  If you disagree with my choice of references, I 
can live with that, but I would be negligent if I did not 
suggest to you the material which has had the greatest 
influence on the material which I present.

Onanism Corruptus: The Sin of Self-Modification
  
     At this time, there is a notion that I would like you 
to store someplace in a corner of your mind, and, from time 
to time, as I spend my energy in conveying to you the 
concept and the reality of a software tool that I believe is 
as powerful as the concept and reality of the computer 
itself, I would like you to recall that notion and consider 
the limiting effect that would be placed on software utility 
were it to be universally enforced.  This notion is 
expressed most succinctly on page 92 of 680x0 Programming by 
Example, written by Stan Kelly-Bootle, under the heading 
Logic Behind Rule C.  The precise sentence which I would 
like you to remember, if for no other reason than that it 
alone justifies the existence of this entire chapter, is 
that which follows:

   "Motorola discourages self-modifying code, so they 
    make it difficult, but not impossible, for a program 
    to write over itself."
   
I have chosen to use Mr. Kelly-Bootle's remarks, not because 
I consider his to be any more naive than those of other 
authors concerning the same subject.  Rather, I have chosen 
his book to be a very reputable source; to what end would I 
choose a non-reputable source?
     I cannot dispute the sincerity of Mr. Kelly-Bootle's 
remarks, nor can I verify or refute his claim of Motorola's 
concerns and intentions.  But I most certainly can say that 
the notion of a microprocessor manufacturer deliberately 
hindering the processing power of a microprocessor leaves me 
breathless.  OK, that's a little strong.  Actually, the 
vehemency expressed in that sentence is somewhat pretended, 
and is merely a ploy which permits me to ventilate my 
opinion about the notion while indulging in a little private 
sick humor.
     But there is nothing sick about the concept of self-
modifying code, and there is nothing humorous about the idea 
of making it difficult.  Because it is this tool alone which 
permits the intelligence level of software to rise above 
mediocrity.  And say what you will about the power of the 
human brain, in some areas in is overwhelmingly bested by 
even mediocre software; and without the ability to self-
modify its programs, the human brain would be about as 
intelligent as a computer program with the same limitation.
     Unlike the sin of self-gratification, the sin of self-
modification will not cause blindness; however, it can lead 
to coitus interruptus.  This condition becomes evident when 
a row of bombs appear across the video screen.  It means, of 
course, that your self-modifying program has screwed things 
up enough to cause the generation of a software interrupt.
     I think that it is safe for me to say that the more 
intelligence you insert into your algorithms, the more 
likely they are to acquire the attribute of 
unpredictability.  So, if you permit them to engage in the 
perverse activity of self-modification, you had better be 
prepared to protect yourself from the consequences if they 
decide to run amuck.  Of course, your first defensive action 
involves quality control.  You can maintain rigid control by 
thoroughly understanding  each instruction used in an 
adaptive algorithm and by being able to precisely predict 
the effects upon the entire computer system as each is 
executed.

Scope of Chapter 7 and Relevant Considerations
  
     The algorithm that is the focus of this chapter is a 
custom trap that reconstructs itself in a disciplined manner 
to form an execution loop about an algorithm under test 
(AUT).  The address of the AUT is passed to the custom trap 
by an invoking program.  The trap copies the AUT to a area 
of memory that is reserved within the boundaries of the 
trap, constructs the execution loop, implements the loop and 
generates appropriate performance data concerning the AUT.  
According to the definition previous established, the 
algorithm to be developed in this chapter is an adaptive 
algorithm.
     As far as I know, there are two ways in which an 
adaptive algorithm can modify itself: it can generate 
executable code within its execution space or it can copy 
executable code from a designated location into that space.  
Of course, there are no restrictions concerning combinations 
of the two methods of adaptation.  In this discussion, I do 
not consider the simple alteration of declared variables to 
be adaptive, although I can understand why some would label 
this as self-modifying.  Neither do I consider the 
alteration of an algorithm's code by an outside agent to be 
adaptive.  When I say that an algorithm is adaptive, I mean 
that its structure permits it to modify its structure.
     While explaining the design and operation of the 
adaptive algorithm, I will mention all of the considerations 
that apply to the programming environment that I have 
adopted; that is the AssemPro environment.  These may not 
apply when other environments are used.  Furthermore, it 
should be understood that I will mention the considerations 
of which I am aware; I can't promise to be infallible.
     As you know, AssemPro provides more than one assembly 
option.  I have shown you some of the effects on produced 
code by each.  As you shall see, the mode used to assemble 
the adaptive algorithm partly determines its structure.  In 
addition, there is the mode of assembly used to generate the 
AUT's code to consider.  The results generated by the 
adaptive algorithm are determined to some extent by the 
assembly mode used on both the adaptive algorithm and the 
algorithm under test.

Initial Structure of the Adaptive Algorithm
  
     Figure 7.1A is a representation of the structure of the 
adaptive algorithm as it exists in memory before it has ever 
been invoked.  The structure is defined by four distinct 
sections: an initialization section; a fixed section which 
installs the AUT, replicates the fourth section and 
initiates execution of the loop; a block of memory in which 
the AUT and the replicated fourth section are to reside; and 
the section which contains the loop branch instruction, code 
to generate the performance report and a data section.
  
Figure 7.1A. Structure of the adaptive algorithm prior to 
initial invocation.
























     Figure 7.1B illustrates the structure of the program 
that contains the algorithm to be tested.  The hands in this 
figure, and those in figure 7.1C, are there to represent the 
movement of the algorithm under test from the invoking 
program to the adaptive algorithm.  These pictorials are 
actually perverse demonstrations of what does not happen.  I 
wish to graphically impress you with the fact that something 
much more powerful than mere movement of data is involved in 
this and in similar data transactions.  The code which forms 
the algorithm under test is not moved; it is copied.  I feel 
that the implications of this fact is deluded by the 
instruction used to perform the transaction.  The situation 
would be expressed much more clearly if the mnemonic for the 
instruction were copy instead of move.  Nevertheless, I too 
use the word move when I mean copy because that is the 
terminology I was taught.  As long as one remembers that 
this transaction we call move is non-destructive, and that 
the copied data remains intact and can be cloned as often as 
desired, either word can be used to indicated the 
transaction which actually takes place.

Figure 7.1B. Structure of the adaptive algorithm invoking 
program.























     The thoughts concerning the copying of data, versus the 
movement of data, expressed about figure 7.1B also apply to 
figure 7.1C.  There you see the AUT being moved into the 
space reserved within the adaptive algorithm.  The section 
of reserved space under the block pictorial of the AUT 
implies that the AUT is small enough so that it never fills 
the reserved space.  Of course, the length of the reserved 
space is programmable within the adaptive algorithm, and, in 
fact, the length of the reserved space could be set 
dynamically at run-time.
  
Figure 7.1C. Algorithm under test being installed within the 
reserved space of the adaptive algorithm.



























     After the AUT has been copied into the reserved space, 
the remaining instructions which form the adaptive algorithm 
and its data must be moved up into the reserved space, 
adjacent to the AUT.  The reason for this will be clearer 
when you view the source and the disassembly listing, but, 
briefly, this is done so that the loop branching instruction 
and attendant data is placed appropriately within the newly 
defined adaptive algorithm structure.  Figure 7.1D 
illustrates the appearance of a portion of the new 
structure.  An important section has been omitted from this 
drawing.
  
Figure 7.1D. Closing the gap between the algorithm under 
test and the fourth section to form the executable loop and 
attendant code.




























     Figure 7.1E is a pictorial of the adaptive algorithm 
structure after its initial invocation.  There you see the 
section that was omitted from figure 7.1D.  Remember that 
the Movable Loop Section and Data Section is not moved; it 
is copied; therefore, the original section of code remains 
in place, until it is removed deliberately or until the 
adaptive algorithm is removed from memory.  There is no 
reason that instructions to remove that section could not be 
included in the adaptive algorithm.  I did not include such 
instructions in this algorithm because the movable sections 
are replicated during each invocation of the trap; 
therefore, they must remain intact.  The structure shown in 
figure 7.1E is valid for all future invocations of the 
adaptive algorithm.  The initially installed AUT and 
attendant code is simply overwritten by future invocations.

Figure 7.1E. Structure of the adaptive algorithm after the 
initial invocation and during all subsequent invocations.
 





















     I have designed the adaptive algorithm as a custom trap 
so that it need simply be invoked by a program containing an 
algorithm for which the execution speed and requisite memory 
is desired.  When I began to design this trap, I realized 
that I could not anticipate all possible ramifications of 
AUT's assembled in the various assembly modes that I have 
discussed, nor could I apriorily judge the most suitable 
mode of assembly for the adaptive algorithm.  Therefore, I 
prepared two programs: one designed for PC-relative 
assembly, the other for Relocatable assembly.  Program 34 is 
a listing of the adaptive algorithm designed for PC-relative 
assembly.  The program installs the adaptive algorithm as 
custom trap #9.  A routine with the same trap number was 
used during the development of the SPEEDTST utility, but its 
usefulness in that function has expired, so it would be best 
not to have the older trap #9 routine in a position that 
might cause confusion about which routine is installed.

Program 34. The adaptive algorithm designed as a custom 
trap.  This particular program has been designed for 
assembly in the PC-relative mode.

 ; Program Name: TRAP_9P.S
 ; Version 1.009

 ; Assembly Instructions:

 ;    Assemble in PC-relative mode and save with a PRG extension.  TRAP_9R.S
 ; is a version of this program that must be assembled in Relocatable mode.
 ; I have prepared two versions because I can't predict the precise requirements
 ; of all possible algorithms which might invoke the custom trap that is 
 ; installed by this program.

 ; Program Function:

 ;    This is a LSR program that establishes a user defined trap #9.  It may
 ; be executed from the desktop, but you may prefer to copy it to the AUTO
 ; folder of your boot partition or floppy disk so that it will execute
 ; automatically during boot.

program_start:                  ; Calculate program size and retain result.
 lea        program_end, a3     ; Fetch program end address.
 suba.l     4(a7), a3           ; Subtract basepage address.

enter_supervisor_mode:
 move.l     #0, -(sp)           ; The zero turns on supervisor mode.
 move.w     #$20, -(sp)         ; Function = super = GEMDOS $20.
 trap       #1                  ; Supervisor stack pointer (SSP) returned in D0.
 addq.l     #6, sp             
 movea.l    d0, a5              ; Save SSP in scratch register.

install_trap_9_routine:         ; Note: pointer = vector = pointer.
 lea        trap_9_routine, a0  ; Fetch address of trap #9 routine.
 move.l     a0, $A4             ; Store trap address at pointer address.
 
enter_user_mode:
 pea        (a5)                ; Restore supervisor stack pointer.
 move.w     #$20, -(sp)         ; Function = super = GEMDOS $20.
 trap       #1
 addq.l     #6, sp 

relinquish_processor_control:   ; Maintain memory residency.
 move.w    #0, -(sp)            ; Exit code. 
 move.l    a3, -(sp)            ; Program size.
 move.w    #$31, -(sp)          ; Function = ptermres = GEMDOS $31.
 trap      #1

trap_9_routine:

 ; NOTE: You may want to execute a program that invokes this trap from the
 ;       AssemPro debugger and single step through the trap instructions, or
 ;       you many want to set breakpoints and use the "Run program" button to
 ;       execute to a breakpoint.  It the exercise of this latter option that
 ;       can cause problems.  If you want to set a breakpoint at an instruction
 ;       that occurs before the "reserved space", no precautions need be taken,
 ;       except that you must realize that you could halt at a position after
 ;       the start time has been initialized, and the execution time will be
 ;       accumulating during the halt.

 ;       But, if you want to set a breakpoint at at an instruction that occurs
 ;       after the "reserved space", you should not do so until the instructions
 ;       that perform the bulk move have been executed.  If you set a breakpoint
 ;       at an instruction in the program space which follows the "reserved
 ;       space" and then execute the bulk move instructions, the breakpoint you
 ;       have set will cause an illegal command error. 

 ; This custom trap must be invoked by a program which contains one or more
 ; algorithms for which performance data, in the form of execution time and
 ; requisite memory, is desired.  The trap must be invoked once for each 
 ; algorithm under test (AUT).  The trap is intended to be a performance 
 ; report generator so that performance data for specific algorithms can be
 ; compared.

 ; If the program invoking the trap is spawned by SPAWN.TTP, the performance
 ; data will be printed to a file that is created by SPAWN.TTP.  The name of
 ; the file will be the name of the spawned program with a DAT suffix.

 ; If the program invoking the trap is executed from the desktop, the 
 ; performance data will be printed to the screen.

 ; The AUT can be assembled in PC-relative or Relocatable mode.

 ; The custom trap expects the following parameters to be contained in the
 ; specified registers prior to invocation:

 ; A0 = The address of a null terminated header to precede the reported
 ;      AUT execution time.

 ; A1 = The address of a null terminated header to precede the reported
 ;      AUT requisite memory.

 ; A3 = The starting address of an algorithm containing one or more instructions.
 ;      This algorithm becomes the AUT upon invocation of the trap.

 ; A4 = The ending address of the AUT.

 ; A5 = At the initial invocation by a specific program, A5 is expected to
 ;      contain the address of a null terminated heading that is a brief
 ;      description of the data that is to be reported by the trap.  During
 ;      all subsequent invocations by that program, A5 must contain the
 ;      address of a null string.

 ; D7 = A word length decimal value which specifies the number of times the
 ;      the AUT is to be executed in a loop in order to generate the execution
 ;      time data.  Register D7 is the only register which cannot be used by
 ;      the AUT.  That's because D7 is used as the AUT execution loop counter.

 ; The custom trap uses the information passed in A3, A4 and D7 to construct
 ; a loop around the AUT.  The loop is executed the number of times specified
 ; in register D7.  The time required to execute the loop is calculated and
 ; printed along with the AUT's requisite memory.

 ; How Trap #9 Works:

 ;     The custom trap is an intelligent, self-modifying algorithm.  Prior
 ; to an initial invocation, the trap #9 routine is composed of three sections.
 ; The first section contains instructions which are permanently located.  The
 ; second section is a 1,024 byte block of reserved space into which the AUT
 ; and the third section is to be copied.  The third section contains the custom
 ; trap instructions that must be copied so that the first instruction in the
 ; third section immediately follows the last instruction of the algorithm
 ; under test.  The size that I chose for the reserved space was arbitrary.
   
 ;     After an invocation, the custom trap calculates the number of bytes in
 ; the algorithm under test.  Then it initializes register D7 for the AUT's
 ; execution loop.  After saving the addresses of the headers that were passed
 ; as parameters so that the registers in which they were passed can be used
 ; by trap #9 and/or the algorithm under test, the trap prints the AUT's
 ; primary heading and the execution time header.  Then it copies the AUT into
 ; the reserved space.

 ;     After the AUT has been copied into the reserved space, the instructions
 ; and data in the third section of the custom trap are moved into immediate
 ; proximity of the AUT so that the first instruction of section three follows
 ; immediately after the last instruction of the algorithm under test.

 ;     The AUT is executed the number of times requested via the value passed
 ; in D7, then the execution time and requisite memory of the AUT are printed.

 ;     After the custom trap has been invoked once, the reserved space will
 ; not be completely clear during the remaining portion of the power-up cycle.
 ; When the trap is subsequently invoked, the instructions that are already in
 ; the reserved space will simply be overwritten by the instructions of the
 ; new algorithm under test and those of the third section.

calculate_length_of_AUT:
 suba.l     a3, a4               ; Subtract start address from end address.

save_heading_addresses:
 lea        time_header, a2      ; Header to precede reported execution time.
 move.l     a0, (a2)            
 lea        memory_header, a2    ; Header to precede reported requisite memory.
 move.l     a1, (a2)           

transfer_stack_pointer:

 ; Upon entrance into this custom trap, A7 contains the address of the system
 ; stack pointer.  Because the system stack may be too short for use by the AUT,
 ; the invoking program must provide a user stack, and, here, I am going to
 ; store the address of that stack in A7.  Before returning to the invoking
 ; program, the system stack pointer must be restored so that the return address
 ; can be found by the processor.

 lea        _SSP, a0             ; Fetch address of declared variable.
 move.l     a7, (a0)             ; Save system stack pointer.
 move       USP, a7              ; Transfer to invoking program's stack.

print_heading:

 ; NOTE: When two or more algorithms are to invoke the trap from a program,
 ;       the heading should be printed only once, at the beginning of the
 ;       report; therefore, the string address in A5 should point to a
 ;       null terminated string during the first invocation of the trap, but
 ;       it should point to a null string on subsequent invocations from the
 ;       same program.
 
 ;       For that reason, the test for NULL string is included below, so that
 ;       only one attempt to print the heading will be made.

 tst.b      (a5)                 ; NULL string test.
 beq.s      print_time_header    ; Branch if null.
 movea.l    a5, a0               ; Print heading.
 bsr        print_string

print_time_header:
 movea.l    time_header, a0      ; Fetch address of time header.
 bsr        print_string

build_algorithm:
 lea        reserved_space, a6   ; Fetch address of reserved space.
 move.w     a4, d3               ; AUT length initializes counter for copy.
 lea        memory, a0           ; Store AUT's requisite memory.
 move.w     d3, (a0)             ; AUT length stored for report.
 subq.w     #1, d3               ; Initialize counter for loop execution.
move_loop:                       ; Move AUT, byte by byte, to the area
 move.b     (a3)+, (a6)+         ; declared as "reserved_space".
 dbra       d3, move_loop        ; Branch until D3 = -1.

 ; A6 is now pointing to the location at which the AUT execution loop's DBRA
 ; instruction must be copied.  The DBRA copy must be processed apart from the
 ; other instructions in the custom trap which must be copied to "close up" the
 ; gap between the last statement of the algorithm under test and the rest
 ; of the custom trap's instructions.

 lea        algorithm_end, a0    ; Calculate number of bytes in this program
 lea        program_end, a1      ; which must be copied into "reserved_space",
 suba.l     a0, a1               ; then initialize counter D3 with the number
 move.w     a1, d3               ; of bytes to copy.
 subq.w     #4, d3               ; Subtract the DBRA requisite memory.
 movea.l    a0, a1               ; Calculate amount the DBRA instruction must
 suba.l     a6, a1               ; be moved and save the new location in scratch
 movea.l    a6, a5               ; register for displacement correction.
 move.w     2(a0), d0            ; Fetch current DBRA displacement value.
 move.l     (a0)+, (a6)+         ; Move the DBRA instruction.
 add.w      a1, d0               ; Correct DBRA displacement to the value it
 move.w     d0, 2(a5)            ; should be after the move.
 subq.w     #1, d3               ; Initialize counter for bulk copy.
_move_loop:                      ; Move rest of algorithm in a bulk copy.
 move.b     (a0)+, (a6)+
 dbra       d3, _move_loop
 subq.w     #1, d7               ; Initialize D7 for AUT loop execution.
 lea        start_time, a0       ; Fetch address of declared variable.
 suba.l     a1, a0               ; Correct address to after-move location.

 ; NOTE: Since processor is in supervisor mode, there is no reason to use
 ;       trap #3 to fetch time.  The 200hz vector can be referenced directly.

 move.l     $4BA, (a0)           ; Fetch and store start time.

algorithm_start:                 ; new location.
reserved_space:  ds.b  1024      ; Space for loop construction = 1024 bytes.
algorithm_end:
 dbra       d7, algorithm_start
 move.l     $4BA, d0             ; Fetch end time.
 sub.l      start_time, d0       ; Subtract start time from end time.
 trap       #10                  ; Convert to decimal milliseconds and print.
print_memory_header:
 movea.l    memory_header, a0    ; Fetch address of memory header.
 bsr.s      print_string
print_requisite_memory:
 move.w     memory, d1           ; Fetch AUT's requisite memory.
 trap       #4                   ; Returns address of decimal string in A0.
 bsr.s      print_string
 lea        header_1, a0         ; Print requisite memory units label.
 bsr.s      print_string

 ; NOTE:  I had thought that I might have to restore the user stack pointer
 ;        before returning to the calling program because I can't know to what
 ;        extent the AUT has corrupted the user stack.

 ;        But, as it turns out, since the value in USP is stored in register
 ;        A7 at the beginning of the program, and since the system stack pointer
 ;        is then active and remains so for the duration of the trap invocation,
 ;        only the value in register A7 (which is the system stack pointer, but
 ;        which points to the user stack) is altered; the value in USP remains
 ;        uncorrupted, therefore, nothing needs be restored but the system stack
 ;        pointer (so that it again points to the system stack).

 ;        On subsequent invocations the value in USP, which remains stable, will
 ;        simply be restored in A7, as often as the trap is invoked.

 movea.l    _SSP, a7             ; Restore system stack pointer so that it
 rte                             ; points to the system stack.

 ;
 ; SUBROUTINES
 ;

print_string:         
 pea        (a0)
 move.w     #9, -(sp) 
 trap       #1        
 addq.l     #6, sp    
 rts

 data
header_1:      dc.b '  bytes',$D,$A,0
 bss
 align
_SSP:          ds.l    1   ; Address of the system stack will be stored here.
start_time:    ds.l    1   ; Variable for time at start of AUT processing.
memory:        ds.w    1   ; Variable for AUT's requisite memory.
time_header:   ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT processing time.
memory_header: ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT requisite memory.
program_end:   ds.l    0
 end

 
     Comprehension of program 34 will be facilitated with 
reference to a disassembly listing of the program as it 
resides in memory.  Figure 7.2 is a portion of that listing.  
A section of the reserved space has been deleted in order to 
reduce the size of the listing.  This listing shows the code 
for the trap before any program has invoked it.

Figure 7.2. Disassembly listing of TRAP_9P.PRG as it resides 
in memory before an initial invocation.

 TRAP_9P.PRG Before First Invocation

01FA36 99CB             SUBA.L A3,A4
01FA38 45FA04B4         LEA $1FEEE(PC),A2
01FA3C 2488             MOVE.L A0,(A2)
01FA3E 45FA04B2         LEA $1FEF2(PC),A2
01FA42 2489             MOVE.L A1,(A2)
01FA44 41FA049E         LEA $1FEE4(PC),A0
01FA48 208F             MOVE.L A7,(A0)
01FA4A 4E6F             MOVE.L USP,A7
01FA4C 4A15             TST.B (A5)
01FA4E 6706             BEQ.S $1FA56
01FA50 204D             MOVEA.L A5,A0
01FA52 6100047A         BSR $1FECE
01FA56 207A0496         MOVEA.L $1FEEE(PC),A0
01FA5A 61000472         BSR $1FECE
01FA5E 4DFA0046         LEA $1FAA6(PC),A6
01FA62 360C             MOVE.W A4,D3
01FA64 41FA0486         LEA $1FEEC(PC),A0
01FA68 3083             MOVE.W D3,(A0)
01FA6A 5343             SUBQ.W #1,D3
01FA6C 1CDB             MOVE.B (A3)+,(A6)+
01FA6E 51CBFFFC         DBRA D3,$1FA6C
01FA72 41FA0432         LEA $1FEA6(PC),A0
01FA76 43FA047E         LEA $1FEF6(PC),A1
01FA7A 93C8             SUBA.L A0,A1
01FA7C 3609             MOVE.W A1,D3
01FA7E 5943             SUBQ.W #4,D3
01FA80 2248             MOVEA.L A0,A1
01FA82 93CE             SUBA.L A6,A1
01FA84 2A4E             MOVEA.L A6,A5
01FA86 30280002         MOVE.W 2(A0),D0
01FA8A 2CD8             MOVE.L (A0)+,(A6)+
01FA8C D049             ADD.W A1,D0
01FA8E 3B400002         MOVE.W D0,2(A5)
01FA92 5343             SUBQ.W #1,D3
01FA94 1CD8             MOVE.B (A0)+,(A6)+
01FA96 51CBFFFC         DBRA D3,$1FA94
01FA9A 5347             SUBQ.W #1,D7
01FA9C 41FA044A         LEA $1FEE8(PC),A0
01FAA0 91C9             SUBA.L A1,A0
01FAA2 20B804BA         MOVE.L $4BA,(A0)
01FAA6 00000000         ORI.B #0,D0
01FAAA 00000000         ORI.B #0,D0

 NOTE: Section of reserved space omitted
       to reduce size of listing.
 
01FE9E 00000000         ORI.B #0,D0
01FEA2 00000000         ORI.B #0,D0
01FEA6 51CFFBFE         DBRA D7,$1FAA6
01FEAA 203804BA         MOVE.L $4BA,D0
01FEAE 90BA0038         SUB.L $1FEE8(PC),D0
01FEB2 4E4A             TRAP #$A
01FEB4 207A003C         MOVEA.L $1FEF2(PC),A0
01FEB8 6114             BSR.S $1FECE
01FEBA 323A0030         MOVE.W $1FEEC(PC),D1
01FEBE 4E44             TRAP #4
01FEC0 610C             BSR.S $1FECE
01FEC2 41FA0016         LEA $1FEDA(PC),A0
01FEC6 6106             BSR.S $1FECE
01FEC8 2E7A001A         MOVEA.L $1FEE4(PC),A7
01FECC 4E73             RTE
01FECE 4850             PEA (A0)
01FED0 3F3C0009         MOVE.W #9,-(A7)
01FED4 4E41             TRAP #1
01FED6 5C8F             ADDQ.L #6,A7
01FED8 4E75             RTS
01FEDA 2020             MOVE.L -(A0),D0
01FEDC 6279             BHI.S $1FF57
01FEDE 7465             MOVEQ #$65,D2
01FEE0 730D             DC.W $730D
01FEE2 0A00FF0A         EORI.B #$A,D0
01FEE6 00000000         ORI.B #0,D0
01FEEA 00000000         ORI.B #0,D0
01FEEE 00000000         ORI.B #0,D0
01FEF2 00000000         ORI.B #0,D0

 
Analysis of TRAP_9P
  
     The analysis of program 34 begins at the label 
algorithm_start in the source listing, at address 01FAA6 in 
the disassembly listing.  The label reserved_space in the 
source listing is superfluous, serving only to indicate that 
the 1024 bytes of defined space is sandwiched between the 
two labels algorithm_start and algorithm_end, which locate 
the boundaries of the algorithm under test after it has been 
installed.  Note that neither the data nor the bss assembler 
pseudo-ops are used before the ds.b 1024 pseudo-op.  If the 
data and bss pseudo-ops are used in conjunction with the 
ds.b pseudo-op to define the reserved space, AssemPro will 
locate the 1024 bytes of defined space in the program's data 
section; therefore, the space reserved would not be between 
the labels that mark the boundaries of the AUT.  That 
relocation of the reserved space is not necessarily 
prejudicial to the structure of an adaptive algorithm if it 
is considered during the design of the algorithm; but it is 
important to know the precise effect of every instruction 
and pseudo-op when dealing with self-modifying algorithms.

Moving the DBRA Instruction
  
     Refer to the dbra instruction at address 01FEA6 in the 
disassembly listing.  The disassembler displays the entire 
instruction in a format that is pleasing to the eye, DBRA 
D7, $1FAA6, because it enables us to readily discern the 
value that will be loaded into the program counter when the 
branch is taken.  But this convenience tends to obscure the 
fact that the instruction exists in memory as 51CFFBFE, 
which is not as pretty, but which more accurately portrays 
the activity involved in assembling and executing the dbra 
instruction.  To wit: the assembler calculates a signed 
displacement between the dbra instruction and a label and 
stores this displacement in the extension word which follows 
the instruction word.  In this particular case, the 
displacement is $FBFE = -1026 (decimal).
     The important thing to realize is that the displacement 
is fixed during assembly and will not change when the dbra 
instruction is copied into the reserved space, following the 
insertion of the AUT.  But the distance between address 
01FAA6 and the dbra instruction will be less then than it is 
now; therefore, something must be done to alter the value in 
the dbra extension word after the instruction has been 
copied into the reserved space.
     Within the source listing, following the two 
instructions after the move_loop label, there is a note 
concerning the movement of the dbra instruction into the 
reserved space.  It is the necessity for the displacement 
correction which requires that the dbra move be accomplished 
in a single transaction, apart from the movement of the 
other code comprising the movable sections.  The source 
listing documentation which accompanies the instructions 
following the note explains the steps involved in 
calculating a new displacement value, but since some of 
those instructions are specific to the movement of the code 
following the dbra instruction, I will repeat the steps here 
so that cognition may be confirmed.

     1. Calculate the total number of bytes of code which 
        must be copied into the reserved space after the AUT 
        has been installed.  This value is the number of 
        bytes existing between the label algorithm_end and 
        the end of the program. It is calculated in register 
        A1, then copied into register D3, which is used as a 
        loop counter when all but the dbra instruction 
        portion of the movable sections are copied into the 
        reserved space.

     2. Because the dbra instruction will be moved apart 
        from the other instruction in the section, its 
        requisite memory (4 bytes) must be subtracted from 
        the counter, D3, before the bulk copy takes place.

     3. Calculate the displacement between the dbra 
        instruction's current location and the location at 
        which it is to be copied.  The dbra instruction's 
        current location is marked by the label 
        algorithm_end, which is still stored in register A0.  
        The value in A0 must be preserved for future 
        calculations, therefore, it is copied into A1.  The 
        value in register A6 is the location to which the 
        dbra instruction must be moved.  Subtracting A6 from 
        A1 puts the number of bytes that the dbra 
        instruction must be moved into A1.  The extension 
        word correction to follow requires that the value in 
        A6 be preserved, so it is copied into register A5.

     4. Fetch the current dbra displacement value.  In the 
        source listing, you can see that this value is 
        stored in register D0.

     5. Move (or copy) the dbra instruction into its new 
        location.

     6. Correct the dbra instruction's displacement value.  
        The correction must be a positive value because the 
        distance between the branch instruction and the 
        branch location has decreased.  Register A1 contains 
        the previously calculated correction, which is 
        simply the number of bytes that the dbra instruction 
        was moved.  In the source listing, you can see that 
        the positive value in A1 is added to the negative 
        value in D0 to obtain the new displacement value.  
        Then the contents of D0 are written to the dbra 
        extension word's new location at 2(A5) with a self-
        modifying instruction.

     The effect of the above steps can be seen in figure 
7.3, a disassembly listing of program 34 after a single 
instruction AUT, MULU #5,D0, has been installed in the 
reserved space, at address 01FAA6.  The new dbra 
displacement is shown in the instruction following; it is 
$FFFA = -6 (decimal).  Within the listing are several notes, 
shown in boldface, that explain specific instruction groups.

Figure 7.3 Disassembly listing of the adaptive algorithm 
portion of TRAP_9P.PRG as it resides in memory after the 
initial invocation.

 TRAP_9P.PRG After First Invocation

01FA36 99CB         SUBA.L A3,A4
01FA38 45FA04B4     LEA $1FEEE(PC),A2
01FA3C 2488         MOVE.L A0,(A2)
01FA3E 45FA04B2     LEA $1FEF2(PC),A2
01FA42 2489         MOVE.L A1,(A2)
01FA44 41FA049E     LEA $1FEE4(PC),A0
01FA48 208F         MOVE.L A7,(A0)
01FA4A 4E6F         MOVE.L USP,A7
01FA4C 4A15         TST.B (A5)
01FA4E 6706         BEQ.S $1FA56
01FA50 204D         MOVEA.L A5,A0
01FA52 6100047A     BSR $1FECE
01FA56 207A0496     MOVEA.L $1FEEE(PC),A0
01FA5A 61000472     BSR $1FECE
01FA5E 4DFA0046     LEA $1FAA6(PC),A6
01FA62 360C         MOVE.W A4,D3
01FA64 41FA0486     LEA $1FEEC(PC),A0
01FA68 3083         MOVE.W D3,(A0)
01FA6A 5343         SUBQ.W #1,D3
01FA6C 1CDB         MOVE.B (A3)+,(A6)+
01FA6E 51CBFFFC     DBRA D3,$1FA6C
01FA72 41FA0432     LEA $1FEA6(PC),A0
01FA76 43FA047E     LEA $1FEF6(PC),A1
01FA7A 93C8         SUBA.L A0,A1
01FA7C 3609         MOVE.W A1,D3
01FA7E 5943         SUBQ.W #4,D3
01FA80 2248         MOVEA.L A0,A1
01FA82 93CE         SUBA.L A6,A1
01FA84 2A4E         MOVEA.L A6,A5
01FA86 30280002     MOVE.W 2(A0),D0
01FA8A 2CD8         MOVE.L (A0)+,(A6)+
01FA8C D049         ADD.W A1,D0
01FA8E 3B400002     MOVE.W D0,2(A5)
01FA92 5343         SUBQ.W #1,D3
01FA94 1CD8         MOVE.B (A0)+,(A6)+
01FA96 51CBFFFC     DBRA D3,$1FA94
01FA9A 5347         SUBQ.W #1,D7
01FA9C 41FA044A     LEA $1FEE8(PC),A0
01FAA0 91C9         SUBA.L A1,A0
01FAA2 20B804BA     MOVE.L $4BA,(A0)
01FAA6 C0FC0005     MULU #5,D0      ; AUT
01FAAA 51CFFFFA     DBRA D7,$1FAA6  ; FFFA = -6
01FAAE 203804BA     MOVE.L $4BA,D0
01FAB2 90BA0038     SUB.L $1FAEC(PC),D0
01FAB6 4E4A         TRAP #$A
01FAB8 207A003C     MOVEA.L $1FAF6(PC),A0
01FABC 6114         BSR.S $1FAD2
01FABE 323A0030     MOVE.W $1FAF0(PC),D1
01FAC2 4E44         TRAP #4
01FAC4 610C         BSR.S $1FAD2
01FAC6 41FA0016     LEA $1FADE(PC),A0
01FACA 6106         BSR.S $1FAD2
01FACC 2E7A001A     MOVEA.L $1FAE8(PC),A7
01FAD0 4E73         RTE

 Below is the print_string subroutine.

01FAD2 4850         PEA (A0)
01FAD4 3F3C0009     MOVE.W #9,-(A7)
01FAD8 4E41         TRAP #1
01FADA 5C8F         ADDQ.L #6,A7
01FADC 4E75         RTS

 The data section appears below.

01FADE 2020         MOVE.L -(A0),D0  ;'  '
01FAE0 6279         BHI.S $1FB5B     ;by
01FAE2 7465         MOVEQ #$65,D2    ;te
01FAE4 730D         DC.W $730D       ;s

 _SSP => $01FAE8

01FAE6 0A000003     EORI.B #3,D0
01FAEA EF3A         ROL.B D7,D2

 start_time (new address) = 01FAEC

01FAEC 00000000     ORI.B #0,D0

 memory => 01FAF0
 time_header => 01FAF2
      
01FAF0 00040006     ORI.B #6,D4

 memory_header => 01FAF6

01FAF4 DBB90006DC1F ADD.L D5,$6DC1F
01FAFA 00000000     ORI.B #0,D0
01FAFE 00000000     ORI.B #0,D0

 NOTE: Section of reserved space omitted
       to reduce size of listing.

01FE9E 00000000     ORI.B #0,D0
01FEA2 00000000     ORI.B #0,D0

 Below is the original movable block.  It has not
 been effected by the move.

01FEA6 51CFFBFE     DBRA D7,$1FAA6
01FEAA 203804BA     MOVE.L $4BA,D0
01FEAE 90BA0038     SUB.L $1FEE8(PC),D0
01FEB2 4E4A         TRAP #$A
01FEB4 207A003C     MOVEA.L $1FEF2(PC),A0
01FEB8 6114         BSR.S $1FECE
01FEBA 323A0030     MOVE.W $1FEEC(PC),D1
01FEBE 4E44         TRAP #4
01FEC0 610C         BSR.S $1FECE
01FEC2 41FA0016     LEA $1FEDA(PC),A0
01FEC6 6106         BSR.S $1FECE
01FEC8 2E7A001A     MOVEA.L $1FEE4(PC),A7
01FECC 4E73         RTE
01FECE 4850         PEA (A0)
01FED0 3F3C0009     MOVE.W #9,-(A7)
01FED4 4E41         TRAP #1
01FED6 5C8F         ADDQ.L #6,A7
01FED8 4E75         RTS
01FEDA 2020         MOVE.L -(A0),D0
01FEDC 6279         BHI.S $1FF57
01FEDE 7465         MOVEQ #$65,D2
01FEE0 730D         DC.W $730D
01FEE2 0A000003     EORI.B #3,D0
01FEE6 EF3A         ROL.B D7,D2

 start_time (old address) = 01FEE8

01FEE8 00000000     ORI.B #0,D0
01FEEC 00040006     ORI.B #6,D4
01FEF0 DBB90006DC1F ADD.L D5,$6DC1F

          
The Bulk Move
  
     The rest of the code in the movable section can be 
moved as a block.  This transaction takes place at the 
_move_loop label in the source listing, at address 01FA94 in 
the disassembly listings.  Note that immediately after the 
block move, the address of the declared variable start_time 
is loaded into register A0, and that, before the time is 
fetched, the contents of register A1 are subtracted from 
those of A0 to correct the address in register A0.  These 
transactions take place at addresses 01FA9C and 01FAA0 of 
the disassembly listings.

Why The Address Of start_time Must BE Corrected
  
     From time to time, we must remind ourselves that pc-
relative addressing can be used discriminatingly, by 
including the (pc) notation in the source operand, or it can 
be forced by the PC-relative assembly mode.  Now, although 
it may not be obvious from discussions in the references, 
when pc-relative addressing is used in the source operand of 
the LEA instruction, it, like the DBRA instruction, performs 
its transaction with a displacement stored in its extension 
word.  This is evident from the machine code at address 
01FA9C, where the extension word can be seen to be $044A = 
1098 (decimal).  To confirm that this is indeed the 
displacement between the LEA instruction and the label 
start_time we need only subtract their addresses:

               $01FEE8 - $01FA9C = $44C
  
and from this subtract the size of the LEA instruction:
  
                $44C - 2 bytes = $44A.
  
     Now, to decide whether or not a correction to this 
displacement is necessary, we need only determine whether or 
not the displacement between the two addresses is altered by 
the bulk move.  Well, of course it does.  The instruction 
and the label will be closer after the move, and, since the 
label will be moved the same distance as was the dbra 
instruction, the same correction factor, which is still in 
A1,  must be applied.  The displacement in the LEA 
instruction's extension word must be corrected at this point 
in the program because the location in which the start time 
is stored will be accessed to compute the AUT's execution 
time after the algorithm_start loop has been executed.  You 
can see that transaction taking place at address 01FAB2 of 
figure 7.3.  There you can also see that the new 
displacement is $0038, and that start_time's new address is 
01FAEC.
     Program 35 is a source listing of the program designed 
to confirm the rudimentary reliability of the adaptive 
algorithm in program 34.  The performance data for the AUTs 
in program 35 should (and does) match that obtained with 
program 32 because the algorithms were copied from that 
program.  The data generated by program 35 follows its 
listing.

Program 35. This program is used to verify that program 34 
functions correctly.

 ; Program Name: TRAP9TST.S
 ;      Version: 1.001

 ; Assembly Instructions:

 ;     Assemble in PC-relative mode and save with a TOS extension.

 ; Execution Instructions:

 ;     Execute from the desktop; or execute SPAWN.TTP, type TRAP9TST.TOS on
 ; its command line and view this program's output in TRAP9TST.DAT.

 ; Program Function:

 ;     Measures the speed of multiplication algorithms.  Verifies that
 ; TRAP_9P functions correctly.

calculate_program_size:
 lea        -$102(pc), a1       ; Fetch basepage start address.
 lea        program_end, a0     ; Fetch program end = array address.
 trap       #6                  ; Return unused memory to op system.
 lea        stack, a7

the_mulu_instruction:
 lea        header_1, a0       
 lea        header_4, a1
 lea        mulu_algorithm_start, a3
 lea        mulu_algorithm_end, a4
 lea        heading, a5
 move.w     #50000, d7

invoke_trap_9:
 trap       #9

addition:
 lea        header_2, a0       
 lea        header_5, a1
 lea        addition_algorithm_start, a3
 lea        addition_algorithm_end, a4
 lea        heading, a5
 move.b     #0, (a5)            ; Store a NULL in first byte to create a
 move.w     #50000, d7          ; null string so that heading gets printed
 trap       #9                  ; only once.

shift_and_add:
 lea        header_3, a0       
 lea        header_6, a1
 lea        shift_and_add_algorithm_start, a3
 lea        shift_and_add_algorithm_end, a4
 lea        heading, a5
 move.w     #50000, d7
 trap       #9

terminate:
 trap       #8

mulu_algorithm_start:
 mulu       #5, d0              ; Instruction in the loop.
mulu_algorithm_end:

addition_algorithm_start:
 move.l     d0, d2              ; To add one.   
 add.l      d0, d0              ; To double to two.
 add.l      d0, d0              ; To double to four.
 add.l      d2, d0              ; To complete multiplication by 5.
addition_algorithm_end:

shift_and_add_algorithm_start:
 move.l     d0, d2              ; Save a copy to add.
 asl.l      #2, d0              ; Shift to multiply by 4. 
 add.l      d2, d0              ; To complete multiplication by 5.
shift_and_add_algorithm_end:

 data
heading:      dc.b   "TRAP9TST Execution Results",$D,$A,$D,$A,0
header_1:     dc.b       "   MULU time:                    ",0
header_2:     dc.b       "   Addition time:                ",0
header_3:     dc.b       "   Shift and add time:           ",0
header_4:     dc.b       "   MULU requisite memory:           ",0
header_5:     dc.b       "   Addition requisite memory:       ",0
header_6:     dc.b       "   Shift and add requisite memory:  ",0
 bss
 align
              ds.l 96
stack:        ds.l  0
program_end:  ds.l  0
 end

TRAP9TST Execution Results

   MULU time:                      360  milliseconds
   MULU requisite memory:            4  bytes
   Addition time:                  260  milliseconds
   Addition requisite memory:        8  bytes
   Shift and add time:             235  milliseconds
   Shift and add requisite memory:   6  bytes


A Relocatable Version of the Adaptive Algorithm

     The adaptive algorithm may also be installed as a trap 
that has been assembled in AssemPro's Relocatable mode.  
According to definitions previously established, program 36 
is probably more appropriately designated as a Combo version 
of program 34, because pc-relative addressing is used as 
circumstances permit.  The choice of assembly modes for LSR 
programs is a bit more engaging than it is for other types 
of programs because the length of time that the program is 
resident is so much longer than the load time.  It may be 
that one decides to accept the longer load time as a 
condition of receiving some other benefit via Relocatable 
assembly, or it may be that circumstances dictate the 
assembly mode.
     From the beginning of the book, my emphasis has been on 
the quest for speed.  To me it seems that all other 
desirable software attributes precipitate naturally from the 
quest for this single feature.  Consider the reason we use 
computers in the first place.  Were speed not the most 
compelling issue, computers would probably not have been 
invented.  That's why, in formulating my thoughts for the 
current discussion, I anticipated that the relative speed of 
the PC-relative assembled adaptive algorithm versus that of 
the Relocatable assembled algorithm would be the most 
obvious primary topic.  But, as it turns out, my attention 
was drawn to a more compelling consideration: that of the 
AUT's addressing and assembly modes.
     As I mentioned in program 34's documentation, at the 
time that I designed that program, I could not predict the 
requirements of all possible AUTs, but I did guess that a 
Relocatable version of the adaptive algorithm might be 
desirable, or required, for some invoking algorithms.  
Simultaneously, I guessed that there would be times when one 
or the other assembly modes might be preferable for the AUT.  
It was while I was comparing the first few lines of the 
disassembly listing for the Relocatable version of the 
custom trap to that of the PC-relative version that I was 
struck with the realization that the assembly mode chosen 
for the AUT would at times be dictated by the instructions 
comprising that algorithm.  Then, if instructions in the AUT 
were to store data in locations being referenced via a 
displacement, that data could be written into the adaptive 
algorithm's program area, thereby disruptively modifying the 
adaptive algorithm.  To illustrate this phenomenon, I have 
chosen a suitable AUT, but first, let me present the source 
file and disassembly listing for program 36.

Program 36. The adaptive algorithm designed for Relocatable 
Assembly.  Execution results follow the listing.

 ; Program Name: TRAP_9R.S
 ; Version 1.005

 ; Assembly Instructions:

 ;    Assemble in Relocatable mode and save with a PRG extension.  TRAP_9P.S
 ; is a version of this program that can be assembled in PC-relative mode.
 ; I have prepared two versions because I can't predict the precise requirements
 ; of all possible algorithms which might invoke the custom trap that is 
 ; installed by this program.

 ; Program Function:

 ;    This is a LSR program that establishes a user defined trap #9.  It may
 ; be executed from the desktop, but you may prefer to copy it to the AUTO
 ; folder of your boot partition or floppy disk so that it will execute
 ; automatically during boot.

program_start:                  ; Calculate program size and retain result.
 lea        program_end(pc), a3 ; Fetch program end address.
 suba.l     4(a7), a3           ; Subtract basepage address.

enter_supervisor_mode:
 move.l     #0, -(sp)           ; The zero turns on supervisor mode.
 move.w     #$20, -(sp)         ; Function = super = GEMDOS $20.
 trap       #1                  ; Go to supervisor mode.
 addq.l     #6, sp              ; Supervisor stack pointer (SSP) returned in D0.
 movea.l    d0, a5              ; Save SSP in scratch register.

install_trap_9_routine:         ; Store trap address at pointer address.
 move.l     #trap_9_routine, $A4

enter_user_mode:
 pea        (a5)                ; Restore supervisor stack pointer.
 move.w     #$20, -(sp)         ; Function = super = GEMDOS $20.
 trap       #1
 addq.l     #6, sp

relinquish_processor_control:   ; Maintain memory residency.
 move.w    #0, -(sp)            ; Exit code.
 move.l    a3, -(sp)            ; Program size.
 move.w    #$31, -(sp)          ; Function = ptermres = GEMDOS $31.
 trap      #1

trap_9_routine:

 ; See documentation in program TRAP_9P.S.

calculate_length_of_AUT:
 suba.l     a3, a4               ; Subtract start address from end address.

save_heading_addresses:
 move.l     a0, time_header      ; Header to precede reported execution time.
 move.l     a1, memory_header    ; Header to precede reported requisite memory.
                             
transfer_stack_pointer:

 ; See documentation in program TRAP_9P.S.

 move.l     a7, _SSP             ; Save system stack pointer.
 move       USP, a7              ; Transfer to invoking program's stack.

print_heading:

 ; See documentation in program TRAP_9P.S.

 tst.b      (a5)                 ; NULL string test.
 beq.s      print_time_header    ; Branch if null.
 movea.l    a5, a0               ; Print heading.
 bsr        print_string

print_time_header:
 movea.l    time_header(pc), a0  ; Fetch address of time header.
 bsr        print_string

build_algorithm:
 lea        reserved(pc), a6     ; Fetch address of reserved space.
 move.w     a4, d3               ; AUT length initializes counter for copy.
 move.w     d3, memory           ; AUT length stored for report.
 subq.w     #1, d3               ; Initialize counter for loop execution.
move_loop:                       ; Move AUT, byte by byte, to the area
 move.b     (a3)+, (a6)+         ; declared as "reserved".
 dbra       d3, move_loop        ; Branch until D3 = -1.

 ; See documentation in program TRAP_9P.S.

 lea        aut_end(pc), a0      ; Calculate number of bytes in this program
 lea        program_end(pc), a1  ; which must be moved into "reserved space",
 suba.l     a0, a1               ; then initialize counter D3 with the number
 move.w     a1, d3               ; of bytes to copy.
 subq.w     #4, d3               ; Subtract the DBRA requisite memory.
 movea.l    a0, a1               ; Calculate amount the DBRA instruction must
 suba.l     a6, a1               ; be moved and save the new location in scratch
 movea.l    a6, a5               ; register for displacement correction.
 move.w     2(a0), d0            ; Fetch current DBRA displacement value.
 move.l     (a0)+, (a6)+         ; Move the DBRA instruction.
 add.w      a1, d0               ; Correct DBRA displacement to the value it
 move.w     d0, 2(a5)            ; should be after the move.
 subq.w     #1, d3               ; Initialize counter for bulk copy.
_move_loop:                      ; Move rest of algorithm in a bulk copy.
 move.b     (a0)+, (a6)+
 dbra       d3, _move_loop
 subq.w     #1, d7               ; Initialize D7 for AUT loop execution.
 lea        start_time(pc), a0   ; Fetch address of declared variable.

 ; NOTE: No correction is necessary for the start time variable, as it was
 ;       in the PC-relative assembled program TRAP_9P, if pc-relative
 ;       addressing is not used for the label in the instruction below that
 ;       subtracts the contents of start_time from d0.  That instruction is
 ;       marked by asterisks below.  In the TRAP_9P program AssemPro used
 ;       pc-relative addressing for that label, as in does for all labels
 ;       when a program is assembled in PC-relative mode, that's why the
 ;       correction for that label was necessary in that program.

 ;       In the instruction above, pc-relative addressing can be used because
 ;       that instruction is not relocated by the bulk move.

 ;       Now, the address that is used in the instruction below is not the
 ;       relocated address of the variable; the original location of the
 ;       variable is used.  When you look at the disassembly listing for this
 ;       program, you will see that the extension longword (not word) contains
 ;       the actual address of the variable, not a displacement.

 ;       Of course, in the instruction above, the extension word does contain
 ;       a displacement, but this displacement remains valid because the
 ;       instruction is not moved.

 ; NOTE: Since processor is in supervisor mode, there is no reason to use
 ;       trap #3 to fetch time.  The 200hz vector can be referenced directly.

 move.l     $4BA, (a0)           ; Fetch and store start time.
aut_start:
reserved:   ds.b  1024           ; Space for loop construction = 1024 bytes.
aut_end:
 dbra       d7, aut_start
 move.l     $4BA, d0             ; Fetch end time.

 ;****
 sub.l      start_time, d0       ; Subtract start time from end time.
 ;****

 trap       #10                  ; Convert to decimal milliseconds and print.
print_memory_header:
 movea.l    memory_header(pc), a0
 bsr.s      print_string
print_requisite_memory:
 move.w     memory(pc), d1       ; Fetch AUT's requisite memory.
 trap       #4                   ; Returns address of decimal string in A0.
 bsr.s      print_string
 lea        header_1(pc), a0     ; Print requisite memory units label.
 bsr.s      print_string

 ; See documentation in program TRAP_9P.S.

 movea.l    _SSP, a7             ; Restore system stack pointer.
 rte

 ;
 ; SUBROUTINES
 ;

print_string:         
 pea        (a0)
 move.w     #9, -(sp) 
 trap       #1        
 addq.l     #6, sp    
 rts

 data
header_1:      dc.b '  bytes',$D,$A,0
 bss
 align
_SSP:          ds.l    1   ; Address of the system stack will be stored here.
start_time:    ds.l    1   ; Variable for time at start of AUT processing.
memory:        ds.w    1   ; Variable for AUT's requisite memory.
time_header:   ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT processing time.
memory_header: ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT requisite memory.
program_end:   ds.l    0
 end


TRAP9TST Execution Results With TRAP_9R.PRG Resident.

These results match those obtained with the PC-relative
assembled adaptive algorithm.

   MULU time:                      360  milliseconds
   MULU requisite memory:            4  bytes
   Addition time:                  255  milliseconds
   Addition requisite memory:        8  bytes
   Shift and add time:             230  milliseconds
   Shift and add requisite memory:   6  bytes


     Program 34 is sufficiently similar to program 36 so 
that most of the documentation for the first serves to 
document the second; nevertheless, I still want to point out 
a few important differences between the programs.  Under the 
label save_heading_addresses, near the beginning of the 
trap_9_routine, note that the addresses are stored directly 
to the labels in program 36 using absolute addressing, as 
opposed to the indirect addressing method used in program 
34.  The absolute addressing mode is also used to store the 
system stack pointer.  But, as you can see, wherever 
possible, pc-relative addressing is indicated in most of the 
instructions that contain labels in the source operand.  
That mode is indicated with the (pc) notation.
     There is one particular instruction in which I 
deliberately avoided pc-relative addressing so that I could 
illustrate a specific advantage of using the absolute 
addressing mode in the Relocatable assembled adaptive 
algorithm.  That is the instruction which subtracts the 
start time from the end time:

                sub.l  start_time, d0.
  
The instruction has been made conspicuous by the ;**** group 
being placed before and after it.  Using absolute addressing 
in this instruction obviates the inconvenience of a 
correction to access the start_time variable, as was done in 
program 34.
  
Figure 7.4. Disassembly listing of TRAP_9R.PRG as it resides 
in memory after the initial invocation of the adaptive 
algorithm.

 TRAP_9R.PRG After First Invocation

01F9FE 47FA04FC         LEA $1FEFC(PC),A3
01FA02 97EF0004         SUBA.L 4(A7),A3
01FA06 2F3C00000000     MOVE.L #0,-(A7)
01FA0C 3F3C0020         MOVE.W #$20,-(A7)
01FA10 4E41             TRAP #1
01FA12 5C8F             ADDQ.L #6,A7
01FA14 2A40             MOVEA.L D0,A5

 Note that absolute addressing is used in both operands
 of the instruction that stores the adaptive algorithm's
 address in the trap #9 vector.

01FA16 23FC0001FA360000 MOVE.L #$1FA36,$A4
       00A4             
01FA20 4855             PEA (A5)
01FA22 3F3C0020         MOVE.W #$20,-(A7)
01FA26 4E41             TRAP #1
01FA28 5C8F             ADDQ.L #6,A7
01FA2A 3F3C0000         MOVE.W #0,-(A7)
01FA2E 2F0B             MOVE.L A3,-(A7)
01FA30 3F3C0031         MOVE.W #$31,-(A7)
01FA34 4E41             TRAP #1

 trap_9 routine starts here

01FA36 99CB             SUBA.L A3,A4
01FA38 23C80001FEF4     MOVE.L A0,$1FEF4
01FA3E 23C90001FEF8     MOVE.L A1,$1FEF8
01FA44 23CF0001FEEA     MOVE.L A7,$1FEEA
01FA4A 4E6F             MOVE.L USP,A7
01FA4C 4A15             TST.B (A5)
01FA4E 6706             BEQ.S $1FA56
01FA50 204D             MOVEA.L A5,A0
01FA52 61000480         BSR $1FED4
01FA56 207A049C         MOVEA.L $1FEF4(PC),A0
01FA5A 61000478         BSR $1FED4
01FA5E 4DFA0046         LEA $1FAA6(PC),A6
01FA62 360C             MOVE.W A4,D3
01FA64 33C30001FEF2     MOVE.W D3,$1FEF2
01FA6A 5343             SUBQ.W #1,D3
01FA6C 1CDB             MOVE.B (A3)+,(A6)+
01FA6E 51CBFFFC         DBRA D3,$1FA6C
01FA72 41FA0432         LEA $1FEA6(PC),A0
01FA76 43FA0484         LEA $1FEFC(PC),A1
01FA7A 93C8             SUBA.L A0,A1
01FA7C 3609             MOVE.W A1,D3
01FA7E 5943             SUBQ.W #4,D3
01FA80 2248             MOVEA.L A0,A1
01FA82 93CE             SUBA.L A6,A1
01FA84 2A4E             MOVEA.L A6,A5
01FA86 30280002         MOVE.W 2(A0),D0
01FA8A 2CD8             MOVE.L (A0)+,(A6)+
01FA8C D049             ADD.W A1,D0
01FA8E 3B400002         MOVE.W D0,2(A5)
01FA92 5343             SUBQ.W #1,D3
01FA94 1CD8             MOVE.B (A0)+,(A6)+
01FA96 51CBFFFC         DBRA D3,$1FA94
01FA9A 5347             SUBQ.W #1,D7
01FA9C 41FA0450         LEA $1FEEE(PC),A0
01FAA0 20B9000004BA     MOVE.L $4BA,(A0)
01FAA6 C0FC0005         MULU #5,D0
01FAAA 51CFFFFA         DBRA D7,$1FAA6
01FAAE 2039000004BA     MOVE.L $4BA,D0
01FAB4 90B90001FEEE     SUB.L $1FEEE,D0
01FABA 4E4A             TRAP #$A
01FABC 207A003E         MOVEA.L $1FAFC(PC),A0
01FAC0 6116             BSR.S $1FAD8
01FAC2 323A0032         MOVE.W $1FAF6(PC),D1
01FAC6 4E44             TRAP #4
01FAC8 610E             BSR.S $1FAD8
01FACA 41FA0018         LEA $1FAE4(PC),A0
01FACE 6108             BSR.S $1FAD8
01FAD0 2E790001FEEA     MOVEA.L $1FEEA,A7
01FAD6 4E73             RTE

 print_string subroutine

01FAD8 4850             PEA (A0)
01FADA 3F3C0009         MOVE.W #9,-(A7)
01FADE 4E41             TRAP #1
01FAE0 5C8F             ADDQ.L #6,A7
01FAE2 4E75             RTS
01FAE4 2020             MOVE.L -(A0),D0
01FAE6 6279             BHI.S $1FB61
01FAE8 7465             MOVEQ #$65,D2
01FAEA 730D             DC.W $730D
01FAEC 0A000003         EORI.B #3,D0
01FAF0 EF40             ASL.W #7,D0
01FAF2 00000000         ORI.B #0,D0
01FAF6 00040006         ORI.B #6,D4
01FAFA DBBF             DC.W $DBBF
01FAFC 0006DC25         ORI.B #$25,D6
01FB00 00000000         ORI.B #0,D0
01FB04 00000000         ORI.B #0,D0

01FE9C 00000000         ORI.B #0,D0
01FEA0 00000000         ORI.B #0,D0

 The movable section.  Starting address is $01FEA6

01FEA4 000051CF         ORI.B #-$31,D0
01FEA8 FBFE             DC.W $FBFE
01FEAA 2039000004BA     MOVE.L $4BA,D0
01FEB0 90B90001FEEE     SUB.L $1FEEE,D0 ; sub.l start_time, d0
01FEB6 4E4A             TRAP #$A
01FEB8 207A003E         MOVEA.L $1FEF8(PC),A0
01FEBC 6116             BSR.S $1FED4
01FEBE 323A0032         MOVE.W $1FEF2(PC),D1
01FEC2 4E44             TRAP #4
01FEC4 610E             BSR.S $1FED4
01FEC6 41FA0018         LEA $1FEE0(PC),A0
01FECA 6108             BSR.S $1FED4
01FECC 2E790001FEEA     MOVEA.L $1FEEA,A7
01FED2 4E73             RTE
01FED4 4850             PEA (A0)
01FED6 3F3C0009         MOVE.W #9,-(A7)
01FEDA 4E41             TRAP #1
01FEDC 5C8F             ADDQ.L #6,A7
01FEDE 4E75             RTS
01FEE0 2020             MOVE.L -(A0),D0
01FEE2 6279             BHI.S $1FF5D
01FEE4 7465             MOVEQ #$65,D2
01FEE6 730D             DC.W $730D
01FEE8 0A000003         EORI.B #3,D0
01FEEC EF40             ASL.W #7,D0
01FEEE 00000000         ORI.B #0,D0
01FEF2 00040006         ORI.B #6,D4
01FEF6 DBBF             DC.W $DBBF
01FEF8 0006DC25         ORI.B #$25,D6
   

     I don't know if I've mentioned it before, but even if I 
have, it is worth pointing out again that the addresses and 
the instructions contained therin are not displayed in 
disassembly listings as neat as one might like.  If you 
refer to the disassembly listing just above this paragraph 
you can see that the address for the variable _SSP, 01FEEA, 
is not displayed.  To locate the contents of that address, 
it is necessary to locate the nearest address that is 
displayed.  In this case, that is address 01FEE8.  There you 
see that the byte stored in that address is the ASCII code 
for a linefeed.  Then, displayed on the same line, at 
address 01FEE9 is the 00 byte inserted by the align pseudo-
op.  Finally, also displayed on the same line, at address 
01FEEA, is the first byte of the value stored in _SSP.  That 
byte is 00.  The next byte of _SSP, at address 01FEEB, is 03 
and is displayed on that same line.  To locate the other two 
bytes stored in _SSP one must look at the next line, which 
is address 01FEEC.
     The value stored in the variable start_time is neatly 
displayed on the next line, at address 01FEEE, but on the 
line following, at address 01FEF2, the first word displayed 
is the contents of the variable memory, while the second 
word shown on that line is the first word of the value 
stored in time_header (address = 01FEF4).  The second word 
of time-header is displayed on the line labeled 01FEF6.  The 
last address, 01FEF8, is the variable memory_header.  After 
a while, you get used to all of this, but I wanted to take 
the opportunity to mention something that is trivial once 
you know the "secret", but which can be a source of 
consternation to one who is not accoustomed to reading the 
listings.
     To the extent that the major difference between the PC-
relative version and the Relocatable version of the custom 
trap is the addressing mode used in particular instructions, 
it seems reasonable to question the advantages, or 
disadvantages, of each addressing mode.  One advantage of 
absolute addressing has already been discussed: it relieves 
one of the address correction burden in some instances.  
Naturally, there is the 16 bit displacement limitation 
attached to pc-relative addressing, but I find this to be 
rather insignificant for two reasons.  I don't write many 
assembly language programs in which instructions and labels 
are 32,767 bytes apart, and when I do, I can find ways to 
circumvent that limitation.
     In maintaining the theme of the book, however, it seems 
prudent to compare the execution speed and requisite memory 
for instructions using the two addressing modes when that 
16-bit limitation of pc-relative addressing is neglected.  
Program 37 was designed to yield the appropriate comparative 
data for this discussion, and, in addition, to serve as a 
vehicle to illustrate possible consequences of the 
disruptive modification phenomenon previously mentioned.

Program 37.  A program that compares the execution speed and 
requisite memory of two algorithms that write data to a 
location.

 ; Program Name: LEA_MOVE.S
 ;      Version: 1.003

 ; Assembly Instructions:

 ;    Assemble in Relocatabe mode and save with a TOS extension.

 ; Program Function:

 ;    Compares the relative speed and memory requirements of

 ;                      lea     label(pc), Am
 ;                      move.l  An, (Am)

 ;    and               lea     label, Am
 ;                      move.l  An, (Am)
 
 ;    to                move.l  An, label
 
 ; The execution time reported is for 50,000 executions of each algorithm.

 ;    In addition, this program's first AUT can disrupt the adaptive algorithm
 ; because the address that is loaded in register A2 depends on the displacement
 ; between the instruction "lea label(pc), a2" and the label it references.

 ;    When that instruction is executed in the adaptive algorithm, whatever
 ; address is the "displacement" distance away from the instruction will be
 ; loaded into register A2.  Then the instruction following, "move.l a0, (a2)
 ; will write whatever is in register A0 into that memory location.

 ;    If the address stored in register A2 while the AUT is being executed by
 ; the adaptive algorithm happens to be within the adaptive algorithm's program
 ; or data space, the results could be unpleasant.

 ;    In fact, an undisciplined store of this type is capable of corrupting any
 ; instruction or data that happens to be separated from the LEA instruction by
 ; an amount equal to the displacement, and the results could be catastrophic.
  
calculate_program_size:
 lea        -$102(pc), a1       ; Fetch basepage start address.
 lea        program_end, a0     ; Fetch program end = array address.
 trap       #6                  ; Return unused memory to op system.
 lea        stack, a7

initialize_registers_1:
 lea        header_1, a0       
 lea        header_2, a1
 lea        lea_move_start, a3
 lea        lea_move_end, a4
 lea        heading, a5
 move.w     #50000, d7
 trap       #9

initialize_registers_2:
 lea        header_3, a0       
 lea        header_4, a1
 lea        long_lea_start, a3
 lea        long_lea_end, a4
 lea        heading, a5
 move.b     #0, (a5)            ; Store a NULL in first byte to create a
 move.w     #50000, d7          ; null string so that heading gets printed
 trap       #9                  ; only once.

initialize_registers_3:
 lea        header_5, a0       
 lea        header_6, a1
 lea        move_start, a3
 lea        move_end, a4
 lea        heading, a5
 move.w     #50000, d7     
 trap       #9             

terminate:
 trap       #8

lea_move_start:                  ; This algorithm is potentially nocuous to
 lea        label(pc), a2        ; the adaptive algorithm because a displacement 
 move.l     a0, (a2)             ; will be stored in A2, not an address.
lea_move_end:

long_lea_start:                  ; This algorithm poses no threat because an
 lea        label, a2            ; address in this program's data area will be
 move.l     a0, (a2)             ; stored in A2.
long_lea_end:

move_start:                      ; This algorithm poses no threat because an
 move.l     a0, label            ; address in this program's data area will be
move_end:                        ; stored in A2.
         
 data
heading:      dc.b       "LEA_MOVE Program Results",$D,$A,$D,$A,0
header_1:     dc.b       "  Elapsed time for lea    label(pc), Am ",$D,$A
              dc.b       "                   move.l An, (Am):      ",0
header_2:     dc.b       "  Memory required for first algorithm:      ",0
header_3:     dc.b $D,$A,"  Elapsed time for lea    label, Am ",$D,$A
              dc.b       "                   move.l An, (Am):      ",0
header_4:     dc.b       "  Memory required for second algorithm:     ",0
header_5:     dc.b $D,$A,"  Elapsed time for move.l An, label:     ",0
header_6:     dc.b       "  Memory required for third algorithm:      ",0
 bss
 align
label:        ds.l  1
              ds.l 96
stack:        ds.l  0
program_end:  ds.l  0 
 end


     Before proceeding with the discussion initiated above, 
I want to show you the alterations that I made to the 
TRAPS.S program so that the adaptive algorithm would be 
installed automatically during boot.  First, I renamed the 
trap installation program from TRAPS.S to CUSTOM.S, then I 
inserted the TRAP_9P.S program into that source file before 
assembling the entire conglomeration as CUSTOM.PRG.  I don't 
want to repeat the entire CUSTOM.S source file, therefore, I 
have listed only the relevant portions in figure 7.5.
  
Figure 7.5. Alterations to TRAPS.S to convert it to 
CUSTOM.S.  The listing below is the contents of a file 
called CUSTOM.DOC.  The listing shows only the changes that 
must be made to TRAPS.S to convert it to CUSTOM.S.  Of 
course, the alterations to TRAPS.S can be made by copying 
the contents of CUSTOM.DOC to that file using a suitable 
editor, such as TEMPUS or 1ST WORD PLUS.


 ; Program Name: CUSTOM.S 
 ; Version 1.006

 ; Algorithms for trap #9, the intelligent algorithm, and trap #10 are included,
 ; along with the other custom traps from the TRAPS.S program.

 ; Assembly Instructions:

 ;    Assemble in PC-relative mode and save with a PRG extension.

install_trap_9_routine:         ; Note: pointer = vector = pointer.
 lea        trap_9_routine, a0  ; Fetch address of trap #9 routine.
 move.l     a0, $A4             ; Store custom trap address in pointer.

trap_9_routine:

 ; NOTE: You may want to execute a program that invokes this trap from the
 ;       AssemPro debugger and single step through the trap instructions, or
 ;       you many want to set breakpoints and use the "Run program" button to
 ;       execute to a breakpoint.  It the exercise of this latter option that
 ;       can cause problems.  If you want to set a breakpoint at an instruction
 ;       that occurs before the "reserved space", no precautions need be taken,
 ;       except that you must realize that you could halt at a position after
 ;       the start time has been initialized, and the execution time will be
 ;       accumulating during the halt.

 ;       But, if you want to set a breakpoint at at an instruction that occurs
 ;       after the "reserved space", you should not do so until the instructions
 ;       that perform the bulk move have been executed.  If you set a breakpoint
 ;       at an instruction in the program space which follows the "reserved
 ;       space" and then execute the bulk move instructions, the breakpoint you
 ;       have set will cause an illegal command error.

 ; This custom trap must be invoked by a program which contains one or more
 ; algorithms for which performance data, in the form of execution time and
 ; requisite memory, is desired.  The trap must be invoked once for each 
 ; algorithm under test (AUT).  The trap is intended to be a performance 
 ; report generator so that performance data for specific algorithms can be
 ; compared.

 ; If the program invoking the trap is spawned by SPAWN.TTP, the performance
 ; data will be printed to a file that is created by SPAWN.TTP.  The name of
 ; the file will be the name of the spawned program with a DAT suffix.

 ; If the program invoking the trap is executed from the desktop, the 
 ; performance data will be printed to the screen.

 ; The AUT can be assembled in PC-relative or Relocatable mode.

 ; The custom trap expects the following parameters to be contained in the
 ; specified registers prior to invocation:

 ; A0 = The address of a null terminated header to precede the reported
 ;      AUT execution time.

 ; A1 = The address of a null terminated header to precede the reported
 ;      AUT requisite memory.

 ; A3 = The starting address of an algorith containing one or more instructions.
 ;      This algorithm becomes the AUT upon invocation of the trap.

 ; A4 = The ending address of the AUT.

 ; A5 = At the initial invocation by a specific program, A5 is expected to
 ;      contain the address of a null terminated heading that is a brief
 ;      description of the data that is to be reported by the trap.  During
 ;      all subsequent invocations by that program, A5 must contain the
 ;      address of a null string.

 ; D7 = A word length decimal value which specifies the number of times the
 ;      the AUT is to be executed in a loop in order to generate the execution
 ;      time data.  Register D7 is the only register which cannot be used by
 ;      the AUT.  That's because D7 is used as the AUT execution loop counter.

 ; The custom trap uses the information passed in A3, A4 and D7 to construct
 ; a loop around the AUT.  The loop is executed the number of times specified
 ; in register D7.  The time required to execute the loop is calculated and
 ; printed along with the AUT's requisite memory.

 ; How Trap #9 Works:

 ;     The custom trap is an intelligent, self-modifying algorithm.  Prior
 ; to an initial invocation, the trap #9 routine is composed of three sections.
 ; The first section contains instructions which are permanently located.  The
 ; second section is a 1,024 byte block of reserved space into which the AUT
 ; and the third section is to be copied.  The third section contains the custom
 ; trap instructions that must be copied so that the first instruction in the
 ; third section immediately follows the last instruction of the algorithm
 ; under test.  The size that I chose for the reserved space was arbitrary.
   
 ;     After an invocation, the custom trap calculates the number of bytes in
 ; the algorithm under test.  Then it initializes register D7 for the AUT's
 ; execution loop.  After saving the addresses of the headers that were passed
 ; as parameters so that the registers in which they were passed can be used
 ; by trap #9 and/or the algorithm under test, the trap prints the AUT's
 ; primary heading and the execution time header.  Then it copies the AUT into
 ; the reserved space.

 ;     After the AUT has been copied into the reserved space, the instructions
 ; and data in the third section of the custom trap are moved into immediate
 ; proximity of the AUT so that the first instruction of section three follows
 ; immediately after the last instruction of the algorithm under test.

 ;     The AUT is executed the number of times requested via the value passed
 ; in D7, then the execution time and requisite memory of the AUT are printed.

 ;     After the custom trap has been invoked once, the reserved space will
 ; not be completely clear during the remaining portion of the power-up cycle.
 ; When the trap is subsequently invoked, the instructions that are already in
 ; the reserved space will simply be overwritten by the instructions of the
 ; new algorithm under test and those of the third section.

calculate_length_of_AUT:
 suba.l     a3, a4               ; Subtract start address from end address.

save_heading_addresses:
 lea        time_header, a2      ; Header to precede reported execution time.
 move.l     a0, (a2)            
 lea        memory_header, a2    ; Header to precede reported requisite memory.
 move.l     a1, (a2)           

transfer_stack_pointer:

 ; Upon entrance into this custom trap, A7 contains the address of the system
 ; stack pointer.  Because the system stack may be too short for use by the AUT,
 ; the invoking program must provide a user stack, and, here, I am going to
 ; store the address of that stack in A7.  Before returning to the invoking
 ; program, the system stack pointer must be restored so that the return address
 ; can be found by the processor.

 lea        _SSP, a0             ; Fetch address of declared variable.
 move.l     a7, (a0)             ; Save system stack pointer.
 move       USP, a7              ; Transfer to invoking program's stack.

print_heading:

 ; NOTE: When two or more algorithms are to invoke the trap from a program,
 ;       the heading should be printed only once, at the beginning of the
 ;       report; therefore, the string address in A5 should point to a
 ;       null terminated string during the first invocation of the trap, but
 ;       it should point to a null string on subsequent invocations from the
 ;       same program.
 
 ;       For that reason, the test for NULL string is included below, so that
 ;       only one attempt to print the heading will be made.

 tst.b      (a5)                 ; NULL string test.
 beq.s      print_time_header    ; Branch if null.
 movea.l    a5, a0               ; Print heading.
 bsr        print_string_9

print_time_header:
 movea.l    time_header, a0      ; Fetch address of time header.
 bsr        print_string_9

build_algorithm:
 lea        reserved_space, a6   ; Fetch address of reserved space.
 move.w     a4, d3               ; AUT length initializes counter for copy.
 lea        memory, a0           ; Store AUT's requisite memory.
 move.w     d3, (a0)             ; AUT length stored for report.
 subq.w     #1, d3               ; Initialize counter for loop execution.
move_loop:                       ; Move AUT, byte by byte, to the area
 move.b     (a3)+, (a6)+         ; declared as "reserved_space".
 dbra       d3, move_loop        ; Branch until D3 = -1.

 ; A6 is now pointing to the location at which the AUT execution loop's DBRA
 ; instruction must be copied.  The DBRA copy must be processed apart from the
 ; other instructions in the custom trap which must be copied to "close up" the
 ; gap between the last statement of the algorithm under test and the rest
 ; of the custom trap's instructions.

 lea        algorithm_end, a0    ; Calculate number of bytes in this program
 lea        trap_9_end, a1       ; which must be copied into "reserved_space",
 suba.l     a0, a1               ; then initialize counter D3 with the number
 move.w     a1, d3               ; of bytes to copy.
 subq.w     #4, d3               ; Subtract the DBRA requisite memory.
 movea.l    a0, a1               ; Calculate amount the DBRA instruction must
 suba.l     a6, a1               ; be moved and save the new location in scratch
 movea.l    a6, a5               ; register for displacement correction.
 move.w     2(a0), d0            ; Fetch current DBRA displacement value.
 move.l     (a0)+, (a6)+         ; Move the DBRA instruction.
 add.w      a1, d0               ; Correct DBRA displacement to the value it
 move.w     d0, 2(a5)            ; should be after the move.
 subq.w     #1, d3               ; Initialize counter for bulk copy.
_move_loop:                      ; Move rest of algorithm in a bulk copy.
 move.b     (a0)+, (a6)+
 dbra       d3, _move_loop
 subq.w     #1, d7               ; Initialize D7 for AUT loop execution.
 lea        start_time, a0       ; Fetch address of declared variable.
 suba.l     a1, a0               ; Correct address to after-move location.

 ; NOTE: Since processor is in supervisor mode, there is no reason to use
 ;       trap #3 to fetch time.  The 200hz vector can be referenced directly.

 move.l     $4BA, (a0)           ; Fetch and store start time.
algorithm_start:
reserved_space:  ds.b  1024      ; Space for loop construction = 1024 bytes.
algorithm_end:
 dbra       d7, algorithm_start
 move.l     $4BA, d0             ; Fetch end time.
 sub.l      start_time, d0       ; Subtract start time from end time.
 trap       #10                  ; Convert to decimal milliseconds and print.
print_memory_header:
 movea.l    memory_header, a0    ; Fetch address of memory header.
 bsr        print_string_9
print_requisite_memory:
 move.w     memory, d1           ; Fetch AUT's requisite memory.
 trap       #4                   ; Returns address of decimal string in A0.
 bsr        print_string_9
 lea        header_1, a0         ; Print requisite memory units label.
 bsr        print_string_9

 ; NOTE:  I had thought that I might have to restore the user stack pointer
 ;        before returning to the calling program because I can't know to what
 ;        extent the AUT has corrupted the user stack.

 ;        But, as it turns out, since the value in USP is stored in register
 ;        A7 at the beginning of the program, and since the system stack pointer
 ;        is then active and remains so for the duration of the trap invocation,
 ;        only the value in register A7 (which is the system stack pointer, but
 ;        which points to the user stack) is altered; the value in USP remains
 ;        uncorrupted, therefore, nothing needs be restored but the system stack
 ;        pointer (so that it again points to the system stack).

 ;        On subsequent invocations the value in USP, which remains stable, will
 ;        simply be restored in A7, as often as the trap is invoked.

 movea.l    _SSP, a7             ; Restore system stack pointer so that it
 rte                             ; points to the system stack.

trap_9_data_and_subroutine:

 ; NOTE: Trap #9 must have its own print_string subroutine because the
 ;       displacements in the bsr print_string instructions in trap #9 are
 ;       not altered by the move of this section into the reserved space.

 ;       Therefore, the displacement between the instructions and the
 ;       print_string subroutine must remained constant.  The only way to
 ;       maintain the displacement (without corrections) is to move the
 ;       subroutine along with the rest of this section.

 ;       Then what happens is this: the bsr print_string instructions located
 ;       above the reserved space cause a branch to the pre-move location of the
 ;       subroutine; those instructions located below the reserved space cause
 ;       a branch to the after-move location of the subroutine.  If you say all
 ;       of this to yourself very quickly, it is less confusing.  I think.

print_string_9:                 ; Expects address of string to be in A0.
 pea        (a0)                ; Push address of string onto stack.
 move.w     #9, -(sp)           ; Function = c_conws = GEMDOS $9.
 trap       #1                  ; GEMDOS call
 addq.l     #6, sp              ; Reset stack pointer to top of stack.
 rts
  
header_1:      dc.b '  bytes',$D,$A,0
 align
_SSP:          ds.l    1   ; Address of the system stack will be stored here.
start_time:    ds.l    1   ; Variable for time at start of AUT processing.
memory:        ds.w    1   ; Variable for AUT's requisite memory.
time_header:   ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT processing time.
memory_header: ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT requisite memory.
trap_9_end:    ds.l    1   ; Marks end of trap #9 section.

 ; This statement and the items in boldface below are not part of the trap_9
 ; routine.  They are there to provide orientation so that the appropriate
 ; sections of this document may be copied into the new CUSTOM.S document.

trap_10_routine:

print_string:                   ; Expects address of string to be in A0.
 pea        (a0)                ; Push address of string onto stack.
 move.w     #9, -(sp)           ; Function = c_conws = GEMDOS $9.
 trap       #1                  ; GEMDOS call
 addq.l     #6, sp              ; Reset stack pointer to top of stack.
 rts

 data
subtrahend:       dc.l   $3B9ACA00,$5F5E100,$989680,$F4240,$186A0,$2710
                  dc.l   $3E8,$64,$A,$1,$0
hex_table:        dc.b   '0123456789ABCDEF'
spawned:          dc.b   $0
space:            dc.b   " ",0

units_label:      dc.b   "  milliseconds", $D,$A,0

 bss
 align                       ; Align storage on a word boundary.
after_load_time:  ds.w   1   ; Spawned program's after load time. 
decimal:          ds.l   3   ; Output buffer.  Must be NULL terminated.
hexadecimal:      ds.l   3   ; Output buffer.  Must be NULL terminated.

program_end:      ds.l   0
 end      


     The execution results of program 37 are shown in figure 
7.6.  The data illustrates that there is no speed nor 
requisite memory difference between the first and third 
algorithms.  The addressing modes used in those algorithms 
is pc-relative for the first and absolute for the third.  
The first algorithm may seem to be hampered by the extra 
instruction needed to indirectly store the data in An, but 
it is only when pc-relative addressing cannot be used with 
the LEA instruction that the extra instruction becomes a 
handicap.  This is evident from the data for the second 
algorithm, where the execution time and requisite memory are 
greater than that for the other two algorithms.  But, in 
general, the algorithms being considered will be those with 
the appearance of algorithms one and two.  Clearly, the 
execution speed and requisite memory of those are identical.

Figure 7.6. Execution results of program 37 with the newly 
created CUSTOM.PRG resident.

LEA_MOVE Program Results

  Elapsed time for lea    label(pc), Am 
                   move.l An, (Am):        205  milliseconds
  Memory required for first algorithm:       6  bytes

  Elapsed time for lea    label, Am 
                   move.l An, (Am):        235  milliseconds
  Memory required for second algorithm:      8  bytes

  Elapsed time for move.l An, label:       205  milliseconds
  Memory required for third algorithm:       6  bytes


     A partial disassembly of the adaptive algorithm during 
invocation, but before AUT loop execution, by each of 
program 37's three AUT's is shown in figure 7.7.  Although 
the addresses here are different than those shown in 
previous disassembly listings, because the custom trap was 
installed by CUSTOM.PRG during boot, it is easy to see that 
the displacement in the extension word of the first AUT's 
LEA instruction causes an address to be loaded into A2 that 
is not located in the invoking program, but is located 
within the custom trap's space.  No problem occurs because 
it just so happens that the address $17D54 falls within the 
unused reserved space.  But the folly of depending on this 
kind of luck should be apparent.  This problem does not 
occur with the second and third AUTs because relative 
addressing is not used in those instructions; therefore the 
address loaded into A2 during invocation by the second and 
third AUTs is located within the invoking program's address 
space.
  
Figure 7.7. A partial disassembly of the adaptive algorithm 
during invocation by program 37's three AUTs.

 LEA_MOVE's 1st AUT in CUSTOM's adaptive

017BCA 45FA0188         LEA $17D54(PC),A2
017BCE 2488             MOVE.L A0,(A2)
017BD0 51CFFFF8         DBRA D7,$17BCA

 LEA_MOVE's 2nd AUT in CUSTOM's adaptive

017BCA 45F90006D730     LEA $6D730,A2
017BD0 2488             MOVE.L A0,(A2)
017BD2 51CFFFF6         DBRA D7,$17BCA

 LEA_MOVE's 3rd AUT in CUSTOM's adaptive

017BCA 23C80006D730     MOVE.L A0,$6D730
017BD0 51CFFFF8         DBRA D7,$17BCA


     I must not leave you with the impression that the 
problem with the address being loaded in the first AUT has 
much to do with the fact that it is not located within the 
boundaries of the invoking program.  No, it is because the 
address it does load is within the boundaries of the 
adaptive algorithm and that address is going to be corrupted 
by the second statement of the first algorithm.  The purpose 
of the three AUT's is to compare the execution speed and 
requisite memory of three algorithms which store data in an 
address that is specified by a label.  As far as the test is 
concerned, the location of the label can be anyplace in 
memory.
     Of course, I would not leave you to suffer this 
dilemma.  I have prepared another version of program 37 and 
another version of the adaptive algorithm to illustrate a 
method of dealing with this problem of referencing labels in 
an AUT's data area from within the execution loop located in 
the adaptive algorithm.  Program 38 is the program that will 
exercise the new adaptive algorithm.  AUT_DATA's execution 
results are shown in figure 7.8.

Program 38. In this program, data areas are declared for 
each AUT, and the variables label_1, label_2 and label_3 are 
the labels for those data areas.

 ; Program Name: AUT_DATA.S
 ;      Version: 1.001

 ; Assembly Instructions:

 ;    Assemble in Relocatabe mode and save with a TOS extension.

 ; Program Function:

 ;    Compares the relative speed and memory requirements of

 ;                      lea     label(pc), Am
 ;                      move.l  An, (Am)

 ;    and               lea     label, Am
 ;                      move.l  An, (Am)
 
 ;    to                move.l  An, label
 
 ; The execution time reported is for 50,000 executions of each algorithm.

 ;    In this program, a data area is declared before the AUT's so that the
 ; first AUT can't disrupt the adaptive algorithm.  The address of the data
 ; area is passed to the adaptive algorithm in register A2.

 ;    A branch statement is included in each AUT so that the adaptive algorithm
 ; will jump over the data area.
  
 ;    Of course, this calls for a redesign of the adaptive algorithm.

calculate_program_size:
 lea        -$102(pc), a1       ; Fetch basepage start address.
 lea        program_end, a0     ; Fetch program end = array address.
 trap       #6                  ; Return unused memory to op system.
 lea        stack, a7

initialize_registers_1:
 lea        header_1, a0       
 lea        header_2, a1
 lea        lea_data_area, a2
 lea        lea_move_start, a3
 lea        lea_move_end, a4
 lea        heading, a5
 move.w     #50000, d7
 trap       #9

initialize_registers_2:
 lea        header_3, a0       
 lea        header_4, a1
 lea        long_data_area, a2
 lea        long_lea_start, a3
 lea        long_lea_end, a4
 lea        heading, a5
 move.b     #0, (a5)            ; Store a NULL in first byte to create a
 move.w     #50000, d7          ; null string so that heading gets printed
 trap       #9                  ; only once.

initialize_registers_3:
 lea        header_5, a0       
 lea        header_6, a1
 lea        move_data_area, a2
 lea        move_start, a3
 lea        move_end, a4
 lea        heading, a5
 move.w     #50000, d7     
 trap       #9             

terminate:
 trap       #8

lea_data_area:
 bra.s      lea_move_start
label_1:    ds.l 1
lea_move_start:                
 lea        label_1(pc), a2      
 move.l     a0, (a2)           
lea_move_end:

long_data_area:
 bra.s      long_lea_start
label_2:    ds.l 1
long_lea_start:              
 lea        label_2, a2        
 move.l     a0, (a2)         
long_lea_end:

move_data_area:
 bra.s      move_start
label_3:    ds.l 1
move_start:                  
 move.l     a0, label_3        
move_end:                    
         
 data
heading:      dc.b       "AUT_DATA Program Results",$D,$A,$D,$A,0
header_1:     dc.b       "  Elapsed time for lea    label(pc), Am ",$D,$A
              dc.b       "                   move.l An, (Am):      ",0
header_2:     dc.b       "  Memory required for first algorithm:      ",0
header_3:     dc.b $D,$A,"  Elapsed time for lea    label, Am ",$D,$A
              dc.b       "                   move.l An, (Am):      ",0
header_4:     dc.b       "  Memory required for second algorithm:     ",0
header_5:     dc.b $D,$A,"  Elapsed time for move.l An, label:     ",0
header_6:     dc.b       "  Memory required for third algorithm:      ",0
 bss
 align
              ds.l 96
stack:        ds.l  0
program_end:  ds.l  0 
 end
 
  
Program 39. A new version of the program that installs the 
adaptive algorithm.  This version is designed to process 
AUT's in which an area of memory has been set aside to be 
used as a data area.  Note that the pseudo-op data is not 
used.

 ; Program Name: TRAP9DAT.S
 ; Version 1.002

 ; Assembly Instructions:

 ;    Assemble in PC-relative mode and save with a PRG extension.

 ; Program Function:

 ;    This is a LSR program that establishes a user defined trap #9.  It may
 ; be executed from the desktop, but you may prefer to copy it to the AUTO
 ; folder of your boot partition or floppy disk so that it will execute
 ; automatically during boot.

 ;    This is a special, single-purpose trap that is used to illustrate a
 ; method of preventing corruption of the adaptive algorithm.

program_start:                  ; Calculate program size and retain result.
 lea        program_end, a3     ; Fetch program end address.
 suba.l     4(a7), a3           ; Subtract basepage address.

enter_supervisor_mode:
 move.l     #0, -(sp)           ; The zero turns on supervisor mode.
 move.w     #$20, -(sp)         ; Function = super = GEMDOS $20.
 trap       #1                  ; Supervisor stack pointer (SSP) returned in D0.
 addq.l     #6, sp             
 movea.l    d0, a5              ; Save SSP in scratch register.

install_trap_9_routine:         ; Note: pointer = vector = pointer.
 lea        trap_9_routine, a0  ; Fetch address of trap #9 routine.
 move.l     a0, $A4             ; Store trap address at pointer address.
 
enter_user_mode:
 pea        (a5)                ; Restore supervisor stack pointer.
 move.w     #$20, -(sp)         ; Function = super = GEMDOS $20.
 trap       #1
 addq.l     #6, sp 

relinquish_processor_control:   ; Maintain memory residency.
 move.w    #0, -(sp)            ; Exit code. 
 move.l    a3, -(sp)            ; Program size.
 move.w    #$31, -(sp)          ; Function = ptermres = GEMDOS $31.
 trap      #1

trap_9_routine:

 ; The custom trap expects the following parameters to be contained in the
 ; specified registers prior to invocation:

 ; A0 = The address of a null terminated header to precede the reported
 ;      AUT execution time.

 ; A1 = The address of a null terminated header to precede the reported
 ;      AUT requisite memory.

 ; A2 = The address of a data area for the algorithm to be tested.  The ending
 ;      address for the data area must be the address stored in register A3; 
 ;      that is, it must be the starting address for the algorithm.

 ; A3 = The starting address of an algorithm containing one or more instructions.
 ;      This algorithm becomes the AUT upon invocation of the trap.

 ; A4 = The ending address of the AUT.

 ; A5 = At the initial invocation by a specific program, A5 is expected to
 ;      contain the address of a null terminated heading that is a brief
 ;      description of the data that is to be reported by the trap.  During
 ;      all subsequent invocations by that program, A5 must contain the
 ;      address of a null string.

 ; D7 = A word length decimal value which specifies the number of times the
 ;      the AUT is to be executed in a loop in order to generate the execution
 ;      time data.  Register D7 is the only register which cannot be used by
 ;      the AUT.  That's because D7 is used as the AUT execution loop counter.
 
calculate_length_of_AUT_plus_data_area:
 suba.l     a2, a4               ; Subtract data start address from AUT start
                                 ; address.
calculate_length_of_AUT_data_area:
 suba.l     a2, a3               ; Subtract AUT start address from AUT end
                                 ; address.
save_heading_addresses:
 lea        time_header, a6      ; Header to precede reported execution time.
 move.l     a0, (a6)
 lea        memory_header, a6    ; Header to precede reported requisite memory.
 move.l     a1, (a6)
 lea        heading, a6          ; Null terminated heading or NULL string.
 move.l     a5, (a6)

transfer_AUT_start_address:      ; Because contents of A2 will be altered soon.
 movea.l    a2, a5

transfer_stack_pointer:
 lea        _SSP, a0             ; Fetch address of declared variable.
 move.l     a7, (a0)             ; Save system stack pointer.
 move       USP, a7              ; Transfer to invoking program's stack.

print_heading:
 movea.l    heading, a0          ; Fetch heading address.
 tst.b      (a0)                 ; NULL string test.
 beq.s      print_time_header    ; Branch if null.
 bsr        print_string

print_time_header:
 movea.l    time_header, a0      ; Fetch address of time header.
 bsr        print_string

move_AUT:
 lea        reserved_space, a6   ; Fetch address of reserved space.
 move.w     a4, d3               ; AUT length initializes counter for copy.
 lea        memory, a0           ; Store AUT's requisite memory.
 move.w     d3, d0               ; Copy total AUT length to D0 for correction.
 sub.w      a3, d0               ; Subtract length of data area.
 move.w     d0, (a0)             ; AUT length stored for report.
 subq.w     #1, d3               ; Initialize counter for loop execution.
move_loop:                       ; Move data area and AUT, byte by byte, to the
 move.b     (a5)+, (a6)+         ; area declared as "reserved_space".
 dbra       d3, move_loop        ; Branch until D3 = -1.

move_adaptive_algorithm:
 lea        algorithm_end, a0    ; Calculate number of bytes in this program
 lea        program_end, a1      ; which must be copied into "reserved_space",
 suba.l     a0, a1               ; then initialize counter D3 with the number
 move.w     a1, d3               ; of bytes to copy.
 subq.w     #4, d3               ; Subtract the DBRA requisite memory.
 movea.l    a0, a1               ; Calculate amount the DBRA instruction must
 suba.l     a6, a1               ; be moved and save the new location in scratch
 movea.l    a6, a5               ; register for displacement correction.
 move.w     2(a0), d0            ; Fetch current DBRA displacement value.
 move.l     (a0)+, (a6)+         ; Move the DBRA instruction.

 ; In this version of the adaptive algorithm, when the DBRA displacement is
 ; corrected, the size of the AUT's data space must be added to the
 ; correction so that the branch will go to the start of the AUT's executable
 ; statements, not to the start of the data space.

 add.w      a3, d0               ; Add length of AUT's data space.
 add.w      a1, d0               ; Correct DBRA displacement to the value it
 move.w     d0, 2(a5)            ; should be after the move.
 subq.w     #1, d3               ; Initialize counter for bulk copy.
_move_loop:                      ; Move rest of algorithm in a bulk copy.
 move.b     (a0)+, (a6)+
 dbra       d3, _move_loop
 subq.w     #1, d7               ; Initialize D7 for AUT loop execution.
 lea        start_time, a0       ; Fetch address of declared variable.
 suba.l     a1, a0               ; Correct address to after-move location.

 ; NOTE: Since processor is in supervisor mode, there is no reason to use
 ;       trap #3 to fetch time.  The 200hz vector can be referenced directly.

 move.l     $4BA, (a0)           ; Fetch and store start time.
algorithm_start:
reserved_space:  ds.b  1024      ; Space for loop construction = 1024 bytes.
algorithm_end:
 dbra       d7, algorithm_start
 move.l     $4BA, d0             ; Fetch end time.
 sub.l      start_time, d0       ; Subtract start time from end time.
 trap       #10                  ; Convert to decimal milliseconds and print.
print_memory_header:
 movea.l    memory_header, a0    ; Fetch address of memory header.
 bsr.s      print_string
print_requisite_memory:
 move.w     memory, d1           ; Fetch AUT's requisite memory.
 trap       #4                   ; Returns address of decimal string in A0.
 bsr.s      print_string
 lea        header_1, a0         ; Print requisite memory units label.
 bsr.s      print_string
 movea.l    _SSP, a7             ; Restore system stack pointer so that it
 rte                             ; points to the system stack.

 ;
 ; SUBROUTINES
 ;

print_string:         
 pea        (a0)
 move.w     #9, -(sp) 
 trap       #1        
 addq.l     #6, sp    
 rts

 data
header_1:      dc.b '  bytes',$D,$A,0
 bss
 align
_SSP:          ds.l    1   ; Address of the system stack will be stored here.
start_time:    ds.l    1   ; Variable for time at start of AUT processing.
memory:        ds.w    1   ; Variable for AUT's requisite memory.
time_header:   ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT processing time.
memory_header: ds.l    1   ; Points to address of header which is to precede
                           ; the reported AUT requisite memory.
heading:       ds.l    1   ; Null terminated heading or NULL string.
program_end:   ds.l    0
 end


Figure 7.8. AUT_DATA's execution results.

AUT_DATA Program Results

  Elapsed time for lea    label(pc), Am 
                   move.l An, (Am):        205  milliseconds
  Memory required for first algorithm:       6  bytes

  Elapsed time for lea    label, Am 
                   move.l An, (Am):        230  milliseconds
  Memory required for second algorithm:      8  bytes

  Elapsed time for move.l An, label:       205  milliseconds
  Memory required for third algorithm:       6  bytes

 
Figure 7.9. Disassembly listing.  The first section is a 
complete listing of the adaptive algorithm during invocation 
by the first AUT.  Only partial listings are shown for the 
invocations by the second and third AUTs.  All listings were 
prepared before execution of the adaptive algorithm's 
performance loop.

 AUT_DATA's 1st AUT in TRAP9DAT

01FA36 99CA             SUBA.L A2,A4
01FA38 97CA             SUBA.L A2,A3
01FA3A 4DFA04C4         LEA $1FF00(PC),A6
01FA3E 2C88             MOVE.L A0,(A6)
01FA40 4DFA04C2         LEA $1FF04(PC),A6
01FA44 2C89             MOVE.L A1,(A6)
01FA46 4DFA04C0         LEA $1FF08(PC),A6
01FA4A 2C8D             MOVE.L A5,(A6)
01FA4C 2A4A             MOVEA.L A2,A5
01FA4E 41FA04A6         LEA $1FEF6(PC),A0
01FA52 208F             MOVE.L A7,(A0)
01FA54 4E6F             MOVE.L USP,A7
01FA56 207A04B0         MOVEA.L $1FF08(PC),A0
01FA5A 4A10             TST.B (A0)
01FA5C 6704             BEQ.S $1FA62
01FA5E 61000480         BSR $1FEE0
01FA62 207A049C         MOVEA.L $1FF00(PC),A0
01FA66 61000478         BSR $1FEE0
01FA6A 4DFA004C         LEA $1FAB8(PC),A6
01FA6E 360C             MOVE.W A4,D3
01FA70 41FA048C         LEA $1FEFE(PC),A0
01FA74 3003             MOVE.W D3,D0
01FA76 904B             SUB.W A3,D0
01FA78 3080             MOVE.W D0,(A0)
01FA7A 5343             SUBQ.W #1,D3
01FA7C 1CDD             MOVE.B (A5)+,(A6)+
01FA7E 51CBFFFC         DBRA D3,$1FA7C
01FA82 41FA0434         LEA $1FEB8(PC),A0
01FA86 43FA0484         LEA $1FF0C(PC),A1
01FA8A 93C8             SUBA.L A0,A1
01FA8C 3609             MOVE.W A1,D3
01FA8E 5943             SUBQ.W #4,D3
01FA90 2248             MOVEA.L A0,A1
01FA92 93CE             SUBA.L A6,A1
01FA94 2A4E             MOVEA.L A6,A5
01FA96 30280002         MOVE.W 2(A0),D0
01FA9A 2CD8             MOVE.L (A0)+,(A6)+
01FA9C D04B             ADD.W A3,D0
01FA9E D049             ADD.W A1,D0
01FAA0 3B400002         MOVE.W D0,2(A5)
01FAA4 5343             SUBQ.W #1,D3
01FAA6 1CD8             MOVE.B (A0)+,(A6)+
01FAA8 51CBFFFC         DBRA D3,$1FAA6
01FAAC 5347             SUBQ.W #1,D7

01FAAE 41FA044A         LEA $1FEFA(PC),A0
01FAB2 91C9             SUBA.L A1,A0
01FAB4 20B804BA         MOVE.L $4BA,(A0)
01FAB8 6004             BRA.S $1FABE
01FABA 00000000         ORI.B #0,D0
01FABE 45FAFFFA         LEA $1FABA(PC),A2
01FAC2 2488             MOVE.L A0,(A2)
01FAC4 51CFFFF8         DBRA D7,$1FABE
01FAC8 203804BA         MOVE.L $4BA,D0
01FACC 90BA0038         SUB.L $1FB06(PC),D0

01FAD0 4E4A             TRAP #$A
01FAD2 207A003C         MOVEA.L $1FB10(PC),A0
01FAD6 6114             BSR.S $1FAEC
01FAD8 323A0030         MOVE.W $1FB0A(PC),D1
01FADC 4E44             TRAP #4
01FADE 610C             BSR.S $1FAEC
01FAE0 41FA0016         LEA $1FAF8(PC),A0
01FAE4 6106             BSR.S $1FAEC
01FAE6 2E7A001A         MOVEA.L $1FB02(PC),A7
01FAEA 4E73             RTE
01FAEC 4850             PEA (A0)
01FAEE 3F3C0009         MOVE.W #9,-(A7)
01FAF2 4E41             TRAP #1
01FAF4 5C8F             ADDQ.L #6,A7
01FAF6 4E75             RTS
01FAF8 2020             MOVE.L -(A0),D0
01FAFA 6279             BHI.S $1FB75
01FAFC 7465             MOVEQ #$65,D2
01FAFE 730D             DC.W $730D
01FB00 0A000004         EORI.B #4,D0
01FB04 0EB000000000     BCLR #0,0(A0,D0.W)
01FB0A 00060006         ORI.B #6,D6
01FB0E FB75             DC.W $FB75
01FB10 0006FBC9         ORI.B #-$37,D6
01FB14 0006FB58         ORI.B #$58,D6
01FB18 040A             DC.W $40A
01FB1A 00000000         ORI.B #0,D0
01FB1E 00000000         ORI.B #0,D0

01FEAE 00000000         ORI.B #0,D0
01FEB2 00000000         ORI.B #0,D0
01FEB6 000051CF         ORI.B #-$31,D0
01FEBA FBFE             DC.W $FBFE 
01FEBC 203804BA         MOVE.L $4BA,D0
01FEC0 90BA0038         SUB.L $1FEFA(PC),D0
01FEC4 4E4A             TRAP #$A
01FEC6 207A003C         MOVEA.L $1FF04(PC),A0
01FECA 6114             BSR.S $1FEE0
01FECC 323A0030         MOVE.W $1FEFE(PC),D1
01FED0 4E44             TRAP #4
01FED2 610C             BSR.S $1FEE0
01FED4 41FA0016         LEA $1FEEC(PC),A0
01FED8 6106             BSR.S $1FEE0
01FEDA 2E7A001A         MOVEA.L $1FEF6(PC),A7
01FEDE 4E73             RTE
01FEE0 4850             PEA (A0)
01FEE2 3F3C0009         MOVE.W #9,-(A7)
01FEE6 4E41             TRAP #1
01FEE8 5C8F             ADDQ.L #6,A7
01FEEA 4E75             RTS
01FEEC 2020             MOVE.L -(A0),D0
01FEEE 6279             BHI.S $1FF69
01FEF0 7465             MOVEQ #$65,D2
01FEF2 730D             DC.W $730D
01FEF4 0A000004         EORI.B #4,D0
01FEF8 0EB000000000     BCLR #0,0(A0,D0.W)
01FEFE 00060006         ORI.B #6,D6
01FF02 FB75             DC.W $FB75
01FF04 0006FBC9         ORI.B #-$37,D6
01FF08 0006FB58         ORI.B #$58,D6

 AUT_DATA's 2nd AUT in TRAP9DAT

01FAAE 41FA044A         LEA $1FEFA(PC),A0
01FAB2 91C9             SUBA.L A1,A0
01FAB4 20B804BA         MOVE.L $4BA,(A0)
01FAB8 6004             BRA.S $1FABE
01FABA 00000000         ORI.B #0,D0
01FABE 45F90006FB40     LEA $6FB40,A2
01FAC4 2488             MOVE.L A0,(A2)
01FAC6 51CFFFF6         DBRA D7,$1FABE
01FACA 203804BA         MOVE.L $4BA,D0

 AUT_DATA's 3rd AUT in TRAP9DAT

01FAAE 41FA044A         LEA $1FEFA(PC),A0
01FAB2 91C9             SUBA.L A1,A0
01FAB4 20B804BA         MOVE.L $4BA,(A0)
01FAB8 6004             BRA.S $1FABE
01FABA 00000000         ORI.B #0,D0
01FABE 23C80006FB4E     MOVE.L A0,$6FB4E
01FAC4 51CFFFF8         DBRA D7,$1FABE
01FAC8 203804BA         MOVE.L $4BA,D0


     In figure 7.9, you can see that only in the performance 
loop for the first AUT does the AUT reference an address 
that is located within the adaptive algorithm's space.  The 
instructions in the other two AUT's reference an address 
that is located within the invoking program's space.  
Knowing how the declared data space will be referenced, you 
can choose the addressing mode that forces the reference to 
be performed in the manner most suited to specific 
applications.  The most important difference between this 
adaptive algorithm and the previous is that this one permits 
instructions to write to a data area without disrupting the 
adaptive algorithm.

Wrapping It Up

     I am going to wrap up this chapter with two more 
comparative programs.  Both programs were executed after the 
custom traps were installed with CUSTOM.PRG.  Program 40 was 
designed to confirm or refute the statement on page 113 of 
the Stan Kelly-Bootie book which asserts that MOVEA.Z 
#<label>, A0 is equivalent to LEA <label>, A0, and faster.  
Program 40 should be assembled in PC-relative mode, saved 
with a TOS extension; then the name of the file should be 
changed to LEAMOVER in the assempro editor, and that file 
should be assembled in Relocatable mode.  Figure 7.10 shows 
the results of LEAMOVEA.TOS; figure 7.11 shows those of 
LEAMOVER.TOS.

Program 40. A program that compares the execution speed and 
requisite memory of two instructions that load an address 
into an address register.
  
 ; Program Name: LEAMOVEA.S
 ;      Version: 1.001

 ; Assembly Instructions:

 ;    Assemble with ASSEMPRO and save with a TOS extension.

 ; Execution Instructions:

 ;     Execute from the desktop; or execute SPAWN.TTP, type LEAMOVEA.TOS on
 ; its command line and view this program's output in LEAMOVEA.DAT.

 ; Program Function:
 
 ;    Confirms (or refutes) the statement on page 113 of the Stan Kelly-
 ; Bootle book, to wit: MOVEA.Z #<label>, A0 is equivalent to LEA, and
 ; faster.

 ;    For each of the two methods of loading the address of a string into
 ; and address register, calculates the memory occupied by each method, and
 ; calculates the execution time in milliseconds required for 50,000
 ; executions of each.

 ; PROGRAM RESULTS:

 ;      When the program containing the two instructions under discussion
 ; is assembled in AssemPro's Relocatable mode, the instructions are
 ; equivalent in speed and requisite memory.

 ;      However, when the program is assembled in AssemPro's PC-relative
 ; mode, the LEA instruction is faster and requires less memory.  The claim
 ; that the MOVEA.Z instruction is faster than the LEA instruction is,
 ; therefore, soundly refuted.

 ;      But, when the program is assembled in PC-relative mode, the MOVEA.Z
 ; instruction does not move the correct value into the address register,
 ; so there is really no choice when either pc-relative addressing or
 ; PC-relative assembly is used--LEA must be used then.

calculate_program_size:
 lea        -$102(pc), a1       ; Fetch basepage start address.
 lea        program_end, a0     ; Fetch program end = array address.
 trap       #6                  ; Return unused memory to op system.
 lea        stack, a7

initialize_registers_1:
 lea        header_1, a0       
 lea        header_2, a1
 lea        lea_start, a3
 lea        lea_end, a4
 lea        heading, a5
 move.w     #50000, d7
 trap       #9

initialize_registers_2:
 lea        header_3, a0       
 lea        header_4, a1
 lea        movea_start, a3
 lea        movea_end, a4
 lea        heading, a5
 move.b     #0, (a5)            ; Store a NULL in first byte to create a
 move.w     #50000, d7          ; null string so that heading gets printed
 trap       #9                  ; only once.

terminate:
 trap       #8

lea_start:
 lea        newline, a2         ; Instruction in the loop.
lea_end:

movea_start:
 movea.l     #newline, a2       ; Instruction in the loop.
movea_end:

 data
heading:      dc.b       'LEAMOVEA Execution Results',$D,$A,$D,$A,0
header_1:     dc.b       '  Elapsed time for LEA:    ',0
header_2:     dc.b       '  Memory required for LEA:    ',0
header_3:     dc.b $D,$A,'  Elapsed time for MOVEA:  ',0
header_4:     dc.b       '  Memory required for MOVEA:  ',0
newline:      dc.b $D,$A,0
 bss
 align
              ds.l 96
stack:        ds.l  0
program_end:  ds.l  0
 end

  
Figure 7.10. Execution results for LEAMOVEA.TOS.

LEAMOVEA Execution Results

  Elapsed time for LEA:      130  milliseconds
  Memory required for LEA:     4  bytes

  Elapsed time for MOVEA:    155  milliseconds
  Memory required for MOVEA:   6  bytes
  
  
Figure 7.11. Execution results for LEAMOVER.TOS.

LEAMOVER Execution Results

  Elapsed time for LEA:      155  milliseconds
  Memory required for LEA:     6  bytes

  Elapsed time for MOVEA:    155  milliseconds
  Memory required for MOVEA:   6  bytes
  
  
     The data shown in figure 7.11 confirms that the 
execution speed and requisite memory for the two 
instructions are equivalent when the program in which they 
reside is assembled in the Relocatable mode.  However, the 
data in figure 7.10 shows that when the program is assembled 
in PC-relative mode, or when pc-relative addressing is used 
in the source operand of the LEA instruction, that 
instruction is faster and uses less memory.
     But there is more to this comparison then is readily 
apparent.  Figure 7.12 is a partial disassembly of the 
adaptive algorithm during invocation of the two PC-relative 
AUT's.  There you can see the futility and danger of trying 
to use the movea instruction to load an address in a PC-
relative assembled program.  The address that is actually 
loaded is located beyond the space of both the invoking 
program and the adaptive algorithm.  Figure 7.13 shows that 
either instruction can be used to load an address that is 
located within the invoking algorithm's space.

Figure 7.12. Partial disassembly of the adaptive algorithm 
during invocation by the two AUT's in LEAMOVEA.TOS.

 LEAMOVEA.TOS partial disassembly in trap

 LEAMOVEA.TOS was prepared by assembling LEAMOVEA.S in AssemPro's PC-relative
 mode.  The address being loaded into A2 by the LEA instruction is located
 within the space of the adaptive algorithm.

017BCA 45FA009F         LEA $17C6B(PC),A2
017BCE 51CFFFFA         DBRA D7,$17BCA

 The address being loaded into A2 by the MOVEA instruction decimal 233 and is
 located beyond the space of the adaptive algorithm and that of the invoking
 program.

017BCA 247C000000E9     MOVEA.L #$E9,A2
017BD0 51CFFFF8         DBRA D7,$17BCA

  
Figure 7.13. Partial disassembly of the adaptive algorithm 
during invocation by the two AUT's in LEAMOVER.TOS.

 LEAMOVER.TOS partial disassembly in trap

 LEAMOVER.TOS was prepared by assembling LEAMOVEA.S in AssemPro's Relocatable
 mode.  The address being loaded into A2 by the LEA instruction is located
 within the space of the invoking algorithm.

017BCA 45F90006D6AF     LEA $6D6AF,A2
017BD0 51CFFFF8         DBRA D7,$17BCA

 The address being loaded into A2 by the MOVEA instruction is located within
 the space of the invoking algorithm.

017BCA 247C0006D6AF     MOVEA.L #$6D6AF,A2
017BD0 51CFFFF8         DBRA D7,$17BCA

  
     Based on the data produced and shown in figures 7.10, 
7.11, 7.12 and 7.13, I conclude that Mr. Kelly-Bootle's 
claim is soundly refuted, and furthermore, when the program 
in which the instructions reside is assembled in PC-relative 
mode, the MOVEA instruction does not move the correct value 
into the address register, so there is really no choice when 
either pc-relative addressing or PC-relative assembly is 
used.  In either of those two cases, the LEA instruction 
must be used.

Just One More, I Promise

     Program 41 compares pea (a0) to move.l a0, -(sp).  I am 
including this program for two reasons.  The first reason is 
to confirm that they are equivalent; the second is to give 
you an example of the kind of information that is contained 
in the Thomas P. Skinner book--the kind of information that 
prompted me to recommend it.  The results of program 41's 
execution follow the listing.  Personally, I think that the 
PEA instruction is the more elegant.

Program 41. Compares two ways of pushing the contents 
of an address register onto the stack.    
  
 ; Program Name: PEA_MOVE.S
 ;      Version: 1.001

 ; Assembly Instructions:

 ;    Assemble in PC-relative mode and save with a TOS extension.

 ; Program Function:

 ;    Compares the relative speed and memory requirements of "pea (a0)" to
 ; that of "move.l a0, -(sp)".  The execution time reported is for
 ; 50,000 executions of each instruction.

 ; Execution Note:

 ;    Invokes traps that are installed by CUSTOM.PRG during boot.

calculate_program_size:
 lea        -$102(pc), a1       ; Fetch basepage start address.
 lea        program_end, a0     ; Fetch program end = array address.
 adda.l     #200512, a0         ; Add in extra large stack space.
 movea.l    a0, a7              ; Point A7 to this program's stack.
 trap       #6                  ; Return unused memory to op system.

initialize_registers_1:
 lea        header_1, a0       
 lea        header_2, a1
 lea        pea_algorithm_start, a3
 lea        pea_algorithm_end, a4
 lea        heading, a5
 move.w     #50000, d7
 trap       #9

initialize_registers_2:
 lea        header_3, a0       
 lea        header_4, a1
 lea        move_algorithm_start, a3
 lea        move_algorithm_end, a4
 lea        heading, a5
 move.b     #0, (a5)            ; Store a NULL in first byte to create a
 move.w     #50000, d7          ; null string so that heading gets printed
 trap       #9                  ; only once.

terminate:
 trap       #8

pea_algorithm_start:
 pea        (a0)                ; Instruction in the loop.
pea_algorithm_end:

move_algorithm_start:
 move.l     a0, -(sp)           ; Instruction in the loop.
move_algorithm_end:
         
 data
heading:      dc.b       "PEA_MOVE Program Results",$D,$A,$D,$A,0
header_1:     dc.b       "  Elapsed time for pea (a0):         ",0
header_2:     dc.b       "  Memory required for pea (a0):         ",0
header_3:     dc.b $D,$A,"  Elapsed time for move.l a0, -(sp): ",0
header_4:     dc.b       "  Memory for move.l a0, -(sp)           ",0
 bss
 align                       
program_end:  ds.l  0 
 end

PEA_MOVE Program Results

  Elapsed time for pea (a0):           155  milliseconds
  Memory required for pea (a0):          2  bytes

  Elapsed time for move.l a0, -(sp):   155  milliseconds
  Memory for move.l a0, -(sp)            2  bytes
  

Conclusion

     The thrust of this chapter was twofold.  First, I 
wanted to present an algorithm that would permit shorter 
versions of programs designed to obtain performance or 
comparative data.  Second, in doing that, I wanted to 
illustrate the inherent power of self-modifying algorithms.  
There are many more things that I could say about such 
algorithms, but I can't allow myself to be drawn into that 
provocative subject--lest I abandon the rest of the book.  I 
leave you with this thought.  Suppose that you learned to do 
truly powerful things with your personal computer.  With 
whom would you share your secrets?  Is it possible that you 
might even discourage others from traveling the routes that 
led to your own success?