APR 1988                FAT-VIDEO 1.21  SETVM           Page V-1



        SETVM(MODE)-Set the Video Mode

        Usage:

          call setvm(mode)

          integer*2 mode

          inputs: mode

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

          This program sets the video mode. The available modes are
        defined below.

        See also getmod().

        mode  Display
        ----   --------
        00   = 40*25 text B&W,cga
        01   = 40*25 color text,cga
        02   = 80*25 B&W text
        03   = 80*25 color text
        04   = 320*200 4-color,cga
        05   = "   "    "         ,color burst off
        06   = 640*200 2-color,cga
        07   = Mono & EGA display
        08   = 160*200 pc jr
        09   = 320*200 pc jr
        0A   = 640*200 pc jr
        0D   = 320*200 EGA
        0E   = 640*200 16-color EGA
        0F   = 640*350 mono graphics,EGA
        10   = 640*350 4/16 color graphics,EGA
                      (4/16-depends on ram)

        Int 10h, fx-00h

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  SETCP           Page V-2



        SETCP(ROW,COL,PAGE) - Set Cursor Position

        Usage:

          call setcp(row,col,page)

          integer*2 row,col,page

          inputs:   page,row,col

          returns:  none

          MS-Fortran 4.0 Large Model

           This subroutine sets the cursor position to
        the values given in row, column and page.  The row
        values are 0-23, the column values are 0-39 or 0-79
        depending on the text mode in use.
           The cursor may be located in graphics modes using
        this function the same as in text modes. See the
        setdp() function regarding pages.

        See also getcp().

        Int 10h, fx-02h

        CGA, Mono, EGA





        APR 1988                FAT-VIDEO 1.21  GETCP           Page V-3



        GETCP(ROW,COL,PAGE) - Get Cursor Position

        Usage:

          call getcp(row,col,page)

          integer*2 row,col,page

          inputs:   page

          returns:  row,col

          MS-Fortran 4.0 Large Model

           This subroutine gets the cursor position for
        the specified page, and returns row, and column.
        The row values are 0-23, the column values are
        0-39 or 0-79 depending on the text mode in use.
        See the setdp() function regarding pages in the
        various adapters.

        See also setcp().

        Int 10h, fx-03h

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  SETDP           Page V-4



        SETDP(PAGE) - SET the Display Page

        Usage:

          call setdp(page)

          integer*2 page

          inputs: page

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine sets the active display page.
        The Mono Adapter only has 1 display page. The CGA
        adapter has 8 display pages in modes 0 and 1, and
        4 text display pages in modes 2 and 3. See the chart
        below for other modes.

        See also getmod().

        Page    Modes(hex)
        -----   ----------
        0-7     00-01 CGA
        0-3     02-03 CGA
        0-7     02-03 EGA
        0-7     0D    EGA
        0-3     0E    EGA
        0-1     0F    EGA
        0-1     10h   EGA

        Int 10h, fx-05h

        CGA, EGA

       APR 1988                FAT-VIDEO 1.21  SCWUP           Page V-5


        SCWUP(LINES,ATTR,ULR,ULC,LRR,LRC) - Scroll Window Up

        Usage:

          call scwup(lines,attr,ulr,ulc,lrr,lrc)

          integer*2 lines,attr,ulr,ulc,lrr,lrc

          inputs:  lines,attr,ulr,ulc,lr,lrc

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine scrolls up the rectangular area defined
        by ulr,ulc and lrr,lrc the specified number of lines,
        filling the blank lines with the background color defined in
        the attribute byte.

           The attribute byte may be set by setab(), or from a
        call to getac().

        See  also scwdn(), cls(), getmod(), setvm().

        lines = 0-25 no. of lines to scroll(0 -> clears window)
        attr  = attribute byte to use, for background color
        ulr   = 0-24 upper left y-coord(row) corner of scroll region
        ulc   = 0-79 "     x "     " (col)              "
        lrr   = 0-24 lower right y-coord(row)
        lrc   = 0-79  "    "     x-coord(col)

        Int 10h, fx-06h

        CGA, Mono, EGA


       APR 1988                FAT-VIDEO 1.21  SCWDN           Page V-6



        SCWDN(LINES,ATTR,ULR,ULC,LRR,LRC) - Scroll Window Down

        Usage:

          call scwdn(lines,attr,ulr,ulc,lrr,lrc)

          integer*2 lines,attr,ulr,ulc,lrr,lrc

          inputs:   lines,attr,ulr,ulc,lrr,lrc

          returns:  none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine scrolls down the rectangular area defined
        by ulr,ulc and lrr,lrc the specified number of lines,
        filling the blank lines with the background color defined in
        the attribute byte.

           The attribute byte may be set by setab(), or returned from a
        call to getac().

        See also scwup(), cls(), getmod(), setvm().

        lines = 0-25 no. of lines to scroll(0 -> clears window)
        attr  = attribute byte to use, for background color
        ulr   = 0-24 upper left y-coord(row) corner of scroll region
        ulc   = 0-79 "     x "     " (col)              "
        lrr   = 0-24 lower right y-coord(row)
        lrc   = 0-79  "    "     x-coord(col)

        Int 10h, fx-07h

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  GETAC           Page V-7



        GETAC(ATTR,KAR,PAGE) - Get the Attribute and Character at the
                               cursor.

        Usage:

          call getac(attr,kar,page)

          integer*2 attr,kar,page

          inputs:   page

          returns:  attr,kar

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine gets the attribute and ascii character code,
        or extended character code, at the current cursor position. The
        display page is not needed in graphics modes. In graphics modes
        if the character is not recognized, a 0 is returned.

           This function will return the ascii or extended code in either
        text or graphics modes.

        See also getab(), wrtac(), wrtacp(), wrtas(), wrtasp().
                 wprint(), wprnas(), setab()

        attr = attribute byte, as output by setab()
        kar  = character ascii code
        Page = legal Page for adapter in use

        Int 10h, fx-08h

        CGA, Mono, EGA


        APR 1988                FAT-VIDEO 1.21  WRTAC           Page V-8


        WRTAC(ATTR,KAR,PAGE) - Write Attribute and Character at the cursor.

        Usage:

          call wrtac(attr,kar,page)

          integer*2 attr,kar,page

          inputs:   attr,kar,page

          returns:  none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine writes the attribute and character at the
        current cursor position. The attribute is the output of getac,
        or of setab. This function works in text and graphics modes.
        The cursor does not advance automatically. The attribute
        controls the color of the foreground, background, intensity,
        and blinking.
           The special codes backspace, carriage return, linefeed
        and bell are not recognized and do cause characters to be
        printed.

        Text Mode:

           The attribute byte can be defined by setab, and both fore
        and back should be specified. The values for the foreground
        color may be 0-15, background 0-7, blink 0 or 1, and inten
        0 or 1.

          Valid attributes in Mono are:
         1) Normal     7-foreground, 0-background
         2) Underlined 1-foreground, 0-background
         3) Reverse    0-foreground, 7-background
         4) Invisible  0-foreground, 0-backgound

            Blinking and Intensity work as well, and may be combined
            with the above foreground/backgound combinations.



       APR 1988                FAT-VIDEO 1.21  WRTAC           Page V-9



        Graphics Mode:

           The color attribute byte should be the foreground color
        0-15. If bit 7 is set the color is xor'ed with the background,
        thus assuring visibility. The attribute byte may be formed
        using setab, by inputting the fore color(0-15), 0 for the back
        color, 0 for inten, and a 1 for blink to xor the color, or 0
        in blink not to.

           Page need not be specified in graphics mode.

        See also getab(), getac(), wrtacp(), wrtas(), wrtasp().
                 wprint(), wprnas(), setab()

        Note: To set the background and border color in graphics
              see setpal(),setbc().

        attr = attribute byte
        kar  = character ascii code
        Page = legal Page for adapter in use

        Int 10h, fx-09h

        CGA, Mono, EGA


        APR 1988                FAT-VIDEO 1.21  WRTACP          Page V-10


        WRTACP(ATTR,KAR,ROW,COL,PAGE) - Write Attribute and Character at
                                        the position given.

        Usage:

          call wrtacp(attr,kar,row,col,page)

          integer*2 attr,kar,row,col,page

          inputs:   attr,kar,row,col,page

          returns:  none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine writes the attribute and character at the
        defined cursor position. The attribute is the output of getac,
        or of setab. This function works in text and graphics modes.
        The cursor does not advance automatically. The attribute
        controls the color of the foreground, background, intensity,
        and blinking.

           The special codes--backspace, carriage return, linefeed
        and bell--are not recognized and do cause characters to be
        printed.

        Text Mode:

           The attribute byte can be defined by setab, and both fore
        and back should be specified. The values for the foreground
        color may be 0-15, background 0-7, blink 0 or 1, and inten
        0 or 1.

        Note: To set the border color in text see setpal().

        Graphics Mode:

           The color attribute byte should be the foreground color
        0-15. If bit 7 is set, the color is xor'ed with the
        background thus assuring visibility. The attribute byte
        may be formed using setab by inputting the fore color (0-15),
        0 for the back color, 0 for inten, and 1 for blink to xor the
        color, or 0 in blink not to.

           Page need not be specified in graphics mode.

        See also getab(), wrtac(), getac(), wrtas(), wrtasp().
                 wprint(), wprnas(), setab()


        APR 1988                FAT-VIDEO 1.21  WRTACP          Page V-11





        Note: To set the background and border color in graphics
              see setpal().

        attr = attribute byte
        kar  = character ascii code
        row  = row(0-24)
        col  = col(0-79)
        Page = legal page for the adapter in use.

        Note: This function is a composite of setcp(), and wrtac().

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  WRTCH           Page V-12


        WRTCH(KAR,COLOR,PAGE) - Write a character at the curren cursor
                                position.
        Usage:

          call wrtch(kar,color,page)

          integer*2 kar,color,page

          inputs:   kar,color,page

          returns:  none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine writes the character at the current
        cursor position. In text mode color is not used.

           In graphics mode the color of the foreground does need
        to be specified.

           The special codes backspace, carriage return, linefeed
        and bell are not recognized and do cause characters
        to be printed.

        kar   = character ascii code
        color = foreground color in graphics
        Page = legal page for adapter in use

        Int 10h, fx-0Ah

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  SETPAL          Page V-13


        SETPAL(ID,COLOR) - Set Palette, Border, Background

        Usage:

          call setpal(id,color)

          integer*2 id,color

          inputs:   id,color

          returns: none

          MS-Fortran 4.0 Large Model

        Description:
           This subroutine sets the border color if in text mode, or the
        border and background color if in graphics mode. In either mode,
        it may also be used to select the active color palette for the
        4-color graphics mode.
           This function only works in the medium resolution graphics
        display (mode 4), on the CGA adapter. The Pcjr or a EGA adapter
        is required in text modes. To set the CGA border color in text
        modes use setbc().

        Text Modes:
        ID    = 0  -> sets border color - EGA only
                1  -> sets palette to use
        COLOR = 0-15 for ID = 0  set border color
                0-1  for ID = 1  set palette

        Graphics Modes:
        ID    = 0 -> sets color of background and border CGA,EGA
                1 -> sets palette to use
        COLOR = 0-3 for ID = 0, in mode4
                0-1 for ID = 1

        palette 0:
                color 0 = current background
                      1 = green
                      2 = red
                      3 = brown
        palette 1:
                color 0 = current background
                      1 = cyan
                      2 = magenta
                      3 = white

        Int 10h, fx-0Bh

        CGA

       APR 1988                FAT-VIDEO 1.21  WRTGP           Page V-14


        WRTGP(COLOR,ROW,COL) - Write Graphics Pixel.

        Usage:

          call wrtgp(color,row,col)

          integer*2 color,row,col

          inputs:  color,row,col

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine writes the graphic pixel at the specified row
        and column with the given color.

        color = legal pixel values: in mode 4,5 med res(0-3)
                                    in mode 6 high res(0-1)
                                    other modes, see your EGA manual.
        row = row(y) coord
                modes: 4,6,0Dh,0Eh(0-199)
                modes: 0Fh-10h(0-349)


        col   = column(x) coord:
                modes: 4,5,0Dh (0-319)
                modes: 6,0Eh,10h(0-639)

        See also getgp().

        Int 10h, fx-0Ch

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   GETGP           Page V-15


        GETGP(COLOR,ROW,COL) - Get Graphics Pixel Color.

        Usage:

          call getgp(color,row,col)

          integer*2 color,row,col

          inputs:   row,col

          returns:  color

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine reads the graphic pixel at the specified row
        and column with the given color.

        color = legal pixel values: in mode 4,5 med res(0-3)
                                    in mode 6 high res(0-1)
                                    EGA - see your manual.
        row = row(y) coord
                modes: 4,6,0Dh,0Eh(0-199)
                modes: 0Fh-10h(0-349)

        col   = column(x) coord:
                modes: 4,5,0Dh (0-319)
                modes: 6,0Eh,10h(0-639)

        Int 10h, fx-0Dh

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   CHTEL           Page V-16


        CHTEL(CHAR,PAGE,COLOR) - Write a Character in Teletype mode.

        Usage:

          call chtel(char,page,color)

          integer*2 char,page,color

          inputs:  char,page,color

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine writes a character to the specified
        page, in the specified foreground color, in graphics mode.

           This function advances the cursor after each write.
        Automatic line wrapping and scrolling are also provided.

           The special codes--backspace, carriage return, linefeed
        and bell--are recognized and do not cause characters
        to be printed.

        CHAR  = character to write.
        PAGE  = Page to write to, not needed in graphics modes.
        COLOR = color of foreground of character, in graphics only.

        See also wrtch().

        Int 10h, fx-0Eh

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   GETMOD          Page V-17



        GETMOD(MODE,NCOL,PAGE) - Get Mode, Number of Columns, and active page.

        Usage:

          call getmod(mode,ncol,page)

          integer*2 mode,ncol,page

          inputs:  none

          returns: mode,ncol,page

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine gets the current screen mode, number of columns
        on screen, and display page.

        See also setvm().

        mode  Display
        ----   --------
        00   = 40*25 text B&W,cga
        01   = 40*25 color text,cga
        02   = 80*25 B&W text
        03   = 80*25 color text
        04   = 320*200 4-color,cga
        05   = "   "    "         ,color burst off
        06   = 640*200 2-color,cga
        07   = Mono & EGA display
        08   = 160*200 pc jr
        09   = 320*200 pc jr
        0A   = 640*200 pc jr
        0D   = 320*200 EGA
        0E   = 640*200 16-color EGA
        0F   = 640*350 mono graphics,EGA
        10   = 640*350 4/16 color graphics,EGA
                      (4/16-depends on ram)
        EGA,VGA: See your manual.

        mode = active mode
        ncol = 40 or 80 columns
        Page = active page


        Int 10h, fx-0Fh

        CGA, Mono, EGA


       APR 1988                FAT-VIDEO 1.21   SETAB           Page V-18


        SETAB(ATTR,FOR,BACK,INT,BLINK) - Set the Attribute Byte.

        Usage:

          call setab(attr,fore,back,int,blink)

          integer*2 attr,fore,back,int,blink

          inputs:   fore,back,int,blink

          returns:  attr

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine forms an attribute byte from the input
        foreground, background, intensity, and blink bytes.

        See also getab().

        ATTR  = attribute byte
        FORE  = foreground color: (0-15), B&W: (0,1,7)
        BACK  = background color: (0-7),  B&W: (0,7)
        INT   = intensity  0-normal, 1-high
        BLINK = blinking   0-off, 1-on

                Colors
                ------
        0 Black         8  Gray
        1 Blue          9  Light Blue
        2 Green         10 Light Green
        3 Cyan          11 Light Cyan
        4 Red           12 Pink
        5 Magenta       13 Light Magenta
        6 Brown         14 Yellow
        7 White         15 Bright White

        Int none

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   GETAB           Page V-19


        GETAB(ATTR,FORE,BACK,INT,BLINK) - Get the Attribute Byte Values.

        Usage:

          call getab(attr,fore,back,int,blink)

          integer*2 attr,fore,back,int,blink

          inputs:  attr

          returns: fore,back,int,blink

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine determines from the attribute byte the
        input foreground, background, intensity, and blink bytes.

        See also setab().

        ATTR  = attribute byte
        FORE  = foreground color: (0-15), B&W: (0,1,7)
        BACK  = background color: (0-7),  B&W: (0,7)
        INT   = intensity  0-normal, 1-high
        BLINK = blinking   0-off, 1-on

                Colors
                ------
        0 Black         8  Gray
        1 Blue          9  Light Blue
        2 Green         10 Light Green
        3 Cyan          11 Light Cyan
        4 Red           12 Pink
        5 Magenta       13 Light Magenta
        6 Brown         14 Yellow
        7 White         15 Bright White

        Int none

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   WRTAS           Page V-20


        WRTAS(ATTR,STRING) - Write Attribute and String at the cursor.

        Usage:

          call wrtas(attr,string)

          integer*2    attr
          character*80 string

          inputs:  attr,string

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This routine writes a string to the screen using the
        attribute byte given.  Special characters are not recognized,
        and are all printed. No carriage return, linefeeds or
        backspace functions work with this function. The string is
        written at the current cursor position.

           In graphics mode, if bit 7 is set in the attribute byte,
        that is if blink is set in a call to setab() and you are in
        graphics mode, then the foreground color is xor'ed with the
        background screen to ensure the character is visible. In text
        mode, the blink byte simply causes the character to blink. Any
        input string must end with a character(0), the null character,
        as shown below.

        See also wrtasp(), wrtac(), wrtacp().

        character*80 string
        string = 'text'//char(0)  Most compilers allow this.
                 'text`'          All compilers allow this.
                 'text'C          Microsoft only.

        ATTR   = attribute byte define by setab()
        STRING = N-byte string terminated with null character

        Int none

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   WRTASP          Page V-21



        WRTASP(ATTR,STRING,ROW,COL,PAGE) - Write the Attribute
                                           and String at Position.

        Usage:

          call wrtasp(attr,string,row,col,page)

          integer*2   attr,row,col,page
          character*n string

          inputs:  attr,string,row,col,page

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This routine writes a string to the screen using the attribute
        byte given.  Special characters are not recognized, and are all
        printed. No carriage return, linefeeds or backspace functions
        work with this function. The string is written at the row, column
        and page position specified on input. This function is otherwise
        identical to wrtas().

           In graphics mode, if bit 7 is set in the attribute byte, that
        is if blink is set in a call to setab() and were in graphics mode,
        then the foreground color is xor'ed with the background screen to
        ensure the character is visible. In text mode, the blink byte
        simply causes the character to blink. Any input string must end
        with a character(0), the null character, as shown below.

        character*80 string
        string = 'text'//char(0)        Most compilers allow this.
                 'text`'                All compilers allow this.
                 'text'C                Microsoft Only.

        See also wrtas(), wrtac(), wrtacp().

        ATTR   = attribute byte define by setab()
        STRING = N-byte string terminated with null character

        Int none

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21   PEEKB           Page V-22




        PEEKB(OFF,SEG,VAL) - Get BYTE at SEG:OFF, anywhere in memory.

        Usage:

          call peekb(off,seg,val)

          integer*2    off,seg or integer*4 off,seg
          integer*2    val

          inputs:  off,seg

          returns: val

          MS-Fortran 4.0 Large Model

        Description:

           This routine peeks at the byte located at seg:off and places it
        in the lower byte of VAL.
           This function must pass an integer*2 for VAL, and an integer*2 or
        integer*4 for off and seg.  If off and/or seg is passed
        as an integer*4, only the lower word is used. Seg and off must be
        declared as integer*4 if they exceed +32k or -32k, as this is the
        largest integer*2 value Fortran can assign. That is if you
        explicitly declare seg= #B800 (hexadecimal cga screen address),
        then seg must be declared as integer*4 or else the compiler will
        assign a negative value to seg. In general, just declare any seg
        definitions as integer*4. Note:  If a video function returns a
        segment address for later use it may be declared integer*2 in all
        cases, as the video functions treat integer*2 values as 0 through
        +64k (unsigned integers).

        See also peekw(), pokeb(),pokew(), allmem(), fremem().


        CGA, Mono, EGA



        APR 1988                FAT-VIDEO 1.21   PEEKW           Page V-23



        PEEKW(OFF,SEG,VAL) - Get WORD at SEG:OFF, anywhere in memory.

        Usage:

          call peekw(off,seg,val)

          integer*2    off,seg or integer*4 off,seg
          integer*2    val

          inputs:   off,seg

          returns:  val

          MS-Fortran 4.0 Large Model

        Description:

           This routine peeks at the word located at seg:off and places it
        in the variable VAL. This function must be passed an integer for
        VAL, and an integer*2 or integer*4 for off and seg.  If off and/or
        seg is passed as an integer*4, only the lower VAL is altered. Seg
        and off must be declared as integer*4 if they exceed +32k or -32k,
        as this is the largest integer*2 value Fortran can assign. That is
        if you explicitly declare seg= #B800 (hexadecimal cga screen
        address), then seg must be declared as integer*4, or else the
        compiler will assign a negative value to seg. In general, just
        declare any seg definitions as integer*4. Note:  If a video
        function returns a segment address for later use, it may be
        declared integer*2 in all cases as the video functions treat
        integer*2 values as 0 through +64k (unsigned integers).

        See also peekb(), pokeb(),pokew(),allemm(),fremem().

        Off     = offset
        Seg     = segment paragraph
        Val     = returned

        Int none

        CGA, Mono, EGA