APR 1988                FAT-VIDEO 1.21  GETMON          Page V-32


        GETMON(NRS,NCS,NRE,NCE,SEG) - Copy a screen window to memory at SEG.

        Usage:

          call getmon(nrs,ncs,nre,nce,seg)

          integer*2 nrs,ncs
          integer*2 nre,nce
          integer*2 seg or integer*4 seg

          inputs: nrs,ncs,nre,nce,seg

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine stores the window section defined by nrs,ncs
        and nre,nce on the screen into the buffer starting at seg.  It is
        up to the calling program to allocate storage via ALLMEM().

           This routine stores the monochrome buffers character and
        attribute bytes for the window defined, to memory at SEG.

           This routine reads directly from the monochrome video buffer,
        and may cause software incompatabilities.

           This function does not clear the window after saving it, but
        once saved you may do anything to the window area, and restore
        the saved window contents using PUTMON().

        See also getvid(), putvid(),getcga(),putcga().

        nrs = first row of window
        ncs = first col of window
        nre = last row of window
        nce = last col of window
        seg = segment of allocated memory, as output from ALLMEM().

        Note: To calcualte the number of paragraphs to request from ALLMEM()
              calculate the following:

                Npar= (((nr*nc)*2)+15)/16  ; nr=nre-nrs+1, nc=nce=ncs+1

        Example:
                Npar=  (((11*41)*2)+15)/16
                call ALLMEM(Npar,SEG,MaxPar)
                if(SEG.eq.7 .or. SEG.eq.8)Go To 1000 ;Error !
                call GETMON(0,0,10,40,SEG)

        See Wopen(),Wclose().
        Restrictions: 80 column mode only !

        Int none

        Mono, EGA

       APR 1988                FAT-VIDEO 1.21  PUTMON          Page V-33


        PUTMON(NRS,NCS,NRE,NCE,SEG) - Copy a window in memory at SEG to
                                      the screen.
        Usage:

          call putmon(nrs,ncs,nre,nce,seg)

          integer*2 nrs,ncs
          integer*2 nre,nce
          integer*2 seg or integer*4 seg

          inputs: nrs,ncs,nre,nce,seg

          returns: none

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine restores the window section defined by nrs,ncs
        and nre,nce onto the screen.  It is up to the calling program to
        free storage via FREMEM().

           This routine restores the monochrome buffers character and
        attribute bytes for the window defined.

           This routine writes directly to the mono video memory buffer.

        See also getvid(), putvid(),getcga(),putcga().

        nrs = first row of window
        ncs = first col of window
        nre = last row of window
        nce = last col of window
        Seg = segment address used in GETMON()

        Example:
                call PUTMON(0,0,10,40,seg)
                call FREMEM(Seg,Ier)
                if(Ier.ne.0)Go To 1000   ; Error !

        See Wopen(),Wclose().
        Restrictions: 80 column mode only !

        Int none

        Mono, EGA

       APR 1988                FAT-VIDEO 1.21  CLS             Page V-34


        CLS() - Clear the Screen.

        Usage:

          call cls()

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine scrolls the entire window up, effectively
        clearing the screen.

           This function determines the active page, gets the attribute
        byte at the cursor, and then scrolls the window, filling the
        blank lines with the color defined by the attribute bytes
        background color.

        See also scwup(), scwdn().

        Int 10h, fx-0Fh, 08h, 06h

        CGA,Mono


        APR 1988                FAT-VIDEO 1.21  RDKBD           Page V-35


        RDKBD(SCAN,KEY) - Read the keyboard.

        Usage:

          call rdkbd(SCAN,KEY)

          integer*2 scan,key

          inputs: none

          returns: scan,key

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine returns the ascii code from the keyboard and
        its scan code. This function doesn't echo the character read from
        the keyboard.

           If key is returned as zero then a special key was hit such as
        the function keys(F1,F2,..) or the cursor keys, or a combination
        of shift,ctrl,alt and a function key. The value
        of the special key is returned in the scan variable.

           If a normal key is struck then key returns the ascii code.
        Once read by rdkbd() a character is removed from the keyboard
        buffer. This function cannot be interrupted by a ctrl-c keypress.
        See chinp() to allow ctrl-c interrupts during a keyboard read.

        See also chinp(), kbdst(), kbdfl().

        scan = scan code if ascii, key code if special key
        key= ascii code or 0 for special key code


        Int 16, fx-00h

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  KBDST           Page V-36


        KBDST(SCAN,ACHAR) - Get the keyboard status.

        Usage:

          call kbdst(SCAN,ACHAR)

          integer*2 scan,key

          inputs: none

          returns: scan,key

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine reports whether a character is is ready at
        the keyboard.  If there are no characters ready then scan and
        key are zero.  If an ascii character is ready, it is returned in
        key.   If a special key is present, then key is zero and scan
        contains the key code.

           This function does not remove characters from the keyboard
        buffer though, as rdkbd() does.

           The keyboard buffer may be cleared by calling this function,
        and if a character is ready, reading it with rdkbd(), and
        doing this until no characters are found.

        See also rdkbd(), kbdfl(), chinp().

        scan = scan code if ascii, key code if special key
        key= ascii code or 0 for special key code

        Int 16h, fx- 02h

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  KBDFL           Page V-37


        KBDFL(FLAGS) - Get the keyboard flags.

        Usage:

          call kbdfl(Flags)

          integer*2 Flags

          inputs: none

          returns: flags

          MS-Fortran 4.0 Large Model

        Description:

           This subroutine returns the keyboard flags byte.  The flags
        indicate which special keys are pressed, such as left-shift,
        right-shift, insert, scroll lock, num lock, and ctrl.

           This is not a generally useful function from Fortran,
        especially with the other keyboard reads available, since
        they can read any key combination. There are some uses for this,
        if you are clever.

        See also rdkbd(), kbdst(), chinp().

        Flag = the low byte of flag has each bit set as defined below.

          Bit Set       Meaning         Dec Value
                7       Insert on       128
                6       Caps on         64
                5       Num Lock on     32
                4       Scroll Lock on  16
                3       Alt key down     8
                2       Ctrl key down    4
                1       Left-Shift down  2
                0       Right-Shift down 1


        Int 16h, fx-02

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  CHINP           Page V-38



        CHINP(KEY) - Get character from keyboard, no echo.

        Usage:

          call chinp(key)

          integer*2 key

          inputs: none

          returns: key

          MS-Fortran 4.0 Large Model Dos2.0

        Description:

          This program reads a character from the keyboard.  This input is
        unfiltered and waits for a keypress.  This function doesn't echo
        the keypress to the screen.

          To read extended key codes, call this routine twice. The first
        call returns zero to indicate a special extended code key, such as
        F1-F10.  A ctrl-c keypress during this function will terminate
        a program. Use rdkbd() to prevent ctrl-c interrupts during a
        keyboard read operation.

        See also rdkbd(), kbdst(), kbdfl().

        KEY = 0 Extended char code, call again for key id
        KEY > 0 ascii character, use char(key) to reference.

        Int 21, fx-08h.

       APR 1988                FAT-VIDEO 1.21  ALLMEM          Page V-39


        ALLMEM(NPAR,SEG,MAXPAR) - Allocate Memory, Dynamically.

        Usage:

          call allmem(NPAR,SEG,MAXPAR)

          integer*2 npar,seg,maxpar
                or
          integer*4 npar,seg,maxpar

          inputs: npar

          returns: seg,maxpar

          MS-Fortran 4.0 Large Model Dos2.0

        Description:

          This program attempts to allocate memory dynamically.  If
        successful it returns the paragraph segment in SEG.  If
        unsuccessful it returns the maximum available paragraphs in
        MAXSEG, and the error code in SEG.  Inputting 640k for NPAR
        returns available memory in MAXPAR if you want xbytes request
        (xbytes+15)/16 paragraphs.

        NPAR-   No. of paragraphs to allocate.
        SEG-    Segment address of allocated memory, or error code.
        MAXPAR- Maximum available memory, or actual allocated.

        See also fremem().

        Error Codes:
                SEG values if allocation failed.
                7 = memory blocks destroyed
                8 = insufficient memory

        Warning:
                SEG should be checked after each allocation.

        Int 21h, fx-48h

        CGA, Mono, EGA

           This only works with the first 640k.  It does not work with
        extended, expanded, or any other memory additions, just the first
        640k !!!



        APR 1988                FAT-VIDEO 1.21  FREMEM          Page V-40


        FREMEM(SEG,IER) - Free Memory.

        Usage:

          call fremem(SEG,IER)

          integer*2 seg,ier  or integer*4 seg,ier

          inputs: seg

          returns: ier

          MS-Fortran 4.0 Large Model Dos2.0

        Description:

          This program frees memory previously allocated.  Normally
        you should only free memory allocated via allmem().  On input, SEG
        is the paragraph segment to free.  On return, IER is set to 0 if
        memory was deallocated, otherwise IER is set to an error code, as
        below.

        SEG-    Segment address returned by allmem().
        IER-    Error code, as below

        See also allmem().

        Error Code:
                IER values
                  0 = no error
                  7 = memory control blocks destroyed
                  9 = bad segment id(not allocated?)

        Warning:
                IER should be checked after every call
                to fremem().

        Note:   DOS will free up any dynamically allocated memory when a
                program terminates.

       APR 1988                FAT-VIDEO 1.21  SETNUL          Page V-41


        SETNUL(STRING)   Null Terminate a String.

        Usage:

          call setnul(string)

          character*255 string

          inputs: string

          returns: string

          MS-Fortran 4.0 Large Model

        Description:

           This function replaces the '`' character with a 0 byte, the
        null terminator. This forms a c-string which is also equivalent
        to appending the char(0) to a string. The following are all identical
        strings as far as the video and window library are concerned.

        string = 'text'C                Used MS-Fortran only.
                or
        string = 'text'//char(0)        Used by many compilers.
                or
        string = 'text`'                Can be used by any compiler.
        call setnul(string)

           The video library functions can use the string defined as
        string = 'text`', it is treated as a null terminated string.  The
        '`' character is considered equivalent to char(0).

        The above string does not have to be passed to setnul() in order
        to be usable by the video library.  The setnul() function is provided
        to assist you in forming true null terminated strings should you
        need to.  The maximum string length, including the null terminator,
        is 255 bytes or anything less.

        CGA, Mono, EGA

       APR 1988                FAT-VIDEO 1.21  REVAB           Page V-42


        REVAB(ATTR,RATTR) - Reverse foreground and background in attribute.

        Usage:

          call revab(attr,rattr)

          integer*2  attr,rattr

          inputs: attr

          returns: rattr

          MS-Fortran Large Model

        Description:

           This function takes the input attribute and reverses the
        foreground and background colors.  It does not alter the
        blink or intensity bits.

        attr  = input attribute
        rattr = output attribute with reverse colors

        See also setab(), getab().


       APR 1988                FAT-VIDEO 1.21  SETBC           Page V-43


        SETBC(COLOR) - Set CGA border color in text modes.

        Usage:

          call setbc(color)

          integer*2  color

          inputs: color

          returns: none

          MS-Fortran Large Model

        Description:

           This function sets the border color in text mode on the
        CGA adapter.  Do not use with the EGA or mono adapter.

           See setpal() to set border colors in graphics mode.

        color = 0-15

                Colors
                ------
        0 Black         8  Gray
        1 Blue          9  Light Blue
        2 Green         10 Light Green
        3 Cyan          11 Light Cyan
        4 Red           12 Pink
        5 Magenta       13 Light Magenta
        6 Brown         14 Yellow
        7 White         15 Bright White

        See also setab(), getab(), setpal().

        CGA Only !

       APR 1988                FAT-VIDEO 1.21  BVEF            Page V-44

+
        BVEF(Flag) - Get the BIOS video equipment flag.

        Usage:

          call bvef(bflag)

          integer*2  bflag

          inputs: none

          returns: bflag

          MS-Fortran Large Model

        Description:

           This function returns the BIOS video equipment flag.

        See also getadp().



        EGAF(Flag) - Get the EGA status flag.

        Usage:

          call egaf(bflag)

          integer*2  egaf

          inputs: none

          returns: egaf

          MS-Fortran Large Model

        Description:

           This function returns the EGA status flag.

        See also getadp().



       APR 1988                FAT-VIDEO 1.21  CGACOF          Page V-45


        CGACOF() - Turn off cursor on CGA adapter.

        Usage:

          call cgacof()

          inputs: none

          returns: none

          MS-Fortran Large Model

        Description:

           This function turns the cursor off on the CGA adapter.

        See also cgacon(), moncof(), moncon().



        CGACON() - Turn on cursor on CGA adapter.

        Usage:

          call cgacon()

          inputs: none

          returns: none

          MS-Fortran Large Model

        Description:

           This function turns the CGA cursor on.

        See also cgacof(), moncof(), moncon().


       APR 1988                FAT-VIDEO 1.21  MONCOF          Page V-46


        MONCOF() - Turn off cursor on monochrome display.

        Usage:

          call moncof()

          inputs: none

          returns: none

          MS-Fortran Large Model

        Description:

           This function turns the mono display cursor off.

        See also cgacof(), cgacon(), moncon().



        MONCON() - Turn on cursor on monochrome display.

        Usage:

          call moncon()

          inputs: none

          returns: none

          MS-Fortran Large Model

        Description:

           This function turns the mono display cursor on.

        See also cgacof(), cgacon(), moncof().



       APR 1988                FAT-VIDEO 1.21  COMLIN          Page V-47


        COMLIN(TAIL) - gets the user typed command line tail. DOS 2.0.

        Usage:

          call comlin(tail)

          character*127 tail

          inputs: none

          returns: tail

          MS-Fortran Large Model - DOS 3.0

        Description:

           This function returns the command line tail used to invoke
        the currently active program.

        tail - character string containing the command tail from the
               MS-DOS command line.



        GETDOS(MAJOR,MINOR) - returns does version .

        Usage:

          call getdos(major,minor)

          integer*2 major,minor

          inputs: none

          returns: major,minor

          MS-Fortran Large Model

        Description:

           This function returns the DOS version number. For DOS 3.20
        major=3 and minor = 20.


       APR 1988                FAT-VIDEO 1.21  GETTIM          Page V-48


        GETTIM(HR,MIN,SEC,HSEC)- returns DOS time.

        Usage:

          call gettim(hr,min,sec,hsec)

          integer*2 hr,min,sec,hsec

          inputs: none

          returns: hr,min,sec,hsec

          MS-Fortran Large Model

        Description:

           This function returns the time as DOS maintains it.

        HR= 0-23 , MIN=0-59, SEC=0-59, HSEC= 0-99



        CLRKBD() - clears the keyboard type ahead buffer.

        Usage:  call clrkbd()

          inputs: none ;   returns: none

        BEEP() - Beeps the speaker

        Usage:  call beep()

          inputs: none ;   returns: none

        CurOff() - Turns the cursor off using the video BIOS.

        Usage:  call CurOff()

          inputs: none ;   returns: none

        CurOn()  - Turns the cursor in using the video BIOS.

        Usage:  call CurOn()

          inputs: none ;   returns: none


       APR 1988                FAT-VIDEO 1.21  GETML          Page V-49


        GETML(NBYTES,SEG,OFF) - Allocate memory dynamically in Lahey
               Fortran. This memory comes from the Lahey Heap.

        Usage:

          call getml(nbytes,seg,off)

          integer*4 nbytes,seg,off

          inputs:  nbytes

          returns: seg,off

          For Lahey Compiler Only !

        Description:

           This function allocates memory dynamically in Lahey-Fortran
        and returns the segment and offset of the allocated memory. This
        memory is allocated from the Lahey Heap. That is Lahey allocates
        available DOS memory at startup. Any memory not required for
        code and data is available as Heap memory. See the Lahey WOPEN().
        source code for an example.

        Error Checking:
                If Seg = 0 and Off = 0 memory not allocated.

        RLSML(NBYTES,SEG,OFF) - Free memory dynamically in Lahey
               Fortran. This memory is returned to the Lahey Heap.

        Usage:

          call rlsml(nbytes,seg,off)

          integer*4 nbytes,seg,off

          inputs:  nbytes,seg,off

          returns: seg,off

          For Lahey Compiler Only !

        Description:

           This function retruns dynamically allocated memory to the Lahey
        Heap. The GETML() routine must have been used to allocate the
        memory prior to a call to free Heap memory. See the Lahey Wclose()
        routine for an example of this function.

        Error checking:

          On return: Seg = 0 safe return.
                         <>0 error return, memory not freed, or bad input.

       APR 1988                FAT-VIDEO 1.21  PEEKL          Page V-50



        PEEKL - Get a Long word value from memory.

        integer*2 OFF,SEG
        integer*4 VALUE
        call PEEKL(OFF,SEG,VALUE)

        call with:
        OFF - offset value from start of segment, <=64k
        SEG - segment value of long word location, <=64k

        returns:
        VALUE - the long word value is returned in this argument.

        example:
          call PEEKL(INT2(0),INT2(#0800),VALUE)
          This call returns long word stored at SEG= Hex 0800, OFF=0.

        Notes: An integer*2 is signed and may range from -32k to +32k.
            If the segment or offset values exceed this amount you should
            declare the segment and offset as integer*4.
          i.e.
            integer*4 SEG,OFF
            integer*4 VALUE
            SEG = #B800  <--- .gt. 32k
            OFF = 0
            call PEEKL(INT2(OFF),INT2(SEG),VALUE)


        POKEL - Store a long word value in memory.

        integer*2 OFF,SEG
        integer*4 VALUE
        call POKEL(OFF,SEG,VALUE)

        call with:
        OFF - offset value from start of segment, <=64k
        SEG - segment value of long word location, <=64k
        VALUE - the long word value to store.

        returns: nothing


        example: VALUE = 128
           call POKEL(Int2(0),Int2(#0800),VALUE)
          This call stores the value 128 at SEG=Hex 0800, OFF = 0.

        Notes: An integer*2 is signed and may be range from -32k to +32k.
            If the segment or offset values exceed this amount you should
            declare the segment and offset as integer*4.
          i.e.
            integer*4 SEG,OFF
            integer*4 VALUE
            SEG = #B800  <--- .gt. 32k
            OFF = 0
            call POKEL(INT2(OFF),INT2(SEG),VALUE)

       APR 1988                FAT-VIDEO 1.21  WRTS          Page V-51



        WRTS(STRING)
         Write a null terminated string to screen using the BIOS.

        character*n string
        string= 'Hello`' or string='Hello'//char(0)
        call wrts(string)

        input: string
        returns: nothing

        Description:

           This function writes a null terminated string to the video
        screen. The routine works in video modes 3 & 7. This is a text
        mode function only. The function writes to screen using the
        BIOS, for hardware compatibility.



        WRTSP(STRINg,ROW,COL,PAGE)

          Write a null terminated string to screen at the position given,
        using the BIOS, for compatibility.

        integer*2 row,col,page
        character*n string
        page=0
        row=2
        col=3
        string= 'Hello`' or string='Hello'//char(0)
        call wrts(string,row,col,page)

        input: string,row,col,page
        returns: nothing

        Description:

           This function writes a null terminated string to the video
        screen at the lcoation specified. The routine works in video
        modes 3 & 7. This is a text mode function only. The function
        writes to screen using the BIOS, for hardware compatibility.

        Row = Row starting position of 1st character, 0-24
        Col = Col starting position of 1st character, 0-79

       APR 1988                FAT-VIDEO 1.21  CPUT            Page V-52



        CPUT(STRING)

           Write a null terminated string to the screen, by writing
        directly to video ram.

        character*n string
        string= 'Hello`' or string='Hello'//char(0)
        call cput(string)

        inputs: string
        returns: none

        Description:

           This founction writs a null terminated string to the screen
        by writing directly to video ram. The routine works in either
        mode 7 or mode 3. This is a text mode function only. The direct
        video ram writing produces very fast output. This routine writes
        one byte per screen character, and is twice as fast as CPUTA, and
       CPUTAP.

        CPUTA(ATTR,STRING)

           Write a null terminated string to the screen using the attribute
        given, by writing directly to video ram.

        integer*2   attr
        character*n string
        attr = 7
        string= 'Hello`' or string='Hello'//char(0)
        call cput(attr,string)

        inputs: string,attr
        returns: none

        Description:

           This function writes a null terminated string to the screen
        using the attribute given, by writing directly to video ram.
        The routine works in either mode 7 or mode 3. This is a text
        mode function only. The direct video ram writing produces very
        fast output. This routine is slower than CPUT, and CPUTP.



       APR 1988                FAT-VIDEO 1.21  CPUTP          Page V-53



        CPUTP(STRING,ROW,COL)

           Write a null terminated string to the screen at the position
        specified, by writing directly to video ram.

        integer*2   row,col
        character*n string
        row=2
        col=2
        string= 'Hello`' or string='Hello'//char(0)
        call cputp(string,row,col)

        inputs: string,row,col
        returns: none

        Description:

           This founction writes a null terminated string to the screen
        at the position specified by writing directly to video ram.
        The routine works in either mode 7 or mode 3. This is a text
        mode function only. The direct video ram writing produces very
        fast output. This routine is faster than CPUTA, and CPUTAP.

        Row = Row starting position of 1st character, 0-24
        Col = Col starting position of 1st character, 0-79


        CPUTAP(ATTR,STRING,ROW,COL)

           Write a null terminated string to the screen using the attribute
        and location given, by writing directly to video ram.

        integer*2   attr,row,col
        character*n string
        attr = 7
        row=2
        col=7
        string= 'Hello`' or string='Hello'//char(0)
        call cput(attr,string)

        inputs: string,attr,row,col
        returns: none

        Description:

           This function writes a null terminated string to the screen
        using the attribute and location given, by writing directly to
        vide ram. The routine works in either mode 7 or mode 3. This is a
        text mode function only. The direct video ram writing produces very
        fast output. This routine is slower than CPUT, and CPUTP.

        Row = Row starting position of 1st character, 0-24
        Col = Col starting position of 1st character, 0-79


       APR 1988                FAT-VIDEO 1.21  CPUTAC          Page V-54



        CPUTAC(ATTR,VALUE)

           Write a character to the video screen using the attribute given,
        by writing directly to video ram.

        integer*2   attr
        integer*2   value
        attr = 7
        value= 65
        call cputac(attr,value)

        inputs: attr,value
        returns: none

        Description:

           This founction writes a character to the screen using the attribute
        given, by writing directly to video ram.
        The routine works in either mode 7 or mode 3. This is a text
        mode function only. The direct video ram writing produces very
        fast output. This routine is slower than CPUTC.

        ATTR = valid attribute byte.
        VALUE= ASCII value of character, or extended value of character.


        CPUTC(VALUE)

           Write a character to the video screen by writing directly to video
        ram, for fast screen output. This routine uses the current screen
        attribute.

        integer*2   value
        value= 65
        call cputc(value)

        inputs: attr,value
        returns: none

        Description:

           This founction writes a character to the screen, by writing directly
        to video ram, and uses the current screen attribute.
          The routine works in either mode 7 or mode 3. This is a text
        mode function only. The direct video ram writing produces very
        fast output. This routine is faster than CPUTAC.

        VALUE = ASCII value of character to write, or extended key value.