.pn 1
.pa
                      REQUIREMENTS AND CONVENTIONS

LIBRY  is  an indexed collection of object modules that can be linked to
other FORTRAN object  modules.   An  object  module  is  a  binary  file
produced  by  a  compiler  that contains machine instructions, data, and
linker flags.  LIBRY contains object modules written in  both  assembler
and  FORTRAN.   The  linker  will take the object module created by your
FORTRAN compiler, add to it what it needs  from  LIBRY,  and  create  an
executable  module.   In  order  to run any program, you must convert it
through these steps into an executable module (unless  you  are  running
interpretive  BASIC).   LIBRY  is  also  compatible  with  a  few  other
programming languages;  however, BASIC is not one of these.  If all  you
have is BASIC don't bother reading any further.  LIBRY is only available
in object module form (the source codes  are  not  available  under  any
circumstances).

On  the  PC  LIBRY  is contained in the file LIBRY.LIB.  On the HP-1000F
LIBRY is contained  in  the  file  %LIBRY.   On  the  HP-A900  LIBRY  is
contained in the file LIBRY.REL.

In  order  to  produce  a  compatible  object  module,  you  must have a
Microsoft FORTRAN compiler (version 3.31 or  later)  or  HP  FTN7X.   In
order  to  link  your object module and LIBRY, you must have a Microsoft
linker (LINK version 3.0 or later - I don't know what versions  of  LINK
that  come  with  DOS  are  compatible  - you get LINK when you purchase
FORTRAN anyway) or HP LOADR or LINK.  Your LINK  (or  DOS)  manual  will
tell  you  how  to access a library.  Refer to the LOADR or LINK manuals
for HP applications.

If you are using a PC you also need two other libraries that  come  with
Microsoft  FORTRAN  (FORTRAN.LIB  and MATH.LIB).  Do not attempt to link
LIBRY.LIB with an object module created by a FORTRAN compiler other than
Microsoft's.   Do  not  attempt  to link LIBRY.LIB with an object module
created by anyone's BASIC compiler.  Do not attempt  to  link  LIBRY.LIB
with  either of the two optional math libraries that come with Microsoft
FORTRAN (8087.LIB or ALTMATH.LIB) as these have some  unidentified  bugs
in them.

If  you  are  using  Microsoft  FORTRAN  don't  use any of the following
metacommands  in  your   FORTRAN   source   code:    $LARGE,   $DECMATH,
$NOFLOATCALLS,  or  $STORAGE  as  they  will  make  your  object  module
incompatible with LIBRY.LIB.

All integers must be of the type INTEGER*2.  Put

          IMPLICIT INTEGER*2 (I-N)

in EVERY program segment (this greatly increases speed too).   For  some
unknown  reason,  the  $STORAGE:2  command does not work as it should in
Microsoft FORTRAN.  All reals must be of the type REAL*4.  Put

          IMPLICIT REAL*4 (A-H,O-Z)

in EVERY program segment.  All double precision reals  must  be  of  the
type REAL*8.  Put

          IMPLICIT REAL*8 (A-H,O-Z)

in each program segment where double precision reals are used.  Remember
that all double precision constants must have a "D" in them in order  to
allocate  the  proper  space (don't pass "0." as a constant to a routine
expecting a double precision real - use "0.D0").  All logicals  must  be
of the type LOGICAL*2.  Character variables can be of any length (I hate
FORTRAN compilers that permit only fixed length character variables so I
do all character manipulation in assembler).

If  you  are  using  a  PC  you  don't  need  a  math coprocessor (Intel
8087/80287) in order to run a program linked with LIBRY;  but it makes a
TREMENDOUS  difference  (a  factor  of  120  or  so  for  floating point
operations).  The  vector  emulations  will  run  even  without  a  math
coprocessor;  but in that case the speed is already so slow that nothing
will help.  The improvement in speed with the vector  emulations  varies
greatly   depending   on  the  relative  speed  of  your  processor  and
coprocessor (not MHz speed but MIPS and FLOPS - a 5MHz 80286 is quite  a
bit  faster than a 5MHz 8086 while a 5MHz 8087 is just as fast as a 5MHz
80287).  The greatest improvement is  realized  on  a  PC  with  a  5MHz
8086/8087 pair;  and the least improvement is realized on an AT.