******************************  TEXT MODE  *******************************

ASM32 Text mode video subroutines (C) Copyright 1993 Douglas Herr
All rights reserved

ASM32 subroutines write directly to the video memory buffer, except
where noted.  ASM32 detects the default display type and screen
dimensions.  ASM32 assumes that CGA equipment requires "snow" control
and behaves accordingly.

EVGA32.LIB, provided with registration, does not include CGA "snow"
control and is somewhat faster and more compact.  EVGA32.LIB will be
best for most 32-bit PCs, but there are many 386SX and 386DX computers
which were upgraded from 16-bit processors with a variety of video systems.
For this reason ASM32 includes support for a variety of video systems.

Multiple pages of video memory are available except with MDA video adapters.
Pages supported by ASM32 are shown below:

video system   screen size    ASM32 support    BIOS support
-------------  -----------    --------------   ---------------
MDA            80 x 25        page  0          page  0
CGA, MCGA      80 x 25        pages 0 - 3      pages 0 - 3
CGA, EGA, VGA  40 x 25        pages 0 - 7      pages 0 - 7
EGA, VGA       80 x 25        pages 0 - 7      pages 0 - 7
EGA            80 x 43        pages 0 - 3      pages 0 - 3
VGA            80 x 50        pages 0 - 3      pages 0 - 3
SEGA, SVGA    132 x 25        pages 0 - 3      pages 0 - 3
SEGA, SVGA    132 x 43        pages 0 & 1      pages 0 & 1
HGC, HGC+, InC 80 x 25        pages 0 - 15     page  0
HGC+, InC      90 x 25        pages 0 - 13     page  0
HGC+, InC      80 x 43        page  0          page  0
HGC+, InC      90 x 43        page  0          page  0

   ASM32 subroutines assume that rows are the vertical dimension and
   columns are the horizontal dimension of a text-mode screen.  The upper
   left corner of the screen is at row=0 and col=0



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ANSICOLOR:   determines color attribute used by ANSI device driver.
             See also IsANSI.
Source:      anscolor.asm

Call with:   no parameters
Returns:     AH = color attribute
Uses:        EAX
Example:

        call  ansicolor         ; get ANSI screen color in AH


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BLINK:       enable or disable blinking attriutes
             disable or enable bright background attributes
Source:      blink.asm

Call with:   AL = 1 for blinking attributes/no bright background attributes
             AL = 0 for no blinking attributes/bright background attributes
Returns:     nothing
Uses:        nothing; all registers and flags are saved
Supports:    All ASM32 text modes
Example:

include codeseg.inc
        .
        .
        .

        mov     al,0
        call    blink            ; turn blinking attributes into bright
                                 ; background attributes
        .
        .
        .
        mov     al,1
        call    blink            ; turn bright background attributes into
                                 ; blinking attributes




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CRTINFO:     central control for ASM32 Text subroutines; determines
             active video system, screen size, page offset.
Source:      crtinfo.asm

Call with:   AH = 0 for page 0 information
             AH = -1 to calculate active page address
Returns:     AL = screen rows
             CH = screen columns
             ES:[EBX] = video buffer address
             DX = 3DAh if CGA, 0 if not CGA
               DX is used to monitor screen retrace, to avoid "snow"
               on older CGA systems.
Uses:        ES, AX, EBX, CX, DX, flags
Supports:    all ASM32 text modes


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CURSORCOLOR: set cursor color and enable color palette (InColor only)
Source:      curscolor.asm ($herc.asm)

Call with:   AH = color attribute (1 - 15)
Returns:     if CF = 0, no error
             if CF = 1, InColor card not installed
Uses:        Carry Flag
Supports:    Hercules InColor card only
Example:

extrn   cursorcolor:proc

.code
        .
        .
        .
        mov   ah,14        ; bright yellow cursor
        call  cursorcolor  ; enable InColor palette, set cursor color




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CURSOROFF:   make hardware cursor invisible at present location
Source:      cursor.asm

Call with:   no parameters
Returns:     nothing
Uses:        nothing
Supports:    CGA, MDA, HGC, HGC+, InC, EGA, VGA, SEGA, SVGA: text mode
Example:     call  cursoroff


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CURSORON:    move cursor to (row, col) and update cursor shape
             Cursor shape is underscore if INSERT is off, larger block
             if INSERT is on.  See also UCursorON.
Source:      cursor.asm (crtinfo.asm)

Call with:   DH = row offset from top of screen
             DL = column offset from left side
Returns:     nothing
Uses:        EAX
Supports:    CGA, MCGA, MDA, HGC, HGC+, InC, EGA, SEGA, SVGA, VGA: text mode
Example:     mov    dh,row        ; vertical coordinate on text screen
             mov    dl,column     ; horizontal coordinate
             call   cursoron




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETSCREEN:   save a screen page to a memory buffer
PUTSCREEN:   copy a saved screen page to the video buffer
Source:      screen.asm (crtinfo.asm, $wcopy.asm)

Call with:   ESI pointing to memory buffer
Returns:     nothing
Uses:        nothing; all flags and registers are saved
Supports:    All ASM32 text modes; includes CGA snow control
Example:     see ScreenBytes for example


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

HSCROLL:     scroll a portion of the screen left or right.
Source:      hscroll.asm ($wdata.asm, $wcopy.asm, a$putw.asm)

Call with:   EBX pointing to corner coordinates
             AH = color attribute for cleared columns
             ECX = number of columns to scroll
               scrolls left if ECX > 0, scrolls right if ECX < 0
               clears area if ECX = 0
Returns:     nothing
Uses:        nothing
Supports:    All ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10          ; row0
             dw     10          ; column0
             dw     20          ; row1
             dw     40          ; column1
@curseg   ends

include codeseg.inc

; code

             .
             .
             .
             lea    ebx,wdata   ; EBX points to window coordinates
             mov    ah,color    ; AH = color attribute for cleared columns
             mov    ecx,columns ; COLUMNS defined elsewhere
             call   hscroll     ; to clear entire window, columns = 0




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

PAINT:       change all color attributes on a text-mode screen
             without re-printing the text
Source:      paint.asm (crtinfo.asm, $paint.asm)

Call with:   AH = new color attribute
Returns:     nothing
Uses:        nothing
Supports:    All ASM32 text modes; includes CGA snow control
Example:     mov   ah,newcolor
             call  paint


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

RECOLOR:     change selected color attributes on a text-mode screen
             Replaces oldcolor attribute with newcolor, without
             re-printing the text.
Source:      recolor.asm (crtinfo.asm, $recolor.asm)

Call with:   AL = color to replace
             AH = new color attribute
Returns:     nothing
Uses:        nothing
Supports:    All ASM32 text modes; includes CGA snow control
Example:     mov   al,oldcolor
             mov   ah,newcolor
             call  recolor



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SCREENBYTES: calculate bytes required to save screen page
             Used with GetScreen and PutScreen.
Source:      scrbytes.asm (crtinfo.asm)

Call with:   no parameters
Returns:     EAX = number of bytes required
Uses:        EAX
Example:

include model.inc

include dataseg.inc

saved_pointer dd ?

@curseg ends

include codeseg.inc

          .
          .
          .

        call  screenbytes
        mov   ebx,eax
        sys   GetMemNear
        jc    drat               ; jump if error control needed
        mov   saved_pointer,esi
        call  getscreen          ; save the screen
          .
          .
          .
        mov   esi,saved_pointer
        call  putscreen          ; restore the initial screen



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SHOWTPAGE:   change video page shown on screen
Source:      tpage.asm (crtinfo.asm, $herc.asm)

Call with:   BL = page number
Returns:     AX = error code
             0 = no error
             -1 = bad page number
Uses:        AX
Supports:    All ASM32 text modes (except MDA equipment, some RamFont modes)
Example:     mov    bl,1               ; show page 1
             call   showtpage



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SNOWOFF:     disables CGA snow control
SNOWON:      enables CGA snow control (ASM32 default)
Source:      crtinfo.asm

Call with:   no parameters
Returns:     nothing
Uses:        no registers or flags
Example:

extrn  snowoff:near
extrn  getcrt:near

include codeseg.inc

; code
       .
       .
       .
       call   getcrt
       cmp    ax,2             ; ASM32 doesn't disable snow control
                               ; on MCGA systems
       jne    short continue
       call   snowoff          ; MCGA doesn't need snow control
continue:


       


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

STR2VBUF:    copies a string to video memory buffer, with selected
             color attribute; includes snow control for CGA systems
Source:      str2vbuf.asm

Call with:   ECX = maximum number of characters to print (will also stop
                  at NUL character)
             DX = 0 to disable snow control
                = 3DAh to enable CGA snow control
                  (if DX = 3DAh on systems without a color monitor,
                  the computer will jam up solid)
             ESI points to first character of string
             ES:[EDI] points to video buffer
             AH = color attribute
             DF = 0 (clear direction flag with CLD)
Returns:     EDI points to video buffer following string
             if AL = 0
                ESI points to byte following string's NUL terminator
             if AL <> 0
                ESI points to next byte in string after the last one
                printed on the screen
Uses:        AL, ECX, EDI, ESI, flags



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TCENTER:     prints a string on the screen, centered horizontally
TNCENTER:    prints ECX bytes of a string on the screen, centered horizontally
Source:      tcenter.asm (crtinfo.asm, str2vbuf.asm, strlen.asm)

Call with:   ESI pointing to the string
             DH = row to print the string on
             AH = color attribute
             (tncenter only) ECX = number of bytes to print
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

     lea     esi,string  ; ESI points to the string
     mov     dh,row
     mov     ah,attr     ; color attribute
     call    tcenter     ; center the string on row in DH




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TCLEAR:      clear a text-mode screen with specified color attribute
Source:      tclear.asm (crtinfo.asm, a$putw.asm)

Call with:   AH = color attribute
Returns:     nothing
Uses:        AL
Supports:    all ASM32 text modes; includes CGA snow control
Example:     mov    ah,color
             call   tclear


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TCOPY:       copies one page of text-mode video memory to another page
Source:      tcopy.asm (crtinfo.asm, tpage.asm, $herc.asm)

Call with:   BH = frompage, BL = topage
Returns:     if CF = 0, all OK
             if CF = 1 and AH = -1, frompage number is out-of-bounds
             if CF = 1 and AL = -1, topage number is out-of-bounds
Uses:        EAX, CF
Supports:    all ASM32 text modes, pages 0 - 15; includes CGA snow control
Example:     mov    bh,0               ; frompage
             mov    bl,1               ; copy from page 0 to page 1
             call   tcopy
             jc     oops               ; oh yuck - an MDA


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TFILL:       fill a text-mode screen with specified character and color
Source:      tclear.asm (crtinfo.asm, a$putw.asm)

Call with:   AH = color attribute, AL = fill character
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:
             mov    ah,color
             mov    al,char              ; AL = character to fill screen
             call   tfill




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TGETCHR:     read character and attribute from text screen
Source:      tgetchr.asm (crtinfo.asm)

Call with:   DH = screen row
             DL = screen column
Returns:     AH = color attribute
             AL = ASCII character code
Supports:    all ASM32 text modes; includes CGA snow control
Example:


extrn tgetchr:near

include dataseg.inc

; data

position label word
column   db 13
row      db 18

@curseg   ends

include codeseg.inc

; code
         .
         .
         .
         mov   dx,position
         call  tgetchr         ; returns with AL = ASCII character code
                               ;  and with AH = color attribute





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TLOAD:       loads a screen image disk file saved by TSave
Source:      tload.asm (crtinfo.asm)

Call with:   EDX = address of ASCIIZ filename in low memory
Returns:     if CF = 1, AX = MS-DOS file I/O error code
             if CF = 0, no error
Uses:        EAX, CF
Supports:    all ASM32 text modes; no CGA snow control
             see also TSave
Example:


extrn   tload:proc

include dataseg.inc

; data

filename  db 'tscreen.bin',0

@curseg   ends

include codeseg.inc

; code
     .
     .
     .
     lea   edx,filename
     call  tload






°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPAGE:       changes active page and shows new active page
Source:      tpage.asm (crtinfo.asm, $herc.asm)

Call with:   BL = page number
             for ASM32 subroutines writing directly to video memory.
             See also UseTPage and ShowTPage.  ASM32's active page is
             not affected by INT  10h mode changes.
             Page -1 may be used on two-monitor systems, directs ASM32
             video output to Monochrome screen (except cursor).
Returns:     AX = error code
             if AX = 0, no error
             if AX = -1, bad page number
             if AX = 1, page may be written to but cannot be shown
Uses:        AX
Supports:    text-mode screens, all row/column configurations
Example:     mov    bl,page
             call   tpage


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPRINT:      print ASCIIZ string directly to video buffer.
             String must be terminated by a NUL character.  The string
             may be in either low memory or high memory.
Source:      tprint.asm (crtinfo.asm, str2vbuf.asm)

Call with:   ESI pointing to the string
             DH = screen row, DL = screen column
             AH = color attribute
Returns:     ECX = bytes printed
Uses:        ECX
Supports:    all ASM32 text modes; includes CGA snow control
Example:
             lea     esi,string   ; ESI points to the string
             mov     dh,row
             mov     dl,column
             mov     ah,attr      ; color attribute
             call    tprint




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPRINTCE:    prints an ASCIIZ string on the screen at specified position
             and specified color, and clears from the end of the string
             to the right edge of the screen.  The string may be in either
             low memory or high memory.
Source:      tprintce.asm (crtinfo.asm, str2vbuf.asm, a$putw.asm)

Call with:   ESI pointing to the string
             DH = screen row, DL = screen column
             AH = color attribute
Returns:     ECX = bytes ptrinted
Uses:        ECX
Supports:    all ASM32 text modes; includes CGA snow control
Example:
             lea     esi,string   ; ESI points to the string
             mov     dh,row
             mov     dl,column
             mov     ah,attr      ; color attribute
             call    tprintce


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPRINTL:     print ASCIIZ string directly to video buffer, lower case
Source:      tprintl.asm (crtinfo.asm)

TPRINTU:     print ASCIIZ string directly to video buffer, upper case
Source:      tprintu.asm (crtinfo.asm)

             String must be terminated by a NUL character.  Similar to TPrint,
             but characters a - z are TPrinted as upper case A - Z (TPrintU)
             or characters A - Z are TPrinted as lower case a - z (TPrintL).
             The string itself is not altered.

Call with:   ESI pointing to the string
             DH = screen row, DL = screen column, AH = color attribute

Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

             lea     esi,string  ; ESI points to the string
             mov     dh,row
             mov     dl,column
             mov     ah,attr     ; color attribute
             call    tprintu


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPUTCHR:     write character and attribute to screen
Source:      tputchr.asm (crtinfo.asm)

Call with:   AL = ASCII character
             AH = color attribute
             DH = screen row
             DL = screen column
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

extrn tputchr:near

include   dataseg.inc

; data

position label word
column   db 13
row      db 18
color    db 32              ; white on blue background

@curseg   ends

include   codeseg.inc

; code
         .
         .
         .
         mov   dx,position
         mov   ah,color
         mov   al,'#'          ; character to write
         call  tgetchr         ; returns with AL = ASCII character code
                               ;  and with AH = color attribute




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TSAVE:       saves a screen image as a disk file; does not compress the image
Source:      tsave.asm (crtinfo.asm)

Call with:   EDX = address of ASCIIZ filename in low memory
Returns:     if CF = 1, AX = MS-DOS file I/O error code
             if CF = 0, no error
Uses:        E AX, CF
Supports:    All ASM32 text modes; no CGA snow control
             see also TLOAD
Example:

extrn   tsave:proc

include dataseg.inc

; data

filename  db 'tscreen.bin',0

@curseg   ends

include codeseg.inc

; code
     .
     .
     .
     lea   edx,filename
     call  tsave


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

UCURSORON:   similar to CursorON, but the underscore cursor is used regardles
             of the state of the INSERT toggle.  See also CursorON.
Source:      cursor.asm (crtinfo.asm)

Call with:   DH = row offset from top of screen
             DL = column offset from left side
Returns:     nothing
Uses:        AX
Supports:    text mode, all pages, all row/column configurations
Example:     mov    dh,row
             mov    dl,col
             call   ucursoron



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

USETPAGE:    establish ASM32's active page
Source:      tpage.asm (crtinfo.asm, $herc.asm)

Call with:   BL = page number
             ASM32 text-mode subroutines can be directed to any video
             page.  ASM32's active page is not affected by INT  10h
             mode changes.  UseTPage does not change the page shown
             on the screen.  See also TPage and ShowTPage.
             If newpage = -1, ASM32 video output is directed to a
             Monochrome screen
Returns:     AX = error code
             if AX = -1, bad page number
Uses:        AX, ES
Supports:    All ASM32 text modes
Example:     mov     bl,page
             call    usetpage




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VSCROLL:     scroll a portion of the screen up or down.
Source:      vscroll.asm ($wdata.asm, $wcopy.asm, a$putw.asm)

Call with:   EBX pointing to corners of scroll area
             AH = color attribute, ECX = number of rows to scroll
             Scrolls up if ECX > 0, scrolls down if ECX < 0, clears area
             if ECX = 0
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10               ; row0
             dw     10               ; column0
                                     ; (row0, column0) = upper left corner
             dw     20               ; row1
             dw     40               ; column1
                                     ; (row1, column1) = lower right corner
@curseg   ends

include codeseg.inc

; code
             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             mov    ah,color
             mov    ecx,3            ; scroll up 3 rows
             call   vscroll



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WCLEAR:      clear a rectangular portion of a text-mode screen
Source:      wclear.asm ($wdata.asm, crtinfo.asm, a$putw.asm)

Call with:   EBX pointing to box corner data
             AH = color attribute
Returns:     nothing
Uses:        AL, flags
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10               ; row0
             dw     10               ; column0
             dw     20               ; row1
             dw     40               ; column1

@curseg   ends

include codeseg.inc

; code
             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             mov    ah,color
             call   wclear           ; clear a box on the screen with corners
                                     ; at (row0, column0), (row1, column0),
                                     ; (row0, column1) and (row1, column1)





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WFILL:       fill a rectangular protion of a text-mode screen with
             specified character and attribute; variation of WClear
Source:      wclear.asm ($wdata.asm, crtinfo.asm, a$putw.asm)

Call with:   EBX pointing to box corner data
             AH = color attribute
             AL = fill character
Returns:     nothing
Uses:        flags
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10               ; row0:    top of fill area
             dw     10               ; column0: left side of fill area
             dw     20               ; row1:    last row of fill area
             dw     40               ; column1: right side of fill area

@curseg   ends

include codeseg.inc

; code
             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             mov    ah,color
             mov    al,'þ'           ; use ASCII 254 to fill
             call   wfill            ; fill a box on the screen with corners
                                     ; at (row0, column0), (row1, column0),
                                     ; (row0, column1) and (row1, column1)




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WFRAME:      draw a box on a text-mode screen
Source:      wframe.asm (a$wdata.asm, a$putw.asm, crtinfo.asm)

Call with:   EBX pointing to box corner data
             AH = color attribute
             AL = box character
             box character is the character associated with an ASCII code
             if AL = 0, a single line is used
             if AL = -1, a double line is drawn
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10               ; row0
             dw     10               ; column0
             dw     20               ; row1
             dw     40               ; column1

@curseg   ends

include codeseg.inc

; code
             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             mov    ah,color
             mov    al,'þ'           ; use ASCII 254 for boundary
             call   wframe           ; draw a box on the screen with corners
                                     ; at (row0, column0), (row1, column0),
                                     ; (row0, column1) and (row1, column1)




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WSIZE:       calculate the memory required to save a screen window
Source:      wsize.asm

Call with:   EBX pointing to row & column coordinates
             The row and column coordinates define the corners of the
             window.
Returns:     EAX = bytes required
Uses:        EAX
Supports:    All ASM32 text modes
Example:     

include dataseg.inc

; data

wdata        dw     10               ; row0
             dw     10               ; column0
             dw     20               ; row1
             dw     40               ; column1

@curseg   ends

include codeseg.inc

; code

             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             call   wsize            ; returns EAX = bytes required
             mov    ebx,eax
             sys    GetMemNear
             jc     oh_no            ; big problem if no space!




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WPAINT:      replace all color attributes in a window of the screen
Source:      wpaint.asm ($wdata.asm, crtinfo.asm, $paint.asm)

Call with:   EBX pointing to window coordinates
             AH = new color attribute
Returns:     nothing
Uses:        nothing; all registers and flags are saved
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10               ; row0
             dw     10               ; column0
             dw     20               ; row1
             dw     40               ; column1

@curseg   ends

include codeseg.inc

; code

             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             mov    ah,color         ; AH = new color attribute
             call   wpaint




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WPRINT:      print ASCIIZ string directly to the video buffer in a
             window of screen, with word wrap.  String must be terminated
             by a NUL character.  WPrint clears any portion of the window
             not occupied by the string.
Source:      WPRINT.ASM (crtinfo.asm, str2vbuf.asm, strlen.asm, $wdata.asm,
                         a$putw.asm)

Call with:   ESI pointing to the string
             EBX pointing to window corners
             AH = color attribute
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

extrn   wframe:proc, wprint:proc

include dataseg.inc

; data
wdata   dw 10,10,20,30          ; window corner data: upper left at row 10,
                                ; column 10; lower right at row 20, column 30
string  db "The quick brown fox jumped over the lazy dog's back",0

@curseg   ends

include codeseg.inc

; code
     .
     .
     .
     lea     esi,string   ; ESI points to the string
     lea     ebx,wdata    ; EBX points to corner data
     mov     ah,12        ; bright red!!
     call    wprint

     dec     wdata        ; stretch the window borders a bit
     dec     wdata+2      ; so I can draw a frame around the silly text
     inc     wdata+4
     inc     wdata+6
     mov     al,-1        ; double-line border
     mov     ah,14        ; bright yellow
     call    wframe



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WRECOLOR:    change selected color attributes in a window of the screen
Source:      wrecolor.asm ($wdata.asm, crtinfo.asm, $recolor.asm)

Call with:   EBX pointing to window corner data
             AL = color attribute to be replaced
             AH = new color attribute
Returns:     nothing
Uses:        nothing; all registers and flags are saved
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata        dw     10               ; row0
             dw     10               ; column0
             dw     20               ; row1
             dw     40               ; column1

@curseg   ends

include codeseg.inc

; code

             .
             .
             .
             lea    ebx,wdata        ; EBX points to window coordinates
             mov    ah,newcolor      ; AH = new color attribute
             mov    al,oldcolor      ; AL = color to be replaced
             call   wrecolor         ; replace oldcolor with newcolor
                                     ; within the window



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WRESTORE:    restore a portion of a text-mode screen from a buffer
WSAVE:       save a portion of a text-mode screen to a buffer
             (handy when using pop-up windows on the screen)
Source:      wsave.asm ($wdata.asm, crtinfo.asm, $wcopy.asm)

Call with:   EDI pointing to memory buffer
             EBX pointing to corner data
             The memory buffer must be sized to hold the entire window.
             See wsize.
Returns:     nothing
Uses:        nothing
Supports:    all ASM32 text modes; includes CGA snow control
Example:

include dataseg.inc

; data

wdata   dw 10               ; row0
        dw 10               ; column0
        dw 20               ; row1
        dw 40               ; column1
buffer  dw 2000h            ; oversize

@curseg   ends

include codeseg.inc

; code

        .
        .
        .
; save a part of the screen
        lea    ebx,wdata        ; EBX points to window coordinates
        lea    edi,buffer       ; point to buffer
        call   wsave
        .
        .
        .
; sometime later ...
; restore the window saved earlier
        lea    ebx,wdata        ; EBX points to window coordinates
        lea    edi,buffer       ; point to buffer
        call   wrestore