**** NOTICE ****
  This is a potentially hazardous routine, and I make no claims whatsoever
  about it's functionability or suitability for a given purpose.  By using
  this routine, you accept any problems that may occur by said use.
****************


Subroutine:  Reboot
Purpose:     Allow user to perform a warm start during program execution
Warnings:    You should ensure that all files have been closed properly
	     before calling this subroutine.  Mis-use can (and probably
	     will) result in corrupt data files.
Setup:	     Link the object file into the main program and declare the
	     subroutine:
	       $link "REBOT.OBJ"
	       declare sub Reboot()
Calling:     CALL Reboot


While other methods can be used to reboot a computer, this one takes
up only 9 bytes.  This is the only method that I have found that will
reliably reboot my computers.  Following is the .ASM code.....

	Public Reboot		; declare Reboot as a public subroutine

Code	Segment	Byte		; define code segment
	assume cs:code		; tell the compiler about the code segment

Reboot	Proc	Far		; reboot is a far process

	mov	ax,0ffffh	; push the segment
	push	ax		; and the offset
	mov	ax,0000h	; of the bios warm start routine
	push	ax		; onto the stack.
	retf			; run the routine.

Reboot	EndP			; end of reboot process

Code	EndS			; end of code segment

	End			; end of .asm program