TASM USER'S MANUAL


      TASM - A Table Driven Cross Assembler for the MSDOS* Environment






                             Thomas N. Anderson
                       Speech Technology Incorporated
                           837 Front Street South
                            Issaquah, WA   98072

                               February, 1989
                                Version 2.7

    [Speech Technology  Incorporated  manufactures electronic devices to
    aid  the  visually  impaired  employing   digital  speech  synthesis
    technology.]


    TASM  software  is  Copyright (C)  1985-1989  by  Speech  Technology
    Incorporated.  All rights reserved.

    This  document  is  Copyright  (C)  1985-1989  by Speech  Technology
    Incorporated.   All rights  reserved.   Permission   is  granted  to
    copy this document and  related software except for the source code.
    The source code,  distributed  to registered  users,   may be copied
    for the sole use of the registered user.

    Portions  of  TASM.EXE (C runtime library)  are Copyright  1987   by
    Microsoft Corporation.



     * MSDOS is a trademark of Microsoft Corporation.



    TASM - Table Driven Assembler Version 2.7                    Page 2


    TABLE OF CONTENTS

    SECTION                                                      PAGE
    _________________________________________________________________
    INTRODUCTION                                                    4
    INVOCATION                                                      5
      File Names                                                    5
      Option Flag: b - Binary Object Format                         6
      Option Flag: c - Contiguous Block Output                      6
      Option Flag: d - Define a Macro                               7
      Option Flag: e - Expand Source                                7
      Option Flag: f - Fill Memory                                  7
      Option Flag: h - Hex Table                                    7
      Option Flag: l - Label Table                                  7
      Option Flag: m - MOS Tehcnology Object Format                 7
      Option Flag: o - Set Number of Bytes per Object Record        7
      Option Flag: p - Page Listing File                            8
      Option Flag: q - Disable Listing File                         8
      Option Flag: r - Set Read Buffer Size                         8
      Option Flag: s - Enable Symbol File Generation                8
      Option Flag: t - Table Name                                   8
      Option Flag: x - Enable Extended Instruction Set              9
    ENVIRONMENT VARIABLES                                          10
      TASMTABS                                                     10
      TASMOPTS                                                     10
    SOURCE FILE FORMAT                                             11
    EXPRESSIONS                                                    13
      Labels                                                       13
      Constants                                                    13
      Location Counter Symbol                                      14
      Operators                                                    15
    ASSEMBLER DIRECTIVES                                           17
      ADDINSTR                                                     17
      BLOCK                                                        17
      BSEG/CSEG/DSEG/NSEG/XSEG                                     17
      BYTE                                                         18
      CODES/NOCODES                                                18
      DB                                                           18
      DW                                                           18
      DEFINE                                                       18
      DEFCONT                                                      20
      EJECT                                                        20
      ELSE                                                         20
      END                                                          21
      ENDIF                                                        21
      EQU                                                          21


    TASM - Table Driven Assembler Version 2.7                    Page 3

      EXPORT                                                       22
      IFDEF                                                        22
      IFNDEF                                                       23
      IF                                                           23
      INCLUDE                                                      23
      LIST/NOLIST                                                  23
      LSFIRST/MSFIRST                                              24
      ORG                                                          24
      PAGE/NOPAGE                                                  24
      SET                                                          25
      SYM/AVSYM                                                    25
      TEXT                                                         26
      TITLE                                                        26
      WORD                                                         27
    OBJECT FILE FORMATS                                            28
      Intel Hex Object Format                                      28
      MOS Technology Hex Object Format                             29
      Binary Object Format                                         29
    LISTING FILE FORMAT                                            30
    PROM PROGRAMMING                                               31
    ERROR MESSAGES                                                 33
    BUGS AND LIMITATIONS                                           35
    6502 INSTRUCTIONS AND ADDRESSING MODES                         36
    8048 INSTRUCTIONS AND ADDRESSING MODES                         39
    8051 INSTRUCTIONS AND ADDRESSING MODES                         44
    8085 INSTRUCTIONS AND ADDRESSING MODES                         49
    Z80 INSTRUCTIONS AND ADDRESSING MODES                          52
    6805 INSTRUCTIONS AND ADDRESSING MODES                         58
    TMS32010 INSTRUCTIONS AND ADDRESSING MODES                     64
    TASM DISTRIBUTION FILES                                        71
    BUILDING TASM FROM THE SOURCE CODE                             72
    TASM INSTRUCTION SET TABLE DEFINITION                          73

    APPENDIX A - SAMPLE LISTING FILE                               78
    APPENDIX B - SAMPLE INSTRUCTION DEFINITION TABLE (TASM65.TAB)  80
    APPENDIX C - ORDERING INFORMATION                              85


    TASM - Table Driven Assembler Version 2.7                    Page 4


    INTRODUCTION

    TASM  is a table driven cross assembler for the MS-DOS  environment.
    Currently,  tables for the 6502,  8048, 8051, 8080/8085, Z80,  6805,
    and TMS32010  microprocessors are supported by  STI, but the user so
    inclined  may  build  tables for other 8 bit  microprocessors   (see
    sections on TASM DISTRIBUTION FILES  and  TASM INSTRUCTION SET TABLE
    DEFINITION for notes on reconfiguring TASM for  other processors).

    TASM characteristics include:

            1.  Powerful expression parsing (17 operators).
            2.  Supports a subset of the 'C' preprocessor commands.
            3.  Macro capability (through use of DEFINE directive).
            4.  Multiple statements per line.
            5.  Supports three object file formats (Intel Hex, MOS
                    Technology Hex, and binary).
            6.  Absolute code generation only.
            7.  Source code available (in C).
            8.  Uniform syntax  across  versions  for  different  target
                    machines.
            9.  Features in support  of  PROM  programming  (preset  all
                    bytes  to  specified value,  output object code in a
                    contiguous block).
            10. Supports  extended  instructions of the Rockwell R65C02.
            11. Tables  can  be   generated  for  other  microprocessors
                    without having to modify the TASM executable module.
            12. Capability to export symbols into a file  with a  format
                    suitable for including  in  a  subsequent  assembly.
            13. Capability to generate  a  symbol  table file compatible
                    with the Avocet 8051 simulator.

    SHAREWARE

    TASM  is distributed as shareware.   TASM is not public domain.  The
    TASM  distribution files may be freely copied (excluding the  source
    code  files)  and  freely used for the purpose  of  evaluating   the
    suitability  of  TASM for a given purpose.   Use of  TASM  beyond  a
    reasonable evaluation period requires registration.   Prolonged  use
    without registration is unethical.




    TASM - Table Driven Assembler Version 2.7                    Page 5


    INVOCATION

    TASM can be invoked as  follows  (optional fields shown in brackets,
    symbolic fields enclosed in <>):

        tasm -<pn> [-<option_flag>] <src_file> [<obj_file> [<lst_file>
                                   [<exp_file> [<sym_file>]]]]

        Where  <option_flag> can be one or more of the following:

            -<pn>           Specify version (<pn> = part number)
            -t<table>       Table (alternate form of above)
            -c              Object file written as a contiguous block
            -e              Show source lines after macro expansion
            -f<xx>          Fill entire memory space with <xx> (hex)
            -h              Produce hex table of the assembled code
            -l              Produce a label table in the listing
            -m              Produce object in MOS Technology format
            -b              Produce object in binary (.COM) format
            -p              Page the listing file
            -q              Quite, disable the listing file
            -r<kb>          Set read buffer size in Kbytes
            -s              Write a symbol table file
            -x[<m>]         Enable extended instruction set (if any)
            -d<macro>       Define a macro (or just a macro label)
            -o<bb>          Bytes per object record (hex)

    The file parameters are defined as follows:

    <src_file>      Source file name
    <obj_file>      Object code file name
    <lst_file>      Listing file name
    <exp_file>      Export file name (generated only if the EXPORT
                        directive is used).
    <sym_file>      Symbol table file (generated only if the "-s" option
                        is invoked or the SYM/AVSYM directives are used.

    The  source file must be specified.  If not,  some usage information
    is  displayed.   Default  file names for all  the  other  files  are
    generated  if  they are not explicitly provided.   The  filename  is
    formed by taking the source filename and changing the extension   to
    one of the following:


    TASM - Table Driven Assembler Version 2.7                    Page 6


    File Type               Extension
    ------------------------------------------
    Object                  .OBJ
    Listing                 .LST
    Export                  .EXP
    Symbol table            .SYM

    TASM  has  no  built-in instruction set  tables.    Instruction  set
    definition files are read at run time.   TASM determines which table
    to use based on the '-<pn>'  field shown above.   For example,   to
    assemble the code in  a file called 'source.asm' one would enter:

            tasm -48  source.asm            for an 8048 assembly
            tasm -65  source.asm            for a  6502 assembly
            tasm -51  source.asm            for an 8051 assembly.
            tasm -85  source.asm            for an 8085 assembly.
            tasm -80  source.asm            for a  Z80  assembly.
            tasm -05  source.asm            for a  6805 assembly.
            tasm -32  source.asm            for a  TMS32010 assembly.

    The file name that the tables are read from is formed by taking  the
    digits  specified  after  the  '-'  and  appending it to 'TASM' then
    appending the '.TAB' extension.  Thus,  the '-48' flag  would  cause
    the  tables  to  be  read from the file 'TASM48.TAB' (See section on
    TASM INSTRUCTION SET DEFINITION).

    It  is  possible to designate tables by non numeric part numbers  if
    the '-t' flag is used.  For example,  if a user built a table called
    TASMF8.TAB then TASM could be invoked as follows:

            tasm -tf8 source.asm


    Each option flag must be  preceded  by  a  dash.  Options  need  not
    precede  the file names, however.  The various options are described
    below:

    b  -  Binary Object Format. This option causes the object file to be
    written in binary - one byte for each byte of code/data.  Note  that
    no  address  information  is  included  in  the  object file in this
    format.  The contiguous block (-c) output mode is forced  when  this
    option is invoked.

    c - Contiguous Block Output. If this option is specified,  then  all
    bytes  in the range from the lowest used byte to the highest will be
    defined in the object file.  Normally,  with the default  Intel  Hex


    TASM - Table Driven Assembler Version 2.7                    Page 7

    object  format  enabled,  if  the Program Counter (PC) jumps forward
    because of an .ORG directive,  the bytes skipped over will not  have
    any  value  assigned  them  in  the  object  file.  With this option
    enabled,  no output to the object file occurs until the end  of  the
    assembly  at  which time the whole block is written.  This is useful
    when using TASM to generate code that will be put  into  a  PROM  so
    that  all  locations  will have a known value.  This option is often
    used in conjunction with the -f option to ensure  all  unused  bytes
    will have a known value.

    d - Define a Macro. Macros  are  be  defined  on  the  command  line
    generally to control the assembly of various IFDEF's that are in the
    source  file.  This is a convenient way to generate various versions
    of object code from a single source file.

    e  -  Expand Source.   Normally TASM shows lines in the listing file
    just  as  they are in the source file.   If the DEFINE directive  is
    used,  however,  it is sometimes desirable to see the source  lines
    after expansion.  Use the '-e' flag to accomplish this.

    f  -  Fill  Memory.  This  option  causes the memory image that TASM
    maintains to be initialized to the value specified by  the  two  hex
    characters  immediately  following the 'f'.  TASM maintains a memory
    image that is a full 64K bytes in size (even if the target processor
    cannot  utilize  that  memory  space).  Invocation  of  this  option
    introduces a 2 second delay at start up (time required to initialize
    all 64K bytes).   See Appendix A for an example.

    h - Hex Table. This option causes a hex table of the produced object
    code to appear in the listing file.  Each line of  the  table  shows
    sixteen bytes of code.  The format is shown in the sample listing in
    Appendix A.

    l - Label Table. This option causes a label table to appear  in  the
    listing  file.  Each  label is  shown  with its corresponding value.
    Macro labels (as established  via  the  DEFINE  directives)  do  not
    appear.  The format is shown in the sample listing in Appendix A.

    m - MOS Technology Object Format. This option causes the object file
    to be written in MOS Technology hex format rather than  the  default
    Intel  hex  format.  See  section  on  OBJECT  FILE  FORMATS  for  a
    description of the format.

    o - Set Number of Bytes per Object Record.  When  generating  object
    code in either the MOS Technology format or the Intel hex format,  a
    default of 24 (decimal) bytes of object are defined on each  record.
    This can be altered by invoking the '-o' option immediately followed


    TASM - Table Driven Assembler Version 2.7                    Page 8

    by  two  hex digits defining the number of bytes per record desired.
    For example,  if 32 bytes per record are desired,  one might  invoke
    TASM as:

            TASM -48 -o20 source.asm

    p - Page Listing File.  This option causes the listing file to  have
    top of page headers and form feeds inserted at appropriate intervals
    (every sixty lines of output).

    q - Disable Listing File.  This option  causes  all  output  to  the
    listing  file  to  be  suppressed,   unless  a  .LIST  directive  is
    encountered in the source file (see LIST/NOLIST directives).

    r  - Set Read Buffer Size.   This option overrides the default  read
    buffer  size of 2 Kbytes.   The first hexadecimal digit  immediately
    after the 'r'  is taken as the number of K bytes to allocate for the
    read  buffer  (.e.g.  '-r8'    indicates an 8  Kbyte  buffer,  '-rf'
    indicates a 15 Kbyte buffer).  Note that that read buffers are taken
    from  the  same memory  pool as labels and macro storage,  and  that
    additional  read buffers are needed if "includes"  are used.   Thus,
    using  8  Kbyte  buffers may be suitable for  most  assemblies,  but
    programs with large numbers  of symbols may not allow such a  value.
    Also,  reducing the buffer  size to 1 Kbyte can  increase the memory
    pool available for label storage, if such is needed.

    s - Enable Symbol File Generation.   If this flag is set,  a  symbol
    file  is  generated at the end of the assembly.   The format of  the
    file  is one line per label,  each label starts in the first  column
    and  is  followed  by white space and then four  hexadecimal  digits
    representing the value of the label.   The following illustrates the
    format:

            label1          FFFE
            label2          FFFF
            label3          1000

    The symbol file name can be provided as the fifth  file name on  the
    the  command line,  or the name will be generated from   the  source
    file name with a '.SYM'  extension.   The symbol table file can also
    be  generated  by invoking the SYM directive.   The AVSYM  directive
    also  generates  the  symbol file but in  a  different  format  (see
    section on ASSEMBLER DIRECTIVES).

    t  - Table Name.    As an alternative to specifying the table to use
    (in the case it starts with a non-numeric).   Thus a table for an F8
    might be selected as:


    TASM - Table Driven Assembler Version 2.7                    Page 9


            TASM -tf8 source.asm

    x - Enable Extended Instruction  Set.  If  a  processor  family  has
    instructions  that  are valid for only certain members,  this option
    can be used to enable those beyond the  basic  standard  instruction
    set.  Presently,  this  option  only  has  significance for the 6502
    and  8048  versions of TASM.   The  6502  version  (TASM  -65 )  has
    extended instructions for the  Rockwell R65C02  and  the  R65C00/21.
    The 8048  version (TASM -48) has extended instructions for the 8041,
    8022,  and 8021. A   hex  digit  may  follow  the 'x'  to indicate a
    mask value used in selecting the appropriate  instruction set.   Bit
    0   of the  mask selects  the  basic instruction set,   thus a '-x1'
    would have no effect.   A  '-x3'  would   enable  the basic set plus
    whatever instructions have bit 1 set in their  class  mask.  A  '-x'
    without  a  digit  following is equivalent to a '-xf' which sets all
    four of the  mask  bits.  (See  section  on  6502  INSTRUCTIONS  AND
    ADDRESSING MODES for details on its extended instructions).



    TASM - Table Driven Assembler Version 2.7                    Page 10


    ENVIRONMENT VARIABLES

    The  TASM  environment  can be customized by  using  the  enviroment
    variables listed below:

    TASMTABS.   This variable specifies the path to be searched for TASM
    instruction  set definition tables.   If it is not defined then  the
    table(s)  must exist in the current working directory.    If it  was
    desired  to put the instruction set definition tables in a directory
    called 'TASM' on a drive called 'C:',  the following statement would
    be appropriate in the AUTOEXEC.BAT file:

            set TASMTABS=C:\TASM

    TASMOPTS.    This variable specifies TASM command line options  that
    are to be invoked every time TASM is executed.  For example, if TASM
    is  being used for 8048  assemblies with binary object  file  output
    desired,   the  following  statement would  be  appropriate  in  the
    AUTOEXEC.BAT file:

            set TASMOPTS=-80 -b




    TASM - Table Driven Assembler Version 2.7                    Page 11


    SOURCE FILE FORMAT
    Statements in the source file must conform to a  format  as  follows
    (except  for assembler directive statements which are described in a
    subsequent section):

            <label>  <operation>    <operand>       <comment>

    All of the fields are optional, under appropriate circumstances.  An
    arbitrary amount of white space (space and tabs) can  separate  each
    field  (as  long as the maximum line length of 255 characters is not
    exceeded).  Each of fields are described below:


    Label Field. If the first character of the line is alphabetic, it is
    assumed  to  be  the  start  of  a label.  Subsequent characters are
    accepted as part of that  label  until  a  space,  tab,  or  ':'  is
    encountered.   The   assembler   assigns   a   value  to  the  label
    corresponding to the current  location  counter.  Labels  can  be  a
    maximum  of  13 characters long.  Labels can contain upper and lower
    case letters, digits, underscores,  and periods (the first character
    must  be alphabetic).  Labels are case sensitive - the label 'START'
    is a different label from 'start'.

    Operation  Field.  The  operation  field  contains  an   instruction
    (opcode)  mnemonic  which  specifies the action to be carried out by
    the  target  processor  when  this  instruction  is  executed.   The
    interpretation  of each mnemonic is dependent on the version of TASM
    being used (see  section  on  OPCODES  AND  ADDRESSING  MODES).  The
    operation  field  may  begin  in  any  column except the first.  The
    operation field is case insensitive.

    Operand Field. The operand field specifies the data to  be  operated
    on  by  the  instruction.  It may include expressions and/or special
    symbols describing the  addressing  mode  to  be  used.  The  actual
    format and interpretation is dependent on the target processor.  For
    a description of the format for currently supported processors,  see
    the section on OPCODES AND ADDRESSING MODES  for  the  processor  of
    interest.

    Comment  Field.  The  comment  field always begins with a semicolon.
    The rest of the line from the semicolon to the end of  the  line  is
    ignored  by  TASM,  but passed on to the listing file for annotation
    purposes.  The comment field must be the last field on a  line,  but
    it may be the only field, starting in column one, if desired.




    TASM - Table Driven Assembler Version 2.7                    Page 12


    Multiple  Statement Lines. If the backslash character is encountered
    on a source line,  it is treated as a newline.  The remainder of the
    line  following  the  backslash  will be processed as an independent
    line of source code.  This allows one to put multiple statements  on
    a line.  This facility is not so useful of itself,  but when coupled
    with the capability  of  the  DEFINE  directive,  powerful  multiple
    statement  macros  can  be  constructed  (see  section  on ASSEMBLER
    DIRECTIVES).  Note that when  using  the  statement  separator,  the
    character  immediately  following  it should be considered the first
    character of a new line,  and thus must either be a start of a label
    or  white space (not an instruction).  As the examples show, a space
    is put between the backslash and the start of the next instruction.




    Some  examples  of  valid  source  statements follow (6502 mnemonics
    shown):

    label1  lda     byte1   ;get the first byte
            dec     byte1
            jne     label1

    ;
    label2
            sta     byte2,X
            ; a multiple statement line follows
            lda     byte1\ sta byte1+4\ lda byte2\ sta byte2+4




    TASM - Table Driven Assembler Version 2.7                    Page 13


    EXPRESSIONS

    Expressions are made  up  of  various  syntactic  elements  (tokens)
    combined  according  to  a set of syntactical rules.  The tokens are
    summarized as follows:

            1.  Labels
            2.  Constants
            3.  Location Counter Symbol
            4.  Operators
            5.  Parenthesis

    Labels. Labels are strings of characters that have a  numeric  value
    associated with them, generally representing an address.  Labels can
    contain  upper  and  lower case letters,  digits,  underscores,  and
    periods.  The first character must be a letter  (to  distinguish  it
    from a numeric constant).  The value of a label is limited to 16 bit
    precision.  Labels can contain up to 13 characters, all of which are
    significant (none are ignored when looking at a label's value, as in
    some assemblers).

    Constants.  Numeric constants must always begin with a decimal digit
    (thus hexadecimal  constants  that  start  with  a  letter  must  be
    prefixed by a '0').  The radix is determined by a letter immediately
    following the digit string according to the following table:

            Radix           Suffix                  Prefix
            ---------------------------------------------------
            2               B or b                    %
            8               O or o                    @
            10              D or d (or nothing)
            16              H or h                    $

    Decimal is the default radix, so decimal constants need no suffix or
    prefix.

    The following representations are equivalent:

            1234H           or      $1234
            100d            or      100
            177400O         or      @177400
            01011000b       or      %01011000

    The  prefixes  are provided for compatibility with some other source
    code formats but introduce a problem of ambiguity.  Both '%' and '$'
    have alternate uses  ('%'  for  modulo,  '$'  for  location  counter


    TASM - Table Driven Assembler Version 2.7                    Page 14

    symbol).  To  resolve this,  some simple rules are employed.  If the
    first character following a '%' is a '0' or '1', it is assumed to be
    a radix specifier and not the modulo  operator.  Similarly,  if  the
    first character following a '$' is a valid hexadecimal digit,  it is
    assumed to be a radix specifier and not the location  counter.  This
    can  cause problems,  however.  Suppose you wanted to find the value
    of the low byte of the label 'PNTR_TABLE', you might do this:

            (PNTR_TABLE%0100h)

    Here the '%' would mistakenly be taken for  a  radix  specifier.  To
    correct  the  problem one need only insert a space in an appropriate
    spot:

            (PNTR_TABLE % 0100h)

    Character  constants  are  single  characters  surrounded  by single
    quotes (following  quote  is  optional).  The  ASCII  value  of  the
    character  in the quotes is returned.  No escape provision exists to
    represent non-printable characters within the quotes,  but  this  is
    not  necessary  since  these  can  be  just as easily represented as
    numeric  constants  (or  using  the  TEXT directive which does allow
    escapes).

    String constants are one or more  characters  surrounded  by  double
    quotes.  Note  that string constants are not allowed in expressions.
    They are only allowable following the 'TITLE' and  'TEXT'  assembler
    directives.

    Location  Counter  Symbol. The current value of the location counter
    (PC) can be used in expressions by placing  a  '$'  in  the  desired
    place.  The  Location Counter Symbol is allowable anywhere a numeric
    constant is.  (Note that if the '$' is followed by a  decimal  digit
    then  it  is  taken to be the hexadecimal radix indicator instead of
    the Location Counter symbol,  as mentioned above).  The '*' may also
    be  used  to  represent the location counter,  but is less preferred
    because of its ambiguity with the multiplicative operator.


    TASM - Table Driven Assembler Version 2.7                    Page 15


    Operators. Expressions can optionally contain operators  to  perform
    some   alterations   or  calculations  on  particular  values.   The
    operators are summarized as follows:

            Operator  Type          Description
            __________________________________________
            +        Additive       addition
            -                       subtraction

            *        Multiplicative multiplication
            /                       division
            %                       modulo
            <<                      logical shift left
            >>                      logical shift right

            ~        Unary          bit inversion (one's complement)
            -                       unary negation

            =        Relational     equal
            ==                      equal
            !=                      not equal
            <                       less than
            >                       greater than
            <=                      less than or equal
            >=                      greater than or equal

            &       Binary          binary 'and'
            |                       binary 'or'
            ^                       binary 'exclusive or'

    The syntax is much the same as in 'C' with the following notes:

            1.  No operator precedence is in effect.  Evaluation is from
                    left to right unless grouped by  parenthesis  (  see
                    example below).

            2.  All evaluations are done with 32 bit signed precision.

            3.  Both '=' and '==' are allowable equality checkers.  This
                    is allowed   since   the  syntax  does  not  provide
                    assignment capability (as '=' would normally imply).

    The relational operators return a value of 1 if the relation is true
    and 0 if it is false.  Thirtytwo bit signed arithmetic is used.

    It is always a good idea to explicitly indicate the desired order of


    TASM - Table Driven Assembler Version 2.7                    Page 16

    evaluation with  parenthesis,  especially  to  maintain  portability
    since  TASM does not evaluate expressions in the same manner as many
    other assemblers.  To understand how it does arrive  at  the  values
    for expressions, consider the following example:

            1 + 2*3 + 4

    TASM would start at the left and read the first token '1'  and  then
    the  operator  '+'.  To  determine  what  to  add  to  the '1',  the
    expression evaluator would be called recursively on the remainder of
    the expression.  The next pass would read the '2' and '*'  and  then
    call  itself again to evaluate the rest.  Another level of recursion
    would take place in evaluating the '4'.  Since it is not followed by
    any more operators, the recursion would start undoing itself and the
    final expression would be evaluated as:

            1 + (2 * (3 + (4))) = 15

    If  the user had desired the '*'  to take precedence,  the following
    could have been done:

            1 + (2*3) + 4

    Use parenthesis liberally.

    Here are some examples of valid expressions:

            (0f800H + tab)
            (label_2 >> 8)
            (label_3 << 8) & $f000
            $ + 4
            010010000100100b + 'a'
            (base + ((label_4 >> 5) & (mask << 2))


    TASM - Table Driven Assembler Version 2.7                    Page 17


    ASSEMBLER DIRECTIVES

    Most of the assembler  directives  have  a  format  similar  to  the
    machine   instruction   format.   However,   instead  of  specifying
    operations for the processor to carry out,  the directives cause the
    assembler  to perform some function related to the assembly process.
    TASM has two types of assembler directives - those  that  mimic  the
    'C'  preprocessor  functions,  and  those  that  resemble  the  more
    traditional assembler directive functions.  Each of  these  will  be
    discussed.

    The  'C' preprocessor style directives are invoked with a '#' as the
    first   character   of   the  line  followed  by   the   appropriate
    directive  (just  as in 'C').  Thus,  these directives cannot have a
    label preceding  them (on the same line).  Note that in the examples
    directives are shown in upper case,  however,  either upper or lower
    case is acceptable.

    ADDINSTR.  This  directive  can  be  used   to   define   additional
    instructions for TASM to use in this assembly.  The format is:

    [<label>]  .ADDINSTR <inst> <args> <opcode> <nbytes> <modop> <class>
                                                         <shift> <binor>

    The fields are separated by white space just as they would appear in
    an instruction definition file as described in  TASM INSTRUCTION SET
    TABLE DEFINITION.

    AVSYM.  See SYM/AVSYM.

    BLOCK. This directive causes the Instruction Pointer to advance  the
    specified  number  of  bytes without assigning values to the skipped
    over locations.  The format is:

            [<label>] .BLOCK        <expr>

    Some valid examples are:

            word1   .BLOCK  2
            byte1   .block  1
            buffer  .block  80

    BSEG/CSEG/DSEG/NSEG/XSEG.   These  directives  can  be  invoked  to
    indicate  the  appropriate  address space for   symbols  and  labels
    defined in the subsequent code.   The invocation of these directives
    in no way affects the code generated, only provides more information


    TASM - Table Driven Assembler Version 2.7                    Page 18

    in  the  symbol  table  file if the  AVSYM  directive  is  employed.
    Segment  control directives such as these are generally supported by
    assemblers  that  generate relocatable object code.   TASM does  not
    generate relocatable object code and does not support a link  phase,
    so  these  directives have no direct effect on the resulting  object
    code. The segments are defined as follows:

            Directive       Segment Description
            ----------------------------------------------------
            BSEG            Bit  address
            CSEG            Code address
            DSEG            Data address (internal RAM)
            NSEG            Number or constant (EQU)
            XSEG            External data address (external RAM)


    BYTE.  This directive allows a value assignment to the byte pointed
    to by the current Instruction Pointer.  The format is:

            [<label>] .BYTE   <expr>

    Only  the lower eight bits of <expr>  are used.   Multiple bytes may
    be assigned by separating them with commas. Here are some examples:

            label1  .BYTE   10010110B
                    .byte   'a'
                    .byte   0
                    .byte   100010110b,'a',0

    CODES/NOCODES.   These directives can be used to alternately turn on
    or off the generation of formatted listing output with line numbers,
    opcodes,  data, etc.   With NOCODES in effect,  the source lines are
    sent to the listing file untouched.  This is useful around blocks of
    comments that need a full 80 columns of width for clarity.

    DB.  This is alternate form of the BYTE directive.

    DW.  This is alternate form of the WORD directive.

    DEFINE.  The  DEFINE  directive  is  one of the most powerful of the
    directives and allows string substitution  with  optional  arguments
    (macros).  The format is as follows:

            #DEFINE  <macro_label>[(<arg_list>)]  [<macro_definition>]

            <macro_label> := character string to be expanded when found
                                    in the source file.


    TASM - Table Driven Assembler Version 2.7                    Page 19


            <arg_list>    := optional argument list for variable
                                    substitution in macro expansion.

            <macro_def>   := character string to replace the occurrences
                                    of <macro_label> in the source file.



    The simplest form of the DEFINE directive might look like this:

            #DEFINE         MLABEL

    Notice  that no substitutionary string is specified.  The purpose of
    a statement like this would typically be to define a label  for  the
    purpose  of  controlling some subsequent conditional assembly (IFDEF
    or IFNDEF).

    A more complicated example,  performing simple  substitution,  might
    look like this:

            #DEFINE         VAR1_LO         (VAR1 & 255)

    This statement would cause all occurrences of the  string  'VAR1_LO'
    in the source to be substituted with '(VAR1 & 255)'.

    As  a  more  complicated  example,   using  the  argument  expansion
    capability, consider this:

            #DEFINE         ADD(xx,yy)      clc\ lda xx\ adc yy\ sta xx

    If the source file then contained a line like this:

            ADD(VARX,VARY)

    It would be expanded to:

            clc\ lda VARX\ adc VARY\ sta VARX

    The above example shows the use of the backslash ('\') character  as
    a  multiple  instruction  statement delimiter.  This approach allows
    the definition of fairly powerful,  multiple statement  macros.  The
    example shown generates 6502 instructions to add one memory location
    to another.

    Some rules associated with the argument list:



    TASM - Table Driven Assembler Version 2.7                    Page 20

            1.  Use a maximum of 10 arguments.

            2.  An argument in the DEFINE statement  must  be  a  unique
                    string  (unique  on  that line) occurring only as an
                    argument  elsewhere  in  the  line.   TASM  does   a
                    straight  forward  search  for the occurrence of the
                    specified argument strings in  the  macro_definition
                    field  and  if  the  string  is  found somewhere not
                    intended,  bad things  will  happen.  In  the  above
                    example,  if  a  simple '(a,b)' had been used as the
                    argument list instead '(xx,yy)',  then each  'a'  in
                    the  definition  would be expanded (e.g.  the 'a' in
                    'lda').

            3.  Each argument should be a maximum of 15 characters.

    Note that macros can be defined on the TASM command line, also, with
    the '-d' option flag.

    DEFCONT.   This  directive  can be used to add to  the  last  macro
    started with a DEFINE directive.   This provides a convenient way to
    define long macros without running off the edge of the page. The ADD
    macro shown above could be defined as follows:

            #DEFINE         ADD(xx,yy)      clc
            #DEFCONT                      \ lda xx
            #DEFCONT                      \ adc yy
            #DEFCONT                      \ sta xx

    EJECT.  This  directive  can  be used to force a Top of Form and the
    generation of a page header on the list file.  It has no  effect  if
    the paging mode is off (see PAGE/NOPAGE).  The format is:

            .EJECT

    ELSE. This directive can optionally be used with IFDEF,  IFNDEF  and
    IF  to  delineate  an alternate block of code to be assembled if the
    block  immediately  following  the  IFDEF,   IFNDEF  or  IF  is  not
    assembled.



    TASM - Table Driven Assembler Version 2.7                    Page 21

    Here are some examples of the use of IFDEF, IFNDEF,  IF,  ELSE,  and
    ENDIF:

            #IFDEF  label1
            lda     byte1
            sta     byte2
            #ENDIF


            #ifdef  label1
            lda     byte1
            #else
            lda     byte2
            #endif

            #ifndef label1
            lda     byte2
            #else
            lda     byte1
            #endif

            #if ($ >= 1000h)
            ; generate an invalid statement to cause an error
            ;  when we go over the 4K boundary.
             !!! PROM bounds exceeded.
            #endif

    END.   This   directive   should  follow  all  code/data  generating
    statements in the source file.  It forces  the  last  record  to  be
    written to the object file.  The format is:

            [<label>]       .END

    ENDIF. This directive must always follow an  IFDEF,  IFNDEF,  or  IF
    directive and signifies the end of the conditional block.

    EQU. This directive can be used to  assign  values  to  labels.  The
    labels  can  then  be  used  in  expressions in place of the literal
    constant.  The format is:

            <label> .EQU  <expr>

    Here is an example:



    TASM - Table Driven Assembler Version 2.7                    Page 22

            MASK    .EQU    F0H
            ;
                    lda     IN_BYTE
                    and     MASK
                    sta     OUT_BYTE

    An  alternate  form  of  'EQU'  is  '='.  The  previous  example  is
    equivalent to:

            MASK    =       F0H
    or
            MASK    =FOH
            MASK    =$FO

    White  space must exist after the label,  but none is required after
    the '='.

    EXPORT.  This directive can be used to define symbols that are to be
    written  to  the export file.   The symbols are written  as  equates
    (using  the  .EQU  directive)  so that the  resulting  file  can  be
    included in a subsequent assembly.   This feature can help  overcome
    some  of  the deficiencies of TASM due to its lack of  a  relocating
    linker. The format is:

    [<label>]  .EXPORT      <symbol>

    The following example illustrates the use of the EXPORT directive and
    the format of the resulting export file:

    Source file:

            .EXPORT         read_byte
            .EXPORT         write_byte
            .EXPORT         open_file

    Resulting export file:

    read_byte       .EQU    $1243
    write_byte      .EQU    $12AF
    open_file       .EQU    $1301

    IFDEF.  This directive can be used to optionally assemble a block of
    code.  It has the following form:

            #IFDEF  <macro_label>

    When invoked,  the list of  macro  labels  (established  via  DEFINE


    TASM - Table Driven Assembler Version 2.7                    Page 23

    directives) is searched.  If the label is found, the following lines
    of  code  are  assembled.  If  not found,  the input file is skipped
    until an ENDIF or ELSE directive is found.

    Lines that are skipped over still appear in the listing file,  but a
    '~'  will appear immediately after the current PC and no object code
    will be generated (this is applicable to IFDEF, IFNDEF, and IF).

    IFNDEF. This directive is the opposite of the IFDEF  directive.  The
    block   of  code  following  is  assembled  only  if  the  specified
    macro_label is undefined.  It has the following form:

            #IFNDEF  <macro_label>

    When invoked,  the list of  macro  labels  (established  via  DEFINE
    directives)  is searched.  If the label is not found,  the following
    lines of code are assembled.  If it is  found,  the  input  file  is
    skipped until an ENDIF or ELSE directive is found.

    IF.  This  directive  can  be used to optionally assemble a block of
    code dependent on the value of a given expression.  The format is as
    follows:

            #IF     <expr>

    If the expression <expr> evaluates to non-zero, the following block
    of code is assembled (until an ENDIF or ELSE is encountered).

    INCLUDE. The INCLUDE directive reads in and assembles the  indicated
    source  file.  INCLUDEs can be nested up to six levels.  This allows
    a convenient means to  keep  common  definitions,  declarations,  or
    subroutines  in  files  to  be included as needed.  The format is as
    follows:

            #INCLUDE        <filename>

    The  <filename>  must  be  enclosed in double quotes.  Here are some
    examples:

            #INCLUDE        "macros.h"
            #include "equates"
            #include "subs.asm"

    LIST/NOLIST.  These directives can be used to alternately turn the
    output to the list file on (LIST) or off (NOLIST).  The format is:


    TASM - Table Driven Assembler Version 2.7                    Page 24


            .LIST
            .NOLIST

    LSFIRST/MSFIRST.   These directives determine the byte order rule to
    be employed for the WORD directive.  The default (whether correct or
    not)   for  all  TASM versions is the least significant  byte  first
    (LSFIRST).  The following illustrates its effect:

            0000  34 12     .word $1234
            0002            .msfirst
            0002  12 34     .word $1234
            0004            .lsfirst
            0004  34 12     .word $1234

    ORG. This directive  provides  the  means  to  set  the  Instruction
    Pointer  (a.k.a.  Program Counter) to the desired value.  The format
    is:

            [<label>] .ORG    <expr>

    The <label> is optional.  The Instruction pointer  is  assigned  the
    value  of  the  expression,  <expr>.  For example,  to generate code
    starting at address 1000H, the following could be done:

            start   .ORG    1000H

    The expression  (<expr>)  may  contain  references  to  the  current
    Instruction Pointer, thus allowing various manipulations to be done.
    For  example,  to align the Instruction Pointer on the next 256 byte
    boundary, the following could be done:

                    .ORG  (($ + FFH) & FF00H)

    ORG can also be used to reserve space without assigning values:

                    .ORG    $+8

    An alternate form of ORG is '*=' or '$='.  Thus  the  following  two
    examples as exactly equivalent to the previous example:

                    *=*+8
                    $=$+8

    PAGE/NOPAGE. These directives can be used to  alternately  turn  the
    paging mode on (PAGE) or off (NOPAGE).  If paging is in effect, then
    every  sixty  lines  of  output  will  be  followed by a Top of Form


    TASM - Table Driven Assembler Version 2.7                    Page 25

    character and a two line header containing  page  number,  filename,
    and the title.  The format is:

            .PAGE
            .NOPAGE

    SET.   This directive allows the value of an existing label  to  be
    changed.  The format is:

            <label>   .SET    <expr>

    The  use  of the SET directive should be avoided since changing  the
    value of a label can sometimes cause phase errors between pass 1 and
    pass 2 of the assembly.

    SYM/AVSYM.    These  directives can be used to cause a symbol  table
    file to be generated.  The format is:

            .SYM    ["<symbol_filename>"]
            .AVSYM  ["<symbol_filename>"]

    For example:

            .SYM    "symbol.map"
            .SYM
            .AVSYM  "prog.sym"
            .AVSYM

    The two directives are similar,  but result in a different format of
    the  symbol table file.   The format of  the   SYM file  is one line
    per  symbol,   each  symbol  starts in the first   column   and   is
    followed   by  white  space  and  then  four   hexadecimal    digits
    representing  the  value of the symbol.    The following illustrates
    the format:

            label1          FFFE
            label2          FFFF
            label3          1000

    The AVSYM is provided to generate symbol tables compatible with  the
    Avocet  8051  simulator.   The format is similar,  but each line  is
    prefixed  by an 'AS'  and each symbol value is prefixed by a segment
    indicator:



    TASM - Table Driven Assembler Version 2.7                    Page 26

            AS      start           C:1000
            AS      read_byte       C:1243
            AS      write_byte      C:1280
            AS      low_nib_mask    N:000F
            AS      buffer          X:0080

    The  segment  prefixes  are determined by the  most  recent  segment
    directive invoked (see BSEG/CSEG/DSEG/NSEG/XSEG directives).

    TEXT.  This  directive  allows  an ASCII string to be used to assign
    values  to  a  sequence  of  locations  starting  at   the   current
    Instruction Pointer.  The format is:

            [<label>] .TEXT   "<string>"

    The  ASCII value of each character in <string> is taken and assigned
    to  the  next  sequential  location.   Some  escape  sequences   are
    supported as follows:

            Escape
            Sequence        Description
            ------------------------------
            \n              Line Feed
            \r              Carriage return
            \b              Backspace
            \t              Tab
            \f              Formfeed
            \\              Backslash
            \"              Quote
            \000            Octal value of character

    Here are some examples:

            message1  .TEXT  "Disk I/O error"
            message2  .text  "Enter file name "
                      .text  "abcdefg\n\r"
                      .text  "I said \"NO\""

    TASM  only  shows  the first six  bytes of the string in the listing
    file, but all bytes are included in the object file.

    TITLE. This directive allows the user to define a title string  that
    appears  at the top of each page of the list file (assuming the PAGE
    mode is on).  The format is:

                    .TITLE  "<string>"



    TASM - Table Driven Assembler Version 2.7                    Page 27

    The string should not exceed 80 characters.  Here are some examples:

                    .TITLE  "Controller version 1.1"
                    .title  "This is the title of the assembly"
                    .title  ""


    WORD. This directive allows a value assignment to the next two bytes
    pointed to by the current Instruction Pointer.  The format is:

            [<label>] .WORD  <expr>

    The  least  significant  byte  of  <expr>  is  put  at  the  current
    Instruction  Pointer  with  the  most  significant  byte at the next
    sequential location (unless the MSFIRST directive has been invoked.
    Here are some examples:

            data_table      .WORD   (data_table + 1)
                            .word   $1234
                            .Word   (('x' - 'a')  << 2)
                            .Word   12,55,32


    END.   This   directive   should  follow  all  code/data  generating
    statements in the source file.  It forces  the  last  record  to  be
    written to the object file.  The format is:

            [<label>]       .END




    TASM - Table Driven Assembler Version 2.7                    Page 28


    OBJECT FILE FORMATS

    TASM supports three object file formats:

            1.  Intel Hex (default).
            2.  MOS Technology Hex.
            3.  Binary

    Each are described below:

    Intel Hex Object Format. This is the default format.  This format is
    line  oriented  and  uses only printable ASCII characters except for
    the carriage return/line feed at the end of each line.  Each line in
    the file assumes the following format:

    :NNAAAARRHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHCCTT

    Where:

    All fields marked 'hex' consist of two  or  four  ASCII  hexadecimal
    digits  (0-9,  A-F).  A maximum of 24 data bytes will be represented
    on each line.

    :       = Record Start Character
    NN      = Byte Count (hex)
    AAAA    = Address of first byte (hex)
    RR      = Record Type (hex, 00 except for last record which is 01)
    HH      = Data Bytes (hex)
    CC      = Check Sum (hex)
    TT      = Line Terminator (carriage return, line feed)

    The last line of the file will be a record conforming to  the  above
    format with a byte count of zero (':00000001FF').

    The checksum is defined as:

            sum      =  byte_count + address_hi + address_lo +
                            record_type + (sum of all data bytes)
            checksum =  ((-sum) & ffh)



    TASM - Table Driven Assembler Version 2.7                    Page 29


    MOS  Technology  Hex Object Format. This format is line oriented and
    uses  only  printable  ASCII  characters  except  for  the  carriage
    return/line  feed  at  the  end of each line.  Each line in the file
    assumes the following format:

    ;NNAAAAHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHHCCCCTT

    Where:

    All fields marked 'hex' consist of two  or  four  ASCII  hexadecimal
    digits  (0-9,  A-F).  A maximum of 24 data bytes will be represented
    on each line.

    ;       = Record Start Character
    NN      = Byte Count (hex)
    AAAA    = Address of first byte (hex)
    HH      = Data Bytes (hex)
    CCCC    = Check Sum (hex)
    TT      = Line Terminator (carriage return, line feed)

    The last line of the file will be a record with a byte count of zero
    (';00').

    The checksum is defined as:

            sum      =  byte_count + address_hi + address_lo +
                            record_type + (sum of all data bytes)
            checksum =  (sum & ffffh)




    Binary   Object   Format.   This  file  format  has  only  a  binary
    representation of each data byte with no address, checksum or format
    description,  whatsoever.  It is often a convenient format to use to
    pass  the  data to other programs on your PC (like a PROM programmer
    package) but because of the  non-printability and  lack  of  address
    information,  it  is  not  often  used to transmit the code to other
    systems.

    Note that when this object format is selected (-b  option),  the  -c
    option  is  forced.  This  is  done so that no ambiguity arises as a
    result of the lack of address information in the file.  Without  the
    -c  option,   discontinuous  blocks  of  object  code  would  appear
    contiguous.


    TASM - Table Driven Assembler Version 2.7                    Page 30


    LISTING FILE FORMAT

    Each line of source code generates one (or more) lines of output  in
    the listing file.  The fields of the output line are as follows:

            1.  Current  source  file  line  number  (4 decimal digits).

            2.  An optional '+' appears if this is  an  'INCLUDE'  file.
                    (One '+' for each level of INCLUDE invoked).

            3.  Current Instruction Pointer (4 hex digits).  An optional
                    '~' follows the Instruction Pointer if the  line  of
                    source  code  is  not  being assembled because of an
                    IFDEF, IFNDEF, or IF directive.

            4.  Resulting code/data generated from this source line (two
                    hex digits per byte, each byte separated by a space,
                    up to four bytes per line).

            5.  The  source  line  exactly  as  it appears in the source
                    file.

    If  paging  is  enabled (by either the '-p' option flag or the .PAGE
    directive) some additional fields will be inserted into the  listing
    file every 60 lines.  These fields are:

            1.  Top of Form (form feed).
            2.  Assembler identifier (e.g. "TASM 6502 Assembler").
            3.  Initial source file name.
            4.  Page number.
            5.  Title.

    For an example of the listing file format, see appendix A.



    TASM - Table Driven Assembler Version 2.7                    Page 31


    PROM PROGRAMMING

    A wide variety of PROM programming equipment is available  that  can
    use  object  code  in  one or more of the formats TASM supports.  We
    will not try to list all such  compatible  systems  here,  but  will
    mention one configuration that has worked well for us.

    We have used the Apparat "IBM PROM Blaster,  24 Pin" (available from
    Apparat Inc.,  4401 Tamarac Parkway,  Denver,  Colorado 80237, $129)
    for programming 24  pin  EPROMs  with  much  success.  The  software
    supplied  with  this  product  will accept a TASM object file in the
    binary  format  (-b  option  flag  on  TASM   command   line).   The
    combination   of  TASM  and  the  PROM  Blaster  make  for  a  truly
    inexpensive solution to the problem of generating  PROMed  code  for
    target microprocessor systems.  (STI is not affiliated or associated
    with Apparat in any way).


    Some additional notes about generating code to be put in PROMs:

            1.  It  is  often  desirable  to  have all bytes in the PROM
                    programmed even if not explicitly assigned  a  value
                    in the source code (e.g.  the bytes are skipped over
                    with a .ORG statement).  This can be accomplished by
                    using the -c (contiguous block) and  the  -f  (fill)
                    command  line option flags.  The -c will ensure that
                    every byte from the lowest byte assigned a value  to
                    the the highest byte assigned a value will be in the
                    object  file  with no gaps.  The -f flag will assign
                    the specified value to all bytes before the assembly
                    begins so that when the object file is written,  all
                    bytes  not  assigned a value in the source code will
                    have a known value.  As an  example,  the  following
                    command  line  will  generate  object  code  in  the
                    default Intel Hex format with all bytes not assigned
                    a value in the source set to EA (hex, 6502 NOP):

                    tasm -65 -c -fEA test.asm

            2.  To ensure that TASM generates object code to  cover  the
                    full  address  range of the target PROM,  put a .ORG
                    statement at the end of the source file set  to  the
                    last address desired.  For example, to generate code
                    to  be  put  in  a  2716  EPROM  (2 Kbytes) from hex
                    address $1000 to $17ff,  do something like  this  in
                    the source file:


    TASM - Table Driven Assembler Version 2.7                    Page 32


                             ;start of the file
                             .ORG    $1000
                             ;rest of the source code follows

                             <source code>

                             ;end of the source code
                             .ORG    $17ff
                             .BYTE   0
                             .END

                    Now,  to  invoke  TASM  to  generate the code in the
                    binary format with all unassigned bytes  set  to  00
                    (6502 BRK), do the following:

                    tasm -65 -b -f00 test.asm

                    Note that -b forces the -c option.


    TASM - Table Driven Assembler Version 2.7                    Page 33


    ERROR MESSAGES


    Error Message                           Description
    --------------------------------------------------------
    unrecognized directive..................A statement starting  with a
                                            '.'  or  '#'  has a mnemonic
                                            that is  not  defined  as  a
                                            directive.

    unrecognized  instruction...............A  statement  has  an opcode
                                            mnemonic   that    is    not
                                            defined.

    unrecognized argument...................A statement has  an  operand
                                            format that is not defined.

    label value misaligned..................The value of a label appears
                                            to have a different value on
                                            the  second pass then it was
                                            computed  to  have  on   the
                                            first    pass.    This    is
                                            generally due to  Zero  Page
                                            Addressing   mode   problems
                                            with  the  6502  version  of
                                            TASM.  Labels  that are used
                                            in operands  for  statements
                                            that   could  utilize   Zero
                                            Page addressing mode  should
                                            always   be  defined  before
                                            used as an operand.

    label table overflow....................To  many  labels  have  been
                                            encountered.

    No END directive before EOF.............The source file did not have
                                            an   END  directive  in  it.
                                            This is not fatal,  but  may
                                            cause  the  last object file
                                            record to be lost.

    No  files  specified....................TASM  was  invoked  with  no
                                            source file specified.


    TASM - Table Driven Assembler Version 2.7                    Page 34


    Unknown  option  flag...................TASM  was  invoked  with  an
                                            undefined option flag on the
                                            command line.

    Source file open error..................TASM was not  able  to  open
                                            the specified source file.

    List file open error....................TASM was not  able  to  open
                                            the specified list file.

    Object file open error..................TASM was not  able  to  open
                                            the specified object file.

    Unknown token...........................Unexpected  characters  were
                                            encountered while parsing an
                                            expression.

    maximum number of macros exceeded.......To  many  macros   (DEFINEs)
                                            have been encountered.

    macro buffer overflow...................The buffer from which  space
                                            is   allocated   for   macro
                                            definitions is exhausted.

    range of relative branch exceeded.......A branch instruction exceeds
                                            the  maximum   range   (6502
                                            Version).

    macro expansion too long................The  expansion  of  a  macro
                                            resulted  in  a  line  that
                                            exceeded the maximum length.


    TASM - Table Driven Assembler Version 2.7                    Page 35


    BUGS AND LIMITATIONS

    Limitations and Specifications
    ----------------------------------------------------------------
    Maximum number of labels                2000
    Maximum length of labels                13 characters
    Maximum address space                   64 Kbytes (65536 bytes)
    Maximum number of nested INCLUDES       4
    Maximum length of TITLE string          79 characters
    Maximum source line length              255 characters
    Maximum length after macro expansion    255 characters
    Maximum length of expressions           255 characters
    Maximum length of pathnames             79 characters
    Maximum length of command line          127 characters

    Maximum number of instructions          500
    Maximum number of macros                1000
    Maximum number of macro arguments       10
    Maximum length of macro argument        16 characters
    Heap size (for labels, macros, & buffers) 20000 bytes
    Memory requirements                     160K

    Bugs

    1.  The 8048 version of TASM does not check for use of memory beyond
            any  reasonable  bounds (e.g.  an 8048 has a maximum address
            space of 4 Kbytes but TASM will let  you  pretend  that  you
            have 64 Kbytes).

    2.  Expression evaluation has no operator precedence in effect which
            can  make  for  unexpected results if not explicitly grouped
            with parenthesis.

    3.  First  page  of  listing file will not show a user defined title
            (defined via TITLE directive).

    4.  TASM sometimes does not generate error messages  for  improperly
            formed expressions.

    5.  TASM expands macros in comments at the end of a line (but not in
            lines that are all comment).

    6.  TASM does not generate an error message when a EQU directive has
            an undefined label on the right hand side.


    TASM - Table Driven Assembler Version 2.7                    Page 36


    6502 INSTRUCTIONS AND ADDRESSING MODES

    The acceptable 6502 opcode mnemonics for TASM are as follows:

             ADC  AND  ASL  BCC  BCS  BEQ  BNE  BMI  BPL  BVC  BVS  BIT
             BRK  CLC  CLD  CLI  CLV  CMP  CPX  CPY  DEC  DEX  DEY  EOR
             INC  INX  INY  JMP  JSR  LDA  LDX  LDY  LSR  NOP  ORA  PHA
             PHP  PLA  PLP  ROL  ROR  RTI  RTS  SBC  SEC  SED  SEI  STA
             STX  STY  TAX  TAY  TSX  TXA  TXS  TYA

    TASM  also  supports the following instructions that are part of the
    Rockwell  R65C02  and  R65C00/21  microprocessor  instruction  sets.
    Those  that  are  marked  as  set A are applicable to the R65C02 and
    those marked as set B are  applicable  to  the  R65C00/21  (A+B  for
    both):

            Mnemonic        Description                Address Mode  Set
            ---------------------------------------------------------------
            ADC             Add with carry             (IND)         A
            AND             And memory with A          (IND)         A
            BIT             Test memory bits with A    ABS,X         A
            BIT             Test memory bits with A    ZP,X          A
            BIT             Test memory bits with A    IMM           A
            CMP             Compare memory with A      (IND)         A
            DEC             Decrement A                A             A
            EOR             Exclusive OR memory with A (IND)         A
            INC             Increment A                A             A
            JMP             Jump                       (ABS,X)       A
            LDA             Load A with memory         (IND)         A
            ORA             OR A with memory           (IND)         A
            SBC             Subtract memory form A     (IND)         A
            STA             Store A in memory          (IND)         A
            STZ             Store zero                 ABS           A
            STZ             Store zero                 ABS,X         A
            STZ             Store zero                 ZP            A
            STZ             Store zero                 ZP,X          A
            TRB             Test and reset memory bit  ABS           A
            TRB             Test and reset memory bit  ZP            A
            TSB             Test and set memory bit    ABS           A
            TSB             Test and set memory bit    ZP            A

            BRA             Branch Always              REL           A+B

            BBR0            Branch on Bit 0 Reset      ZP,REL        A+B
            BBR1            Branch on Bit 1 Reset      ZP,REL        A+B
            BBR2            Branch on Bit 2 Reset      ZP,REL        A+B


    TASM - Table Driven Assembler Version 2.7                    Page 37

            BBR3            Branch on Bit 3 Reset      ZP,REL        A+B
            BBR4            Branch on Bit 4 Reset      ZP,REL        A+B
            BBR5            Branch on Bit 5 Reset      ZP,REL        A+B
            BBR6            Branch on Bit 6 Reset      ZP,REL        A+B
            BBR7            Branch on Bit 7 Reset      ZP,REL        A+B

            BBS0            Branch on Bit 0 Set        ZP,REL        A+B
            BBS1            Branch on Bit 1 Set        ZP,REL        A+B
            BBS2            Branch on Bit 2 Set        ZP,REL        A+B
            BBS3            Branch on Bit 3 Set        ZP,REL        A+B
            BBS4            Branch on Bit 4 Set        ZP,REL        A+B
            BBS5            Branch on Bit 5 Set        ZP,REL        A+B
            BBS6            Branch on Bit 6 Set        ZP,REL        A+B
            BBS7            Branch on Bit 7 Set        ZP,REL        A+B

            MUL             Multiply                   Implied       B

            PHX             Push Index X               Implied       A+B
            PHY             Push Index Y               Implied       A+B
            PLX             Pull Index X               Implied       A+B
            PLY             Pull Index Y               Implied       A+B

            RMB0            Reset Memory Bit 0         ZP            A+B
            RMB1            Reset Memory Bit 1         ZP            A+B
            RMB2            Reset Memory Bit 2         ZP            A+B
            RMB3            Reset Memory Bit 3         ZP            A+B
            RMB4            Reset Memory Bit 4         ZP            A+B
            RMB5            Reset Memory Bit 5         ZP            A+B
            RMB6            Reset Memory Bit 6         ZP            A+B
            RMB7            Reset Memory Bit 7         ZP            A+B

            SMB0            Set   Memory Bit 0         ZP            A+B
            SMB1            Set   Memory Bit 1         ZP            A+B
            SMB2            Set   Memory Bit 2         ZP            A+B
            SMB3            Set   Memory Bit 3         ZP            A+B
            SMB4            Set   Memory Bit 4         ZP            A+B
            SMB5            Set   Memory Bit 5         ZP            A+B
            SMB6            Set   Memory Bit 6         ZP            A+B
            SMB7            Set   Memory Bit 7         ZP            A+B

    Note that correct assembly of these extended  instructions  has  not
    been tested on a target system.


    TASM - Table Driven Assembler Version 2.7                    Page 38


    Addressing  modes  are denoted as follows:

            ABS               Absolute
            ZP                Zero Page
            ABS,X             Absolute X
            ZP,X              Zero Page X
            ABS,Y             Absolute Y
            ZP,Y              Zero Page Y
            A                 Accumulator
            (IND,X)           Indirect X
            (IND),Y           Indirect Y
            (IND)             Indirect
            #IMM              Immediate
            REL               Relative (Branch instructions only)
            ZP,REL            Zero Page, Relative
            Implied           Implied

    Note  that Zero Page addressing can not be explicitly requested.  It
    is used if the value of the operand is  representable  in  a  single
    byte for the applicable statements.

    The '-x' command line option can be  used  to  enable  the  extended
    instructions.  A  '-x'  with  no  digit  following  will  enable the
    standard set plus both extended sets.  The 6502 version of TASM uses
    three bits in the instruction class  mask  to  determine  whether  a
    given  instruction  is enabled or not.  Bit 0 enables the basic set,
    bit 1 enables set A (R65C02) and bit 2 enables  set  B  (R65C00/21).
    The following table shows various options:

            Class Mask        Enabled Instructions
                            BASIC   R65C02  R65C00/21
            --------------------------------------------
            1               yes     no      no
            2               no      yes     no
            3               yes     yes     no
            4               no      no      yes
            5               yes     no      yes
            6               no      yes     yes
            7               yes     yes     yes

    Thus,  to enable the basic set plus the R65C02 instructions,  invoke
    the '-x3' command line option.

    See manufacturer's data for  a  more  complete  description  of  the
    meaning of the mnemonics and addressing modes.


    TASM - Table Driven Assembler Version 2.7                    Page 39


    8048 INSTRUCTIONS AND ADDRESSING MODES

    The following list shows the acceptable opcode mnemonics  and  their
    corresponding  operand  formats for the 8048 version of TASM.  Where
    'Rn' is seen,  R0 through R7  may  be  substituted.  Other  symbolic
    fields are as follows:

            SYMBOLIC            DESCRIPTION
            -----------------------------------------------
            <addr8>             Absolute address (8 bits)
            <addr11>            Absolute address (11 bits)
            <immed>             Immediate data

    Any valid TASM expression can appear in the  place  of  any  of  the
    above symbolics.

    The lines that are marked with an (8041),  (8022),  or (8021) on the
    far  right are extended instructions that are available only if a -x
    option has  been  invoked  on  the  command  line.  The  classes  of
    instructions  (and their bit assignment in the class mask) are shown
    below:

            BIT     PROCESSOR
            -------------------------------
            0       8X48, 8035, 8039, 8049
            1       8X41A
            2       8022
            3       8021

    Thus, to enable the basic 8048 set plus the 8022 set, a -x5 could be
    used on the command line.

    Note that some of the base instructions should be disabled  for  the
    8041, 8022, and 8021, but are not.

    OPCODE  OPERANDS        DESCRIPTION
    -------------------------------------------------------------------
    ADD     A,Rn            Add Register to Acc
    ADD     A,@R0           Add Indirect RAM to Acc
    ADD     A,@R1           Add Indirect RAM to Acc
    ADD     A,#<immed>      Add Immediate data to Acc

    ADDC    A,Rn            Add Register to Acc with carry
    ADDC    A,@R0           Add Indirect RAM to Acc with carry
    ADDC    A,@R1           Add Indirect RAM to Acc with carry
    ADDC    A,#<immed>      Add Immediate data to Acc with carry


    TASM - Table Driven Assembler Version 2.7                    Page 40


    ANL     A,Rn            AND Register to Acc
    ANL     A,@R0           AND Indirect RAM to Acc
    ANL     A,@R1           AND Indirect RAM to Acc
    ANL     A,#<immed>      AND Immediate data to Acc
    ANL     BUS,#<immed>    AND Immediate data to BUS
    ANL     P1,#<immed>     AND Immediate data to port P1
    ANL     P2,#<immed>     AND Immediate data to port P2

    ANLD    P4,A            AND Acc to Expander port P4
    ANLD    P5,A            AND Acc to Expander port P5
    ANLD    P6,A            AND Acc to Expander port P6
    ANLD    P7,A            AND Acc to Expander port P7

    CALL    <addr11>        Call subroutine

    CLR     A               Clear Acc
    CLR     C               Clear Carry
    CLR     F0              Clear Flag 0
    CLR     F1              Clear Flag 1

    CPL     A               Complement Acc
    CPL     C               Complement Carry
    CPL     F0              Complement Flag F0
    CPL     F1              Complement Flag F1

    DA      A               Decimal adjust Acc

    DEC     A               Decrement Acc
    DEC     Rn              Decrement Register

    DIS     I               Disable Interrupts
    DIS     TCNTI           Disable Timer/Counter Interrupt

    DJNZ    Rn,<addr8>      Decrement Register and Jump if nonzero

    EN      DMA             Enable DMA                           (8041)
    EN      FLAGS           Enable Flags                         (8041)
    EN      I               Enable External Interrupt
    EN      TCNTI           Enable Timer/Counter Interrupt
    ENT0    CLK             Enable Clock Output

    IN      A,DBB           Input Data Bus to Acc                (8041)
    IN      A,P0            Input Port 0 to Acc                  (8021)
    IN      A,P1            Input Port 1 to Acc
    IN      A,P2            Input Port 2 to Acc



    TASM - Table Driven Assembler Version 2.7                    Page 41

    INC     A               Increment Acc
    INC     Rn              Increment Register
    INC     @R0             Increment Indirect RAM
    INC     @R1             Increment Indirect RAM

    INS     A,BUS           Strobed Input of Bus to Acc

    JB0     <addr8>         Jump if Acc bit 0 is set
    JB1     <addr8>         Jump if Acc bit 1 is set
    JB2     <addr8>         Jump if Acc bit 2 is set
    JB3     <addr8>         Jump if Acc bit 3 is set
    JB4     <addr8>         Jump if Acc bit 4 is set
    JB5     <addr8>         Jump if Acc bit 5 is set
    JB6     <addr8>         Jump if Acc bit 6 is set
    JB7     <addr8>         Jump if Acc bit 7 is set
    JMP     <addr11>        Jump
    JC      <addr8>         Jump if Carry is set
    JF0     <addr8>         Jump if Flag F0 is set
    JF1     <addr8>         Jump if Flag F1 is set
    JNC     <addr8>         Jump if Carry is clear
    JNI     <addr8>         Jump if Interrupt input is clear
    JNIBF   <addr8>         Jump if IBF is clear                 (8041)
    JNT0    <addr8>         Jump if T0 is clear
    JNT1    <addr8>         Jump if T1 is clear
    JNZ     <addr8>         Jump if Acc is not zero
    JOBF    <addr8>         Jump if OBF is set                   (8041)
    JTF     <addr8>         Jump if Timer Flag is set
    JT0     <addr8>         Jump if T0 pin is high
    JT1     <addr8>         Jump if T1 pin is high
    JZ      <addr8>         Jump if Acc is zero
    JMPP    @A              Jump Indirect (current page)

    MOV     A,PSW           Move PSW to Acc
    MOV     A,Rn            Move Register to Acc
    MOV     A,T             Move Timer/Counter to Acc
    MOV     A,@R0           Move Indirect RAM to Acc
    MOV     A,@R1           Move Indirect RAM to Acc
    MOV     A,#<immed>      Move Immediate data to Acc
    MOV     PSW,A           Move Acc to PSW
    MOV     Rn,A            Move Acc to Register
    MOV     Rn,#<immed>     Move Immediate data to Register
    MOV     STS,A           Move Acc to STS                      (8041)
    MOV     T,A             Move Acc to Timer/Counter
    MOV     @R0,A           Move Acc to Indirect RAM
    MOV     @R1,A           Move Acc to Indirect RAM
    MOV     @R0,#<immed>    Move Immediate data to Indirect RAM
    MOV     @R1,#<immed>    Move Immediate data to Indirect RAM


    TASM - Table Driven Assembler Version 2.7                    Page 42


    MOVD    A,P4            Move half-byte Port 4 to Acc (lower nibble)
    MOVD    A,P5            Move half-byte Port 5 to Acc (lower nibble)
    MOVD    A,P6            Move half-byte Port 6 to Acc (lower nibble)
    MOVD    A,P7            Move half-byte Port 7 to Acc (lower nibble)
    MOVD    P4,A            Move lower nibble of Acc to Port 4
    MOVD    P5,A            Move lower nibble of Acc to Port 5
    MOVD    P6,A            Move lower nibble of Acc to Port 6
    MOVD    P7,A            Move lower nibble of Acc to Port 7

    MOVP    A,@A            Move Indirect Program data to Acc
    MOVP3   A,@A            Move Indirect Program data to Acc (page 3)

    MOVX    A,@R0           Move Indirect External RAM to Acc
    MOVX    A,@R1           Move Indirect External RAM to Acc
    MOVX    @R0,A           Move Acc to Indirect External RAM
    MOVX    @R1,A           Move Acc to Indirect External RAM

    NOP                     No operation

    ORL     A,Rn            OR Register to Acc
    ORL     A,@R0           OR Indirect RAM to Acc
    ORL     A,@R1           OR Indirect RAM to Acc
    ORL     A,#<immed>      OR Immediate data to Acc
    ORL     BUS,#<immed>    OR Immediate data to BUS
    ORL     P1,#<immed>     OR Immediate data to port P1
    ORL     P2,#<immed>     OR Immediate data to port P2

    ORLD    P4,A            OR lower nibble of Acc with P4
    ORLD    P5,A            OR lower nibble of Acc with P5
    ORLD    P6,A            OR lower nibble of Acc with P6
    ORLD    P7,A            OR lower nibble of Acc with P7

    OUTL    BUS,A           Output Acc to Bus
    OUT     DBB,A           Output Acc to DBB                    (8041)
    OUTL    P0,A            Output Acc to Port P0                (8021)
    OUTL    P1,A            Output Acc to Port P1
    OUTL    P2,A            Output Acc to Port P2

    RAD                     Move A/D Converter to Acc            (8022)

    RET                     Return from subroutine
    RETI                    Return from Interrupt w/o PSW restore(8022)
    RETR                    Return from Interrupt w/  PSW restore

    RL      A               Rotate Acc Left
    RLC     A               Rotate Acc Left through Carry


    TASM - Table Driven Assembler Version 2.7                    Page 43

    RR      A               Rotate Acc Right
    RRC     A               Rotate Acc Right through Carry

    SEL     AN0             Select Analog Input 0                (8022)
    SEL     AN1             Select Analog Input 1                (8022)
    SEL     MB0             Select Memory Bank 0
    SEL     MB1             Select Memory Bank 1
    SEL     RB0             Select Register Bank 0
    SEL     RB1             Select Register Bank 1

    STOP    TCNT            Stop Timer/Counter
    STRT    CNT             Start Counter
    STRT    T               Start Timer

    SWAP    A               Swap nibbles of Acc

    XCH     A,Rn            Exchange Register with Acc
    XCH     A,@R0           Exchange Indirect RAM with Acc
    XCH     A,@R1           Exchange Indirect RAM with Acc

    XCHD    A,@R0           Exchange lower nibble of Indirect RAM w/ Acc
    XCHD    A,@R1           Exchange lower nibble of Indirect RAM w/ Acc

    XRL     A,Rn            Exclusive OR Register to Acc
    XRL     A,@R0           Exclusive OR Indirect RAM to Acc
    XRL     A,@R1           Exclusive OR Indirect RAM to Acc
    XRL     A,#<immed>      Exclusive OR Immediate data to Acc


    See manufacturer's data for  a  more  complete  description  of  the
    meaning of the mnemonics and addressing modes.


    TASM - Table Driven Assembler Version 2.7                    Page 44


    8051 INSTRUCTIONS AND ADDRESSING MODES

    The following list shows the acceptable opcode mnemonics  and  their
    corresponding  operand  formats for the 8051 version of TASM.  Where
    'Rn' is seen,  R0 through R7  may  be  substituted.  Other  symbolic
    fields are as follows:

            SYMBOLIC            DESCRIPTION
            -----------------------------------------------
            <addr11>            Absolute address (11 bits)
            <addr16>            Absolute address (16 bits)
            <bit>               Bit address
            <immed>             Immediate data
            <direct>            Direct RAM address
            <rel>               Relative address

    Any valid TASM expression can appear in the  place  of  any  of  the
    above symbolics.

    OPCODE  OPERAND             DESCRIPTION
    --------------------------------------------------------------------
    ACALL   <addr11>            Absolute Call

    ADD     A,Rn                Add Register to Acc
    ADD     A,@R0               Add Indirect RAM to Acc
    ADD     A,@R1               Add Indirect RAM to Acc
    ADD     A,#<immed>          Add Immediate data to Acc
    ADD     A,<direct>          Add Direct RAM to Acc

    ADDC    A,Rn                Add Register to Acc with carry
    ADDC    A,@R0               Add Indirect RAM to Acc with carry
    ADDC    A,@R1               Add Indirect RAM to Acc with carry
    ADDC    A,#<immed>          Add Immediate data to Acc with carry
    ADDC    A,<direct>          Add Direct RAM to Acc with carry

    AJMP    <addr11>            Absolute Jump

    ANL     A,Rn                AND Register and Acc
    ANL     A,@R0               AND Indirect RAM and Acc
    ANL     A,@R1               AND Indirect RAM and Acc
    ANL     A,#<immed>          AND Immediate data and Acc
    ANL     A,<direct>          AND Direct RAM and Acc
    ANL     C,/<direct>         AND Complement of direct bit to Carry
    ANL     C,<direct>          AND direct bit to Carry
    ANL     <direct>,A          AND Acc to direct RAM
    ANL     <direct>,#<immed>   AND Immediate data and direct RAM


    TASM - Table Driven Assembler Version 2.7                    Page 45


    CJNE    A,#<immed>,<rel>    Compare Immediate to Acc   and JNE
    CJNE    A,<direct>,<rel>    Compare direct RAM to Acc and JNE
    CJNE    Rn,#<immed>,<rel>   Compare Immediate to Register and JNE
    CJNE    @R0,#<immed>,<rel>  Compare Immediate to Indirect RAM and JNE
    CJNE    @R1,#<immed>,<rel>  Compare Immediate to Indirect RAM and JNE

    CLR     A                   Clear Accumulator
    CLR     C                   Clear Carry
    CLR     <direct>            Clear Direct RAM

    CPL     A                   Complement Accumulator
    CPL     C                   Complement Carry
    CPL     <direct>            Complement Direct RAM

    DA      A                   Decimal Adjust Accumulator

    DEC     A                   Decrement Acc
    DEC     Rn                  Decrement Register
    DEC     @R0                 Decrement Indirect RAM
    DEC     @R1                 Decrement Indirect RAM
    DEC     <direct>            Decrement Direct RAM

    DIV     AB                  Divide Acc by B

    DJNZ    Rn,<rel>            Decrement Register and JNZ
    DJNZ    <direct>,<rel>      Decrement Direct RAM and JNZ

    INC     A                   Increment Acc
    INC     Rn                  Increment Register
    INC     @R0                 Increment Indirect RAM
    INC     @R1                 Increment Indirect RAM
    INC     DPTR                Increment Data Pointer
    INC     <direct>            Increment Direct RAM

    JB      <bit>,<rel>         Jump if Bit is set
    JBC     <bit>,<rel>         Jump if Bit is set & clear Bit
    JC      <rel>               Jump if Carry is set
    JMP     @A+DPTR             Jump indirect relative to Data Pointer
    JNB     <bit>,<rel>         Jump if Bit is clear
    JNC     <rel>               Jump if Carry is clear
    JNZ     <rel>               Jump if Acc is not zero
    JZ      <rel>               Jump if Acc is zero

    LCALL   <addr16>            Long Subroutine Call
    LJMP    <addr16>            Long Jump



    TASM - Table Driven Assembler Version 2.7                    Page 46

    MOV     A,Rn                Move Register to Acc
    MOV     A,@R0               Move Indirect RAM to Acc
    MOV     A,@R1               Move Indirect RAM to Acc
    MOV     A,#<immed>          Move Immediate data to Acc
    MOV     A,<direct>          Move direct RAM to Acc
    MOV     C,<bit>             Move bit to Acc
    MOV     DPTR,#<immed>       Move immediate data to Data Pointer
    MOV     Rn,A                Move Acc to Register
    MOV     Rn,#<immed>         Move Immediate data to Register
    MOV     Rn,<direct>         Move Direct RAM to Register
    MOV     @R0,A               Move Acc to Indirect RAM
    MOV     @R1,A               Move Acc to Indirect RAM
    MOV     @R0,#<immed>        Move Immediate data to Indirect RAM
    MOV     @R1,#<immed>        Move Immediate data to Indirect RAM
    MOV     @R0,<direct>        Move Direct RAM to Indirect RAM
    MOV     @R1,<direct>        Move Direct RAM to Indirect RAM
    MOV     <direct>,A          Move Acc to Direct RAM
    MOV     <bit>,C             Move Carry to Bit
    MOV     <direct>,Rn         Move Register to Direct RAM
    MOV     <direct>,@R0        Move Indirect RAM to Direct RAM
    MOV     <direct>,@R1        Move Indirect RAM to Direct RAM
    MOV     <direct>,#<immed>   Move Immediate data to Direct RAM
    MOV     <direct>,<direct>   Move Direct RAM to Direct RAM
    MOVC    A,@A+DPTR           Move code byte relative to DPTR to Acc
    MOVC    A,@A+PC             Move code byte relative to PC to Acc

    MOVX    A,@R0               Move external RAM to Acc
    MOVX    A,@R1               Move external RAM to Acc
    MOVX    A,@DPTR             Move external RAM to Acc (16 bit addr)
    MOVX    @R0,A               Move Acc to external RAM
    MOVX    @R1,A               Move Acc to external RAM
    MOVX    @DPTR,A             Move Acc to external RAM (16 bit addr)

    MUL     AB                  Multiply Acc by B

    NOP                         No operation

    ORL     A,Rn                OR Register and Acc
    ORL     A,@R0               OR Indirect RAM and Acc
    ORL     A,@R1               OR Indirect RAM and Acc
    ORL     A,#<immed>          OR Immediate data and Acc
    ORL     A,<direct>          OR Direct RAM and Acc
    ORL     C,/<direct>         OR Complement of direct bit to Carry
    ORL     C,<direct>          OR direct bit to Carry
    ORL     <direct>,A          OR Acc to direct RAM
    ORL     <direct>,#<immed>   OR Immediate data and direct RAM



    TASM - Table Driven Assembler Version 2.7                    Page 47

    POP     <direct>            Pop  from Stack and put in Direct RAM
    PUSH    <direct>            Push from Direct RAM to Stack

    RET                         Return from subroutine
    RETI                        Return from Interrupt

    RL      A                   Rotate Acc left
    RLC     A                   Rotate Acc left through Carry
    RR      A                   Rotate Acc right
    RRC     A                   Rotate Acc right through Carry

    SETB    C                   Set the Carry Bit
    SETB    <bit>               Set Direct Bit

    SJMP    <rel>               Short jump

    SUBB    A,Rn                Subtract Register from Acc with Borrow
    SUBB    A,@R0               Subtract Indirect RAM from Acc w/ Borrow
    SUBB    A,@R1               Subtract Indirect RAM from Acc w/ Borrow
    SUBB    A,#<immed>          Subtract Immediate data from Acc w/ Borrow
    SUBB    A,<direct>          Subtract Direct RAM from Acc w/ Borrow

    SWAP    A                   Swap nibbles of Acc

    XCH     A,Rn                Exchange Acc with Register
    XCH     A,@R0               Exchange Acc with Indirect RAM
    XCH     A,@R1               Exchange Acc with Indirect RAM
    XCH     A,<direct>          Exchange Acc with Direct RAM

    XCHD    A,@R0               Exchange Digit in Acc with Indirect RAM
    XCHD    A,@R1               Exchange Digit in Acc with Indirect RAM

    XRL     A,Rn                Exclusive OR Register and Acc
    XRL     A,@R0               Exclusive OR Indirect RAM and Acc
    XRL     A,@R1               Exclusive OR Indirect RAM and Acc
    XRL     A,#<immed>          Exclusive OR Immediate data and Acc
    XRL     A,<direct>          Exclusive OR Direct RAM and Acc
    XRL     <direct>,A          Exclusive OR Acc to direct RAM
    XRL     <direct>,#<immed>   Exclusive OR Immediate data and direct RAM

    Note  that  the above tables do not automatically define the various
    mnemonics that may be  used  for  addressing  the  special  function
    registers  of  the  8051.  The  user  may  wish  to set up a file of
    equates (EQU's) that can be included in the  source  file  for  this
    purpose.  The following illustrates some of the appropriate equates:




    TASM - Table Driven Assembler Version 2.7                    Page 48

    P0      .equ    080H    ;Port 0
    SP      .equ    081H    ;Stack pointer
    DPL     .equ    082H
    DPH     .equ    083H
    PCON    .equ    087H
    TCON    .equ    088H
    TMOD    .equ    089H
    TL0     .equ    08AH
    TL1     .equ    08BH
    TH0     .equ    08CH
    TH1     .equ    08DH
    P1      .equ    090H    ;Port 1
    SCON    .equ    098H
    SBUF    .equ    099H
    P2      .equ    0A0H    ;Port 2
    IEC     .equ    0A8H
    P3      .equ    0B0H    ;Port 3
    IPC     .equ    0B8H
    PSW     .equ    0D0H
    ACC     .equ    0E0H    ;Accumulator
    B       .equ    0F0H    ;Secondary Accumulator
    ;Now some bit addresses
    P0.0    .equ    080H    ;Port 0 bit 0
    P0.1    .equ    081H    ;Port 0 bit 1
    P0.2    .equ    082H    ;Port 0 bit 2
    P0.3    .equ    083H    ;Port 0 bit 3
    P0.4    .equ    080H    ;Port 0 bit 4
    P0.5    .equ    081H    ;Port 0 bit 5
    P0.6    .equ    082H    ;Port 0 bit 6
    P0.7    .equ    083H    ;Port 0 bit 7
    ACC.0   .equ    0E0H    ;Acc bit 0
    ACC.1   .equ    0E1H    ;Acc bit 1
    ACC.2   .equ    0E2H    ;Acc bit 2
    ACC.3   .equ    0E3H    ;Acc bit 3
    ACC.4   .equ    0E4H    ;Acc bit 4
    ACC.5   .equ    0E5H    ;Acc bit 5
    ACC.6   .equ    0E6H    ;Acc bit 6
    ACC.7   .equ    0E7H    ;Acc bit 7

    See the manufacturer's data sheets for more information.


    TASM - Table Driven Assembler Version 2.7                    Page 49


    8085 INSTRUCTIONS AND ADDRESSING MODES

    The following list shows the acceptable opcode mnemonics  and  their
    corresponding  operand  formats for the 8085  version of TASM.   The
    following symbols are used in the table:

            SYMBOLIC            DESCRIPTION
            -----------------------------------------------
            <addr>              Absolute address (16 bits)
            <data>              Immediate data (8 bits)
            <data16>            Immediate data (16 bits)
            <reg>               Register (A,B,C,D,E,H,L)
            <rp>                Register pair (B,D,H,SP)
            <port>              Port address (0-255)
            <int>               Interrupt level (0 - 7)

    Any valid TASM expression can appear in the  place  of  any  of  the
    above symbolics except <reg>, <rp> and <int>.

    OPCODE  OPERAND        DESCRIPTION
    --------------------------------------------------------------------
    ACI      <data>         Add immediate to A with carry
    ADC      <reg>          Add <reg> to A with carry
    ADC      M              Add indirect memory (HL) with carry
    ADD      <reg>          Add <reg> to A
    ADD      M              Add indirect memory (HL) to A
    ADI      <data>         Add immediate to A

    ANA      <reg>          And register with A
    ANA      M              And indirect memory (HL) to A
    ANI      <data>         And immediate to A

    CALL     <addr>         Call subroutine at <addr>
    CC       <addr>         Call subroutine if carry set
    CNC      <addr>         Call subroutine if carry clear
    CZ       <addr>         Call subroutine if zero
    CNZ      <addr>         Call subroutine if non zero
    CP       <addr>         Call subroutine if positive
    CM       <addr>         Call subroutine if negative
    CPE      <addr>         Call subroutine if even parity
    CPO      <addr>         Call subroutine if odd  parity
    CMA                     Complement A
    CMC                     Complemennt carry
    CMP      <reg>          Compare register with A
    CMP      M              Compare indirect memory (HL) with A
    CPI      <data>         Compare immediate data with A


    TASM - Table Driven Assembler Version 2.7                    Page 50


    DAA                     Decimal adjust A
    DAD      <rp>           Add register pair to HL
    DCR      <reg>          Decrement register
    DCR      M              Decrement indirect memory (HL)
    DCX      <rp>           Decrement register pair

    DI                      Disable interrupts
    EI                      Enable interrupts
    HLT                     Halt

    IN       <port>         Input on port
    INR      <reg>          Increment register
    INR      M              Increment indirect memory (HL)
    INX      <rp>           Increment register pair

    JMP      <addr>         Jump
    JC       <addr>         Jump if carry set
    JNC      <addr>         Jump if carry clear
    JZ       <addr>         Jump if zero
    JNZ      <addr>         Jump if not zero
    JM       <addr>         Jump if minus
    JP       <addr>         Jump if plus
    JPE      <addr>         Jump if parity even
    JPO      <addr>         Jump if parity odd

    LDA      <addr>         Load A direct from memory
    LDAX     B              Load A indirect from memory using BC
    LDAX     D              Load A indirect from memory using DE
    LHLD     <addr>         Load HL direct from memory
    LXI      <rp>,<data16>  Load register pair with immediate data

    MOV      <reg>,<reg>    Move register to register
    MOV      <reg>,M        Move indirect memory (HL) to register
    MVI      <reg>,<data>   Move immediate data to register

    NOP                     No operation

    ORA      <reg>          Or register with A
    ORA      M              Or indirect memory (HL) with A
    ORI      <data>         Or immediate data to A
    OUT      <port>         Ouput to port

    PCHL                    Jump to instruction at (HL)
    POP      <rp>           Pop  register pair (excluding SP) from stack
    PUSH     <rp>           Push register pair (excluding SP) onto stack
    POP      PSW            Pop  PSW from stack


    TASM - Table Driven Assembler Version 2.7                    Page 51

    PUSH     PSW            Pop  PSW onto stack

    RAL                     Rotate A left  with carry
    RAR                     Rotate A right with carry
    RLC                     Rotate A left  with branch carry
    RRC                     Rotate A right with branch carry

    RET                     Return from subroutine
    RZ                      Return if zero
    RNZ                     Return if non zero
    RC                      Return if carry set
    RNC                     Return if carry clear
    RM                      Return if minus
    RP                      Return if plus
    RPE                     Return if parity even
    RPO                     Return if parity odd

    RIM                     Read interrupt mask
    RST      <int>          Restart at vector <int>

    SBB      <reg>          Subtract <reg> from A         with borrow
    SBB      M              Subtract indirect memory (HL) with borrow
    SBI      <data>         Subtract immediate from A     with borrow
    SUB      <reg>          Subtract <reg> from A
    SUB      M              Subtract indirect memory (HL) from A
    SUI      <data>         Subtract immediate from A

    SHLD     <addr>         Store HL
    SIM                     Store Interrupt mask
    SPHL                    Exchange SP with HL

    STA      <addr>         Store A direct memory
    STAX     B              Store A indirect using BC
    STAX     D              Store A indirect using DE

    STC                     Set carry

    XRA      <reg>          Exclusive OR A with register
    XRA      M              Exclusive Or A with indirect memory (HL)
    XRI      <data>         Exclusive Or A with immediate data
    XCHG                    Exchange DE with HL
    XTHL                    Exchange HL with top of stack

    See the manufacturer's data sheets for more information.


    TASM - Table Driven Assembler Version 2.7                    Page 52


    Z80 INSTRUCTIONS AND ADDRESSING MODES

    The following list shows the acceptable opcode mnemonics  and  their
    corresponding   operand  formats for the Z80  version of TASM.   The
    following symbols are used in the table:

            SYMBOLIC            DESCRIPTION
            -----------------------------------------------
            <addr>              Absolute address (16 bits)
            <bit>               Bit address
            <data>              Immediate data (8 bits)
            <data16>            Immediate data (16 bits)
            <disp>              Relative address
            <reg>               Register (A, B, C, D, E, H, or L)
            <rp>                Register pair (BC, DE, HL, or SP)
            <port>              Port (0 - 255)
            <cond>              Condition
                                    NZ - not zero
                                    Z  - zero
                                    NC - not carry
                                    C  - carry
                                    PO - parity odd
                                    PE - parity even
                                    P  - positive
                                    M  - minus

    Any valid TASM expression can appear in the  place  of the  <addr>,
    <bit>, <data>, <data16>, or <disp> symbolics.

    OPCODE  OPERAND         DESCRIPTION
    --------------------------------------------------------------------
    ADC  A,<data>           Add immediate with carry to accumulator
    ADC  A,<reg>            Add register with carry to accumulator
    ADC  A,(HL)             Add indirect memory with carry to accumulator
    ADC  A,(IX+<disp>)      Add indirect memory with carry to accumulator
    ADC  A,(IY+<disp>)      Add indirect memory with carry to accumulator
    ADC  HL,<rp>            Add register pair with carry to HL

    ADD  A,<data>           Add immediate to accumulator
    ADD  A,<reg>            Add register to accumulator
    ADD  A,(HL)             Add indirect memory to accumulator
    ADD  A,(IX+<disp>)      Add indirect memory to accumulator
    ADD  A,(IY+<disp>)      Add indirect memory to accumulator
    ADD  HL,<rp>            Add register pair to HL
    ADD  IX,<rp>            Add register pair to index register
    ADD  IY,<rp>            Add register pair to index register


    TASM - Table Driven Assembler Version 2.7                    Page 53


    AND  <data>             And immediate with accumulator
    AND  <reg>              And register  with accumulator
    AND  (HL)               And memory with accumulator
    AND  (IX+<disp>)        And memory with accumulator
    AND  (IY+<disp>)        And memory with accumulator

    BIT  <bit>,<reg>        Test <bit> in register
    BIT  <bit>,(HL)         Test <bit> in indirect memory
    BIT  <bit>,(IY+<disp>)  Test <bit> in indirect memory
    BIT  <bit>,(IX+<disp>)  Test <bit> in indirect memory

    CALL <addr>             Call the routine at <addr>
    CALL <cond>,<addr>      Call the routine if <cond> is satisfied

    CCF                     Complement carry flag

    CP   <data>             Compare immediate data with accumulator
    CP   <reg>              Compare register with accumulator
    CP   (HL)               Compare indirect memory with accumulator
    CP   (IX+<disp>)        Compare indirect memory with accumulator
    CP   (IY+<disp>)        Compare indirect memory with accumulator
    CPD                     Compare accumulator with memory and
                                decrement address and byte counters
    CPDR                    Compare accumulator with memory and
                                decrement address and byte counter,
                                continue until match is found or
                                byte counter is zero

    CPI                     Compare accumulator with memory and
                                increment address and byte counters
    CPIR                    Compare accumulator with memory and
                                increment address and byte counter,
                                continue until match is found or
                                byte counter is zero
    CPL                     Complement the accumulator
    DAA                     Decimal adjust accumulator
    DEC  <reg>              Decrement register contents
    DI                      Disable interrupts
    DJNZ <disp>             Decrement reg B and jump relative if zero
    EI                      Enable interrupts
    EX   AF,AF'             Exchange program status and alt program stat
    EX   DE,HL              Exchange DE and HL contents
    EX   (SP),HL            Exchange contents of HL and top of stack
    EX   (SP),IX            Exchange contents of IX and top of stack
    EX   (SP),IY            Exchange contents of IY and top of stack
    EXX                     Exchange register pairs and alt reg pairs


    TASM - Table Driven Assembler Version 2.7                    Page 54

    HALT                    Program execution stops
    IM   0                  Interrupt mode 0
    IM   1                  Interrupt mode 1
    IM   2                  Interrupt mode 2
    IN   A,<port>           Input port to accumulator
    INC  <reg>              Increment contents of register
    INC  <rp>               Increment contents of register pair
    INC  IX                 Increment IX
    INC  IY                 Increment IY
    INC  (HL)               Increment indirect memory
    INC  (IX+<disp>)        Increment indirect memory
    INC  (IY+<disp>)        Increment indirect memory
    IND                     Input to memory and decrement pointer
    INDR                    Input to memory and decrement pointer until
                                byte counter is zero
    INI                     Input to memory and increment pointer
    INIR                    Input to memory and increment pointer until
                                byte counter is zero
    IN   <reg>,(C)          Input to register

    JP   <addr>             Jump to location
    JP   <cond>,<addr>      Jump to location if condition satisifed
    JP   (HL)               Jump to location pointed to by HL
    JP   (IX)               Jump to location pointed to by IX
    JP   (IY)               Jump to location pointed to by IY

    JR   <disp>             Jump relative
    JR   C,<disp>           Jump relative if carry is set
    JR   NC,<disp>          Jump relative if carry bit is reset
    JR   NZ,<disp>          Jump relative if zero flag is reset
    JR   Z,<disp>           Jump relative if zero flag is set

    LD   A,I                Move interrupt vector contents to accumulator
    LD   A,R                Move refresh reg contents to accumulator
    LD   A,(<addr>)         Load accumulator indirect from memory
    LD   A,(<rp>)           Load accumulator indirect from memory by <rp>
    LD   <reg>,<reg>        Load source register to destination register
    LD   <rp>,(<addr>)      Load register pair indirect from memory
    LD   IX,(<addr>)        Load IX indirect from memory
    LD   IY,(<addr>)        Load IY indirect from memory
    LD   I,A                Load interrup vector from accumulator
    LD   R,A                Load refresh register from accumulator
    LD   <reg>,<data>       Load register with immediate data
    LD   <rp>,<data16>      Load register pair with immediate data
    LD   IX,<data16>        Load  IX  with immediate data
    LD   IY,<data16>        Load  IY  with immediate data
    LD   <reg>,(HL)         Load register indirect from memory


    TASM - Table Driven Assembler Version 2.7                    Page 55

    LD   <reg>,(IX+<disp>)  Load register indirect from memory
    LD   <reg>,(IY+<disp>)  Load register indirect from memory
    LD   SP,HL              Load contents of HL to stack pointer
    LD   SP,IX              Load contents of IX to stack pointer
    LD   SP,IY              Load contents of IY to stack pointer
    LD   (addr),A           Load contents of A to memory
    LD   (<addr>),HL        Load contents of HL to memory
    LD   (<addr>),<rp>      Load contents of register pair to memory
    LD   (<addr>),IX        Load contents of IX to memory
    LD   (<addr>),IY        Load contents of IY to memory
    LD   (HL),<data>        Load immediate into indirect memory
    LD   (IX+<disp>),<data> Load immediate into indirect memory
    LD   (IY+<disp>),<data> Load immediate into indirect memory
    LD   (HL),<reg>         Load register  into indirect memory
    LD   (IX+<disp>),<reg>  Load register  into indirect memory
    LD   (IY+<disp>),<reg>  Load register  into indirect memory
    LD   (<rp>),A           Load accumulator into indirect memory
    LDD                     Transfer data between memory and decrement
                                destination and source addresses
    LDDR                    Transfer data between memory until byte
                                counter is zero, decrement destintation
                                and source addresses
    LDI                     Transfer data between memory and increment
                                destination and source addresses
    LDIR                    Transfer data between memory until byte
                                counter is zero, increment destination
                                and source addresses
    NEG                     Negate contents of accumulator
    NOP                     No operation
    OR   <data>             Or immediate with accumulator
    OR   <reg>              Or register with accumulator
    OR   (HL)               Or indirect memory with accumulator
    OR   (IX+<disp>)        Or indirect memory with accumulator
    OR   (IY+<disp>)        Or indirect memory with accumulator
    OUT  (C),<reg>          Output from registor
    OUTD                    Output from memory, decrement address
    OTDR                    Output from memory, decrement address
                                continue until reg B is zero
    OUTI                    Output from memory, increment address
    OTIR                    Output from memory, increment address
                                continue until reg B is zero
    OUT  <port>,A           Output from accumulator
    POP  <rp>               Load register pair from top of stack
    POP  IX                 Load IX from top of stack
    POP  IY                 Load IY from top of stack
    PUSH <rp>               Store resister pair on top of stack
    PUSH IX                 Store IX on top of stack


    TASM - Table Driven Assembler Version 2.7                    Page 56

    PUSH IY                 Store IY on top of stack
    RES  <bit>,<reg>        Reset register bit
    RES  <bit>,(HL)         Reset bit at indirect memory location
    RES  <bit>,(IX+disp)    Reset bit at indirect memory location
    RES  <bit>,(IY+<disp>)  Reset bit at indirect memory location
    RET                     Return from subroutine
    RET  <cond>             Return from subroutine if condition true
    RETI                    Return from interrupt
    RETN                    Return from non-maskable interrupt
    RL   <reg>              Rotate left through carry register contents
    RL   (HL)               Rotate left through carry indirect memory
    RL   (IX+<disp>)        Rotate left through carry indirect memory
    RL   (IY+<disp>)        Rotate left through carry indirect memory
    RLA                     Rotate left through carry accumulator
    RLC  <reg>              Rotate left branch  carry register contents
    RLC  (HL)               Rotate left branch  carry indirect memory
    RLC  (IX+<disp>)        Rotate left branch  carry indirect memory
    RLC  (IY+<disp>)        Rotate left branch  carry indirect memory
    RLCA                    Rotate left accumulator
    RLD                     Rotate one BCD digit left between the
                                accumulator and memory
    RR   <reg>              Rotate right through carry register contents
    RR   (HL)               Rotate right through carry indirect memory
    RR   (IX+<disp>)        Rotate right through carry indirect memory
    RR   (IY+<disp>)        Rotate right through carry indirect memory
    RRA                     Rotate right through carry accumulator
    RRC  <reg>              Rotate right branch  carry register contents
    RRC  (HL)               Rotate right branch  carry indirect memory
    RRC  (IX+<disp>)        Rotate right branch  carry indirect memory
    RRC  (IY+<disp>)        Rotate right branch  carry indirect memory
    RRCA                    Rotate right branch  carry accumulator
    RRD                     Rotate one BCD digit right between the
                                accumulator and memory
    RST                     Restart
    SBC  A,<data>           Subtract data            from A with borrow
    SBC  A,<reg>            Subtract register        from A with borrow
    SBC  A,(HL)             Subtract indirect memory from A with borrow
    SBC  A,(IX+<disp>)      Subtract indirect memory from A with borrow
    SBC  A,(IY+<disp>)      Subtract indirect memory from A with borrow
    SBC  HL,<rp>            Subtract register pair from HL with borrow
    SCF                     Set carry flag
    SET  <bit>,<reg>        Set register bit
    SET  <bit>,(HL)         Set indirect memory bit
    SET  <bit>,(IX+<disp>)  Set indirect memory bit
    SET  <bit>,(IY+<disp>)  Set indirect memory bit
    SLA  <reg>              Shift register left arithmetic
    SLA  (HL)               Shift indirect memory left arithmetic


    TASM - Table Driven Assembler Version 2.7                    Page 57

    SLA  (IX+<disp>)        Shift indirect memory left arithmetic
    SLA  (IY+<disp>)        Shift indirect memory left arithmetic
    SRA  <reg>              Shift register right arithmetic
    SRA  (HL)               Shift indirect memory right arithmetic
    SRA  (IX+<disp>)        Shift indirect memory right arithmetic
    SRA  (IY+<disp>)        Shift indirect memory right arithmetic
    SRL  <reg>              Shift register right logical
    SRL  (HL)               Shift indirect memory right logical
    SRL  (IX+<disp>)        Shift indirect memory right logical
    SRL  (IY+<disp>)        Shift indirect memory right logical
    SUB  <data>             Subtract immediate from accumulator
    SUB  <reg>              Subtract register from accumulator
    SUB  (HL)               Subtract indirect memory from accumulator
    SUB  (IX+<disp>)        Subtract indirect memory from accumulator
    SUB  (IY+<disp>)        Subtract indirect memory from accumulator
    XOR  <data>             Exclusive or immediate with accumulator
    XOR  <reg>              Exclusive or register with accumulator
    XOR  (HL)               Exclusive or indirect memory with accumulator
    XOR  (IX+<disp>)        Exclusive or indirect memory with accumulator
    XOR  (IY+<disp>)        Exclusive or indirect memory with accumulator

    See the manufacturer's data sheets for more information.


    TASM - Table Driven Assembler Version 2.7                    Page 58


    6805 INSTRUCTIONS AND ADDRESSING MODES

    The following list shows the acceptable opcode mnemonics  and  their
    corresponding   operand  formats for the 6805  version of TASM.   The
    following symbols are used in the table:

            SYMBOLIC            DESCRIPTION
            -----------------------------------------------
            <addr>              Absolute address (16 bits)
            <addr8>             Absolute address (8 bits)
            <bit>               Bit address
            <data>              Immediate data (8 bits)
            <rel>               Relative address

    Any valid TASM expression can appear in the  place  of the  <addr>,
    <addr8>, <bit>, <data>, or <rel> symbolics.

    OPCODE  OPERAND         DESCRIPTION
    --------------------------------------------------------------
    ADC     #<data>         Add with carry, immediate
    ADC     ,X              Add with carry, indexed, no offset
    ADC     <addr8>,X       Add with carry, indexed, 1 byte offset
    ADC     <addr>,X        Add with carry, indexed, 2 byte offset
    ADC     <addr8>         Add with carry, direct
    ADC     <addr>          Add with carry, extended

    ADD     #<data>         Add, immediate
    ADD     ,X              Add, indexed, no offset
    ADD     <addr8>,X       Add, indexed, 1 byte offset
    ADD     <addr>,X        Add, indexed, 2 byte offset
    ADD     <addr8>         Add, direct
    ADD     <addr>          Add, extended

    AND     #<data>         And, immediate
    AND     ,X              And, indexed, no offset
    AND     <addr8>,X       And, indexed, 1 byte offset
    AND     <addr>,X        And, indexed, 2 byte offset
    AND     <addr8>         And, direct
    AND     <addr>          And, extended

    ASLA                    Arithmetic Shift Left, accumulator
    ASLX                    Arithmetic Shift Left, index register
    ASL     <addr8>         Arithmetic Shift Left, direct
    ASL     ,X              Arithmetic Shift Left, indexed, no offset
    ASL     <addr8>,X       Arithmetic Shift Left, indexed, 1 byte offset



    TASM - Table Driven Assembler Version 2.7                    Page 59

    ASRA                    Arithmetic Shift Right, accumulator
    ASRX                    Arithmetic Shift Right, index register
    ASR     <addr8>         Arithmetic Shift Right, direct
    ASR     ,X              Arithmetic Shift Right, indexed, no offset
    ASR     <addr8>,X       Arithmetic Shift Right, indexed, 1 byte offset

    BCC     <rel>           Branch if carry clear
    BCLR    <bit>,<addr8>   Bit Clear in memory
    BCS     <rel>           Branch if carry set
    BEQ     <rel>           Branch if equal
    BHCC    <rel>           Branch if half carry clear
    BHCS    <rel>           Branch if half carry set
    BHI     <rel.           Branch if higher
    BHS     <rel>           Branch if higher or same
    BIH     <rel>           Branch if interrupt line is high
    BIL     <rel>           Branch if interrupt is low

    BIT     #<data>         Bit test, immediate
    BIT     ,X              Bit test, indexed, no offset
    BIT     <addr8>,X       Bit test, indexed, 1 byte offset
    BIT     <addr>,X        Bit test, indexed, 2 byte offset
    BIT     <addr8>         Bit test, direct
    BIT     <addr>          Bit test, extended

    BLO     <rel>           Branch if lower
    BLS     <rel>           Branch if lower or same
    BMC     <rel>           Branch if interrupt mask is clear
    BMI     <rel>           Branch if minus
    BMS     <rel>           Branch if interuupt mask bit is set
    BNE     <rel>           Branch if not equal
    BPL     <rel>           Branch if plus
    BRA     <rel>           Branch always
    BRCLR   <bit>,<addr8>,<rel>     Branch if bit is clear
    BRN     <rel>           Branch never
    BRSET   <bit>,<addr8>,<rel>     Branch if bit is set
    BSET    <bit>,<addr8>   Bit set in memory
    BSR     <rel>           Branch to subroutine

    CLC                     Clear carry bit
    CLI                     Clear interuupt mask bit

    CLRA                    Clear, accumulator
    CLRX                    Clear, index register
    CLR     <addr8>         Clear, direct
    CLR     ,X              Clear, indexed, no offset
    CLR     <addr8>,X       Clear, indexed, 1 byte offset



    TASM - Table Driven Assembler Version 2.7                    Page 60

    CMP     #<data>         Compare Acc, immediate
    CMP     ,X              Compare Acc, indexed, no offset
    CMP     <addr8>,X       Compare Acc, indexed, 1 byte offset
    CMP     <addr>,X        Compare Acc, indexed, 2 byte offset
    CMP     <addr8>         Compare Acc, direct
    CMP     <addr>          Compare Acc, extended

    COMA                    Complement, accumulator
    COMX                    Complement, index register
    COM     <addr8>         Complement, direct
    COM     ,X              Complement, indexed, no offset
    COM     <addr8>,X       Complement, indexed, 1 byte offset

    CPX     #<data>         Compare Index, immediate
    CPX     ,X              Compare Index, indexed, no offset
    CPX     <addr8>,X       Compare Index, indexed, 1 byte offset
    CPX     <addr>,X        Compare Index, indexed, 2 byte offset
    CPX     <addr8>         Compare Index, direct
    CPX     <addr>          Compare Index, extended

    DECA                    Decrement, accumulator
    DECX                    Decrement, index register
    DEX                     Decrement, index register (alternate of DECX)
    DEC     <addr8>         Decrement, direct
    DEC     ,X              Decrement, indexed, no offset
    DEC     <addr8>,X       Decrement, indexed, 1 byte offset

    EOR     #<data>         Exclusive OR, immediate
    EOR     ,X              Exclusive OR, indexed, no offset
    EOR     <addr8>,X       Exclusive OR, indexed, 1 byte offset
    EOR     <addr>,X        Exclusive OR, indexed, 2 byte offset
    EOR     <addr8>         Exclusive OR, direct
    EOR     <addr>          Exclusive OR, extended

    INCA                    Increment, accumulator
    INCX                    Increment, index register
    INX                     Increment, index register (alternate of INCX)
    INC     <addr8>         Increment, direct
    INC     ,X              Increment, indexed, no offset
    INC     <addr8>,X       Increment, indexed, 1 byte offset

    JMP     ,X              Jump, indexed, no offset
    JMP     <addr8>,X       Jump, indexed, 1 byte offset
    JMP     <addr>,X        Jump, indexed, 2 byte offset
    JMP     <addr8>         Jump, direct
    JMP     <addr>          Jump, extended



    TASM - Table Driven Assembler Version 2.7                    Page 61

    JSR     ,X              Jump Subroutine, indexed, no offset
    JSR     <addr8>,X       Jump Subroutine, indexed, 1 byte offset
    JSR     <addr>,X        Jump Subroutine, indexed, 2 byte offset
    JSR     <addr8>         Jump Subroutine, direct
    JSR     <addr>          Jump Subroutine, extended

    LDA     #<data>         Load Acc, immediate
    LDA     ,X              Load Acc, indexed, no offset
    LDA     <addr8>,X       Load Acc, indexed, 1 byte offset
    LDA     <addr>,X        Load Acc, indexed, 2 byte offset
    LDA     <addr8>         Load Acc, direct
    LDA     <addr>          Load Acc, extended

    LDX     #<data>         Load Index, immediate
    LDX     ,X              Load Index, indexed, no offset
    LDX     <addr8>,X       Load Index, indexed, 1 byte offset
    LDX     <addr>,X        Load Index, indexed, 2 byte offset
    LDX     <addr8>         Load Index, direct
    LDX     <addr>          Load Index, extended

    LSLA                    Logical Shift Left, accumulator
    LSLX                    Logical Shift Left, index register
    LSL     <addr8>         Logical Shift Left, direct
    LSL     ,X              Logical Shift Left, indexed, no offset
    LSL     <addr8>,X       Logical Shift Left, indexed, 1 byte offset

    LSRA                    Logical Shift Right, accumulator
    LSRX                    Logical Shift Right, index register
    LSR     <addr8>         Logical Shift Right, direct
    LSR     ,X              Logical Shift Right, indexed, no offset
    LSR     <addr8>,X       Logical Shift Right, indexed, 1 byte offset

    NEGA                    Negate, accumulator
    NEGX                    Negate, index register
    NEG     <addr8>         Negate, direct
    NEG     ,X              Negate, indexed, no offset
    NEG     <addr8>,X       Negate, indexed, 1 byte offset

    NOP                     No Operation

    ORA     #<data>         Inclusive OR Acc, immediate
    ORA     ,X              Inclusive OR Acc, indexed, no offset
    ORA     <addr8>,X       Inclusive OR Acc, indexed, 1 byte offset
    ORA     <addr>,X        Inclusive OR Acc, indexed, 2 byte offset
    ORA     <addr8>         Inclusive OR Acc, direct
    ORA     <addr>          Inclusive OR Acc, extended



    TASM - Table Driven Assembler Version 2.7                    Page 62

    ROLA                    Rotate Left thru Carry, accumulator
    ROLX                    Rotate Left thru Carry, index register
    ROL     <addr8>         Rotate Left thru Carry, direct
    ROL     ,X              Rotate Left thru Carry, indexed, no offset
    ROL     <addr8>,X       Rotate Left thru Carry, indexed, 1 byte offset

    RORA                    Rotate Right thru Carry, accumulator
    RORX                    Rotate Right thru Carry, index register
    ROR     <addr8>         Rotate Right thru Carry, direct
    ROR     ,X              Rotate Right thru Carry, indexed, no offset
    ROR     <addr8>,X       Rotate Right thru Carry, indexed, 1 byte offset

    RSP                     Reset Stack Pointer
    RTI                     Return from Interrupt
    RTS                     Return from Subroutine

    SBC     #<data>         Subtract with Carry, immediate
    SBC     ,X              Subtract with Carry, indexed, no offset
    SBC     <addr8>,X       Subtract with Carry, indexed, 1 byte offset
    SBC     <addr>,X        Subtract with Carry, indexed, 2 byte offset
    SBC     <addr8>         Subtract with Carry, direct
    SBC     <addr>          Subtract with Carry, extended

    SEC                     Set carry bit
    SEI                     Set interrupt Mask bit

    STA     #<data>         Store Acc, immediate
    STA     ,X              Store Acc, indexed, no offset
    STA     <addr8>,X       Store Acc, indexed, 1 byte offset
    STA     <addr>,X        Store Acc, indexed, 2 byte offset
    STA     <addr8>         Store Acc, direct
    STA     <addr>          Store Acc, extended

    STOP                    Enable IRQ, Stop Oscillator

    STX     #<data>         Store Index, immediate
    STX     ,X              Store Index, indexed, no offset
    STX     <addr8>,X       Store Index, indexed, 1 byte offset
    STX     <addr>,X        Store Index, indexed, 2 byte offset
    STX     <addr8>         Store Index, direct
    STX     <addr>          Store Index, extended

    SUB     #<data>         Subtract, immediate
    SUB     ,X              Subtract, indexed, no offset
    SUB     <addr8>,X       Subtract, indexed, 1 byte offset
    SUB     <addr>,X        Subtract, indexed, 2 byte offset
    SUB     <addr8>         Subtract, direct


    TASM - Table Driven Assembler Version 2.7                    Page 63

    SUB     <addr>          Subtract, extended

    SWI                     Software Interrupt

    TAX                     Transfer Acc to Index

    TSTA                    Test for neg or zero, accumulator
    TSTX                    Test for neg or zero, index register
    TST     <addr8>         Test for neg or zero, direct
    TST     ,X              Test for neg or zero, indexed, no offset
    TST     <addr8>,X       Test for neg or zero, indexed, 1 byte offset

    TXA                     Transfer Index to Acc

    WAIT                    Enable Interrupt, Stop Processor


    See the manufacturer's data sheets for more information.



    TASM - Table Driven Assembler Version 2.7                    Page 64


    TMS32010 INSTRUCTIONS AND ADDRESSING MODES

    The following list shows the acceptable opcode mnemonics  and  their
    corresponding   operand  formats for the TMS32010   version of TASM.
    The following symbols are used in the table:

            SYMBOLIC            DESCRIPTION
            -----------------------------------------------
            <ar>                Auxiliary register (AR0, AR1)
            <arp>               Auxiliary register pointer
            <dma>               Direct memory address
            <pma>               Program memory address
            <port>              Port address (0 - 7)
            <shift>             Shift count  (0 - 15)
            <const1>            Constant (1 bit)
            <const8>            Constant (8 bit)
            <const13>           Constant (13 bit)

    Any valid TASM expression can appear in the  place  of  any  of  the
    above symbolics.

    OPCODE   OPERAND            DESCRIPTION
    --------------------------------------------------------------------
    ABS                         Absolute value of ACC

    ADD      *+,<shift>,<arp>   Add to ACC with shift
    ADD      *-,<shift>,<arp>
    ADD      *, <shift>,<arp>
    ADD      *+,<shift>
    ADD      *-,<shift>
    ADD      *, <shift>
    ADD      *+
    ADD      *-
    ADD      *
    ADD      <dma>,<shift>
    ADD      <dma>

    ADDH     *+,<arp>           Add to high-order ACC bits
    ADDH     *-,<arp>
    ADDH     *, <arp>
    ADDH     *+
    ADDH     *-
    ADDH     *
    ADDH     <dma>

    ADDS     *+,<arp>           Add to ACC with no sign extension


    TASM - Table Driven Assembler Version 2.7                    Page 65

    ADDS     *-,<arp>
    ADDS     *, <arp>
    ADDS     *+
    ADDS     *-
    ADDS     *
    ADDS     <dma>

    AND      *+,<arp>           AND with ACC
    AND      *-,<arp>
    AND      *, <arp>
    AND      *+
    AND      *-
    AND      *
    AND      <dma>

    APAC                        Add P register to ACC

    B        <pma>              Branch unconditionally
    BANZ     <pma>              Branch on auxiliary register not zero
    BGEZ     <pma>              Branch if ACC >= 0
    BGZ      <pma>              Branch if ACC >  0
    BIOZ     <pma>              Branch on BIO- = 0
    BLEZ     <pma>              Branch if ACC <= 0
    BLZ      <pma>              Branch if ACC <  0
    BNZ      <pma>              Branch if ACC <> 0
    BV       <pma>              Branch on overflow
    BZ       <pma>              Branch if ACC =  0

    CALA                        Call subroutine from ACC
    CALL     <pma>              Call subroutine at <pma>

    DINT                        Disable interrupt

    DMOV     *+,<arp>           Data move in memory
    DMOV     *-,<arp>
    DMOV     *, <arp>
    DMOV     *+
    DMOV     *-
    DMOV     *
    DMOV     <dma>

    EINT                        Enable Interrupt

    IN       *+,<port> ,<arp>   Input data from port
    IN       *-,<port> ,<arp>
    IN       * ,<port> ,<arp>
    IN       *+,<port>


    TASM - Table Driven Assembler Version 2.7                    Page 66

    IN       *-,<port>
    IN       * ,<port>
    IN       <dma>,<port>

    LAC      *+,<shift>,<arp>   Load ACC with shift
    LAC      *-,<shift>,<arp>
    LAC      *, <shift>,<arp>
    LAC      *+,<shift>
    LAC      *-,<shift>
    LAC      *, <shift>
    LAC      *+
    LAC      *-
    LAC      *
    LAC      <dma>,<shift>
    LAC      <dma>

    LACK     <const8>                   Load ACC with 8 bit constant

    LAR      <ar>,*+,<arp>              Load auxiliary Register
    LAR      <ar>,*-,<arp>
    LAR      <ar>,*, <arp>
    LAR      <ar>,*+
    LAR      <ar>,*-
    LAR      <ar>,*
    LAR      <ar>,<dma>

    LARK     <ar>,<const8>              Load aux register with constant
    LARP     <const1>                   Load aux register pointer immed

    LDP      *+,<arp>                   Load data memory page pointer
    LDP      *-,<arp>
    LDP      *, <arp>
    LDP      *+
    LDP      *-
    LDP      *
    LDP      <dma>

    LDPK     <const1>                   Load data page pointer immediate

    LST      *+,<arp>                   Load status from data memory
    LST      *-,<arp>
    LST      *, <arp>
    LST      *+
    LST      *-
    LST      *
    LST      <dma>



    TASM - Table Driven Assembler Version 2.7                    Page 67

    LT       *+,<arp>                   Load T register
    LT       *-,<arp>
    LT       *, <arp>
    LT       *+
    LT       *-
    LT       *
    LT       <dma>

    LTA      *+,<arp>                   Load T register and accumulate
    LTA      *-,<arp>                     product
    LTA      *, <arp>
    LTA      *+
    LTA      *-
    LTA      *
    LTA      <dma>

    LTD      *+,<arp>                   Load T reg, accumulate product,
    LTD      *-,<arp>                     and move
    LTD      *, <arp>
    LTD      *+
    LTD      *-
    LTD      *
    LTD      <dma>

    MAR      *+,<arp>                   Modify auxiliary register
    MAR      *-,<arp>
    MAR      *, <arp>
    MAR      *+
    MAR      *-
    MAR      *
    MAR      <dma>

    MPY      *+,<arp>                   Multiply
    MPY      *-,<arp>
    MPY      *, <arp>
    MPY      *+
    MPY      *-
    MPY      *
    MPY      <dma>

    MPYK     <const13>                  Multiply immediate

    NOP                                 No Operation

    OR       *+,<arp>                   OR  with low order bits of ACC
    OR       *-,<arp>
    OR       *, <arp>


    TASM - Table Driven Assembler Version 2.7                    Page 68

    OR       *+
    OR       *-
    OR       *
    OR       <dma>

    OUT      *+,<port>,<arp>            Output data to port
    OUT      *-,<port>,<arp>
    OUT      *, <port>,<arp>
    OUT      *+,<port>
    OUT      *-,<port>
    OUT      *, <port>
    OUT      <dma>,<port>

    PAC                                 Load ACC with P register
    POP                                 Pop top of stack to ACC
    PUSH                                Push ACC onto stack
    RET                                 Return from subroutine
    ROVM                                Reset overflow mode register

    SACH     *+,<shift>,<arp>           Store ACC high with shift
    SACH     *-,<shift>,<arp>             Note: shift can only be 0, 1,
    SACH     *, <shift>,<arp>                   or 4
    SACH     *+,<shift>
    SACH     *-,<shift>
    SACH     *, <shift>
    SACH     *+
    SACH     *-
    SACH     *
    SACH     <dma>,<shift>
    SACH     <dma>

    SACL     *+,<arp>                   Store ACC low
    SACL     *-,<arp>
    SACL     *, <arp>
    SACL     *+
    SACL     *-
    SACL     *
    SACL     <dma>

    SAR      <ar>,*+,<arp>              Store auxiliary Register
    SAR      <ar>,*-,<arp>
    SAR      <ar>,*, <arp>
    SAR      <ar>,*+
    SAR      <ar>,*-
    SAR      <ar>,*
    SAR      <ar>,<dma>



    TASM - Table Driven Assembler Version 2.7                    Page 69

    SOVM                                Set overflow mode register
    SPAC                                Subtract P register from ACC

    SST      *+,<arp>                   Store status
    SST      *-,<arp>
    SST      *, <arp>
    SST      *+
    SST      *-
    SST      *
    SST      <dma>

    SUB      *+,<shift>,<arp>           Subtract from ACC with shift
    SUB      *-,<shift>,<arp>
    SUB      *, <shift>,<arp>
    SUB      *+,<shift>
    SUB      *-,<shift>
    SUB      *, <shift>
    SUB      *+
    SUB      *-
    SUB      *
    SUB      <dma>,<shift>
    SUB      <dma>

    SUBC     *+,<arp>                   Conditional subtract
    SUBC     *-,<arp>
    SUBC     *, <arp>
    SUBC     *+
    SUBC     *-
    SUBC     *
    SUBC     <dma>

    SUBH     *+,<arp>                   Subtract from high-order ACC
    SUBH     *-,<arp>
    SUBH     *, <arp>
    SUBH     *+
    SUBH     *-
    SUBH     *
    SUBH     <dma>

    SUBS     *+,<arp>                   Subtract from low ACC with
    SUBS     *-,<arp>                     sign-extension suppressed
    SUBS     *, <arp>
    SUBS     *+
    SUBS     *-
    SUBS     *
    SUBS     <dma>



    TASM - Table Driven Assembler Version 2.7                    Page 70

    TBLR     *+,<arp>                   Table Read
    TBLR     *-,<arp>
    TBLR     *, <arp>
    TBLR     *+
    TBLR     *-
    TBLR     *
    TBLR     <dma>

    TBLW     *+,<arp>                   Table Write
    TBLW     *-,<arp>
    TBLW     *, <arp>
    TBLW     *+
    TBLW     *-
    TBLW     *
    TBLW     <dma>

    XOR      *+,<arp>                   Exclusive OR with low bits of ACC
    XOR      *-,<arp>
    XOR      *, <arp>
    XOR      *+
    XOR      *-
    XOR      *
    XOR      <dma>

    ZAC                                 Zero the ACC

    ZALH     *+,<arp>                   Zero ACC and load high
    ZALH     *-,<arp>
    ZALH     *, <arp>
    ZALH     *+
    ZALH     *-
    ZALH     *
    ZALH     <dma>

    ZALS     *+,<arp>                   Zero ACC and load low with
    ZALS     *-,<arp>                     sign extension suppressed
    ZALS     *, <arp>
    ZALS     *+
    ZALS     *-
    ZALS     *
    ZALS     <dma>


    See manufacturer's data for more information.


    TASM - Table Driven Assembler Version 2.7                    Page 71


    TASM DISTRIBUTION FILES

    TASM  is  distributed  in  two  different  packages  - an executable
    package and a source package.  The files  associated  with  each  of
    these are described below:

            EXECUTABLE (SHAREWARE) PACKAGE
            ------------------------------------------------------------
            1.  TASM.EXE          - TASM Assembler, executable
            2.  TASM48.TAB        - 8048 Instruction definition table
            3.  TASM51.TAB        - 8051 Instruction definition table
            4.  TASM65.TAB        - 6502 Instruction definition table
            5.  TASM85.TAB        - 8085 Instruction definition table
            6.  TASM80.TAB        - Z80  Instruction definition table
            7.  TASM05.TAB        - 6805 Instruction definition table
            8.  TASM.DOC          - TASM Documentation
            9.  README            - Brief Explanation of Disk contents
            10. ORDER.FRM         - Order Form
            11. COPYRIGH.T        - Copyright notice

            SOURCE PACKAGE
            ------------------------------------------------------------
            1.  TASM.EXE          - TASM Assembler, executable
            2.  TASM48.TAB        - 8048 Instruction definition table
            3.  TASM51.TAB        - 8051 Instruction definition table
            4.  TASM65.TAB        - 6502 Instruction definition table
            5.  TASM85.TAB        - 8085 Instruction definition table
            6.  TASM80.TAB        - Z80  Instruction definition table
            7.  TASM80.TAB        - 6805 Instruction definition table
            8.  TASM.DOC          - TASM Documentation
            9.  README            - Brief Explanation of Disk contents
            10. ORDER.FRM         - Order Form
            11. COPYRIGH.T        - Copyright notice

            12. TASM.C            - TASM mainline source code
            13. MACRO.C           - Macro expander and other functions
            14. TASM.H            - Header file defining TASM constants
            15. TASM.MAK          - Make file for building TASM

    The  'C'  modules  can  be compiled with the Microsoft 'C' compiler,
    version 5.0   using  the  small  memory  model.  It  should  not  be
    difficult  to use other 'C'   compilers.   See section on  'BUILDING
    TASM  FROM  THE SOURCE CODE'   for  more   information   on    using
    other compilers.



    TASM - Table Driven Assembler Version 2.7                    Page 72


    BUILDING TASM FROM THE SOURCE CODE

    TASM  can  be built using the provided 'make'  file,  assuming   the
    Microsoft C compiler (version 5.0) is available.  The can be done as
    follows:

            make tasm.mak


    For UNIX, try this:

            %cc -DUNIX tasm.c macro.c  -o tasm

    The header file tasm.h should also be available.

    Note  that the UNIX flag is being defined on the command line.  This
    causes the following things to happen:

            1.  Tasm.h includes somewhat different system include files
                    appropriate for the UNIX environment.

            2.  TASM declares a 64 Kbyte array  in  which  to  hold  the
                    assembled    opcodes    and    data  in  a  slightly
                    different way.   MS C must use the 'far' keyword for
                    such  an  array  to give it a segment  all  its  own
                    (assuming use of the small memory model).  Most UNIX
                    environments do not have need for such syntax.



    TASM - Table Driven Assembler Version 2.7                    Page 73


    TASM INSTRUCTION SET TABLE DEFINITION

    The tables that control TASM's interpretation of the source file are
    read from a file at run time.  The table file name is determined  by
    taking  the  numeric option field specified on the TASM command line
    and appending it to the string "TASM", then a  ".TAB"  extension  is
    added.  Thus, if the following command line is entered:

            tasm -51  test.asm

    then TASM would read the table file named "TASM51.TAB".


    The following rules apply to the structure of the table file:

            1.  The  first  line  of  the  file  should contain a string
                    surrounded by double quotes that should identify the
                    version of the assembler  table.  This  string  will
                    appear at the top of each page in the list file.  It
                    should be limited to 24 characters.
            2.  Any line that starts with a '.' is considered a directive.
                    The following directives are available:

                    DIRECTIVE       MEANING
                    ----------------------------------------------------
                    MSFIRST         Generate opcodes MS byte first.
                    ALTWILD         Use '@' instead of '*' as the
                                    wild card in the table.

            3.  Any   line  whose  first  character  is not a '.' and is
                    not  alphabetic is considered to be a comment and is
                    discarded.

            4.  Any  line  that has an alphabetic character as the first
                    character is assumed to be an instruction definition
                    record  and  is  parsed  to   build   the   internal
                    representation   of   the  instruction  set  tables.
                    Eight  fields   (separated  by  white  space)    are
                    expected,  as follows:



    TASM - Table Driven Assembler Version 2.7                    Page 74

                    Field Name      Description
                    --------------------------------------------
                    INSTRUCTION     Instruction Mnemonic
                    ARGS            Argument definition
                    OPCODE          Opcode value
                    NBYTES          Number of bytes
                    MODOP           Modifier operation
                    CLASS           Instruction class
                    SHIFT           Argument left shift count
                    OR              Argument bitwise OR mask

                    INSTRUCTION.  The  INSTRUCTION  field should contain
                    the string to be  used  as  the  mnemonic  for  this
                    instruction.  Upper case letters should be used (the
                    source statements are converted to upper case before
                    comparison).


                    ARGS.   The  ARGS  field  should  contain  a  string
                    describing  the  format  of  the operand field.  All
                    characters are taken literally except the '*'  which
                    denotes  the  presence  of  a valid TASM expression.
                    Multiple '*'s can be used,  but all but the last one
                    must  be  followed  by  a  comma.  If  a  single '*'
                    appears in the ARGS field,  then the default  action
                    of  TASM  will  be  to  determine  the  value of the
                    expression that matches the field and insert one  or
                    two  bytes  of  it into the object file depending on
                    the NBYTES field.  If multiple '*'s are  used,  then
                    special  operators  (MODOP)  must  be  used  to take
                    advantage of them (see the examples below).  An ARGS
                    field of a pair  of  double  quotes  means  that  no
                    arguments are expected.


                    OPCODE.  The OPCODE field should contain the  opcode
                    value    (two  to  six  hex   digits)   for   this
                    instruction  and  address mode.   Each pair  of  hex
                    digits  represent  a  single  byte  of  the  opcode,
                    ordered with the right most pair being placed in the
                    lowest memory location.


                    NBYTES.  The NBYTES field should specify the  number
                    of  bytes  this  instruction  is to occupy (a single
                    decimal  digit).   This number includes both  opcode
                    bytes and argument bytes, thus,  the number of bytes


    TASM - Table Driven Assembler Version 2.7                    Page 75

                    of argument is computed by subtracting the number of
                    bytes  of  opcode  (dictated by the  length  of  the
                    OPCODE field) from NBYTES.


                    MODOP.  The MODOP field determines  if  any  special
                    operations   need   to  be  performed  on  the  code
                    generated for this  instruction.  For  example,  the
                    zero-page  addressing  mode of the 6502 is a special
                    case of the absolute addressing mode, and is handled
                    by a special MODOP code (see appendix B).  The  list
                    of operators is as follows:


                    MODOP       DESCRIPTION
                    ---------------------------------------------------
                    NOTOUCH     Do nothing to instruction or args
                    JMPPAGE     Put bits 8-10 of first arg into
                                bits 5-7 of opcode (8048 JMP)
                    ZPAGE       If arg < 256 then use zero-page (6502)
                    R1          Make arg relative to PC (single byte)
                    R2          Make arg relative to PC (two byte)
                    CREL        Combine LS bytes of first two args
                                making the second one relative to PC
                    SWAP        Swap bytes of first arg
                    COMBINE     Combine LS bytes of first two args into
                                first arg (arg1 -> LSB, arg2 ->MSB).
                    CSWAP       Combine LS bytes of first two args into
                                first arg and swap.
                    ZBIT        Z80 bit instructions.
                    MBIT        Motorola (6805) bit instructions
                    MZERO       Motorola (6805) zero page (direct)
                    3ARG        Three args, one byte each.
                    3REL        Three args, one byte each, last one
                                relative
                    T1          TMS320 instruction with one arg.  Shift
                                according to SHIFT and mask with OR and
                                OR into opcode.  If a second arg exists
                                assume it is an <arp> and OR into   LSB
                                of opcode.
                    TDMA        TMS320 instruction with first arg <dma>.
                                Second arg gets shift/and/or  treatment
                                as with T1.
                    TAR         TMS320 instruction with first arg <ar>.
                                Second arg gets shift/and/or  treatment
                                as with T1.



    TASM - Table Driven Assembler Version 2.7                    Page 76

                    Note  that the reason for the combining of arguments
                    (COMBINE and CSWAP) is that TASM  assumes  that  all
                    object  bytes  to be inserted in the object file are
                    derived from a variable representing  the  value  of
                    the  first  argument (argval).  If two arguments are
                    in the  ARGS  field,  then  one  of  the  previously
                    mentioned  MODOP`s  must  be  used.  They  have  the
                    effect of combining the low bytes of the  first  two
                    arguments  into the variable (argval) from which the
                    object  code  will  be  generated.  TASM`s  argument
                    parsing   routine  can  handle  a  large  number  of
                    arguments,  but the code that generates  the  object
                    code is less capable.

                    CLASS.  The  CLASS  field is used to specify whether
                    this instruction is part of the standard instruction
                    set or a member of a set of  extended  instructions.
                    Bit 0 of this field should be set to denote a member
                    of  the standard instruction set.  Other bits can be
                    used as needed  to  establish  several  classes  (or
                    sets)   of  instructions  that  can  be  enabled  or
                    disabled via  the  '-x'  command  line  option  (see
                    section on 6502 INSTRUCTIONS AND ADDRESSING MODES).

                    SHIFT (optional).   The SHIFT field is used to cause
                    the  first  argument of the given instruction to  be
                    shifted left the specified number of bits.   (Except
                    T1, TDMA, TAR MODOPS as noted below).

                    OR  (optional).   The OR field is used to perform  a
                    bitwise  OR  with  the first argument of  the  given
                    instruction.  Specified as hex digits.  (Except  T1,
                    TDMA, TAR MODOPS as noted below).

    Note that the SHIFT/OR fields are used somewhat differently for  T1,
    TDMA,  and TAR MODOPS.  In those cases,  the SHIFT and OR fields are
    used  but the OR field is really an AND mask and the result is  OR'd
    with the opcode.

    The   following  table   shows   possible    instruction  definition
    records,  followed  by  possible  source statements that would match
    it,    followed by the resulting object code that would be generated
    (in hex):


    TASM - Table Driven Assembler Version 2.7                    Page 77

                                              EXAMPLE         EXAMPLE
    INSTRUCTION DEFINITION                    SOURCE          OBJECT
    -------------------------------------------------------------------
    XYZ  *      FF   3  NOTOUCH 1             xyz 1234h       FF 34 12
    XYZ  *      FF   2  NOTOUCH 1             xyz 1234h       FF 34
    ZYX  *      FE   3  SWAP    1             zyx 1234h       FE 12 34
    ZYX  *      FE   3  R2      1             zyx $+4         FE 01 00
    ABC  *,*    FD   3  COMBINE 1             abc 45h,67h     FD 45 67
    ABC  *,*    FD   3  CSWAP   1             abc 45h,67h     FD 67 45
    ADD  A,#*   FC   2  NOTOUCH 1             add A,#'B'      FC 42
    RET  ""     FB   1  NOTOUCH 1             ret             FB
    LD   IX,*   21DD 4  NOTOUCH 1             ld  IX,1234h    DD 21 34 12
    LD   IX,*   21DD 4  NOTOUCH 1 1 0         ld  IX,1234h    DD 21 68 24
    LD   IX,*   21DD 4  NOTOUCH 1 0 1         ld  IX,1234h    DD 21 35 12
    LD   IX,*   21DD 4  NOTOUCH 1 1 1         ld  IX,1234h    DD 21 69 24
    LD   IX,*   21DD 4  NOTOUCH 1 8 12        ld  IX,34h      DD 21 12 34

    See Appendix B for more examples.

    The  order  of  the  entries for various addressing modes of a given
    instruction is important.  Since the wild card matches anything,  it
    is  important to specify the ARGS for the addressing modes that have
    the  most  qualifying  characters  first.   For   example,   if   an
    instruction  had  two  addressing  modes,   one  that  accepted  any
    expression,  and another that required a pound sign in front  of  an
    expression,  the  pound  sign  entry  should  go first otherwise all
    occurrences of the instruction would match  the  more  general  ARGS
    expression   that  it  encountered  first.   The  following  entries
    illustrate the proper sequencing:

            ADD #*  12 3 NOTOUCH 1
            ADD *   13 3 NOTOUCH 1



    TASM - Table Driven Assembler Version 2.7                    Page 78


    APPENDIX A - SAMPLE LISTING FILE

    The listing was generated by issuing the command:
            tasm -65 -p -l -h -f00 t.asm

    TASM 6502 Assembler.            t.asm                         page 1
    Speech Technology Incorporated.

    0001   0000             ;This is a simple example of an assembly
    0002   0000             ;include a file just for fun
    0003   0000             #include        "include.h"
    0001+  0000             ;this is just a simple include file
    0002+  0000             exit    .equ    7e00h
    0003+  0000             ;
    0004+  0000             ; That's all
    0004   0000             ;
    0005   0000             ; define two byte increment macro
    0006   0000             #define INCZ(p) ldx #p\ inc 0,x\ bne $+4\ inc 1,x
    0007   0000             ;
    0008   0000             start   .org    $0
    0009   0000             mask    .equ    $5678
    0010   0000
    0011   0000 0A          byte1   .byte   10
    0012   0001 D2 04       word1   .word   1234
    0013   0003 34 12       word2   .word   $1234
    0014   0005             ;skip past a few locations to start code
    0015   0020                     .org    $0020
    0016   0020             begin
    0017   0020             ;     let's just increment word1 the number
    0018   0020             ;     of times indicated by byte1 (use the
    0019   0020             ;     double byte increment macro INCZ).
    0020   0020             loop1
    0021   0020 A2 01               ldx #word1\ inc 0,x\ bne $+4\ inc 1,x
    0021   0022 F6 00
    0021   0024 D0 02
    0021   0026 F6 01
    0022   0028 C6 00               dec     byte1   ;decrement the count
    0023   002A D0 F4               bne     loop1   ;loop until zero
    0024   002C
    0025   002C             ; Now  let's just do some simple arithmetic
    0026   002C A5 56               lda     (mask >> 8)
    0027   002E AD 00 56            lda     (mask & 0ff00h)
    0028   0031 A5 57               lda     ((mask >> 8) & 0ffh) + word1
    0029   0033 4C 00 7E            jmp     exit
    0030   0036                     .end


    TASM - Table Driven Assembler Version 2.7                    Page 79



    Label        Value      Label        Value      Label        Value
    ------------------      ------------------      ------------------
    exit          7E00      start         0000      mask          5678
    byte1         0000      word1         0001      word2         0003
    begin         0020      loop1         0020

    ADDR  00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E 0F
    -----------------------------------------------------
    0000  0A D2 04 34 12 00 00 00 00 00 00 00 00 00 00 00
    0010  00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00
    0020  A2 01 F6 00 D0 02 F6 01 C6 00 D0 F4 A5 56 AD 00
    0030  56 A5 57 4C 00 7E 00 00 00 00 00 00 00 00 00 00

    tasm: Number of errors = 0



    TASM - Table Driven Assembler Version 2.7                    Page 80


    APPENDIX B - SAMPLE INSTRUCTION DEFINITION TABLE (TASM65.TAB)

    "TASM 6502 Assembler.    "
    /* This is the instruction set definition table
    /*   for the 6502 version of TASM.
    /*      Thomas N. Anderson, Speech Technology Incorporated, Feb 1986.
    /*  First line of this file is a banner that will appear at the
    /*  top of each page of the TASM listing file (not the same as
    /*  the TITLE).  Should be limited to 24 characters.
    /*  Any other line that does not start with an upper case letter is
    /*  ignored.
    /*  See TASM manual for info on table structure.
    /*  Note that there are two classes of extended instructions beyond
    /*    the standard set.  The classes are assigned bits as follows:
    /*      bit 0 = standard set
    /*      bit 1 = extended instructions for R65C02
    /*      bit 2 = extended instructions for R65C00/21
    /*
    /*INSTR ARGS OPCODE BYTES MOD CLASS SHIFT OR */
    /*-------------------------------------------*/
    ADC  #*     69    2  NOP 1
    ADC  (*,X)  61    2  NOP 1
    ADC  (*),Y  71    2  NOP 1
    ADC  (*)    72    2  NOP 2   /* R65C02 */
    ADC  *,X    7D    3  ZP  1
    ADC  *,Y    79    3  NOP 1
    ADC  *      6D    3  ZP  1

    AND  #*     29    2  NOP 1
    AND  (*,X)  21    2  NOP 1
    AND  (*),Y  31    2  NOP 1
    AND  (*)    32    2  NOP 2   /* R65C02 */
    AND  *,X    3D    3  ZP  1
    AND  *,Y    39    3  NOP 1
    AND  *      2D    3  ZP  1

    ASL  A      0A    1  NOP 1
    ASL  *,X    1E    3  ZP  1
    ASL  *      0E    3  ZP  1

    BCC  *      90    2  R1  1
    BCS  *      B0    2  R1  1
    BEQ  *      F0    2  R1  1
    BNE  *      D0    2  R1  1
    BMI  *      30    2  R1  1
    BPL  *      10    2  R1  1


    TASM - Table Driven Assembler Version 2.7                    Page 81

    BVC  *      50    2  R1  1
    BVS  *      70    2  R1  1

    BIT  #*     89    2  NOP 2
    BIT  *,X    3C    3  ZP  2
    BIT  *      2C    3  ZP  1

    BRK  ""     00    1  NOP 1

    CLC  ""     18    1  NOP 1
    CLD  ""     D8    1  NOP 1
    CLI  ""     58    1  NOP 1
    CLV  ""     B8    1  NOP 1
    CMP  #*     C9    2  NOP 1
    CMP  (*,X)  C1    2  NOP 1
    CMP  (*),Y  D1    2  NOP 1
    CMP  (*)    D2    2  NOP 2
    CMP  *,X    DD    3  ZP  1
    CMP  *,Y    D9    3  NOP 1
    CMP  *      CD    3  ZP  1

    CPX  #*     E0    2  NOP 1
    CPX  *      EC    3  ZP  1
    CPY  #*     C0    2  NOP 1
    CPY  *      CC    3  ZP  1

    DEC  A      3A    3  NOP 2
    DEC  *,X    DE    3  ZP  1
    DEC  *      CE    3  ZP  1

    DEX  ""     CA    1  NOP 1
    DEY  ""     88    1  NOP 1

    EOR  #*     49    2  NOP 1
    EOR  (*,X)  41    2  NOP 1
    EOR  (*),Y  51    2  NOP 1
    EOR  (*)    52    2  NOP 2
    EOR  *,X    5D    3  ZP  1
    EOR  *,Y    59    3  NOP 1
    EOR  *      4D    3  ZP  1

    INC  A      1A    3  NOP 2
    INC  *,X    FE    3  ZP  1
    INC  *      EE    3  ZP  1

    INX  ""     E8    1  NOP 1
    INY  ""     C8    1  NOP 1


    TASM - Table Driven Assembler Version 2.7                    Page 82


    JMP  (*,X)  7C    3  NOP 2
    JMP  (*)    6C    3  NOP 1
    JMP  *      4C    3  NOP 1

    JSR  *      20    3  NOP 1

    LDA  #*     A9    2  NOP 1
    LDA  (*,X)  A1    2  NOP 1
    LDA  (*),Y  B1    2  NOP 1
    LDA  (*)    B2    2  NOP 2
    LDA  *,X    BD    3  ZP  1
    LDA  *,Y    B9    3  NOP 1
    LDA  *      AD    3  ZP  1

    LDX  #*     A2    2  NOP 1
    LDX  *,Y    BE    3  ZP  1
    LDX  *      AE    3  ZP  1

    LDY  #*     A0    2  NOP 1
    LDY  *,X    BC    3  ZP  1
    LDY  *      AC    3  ZP  1

    LSR  A      4A    1  NOP 1
    LSR  *,X    5E    3  ZP  1
    LSR  *      4E    3  ZP  1

    NOP  ""     EA    1  NOP 1

    ORA  #*     09    2  NOP 1
    ORA  (*,X)  01    2  NOP 1
    ORA  (*),Y  11    2  NOP 1
    ORA  (*)    12    2  NOP 2
    ORA  *,X    1D    3  ZP  1
    ORA  *,Y    19    3  NOP 1
    ORA  *      0D    3  ZP  1

    PHA  ""     48    1  NOP 1
    PHP  ""     08    1  NOP 1
    PLA  ""     68    1  NOP 1
    PLP  ""     28    1  NOP 1

    ROL  A      2A    1  NOP 1
    ROL  *,X    3E    3  ZP  1
    ROL  *      2E    3  ZP  1

    ROR  A      6A    1  NOP 1


    TASM - Table Driven Assembler Version 2.7                    Page 83

    ROR  *,X    7E    3  ZP  1
    ROR  *      6E    3  ZP  1

    RTI  ""     40    1  NOP 1
    RTS  ""     60    1  NOP 1

    SBC  #*     E9    2  NOP 1
    SBC  (*,X)  E1    2  NOP 1
    SBC  (*),Y  F1    2  NOP 1
    SBC  (*)    F2    2  NOP 2
    SBC  *,X    FD    3  ZP  1
    SBC  *,Y    F9    3  NOP 1
    SBC  *      ED    3  ZP  1

    SEC  ""     38    1  NOP 1
    SED  ""     F8    1  NOP 1
    SEI  ""     78    1  NOP 1

    STA  (*,X)  81    2  NOP 1
    STA  (*),Y  91    2  NOP 1
    STA  (*)    92    2  NOP 2
    STA  *,X    9D    3  ZP  1
    STA  *,Y    99    3  NOP 1
    STA  *      8D    3  ZP  1

    STX  *,Y    96    2  ZP  1
    STX  *      8E    3  ZP  1

    STY  *,X    94    2  NOP 1
    STY  *      8C    3  ZP  1

    TAX  ""     AA    1  NOP 1
    TAY  ""     A8    1  NOP 1
    TSX  ""     BA    1  NOP 1
    TXA  ""     8A    1  NOP 1
    TXS  ""     9A    1  NOP 1
    TYA  ""     98    1  NOP 1

    /* Here are the extended instructions that are totally new */

    BRA  *      80    2  R1  6

    BBR0 *,*    0f    3  CR  6
    BBR1 *,*    1f    3  CR  6
    BBR2 *,*    2f    3  CR  6
    BBR3 *,*    3f    3  CR  6
    BBR4 *,*    4f    3  CR  6


    TASM - Table Driven Assembler Version 2.7                    Page 84

    BBR5 *,*    5f    3  CR  6
    BBR6 *,*    6f    3  CR  6
    BBR7 *,*    7f    3  CR  6

    BBS0 *,*    8f    3  CR  6
    BBS1 *,*    9f    3  CR  6
    BBS2 *,*    af    3  CR  6
    BBS3 *,*    bf    3  CR  6
    BBS4 *,*    cf    3  CR  6
    BBS5 *,*    df    3  CR  6
    BBS6 *,*    ef    3  CR  6
    BBS7 *,*    ff    3  CR  6

    MUL  ""     02    1  NOP 4  /* R65C00/21 only*/

    PHX  ""     da    1  NOP 6
    PHY  ""     5a    1  NOP 6
    PLX  ""     fa    1  NOP 6
    PLY  ""     7a    1  NOP 6

    RMB0 *      07    2  NOP 6
    RMB1 *      17    2  NOP 6
    RMB2 *      27    2  NOP 6
    RMB3 *      37    2  NOP 6
    RMB4 *      47    2  NOP 6
    RMB5 *      57    2  NOP 6
    RMB6 *      67    2  NOP 6
    RMB7 *      77    2  NOP 6

    SMB0 *      87    2  NOP 6
    SMB1 *      97    2  NOP 6
    SMB2 *      a7    2  NOP 6
    SMB3 *      b7    2  NOP 6
    SMB4 *      c7    2  NOP 6
    SMB5 *      d7    2  NOP 6
    SMB6 *      e7    2  NOP 6
    SMB7 *      f7    2  NOP 6

    /* The following extended instructions are available on the
            R65C02 but not the R65C00/21 */

    STZ  *,X    9e    3  ZP  2
    STZ  *      9c    3  ZP  2

    TRB  *      1c    3  ZP  2
    TSB  *      0c    3  ZP  2



    TASM - Table Driven Assembler Version 2.7                    Page 85


    APPENDIX C - ORDERING INFORMATION

    TASM    is  distributed as shareware.    The shareware  portion   of
    the  product may be freely copied and used for evaluation  purposes.
    Use  of   TASM  beyond  a  reasonable  evaluation  period   requires
    registration. Registered  users  receive the following benefits:

            1.  The recent version of TASM.
            2.  TASM source code (in C).
            3.  Bound TASM manual.
            4.  Telephone support.
            5.  Knowledge that they are supporting  the  development  of
                    useful but inexpensive software.

    DESCRIPTION                             UNIT PRICE            PRICE
    --------------------------------------------------------------------
    TASM Registration (TASM, manual, & source)  $30.00           _______

    TASM User's Manual (included above)          10.00           _______

    TASM update for registered users             10.00           _______
       (latest source, executable, and manual)

    TASM shareware disk                          10.00           _______

    Subtotal                                                     _______

    Tax (Washington state residents add 8.1%)                    _______

    Foreign postage (outside North America) add $10.00           _______
      (Foreign orders must be in US funds drawn on a US bank).

    TOTAL (post paid)                                            _______

    Shipping Address: __________________________________________________

                      __________________________________________________

                      __________________________________________________

    Send check or money order (no credit cards) to: Speech Technology Inc.
                                                    Software Division
                                                    837 Front Street South
                                                    Issaquah,  WA  98027