Chapter12               L.O.V.E. FORTH



12.0 8086/8 Register Usage
     ---------------------

The register usage is summarised as follows:

     SI - Forth interpretive pointer (IP)
     SP - Parameter stack    }  sometimes these pointers are
     BP - Return stack       }           exchanged

     CS - Points to code segment CS:
     DS - Points to thread segment TS:
     SS - Points to stack segment SS:
     ES - Points to variable segment VS:

     DI - reserved for use as local variable stack pointer

     On entry to a word:

     BX - points to the compilation address of the word being
                     executed
     AX - is destroyed between words
     CX, DX - may be used as scratch registers


12.1 Kernel examples of register usage
     ---------------------------------

CODE LIT     ( -- N )
      WORD LODS   AX PUSH   NEXT-JMP C;

( LODS  always loads relative to DS = TS: )
( PUSH  stores relative to SS )
( all code executes relative to CS )

CODE @
     BX POP   ES: [BX] PUSH   NEXT-JMP C;
( POP   always loads relative to SS )
( [BX]  must be overridden to fetch from ES: )
(   PUSH always relative to SS)

CODE FILL            ( addr, count, value -- )
    DX, DI MOV                             ( save value of DI )
    AX POP    CX POP    DI POP             ( get parameters)
    AH, AL MOV  CX, 1 SHR                  ( odd number of bytes ?)
    IFU< BYTE STOS ( odd # bytes )  THEN   ( store odd one)
    REP WORD STOS                          ( store the remainder)
    DI, DX MOV NEXT-JMP C;                 ( restore DI)

( POP   always loads relative to SS )
( STOS  always stores relative to ES  = VS: )