Chapter14               L.O.V.E. FORTH



14.0 RPN Assembler
     -------------

	This is a classic Forth assembler that utilizes   RPN   syntax.
During assembly, the arguments and opcodes are executed to produce
instructions which are added to the code segment.  Those who prefer normal
assembler syntax should use the newer third party assembler facility.  This
RPN assembler is included only for older code, or code appearing on
screens.

	Though this assembler is large, this penalty is minimized by
including it as a virtual vocabulary.  When the interpreter encounters
either the  word   CODE   or   ;CODE, the assembler will be called into
upper memory and the assembling of code will start.  When no longer needed,
it can be removed by the word   FORGET-SYS.  It is automatically removed by
SAVE"   or any word that calls another virtual subsystem.

	It is assumed that the user has access to an 8086/8088 handbook
such as:  "iAPX 86,88 User's Manual" by Intel Corporation or "THE 8086 BOOK
includes the 8088" by R.Rector and G.Alexy, OSBORNE/McGraw-Hill (though the
latter has many errors).


14.1 Using the RPN assembler
     -----------------------

	Normally the external assembler/linker is provided for assembling
code. In order for the RPN assembler to be used, it must be loaded in. The
source code is provided for this.  Type the following:
    INCLUDE"   LOADRASM.TXT"   (enter)
To make the change permanent, simply save the forth system with
    SAVE"   filename.EXE"


14.2 Format for Code Words
     ---------------------
	Assembling is initiated by either   CODE   or   ;CODE   and
terminated by  C;  (or its alias  END-CODE ).   The exit point(s) in a code
NEXT-JMP   assembles the following in-line code:

           WORD LODS  BX, AX MOV  WORD [BX] JMP

The following are examples of usage:

CODE U/MOD BX POP  DX POP  AX POP  DX, BX CMP
           IFU<  BX DIV DX PUSH APUSH-JMP
           THEN  AX, # -1 MOV  AX PUSH  APUSH-JMP C;

: CONSTANT CREATE: TS:,
    ;CODE
           2 [BX] PUSH  NEXT-JMP C;


14.3 Logical Operators
     -----------------
	Logical operators have been added to the Assembler to simplify
writing and reading the assembly code.  They also obviate labels and
forward referencing.  The logical test words can be used after any
operation code, that causes the appropriate status flags to be set or
cleared; i.e.  CMP   CMPS   OR    ADD   SUB   etc.

	With the exception of   REPEAT   and   AGAIN ,  which assemble
unconditional signed relative two-byte jumps, these logical operators
assemble one-byte jumps.  The assembler will detect an attempt to assemble
an  out-of-range jump, and will print an appropriate error message, and
stop assembling.


		DO .. LEAVE .. LOOP.   This construct differs from the high-level
FORTH construct in that only one argument is used.  The  CX  register must
contain the count upon reaching   LOOP.  The   LEAVE operation will set the
CX register to 1 which is first decremented upon reaching LOOP; then, an
exit from the   LOOP   is made if the  CX register is 0.  If the  CX
register is not 0 upon reaching   LOOP,  the program counter will be set to
the instruction just after  DO.  The count placed in the  CX register  can
vary from 1 to FFFF (65535 decimal).  The following is a simple
illustration of usage:

( starting at addr, searches n bytes for char)
( addr  n  char  ---  addr -1  or  0 )
CODE CHARSRCH
     AX POP  CX POP  DX, DI MOV  DI POP
     DO  SCAS
        IF= DI DEC  DI PUSH  DI, DX MOV  AX, # -1 MOV  APUSH-JMP
        THEN
     LOOP  CX PUSH  DI, DX MOV  NEXT-JMP C;

	The sequence: 	IF=
			IF<
			IF0<
			IFU< ... ELSE ... THEN
will calculate the relative one-byte jumps and assemble the appropriate
code, ie.  JNZ    JNL    JNB    or   JMP .    The IF operators can be used
after any operation that sets the appropriate flags.  (Note that
AX, AX OR   has the same effect as AX, # 0 CMP but requires one less cycle).

	If the logical test is immediately followed by the word 'non'
('not' was not used to avoid conflict with the  NOT  op code), the test is
negated.  For example,  AX, BX CMP  IF= non ... would perform the operation
following IF=  if the  AX  and the  BX  registers were not equal.

The following are examples of usage.

CODE MAX  AX POP  BX POP  AX, BX CMP
          IF< BX PUSH  ELSE  AX PUSH  THEN NEXT-JMP C;

CODE U<   CX POP  BX POP  AX, AX XOR  BX, CX CMP
          IFU< AX DEC THEN  APUSH-JMP C;

CODE ABS  AX POP  AX, AX OR
          IF0< AX NEG THEN  APUSH-JMP C;

CODE DIGIT DX POP  BX POP  AX, AX XOR  BL, # 48 SUB
          IF< non  BL, # 10 CMP
             IF< non BL, # 7 CMP
                IF<  APUSH-JMP THEN
             THEN BL, DL CMP
             IF< AX DEC  DX, DX XOR DL, BL MOV  DX PUSH
             THEN
          THEN APUSH-JMP C;

	In a similar manner, the following logical sequences will compile
the appropriate offsets and jump codes.

BEGIN .. AGAIN
BEGIN .. UNTIL= (or) UNTIL< (or) UNTILU< (or) UNTIL0<
BEGIN .. WHILE= (or) WHILE< (or) WHILEU< (or) WHILE0< ... REPEAT


	Because the operation code word   TEST   produces a logical result,
that appears to be the reverse of the foregoing conditional branch words, a
separate set of words are provided to replace them, namely:   IFTEST
 IFNOTEST,   WHILETEST,   WHILENOTEST.    Do not use the word 'non' to
negate these words. For example   IFNOTEST   is the negative of  IFTEST.

	The following word from the   EDITOR   illustrates a combined usage
of these operators.  The word <#SPCS?> will determine the number of blank
spaces at the end of a 64 character line on the display.  The operation is
performed during retrace cycles.

( L#ADDR X-offset llength -- n )
CODE <#SPCS?>
  -2 [BP], DI MOV
  CX POP  AX POP  AX, CX ADD  AX, 1 SHL  AX DEC
  DI POP  ES PUSH  ES: DX, CRTPORT MOV  ES: ES, CRTSEG MOV
  DI, AX ADD  BX, BX XOR  STD
   BEGIN  DI DEC  CX DEC
      BEGIN  AL, DX IN  AL, # 1 TEST  UNTILNOTEST  CLI
      BEGIN  AL, DX IN  AL, # 1 TEST  UNTILTEST    AL, # 20 MOV  SCAS
      IF=  BX INC  ELSE  CX, CX XOR  THEN  CX, # 0 CMP
   UNTIL=  CLD  STI  ES POP  BX PUSH
   DI, -2 [BP] MOV  NEXT-JMP C;


14.4 Assembler Addressing
     --------------------

	The following nomenclature is used in defining the arguments for
the assembler operation codes:

        ac      = AX or AL

        reg     = AX AH AL BX BH BL CX CH CL DX DH DL SI DI BP or SP

        mem/reg = any register, a direct memory address,
                  [BX+SI] [BX+DI] [BP+SI] [BP+DI] [SI] [DI]
                  [BX] [BP], or any bracketed expression plus a
                  preceding displacement.

        port    = a number, 0 through FFFF (hex)

        data    = a number, 0 through FFFF (hex)

        segreg  = CS DS ES or SS

        size    = BYTE  or WORD  (if unspecified, BYTE is assumed)

        n       = 0 to FF (hex)


14.5 Assembler operation codes
     -------------------------

	On the following page are the operation codes that can be assembled
by the assembler, and the required formats for the arguments.  Note that
the symbol # followed by a space must precede data.  Also, when two
arguments are used, they must be separated by a comma followed by a space.
If a register is the first argument, the comma is part of the register
label, eg:

                AX, BX MOV
	If the first argument is a number for a port or an address, a space
must precede the comma, eg.
                0FE42 , BX MOV.

	Where there is a one-byte versus two-byte ambiguity, the default is
one byte. To force a two-byte operation, precede the operation code with
the word  WORD   eg.
                WORD [BX] NEG.

	Note that when using addresses with   JMPs   and   CALLs   the best
size offset (8 or 16 bit) is selected by the assembler.  To specify
intersegment  JMPs,  CALLs  +RETs  and RETs  the prefix FAR is used.

   For example:

    to perform an intersegment indirect branch, the following sequence
    is used:

         FAR  [BX]  JMP
    When   FAR   is not used an intrasegment branch is assumed.


	Segment overrides are specified by placing  CS:  DS:  ES:  or  SS:
in front of the operation they are to modify.

Before exiting from a code word via   NEXT-JMP   you must restore the
following registers to the values they had upon entry to the routine:
                SI, DI
                CS, DS, SS, ES
The flags DF, IM must both be restored with the instructions:
                STI and CLD.
The following registers must not have unreasonable changes:
                SP, BP
For more information on register usage see the implementation notes.


14.6 Assembler LABELs
     ----------------

	In order to create branching or other labels within a code word,
the declaration   LABEL   can be used.  This creates a  CONSTANT based on
the current code segment dictionary pointer.  This can be refered to in
high-level Forth.  This relies on the L.O.V.E. Forth characteristic, that
CONSTANTS only add code to the thread and head segments.

      Example:

     CODE S>D        ( signed conversion ( n -- d )
        AX POP  CWD
         LABEL DXAX-PUSH ( push dx and ax )
          DX PUSH  AX PUSH  NEXT-JMP C;

CODE D2*   ( double double ( d-- d)
   AX POP  DX POP  DX, 1 SHL  AX, 1 ROL  DXAX-PUSH JMP C;


14.7 Operation Codes
     ---------------

      AAA                     AAD                     AAM
                AAS
     ac, # data ADC     mem/reg, # data ADC *  mem/reg, mem/reg ADC
     ac, # data ADD     mem/reg, # data ADD *  mem/reg, mem/reg ADD
     ac, # data AND     mem/reg, # data AND *  mem/reg, mem/reg AND
       address CALL            mem/reg CALL                     CBW
                CLC                     CLD                     CLI
                CMC
     ac, # data CMP     mem/reg, # data CMP *  mem/reg, mem/reg CMP
          size CMPS                     CWD                     DAA
                DAS                 reg DEC             mem/reg DEC *
        mem/reg DIV *                   HLT            mem/reg IDIV *
       mem/reg IMUL *             ac, DX IN             ac, port IN
            reg INC             mem/reg INC *                 n INT
               INTO                    IRET
         address JA             address JAE              address JB
        address JBE            address JCXZ              address JE
         address JB             address JGE              address JL
        address JLE             address JMP             mem/reg JMP
        address JNA            address JNAE             address JNB
       address JNBE             address JNE             address JNG
       address JNGE             address JNL            address JNLE
        address JNO             address JNP             address JNS
        address JNZ              address JO              address JP
        address JPE             address JPO              address JS
        address JZ                     LAHF
   reg, mem/reg LDS        reg, mem/reg LES        reg, mem/reg LEA
               LOCK               size LODS            address LOOP
     address LOOPNE          address LOOPNZ           address LOOPZ
    reg, # data MOV     mem/reg, # data MOV *  mem/reg, mem/reg MOV
    ac, address MOV     segreg, mem/reg MOV     mem/reg, segreg MOV
   address , ac MOV               size MOVS             mem/reg MUL *
        mem/reg NEG *                   NOP             mem/reg NOT *
      ac, # data OR      mem/reg, # data OR *   mem/reg, mem/reg OR
         DX, ac OUT           port , ac OUT
            reg POP             mem/reg POP     segreg (not CS) POP
               POPF                   PUSHF
           reg PUSH            mem/reg PUSH             segreg PUSH
     mem/reg, 1 RCL *       mem/reg, CL RCL *
     mem/reg, 1 RCR *       mem/reg, CL RCR *
                REP                    REPE                   REPNE
              REPNZ                    REPZ                     RET
     mem/reg, 1 ROL *       mem/reg, CL ROL *
     mem/reg, 1 ROR *       mem/reg, CL ROR *
               SAHF
     mem/reg, 1 SAL *       mem/reg, CL SAL *
     mem/reg, 1 SAR *       mem/reg, CL SAR *
     ac, # data SBB     mem/reg, # data SBB *  mem/reg, mem/reg SBB
          size SCAS
     mem/reg, 1 SHL *       mem/reg, CL SHL *
     mem/reg, 1 SHR *       mem/reg, CL SHR *
                STC                     STD                     STI
          size STOS
     ac, # data SUB     mem/reg, # data SUB *  mem/reg, mem/reg SUB
    ac, # data TEST    mem/reg, # data TEST *     reg, mem/reg TEST
               WAIT            AX, reg XCHG       reg, mem/reg XCHG
               XLAT
     ac, # data XOR     mem/reg, # data XOR *  mem/reg, mem/reg XOR
             n +RET
* these operations require a size   BYTE,  WORD   when the operand is
  a memory location(s).