John Lewkowicz
       New York State College of Veterinary Medicine
                     Cornell University
                     Ithaca, N.Y. 14853


                       Copyright 1986





Permission is hereby granted to  copy  and  distribute  this
document  and  the  programs/data bases described herein for
any non-commercial purpose. Any use  of  this  material  for
commercial  advantage  without  the prior written consent of
the author is prohibited.












































                        Introduction

     This utility package is a unified collection  of  MUMPS
programs designed to aid programmers in developing and main-
taining MUMPS programs  and  data  bases.  It  provides  for
creating, editing, listing, saving, restoring and killing of
both routines and globals in a single interactive package.

To invoke any of the utility functions, issue the command:
                           DO ^%M

while in direct mode. The first time the program is  run  on
any  system  it will automatically initialize all data bases
and ask for various default conditions.

     This  package  was  designed  specifically  to  run  on
MicroMUMPS  developed  at  UC  Davis  by Dr. Walters and his
associates. It is written in standard MUMPS but makes use of
many  special  Z-extensions to the language provided by that
implementation. In addition, it  is  set  up  to  run  in  a
single-user  environment,  since none of the scratch globals
support multiple users.

     All programs and globals in the utility  package  begin
with  the  characters  %M, as will any future extensions. No
data bases are needed initially  since  any  necessary  ones
(such  as  the  terminal  definition  global  %MTC)  will be
created for you the first time the package is executed.  Try
to  avoid  creating  programs  or routines starting with %M,
since they might conflict with  future  expansions  of  this
utility package.

     All terminal I/O (including Console,  Printer,  Sequen-
tial MSDOS files, etc) is coordinated via a terminal defini-
tion program and data base to  provide  considerable  device
independence.  This package makes use of many special termi-
nal characteristics (such as High and Low intensity) if they
are  available.  You  can  use one of the initial options to
define or modify new terminals and to tie a  given  terminal
type  to a specific I/O port. The first time this package is
run, neutral default definitions are used, but you can  pick
the  Terminal  option to Define/Tie a new definition to your
Console  or  Printer.  This  reconfiguration  will   improve
interactions with the program.

     A special feature available when  Saving  or  Restoring
either  Routines  or Globals is that they can be transmitted
between computers by directing Input/Output of the Save file
to MicroMUMPS device number 5.  The user need only establish
a hardware link via the communications port and %M will han-
dle all the rest.


                           2

            







MicroMUMPS Utilities                      Cornell University


     %M also supports multiple  volume  global  saves  which
permit  saving  large  data  bases  on  multiple floppy disk
volumes. Routine saves are still output  to  single  volumes
since it is assumed the programmer can subdivide routines to
distribute them on more than one floppy disk.

Standard Conventions

     There are a number of keyboard and  name  specification
standards  that  are  available in this package. Some of the
conventions are always in effect (like ?  and  ??),  whereas
others  (such  as  ?L)  are  only  available  when logically
needed.

? and ?? can be used to answer any question in  the  package
   to  get  additional HELP on how to answer that particular
   question. A single question mark (?)  will  get  you  one
   line  of  abbreviated  help.  A double question mark (??)
   will get you the same abbreviated HELP line together with
   any extended help available.

^       always lets you back up to the previous question  or
   set of questions.

: and ::  Whenever you see a ":", in indicates that the pro-
   gram  is  waiting  for  a  keyboard entry. A double colon
   ("::") is displayed whenever a default  answer  has  been
   supplied  for you. If a default answer has been supplied,
   you can accept it by pressing the <RETURN> key.

"?L" can be entered (when appropriate) to  get  a  directory
   listing  (either routines or globals depending on earlier
   choices). This option is available on all routine or glo-
   bal name specification questions.

"?S"    is similar to "?L" except that  it  lists  only  the
   selected  routine  or  global  names  (more  on selection
   later).

   Routine/Global Name entry -  when  selecting  routine  or
   global  names  (i.e.,  to  flag them for listing, saving,
   restoring, etc), you can either enter specific names (one
   at  a time) or use the ``wild card'' characters ``*'' and
   ``?''. The ? character in a name  represents  any  single
   character,  whereas the * character represents any number
   of characters. For example:

   ``A*B"  selects all names starting with ``A'' and  ending
      with the character ``B'' regardless of name length.

   ``A?B'' selects all three-character names  starting  with
      ``A'' and ending with ``B.''

  

                             3







MicroMUMPS Utilities                      Cornell University


   Combinations of the above are allowed, but avoid the spe-
   cial  cases  of  ?,  ??,  ?L and ?S as they conflict with
   other conventions already discussed.

   The ' (not) character is used to de-select  one  or  more
   names from the list already specified. For example,

   A*      selects all names starting with ``A''
   A1*     subsequently de-selects  all  names  within  that
      subset that start with the characters A1.

Global Reference - when working on globals,  often  you  are
   given  the option to specify an individual global or part
   of a global. This option is  used  instead  of  the  name
   question  to  permit  you  to  pick  individual  nodes or
   branches of a global (e.g., to list or  edit  part  of  a
   global)  rather  than  groups of global names (e.g., when
   saving or restoring  globals).  When  entering  a  Global
   Specification, the following rules apply:

NAME ONLY (^XYZ) implies that you want to process the entire
      global
FULL Reference (^XYZ(1,"ABC",2)) implies that  you  want  to
      work on that node only.
PARTIAL REFERENCE (^XYZ(1, or ^XYZ(1   )  implies  that  you
      want to work on that node and all of its descendants.





























                               4







MicroMUMPS Utilities                      Cornell University


              Functional Descriptions - Routines
Directory
      A directory of all  routines is  maintained  in  ^%MU.
This directory is updated when editing, restoring or killing 
routines. If you choose the option to refresh the directory,  
a temporary MSDOS file SCRATCH.DAT is created and killed  in 
the process of creating the new  directory. You  may specify 
the Drive and output device for the directory.

Edit
      An option used to create and edit routines.  The rou-
tine to be edited is loaded into a scratch global ^%MRE and 
all edit operations are performed on that global.  The rou-
tine on disk is NOT updated until you  give  the editor the 
File command.  When specifying a  name  to  be  edited, you 
can enter an asterisk (*) to  indicate that you wish to use 
the routine currently in ^%MRE, thereby saving load time.

      The editor also allows you to enter  COMMENTS  associ-
ated with labels in a routine. These comments are held in %M 
and  do  NOT  take  up  partition  space when the program is 
executed.  They can be printed with the program  when  using 
the List option.  They can also be Saved and  Restored along 
with the routines.

      To Enter/Edit comments for a given label in  the  rou-
tine being edited, simply enter a semicolon  and  the  Label 
name when the editor is looking for a command (eg, you could 
enter ':LABEL' to Enter/Edit comments for the label LABEL).

List
      This  option allows you to list  routines  (optionally
with their comments) on the device of your choice. NOTE that 
you will want to use the terminal definition option to esta-
blish the  parameters of  your devices  (printer, etc.).  If 
output is to the console or any CRT device, the program will 
pause with a keyboard read at the end of each page.

Find
      This command allows  you to search  for  one  or  more
strings (or patterns) in a specified set of selected routines. 
You specify where the search results are to be directed. (If 
a CRT, the program pauses at the end of each page).

Change
      Change  allows you to change one or more strings in  a
specified set  of routines to new strings.  Output  trace of 
the  changes can  be directed  to the device of your choice. 
(But  no pauses  at the  end of each screen for CRT's.)  You 
can  set the  TO string to  a null (<return> only) to delete 
the target (FROM) string. 




                             5







MicroMUMPS Utilities                      Cornell University


Save
       Save allows you to save a specified set  of  routines
(with an option to  include  the  comments)  to  a specified 
output device - an MSDOS sequential  file (devices 2,3, or 4 
in MicroMUMPS).  You will be asked for a Drive and File name 
for the output file.

      Note: You can specify device  5  to  direct  the  save
operation to the external  communication port.  This  option 
can  be  used  in  conjunction  with  a RESTORE operation on 
another  computer (also using device 5) to effect  computer-
to-computer transfers of routines and globals.  However, use  
of  inter-computer transfers requires that the communication 
ports are properly set  up prior to initiating this process. 
Failure to do so  will probably  hang the system and require
rebooting with consequent loss of workspace files.

Restore
      Restore allows you to  restore routines, and,  option-
ally, comments that  were Saved with  the Save  option.  You 
specify the name(s) that are to be  restored and whether  or  
not you want the comments  associated with those routines to
be restored also.  For UCD MicroMUMPS version 5.0 and later, 
this function will restore the routines to  ASCII files with 
the .MMP extention.   You  will still  need to  ZFETCH  them  
into the routines library file.

      Note: You can restore from device 5 to read information
being transmitted from another computer (see Save option above).

Kill
      Kill allows you to remove a specified set of routines.  
It also kills the routines entry in the directory (^%MU) and 
any comments that are associated with this routine (^%M).

Xtended Directory
       This function acts in a manner similar to the  DIREC-
TORY command but also lists the  first line of each  routine 
and the second line if it is a comment line.  It  is a  very 
useful  convention to  have the  first line  of each routine 
contain (as a comment) the author's name and optionally  the 
last date modified, and the 2nd line of  each  routine  be a  
comment line that briefly describes  the function of the rou-
tine.  As an  example, the following two lines could  be  the  
first two lines of the routine %M:
  
   %M   ;John Lewkowicz - NYS College of Veterinary Medicine
        ;Programmer Utilities - Main Entry Point and Dispatch

The X  function would then list both of these lines when dis-
playing the directory.





                             6






MicroMUMPS Utilities                      Cornell University


               Functional Description - Globals
Directory

     Directory gives you a directory of  all  globals.  This
directory  is  maintained  in  ^%MU,  similar to the routine
directory. Since it is much easier to create and delete glo-
bals  and harder (if not impossible) to track these changes,
it is recommended that you refresh the directory before  you
list   it.  When  refreshing,  the  temporary  scratch  file
SCRATCH.DAT is created and deleted. You  will  also  get  to
specify the Drive and output device for the directory.

Edit

     Edit lets you edit a global reference  (entire  global,
specific  node,  or  specific branch). It loops through your
reference, displaying each node and  getting  your  changes.
After  each  node  you  can  specify  whether to do the node
Again, go on to the Next node or Stop  editing  this  refer-
ence.

List

     List lets you list a global reference (all or  part  of
the  global)  to a specified device. If that device is a CRT
(as defined by the Terminal definition option), the  program
will pause at the end of each screen.

Find

     Find allows you to search for one or more  strings  (or
patterns)  for  a  given  global reference. Output of search
results is sent to the device of  your  choice,  with  CRT's
pausing at the end of each screen.

Change

     Change allows you to change one or more strings  (FROM)
to new strings (TO) for a global reference (all or part of a
global). A trace of the changes is output to the  device  of
your  choice.  There are NO pauses at the end of a screen on
CRT's. The TO string can be a null ("") to DELETE  the  FROM
string.

Save

     Save allows you to output one  or  more  globals  to  a
specified  output  device.  Usually  output is to one of the
sequential MSDOS files (devices 2,3, or  4  in  MicroMUMPS),
and  you  will  be  asked  to  enter the drive and file name
specification for the output file.

When doing a global Save, you can specify the maximum number


                             7







MicroMUMPS Utilities                      Cornell University


of  bytes  to  output to the output file. If you make use of
this feature, you can create multiple output files (volumes)
to  save  large  data bases on floppy disks. For example, to
save 1MBYTE worth of data on  5  1/4"  double-sided,  double
density  disks with 360K bytes on each disk, you could indi-
cate that the maximum bytes to output is 360K  (in  response
to  the  question  asked  just before the ``Ready to Start''
question). The utility would then start a  global  Save  and
continue  through  the  first  360K bytes. At that time, the
output file is closed and you will be advised to remove  the
disk,  insert a new one, and define where the continued out-
put is to go. Naming each of the continuation files is  your
responsibility. Each of the resulting save files is complete
and standalone (including a definition of  Date/Time  lines)
and  can  be  individually  restored  when using the RESTORE
option.

Restore

     Restore allows you to retrieve one  or  more  specified
global names from a file created with the Save option.

Kill

     Kill allows you to remove a  specified  set  of  global
names.  Deleted  globals are also removed from the directory
in ^%MU.

Xtended Directory

     This command will provide you with a  global  directory
on  a  specified output device and will list along with each
entry the contents of the top data node if  it  is  defined.
Thus,  you can comment the data base by defining a string at
the name level, for example:

^%MTC="Terminal Definition and Port Assignments"

















  
                               8







MicroMUMPS Utilities                      Cornell University


                  Terminal Characteristics


     This utility allows you to define  the  characteristics
of  specific  terminals and to tie those terminals logically
to UCD MicroMUMPS port assignments. using these  definitions
in programs (for example this utility package %M) allows the
programmer  a  certain  device  independence  difficult   to
achieve  when  device-specific  codes  are used in programs.
Most of the terminal specific values that might be of use to
a  programmer  are maintained by this utility and can be set
up once at the beginning of a package initialization.  These
parameters include:

Right Margin - The number of characters that will fit on one
   line.   Use  of  this  parameter allows the programmer to
   ensure that data fits on a line, to center data, etc.  As
   an  example,  to  center  a string of data on a line, the
   following code could be used (assuming string to be  cen-
   tered  is  in  variable  `X' and variable RM contains the
   value for the right margin):

   W !,?RM2-$L(X)2),X,!

Screen Length - The number of  lines  that  will  fit  on  a
   screen  or page. This parameter permits the programmer to
   pause at the end of a screen or start  a  new  page  with
   header information, etc.

Form Feed - The character sequence necessary  to  clear  the
   screen  and  start  a  new page. The MUMPS ``#'' does NOT
   always perform this function depending  on  the  terminal
   and  the use of SETMUMPS described in the MicroMUMPS User
   Manual. If this value is initialized correctly, the  pro-
   grammer can always clear the screen with a

   W @FF   or      W @IOFF

High Intensity - If a terminal supports multiple intensities
   (or  multiple  colors),  it  is possible to switch to the
   High intensity (or a designated color) by writing out the
   character sequence of this variable with a

   W @LH   or      W @IOLH

Low Intensity - String of characters that will switch termi-
   nals  that  support  dual intensity back to LOW intensity
   (or a specified color) by writing the command

   W @HL   or      W @IOHL

   In all cases where outputting these strings or  executing
   strings  of  code, the codes are set up so that terminals


                             9







MicroMUMPS Utilities                      Cornell University


   that do not  support  a  feature  will  not  be  affected
   adversely.  For  example, a terminal that doesn't support
   dual intensity would have a high intensity and low inten-
   sity  string  of  ``*0'', which would result in a W *0 to
   the device, a command that would not affect the terminal.

Cursor Positioning - On terminals that support cursor  posi-
   tioning,  you  can Xecute an indirect MUMPS command after
   setting the desired X and Y positions as follows:

   S DX=10,DY=20 X XY...          -or- S DX=10,DY=20 X IOXY

Terminal Type - The variable SUB (or IOST) contains a string
   that  defines  the  terminal  type.  The  first character
   defines the general type (C=CRT, P=printer, O=Other), and
   the rest of the string is free text defining the specific
   type (e.g., DEC LA120).

The following entry points are available to  the  programmer
for general access to these terminal values:

   CURRENT^%MTC will open the device specified  in  $IO  and
   return the following parameters

           FF - Form Feed character sequence
           HL - High to Low Intensity switch character sequence
           LH - Low to High Intensity switch character sequence
           RM - Right Margin
           SL - Screen Length
           XY - Cursor positioning command
           SUB - Terminal Subtype

   In addition  to  opening  the  device  if  necessary,  an
   optional  startup string will be sent to the device (this
   function can be used to set up initial  default  terminal
   conditions such as high intensity, printer pitch, etc.).

^%MTC will let the user pick which of the  MUMPS  I/O  ports
   they wish to direct output To/From. On return, the device
   has been opened, an optional  initialization  string  has
   been  output  to  the device, and the following variables
   are available for use by the program:

           IO -    Device Number selected (numeric)
                   0 - Console
                   1 - Printer port
                   2 - Sequential MSDOS file
                   3 - Sequential MSDOS file
                   4 - Sequential MSDOS file
                   5 - AUX port for external communication

           IOFF -  Character sequence to clear screen/start new page
           IOHL -  Character sequence to go to low intensity
           IOLH -  Character sequence to go to hight intensity

                             10







MicroMUMPS Utilities                      Cornell University


           IORM -  Right Margin (characters/line -1)
           IOSL - Screen/Page length (lines -1)
           IOST -  Terminal Subtype (see SUB above)
           IOXY -  MUMPS command string Xecuted to position cursor

   If the device selected is an MSDOS sequential file,  then
   the  default  setup  code for those devices (2-4) will be
   Xecuted and the program will ask  the  user  for  a  file
   specification  (Drive  and  File Name) and then open that
   file.













































                               11







MicroMUMPS Utilities                      Cornell University


                    Defining a Terminal



     This option is used to define a new terminal type or to
modify  the  definition  of  an  existing  terminal (such as
startup strings, right margin, etc).  The  parameters  main-
tained by this utility reside in ^%MTC. This global does not
need to exist when you first run  the  %M  utility  package,
since  it will be initialized by ^%M8 to include a number of
standard CRTs and Printers as well as the  MSDOS  sequential
files. If the terminals on your system are in the file after
this  initialization,  you  can  use  the  ``Defining  MUMPS
Ports''  option  to  attach  a  specified terminal type to a
specific I/O port.

     This utility option  allows  you  to  define  terminal-
specific  characteristics.  Enter  a  ``?'' or ``??'' if you
need help on a specific question. After entering the  termi-
nal  specification,  there will be NO apparent change on the
terminal, since you have not yet assigned  these  parameters
to a Port number.

Example (ADM3A CRT)     (user responses in bold face)

        Terminal Name: ADM3A    name of terminal
        Description: C-Lear-Siegler ADM3A
        Form Feed Character(s): *26,#   (# resets MUMPS $X,$Y)
        Hi->LO characters: *27,*41      (use *0 if not available)
        LO->HI character(s): *27,*40    (use *0 if not available)
        Right Margin: 79        (characters per line - 1)
        Screen Length: 23       (Lines per page - 1)
        Cursor Positioning: W *24,"=",*DY+32,*DX+32     (move to DX,DY)
        Startup Code: O %IO U %IO W *27,*40     (start at high intensity)





















                               12







MicroMUMPS Utilities                      Cornell University


                   Defining a MUMPS Port


     This function allows you to assign one of  the  defined
terminal  types  and  its  parameters  to one of the numeric
MicroMUMPS ports (0-4). The ports are defined as:

        0 -     Console (input/output)
        1 -     Printer (output only)
        2 -     MSDOS sequential file (input-output)
        3 -     MSDOS sequential file (input-output)
        4 -     MSDOS sequential file (input-output)
        5 -     AUX port (COM1 or COM2)

     After you have tied a terminal to a port,  the  program
will issue a

D CURRENT^%MTC

and set up the correct parameters for the appropriate port.






      Utility Data Bases (Globals used by %M package)

^%M - Holds user-generated comments associated with specific
   labels for specific routines. Entered/Edited when editing
   Routines.

^%MD - Defines the default Routine library and Global drives
   to  be  used  when running the %M utility functions. Ini-
   tialized first time  through  routine  %M8.  %M8  can  be
   invoked directly (D ^%M8) to change these defaults.

^%MRE - Temporary scratch file into which routine lines  are
   written when editing a routine. All of the actual editing
   of these lines is done on data in this global.

^%MTC - Contains device descriptions and current assignments
   of the MUMPS ports.

^%MU - Utility global that holds  directories  (Routine  and
   Global)  as well as Routine and Global restore specifica-
   tions.








                               13







MicroMUMPS Utilities                      Cornell University


                    ^%M Global Structure

Description

     This global contains free text comments associated with
a  given  routine and label. The data is entered/edited when
editing routines.  It is used when listing routines and  can
be  saved  and  restored  with  the  routines  at the user's
option.

Structure

                                |-----|
                                | %M  |
                                |-----|
                                  /\
                                 /  \ (ROUTINE)
                                /
                             |---|
                             |---|
                               /\
                              /  \  (LABEL)
                             /
                -------------------
                |  |  |  |  |  |  |
                |(0)              |(n)
           |---------|         |------|
           |last line|         | Data |
           |  used   |         |------|
           |---------|

ROUTINE is a Routine Name
LABEL  is a Routine line label
last line used is an integer pointing to the last data node (n)
Data contains free text comments



                   ^%MD Global Structure

Description

     This global contains the  Default  Routine  and  Global
drives used by the Utility package %M.

Structure

        ^%MD=RG

R       is the default Routine drive (A-P)

G       is the default Global Drive (A-P)



                               14







MicroMUMPS Utilities                      Cornell University


                   ^%MRE Global Structure

Description

     This global holds the routine currently  being  edited.
The editor is line-oriented, and the line number is the sub-
script into this global.



Structure

                                |------|
                                | %M   |
                                |------|
                                  /\
                                 /  \ (ROUTINE)
                                /
                             |---|
                             |---|
                               /\
                              /  \  (LABEL)
                             /
                -------------------
                |  |  |  |  |  |  |
                |(0)              |(n)
           |---------|         |-----|
           |last line|         | Data|
           |  used   |         |-----|
           |---------|

ROUTINE is a Routine Name
LABEL  is a Routine line label
last line used is an integer pointing to the last data node (n)
Data contains free text comments


















   

                              15







MicroMUMPS Utilities                      Cornell University


                   ^%MTC Global Structure


Description

     This  global  contains  terminal  definitions  and  the
current MUMPS port assignments. It is initialized by routine
%M8 and updated  by  routine  %MTC  (at  labels  DEFINE  and
DEFAULT).


Structure


                                |---------|
                                | ^%MTC   |
                                |---------|
                                    /\
                                   /  \
                                  /(n) \ (TERMINAL)
                                 /      \
                        |---------|     |------|
                        | Terminal|     | Desc |
                        |---------|     |------|

n is an integer MUMPS port number (0-5)
Terminal is a terminal name like ADM3A
Desc is a description of the terminal in the following format:

        Desc = ``FF~HL~LH~RM~SL~XY~TD~SC'' where:

                FF - Form Feed sequence
                HL - Low intensity sequence
                LH - High intensity sequence
                RM - Right Margin
                SL - Screen Length
                XY - Cursor Positioning code
                TD - Terminal description (such as C-ADM3A)
                SC - Startup code to be eXecuted when Opening device
















                               16







MicroMUMPS Utilities                      Cornell University


                   ^%MU Global Structure


Description

     A utility global for use by the %M utility package.  It
holds  directories (both Routine and Global) as well as Rou-
tine and Global restore specifications.


Structure


                                        |--------|
                                        | ^%MU   |
                                        |--------|
                                           /\
                                          /  \
                                         /    \
                                  -------      ---------------
                                  |                          |
                        (``ROU'' or ``GBL'')    (``RESR'' or ``RESG'')
                                  |                          |
                                |---|                      |---|
                                |---|                      |---|
                                  /\                        /\
                                 /  \ (NAME)               /  \  (n)
                                /    \                    /    \
                        |-----------|            |----------------|
                        |SELECTED   |            |SPECIFICATION   |
                        |-----------|            |----------------|

NAME is a Routine or Global Name (depending on  whether  the
   subscript is ``ROU'' or ``GBL'').

SELECTED os a True/False indication (1/0) as to whether  the
   name has been selected or not.

SPECIFICATION is a restore specification (either Routine  or
   Global  depending  on  whether  the previous subscript is
   ``RESR'' or ``RESG'' in the following format:

   NAME:IF

   where Name is the actual user entry (such as X?Z*) and IF
   is the indirect pattern match that will be used to test a
   target name (such as 1"A"1E1"B".E).








                               17







MicroMUMPS Utilities                      Cornell University


                Save-Restore File Structure

     The Save/Restore routines and globals are  written  out
as  sequential  files  to  the designated devices. The first
line is always a free text description of the file  and  the
second  line  is a free text data and time. Both lines could
be nulls.
------------------------------------------------------------
GLOBAL                         ROUTINE
``Description''                ``Description''
``Date and Time''              ``Date and Time''
Global Reference               Routine name
   data element                   routine line
Global reference                  routine line
   data element                   routine line
   .                              .
   .                              .
   .                              .
(Blank global reference        (Blank routine line is used
indicates file done)           to indicate end of routine)
                               Routine name
                                  routine line
                                  routine line
                                  .
                                  .
                                  .
                               (blank routine name indicates
                               end of file)


     You can use %M to save and restore  both  routines  and
globals  between  computers  without  the creation of a tem-
porary file (using device #5 on both computers. If you  want
to  transmit  or receive routines or globals from OTHER sys-
tems, you can use the following sections of  MUMPS  code  to
transmit  (TX)  or receive (RX) a line (L) to/from the other
machine.

TX R X G TX:X'="" W L,! R X G TX:X'="" W $L(L),! R X G TX:X'=""
   Q
RX R !,A:10 E  W "*-ERROR-*",! G RX
R1 R !,X:10 E  W "*-ERROR-*",! G RX
   S X=$S(X'?1N.N:0,$L(A)'=X:0,1:1) W $S(X:"",1:"*-ERROR-*"),!
   G RX:'X
   Q

The code above  assumes  that  the  device  in-USE  for  the
read/writes  is connected to the microcomputer via an RS-232
serial line and that  echo  is  turned  off,  and  that  the
default  line  length  is  set  at  255  characters (i.e., O
DEV:(255:1) for Intersystems MUMPS).




                               18







MicroMUMPS Utilities                      Cornell University


                  Utility Package Routines

%M      Main  entry  point.   Gets   primary   options   and
     dispatches  control to other routines in the package as
     appropriate. Also  processes  name  specifications  and
     flags (selecting) entries in appropriate directories.

%M0     Processes Directory requests (including  ``?L''  and
     ``?S''), and both Global and Routine List options.

%M1     Controls the Editing of both Routines  and  Globals.
     The actual editing of routines is handled by the %ME...
     routines, but global editing is done by %M1.

%M2     Processes Delete and Find options for  Routines  and
     for Globals.

%M3     Processes the Change option for Routines and Globals.

%M4     Performs Save and Restore operations for  both  Rou-
     tines and Globals.

%M5     Gets user options for Terminal and  Port  specifica-
     tions. Dispatches control to %MTC for actual updates.

%M6     Does actual Routine/Global Save or Restore  (%M4  is
     used  to  collect  options  and set up for Save/Restore
     operation.

%M7     Handles eXtended Directory  for  both  Routines  and
     Globals.

%M8     Initializes both the default drive data base  (^%MD)
     and the terminal characteristic data base (^%MTC).

%M9     Displays help text for the Utility package.

%M10    A Continuation of %M9 help text).

%MEDT   Routine and comment file editor.

%MEDT1  Continuation of %MEDT.

%MEDTE  Extended explanations for %MEDT.

%MEDTE1 Continuation of %MEDTE.

%MTC    Terminal definition routine. Entry points at
             %MTC    to let user select a port.
             CURRENT^%MTC to get current device parameters.

%MTCD   Continuation of %MTC with  entry  points  to  define
     characteristics  of a terminal (DEFINE) and to assign a
     terminal to a MUMPS I/O port (DEFAULT).

%MTCH   Used to display help text for %MTC questions.

                               19