%%% ====================================================================
%%%  @LaTeX-style-file{
%%%     author          = "Braams J.L.",
%%%     version         = "3.1b",
%%%     date            = "11 October 1993",
%%%     time            = "09:12:24 MET",
%%%     filename        = "changebar.doc",
%%%     address         = "PTT Research
%%%                        St. Paulusstraat 4
%%%                        2264 XZ Leidschendam
%%%                        The Netherlands",
%%%     telephone       = "(70) 3325051",
%%%     FAX             = "(70) 3326477",
%%%     checksum        = "51434 1276 6008 47620",
%%%     email           = "J.L.Braams@research.ptt.nl (Internet)",
%%%     codetable       = "ISO/ASCII",
%%%     keywords        = "",
%%%     supported       = "yes",
%%%     abstract        = "",
%%%     docstring       = "THis LaTeX document style option implements
%%%                        changebars for LaTeX documents. It supports
%%%                        various printer drivers through a selection
%%%                        mechanism.
%%%
%%%                        The checksum field above contains a CRC-16
%%%                        checksum as the first value, followed by the
%%%                        equivalent of the standard UNIX wc (word
%%%                        count) utility output of lines, words, and
%%%                        characters.  This is produced by Robert
%%%                        Solovay's checksum utility.",
%%%  }
%%% ====================================================================
\def\fileversion{v3.1b}
\def\filedate{11 october 93}
%\def\docdate{3 July 93}
%
% \changes{3.1}{2 jul 93}{Removed a number of typos}
% \changes{3.1a}{3 aug 93}{Uncommented `filedate and `fileversion}
% \CheckSum{796}
%
% \title{The Changebar document style option
%         \thanks{This file has version number \fileversion,
%                 last revised \filedate,
%                 documentation dated \docdate.}}
%
% \author{Michael Fine\\Distributed Systems Architecture}
%
%
% \author{Johannes Braams\\
%         PTT Research Neher Laboratories\\
%         P.O. Box 421\\
%         2260 AK Leidschendam\\
%         {\tt J.L.Braams@research.ptt.nl}}
%
% \date{Printed \today}
%
% \maketitle
%
% \begin{multicols}{2}
%  \tableofcontents
% \end{multicols}
%
% \begin{abstract}
%    This document style-option implements a way to indicate modifications in
%    a \LaTeX-document by putting bars in the margin. It realizes this by
%    making use of the \verb=\special= commands supported by `dvi drivers'.
%    Currently four different drivers are supported. More can easily be added.
% \end{abstract}
%
% \section{Introduction}
%
% IMPORTANT NOTE: Just as with cross references and labels, you
% usually need to process the document twice (and sometimes three
% times) to ensure that the changebars come out correctly.  However, a
% warning will be given if another pass is required.
%
%
% FEATURES:
%
%       Changebars may be nested within each other.  Each level of
%       nesting can be given a different thickness bar.
%
%       Changebars may be nested in other environments including floats
%       and footnotes.
%
%       Changebars are applied to all the material within the ``barred''
%       environment, including floating bodies regardless of where the
%       floats float to.  An exeception to this is margin floats.
%
%       Changebars may cross page boundaries.
%
% \section{The user interface}
%
%    This style file provides a number of extra macros, these are described
%    in short below.
%
% \DescribeMacro{\driver}
%    In the preamble of a document the driver that will be used to print
%    the document can be indicated. The macro \verb=\driver= takes one
%    argument. The argument can be one of:
%    \begin{itemize}
%      \item DVItoLN03
%      \item DVItoPS
%      \item DVIps
%      \item em\TeX
%    \end{itemize}
%    The argument to \verb=\driver= is case-insensitive.
%
% \DescribeMacro{\cbstart}
% \DescribeMacro{\cbend}
%    All material between the macros \verb=\cbstart= and \verb=\cbend=
%    is barred.  The nesting of multiple changebars is allowed.
%    The macro \verb=\cbstart= has an optional parameter that specifies the
%    width of the bar. The syntax is \verb=\cbstart[=\meta{dimension}{\tt]}.
%    If no width is specified, the current value of the parameter
%    \verb=\changebarwidth= is used.  Note that
%    \verb=\cbstart= and \verb=\cbend= can be used anywhere but
%    must be correctly nested with floats and footnotes.  That is,
%    one cannot have one end of the bar inside a floating insertion
%    and the other outside, but that would be a meaningless thing
%    to do anyhow.
%
% \DescribeEnv{changebar}
%    Apart from the macros \verb=\cbstart= and \verb=\cbend= a proper
%    \LaTeX\ environment is defined. The advantage of using the environment
%    whenever possible is that \LaTeX\ will do all the work with respect
%    to checking the correct nesting of different environments.
%
% \DescribeMacro{\cbdelete}
%    The macro \verb=\cbdelete= puts a square bar in the margin to indicate
%    that some text was removed from the document. The macro has an optional
%    argument to specify the width of the bar. When no argument is specified
%    the current value of the parameter \verb=\deletebarwidth= will be used.
%
% \DescribeMacro{\nochangebars}
%    The macro \verb=\nochangebars= disables the changebar commands.
%
% \subsection{Changebar parameters}
%
% \DescribeMacro{\changebarwidth}
%    The width of the changebars is controlled with the \LaTeX\ length
%    parameter \verb=\changebarwidth=.
%    The value of it can be changed with the \verb=\setlength= command.
%    Changing the value of \verb=\changebarwidth= affects all subsequent
%    changebars subject to the scoping rules of \verb=\setlength=.
%
% \DescribeMacro{\deletebarwidth}
%    The width of the deletebars is controlled with the \LaTeX\ length
%    parameter \verb=\deletebarwidth=.
%    The value of it can be changed with the \verb=\setlength= command.
%    Changing the value of \verb=\changebarwidth= affects all subsequent
%    deletebars subject to the scoping rules of \verb=\setlength=.
%
% \DescribeMacro{\changebarsep}
%    The separation between the text and the changebars is determined
%    by the value of the \LaTeX\ length parameter \verb=\changebarsep=.
%
% \DescribeVar{changebargrey}
%    When one of the supported dvi to PostScript translators is used
%    the `blackness' of the bars can be controlled. The \LaTeX\ counter
%    {\tt changebargrey} is used for this purpose. Its value can be
%    changed with a command like:
%    \begin{verbatim}
%    \setcounter{changebargrey}{85}
%    \end{verbatim}
%    The value of the counter is a percentage, where the value 0 yields
%    black bars, the value 100 yields white bars.
%
% \DescribeVar{outerbars}
%    The changebars will be printed in the `inside' margin of your document.
%    This means they appear on the left side of the page. When {\tt twoside}
%    is in effect the bars will be printed on the right side of even pages.
%    This behaviour can be changed by including the command
%    \verb=\outerbarstrue= in your document.
%
%
% \section{Deficiencies and bugs}
%
% \begin{itemize}
%  \item
%    The macros blindly use specials points \verb=\cb@minpoint= through
%    \verb=\cb@maxpoint=. If this conflicts with another set of macros, the
%    results will be unpredictable.  (What is really needed is a
%    \verb=\newspecialpoint=, analogous to \verb=\newcount= etc.)
%
%  \item
%    There is a limit of
%    $(\mbox{\tt\bsl cb@maxpoint}-\mbox{\tt\bsl cb@minpoint}+1)/2$ bars per
%    page (two special points per bar).  Using more than this number
%    yeilds unpredictable results (but that could be called a feature
%    for a page with so many bars).  This limitation could be
%    increased if desired.
%
%  \item
%    Internal macro names are all of the form \verb=\cb@xxxx=.
%    No checking for conflicts with other macros is done.
%
%  \item
%    This implementation has not been designed for two column
%    printing.
%
%  \item
%    The algorithms may fail if a floating insertion is split over
%    multiple pages.  In \LaTeX\ floats are not split but footnotes may
%    be.  The simplest fix to this is to prevent footnotes from being
%    split but this may make \TeX\ very unhappy.
%
%  \item
%    The \verb=\cbend= normally gets ``attached'' to the token after it rather
%    than the one before it.  This may lead to a longer bar than
%    intended.  For example, consider the sequence `word1 \verb=\cbend=
%    word2'.  If there is a line break between `word1' and `word2'
%    the bar will incorrectly be extended an extra line.  This
%    particular case can be fixed with the incantation `word1\verb=\cbend{}=
%    word2'.
%  \end{itemize}
%
% \section{The basic algorithm}
%
%    The changebars are implemented using the \verb=\specials= of various
%    {\tt dvi} interpreting programs like {\tt DVItoLN03} or {\tt DVIps}.
%    In essence, the start of changebar defines a \verb=\special= point
%    in the margin at the current vertical position on the page.
%    The end of a changebar defines another point and then joins
%    the two using the ``connect'' \verb=\special=.
%
%    This works fine as long as the two points being connected lie on
%    the same page.  However, if they don't, the bar must be
%    artificially terminated at the page break and restarted at the
%    top of the next page.  The only way to do this (that I can think
%    of) is to modify the output routine so that it checks if any bar
%    is in progress when it ships out a page and, if so, adds the
%    necessary artificial end and begin.
%
%    The obvious way to indicate to the output routine that a bar is
%    in progress is to set a flag when the bar is begun and to unset
%    this flag when the bar is ended.  This works most of the time
%    but, because of the asynchronous behavior of the output routine,
%    errors occur if the bar begins or ends near a page break.  To
%    illustrate, consider the following scenerio.
%
%    \begin{verbatim}
%    blah blah blah          % page n
%    blah blah blah
%    \cbstart                % this does its thing and set the flag
%    more blah
%               <-------------- pagebreak occurs here
%    more blah
%    \cbend                  % does its thing and unsets flag
%    blah blah
%    \end{verbatim}
%
%    Since \TeX\ process ahead of the page break before invoking the
%    output routine, it is possible that the \verb=\cbend= is
%    processed, and the flag unset, before the output routine is
%    called.  If this happens, the necessary artificial end and begin
%    will not be added to page $n$ and $n+1$, respectively.  Thus, it is
%    not possible to use a flag to signal the output routine that a
%    bar crosses a page break, and some other mechanism is required.
%
%    The method used with these macros is to create a list of the
%    beginning and end points of each bar in the document together
%    with the page number corresponding to each point.  Then, as a
%    page is completed, a modified output routine checks the list to
%    determine if any bars begun on or before the current page are
%    terminated on subsequent pages, and handles those bars
%    appropriately.  To build the list, information about each
%    changebar is written to the {\tt .aux} file as bars are processed.
%    This information is re-read when the document is next processed.
%    Thus, to ensure that changebars are correct, the document must
%    be processed twice, but this is required for \LaTeX\ anyway.
%
%    This approach is sufficiently general to allow nested bars, bars
%    in floating insertions, and bars around floating insertions.
%    Bars inside floats and footnotes are handled in the same way as
%    bars in regular text.  Bars that encompass floats or footnotes
%    are handled by creating an additional bar that floats with the
%    floating material.  Modifications to the appropriate \LaTeX\
%    macros check for this condition and add the extra bar.
%
%\StopEventually{
% \IndexPrologue{\section*{Index}%
%  \markboth{Index}{Index}%
%   Numbers in {\it italics\/} indicate the page where the
%   macro is described, the underlined numbers indicate
%   the number of the line of code where the macro is defined,
%   all other numbers indicate where a macro is used.}
%
% \GlossaryPrologue{\section*{History of changes}%
%    \markboth{History of changes}{History of changes}%
%    The numbers behind the changes indicate the page where
%    the macrocode is described.\hfil\null}
%
%  \PrintIndex
%^^AA \PrintChanges
% }
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
% \section{The implementation}
%
%    We begin by identifying ourselves by writing a message in the
%    transcript of the session.
%
% \subsection{Declarations And Initializations}
%
%    \begin{macrocode}
\wlog{Document style option `changebar', \fileversion\space<\filedate>}
%    \end{macrocode}
%
% \begin{macro}{\atcatcode}
%    In this file, a lot of control sequences contain {\tt @}-signs.
%    To be able to do this the category of the {\tt @} has to be `letter'.
%    Therefore we save the current category code and restore it later.
%    For this purpose the control sequence \verb=\atcatcode= is used.
%
%    \begin{macrocode}
\chardef\atcatcode=\catcode`\@
\catcode`\@=11\relax
%    \end{macrocode}
% \end{macro}
%
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
%
% \begin{macro}{\cb@maxpoint}
%    The original version of {\tt changebar.sty} only supported the
%    {\tt DVItoLN03} specials. The {\tt LN03} printer has a maximum
%    number of points that can be defined on a page. Also for some
%    PostScript printers the number of points that can be defined
%    can be limited by the amount of memory used. Therefore, the
%    consecutive numbering of points has to be reset when the maximum
%    is reached. This maximum can be adapted to the printers needs.
%    \begin{macrocode}
\def\cb@maxpoint{80}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@minpoint}
%    When resetting the point number we need to know what to reset
%    it to, this is minimum number is stored in \verb=\cb@minpoint=.
%    {\bf This number has to be ODD} because the algorithm that decides
%    whether a bar has to be continued on the next page depends on this.
%    \begin{macrocode}
\def\cb@minpoint{1}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@nil}
%    Sometimes a void value for a point has to be returned by one
%    of the macros. For this purpose \verb=\cb@nil= is used.
%    \begin{macrocode}
\def\cb@nil{0}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@nextpoint}
% \begin{macro}{\cb@currentpoint}
%    The number of the next special point is stored in the count
%    register \verb=\cb@nextpoint= and initially equal to
%    \verb=\cb@minpoint=. The number of the current point is stored in
%    \verb=\cb@currentpoint=.
%    \begin{macrocode}
\newcount\cb@nextpoint
\cb@nextpoint=\cb@minpoint
\newcount\cb@currentpoint
%    \end{macrocode}
% \end{macro}
% \end{macro}
%
% \begin{macro}{\cb@page}
% \begin{macro}{\cb@pagecount}
%    The macros need to keep track of the number of pages output
%    so far. For this goal the counter \verb=\cb@pagecount= is used.
%    When a pagenumber is read from the history list, it is stored in
%    the counter \verb=\cb@page=. The counter \verb=cb@pagecount= is
%    initially $0$; it gets incremented during the call to
%    \verb=\@makebox= (see section~\ref{pagebreak}).
%    \begin{macrocode}
\newcount\cb@page
\newcount\cb@pagecount
\cb@pagecount=0
%    \end{macrocode}
% \end{macro}
% \end{macro}
%
% \begin{Var}{outerbars}
%    A switch is provided to control where the changebars will be printed.
%    The initial value of the switch is {\tt false}.
%    \begin{macrocode}
\newif\ifouterbars \outerbarsfalse
%    \end{macrocode}
% \end{Var}
%
% \begin{macro}{\cb@positions}
%
%    This macro calculates the (horizontal) positions of the changebars.
%    The calculations take {\tt twoside} into account. Also the setting
%    of the switch {\tt outerbars} is checked.
%
%    Because the margins can differ for even and odd pages and
%    because changebars are sometimes on different sides of the paper
%    we need two dimensions to store the result.
%
%    Since the changebars are drawn with the {\sc PostScript}
%    command {\tt lineto} and not as \TeX{}-like rules the reference
%    points lie on the center of the changebar, therefore the
%    calculation has to add or subtract half of the width of the bar
%    to keep \verb+\changebarsep+ whitespace between the bar and
%    the body text.
%    \begin{macrocode}
\newdimen\cb@odd
\newdimen\cb@even
%    \end{macrocode}
%    First the position for odd pages is calculated. In this case the use
%    of the {\tt twoside} option does not effect the positioning of the
%    changebars.
% \changes{3.1}{2 jul 93}{Corrected positioning of PostScript bars}
%    \begin{macrocode}
\def\cb@positions{%
  \global\cb@odd =\hoffset
  \global\advance\cb@odd by \oddsidemargin
  \ifouterbars
    \global\advance\cb@odd by \textwidth
    \global\advance\cb@odd by \changebarsep
    \global\advance\cb@odd by 0.5\changebarwidth
  \else
    \global\advance\cb@odd by -\changebarsep
    \global\advance\cb@odd by -0.5\changebarwidth
  \fi
%    \end{macrocode}
%    On even pages the use of the {\tt twoside} option results in a different
%    placement of the bars.
%    \begin{macrocode}
  \global\cb@even =\hoffset
  \global\advance\cb@even by \evensidemargin
  \if@twoside
    \ifouterbars
      \global\advance\cb@even by -\changebarsep
      \global\advance\cb@even by -0.5\changebarwidth
    \else
      \global\advance\cb@even by \textwidth
      \global\advance\cb@even by \changebarsep
      \global\advance\cb@even by 0.5\changebarwidth
    \fi
  \else
    \ifouterbars
      \global\advance\cb@even by \textwidth
      \global\advance\cb@even by \changebarsep
      \global\advance\cb@even by 0.5\changebarwidth
    \else
      \global\advance\cb@even by -\changebarsep
      \global\advance\cb@even by -0.5\changebarwidth
    \fi
  \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@removedim}
%    In PostScript code length specifications are without dimensions.
%    Therefore we need a way to remove the letters `pt' from the
%    result of the operation \verb=\the\=\meta{dimen}.
%    This can be done by defining a command that has a delimited
%    argument like:
%    \begin{verbatim}
%    \def\cb@removedim#1pt{#1}
%    \end{verbatim}
%    We encounter one problem though, the category code of the letters
%    `pt' is 12 when produced as the output from \verb=\the\=\meta{dimen}.
%    Thus the characters that delimit the argument of \verb=\cb@removedim=
%    also have to have category code 12. To keep the changes local
%    the macro \verb=\cb@removedim= is defined in a group.
%    \begin{macrocode}
{\catcode`\p=12\catcode`\t=12 \gdef\cb@removedim#1pt{#1}}
%    \end{macrocode}
% \end{macro}
%
% \subsection{User Level Commands And Parameters}
%
% \begin{macro}{\driver}
%    The user can select the specials that should be used by calling
%    the command {\tt\bsl driver\{}\meta{drivername}{\tt\}}.
%    Possible choices are:
%    \begin{itemize}
%    \item DVItoLN03
%    \item DVItoPS
%    \item DVIps
%    \item em\TeX
%    \end{itemize}
%    This command can only be used in the preamble of the document.
%
%    The argument should be case-insensitive, so it is turned into
%    a string containing all uppercase characters. To keep some definitions
%    local, everything is done within a group.
% \changes{3.1}{2 jul 93}{Removed some spurious spaces}
%    \begin{macrocode}
\def\driver#1{%
  \bgroup\edef\next{\def\noexpand\tempa{#1}}%
    \uppercase\expandafter{\next}%
    \def\LN{DVITOLN03}%
    \def\DVItoPS{DVITOPS}%
    \def\DVIPS{DVIPS}%
    \def\emTeX{EMTEX}%
%    \end{macrocode}
%    The choice has to be communicated to the macro \verb=\cb@setup@specials=
%    that will be called from within \verb=\document=. For this puprose the
%    control sequence \verb=\cb@driver@setup= is used. It receives a numeric
%    value using \verb=\chardef=.
%    \begin{macrocode}
    \global\chardef\cb@driver@setup=0\relax
    \ifx\tempa\LN      \global\chardef\cb@driver@setup=0\fi
    \ifx\tempa\DVItoPS \global\chardef\cb@driver@setup=1\fi
    \ifx\tempa\DVIPS   \global\chardef\cb@driver@setup=2\fi
    \ifx\tempa\emTeX   \global\chardef\cb@driver@setup=3\fi
  \egroup}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\@preamblecmds}
%    We add \verb+\driver+ to \verb+\@preamblecmds+, which is a
%    list of commands to be used only in the preamble of a document.
%
%    \begin{macrocode}
{\def\do{\noexpand\do\noexpand}
 \xdef\@preamblecmds{\@preamblecmds \do\driver}
}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@setup@specials}
%    The macro \verb=\cb@setup@specials= defines macros containing the
%    driver specific \verb=\special= macros. It will be called from
%    within the \verb=\begin{document}= command.
%
% \begin{macro}{\cb@defpoint}
%    The macro \verb=\cb@defpoint= is used to define one of the two
%    points of a bar. It has two arguments, the number of the point
%    and the distance from the left side of the paper; so its syntax
%    is:
%    \verb=\cb@defpoint{=\meta{number}{\tt \}\{}\meta{length}{\tt\}}.
% \begin{macro}{\cb@resetpoints}
%    The macro \verb=\cb@resetpoints= can be used to instruct the
%    printer driver that it should send a corresponding instruction
%    to the printer. This is really only used for the {\sf LN03} printer.
%
% \begin{macro}{\cb@connect}
%    The macro \verb=\cb@connect= is used to instruct the printer driver
%    to connect two points with a bar. The syntax is
%    \verb=\cb@connect{=\meta{number}{\tt\}\{}\meta{number}%
%                                    {\tt\}\{}\meta{length}{\tt\}}
%    The two \meta{number}s indicate the two points to be connected;
%    the \meta{length} is the width of the bar.
%
%    \begin{macrocode}
\def\cb@setup@specials{%
%    \end{macrocode}
%    The control sequence \verb=\cb@driver@setup= expands to a number which
%    indicates the driver that will be used.
%    The original {\tt changebar.sty} was written with only the
%    the \verb=\special= syntax of the program {\tt DVItoLN3} (actually
%    one of its predecessors, {\tt ln03dvi}). Therefore this syntax
%    is defined first.
%    \begin{macrocode}
\ifcase\cb@driver@setup
  \def\cb@defpoint##1##2{\special{ln03:defpoint \the##1(\the##2,)}}
  \def\cb@connect##1##2##3{%
    \special{ln03:connect \the##1\space\space \the##2\space \the##3}}
  \def\cb@resetpoints{%
    \special{ln03:resetpoints \cb@minpoint \space\cb@maxpoint}}
%    \end{macrocode}
%    The first extension to the {changebar} option was for the
%    \verb=\special= syntax of the program {\tt DVItoPS} by James Clark.
%    \begin{macrocode}
\or
  \def\cb@defpoint##1##2{%
    \special{dvitops: inline
                \expandafter\cb@removedim\the##2\space 6.5536 mul\space
                /CBarX\the##1\space exch def currentpoint exch pop
                /CBarY\the##1\space exch def}}
  \def\cb@connect##1##2##3{%
    \special{dvitops: inline
                gsave \thechangebargrey\space 100 div setgray
                \expandafter\cb@removedim\the##3\space 6.5536 mul\space
                CBarX\the##1\space\space CBarY\the##1\space\space moveto
                CBarX\the##2\space\space CBarY\the##2\space\space lineto
                stroke grestore}}
  \let\cb@resetpoints\relax
%    \end{macrocode}
%    Also the program {\tt DVIps} by Thomas Rockicki is supported. The
%    PostScript code is nearly the same as for {\tt DVItoPS}, but the
%    coordinate space has a different dimension. Also this code has been
%    made resolution independent, whereas the code for {\tt DVItoPS}
%    might still be resolution dependent.
%
%    So far all the positions have been calculated in {\tt pt} units.
%    DVIps uses pixels internally, so we have to convert {\tt pt}s
%    into pixels which of course is done by dividing by 72.27
%    ({\tt pt}s per inch) and multiplying by {\tt Resolution}
%    giving the resolution of the {\sc PostScript} device in use
%    as a {\sc PostScript} variable.
%    \begin{macrocode}
\or
  \def\cb@defpoint##1##2{%
     \special{ps:
                \expandafter\cb@removedim\the##2\space
                Resolution\space mul\space 72.27\space div\space
                /CBarX\the##1\space exch def currentpoint exch pop
                /CBarY\the##1\space exch def}}
    \def\cb@connect##1##2##3{%
      \special{ps:
                gsave \thechangebargrey\space 100 div setgray
                \expandafter\cb@removedim\the##3\space
                Resolution\space mul\space 72.27\space div\space
                setlinewidth
                CBarX\the##1\space\space CBarY\the##1\space\space moveto
                CBarX\the##2\space\space CBarY\the##2\space\space lineto
                stroke grestore}}
    \let\cb@resetpoints\relax
%    \end{macrocode}
%    The latest addition is for the drivers written by Eberhard Mattes.
%    The \verb=\special= syntax used here will be supported with version
%    1.5 of his driver programs. This version will probably be released
%    late in 1991, therefore we add a warning for now.
%    \begin{macrocode}
\or
  \typeout{Changebar Warning: changebars only supported for v1.5+ of dvidrv}%
  \def\cb@defpoint##1##2{\special{em:point \the##1,\the##2}}%
  \def\cb@connect##1##2##3{\special{em:line \the##1,\the##2,\the##3}}%
  \let\cb@resetpoints\relax
%    \end{macrocode}
%    When code for other drivers should be added it can be inserted here.
%    When someone makes a mistake and somehow selects an unknown driver
%    a warning is issued and the macros are defined to be noops.
%    \begin{macrocode}
\else
  \typeout{Changebar Warning: changebars not supported in unknown setup}
  \def\cb@defpoint##1##2{}%
  \def\cb@connect##1##2##3{}%
  \let\cb@resetpoints\relax
\fi
%    \end{macrocode}
%    The last thing to do is to forget about \verb=\cb@setup@specials=.
%    \begin{macrocode}
\global\let\cb@setup@specials\relax}
%    \end{macrocode}
% \end{macro}
% \end{macro}
% \end{macro}
% \end{macro}
%
% \begin{macro}{\cbstart}
%
%    The macro \verb=\cbstart= starts a new changebar. It has an (optional)
%    argument that will be used to determine the width of the bar.
%    The default width is \verb=\changebarwidth=.
%    \begin{macrocode}
\def\cbstart{\@ifnextchar [{\cb@start}{\cb@start[\changebarwidth]}}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cbend}
%    The macro \verb=\cbend= (surprisingly) ends a changebar. The macros
%    \verb=\cbstart= and \verb=\cbend= can be used when the use of a
%    proper \LaTeX\ environment is not possible.
%    \begin{macrocode}
\def\cbend{\cb@end}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cbdelete}
%    The macro \verb=\cbdelete= inserts a `deletebar' in the margin.
%    It too has an optional argument to determine the width of the bar.
%    The default width (and length) of it are stored in
%    \verb=\deletebarwidth=.
%    \begin{macrocode}
\def\cbdelete{\@ifnextchar [{\cb@delete}{\cb@delete[\deletebarwidth]}}
%    \end{macrocode}
%
% \begin{macro}{\cb@delete}
%    Deletebars are implemented as a special `change bar'. The bar
%    is started and immediately ended. It is as long as it is wide.
%    \begin{macrocode}
\def\cb@delete[#1]{\vbox to 0pt{\vss\cb@start[#1]\vskip #1\cb@end}}
%    \end{macrocode}
% \end{macro}
% \end{macro}
%
% \begin{macro}{\changebar}
% \begin{macro}{\endchangebar}
%    The macros \verb=\changebar= and \verb=\endchangebar= have the
%    same function as \verb=\cbstart= and \verb=\cbend= but they can be used
%    as a \LaTeX\ environment to enforce correct nesting.
%    They can {\em not\/} be used in the {\sf tabular} and
%    {\sf tabbing} environments.
%    \begin{macrocode}
\def\changebar{\@ifnextchar [{\cb@start}{\cb@start[\changebarwidth]}}%
\def\endchangebar{\cb@end}
%    \end{macrocode}
% \end{macro}
% \end{macro}
%
% \begin{macro}{\nochangebars}
%    To disable changebars altogether without having to remove them from the
%    document the macro \verb=\nochangebars= is provided. It makes noops
%    from a couple of internal macros.
%    \begin{macrocode}
\def\nochangebars{\def\cb@start[##1]{}%
                  \def\cb@delete[##1]{}%
                  \let\cb@end\relax}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\changebarwidth}
%    The default width of the changebars is stored in the dimen register
%    \verb=\changebarwidth=.
%    \begin{macrocode}
\newlength{\changebarwidth}
\setlength{\changebarwidth}{2pt}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\deletebarwidth}
%    The default width of the deletebars is stored in the dimen register
%    \verb=\deletebarwidth=.
%    \begin{macrocode}
\newlength{\deletebarwidth}
\setlength{\deletebarwidth}{4pt}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\changebarsep}
%    The default separation between all bars and the text is stored in the
%    dimen register \verb=\changebarsep=.
%    \begin{macrocode}
\newlength{\changebarsep}
\setlength{\changebarsep}{30pt}
%    \end{macrocode}
% \end{macro}
%
% \begin{Var}{changebargrey}
%    When the document is printed using one of the PostScript drivers
%    the bars do not need to be black; with PostScript is possible to
%    have grey bars. The pecentage of greyness of the bar is stored
%    in the count register \verb=\changebargrey=. It can have values
%    between $0$ (meaning white) and $100$ (meaning black).
%
%    \begin{macrocode}
\newcounter{changebargrey}
\setcounter{changebargrey}{65}
%    \end{macrocode}
% \end{Var}
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
% \subsection{Macros for beginning and ending bars}
%
%
% \begin{macro}{\cb@start}
%    This macro is used to start a change bar.  It assigns a new value to
%    the current point and advances the counter for the next point to be
%    assigned.  It pushes this info onto \verb=\cb@currentlist= and then
%    sets the point by calling \verb=\cb@setBeginPoint= with the point number.
%    Finally, it writes the aux file.
%
%    \begin{macrocode}
\def\cb@start[#1]{\cb@currentpoint=\cb@nextpoint
        \@tempdima=#1\relax                             % for \cb@push
        \cb@push\cb@currentlist
        \ifvmode \cb@setBeginPoint\cb@currentpoint
        \else \vbox to 0pt{\vskip -\ht\strutbox         %jump up a line to
        \cb@setBeginPoint\cb@currentpoint               %set point
        \vskip \ht\strutbox}\fi
        \cb@writeAux\cb@advancePoint}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@advancePoint}
%    The macro \verb=\cb@advancePoint= advances the count register
%    \verb=\cb@nextpoint=. When the maximum number is reached, the
%    numbering is reset.
%    \begin{macrocode}
\def\cb@advancePoint{%
  \global\advance\cb@nextpoint by 2\relax
  \ifnum\cb@nextpoint>\cb@maxpoint
    \global\cb@nextpoint=\cb@minpoint\relax
  \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@end}
%    This macro is used to end a changebar.  It pops the current point and
%    nesting level off \verb=\cb@currentlist= and sets the end point by calling
%    \verb=\cb@setEndPoint= with the parameter corresponding to the
%    {\bf beginning} point number.
%    It writes the {\tt .aux} file and joins the points.
%
%    \begin{macrocode}
\def\cb@end{%
  \cb@pop\cb@currentlist
  \ifnum\cb@currentpoint=\cb@nil
    \typeout{Changebar Warning: Badly nested changebars;
                                Expect erroneous results}%
  \else
    \cb@setEndPoint\cb@currentpoint
    \advance\cb@currentpoint by1\cb@writeAux
  \fi}
%    \end{macrocode}
%\end{macro}
%
% \begin{macro}{\cb@setBeginPoint}
%    The macro \verb=\cb@setBeginPoint= is used to assign a position
%    to point number $\#1$. It determines wether the point is on an even
%    or an odd page and uses the right dimension to position the point.
%    Keep in mind that the value of \verb=\cb@pagecount= is one less than
%    the value of \verb=\c@page= unless the latter has been reset by the user.
%
%    \begin{macrocode}
\def\cb@setBeginPoint#1{%
  \ifodd\cb@pagecount
    \cb@defpoint{#1}{\cb@even}%
  \else
    \cb@defpoint{#1}{\cb@odd}%
  \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@setEndPoint}
%    The macro \verb=\cb@setEndPoint= is used to assign a position
%    to point $\#1+1$. It then instructs the driver to connect
%    $\#1$ and $\#1+1$ with a bar.
%    It is assumed that the width of bar is stored in \verb=\@tempdima=.
%
%    \begin{macrocode}
\def\cb@setEndPoint#1{%
  \@tempcnta=#1\advance\@tempcnta by1\relax
  \ifodd\cb@pagecount
    \cb@defpoint{\@tempcnta}{\cb@even}%
  \else
    \cb@defpoint{\@tempcnta}{\cb@odd}%
  \fi
  \cb@connect{#1}{\@tempcnta}{\@tempdima}}%
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@writeAux}
%    The macro \verb=\cb@writeAux= is used to write information about
%    a changebar point to the auxiliary file. The number of the point,
%    the pagenumber and the width of the bar are written out as arguments
%    to \verb=\cb@barpoint=. This latter macro will be expanded when the
%    auxiliary file is read in.
%    It is assumed that the width of bar is stored in \verb=\@tempdima=.
%
%    The code is only executed when auxiliary files are enabled.
%    It seems to be of no use trying to write to an unopened file.
%    \begin{macrocode}
\def\cb@writeAux{%
  \if@filesw
    \begingroup
      \edef\point{\the\cb@currentpoint}%
      \edef\level{\the\@tempdima}%
      \let\the=0%
      \edef\cb@temp{\write\@auxout
          {\string\cb@barpoint{\point}{\the\cb@pagecount}{\level}}}%
      \cb@temp
    \endgroup
  \fi}
%    \end{macrocode}
% \end{macro}
%
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
% \subsection{Macros for Making It Work Across Page Breaks}
% \label{pagebreak}
%
% \begin{macro}{\@makecol}
%
% Modifies the \LaTeX\ macros to end the changebars spanning the current
% page (if any) and restart them on the next page.  Does the
% following: It resets special points for this page.  Adds begin bars
% to top of box255.  The bars to be begun are saved in \verb=\cb@beginSaves=.
% Increments the changebar-internal page counter so that the value
% corresponds to the number of this page in strictly sequential order
% (the \LaTeX\ page number can be reset).  Then it builds the list
% \verb=\cb@spanlist=, then calls \verb=\cb@processActive= to process
%    the elements on the list, then it executes the original \verb=\@makecol=.
%
%    \begin{macrocode}
\let\cb@makecol=\@makecol
\def\@makecol{%
  \setbox\@cclv=\vbox{\cb@resetpoints\cb@beginSaves\unvbox\@cclv}%
  \gdef\cb@beginSaves{}
  \global\advance\cb@pagecount by 1\relax
  \cb@buildActive\cb@processActive
  \cb@makecol}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@processActive}
%
% Processes each element on span list.  Each element represents a bar
% that crosses the page break.  There could be more than one if bars are
% nested.  Works as folows:
%
% \begin{verbatim}
%       pop top element of span list
%       if point null (i.e., list empty) then done
%       else
%           do an end bar on box255
%           save start for new bar at top of next page in \cb@startSaves
%           push active point back onto history list (need to reprocess
%               on next page).
% \end{verbatim}
%
%    \begin{macrocode}
\def\cb@processActive{%
  \cb@pop\cb@spanlist
  \ifnum\cb@currentpoint=\cb@nil
  \else
    \setbox\@cclv=\vbox{\unvbox\@cclv\advance\cb@pagecount by -1\relax
                        \cb@setEndPoint\cb@currentpoint}%
    \cb@saveBeginPoint\cb@currentpoint
    \cb@push\cb@history
    \cb@processActive
  \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@saveBeginPoint}
%
%    Saves a \verb=\special= to begin a point in expanded macro
%    \verb=\cb@beginSaves=.
%    This is then used to start all spanning bars at the top of the next
%    page.  It is almost the same as \verb=\cb@setBeginPoint=.
%
%    \begin{macrocode}
\def\cb@saveBeginPoint#1{%
  \ifodd\cb@pagecount
    \xdef\cb@beginSaves{\cb@defpoint{#1}{\cb@even}\cb@beginSaves}%
  \else
    \xdef\cb@beginSaves{\cb@defpoint{#1}{\cb@odd}\cb@beginSaves}%
  \fi}
%    \end{macrocode}
%
%    \begin{macrocode}
\def\cb@beginSaves{}                % initially empty
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@buildActive}
%
% Initializes the spanlist to null.
%
%    \begin{macrocode}
\def\cb@buildActive{\cb@initlist\cb@spanlist\cb@pushNextActive}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@pushNextActive}
%    Pops top of history list.  If point is on future page,
%    push back onto history list.  If point on current
%    or previous page and odd, add point to span list; if even, pop span
%    list since this bar has terminated on current page.
%    \begin{macrocode}
\def\cb@pushNextActive{%
  \cb@pop\cb@history
  \ifnum\cb@currentpoint=\cb@nil
  \else
    \ifnum\cb@page>\cb@pagecount
      \cb@push\cb@history
    \else
      \ifodd\cb@currentpoint
        \cb@push\cb@spanlist
      \else
        \cb@pop\cb@spanlist
      \fi
      \cb@pushNextActive
    \fi
  \fi}
%    \end{macrocode}
% \end{macro}
%
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
% \subsection{Macros For Managing The Lists of Bar points}
%
% The macros make use of three lists corresponding to \verb=\special=
% defpoints.  Each list takes the form
%       {\tt <element> ... <element>}
%
%    Each element is of the form {\tt xxxnyyypzzzl} where {\tt xxx} is
%    the number of the special point, {\tt yyy} is the page on which
%    this point is set, and {\tt zzz} is the dimension used when
%    connecting this point.
%
%    The list \verb=\cb@history= is built from the log information and
%    initially lists all the points.  As pages are processed, points
%    are popped off the list and discarded.
%
%    The list \verb=\cb@spanlist= is a temporary list used by the
%    output routine and contains the list of all bars crossing the
%    current page (there may be more than one with nested bars).
%    It is built by popping elements off the history list.
%
%    The list \verb=\cb@currentlist= contains all the current bars.
%    A \verb=\cb@start= pushes an element onto this list.
%    A \verb=\cb@end= pops the top element off the list and uses the
%    info to terminate the bar.
%
% For performance and memory reasons, the history list, which can be
% very long, is special cased and a file is used to store this list
% rather than an internal macro.  The ``external'' interface to this
% list is identical to what is described above.  However, when the
% history list is popped, a line from the file is first read and
% appended to the macro \verb=\cb@history=.
%
%
% \begin{macro}{\cb@initlist}
% Initialize a list
%    \begin{macrocode}
\def\cb@initlist#1{\xdef#1{}}
%    \end{macrocode}
% \end{macro}
%
%  Initializations, etc.
%
%    \begin{macrocode}
\cb@initlist\cb@history         % the history list; initially empty
\cb@initlist\cb@spanlist        % list of bars spanning current page
\cb@initlist\cb@currentlist     % used to implement nesting without using
                                % TeX grouping

\newwrite\cb@write              % file for history list
\newread\cb@read
\immediate\openout\cb@write=\jobname.cb % open for building of history list
%    \end{macrocode}
%
%
% \begin{macro}{\cb@pop}
%
%    This pops the top element off the named list and puts the point value
%    into \verb=\cb@currentpoin=t, the page value into \verb=\cb@page= and
%    the bar width into \verb=\@tempdima=. If the list is empty,
%    returns a void value (\verb=\cb@nil=) in \verb=\cb@currentpoint=
%    and sets \verb+\cb@page=0+.
%
%    \begin{macrocode}
\def\cb@pop#1{%
  \ifx #1\cb@history
    \ifeof\cb@read
    \else
      {\endlinechar=-1\read\cb@read to\@temp
       \xdef\cb@history{\cb@history\@temp}%
      }%
    \fi
  \fi
  \ifx#1\@empty
    \cb@currentpoint=\cb@nil\cb@page=0\relax
  \else
    \expandafter\cb@carcdr#1e#1%
  \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@cardr}
%    Used to `decode' a list entry.
%    \begin{macrocode}
\def\cb@carcdr#1n#2p#3l#4e#5{%
  \cb@currentpoint=#1\cb@page=#2\relax\@tempdima=#3\xdef#5{#4}}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@push}
%
%    Pushes \verb=\cb@currentpoint=, \verb=\cb@page= and \verb=\@tempdima=
%    onto the top of the named list.
%
%    \begin{macrocode}
\def\cb@push#1{%
  \xdef#1{\the\cb@currentpoint n\the\cb@page p\the\@tempdima l#1}}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@barpoint}
%
% For populating the history file.
% Writes one line to {\tt .cb} file which is equivalent to one \meta{element}
% described above.
%    \begin{macrocode}
\def\cb@barpoint#1#2#3{\immediate\write\cb@write{#1n#2p#3l}}
%    \end{macrocode}
% \end{macro}
%
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
% \subsection{Macros For Checking That The {\tt .aux} File Is Stable}
%
% \begin{macro}{\document}
%
%    For these macros we need to modify the \LaTeX-command
%    \verb=\begin{document}=. The way to this is first save
%    the old definition of the macro.
%    \begin{macrocode}
\let\cb@document=\document
%    \end{macrocode}
%    Then it can be redefined including a call to the saved old definition.
%    While reading the {\tt .aux}-file \LaTeX{} has created the history
%    list in a separate file. We need to close that file and open it
%    for reading. Also the `initialistion' of the \verb=\special=
%    commands has to take place.
%    While we are modifying the macro we also include the computation
%    of the possible positions of the changebars
%
%    \begin{macrocode}
\def\document{\cb@document
              \cb@setup@specials
              \cb@positions
              \immediate\closeout\cb@write
              \immediate\openin\cb@read=\jobname.cb}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\enddocument}
%
%    Does a \verb=\clearpage= to flush rest of document.
%    Then closes {\tt .cb} file and reopens it for checking.
%    Inits history list (to be read from file).
%    Lets \verb+\cb@barpoint=\cb@checkhistory+ for checking.
%
%    \begin{macrocode}
\let\cb@enddocument\enddocument
%    \end{macrocode}
%
%    \begin{macrocode}
\def\enddocument{\clearpage\cb@initlist\cb@history
   \immediate\closein\cb@read\immediate\openin\cb@read=\jobname.cb%
   \let\cb@barpoint=\cb@checkHistory\cb@enddocument}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@checkHistory}
%
%    Pops the top of the history list (\verb=\jobname.cb=) and
%    checks to see if the point and page numbers are the same as the
%    arguments $\#1$ and $\#2$ respectively.  Prints a warning message if
%    different.
%
%    \begin{macrocode}
\def\cb@checkHistory#1#2#3{\cb@pop\cb@history
        \ifnum #1=\cb@currentpoint\relax
            \ifnum #2=\cb@page\relax  % do nothing
            \else \cb@error           % page numbers mismatched
            \fi
        \else \cb@error               % point numbers mismatched
        \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\cb@error}
%    When a mismatch between the changebar information in the
%    auxiliary file and the history list is detected a warning is issued;
%    further checking is disabled.
%    \begin{macrocode}
\def\cb@error{%
  \message{Changebar Warning: Changebar info has changed. %
                              Rerun to get right.}
  \gdef\cb@checkHistory##1##2##3{}%
  \let\cb@barpoint=\cb@checkHistory}
%    \end{macrocode}
% \end{macro}
%
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%
% \subsection{Macros For Making It Work With Nested Floats/Footnotes}
%
%
% \begin{macro}{\end@float}
%
% This is a replacement for the \LaTeX-macro of the same name.  All it
% does is check to see if changebars are active and, if so, it puts
% changebars around the box containing the float.  Then it calls the
% original \LaTeX\ \verb=\end@float=.
%
%    \begin{macrocode}
\let\cb@endfloat=\end@float
%    \end{macrocode}
%    \begin{macrocode}
\def\end@float{%
  \cb@pop\cb@currentlist
  \ifnum\cb@currentpoint=\cb@nil
  \else
    \cb@push\cb@currentlist
    \global\@tempdima=\@tempdima
    \egroup
    \global\setbox\@currbox=%
        \vbox\bgroup\cb@start[\@tempdima]\unvbox\@currbox\cb@end
  \fi
  \cb@endfloat}
%    \end{macrocode}
%
%    \begin{macrocode}
\let\endfigure=\end@float       % need to rebind these to new def
\let\endtable=\end@float
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\@footnotetext}
%
% Replacement for the \LaTeX\ macro of the same name.  Simply checks to
% see if changebars are active and if so wraps the macro argument
% (i.e., the footnote) in changebars.
%
% \changes{3.1b}{11-10-93}{Added missing percent sign to prevent
%                          spurious white space in the output.}
%    \begin{macrocode}
\let\cb@footnote=\@footnotetext
%    \end{macrocode}
%    \begin{macrocode}
\long\def\@footnotetext#1{%
  \cb@pop\cb@currentlist
  \ifnum\cb@currentpoint=\cb@nil
    \cb@footnote{#1}%
  \else
    \cb@push\cb@currentlist
    \edef\cb@temp{\the\@tempdima}%
    \cb@footnote{\cb@start[\cb@temp]#1\cb@end}%
  \fi}
%    \end{macrocode}
% \end{macro}
%
% \begin{macro}{\@mpfootnotetext}
%
% Replacement for the \LaTeX\ macro of the same name.  Same thing as
% \verb=\@footnotetext=.
%
% \changes{3.1b}{11-10-93}{Added missing percent sign to prevent
%                          spurious white space in the output.}
%    \begin{macrocode}
\let\cb@mpfootnote=\@mpfootnotetext
%    \end{macrocode}
%    \begin{macrocode}
\long\def\@mpfootnotetext#1{%
  \cb@pop\cb@currentlist
  \ifnum\cb@currentpoint=\cb@nil
    \cb@mpfootnote{#1}%
  \else
    \cb@push\cb@currentlist
    \edef\cb@temp{\the\@tempdima}%
    \cb@mpfootnote{\cb@start[\cb@temp]#1\cb@end}%
  \fi}
%    \end{macrocode}
% \end{macro}
%
%    Finally, the category code of {\tt @} is reset to its original
%    value. The macrospace used by \verb=\atcatcode= is freed.
%    \begin{macrocode}
\catcode`\@=\atcatcode \let\atcatcode\relax
%    \end{macrocode}
% %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% \Finale
\endinput
%% \CharacterTable
%%  {Upper-case    \A\B\C\D\E\F\G\H\I\J\K\L\M\N\O\P\Q\R\S\T\U\V\W\X\Y\Z
%%   Lower-case    \a\b\c\d\e\f\g\h\i\j\k\l\m\n\o\p\q\r\s\t\u\v\w\x\y\z
%%   Digits        \0\1\2\3\4\5\6\7\8\9
%%   Exclamation   \!     Double quote  \"     Hash (number) \#
%%   Dollar        \$     Percent       \%     Ampersand     \&
%%   Acute accent  \'     Left paren    \(     Right paren   \)
%%   Asterisk      \*     Plus          \+     Comma         \,
%%   Minus         \-     Point         \.     Solidus       \/
%%   Colon         \:     Semicolon     \;     Less than     \<
%%   Equals        \=     Greater than  \>     Question mark \?
%%   Commercial at \@     Left bracket  \[     Backslash     \\
%%   Right bracket \]     Circumflex    \^     Underscore    \_
%%   Grave accent  \`     Left brace    \{     Vertical bar  \|
%%   Right brace   \}     Tilde         \~}
%%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%