Documentation for CHANGE.BA

12/15/84 by Rick Perry

CHANGE.BA is a Model 100 utility program that incorporates menu driven directory access and manipulation, conversion of binary .CO files into ASCII Hex text .DO (and vice-versa), and also conversions between .CA Lucid Calcsheet files and .CO.

The program starts by displaying a complete RAM directory menu.  Press the arrow keys and/or spacebar & BKSP to position the cursor over a particular file name.

Press ENTER to "execute" the file, i.e. if it's a BASIC, ROM or M/L program (excluding Lucid, .CA's, and .CO's with Exe address of 0) it will be executed (for .CO's, HIMEM will be reset if necessary); if it's a text file you will go into TEXT.

Press LABEL to display info about the file, i.e. file type & start address, and Dfile length in bytes for non-ROM files, and Top, End, & Exe addresses for binary RAM files.  Typical display for SECURE.CO file is:

CO @ 45180 + 865  62101,62959,62101

indicating that file uses 865 bytes of RAM starting at address 45180.  The other available features are mostly function key driven:


(F1) >Hex   Change binary to hex text

When pressing F1, if cursor is currently over a RAM M/L file name, appropriate HIMEM space will be CLEARed, that file will be LOADMed automatically, and its Top, End, & Exe addresses used in the conversion.  If cursor is not over M/L file name, program will assume that you want to convert binary code that is already loaded between HIMEM & MAXRAM, and will prompt for desired Top, End, & Exe addresses (defaults are HIMEM, MAXRAM-1, & HIMEM; if code is not executable from main menu, enter Exe address as 0).

Program prompts for "Hex output file:"; enter name for .DO file which is to be created (can be CAS: or COM: etc.).  Null entry restarts program.  Format of Hex file is: Top, End, Exe decimal addresses on first line; following lines, up to 78 hex chars each, representing 39 bytes of binary code; decimal checksum on last line.  Checksum is calculated as sum of Top, End, Exe addresses plus the binary code byte values.

After conversion, if file was LOADMed by the program, HIMEM is reset to MAXRAM before restarting.


(F2) >Bin   Change hex text to binary

When pressing F2, if cursor is currently over a text file name, that file will automatically be used as input; otherwise, program prompts for "Hex input file:" (null entry restarts program) which can come from RAM, CAS: COM:, etc.

If Top address (read from hex input file) is less than HIMEM, then appropriate space will be CLEARed before continuing.  In this case, if input file name entry contained a colon (":"), you will be prompted to "Rewind input file".  This is necessary because the file must be CLOSEd & reOPENed before continuing, and, for example, if the input file was being taken from CAS:, you would need to rewind tape to start of file.

Next prompt is for ".CO out put file:"; enter name for .CO file which is to be created.  Null entry causes code to be loaded into RAM above HIMEM, but not SAVEMed as additional RAM file.

After conversion, if hex input file name did not contain colon (":"), "Kill hex input file?" prompt appears.  Press "Y" or "y" and input file will be KILLed before SAVEMing the .CO.  This feature is provided in case you don't have sufficient free space to keep both the hex & .CO in RAM.

If .CO output file name was specified, HIMEM is reset to MAXRAM after SAVEMing, before restarting.


(F3) >CA   Change .CO file to .CA Lucid Calcsheet

This function should only be applied to Lucid Calcsheet files previously changed from .CA to .CO using function F4 of this program.  The program can't absolutely check that the M/L file, on which the cursor is positioned, had a .CA origin.  But if the file is not M/L type, or if its End address is not MAXRAM-1, or if its Exe address is not 0, then conversion won't be attempted and program will just make a nasty buzz sound.

Assuming the cursor was positioned over a valid file when pressing F3, three things will happen: Top address of file will be changed to 65535, Exe address changed to 63012, and extension changed to "CA".


(F4) >CO   Change .CA Lucid Calcsheet file to .CO

Program checks that file, over which the cursor is positioned, is M/L type with Top address of 65535 & Exe address of 63012.  If so, three things happen: Top address of file will be changed to MAXRAM minus number of bytes of code in file, Exe address changed to 0, and extension changed to "CO".  Resulting file can then be LOADMed, etc. from BASIC, and processed via F1 (>Hex) and F3 (>CA) functions of this program.


(F5) Name   Change file names and extensions

Cursor should be positioned over target file before pressing F5.  Program prompts for "New name:", then "New extension:".  Null entry leaves name or extension unchanged.

This function does not use the BASIC NAME command, rather it pokes the new file name directly into the RAM directory. Thus, you can do strange things, like use lowercase names, blank extensions, etc.  It is not advisable to change extensions from one type to another (e.g. from BA to DO).  Also, note that use of lowercase file names and/or wierd extensions, will prevent files from being accessed via BASIC, although they should still be available from the M100 main menu.


(F6) Invs   Change file visibility status

As you move the cursor around on the program menu, the "Invs" key label will change to inverse video if a file has been set invisible.  Press F6 to switch the visibility status of any file.

Cautions regarding access to invisible files:

Only invisible BASIC files can be accessed safely directly from the M100 main menu by typing in the name at the "Select:" prompt.  Invisible text files can be accessed by first going into TEXT, then entering the file name.  Invisible M/L files can still be LOADMed and/or RUNMed from BASIC.  Invisible ROM programs can be accessed via CHANGE program or by CALLing the appropriate address from BASIC.


If you try to make Lucid invisible, the program will remove it from the menu completely, same as CALL 63012,0,1 per Lucid manual.


(F7) Kill   KILL a file

Program prompts "Kill?" regarding file over which cursor is positioned.  Press "Y" or "y" if you really want the file KILLed.

Note that an error occurs in attempting to KILL a file whose name is unacceptable to BASIC.


(F8) Menu   Return to M100 Main Menu


Additional information:

The program uses an ON ERROR GOTO to detect and display (but not recover from) errors.  The most common types of possible errors occur when trying to process a file whose name has been altered to a form unacceptable to BASIC.  After seeing an error message display, press ENTER to restart the program, or press any other key to exit to BASIC.

You may want to extract some of the code from this program in order to include similiar features in your own programs. Also, since the functions are fairly modular, you can easily eliminate unwanted functions by replacing the appropriate subroutines with RETURNs.  Please feel free to do so.

Some things I think are neat: the display of two character BASIC error message in error handling section; file menu display (that code was adapted from a program by Jesse Bob Overholt; possible modification for use in other applications would be to check the file type code byte or file extension and only display certain files (e.g. BA or DO) in menu form for selection by user).

Watch out for invisible files Suzuk.i (BASIC program with no name) and Hayas.hi (the PASTE buffer).  It's Ok to rename and/or "execute" them, but if you go into TEXT with Hayas.hi, don't use Select, Cut, Copy, or Paste keys.

Lucid users may notice a file, "4 PCS.G", which is the Calcsheet formula paste buffer.  This can be renamed as something.CO and then KILLed if desired.


Final warning!!!

Be careful in using this program.  Nasty cold-start consequences may follow abuse.  Used properly, it is safe.