C-KERMIT FOR OS-9/68KVersion: 5A(188)Date:    November 23, 1992Adapted to OS-9 by Christian Hemsing, RWTH, Aachen, GermanyE-Mail: CHRIS@LFM.RWTH-AACHEN.DEOS-9/68K C-Kermit Capabilities at a Glance:  Local operation:                   Yes  Remote operation:                  Yes  Transfer text files:               Yes  Transfer binary files:             Yes  International text:                Yes  Wildcard send:                     Yes  File transfer interruption:        Yes  Filename collision actions:        Yes  Can time out:                      Yes  8th-bit prefixing:                 Yes  Repeat count prefixing:            Yes  Alternate block checks:            Yes  Automatic parity detection:        Yes  Dynamic packet length:             Yes  CONNECT mode:                      Yes  Terminal emulation:                No (uses console driver)  Communication settings:            Yes  Transmit BREAK:                    Yes  Support for dialout modems:        Yes  TCP/IP support:                    No  X.25 support:                      No  IBM mainframe communication:       Yes  Transaction logging:               Yes  Session logging:                   Yes  Debug logging:                     Yes  Packet logging:                    Yes  Act as server:                     Yes  Talk to server:                    Yes  Advanced server functions:         Yes  Security for server:               Yes  Local file management:             Yes  Command/Init files:                Yes (Init file: .kermrc)  Long packets:                      Yes  Sliding Windows:                   Yes  File attributes packets:           Yes  Command macros:                    Yes  Script programming language:       Yes  Raw file transmit and capture:     YesOS-9/68K BACKGROUNDOS-9/68k is a multiuser, multitasking operating system designed to run onall Motorola 680x0 family processors from Microware Systems Corporation, 1900N.W. 114th Street, Des Moines, Iowa 50332 (Trademarks: Microware, OS-9,OS-9/68000, OS-9000).Due to its modular design, most of the code is completely hardwareindependent, so it can be easily be ported to a different hardware by writingnew device drivers.The original (1980) OS-9/6809 was designed for the Motorola 6809 processor.Later (1983) they switched to the 680x0 family and released OS-9/68000.  Forspeed and compactness reasons most of the OS-9/68000 kernel is written in680x0 assembler language.  Now there is a so-called OS-9000 by Microware.  Itskernel is written in C and thus it is portable.  It is presently available for680x0 and Intel's 80386/486, and Microware plans to add further support forRISC and CISC processors.  (C-Kermit has not yet been tested under OS-9000.)The 100% ROM-able, fast, compact code in conjunction with real-timecapabilities make OS-9/68k ideal for ROM-based systems used in measuring,controlling, etc.  It has found a wide acceptance within the scientific andindustrial world.Yet, a full disk based OS-9/68k offers a program development environmentsimilar to UNIX. This includes (of course, limited) UNIX sofware compatibilityat C source code level, source code level debugging, UNIX I/O model, UNIX task model, UNIX-like shell and networking.A number of UNIX utilities like lex, yacc, lint, etc, have been ported toOS-9/68k.The basic commands of OS-9 are:  DEL     delete a file  DELDIR  delete a directory  MAKDIR  create a directory  DIR     directory listing  PROCS   show currently running processes  LIST    type contents of a text file  CWD     change working directory  PD      print working directoryAll commands can be given a "-?" as a switch, which will display a brief(usually sufficient) help message.All command references (like all references to names on OS-9/68k) are NOTcase sensitive (switches, though, may be case sensitive since they areinterpreted by the running program).On OS-9 systems you can redirect stdin, stdout, stderr just like in UNIX,and you can run programs (including Kermit) in the background.Pipelines work just like in UNIX.OS-9 doesn't know anything about character sets; all messages are in Englishusing ascii.OS-9 does not generally have windows etc. (windows has been ported by someone,though). You can't really say anything about the terminal emulation.Many systems don't even have a console, but only RS232 lines, with noaction by th driver whatsoever. So it depends on the terminal conncted tothat line.In case a display is already part of the machine, then it depends on thevendor (which usually also does the portation), which emulation the consolewill have. E.g. I have ported OS-9 to Atari, which includes a VT52 emulationon the console.OS-9 is really meant to be ported, so no restrictions are given.OS-9/68K DEVICESAll devices (terminal lines, networks, disks) can have arbitrary names butthe usual convention is: Terminal lines:   term  the console terminal   t1    terminal line #1   :   tn    terminal line #n Harddisks:   h0    hard disk #0   h1    hard disk #1   :   hn    harddisk #n Floppy disks (diskettes):   d0    floppy disk drive #0   d1    floppy disk drive #1   :   d0    floppy disk drive #nA path name starting with a slash ("/") must always include a device nameas the first field.  For example, the C-Kermit command SET LINE /T3 wouldselect the terminal line /t3.The console terminal is either a real terminal, or the screen and keyboard ofa workstation such as a Macintosh, Amiga, or Atari ST that is running OS-9.Terminal emulation is not done by OS-9 C-Kermit, but rather by the realterminal or the workstation console driver.  This includes the capability todisplay national and international characters.THE OS-9/68K FILE SYSTEMThe file system is tree-structured just like the UNIX file system.  /h0/chrismeans the directory  or file "chris" on hard disk #0.  chris/rubbishmeans the subdirectory or file "rubbish" in the subdirectory "chris" of thecurrent directory.The command "chd" without any parameters will always take you to your homedirectory.Wildcard expansion is performed by the shell with two metacharacters:  * stands for an arbitrary string of arbitrary length  ? denotes a single characterC-Kermit/OS-9 also expands wildcards itself, using the same notation, forexample:  C-Kermit>send ck*.\?(Note: the question mark must be prefixed by "\" to override its normalfunction of giving a help message.)OS-9/68k files are sequential streams of 8-bit bytes, just like in UNIX,except that carriage return (CR, ASCII 13) is the line terminator, rather thanlinefeed (LF, ASCII 10).  Binary files are simply streams of arbitrary 8-bitbytes.  The OS-9 operating system and utilities are "8-bit clean", so textfiles can use any ASCII-based character set that is compatible with yourdisplay and data entry devices, for example ISO 8859-1 Latin Alphabet 1.Unlike UNIX, OS-9/68k has a built-in method to gain exclusive access todevices, so no lock files are needed.  The user will be told if the device isalready in use.TO BUILD C-KERMIT FOR OS-9:Collect all the C-Kermit source files into a directory:  ckc*.c, ckc*.h, cku*.c, cku*.h, ckwart.c, ckcpro.w, ck9*.*There are two makefiles: ck9ker.mak and ck9ker.gcc.  If you have a runningversion of the GNU C compiler, use ck9ker.gcc (it produces smaller, moreefficient code); otherwise use ck9ker.mak which uses the standard OS-9/68k Ccompiler.  Read the appropropriate makefile, edit the necessary changesmentioned there, create the subdirectories, and make the new Kermit by typing:  make -f=ck9ker.makor:  make -f=ck9ker.gccRead the "beware file" ck9ker.bwr for hints relating to the OS-9 terminaldriver.USING OS-9 C-KERMITThe commands and operation of OS-9 C-Kermit should be identical to those ofUNIX C-Kermit, with the exceptions noted above and in the "beware file".  Theuser documentation for C-Kermit is:  Frank da Cruz and Christine M. Gianone, "Using C-Kermit", Digital Press,  Burlington, MA, 1993, approx. 500 pages.      Order Number: EY-J896E-DP    Digital Press ISBN: 1-55558-108-0    Prentice Hall ISBN: 0-13-037490-3  US single-copy price: $34.95; quantity discounts available.  Available in  computer bookstores or directly from Digital Press.  In the USA, call  Digital Press toll-free 1-800-344-4825 to order; major credit cards  accepted.  Overseas, order through your bookstore or your local Digital  Equipment Corporation branch.  Can also be ordered from:    Kermit Development and Distribution    Columbia University Center for Computing Activities    612 West 115th Street    New York, NY  10025  USA    Telephone: (USA) 212 854-3703(END OF CK9KER.DOC)