Take note of the following change in the PCI Devices screen on
page 3-19 of the PI16 User’s Guide.

PCI Devices

PCI Device, Slot #1:

Enable Master:	[Enabled]
Use Default Latency Timer Value:	[Yes]
Latency Timer Value:	[0040]

PCI Device, Slot #2:

Enable Master:	[Enabled]
Use Default Latency Timer Value:	[Yes]
Latency Timer Value:	[0040]

PCI Device, Slot #3:

Enable Master:	[Disabled]
Use Default Latency Timer Value:	[Yes]
Latency Timer Value:	[0040]

PCI Device, Slot #4:

Enable Master:	[Disabled]
Use Default Latency Timer Value:	[Yes]
Latency Timer Value:	[0040]

PCI IRQ Line 1: [Auto Select] PCI IRQ Line 2: [Auto Select] PCI IRQ Line 3: [Auto Select] PCI IRQ Line 4: [Auto Select]

Move Esc Exit PgUp Previous Value F5 Previous Configuration F1 Help PgDn Next Value F6 Default Configuration

PCI IRQ Line 1 to Line 4

These parameters allow you to specify interrupts for PCI devices to avoid IRQ assignment conflict with non-PnP ISA devices.  The selections for these parameters are 5, 6, 9, 10, 11, 12, 14, 15, Auto, and Disabled.

Make sure not to assign a PCI device with any IRQ currently in use by a non-PnP ISA device.

Use the selection Auto Select only if no non-PnP ISA devices are installed in your system.