Floppy.device 1.0 © 1995 by OR
              ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

                      INTRODUCTION

   An improvement over the trackdisk.device.
   It's freeware.


 REQUIREMENTS:
 KS2.0+, 8372 Agnushr+


 TESTED AT THESE SYSTEMS:
 A1200, internal floppy drive 

 
 
                       FEATURES

  - Trackdisk compatible.
  - 16% faster data access than trackdisk.
  - 9% big disk size than trackdisk.
  - Supports only 1MB capacity drives (this release only).
  - Bootable and nonbootable versions available.




                    PROGRAMING INFO
                 
  - AbortIO() function returns IOERR_NOCMD.
  - ETD_XXX, TD_RAWREAD, TD_RAWWRITE commands not supported.
  - DiskChange interrupt work for all devices.
  - Blitter stuff is done by QBlit() like trackdisk.
  - Do not forget to update before TD_MOTOR-off command.
  - CMD_CLEAR and CMD_UPDATE commands only affects floppy.device buffers.
  - TD_FORMAT command firstly updates and clears buffers, and doesnt
    verifies and buffers will be stay in cleared.      
  - TD_REMOVE command is supported but should not be used.  
  - CMD_UPDATE & CMD_WRITE commands verifies the written track
    (no comparing).
  - No drive clicks.
  - Retry count is zero.
  - Two track buffers (lower and upper sides of current cylinder).
  - Phisical track range is 12596<>12730 bytes (mfm) assumed.
  - Dos will call CMD_UPDATE and CMD_CLEAR commands after disk removed     
    (if mounted). At this time, if buffers were not updated disk-light will
    blink and buffers will be cleared.



                      INSTALLATION

    Copy nonbootable/floppy.device or bootable/floppy.device to
    Devs: directory.
    Copy FS0 and FS0.info to Devs:DosDrivers directory.
    Double click the FS0 icon to mount the drive or it can be used
    standalone.



                     HINTS AND TIPS
 
  - Nonbootable version may be a little bit faster than the bootable 
    version if a fast memory exist in the system ($C00000 may not a real
    fast memory..).
  - Do not use bootable version in A500/A2000 which have 1MB chip memory,
    due to clearing beyond of the first 512KB chip memory after reset.
  - Sometimes after mount command the device handler will be not
    activated. You may use DiskChange command.
  - 'Avail flush' command removes the device from memory if it is
    available.
  - 'Assign FS0: dismount' command is available.

    


 Disk size:
  
  Drive capacity  floppy format  trackdisk format  PC format  
  --------------  -------------  ----------------  ---------
       1MB             960KB          880KB           720KB 
       2MB            1960KB         1760KB          1440KB
       4MB            3920KB         3520KB          2880KB



     Email address:
     Bitnet:   PROHST03@TREARN
     Internet: PROHST03@VM3090.EGE.EDU.TR
*<>*