NOTE TO DOUG:
	Streams are not implemented yet.  The maximum packet size is 8K+256
	bytes.	See iopar.c for example code.

	Note that the io requests (see parnet/devices/parnet.h) have a
	secondary io_Data2 and io_Length2 field which allows you to write
	from two buffers and read into two buffers... to prevent even more
	buffer copying.  Be sure that said fields are NULL/0 when not used.

	AbortIO() works with CMD_READ requests for the datagram protocol.
	The protocol and port must always be specified at OpenDevice() time,
	while io_Addr (at least for datagrams) may be set on a per-io-request
	basis.	I picked an arbitrary port for iopar.c ... a connection going
	the other direction can be had by using a different port.

	Collision Warning:  DGRAMS are not reliable when collisions are
	possible.  However, you will know when the write fails (io_Error will
	return non-zero) so you *can* setup some code to retry if you wish.
	This is pretty much required if you intend to allow cross-mounting
	and stick with the DGRAM protocol.

	Eventually we may want to move to a STREAM protocol... once it gets
	implemented.  But then again, datagrams are so efficient you might
	not.  I dunno.	The CONNECT/LISTEN stuff applies only to the STREAM
	protocol which has not been implemented yet.

				-Matt


			    PARNET.DEVICE DOC

			     GENERAL OVERVIEW

    The parnet.device driver works with one or MORE Amigas connected together
    via a common, custom parallel port cable.  Refer to doc/Cable.DOC for
    information on how to construct the cable.	Taking overhead into account
    communication runs at about 23KBytes/sec (230KBaud).

    The limits of the network have not been determined yet, I have only been
    able to test it with two Amiga's.  I am almost positive that it would
    work with three or four Amigas assuming somebody takes the time to
    construct the cableing.

    The network is based on machine addresses and rendezvous ports.  Each
    machine on the network must have a unique address in the range 1-254.
    0 and 255 are reserved.  This network has no broadcast capability.

    Multiple connections may exist between any two machines.  Each packet
    contains a destination port number as well as a destination address.
    Port numbers are unsigned words and may take on the value 0x0000 to
    0x7FFF (0x8000-0xFFFF are reserved for stream connections).

    A number of protocols may be used:

	(1) Control Protocol, used for sending control commands to the
	    device rather than packets over the network.  Not really
	    a protocol.

	(2) DATA-GRAM Protocol, used for sending semi-reliable data between
	    machines.

	(3) STREAM Protocol, used for sending reliable data between machines.


				DATAGRAMS

    To use the datagram protocol you must specify the port number in the
    OpenDevice() command.  Once you successfully open the device you may
    issue CMD_READ and CMD_WRITE's to the device.  CMD_WRITE Iobs must
    have a valid destination address in io_Addr.  You may modify this address
    at any time before sending off the request.

    When a machine receives a datagram packet it copies it to the currently
    pending CMD_READ request.  If you have not queued any CMD_READ requests
    the packet is LOST.  The sending machine does not know whether a packet
    it sends is thrown away or used.  I REPEAT, If there is no CMD_READ
    request queued for a given port any packet sent to that port will be
    lost!!!!

    Normally one uses datagrams to implement one's own high level stream
    protocol.  Using datagrams has very low cost and, in fact, using
    synchronous IO (DoIO()) will in many cases be able to send the packet
    without doing a task switch.  Normally when one uses datagrams in this
    manner one has several CMD_READ requests queued.  Never assume that
    the receiving machine can keep up with the rate the sending machine
    can send (this is normally fixed by having the sending machine wait for
    an ack of some sort).

    Finally, blocking is maintained.  If the remote machine sends a 256 byte
    packet and your pending CMD_READ can only handle 25, then only 25 bytes
    will be copied and the rest thrown away.  If you CMD_READ can handle,
    say, 300, then all 256 bytes will be copied.  The maximum packet size
    is 4KBytes.


				  STREAMS

    The Stream protocol provides the following services:

	    - No loss of data
	    - Data is reliable
	    - No blocking factors
	    - Rate Control

    Openning a stream protocol connection is a two step process.  You must
    specify a valid stream port in the OpenDevice() command.  OpenDevice()
    will fill in the io_Unit field for that port.  The resulting Iob may
    then be used to issue PPD_CONNECT and PPD_LISTEN commands.

    To connect to a remote machine copy the Iob to a new Iob (so the old
    one is saved) and issue a PPD_CONNECT command using the new Iob.  The
    stream protocol will arbitrate a connection with the remote machine
    and then put that connection onto a dynamically determined port (in
    the 0x8000-0xFFFF range), modifying the io_Unit field of the request
    if the PPD_CONNECT is successful.  Further communication for that
    connection must occur using the modified Iob.  That is, once a
    connection is established further communication occurs on a different
    port.

    You may still issue PPD_CONNECT and PPD_LISTEN commands on the original
    Iob for the port.  Multiple tasks may open the same stream port but if
    more than one task attempts a PPD_LISTEN then the task that actually
    gets an incomming connection is indeterminant.

    To allow a remote machine to connect to a stream port you must issue a
    PPD_LISTEN request in the same manner as the PPD_CONNECT request.
    The PPD_LISTEN request waits for an incomming connection.  If you expect
    to get several incomming connections at once you may want to issue
    several PPD_LISTEN requests.  PPD_LISTEN returns when an incomming
    connection is established and the io_Unit field is modified.  Further
    communication for that connection must occur using the modified Iob.

    You may CloseDevice() the original io_Unit without having to
    CloseDevice() connected units.  You MUST CloseDevice() a connected
    unit when done with the connection.  That is, once a connection is
    established it is independant of the original rendezvous port.

    Reading and Writing to a stream unit works somewhat like reading and
    writing the serial port except that the data is reliably transmitted.
    CMD_WRITE requests may block if the receiving machine's buffer is full.
    CMD_READ requests block until at least 1 byte of data is available
    then return immediately.  NO DATA IS LOST if new data comes in before
    you can queue a CMD_READ request, and it is impossible for the sender
    to overload the receiver.  You may also issue arbitrarily sized writes
    but remember that all blocking factors are removed.  Issuing a 200 byte
    write does not guarentee that all 200 bytes will be sent in the same
    low level packet.

			    IO COMMANDS


    PPD_SETADDR     This command sets our network address and may be sent
		    to any valid unit and always effects the entire device.

		    Valid addresses range from 1 to 254.  This command may
		    be sent via any unit.

    PPD_SETTO	    This command sets our network timeout and works like
		    PPD_SETADDR.. might be required when configuring with
		    faster processors due to timeout loops in the low level
		    packet send (the only way to make it go fast). This
		    command may be sent via any unit.

    PPD_SHUTDOWN    This command effects only connected STREAM units and
		    shutsdown one or both sides of the connection without
		    deallocating the unit structure.  It may be used to
		    send an EOF to other side, for example, or to inform
		    the other side that you are no longer receiving.

		    Set io_Flags to:	0x01	no more reads
					0x02	no more writes (send EOF)
					0x03	both

    PPD_CONNECT     This command effects only unconnected STREAM units
		    (returned by OpenDevice) and allocates a port and
		    establishes a stream connection on it, returning the
		    new port and io_Unit if the connection is successful.

		    Several PPD_CONNECT commands may be queued to the device
		    at once.

		    On success, remember that the modified Iob is a completely
		    different Unit that must be CloseDevice()d to terminate.

    PPD_LISTEN	    This command effects only unconnected STREAM units
		    as PPD_CONNECT and waits for a connection to be
		    established by a remote host, returning only when the
		    connection is established.	As in PPD_CONNECT a new
		    io_Unit is allocated for the connection.

		    Several PPD_LISTEN commands may be queued to the device
		    at once and mixed with PPD_CONNECT commands (i.e. they
		    are independant).  Note that in some cases you want to
		    queue more than one in case several remote connect
		    requests occur at once.

		    On success, remember that the modified Iob is a completely
		    different Unit that must be CloseDevice()d to terminate.