HP-48SX Questions, Answers, & Useful Tidbits 
 
 
     This list contains information which has not necessarily been verified, 
and is not guaranteed to be correct, or even reflecting reality.  It was 
compiled from various postings in comp.sys.handhelds, as well as other 
sources.  Also note that, while the maintainer is an employee of 
Hewlett-Packard, this list is not officially sanctioned by Hewlett-Packard 
(the maintainer is doing this on his own time, and has absolutely no 
connections with the HP division that makes calculators). 
 
Please send any comments or suggestions to: 
 
        Darryl Okahata 
        Internet: darrylo%hpnmd@relay.hp.com 
        CompuServe: 75206,3074 
 
Summary of questions: 
 
 1* I'm a novice, and I have some questions.  Where should I start? 
 2* How can I tell what ROM revision I have? 
 3* What bugs exist in the various versions of the HP-48SX? 
 4* What is \->ASC or ASC\->? 
 5* How can I get \->ASC and \->ASC? 
 6* Why does my HP-48SX occasionally "freeze" for a moment? 
 7* Why does (1/3)*3 equal 0.999999999999? 
 8* I want `pi' to be a numeric value, not a symbol.  What's happening? 
 9* If I add two temperatures like 34 deg.F and 11 deg.F, I get 504.67 deg.F. 
    Why don't I get 45 deg.F? 
10* Why do I get corrupted binary files with kermit? 
11* My RAM card was plugged into the calculator when I changed the RAM card 
    battery, yet I lost all the information on the card.  What happened? 
12* Why do I get an "Invalid card data" error when I merge a RAM card? 
13* My HP-48SX seems to take longer to turn on and off.  What's going on? 
14* I can't account for some of the RAM in the HP-48SX (I can't tell where 
    it's being used).  What's going on? 
15* How do I get rid of the HYDE library? 
16* How can I transfer programs/data from my HP-28S to my HP-48SX? 
17* I could speed up my HP-28S.  How can I speed up my HP-48SX? 
18* Why does the HP-48SX display flicker slightly? 
19* I've heard that other manufacturer's RAM cards will work with the HP-48SX. 
    Is this true?  Will it work? 
20* What library ID numbers have already been used? 
21* What do the funny symbols \->, \GS+, etc., mean? 
22* What tricks are there for manipulating matrices? 
23* How do I store fields of variable length string data in a compact, rapidly 
    accessible manner that does not require the overhead of storing strings in 
    lists? 
24* What is "Vectored Enter", and how do I use it? 
25* How can I tell, from within a program, if the battery is low? 
26* I've heard the names "RPL", "Saturn", "STAR", "Voyager", etc..  What do 
    they mean? 
27* Appendix A: ASC\-> and \->ASC functions: 
28* Appendix B: Using non-HP RAM cards in your HP-48SX: 
29* Appendix C: Compact Data Storage: 
30* Appendix D: Various useful functions 
 
 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 1* I'm a novice, and I have some questions.  Where should I start? 
 
  Start by perusing the HP-48SX manuals. 
 
  Also, look over the section "Answers to Common Questions", in Appendix A 
(Volume II) of the manual. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 2* How can I tell what ROM revision I have? 
 
  Do the following: 
 
  1. Turn the calculator on (press ON and then release). 
 
  2.  Press ON again, and while holding it down, hit the "D" key (the fourth 
     white key in the top row) and then release the ON key.  You should get 
     three vertical lines in the display, one down the middle.   
 
  3.  Hit the backspace key (it says DROP and CLR over it).  You should get 
     some meaningless hexadecimal in the first line of the display.  (Mine says 
     705D9:1B8D...). 
 
  4. Press and hold down the EVAL key.  It should say: 
 
        Version HP48-* 
        Copyright HP 1989 
 
     where the * is an uppercase letter (A, B, etc.) indicating 
     the ROM version. 
 
  5. Release the EVAL key.  Hold down ON and hit "C" (the third white key in 
     the top row.  This is a general reset operation that returns the 
     calculator to normal from the diagnostic stuff (which is where ON-D puts 
     you). 
 
  (The above was mostly taken from a posting by Mark Adler -- 
  madler@tybalt.caltech.edu) 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 3* What bugs exist in the various versions of the HP-48SX? 
 
   Version(s)   Bug 
  ---------------------------------------------------------------------- 
      A         DEFINE rounds numbers in user-defined functions if STD 
                is not the current display mode. 
 
      A         KGET on a zero length file from another machine will 
                cause the calculator memory to be cleared. 
 
      A         NXEQ from the Graphics Environment with flag -3 set (SYM 
                off in Modes) can overwrite the current equation with a 
                number. 
 
      A         Displaying the clock in 24-hour format causes the 
                one-digits for minutes to be incorrect in the alarm 
                catalog. 
 
    A,B,C       INV returns an incorrect result if used on an 8x8 or 
                larger matrix.  To get around this problem, divide the 
                identity matrix with the matrix to invert. 
 
   A,B,C,D      Entering a symbolic complex number in polar form like 
                '(A,<B)' (where < is really the funny little angle 
                symbol), gives an expression in A and B that is wrong 
                (the A and B are interchanged so A is the angle and B is 
                the magnitude). 
 
   A,B,C,D      If the clock is displayed during an ARCHIVE via RS-232, 
                there is a chance (not 100%) that calculator memory will 
                be cleared, after the transfer.  The workaround is to 
                turn the clock display off before doing the transfer. 
 
   A,B,C,D      TRNC and RND allow for an array in level 2 and a 
                symbolic in level 1 of the stack. This allows you to put 
                an array in a symbolic.  Example: 
 
                                [ 2 3 ] 
                                '7/8' 
                                RND 
                 
                returns 'RND(UNKNOWN,7/8)' 
 
  (The above was mostly copied from postings by Mark Adler 
  (madler@tybalt.caltech.edu) or Jurjen NE Bos (jurjen@cwi.nl).) 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 4* What is \->ASC or ASC\->? 
 
  These functions were written by William Wickes to facilitate transferring 
  HP-48SX binary objects in an ASCII format (useful when transferring objects 
  via electronic mail).  Some HP-48SX objects, like libraries, cannot normally 
  be converted into ASCII, unlike program objects, and these functions make it 
  possible to do so. 
 
  The \->ASC function converts the object in level 1 into an ASCII string, 
  which can then be uploaded to a computer for mailing. 
 
  The ASC\-> function converts the string object in level 1 back into an 
  object.  A checksum is used to insure that the decoding is correct. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 5* How can I get \->ASC and \->ASC? 
 
  A copy of these programs are given in Appendix A, near the end of this 
  file. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 6* Why does my HP-48SX occasionally "freeze" for a moment? 
 
  The HP-48SX must occasionally do "garbage collection" to free up unused 
  memory, and it is this garbage collection that is causing the momentary 
  "freeze".  "Garbage collection" is where the HP-48SX scans through memory, 
  looking for objects that are no longer used.   
 
  Using less stack supposedly makes garbage collection go faster. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 7* Why does (1/3)*3 equal 0.999999999999? 
 
  This is due to the way numbers are typically represented by computers and 
  calculators.  There are some numbers, like `1/3' and `pi', that cannot be 
  exactly represented internally.  As a result, any calculations that use these 
  numbers are bound to be off.   
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 8* I want `pi' to be a numeric value, not a symbol.  What's happening? 
 
  You are using "Symbolic Results Mode".  To turn this mode on or off, go to 
  the MODES menu (press orange/left-shift MODES), and press the "SYM" softkey. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
 9* If I add two temperatures like 34 deg.F and 11 deg.F, I get 504.67 deg.F. 
  Why don't I get 45 deg.F? 
 
  If the units attached to the number consists only of a temperature and 
  nothing else, operations are done using an absolute temperature scale 
  (relative to absolute zero).  If the units consists of a temperature and 
  something else, such as degrees/minute, the operation will not be done using 
  an absolute temperature scale. 
 
  It also does not make any physical sense to add two temperatures.  You can't 
  add a cup of water at 20 degrees C to a cup of water at 30 degrees C and end 
  up with two cups of water at 50 degrees C. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
10* Why do I get corrupted binary files with kermit? 
 
  Some versions of kermit distinguish between ASCII and binary files, and so 
  you have to worry about the transfer modes at *BOTH* ends of the connection 
  (the HP-48SX end and the computer end).  For example, when receiving ASCII 
  files, Unix kermit must translate CR/LF pairs into LF.  If the HP-48SX is 
  transmitting a binary file, but the Unix kermit is expecting ASCII, any CR/LF 
  pairs in the binary file will get translated to LF, corrupting the binary 
  file.  Unfortunately, you cannot "uncorrupt" the corrupted binary file by 
  simply reversing the transfer and expecting kermit to translate LF to CR/LF. 
  This is because the binary file may contain occurrences of LF that were not 
  originally part of a CR/LF sequence.   
 
  Kermit running on IBM PC clones do not have to translate any incoming CR/LF 
  pairs, which is why you do not see this problem there. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
11* My RAM card was plugged into the calculator when I changed the RAM 
  card battery, yet I lost all the information on the card.  What 
  happened? 
 
  You forgot to turn ON the calculator before changing the battery.  The 
  HP-48SX only supplies power to the RAM card while the HP-48SX is turned on. 
  While the calculator is turned off, no power is supplied by the calculator, 
  and all power comes from the RAM card battery.  If you then take out the 
  battery from the RAM card while the calculator is turned OFF, the RAM card 
  has no source of power, and you will lose all of the contents in the RAM 
  card. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
12* Why do I get an "Invalid card data" error when I merge a RAM card? 
 
  This message is usually seen when you plug a brand-new RAM card into an 
  HP-48SX.  In this case, this message is normal and is harmless.  It just 
  means that there was no (valid) data on the card. 
 
  If you see this message under any other conditions, it could be one of the 
  following: 
 
     1. You took the battery out of the RAM card while the card was out 
        of the calculator. 
 
     2. You took the battery out of the RAM card while the card was in 
        the calculator *BUT* the calculator was turned off. 
 
     3. The RAM card battery is dead. 
 
     4. There is a problem with either the calculator, the RAM card, or 
        both. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
13* My HP-48SX seems to take longer to turn on and off.  What's going on? 
 
  The usual causes for this are RAM/ROM cards and libraries.  When you turn the 
  calculator on, it checks RAM (the more you have, the longer it takes), and 
  checks to see if any libraries need initializing. 
 
  Also, having a lot of alarms can supposedly also cause this.   
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
14* I can't account for some of the RAM in the HP-48SX (I can't tell where 
  it's being used).  What's going on? 
 
  It can be any one of a number of things: 
 
 
--------------------------------------------------------------------------- 
  Enabling the use of LAST STACK, LAST ARG, LAST CMD, etc., uses up extra RAM, 
  as the calculator has to keep track of the last stack, arguments, command, 
  etc..  This is particularly important with LAST STACK if you have a 
  large/complex stack, as the HP-48SX has to keep enough information around to 
  recreate the stack after each operation.  You can clear out these variables 
  by pressing ON-C (but also note that this will clear out the stack, the 
  graphics PICT, etc.). 
 
--------------------------------------------------------------------------- 
    From billw@hpcvra.CV.HP.COM Fri Mar  1 17:00:00 1991 
    From: billw@hpcvra.CV.HP.COM (William C Wickes) 
    Date: Wed, 1 Aug 1990 19:51:37 GMT 
    Subject: DOERR: An HP48SX memory eater 
    Organization: Hewlett-Packard Co., Corvallis, OR, USA 
    Newsgroups: comp.sys.handhelds 
 
  Here's a candidate for "most obscure way to use up memory on the HP 48SX." 
  When a program executes DOERR with a string argument, the string and hence 
  the program too if the string is embedded in the program are referenced for 
  the sake of the ERRM command.  Thus if you purge the program, the memory used 
  by the program is not reclaimed until the ERRM reference is updated to a new 
  string.  If the string is in a port, you will get the Object In Use error if 
  you try to purge the library or backup object containing the string.   
 
  A system halt prior to a PURGE will not help unless the object is in port 1 
  or port 2 (it will reclaim memory held by a successfully purged but still 
  referenced object).  For port 0 objects, the only way to break the reference 
  is to execute DOERR again with a new string.   
 
--------------------------------------------------------------------------- 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
15* How do I get rid of the HYDE library? 
 
  Getting rid of the HYDE library can be fun.  Here's how to do it: 
 
  1. Go the HOME directory. 
 
  2. Press left-shift (orange) LIBRARY.  The calculator is now 
     displaying a menu of libraries attached to the HOME directory. 
 
  3. Press the menu key that says "STRA".  You are now accessing the 
     HYDE library. 
 
  4. Press the menu key that says "JEKY".  You have now disabled the 
     HYDE library and restored the old (standard) set of messages. 
 
  5. Make sure that a pointer to the library is not on the stack.  The 
     easiest way to do this is to clear the stack using CLR. 
 
  6. Detach the library using: 
 
       :0:998 DETACH 
 
  7. Purge the library using: 
 
       :0:998 PURGE 
 
     When you execute the PURGE, the screen will "jump"/"be messed up" 
     for a brief moment.  Don't worry about it -- it doesn't hurt. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
16* How can I transfer programs/data from my HP-28S to my HP-48SX? 
 
  You use a program called "INPRT", which is available from various archives, 
  and is also included in the IBM-version of the HP-48SX serial cable kit and 
  in the Program Development Library. 
 
  INPRT sends a program to the I/R output of the HP-28S, and the HP-48SX 
  receives it via its I/R input. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
17* I could speed up my HP-28S.  How can I speed up my HP-48SX? 
 
  You can't.  Unlike the HP-28S, the clock speed in the HP-48SX is hardwired to 
  2 MHz. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
18* Why does the HP-48SX display flicker slightly? 
 
  Display flicker is usually caused by fluorescent lights (the rapid pulsing of 
  the fluorescent lights, which is normally unnoticeable, interacts with the 
  rapid pulsing/scanning of the HP-48SX LCD display, which is also normally 
  unnoticeable).  It's normal and harmless. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
19* I've heard that other manufacturer's RAM cards will work with the 
  HP-48SX.  Is this true?  Will it work? 
 
  While some cards may work, there is a chance that you may severely damage 
  your HP-48SX. 
 
  For more information, see Appendix B, "Using non-HP RAM cards in your 
  HP-48SX", near the end of this file. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
20* What library ID numbers have already been used? 
 
         766    -- HP EPSPRINT.LIB library 
         767    -- HP PCLPRINT.LIB library 
         768    -- HP Stopwatch library 
         777    -- "TenK" library 
         998    -- "HYDE" library 
        1092    -- MLDL library (Jan Brittenson -- bson@erice.ai.mit.edu) 
                   (In development -- not officially released) 
        1644    -- SWING ("VMS" graphical directory browser) 
        1791    -- TOOLs library 
        1793    -- New IFERR library 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
21* What do the funny symbols \->, \GS+, etc., mean? 
 
  These are the ASCII representation of the special HP-48SX graphical 
  characters.  See the section "Character Translations" in Chapter 33 (Volume 
  II) of the manual for a table of symbols <--> ASCII representations.   
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
22* What tricks are there for manipulating matrices? 
 
  You can build up a matrix by rows using \GS+ 
 
  You can take a matrix apart by rows using \GS- 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
23* How do I store fields of variable length string data in a compact, 
  rapidly accessible manner that does not require the overhead of 
  storing strings in lists? 
 
  See Appendix C, "Compact Data Storage", near the end of this file. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
24* What is "Vectored Enter", and how do I use it? 
 
  From billw@hpcvra.CV.HP.COM Fri Mar  1 17:00:00 1991 
  From: billw@hpcvra.CV.HP.COM (William C Wickes) 
  Date: Mon, 12 Mar 1990 21:21:55 GMT 
  Subject: HP-48SX Vectored Enter 
  Organization: Hewlett-Packard Co., Corvallis, OR, USA 
  Newsgroups: comp.sys.handhelds 
 
  The HP-48SX manuals do not document a very powerful feature that we call 
  "Vectored ENTER," that allows you in effect to redefine or bypass the 
  command line parser and to have a shot at the stack etc. after the command 
  line has been executed. 
 
  Keys that execute an automatic ENTER perform a two-step process: 
 
  1.  The command line is parsed and evaluated. 
  2.  The key definition is executed. 
 
  When flags -62 and -63 are both set, the system extends this process as 
  follows: 
 
  1.  The current path is searched for a global variable named *aENTER (here 
  "*a" is the Greek alpha character--character 140).  If present, the command 
  line is entered as a string object and *aENTER is executed.  If absent, the 
  command line is parsed and evaluated normally. 
 
  2.  The key definition is executed. 
 
  3.  The current path is searched for a global variable named *bENTER ("*b" is 
  Greek beta--character 223).  If present, then a string representing the key 
  definition is put on the stack, and *bENTER is executed.  The string is the 
  key definition object's name if it is a command, XLIB name, global or local 
  name, or an empty string for other object types; its primary purpose is to 
  implement things like the TRACE mode on other calcs, where you can print a 
  running record of what you do. 
 
  A simple example of the use of *aENTER is to create a more convenient binary 
  calculator, where *aENTER slaps a "#" on the front of the command line so you 
  don't have to bother when entering numbers. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
25* How can I tell, from within a program, if the battery is low? 
 
  Preston Brown (prestonb@hpcvra.CV.HP.COM) posted the following: 
 
  The following 48SX program reports the status of the ALERT annunciator. 
  The ALERT annunciator is activated by alarms or low battery. 
 
  This program is provided free of charge "as is" and has no warranty.  No one 
  is liable for any consequential damages. 
 
  Preston 
 
%%HP:T(3)A(D)F(.); 
\<< 
RCLF 
8 STWS #FFh #0h + 
#10Bh 
#6595Ah SYSEVAL 
#8h AND #0h > 
SWAP STOF 
\>> 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
26* I've heard the names "RPL", "Saturn", "STAR", "Voyager", etc..  What 
  do they mean? 
 
    ASAP 
        This is a simple Saturn assembler, written in the perl language (and is 
        therefore usable mostly on Unix machines). 
 
    Chip8 
        This is a machine-code program that was inspired by the chip8 video 
        game interpreter for the CDP1802 microprocessor several years back. 
        Chip8 allows you to write a simple graphics-based video game for the 
        HP-48SX.  Among the games written are "clones" of breakout, pacman, and 
        pong, to name a few (about half?). 
 
    HYDE 
        This is the "HYDE" library, whose only purpose is to change the error 
        messages in the HP-48SX to make it "user unfriendly". 
 
    ML 
        Machine Language.  This is usually used in reference to HP-48SX 
        assembly language programming.   
 
    MLDL 
        Machine Language Development Library.  This is a library, which is 
        still under development, that allows you to debug machine language 
        programs with only an HP-48SX.   
 
    PDL 
        "Program Development Link".  This is an MSDOS program, sold by 
        Hewlett-Packard, that allows you to write and develop HP-48SX 
        applications from your IBM PC clone.  Programs are written on your PC, 
        transferred to the HP-48SX, and tested from your *PC* (and *not* the 
        HP-48SX). 
 
    RPL 
        RPL is the name of the language used to program the HP-48SX and HP-28 
        series calculators.  While many people consider RPL to stand for 
        "Reverse Polish Lisp", an HP Journal article described RPL as 
        "ROM-based Procedural Language".  To muddy the waters, it's also 
        interesting to note that the HP-48SX development team considers RPL to 
        mean "Reverse Polish Lisp", and not what was mentioned in the HP 
        Journal.  [Note: See RPL.TXT on this disk.  -jkh-] 
 
    SASS 
        SASS is a simple Saturn assembler, written in C/yacc (BSD Unix & 
        Bison).  It uses Alonzo Gariepy's mnemonics. 
 
    Saturn 
        "Saturn" is the internal code name for the processor used in the 
        HP-48SX, HP-28 series, and the HP-75/71B calculators. 
 
    STAR 
        This is the "Saturn Macro Assembler" (how "STAR" comes from this, I 
        don't know), an assembler that mostly uses Alonzo Gariepy's mnemonics. 
        It's written in C and runs on many different machines (PCs, Amigas, 
        Unices, etc.).  STAR is available via anonymous ftp from ftp.ai.mit.edu 
        in "/pub/star-1.04.4.tar.Z".  It's also available from various bulletin 
        boards (the HP forum in CompuServe also has a copy).  The latest 
        version is "1.04.4". 
 
    SWING 
        SWING is a library program that displays a graphical tree structure of 
        the directory hierarchy in your HP-48SX, and allows you to move from 
        directory to directory using the arrow keys (it is supposedly based 
        upon an old PD VMS utility). 
 
    Voyager 
        Voyager is an "interactive disassembler" for IBM PC clones that 
        disassembles HP-48SX RPL and machine code.  You download a copy of the 
        RAM *and* ROM in your HP-48SX to your PC, and run Voyager.  Using 
        Voyager, you can then view the disassembled or unthreaded code. 
        Unfortunately (or fortunately), Voyager uses the HP mnemonics, and not 
        Alonzo Gariepy's mnemonics.  Voyager is available from the HP BBS (I 
        think), via anonymous ftp from the HP BBS (hpcvbbs.cv.hp.com), and from 
        various bulletin boards (the HP forum in CompuServe also has a copy). 
        The latest version is "1.07". 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
27* Appendix A: ASC\-> and \->ASC functions: 
 
From billw@hpcvra.CV.HP.COM Fri Mar  1 17:00:00 1991 
From: billw@hpcvra.CV.HP.COM (William C Wickes) 
Date: Fri, 17 Aug 1990 22:27:42 GMT 
Subject: HP 48 Object Encoding 
Organization: Hewlett-Packard Co., Corvallis, OR, USA 
 
 
                      ASCII Encoding HP 48SX Objects 
 
Sending an HP 48SX object via electronic mail can be difficult if the object 
does not have an ASCII form, such as is the case for library objects.  There 
are various encoding schemes available on different computer systems, but these 
require that the sender and receiver have similar computers, or at least 
compatible encode/decode schemes.  The programs listed below perform the 
encoding and decoding on the HP 48SX itself, which has the advantage of being 
completely independent of any computer. 
 
The programs are nominally called \->ASC and ASC\->.  The former takes an 
object from the stack and converts it to a string, in which each nibble of the 
object and its checksum is converted to a character 0-9 or A-F.  (The object 
must be in RAM, otherwise a "ROM Object" error is returned.) For sake of easy 
inclusion in email letters, the string is broken up by linefeed characters 
after every 64 characters. 
 
ASC\-> is the inverse of \->ASC: it takes a string created by \->ASC and 
converts it back into an object.  When you transmit the encoded strings, be 
sure not to change the string; ASC\-> uses the checksum encoded in the string 
to verify that the decoding is correct.  An "Invalid String" error is returned 
if the result object does not match the original object encoded by \->ASC. 
When you upload a string to your computer, use HP 48 translate mode 3 so that 
the HP 48 will convert any CR/LF's back to LF's when the string is later 
downloaded. 
 
Two versions of ASC\-> are included here.  The first (P1) is in HP 48 user 
language, using SYSEVALs to execute system objects.  P2 is a string that the 
setup program uses P1 to decode into an executable ASC\->--then P1 is 
discarded.  The second version is more compact than the first, and also 
uneditable and therefore safer (but it can't be transmitted in ASCII form, 
which helps to make the point of this exercise). 
 
Here are the programs, contained in a directory: 
 
(start) 
%%HP: T(3)A(D)F(.); 
DIR 
P1              @ ASC\-> Version 1. 
\<< 
  IF DUP TYPE 2 \=/ 
  THEN "Not A String" DOERR 
  END RCWS \-> ws 
  \<< 16 STWS 
    #0 NEWOB SWAP DUP SIZE 
    IF DUP 4 < 
    THEN DROP SWAP DROP "Invalid String" DOERR 
    END 
    DUP 65 / IP - 4 - # 18CEAh SYSEVAL 
    "" OVER # 61C1Ch SYSEVAL 
    SWAP # 6641F8000AF02DCCh 
    # 130480679BF8CC0h # 518Ah SYSEVAL 
    # 19610313418D7EA4h # 518Ah SYSEVAL 
    # 7134147114103123h # 518Ah SYSEVAL 
    # 5F6A971131607414h # 518Ah SYSEVAL 
    # 12EA1717EA3F130Ch # 518Ah SYSEVAL 
    # 280826B3012808F4h # 518Ah SYSEVAL 
    # 6B7028080BEE9091h # 518Ah SYSEVAL 
    # BE5DC1710610C512h # 518Ah SYSEVAL 
    # 705D00003431A078h # 518Ah SYSEVAL 
    # 3D8FA26058961431h # 518Ah SYSEVAL 
    # 312B0514h # 518Ah SYSEVAL 
    # 18F23h SYSEVAL 
    DUP BYTES DROP 4 ROLL 
    IF == 
    THEN SWAP DROP 
    ELSE DROP "Invalid String" DOERR 
    END ws STWS 
  \>> 
\>> 
 
P2      @ ASC\->  Version 2.  To be converted by ASC\-> version 1. 
 
"D9D20D29512BF81D0040D9D20E4A209000000007566074726636508813011920 
140007FE30B9F060ED3071040CA1304EC3039916D9D2085230B9F06C2A201200 
094E66716C696460235472796E676933A1B21300ED30FD5502C230C1C1632230 
CCD20FA0008F14660CC8FB97608403104AE7D814313016913213014117414317 
414706131179A6F5C031F3AE7171AE214F8082103B6280821909EEB0808207B6 
215C0160171CD5EB870A13430000D50713416985062AF8D341508813044950B9 
F06BBF06EFC36B9F0644230C2A201200094E66716C696460235472796E676933 
A1B2130B21300373" 
 
 
P3      @\->ASC.     To be converted by ASC\->. 
"D9D20D2951881304495032230FD5502C230A752688130ADB467FE30322306AC3 
0CB916E0E30CBD30F6E30C1C1632230CCD20DC0008F14660CC8FB97608403104 
AE7D8143130169174147061741431311534AC6B4415141534946908D9B026155 
4A6F53131F3AE731A014C161AE215F08082103A6280821939EEC08082170A621 
4C161170CD56B870A18503430000D5071351796A9F8D2D02639916D9D2085230 
C2A209100025F4D402F426A6563647933A1B2130A2116B213033C0" 
 
SETUP   @Automatic setup program 
\<< P2 P1 'ASC\->' STO 
    P3 ASC\-> '\->ASC' STO 
    { P1 P2 P3 SETUP } PURGE 
\>> 
 
END 
(end) 
 
 
Installation instructions: 
 
1.  Edit the above text between (start) and (end) into a text file named CONV 
    (for example).  Be sure that you leave the strings exactly as entered 
    above, with no extra spaces or other invisible characters at the beginnings 
    or ends of the lines. 
2.  Set the HP 48SX into ASCII transfer mode. 
3.  Using Kermit, download CONV text file to the 48, verify its checksum 
    (6C8Ah). 
4.  Execute CONV to make it the current directory. 
5.  Execute SETUP. 
6.  The directory CONV now contains ASC\-> and \->ASC, ready to use. 
 
To archive the decoded versions of ASC\-> and \->ASC back on your computer, 
be sure to set the HP 48SX in binary transfer mode before uploading. 
 
Disclaimers: 
 
+ Use the programs at your own risk.  Any time you delve into the SYSEVAL 
world, there are increased dangers.  Archive your 48 memory before 
experimenting with these programs!  Also, verify the checksums of objects 
defined above to make sure they have been downloaded correctly, before 
executing ASC\->. 
 
+ I will not answer questions about how the programs work.  This is not because 
of any great secrecy, but rather because it's hard to give any answer that 
doesn't lead to more questions, and more, and more... 
 
+ 48 hackers are welcome to mine any nuggets they can from the programs, and 
from the fact that \->ASC is a convenient way to decompile an object. 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
28* Appendix B: Using non-HP RAM cards in your HP-48SX: 
 
  If you use RAM cards that are NOT designed for the HP-48SX, it is possible to 
  severely damage your HP-48SX.  If you want to be safe, you should only use 
  RAM cards designed for the HP-48SX. 
 
  Here is an edited discussion from comp.sys.handhelds. 
 
  From steveh@hpcvra.CV.HP.COM Fri Mar  1 17:00:00 1991 
  From: steveh@hpcvra.CV.HP.COM (Steve Harper) 
  Date: Thu, 10 May 1990 22:46:09 GMT 
  Subject: RE: HP48SX Memory Card Pricing 
  Organization: Hewlett-Packard Co., Corvallis, OR, USA 
 
  There has been a substantial amount of comment regarding the memory cards for 
  the HP48SX and their prices.  My purpose in this response is not to attempt 
  to justify any particular price, but rather to present the technical reasons 
  why there is a substantial price difference between the memory cards and 
  other types of expansion memory for PC's, for example, with which users are 
  probably more familiar. 
 
  Some users have correctly pointed out that the memory in the cards is static 
  RAM rather than dynamic RAM commonly used in PC's.  Dynamic RAM uses one 
  transistor and a capacitor for each bit of memory whereas static RAM requires 
  either four transistors and two resistors, or six transistors.  The net 
  result is that an equivalent amount of static RAM is much larger and 
  therefore much more expensive than dynamic RAM.  The advantage is that static 
  RAM doesn't need to continually be running and drawing current (refresh 
  cycles) to retain the contents of memory. 
 
  In addition, the static memory used in the cards is not just any static 
  memory, but is specially processed and/or selected for very low standby 
  current.  This allows the backup battery in the card to keep memory alive for 
  a very long time, rather than requiring the user to replace it every few 
  months.  The special processing and/or special testing to select low current 
  parts adds to the already higher cost of the static RAM chips. 
 
  The standard molded plastic DIP package used for most integrated circuits, 
  including memory chips, is relatively inexpensive because of its simplicity 
  and the huge volumes.  Unfortunately, these packages are too large to put 
  into a memory card.  Therefore, the card manufacturer mounts the individual 
  silicon memory chips directly on a special thin PC board together with the 
  memory support chips.  Because multiple chips are being placed in a single 
  hybrid package in a special process which has lower volume, yields are lower 
  and this again causes the cost to be higher.  Indeed, the yield becomes 
  exponentially worse as the number of chips and interconnections increases in 
  such a packaging process. 
 
  In addition to the memory chips themselves, two more integrated circuits and 
  several discrete components are required for power and logic control.  A 
  bipolar technology chip senses the external voltage and switches the power to 
  the chips from the internal keep-alive battery as needed.  A CMOS gate array 
  chip protects the memory address and data lines from glitches/ESD when the 
  card is not plugged in.  This chip also generates the proper enabling signals 
  when there are multiple memory chips in the card, as is presently the case 
  with the 128 Kbyte RAM card.  These chips must be designed for extremely low 
  current, just as the memory chips are. 
 
  In addition to the battery and the battery holder, the other mechanical parts 
  are important, too.  The molded plastic frame holds the PC board and provides 
  the foundation for the metal overlays and the shutter-and-springs assembly 
  which protects the contacts from ESD and from contaminants.  The 
  write-protect switch is also an important feature.  It is quite expensive for 
  the manufacturer to make the tools necessary to fabricate each of these parts 
  as well as the tools to assemble and test the complete card.  While the 
  volume of memory cards is relatively low this tooling cost represents a 
  significant part of the cost of each card. 
 
  Admittedly, there are other alternatives, such as those presently used in 
  PC's, to provide a memory expansion capability.  To provide that kind of 
  expansion would require the calculator to be much larger than it is and 
  possibly more expensive.  This is clearly very undesirable. 
 
  Other features that were felt to be essential were the ability to distribute 
  software applications and to share and archive/backup user-created programs 
  and data.  Other expansion alternatives do not provide these important 
  benefits.  The IO capabilities of the calculator provide these features only 
  to a limited degree.   
 
  One other item bears repeating here: Memory cards for use in the calculator 
  will clearly indicate that they are for use with the HP48SX.  Other memory 
  cards exist which are mechanically compatible with the HP48S, but these cards 
  cannot be relied upon to work electrically in the calculator.  The HP48SX 
  cards are designed for a lower supply voltage range.  Use of the other cards 
  may cause memory loss, and under certain circumstances may even damage your 
  calculator electrically. 
 
  From steveh@hpcvra.CV.HP.COM Fri Mar  1 17:00:00 1991 
  From: steveh@hpcvra.CV.HP.COM (Steve Harper) 
  Date: Fri, 11 May 1990 16:52:07 GMT 
  Subject: Re: Memory Card: Give Us *True* Facts! 
  Organization: Hewlett-Packard Co., Corvallis, OR, USA 
 
  My previous statement that under certain circumstances the calculator may 
  even be damaged electrically is not a ploy.  If the calculator's internal 
  power supply voltage happens to be near the low end of the range, say 4.1 V, 
  and the voltage at which the card's voltage control chip shuts it down 
  happens to be near the high end of its range, say 4.2 V (this can and does 
  occasionally occur for the non-HP48SX cards), then the calculator will start 
  to drive the memory address lines and the card will still have these clamped 
  to ground (that's what it does to protect itself when there is not sufficient 
  system voltage to run).  This unfortunate situation may simply trash your 
  memory, or if the calculator tries to drive enough of the lines high at the 
  same time, several hundred milliamps may flow...for awhile that is, until 
  something gives up...  On the other hand, your calculator and a particular 
  non-HP48SX card may work just fine if those voltages happen to be at the 
  other end of their ranges.  These voltages are also slightly temperature 
  sensitive.  It may work in the classroom or office and not at the beach, or 
  vice versa.  The voltage trip point of the HP48SX cards has been set lower (a 
  different voltage control chip) so that this cannot occur, regardless of part 
  and temperature variations. 
 
  One other item was brought to my attention yesterday by Preston Brown that I 
  should have included in my original posting here.  While most of us recognize 
  that comparing ram cards to a handful of dynamic ram chips to plug into your 
  PC is apples and oranges, it may be more interesting to compare the HP48SX 
  cards with cards for other products, like the Atari Portfolio, the Poquet, 
  the NEC Ultralite, etc.  I believe you will find that the prices on the 
  HP48SX cards are not at all out of line. 
 
  Steve 
  "I claim all disclaimers..." 
 
  the non-HP48SX cards 
 
  From prestonb@hpcvra.CV.HP.COM Fri Mar  1 17:00:00 1991 
  From: prestonb@hpcvra.CV.HP.COM (Preston Brown) 
  Date: Thu, 17 May 1990 17:26:53 GMT 
  Subject: Re: Memory Card: Give Us *True* Facts! 
  Organization: Hewlett-Packard Co., Corvallis, OR, USA 
 
  When the RAM cards detect that voltage is too low to operate they clamp the 
  address lines to ground.  This clamping is done by turning on the output 
  drivers of a custom chip included on the card.  The clamping current is 
  speced at 2mA min at the Vol output level.  Since the 48 can be trying to 
  drive the line all the way high even more current is typical.  10mA per fight 
  is not uncommon with totals of several hundred mAs. 
 
  The VDD power supply is regulated at 4.1 - 4.9 with typical parts at the low 
  end (4.3).  The power to the cards is switched thru a transistor, creating up 
  to a 0.1V drop.  Standard Epson cards have a significant chance of seeing 
  this voltage as to low and shutting down.  We have seen cards do this in the 
  lab.  When it occurs the calculator locks up with VDD pulled down to about 
  2.5V and 250mA being drawn from the batteries.  This current drain greatly 
  exceeds the ratings for the power supply and can damage your calc.  The least 
  that will happen is a loss of memory. 
 
  Now, why didn't we regulate VDD higher?  The 48 has two power supplies VDD at 
  4.3 and VH at 8.5.  VH cannot be regulated higher without exceeding the spec 
  for our CMOS IC process.  VH is used as the + voltage for the I/O.  In order 
  to meet a +3V output level VH must be more then 3.6V above VDD.  (VDD is used 
  as I/O ground).  Our power supply system increase the battery life and 
  reduces the cost greatly for the wired I/O. 
 
  Preston 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
29* Appendix C: Compact Data Storage: 
 
  From Jim Donnelly (jimd@cv.hp.com): 
 
  A simple length-encoding technique can be put to use for a free-format, very 
  compact multi-field data storage system.  Two tiny programs, SUBNUM and 
  STRCON are here to help the process, and are listed near the end of this 
  note.  At the end of the note is a directory that may be downloaded into the 
  HP 48 that contains the examples. 
 
  The principle is to store starting indices in the beginning of a string that 
  point to fields stored subsequently in the string.  The indices are stored in 
  field order, with an additional index at the end to accommodate the last 
  field.  There are several small points worth mentioning: 
 
  1) Fields may be 0-length using this technique. 
  2) The execution time is uniform across all fields. 
  3) This technique saves about 4 bytes per field after the first field, 
     because the string prolog and length are omitted for fields 2 -> n. 
 
 
        EXAMPLE: 
        -------- 
 
                         Indices  |          Fields 
          Character               |     1 11111111 12222222222 
          Position :   1  2  3  4 |567890 12345678 90123456789 
                      +--+--+--+--+------+--------+-----------+ 
          String :    | 5|11|19|30|Field1| Field2 |  Field 3  | 
                      +--+--+--+--+------+--------+-----------+ 
 
  This is a string that contains 3 fields, and therefore 4 index entries.  The 
  first field begins at character 5, the second field begins at character 11, 
  and the third field begins at character 19.  To keep the pattern consistent, 
  notice that the index for field 4 is 30, which is one more than the length of 
  the 29 character data string. 
 
  To extract the second field, place the string on the stack, use SUBNUM on 
  character 2 to extract the starting position, use SUBNUM on character 3 to 
  extract the (ending position +1), subtract 1 from the (ending position+1), 
  then do a SUB to get the field data.  NOTE: The index for field 1 is stored 
  as character code 5, NOT "5"!  To place the field index for field 1 in the 
  string, you would execute "data" 1 5 CHR REPL. 
 
 
        PROGRAM: 
        -------- 
 
  The following program accepts an encoded data string in level 2 and a field 
  number in level 1: 
 
        DECODE   "data"  field#  -->  "field" 
 
        <<  --> f 
          << 
            DUP f SUBNUM                ; "data" start --> 
            OVER f 1 + SUBNUM           ; "data" start end+1 --> 
            1 -                         ; "data" start end --> 
            SUB                         ; "field" --> 
          >> 
        >> 
 
 
        DATA ENCODING 
        ------------- 
 
  The following program expects a series of 'n' strings on the stack and 
  encodes them into a data string suitable for reading by the first example 
  above. 
 
  The programs SUBNUM and STRCON are used to assemble the indices. 
 
        ENCODE      field n  ...  field 1   n   -->  "data" 
 
        << DUP 2 + DUP 1 - STRCON --> n  data 
          << 
            1 n 
            FOR i 
              data i SUBNUM OVER SIZE   ; ... field index fieldsize 
              + data SWAP               ; ... field "data" index' 
              i 1 + i + SWAP CHR REPL   ; ... field "data"' 
              SWAP + 'data' STO         ; ... 
            NEXT 
            data                        ; "data" 
          >> 
        >> 
 
  In this example, four strings are encoded: 
 
        Input:  5: "String" 
                4: "Str" 
                3: "STR" 
                2: "STRING" 
                1:         4 
 
        Output: "xxxxxSTRINGSTRStrString"      (23 character string) 
        (The first five characters have codes 6, 12, 15, 18, and 24) 
 
 
 
        VARIATION: 
        ---------- 
 
  The technique above has a practical limit of storing up to 254 characters of 
  data in a string.  To overcome this, just allocate two bytes for each field 
  position.  The code to extract the starting index for becomes a little more 
  busy.  In this case, the index is stored as two characters in hex. 
 
                      Indices  |          Fields 
       Character               | 11111 11111222 22222223333 
       Position :   12 34 56 78|901234 56789012 34567890123 
                   +--+--+--+--+------+--------+-----------+ 
       String :    |09|0F|17|21|Field1| Field2 |  Field 3  | 
                   +--+--+--+--+------+--------+-----------+ 
 
           <<  --> f 
             << 
                DUP f 2 * 1 -           ; "data" "data" indx1 --> 
                SUBNUM 16 *             ; "data" 16*start_left_byte  --> 
                OVER f 2 * SUBNUM +     ; "data" start 
                OVER f 2 * 1 + SUBNUM   ; "data" start end_left_byte --> 
                16 * 3PICK f 1 + 2 * 
                SUBNUM + 1 -            ; "data" start end --> 
                SUB                     ; "field"  --> 
             >> 
           >> 
 
 
 
        TWO VERY TINY HELPFUL PROGRAMS 
        ------------------------------ 
 
        SUBNUM          "string"  position  -->  code 
 
        << DUP SUB NUM >> 
 
 
 
        STRCON          code  count  -->  "repeated string" 
 
        << -->  code count 
          << "" code CHR 'code' STO 
             1 count START code + NEXT 
          >> 
        >> 
 
 
        A DIRECTORY YOU CAN DOWNLOAD 
        ---------------------------- 
 
  This is a directory object.  Cut after the === to the end of the file and 
  download to your HP 48 using the ASCII transfer. 
 
======================================================================== 
%%HP: T(3)A(D)F(.); 
DIR 
  DECODE 
    \<< \-> f 
      \<< DUP f 
SUBNUM OVER f 1 + 
SUBNUM 1 - SUB 
      \>> 
    \>> 
  ENCODE 
    \<< DUP 2 + DUP 1 
- STRCON \-> n data 
      \<< 1 n 
        FOR i data 
i SUBNUM OVER SIZE 
+ data SWAP i 1 + 
SWAP CHR REPL SWAP 
+ 'data' STO 
        NEXT data 
      \>> 
    \>> 
  STRCON 
    \<< \-> code count 
      \<< "" code CHR 
'code' STO 1 count 
        START code 
+ 
        NEXT 
      \>> 
    \>> 
  SUBNUM 
    \<< DUP SUB NUM 
    \>> 
END 
 
bŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽŽb 
 
30* Appendix D: Various useful functions 
 
  (Shamelessly lifted from the HP-41C manual:) 
 
  The LASTX function is useful in calculations where a number occurs more than 
  once.  By recovering a number using LASTX, you do not have to key that number 
  into the calculator again. 
 
  For example, calculate: 
 
                96.704 + 52.394706 
               -------------------- 
                     52.394706 
 
        Keystrokes:                     X: 
       ------------------              -------------------- 
        96.704 ENTER                    96.704 
        52.304706 +                     149.098706 
        LASTX                           52.304706 
        /                               2.84568265351 
 
@ 
@ This is a version of LASTX for the HP-48SX 
@ 
%%HP: T(3)A(D)F(.); 
\<< DEPTH \-> n 
  \<< LASTARG DEPTH n - DUP \-> s 
    \<< ROLLD s 1 - DROPN 
    \>> 
  \>> 
\>>