(Comp.sys.handhelds) 
Item: 1979 by sjthomas at cup.portal.com 
Author: [Stephen J Thomas] 
  Subj: CMT 128K RAM cards 
  Date: Wed Feb 06 1991 
 
There have been a few postings here on c.s.h.  inquiring about the CMT 128K RAM 
cards for the HP 48SX.  There have been rumors about the CMT cards providing a 
low battery warning and the physical size of the CMT cards.  I called CMT's BBS 
and posed these questions to them. 
 
This posting has three parts: 
 
  1.  CMT's reply to rumors that their RAM cards do not provide 
      low battery warnings. 
 
  2.  Several questions I posed about the physical chararcteristics 
      and warranty of the CMT RAM cards. 
 
  3.  CMT's reply to my questions in part 2. 
 
I've edited out some chit-chat from my comments, but not CMT's. 
 
Stephen J Thomas        sjthomas@cup.portal.com 
 
 
Part 1 =============================================================== 
 
 
From:    Reed Lacy 
Msg #4, 21-Jan-91 03:00pm 
Subject: 128R Low Batt & Power 
To: Stephen Thomas 
 
I am going to answer you by sending you a copy of a short report that includes 
enough information to more than answer your question.  Thank-you for using our 
card.  Here is the report: 
 
The SRAM cards have two power sources.  The first of these is the battery that 
is installed in the card.  The currents drawn from this battery are shown in 
Table 1.  The other source of power is from the HP-48SX battery when the card 
is installed in the HP-48SX.  The currents from this are shown in Table 2. 
 
Table 1: 
-------- 
Card Battery current of the HP 128K SRAM card versus the CMT 128K SRAM card 
with the card removed from the HP-48SX.  Switch position is indicated as "Read" 
or "Read/Write". 
 
 
      Card            Read              Read/Write 
                      Current           Current 
 
      CMT 128K SRAM   0.2876 microamps  0.3003 microamps 
      HP  128K SRAM   1.649  microamps  1.676  microamps 
 
 
 
Table 2: 
-------- 
Current draw of the memory cards with 4.4 volts applied to the card and all 
address and control lines held at ground.  This is close to the current draw 
that occurs when the card is installed in a HP-48SX that is turned on. 
 
 
      Card            Read/Write 
                      Current 
 
     HP-128K  SRAM    845    microamps 
     CMT-128K SRAM      2.0  microamps 
 
 
 
Assuming that the card is sitting on the shelf, Table 1 would be the current 
draw that is applicable.  The batteries that are used in the card are 75 
mA-hour batteries.  Using this the expected life of the battery in the two 
different cards is: 
 
     HP  128K SRAM ->  44,749 hours ->   5  years 
     CMT 128K SRAM -> 249,750 hours ->  28  years 
 
This isn't realistic because the lithium batteries decay all by themselves in 
about 5 years.  It does show that the CMT card's battery will definitely last 
for 2 years and will probably last for 5 years.  The extra battery life makes 
data stored in a CMT card more secure than the data in a HP card. 
 
Table 2 shows that the CMT card draws significantly less operating current than 
the HP card.  This will result in a longer system battery life for the HP-48SX. 
 
The HP-48SX low battery indicator works with the CMT cards if a battery is 
installed.  Without a battery installed, the low battery indicator does not 
work.  This is a side effect of designing the card for low power usage.  We 
felt that the decrease in power usage was worth this trade off. 
 
Based on these figures I recommend that the battery in the card gets changed 
every 2 years.  Since the power consumption is so low I also recommend that the 
battery remain inside the card during storage and shipping. 
 
 
Part 2 =============================================================== 
 
From:    Stephen Thomas 
To:      Reed Lacy                     Msg #6, 31-Jan-91 08:21pm 
Subject: 128R Questions 
 
I've heard some other questions and rumors about the CMT card, and I wonder if 
you would care to address these: 
 
1.  EduCALC is claiming that CMT has extended the warranty on the RAM cards 
    from 90 days to 1 year. 
 
2.  It is obvious that the CMT fits the 48 more tightly than the HP cards -- 
    this is especially apparent in port 2.  There are _rumors_ that HP is 
    concerned that the CMT card will spread the electrical pin connections in 
    the 48, increasing the risk that other cards may not make good electrical 
    contact.  Is this true?  If so, is CMT taking steps to correct this? 
 
3.  I've read one comment that the (gold?) plating on the electrical contacts 
    of the CMT RAM card seem to have been fairly well etched after just a few 
    insertion/removals.  Do you have any information about the quality of these 
    contacts, or the number of insertion/ removals expected from a CMT card? 
 
4.  [I've been asked] about the ESD protection of the CMT card since it does 
    not have a "shutter" (contact cover).  [What is a "transorb"?] Perhaps you 
    could shed some light on this. 
 
I'm not trying to harass CMT....I've held your products in high regard.  But 
many of us plugging these cards into our 48's have some genuine concerns. 
 
Thanks for any info you can share.        Stephen Thomas 
 
 
Part 3  - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - 
 
From:    Eric Gakstatter 
Msg #7, 01-Feb-91 02:04pm 
Subject: Re: 128R Questions 
 
Dear Mr. Thomas, 
 
Thank you for your questions and input.  We appreciate it that you care enough 
to ask. 
 
I will respond to your questions by answering the first one then giving an 
answer that groups the next three together since they are all interrelated. 
 
1.  Yes all CMT cards for the HP-48SX bought from EDUCALC have a 1 year 
warranty. 
 
2,3,4.  Yes our cards do fit more tightly, but this will not cause damage to 
the connector.  The connector in the HP-48SX is designed with plastic bars 
between each connecting spring so that the springs can not be depressed far 
enough to cause any damage.  If a card is too thick, it won't fit in the 
connector. 
 
We use the same connector as HP does for our card tester and it has had 
hundreds of cards inserted without a single failure.  All of the HP-48's that 
we have used in testing and developing the cards have had hundreds of our cards 
installed and removed without a problem.  We have tested an individual card for 
over 1,000 installations with no failure that wasn't cured by cleaning the 
contacts with a cotton swab moistened (not soaked) with isopropyl alcohol. 
However, we do recommend that users minimize the number of insertions/removals. 
This applies to all connectors of this type, not just CMT's. 
 
The transzorb is a high speed transient absorber that is used to help protect 
the card's circuitry from transient voltage spikes.  The shutter is patented by 
EPSON (I believe) so we chose to use tranzorbs for protection against ESD. 
 
We believe we have done our homework on this matter.  We have produced and 
tested hundreds of cards and not experienced an ESD or mechanical problem.  As 
you know, we are not new to this kind of technology.  CMT became the dominant 
supplier (and in some cases, the only supplier) of plug-in modules for the 
HP-41C/CV/CX, HP-71B and HP-75 hand-held calculators that proved to be VERY 
reliable.  They experienced no ESD or mechanical problems and there are 
literally tens or hundreds of thousands (I don't know the number) of these 
modules sold worldwide. 
 
We do recommend that when the card is not in the HP-48SX that you store the 
card in its ESD protection bag and that you keep your fingers away from the 
gold connectors.  This is really no different then the normal precautions that 
you would take with any circuit board.  We feel that the HP-48SX, the card 
connectors, and the CMT memory cards are quality products that should bring you 
years of use. 
 
===== 
 
[Personal note: I have had two 128K RAMs in my 48 for some time now, 
one is HP's and the other is CMT's.  Both work great.  -jkh-]