(Comp.sys.handhelds) 
Item: 3008 by ftg0673 at tamsun.tamu.edu 
---------- 
  Resp: 1 of 2 by ftg0673 at tamsun.tamu.edu 
Author: [Rick Grevelle] 
  Date: Mon May 06 1991 
 
Several months ago Wickes posted a tongue-in-cheek library to which he later 
referred as the Bart Simpson Library.  Basically it contained every message 
array in the 48 which of course had been altered to provide a completely new 
set of messages intended to amuse.  In his lecture at the Philadelphia area 
user group meeting last year he alluded, as well as illustrated with another 
library, that this customized message capability had been done purposefully 
to allow the use of other languages.  This article describes the information 
necessary to override any or all of the intrinsic message arrays with in the 
48.  However, for those individuals who remain too intimidated to delve into 
the world of internals, there are still no means provided here by which any 
of the error messages can be interjected with the name of a specific program 
responsible for generating the error. 
 
 
Rick Grevelle 
 
 
                        Customizing Message Arrays 
 
============================================================================= 
 
 
By default, the 48 contains thirteen libraries.  Here is a summary of these: 
 
                        Relevant Library Addresses 
 
----------------------------------------------------------------------------- 
Number/Address |  Hash Table |  Message Array |  Link Table |  Config Routine 
----------------------------------------------------------------------------- 
  #0h/#028E3h  |    none     |    #72000h  *  |    none     |    #0BB40h **   
----------------------------------------------------------------------------- 
  #1h/#10F14h  |    none     |    #72704h  *  |    none     |    #11086h **   
----------------------------------------------------------------------------- 
  #2h/#189E8h  |   #7448Ah * |    #72DCFh  *  |   #22651h   |    #18A01h      
----------------------------------------------------------------------------- 
  #3h/#29DB3h  |    none     |    #72F1Eh  *  |    none     |     none        
----------------------------------------------------------------------------- 
  #5h/#35504h  |    none     |    #736F9h  *  |    none     |     none        
----------------------------------------------------------------------------- 
  #6h/#2C086h  |    none     |    #72FE6h  *  |    none     |     none        
----------------------------------------------------------------------------- 
  #Ah/#32F5Eh  |    none     |    #72281h  *  |    none     |     none        
-----------------------------------------------------------------------------  
  #Bh/#0F05Ch  |    none     |    #726A5h  *  |    none     |     none        
----------------------------------------------------------------------------- 
  #Ch/#2D340h  |    none     |    #7232Ch  *  |    none     |    #2D359h **    
----------------------------------------------------------------------------- 
  #Dh/#0CABEh  |    none     |    #7260Ah  *  |    none     |    #0CAD7h **    
----------------------------------------------------------------------------- 
 #19h/#0BE14h  |    none     |     none       |    none     |     none        
----------------------------------------------------------------------------- 
 #F0h/#38836h  |    none     |     none       |   #3834Fh   |     none        
----------------------------------------------------------------------------- 
#700h/#22DE5h  |   #7247Ch * |     none       |   #22E08h   |    #22EA3h **   
----------------------------------------------------------------------------- 
 
            *  covered ROM address       **  non-auto attaching 
 
 
Only ten of the thirteen libraries contain message arrays, of which there is 
one whose configuration routine is auto attaching.  To override any of these 
message arrays the library to which it belongs must first be attached.  Then 
the replacement message array, which can be stored in either a library as an 
XLIB or a directory as a GLOBAL variable, must be attached via the use of an 
unavailable user language command.  The directory which has been provided at 
end of this article contains all ten of the 48's message arrays, each stored  
in GLOBAL variables corresponding to library's hexadecimal number.  Routines 
used for attaching and detaching these message arrays have been included. 
 
Because most users will not be interested in changing all of the 48's message 
arrays, it won't be necessary for those individuals to store and attach every 
one of these.  It is for this reason I'm providing the following illustration 
which will demonstrate how to attach and override a single message array, and 
then return control to the default.  In order to benefit those whose capacity 
to program the calculator is limited to user language, the information that's 
being presented here is in a format understandable and familiar to all of us. 
Others whose programming skills are already advanced will need only a look at 
the two routines CUSTOM and DEFAULT after reading this material to understand 
their function. 
 
All of the object types not supported by the display routines can be found in 
the message array belonging to library #1.  I've always hated those Externals 
appearing in the display.  Greater than ninety percent of these are merely an 
assortment of the prefixed machine routines of which the SYSTEM RPL is built. 
Perhaps if Hewlett-Packard had foreseen the immense popularity of the 48 they 
would have taken the time to do things a bit differently.  Because it is most 
unlikely any of the objects represented by Externals would be something other 
than prefixed machine code, it might be preferable for the display routine to 
to use Address instead.  So for the example chosen the message array is going 
to be changed such that all Externals will appear as Address. 
 
 
        o  First, it will most always be desirable to start by altering 
           a copy of the default message array.  This will be much less 
           trouble than constructing an array from scratch.  It's not a 
           major task to recall a copy of any of the ten default arrays 
           to the stack, but to alter an array of strings, two routines   
           from the HACKIT library, OUT\->, and \->ARR will be needed. 
 
        o  The message arrays for all of the ROM libraries can be found 
           in the 32K bank of ROM that's normally covered by RAM.  It's 
           for this reason that it is often referred to as covered ROM. 
           Recalling objects from this usually inaccessible bank of ROM 
           requires only two steps, and of course the object's address. 
 
        o  Recall a copy of the message array from a library by placing 
           the location of the message array in level one, #72704h, and 
           executing \<< #05A03h SYSEVAL #0C612h SYSEVAL \>>.  An array 
           of string which is the message array from library #1 will be 
           the result.  Consult the table for the addresses to the rest 
           of the message arrays.                  
 
        o  Use the OUT\-> command in the HACKIT library for decomposing 
           the array into its sixty-two constituent strings.  It is now 
           possible to edit any of the individual strings, then altering 
           or completely replacing the string.  Make sure you've put the 
           string back in its appropriate position on the stack after it 
           has been altered.  Use \->ARR to recompile the message array 
           of strings. 
 
        o  After the array has been altered, store it in a GLOBAL name, 
           and attach the library from which it came, if it hasn't been 
           done previously.  Note only one out of the ten ROM libraries 
           is auto attaching; all others must be attached.  ATTACH will 
           not work for ROM libraries so place the binary number of the 
           library, #1h, in level one, and then execute these SYSEVALs: 
           \<< #05A03h SYSEVAL #07709h SYSEVAL \>>. 
 
        o  Next the array must be identified as the replacement for the 
           default array and attached too.  Again, this will need to be 
           done using SYSEVALs, so once more place the library's binary 
           number in level one, and the GLOBAL in which the replacement 
           message array is stored in level two, and use the following: 
           \<< #05A03h SYSEVAL SWAP RCL #0764Eh SYSEVAL \>> 
 
        o  Nullify the above procedure by detaching the library, and in 
           the case of library #2h, reattach.  To detach put the number  
           of the library being detached in level one and execute this: 
           \<< #05A03h SYSEVAL #076AEh SYSEVAL \>>. 
 
 
The following directory contains all of the 48's default message arrays with 
an exception; the string "External" in library #1h was changed to "Address". 
The affect of this can be viewed by installing the directory, then recalling 
the contents of the CUSTOM variable to the stack, and toggling both commands 
CUSTOM and DEFAULT.  The display auto refreshes after each key press so that 
the unsupported prefixed machine routines will change back and forth between 
External and Address.  Last it should be mentioned that if it's desirable to 
convert the directory into a library, it would be advisable to place all the 
GLOBAL names containing message arrays in a list in $HIDDEN so that they are 
not visible in the library.  GLOBAL names beginning with the letter "A" will 
contain message arrays.  Characters following each dot relate the library's 
hexadecimal number to the message array contain in the variable.