(Comp.sys.hp48) 
Item: 154 by dougc at bert.cs.byu.edu 
Author: [Douglas R. Cannon] 
  Subj: HP48 currents for various operations 
  Date: Fri Nov 08 1991 
 
  I was playing around the other day and decieded that I wanted to know just 
how much current the HP48 uses with different operations.  Everyone is always 
saying, "IR transmissions cause a great drain on the batteries..." or, 
"Lots of number crunching will cause significant battery drain..." So, I 
wanted to know how much. 
 
  In the hopes that this is interesting to others, I am posting a partial 
list that I have begun to compile.  These are simple operations that I was 
able to think of in 10 minutes or less.  If anyone has ideas for other 
operations that should be tested, please email me.  I would like to make this 
list as complete as possible.  Also, any comments, or questions are readily 
accepted. 
 
This is the current drawn from the batteries, given the operation: 
 
 
Current |       Operation                       |  Other 
 ( mA ) |                                       | 
------------------------------------------------------------------------ 
0.016   | HP OFF                                | probably not reliable 
2.22    | idle                                  | 
7.0     | "normal" program execution            | ( most programs ) 
7.0     | Stack manipulations                   | 
7.0     | yat 1.0 ( Tetris... )                 | 
6.62    | BEEP                                  | 600 Hz 
8.84    | BEEP                                  | 8000 Hz 
8.85    | BEEP                                  | 10000 and above 
7.0     | XMITRM ( IR remote controller )       | 16.0 mA briefly 
< 4.6   | Clock on in status line               | fluctuates (2.22 - 4.6 mA) 
3.6     | Command line input                    | idle 
2.27    | Stack depth of 500                    | idle 
6.8     | Plotter                               | sin(x) 
< 3.9   | Edit mode                             | ( 3.6 - 3.9 ) 
7.2     | Edit mode when checking syntax        | or moving cursor 
--------| WIRE TRANSMISSIONS -------------------|------------------- 
2.22    | idle, port closed                     | 
3.22    | idle, port open! (connected)          | connected to a Mac 
2.52    | idle, port open  ( not connected )    | 
8.15    | transferring to a mac                 | maximum 
--------| IR TRANSMISSIONS ---------------------|------------------- 
2.22    | idle, port closed                     | 
3.22    | idle, port open (wire connected)      | figure this out! 
2.52    | idle, port open ( wire not connected )| this one too. 
7.2     | Transmitting, trying to connect       | couldn't test a real trans. 
15.7    | Printing ( no printer near by )       | All time high! 
-------------------------------------------------------------------- 
A couple of notes: 
  Pressing ON does not close the I/O port, but turning the HP OFF, then ON, 
the port is closed.  ( I guess the manual wasn't kidding when it said to 
always close the port! ) 
  Notice the clock.  The ammeter showed a lot of fluctuation, but I am guessing 
that HP draws 2.22 mA as normal, then each time an interrupt is received for 
the clock, it momentarily draws around 4.6 mA. 
-------------------------------------------------------------------- 
 
So that you can try this at home... 
 
How it was done: 
 
It was rather simple, of course.  I just took out one of the batteries, 
connected it back in with wires, placing my ammeter in series with the 
batteries.  Then, nervously, I turned it on.  Since it didn't explode, I was 
able to make the measurements shown.  I feel that the measurements are good, 
since the ammeter I used has only a 250 mV maximum burden at fullscale 
of 200 mA.  The only measurement I need to do more accurately is when the 
HP is off. 
 
--------------------- 
Douglas R. Cannon 
dougc@bert.cs.byu.edu 
---------------------