(Comp.sys.hp48) 
Item: 438 by stevev@greylady.uoregon.edu 
Author: [Steve VanDevender] 
  Subj: REMOTE4: IR and IR2--IR remote-control sampling programs 
  Date: Tue Dec 31 1991 
 
[Note: Also see REMOTE3 on this disk for another programmer's approach 
 to turning the HP 48 into a universal infrared remote control.  -jkh-] 
 
These programs embody a new way of performing infrared remote control 
sampling on the HP-48.  The previously distributed remote sampling 
programs sampled IR input by continually reading the IR input and 
immediately writing it out to memory.  These programs use a different 
approach--they continually sample the IR input while incrementing a 
timing count, and only write information to memory when the IR state 
changes or the counter overflows.  This approach increases the 
effective sampling rate under many circumstances and greatly reduces 
the amount of memory needed to store samples.  I have also paid 
special attention to instruction timing to make sure that the timing 
characteristics of the sampling and playback routines are as nearly 
identical as possible; this has been a problem with some previous 
attempts at remote sampling. 
 
One of my motivations for writing these programs was that the other IR 
samplers I tried wouldn't work at all with my VCR.  Both of these work 
with my VCR, although I have obtained mixed results using these 
programs with other kinds of remotes.  I am hoping that these programs 
will be more effective than previous attempts, and that the techniques 
I have used here can be improved upon by others. 
 
There are two separate IR sampling systems included here.  The first, 
in the IR subdirectory, are the first programs I developed that 
worked.  They store 3-nibble sample units--1 nibble for the current IR 
input state, and 2 nibbles for a repeat count.  The inner loop of the 
sampling and playback routines runs at about 25 microseconds per loop 
iteration, and take about 40 microseconds to write out the sample data 
and re-enter the inner loop.  These routines will make samples of 
about 90 bytes that work with my VCR.  The second, in IR2, are 
2-nibble samples containing a 1-nibble repeat count.  The inner loop 
of these routines runs at about 23 microseconds per iteration, but 
sample string are a little over twice as long, at 224 bytes for 
samples that work with my VCR. Interestingly enough, though, Lutz 
Vieweg's RFP program will pack samples created by either set of 
routines to about the same length of 60 bytes.  [Note: See RF on 
Goodies Disk #5 in the PROGRAMR directory.  -jkh-] 
 
The directory IR contains the 3-nibble sampling routines, and the 
directory IR2 contains the 2-nibble sampling routines.  IR contains 
the user RPL programs SAMPLE and PLAYBACK and the machine code objects 
IRSAMP and IRPLAY.  IR2 contains SAMPLE2, PLAYBACK2, IRSAMP2, and 
IRPLAY2. 
 
The program SAMPLE (SAMPLE2) will take either a real number in level 
1, which is used to generate a string of that length to receive the 
sample, or a string which will be overwritten with sample data. It 
calls the machine-language program IRSAMP (IRSAMP2) which performs the 
sampling.  IRSAMP checks for a string object in level 1, which must 
have SIZE > 1, and aborts if it doesn't find one.  It then waits up to 
15 seconds for IR input, (that is, for you to place your remote 
control next to the calculator and press the button for the remote 
function you want to sample) and aborts if none is received in that 
time. Otherwise it begins sampling and exits when the end of the 
string in level 1 is reached.  I have found that holding an IR remote 
too close to the calculator during sampling will often result in 
ineffective samples; I get best results with the remote about 5-10 cm 
from the IR input port. 
 
The program PLAYBACK (PLAYBACK2) will take a string in level 1 and 
feed it to IRPLAY (IRPLAY2), then drop the string.  You can feed 
strings directly to IRPLAY if you wish, but they will be left on the 
stack (although this is a useful way to test samples without having to 
recover them with LASTARG).  You should only feed strings created with 
IRSAMP to PLAYBACK or IRPLAY.  It is possible to create strings which 
leave the HP-48 IR LED on for long periods of time, which drains the 
batteries and may cause hardware damage.  In any case, IRPLAY will 
turn the IR LED off before exiting. 
 
Two of my friends who have tested these programs have reported that 
they have experienced crashes while using them, although one report 
did not appear to involve memory corruption or any other damage. 
Therefore, I do not guarantee these programs to be bug-free--they may 
cause crashes, memory corruption, or even hardware damage if used 
improperly, although I can also say that I have had no problems for 
over a week since I debugged the routines in the IR directory. 
Neither are they guaranteed to work with any IR remote control, 
although I suspect they will have greater success than previous remote 
sampling programs. 
 
I would like to thank Dave Marsh for his original IR sampling 
programs, which I have copied small parts of and which were my main 
source of technical information in writing these programs, and Jan 
Brittenson for his excellent STAR assembler and MLDL debugger which 
made writing and debugging these programs easy. 
 
-- 
Steve VanDevender   stevev@greylady.uoregon.edu