Here's the information that I promised in an earlier note regarding programming
graphics on the HP 95LX.  Caveat Programmer.

Everett Kaser                   Hewlett-Packard Company
...hplabs!hp-pcd!everett        work: (503) 750-3569   Corvallis, Oregon
everett%hpcvra@hplabs.hp.com    home: (503) 928-5259   Albany, Oregon
----------------------------- cut here --------------------------------------
         __________________________________

	HP 95LX Low-level Graphics Support
	__________________________________

	Copyright 1991 Hewlett-Packard Company
	All rights reserved
	(distributed with permission)
	____________
	INTRODUCTION

	The package of low-level routines provided in the HP 95LX that are
	available for use by applications programs support these functions:

		 1) setting the display mode to alpha or graphics.
                 2) setting a fill mask.
		 3) getting information about the current graphics settings.
		 4) setting a logical origin to which all other graphics
			operations are relative.
		 5) setting a rectangular clip region.
		 6) drawing an outlined, solid-filled, or pattern-filled
			rectangle.
		 7) drawing a line.
		 8) plotting a point.
		 9) moving the current pen location.
		10) setting the current pen color.
		11) setting the current replacement rule.
		12) setting the current line-type.
		13) reading the current color value of a point.
		14) reading a rectangular image.
		15) writing a rectangular image.
		16) labeling text using the internal 6x8 font.

	All of the routines which plot to the display always obey the current
	logical origin, clip region, pen color, replacement rule, and (where
	appropriate) line-type and fill-mask.

	The pen color can be 0 or 1.

	The replacement rule can be one of FORCE, AND, OR, or XOR.  Writing
	a rectangular image can optionally invert the image before applying
	the specified replacement rule.  Writing an image is different from
	all other plotting in that it uses an argument as the replacement
	rule rather than the current replacement rule.

	The line-type is a 16-bit value whose bits are used repeatedly when
	drawing a line or an outlined rectangle.

	The fill-mask is an 8-byte value which specifies an 8-bit by 8-bit
	rectangular mask which is used repeatedly when drawing a pattern-filled
	rectangle.
         The general process to do graphics is:

		1) set the display mode to graphics
		2) set the desired pen color, replacement rule, linetype,
			fillmask, logical origin, and clip region, if different
			than the default values set by the set-mode function.
		3) perform the desired drawing using the attributes setup by
			step 2).
		4) repeat steps 2) and 3) until done.
		5) set the display mode back to alpha.

	The graphics routines are accessed through software interrupt 5F (hex).
	The required arguments are loaded into specific CPU registers, the
	requested function number is loaded into the AH register, and then an
	INT 5Fh instruction is executed.  Unless otherwise stated, all
	functions preserve ALL registers except for AX.

	X-coordinates always get larger (more positive) when moving to the
	right on the display.  Y-coordinates always get larger when moving
	down (towards the bottom) on the display.  The default origin is in
	the top-left corner of the display.

	Although the interface is designed primarily as an assembly language
	interface, it is simple to write an assembly language module that can
	provide a library of corresponding functions to a C program.  A sample
	is provided in Appendix A.
         ______________
        SET VIDEO MODE

	Forces the current video mode to alpha or graphics and clears the
	display.

	Entry conditions:

		AH = 0
		AL = requested mode.
			07h = alpha (system manager compliant)
			20h = graphics (system manager compliant)
			87h = alpha (non-system manager)
			A0h = graphics (non-system manager)

	Sub-functions 07h and 20h call the System Manager routine to change
	video modes, thus letting the System Manager know that the display has
	changed modes and the display contents destroyed.  This is important
	for any applications which are intended to be system manager compliant.

	Sub-functions 87h and A0h call the BIOS directly in order to change
	display modes, thus by-passing the System Manager.  These should be
	used by programs that are NOT System Manager compliant, so that they
	will function correctly whether the system was booted into the System
	Manager or if it was booted straight into DOS (by placing a SHELL=
	command in a CONFIG.SYS file).

	After a SET_MODE call to change to graphics, the defaults are:

		Logical origin		(0, 0)
		Clip region		(0, 0) thru (239, 127)
		Pen location		(0, 0)
		Pen color		1
		Replacement rule	FORCE
		Line-type		0FFFFh
		Fill mask		0FFh,0FFh,0FFh,0FFh,0FFh,0FFh,0FFh,0FFh

	Sample assembly code:

		mov	ax,0020h	; set mode to GRAPHICS
		int	5fh
			.
			.
			.
		mov	ax,0007h	; set mode to ALPHA
		int	5fh

         _____________
        SET FILL MASK

	Sets the eight-byte fill mask used by DRAW_RECTANGLE when pattern-
	filling.

	Entry conditions:

		AH = 1
		ES:DI = address of 8 bytes of fillmask.

	The default fillmask after a mode set to graphics is eight bytes of
	0ffh (which would result in a solid-fill).

	The fillmask is always aligned with the byte boundaries of the display
	memory, and it is then clipped by the rectangle being drawn.  This
	means that as the rectangle is shifted bit-by-bit, the pattern appears
	to exist on a plane behind the rectangle, and that the rectangle is
	a moving window onto that plane.  It's tough to describe, and a little
	experimentation should make it plain.

	Sample assembly code:

		fmask1	db	055h, 0aah, 055h, 0aah, 055h, 0aah, 055h, 0aah
			.
			.
			.
		assume	es:dgroup
		lea	di,fmask1
		mov	ah,1
		int	5fh		; set fillmask pattern to FMASK1

         ________________________________
        GET CURRENT GRAPHICS INFORMATION

	Returns current information about the state of the graphics functions.

	At entry:

		AH = 2
		ES:DI = address of a 36-byte long buffer into which the
			graphics information will be placed.  At exit from
			this function, the buffer contents will be:

		      offset  size
			 0   1-byte CURRENT VIDEO MODE
			 1   1-byte DEFAULT VIDEO MODE
			 2   1-word WIDTH OF DISPLAY IN PIXELS
			 4   1-word HEIGHT OF DISPLAY IN PIXELS
			 6   1-word CURRENT X-LOCATION OF PEN
			 8   1-word CURRENT Y-LOCATION OF PEN
			10   1-word CURRENT LINE-TYPE
			12   1-word CURRENT REPLACEMENT RULE
			14   1-word CURRENT PEN COLOR
			16   1-word CURRENT X-MINIMUM OF CLIP REGION
			18   1-word CURRENT X-MAXIMUM OF CLIP REGION
			20   1-word CURRENT Y-MINIMUM OF CLIP REGION
			22   1-word CURRENT Y-MAXIMUM OF CLIP REGION
			24   1-word CURRENT X-LOCATION OF LOGICAL ORIGIN
			26   1-word CURRENT Y-LOCATION OF LOGICAL ORIGIN
		      28-35  8-bytes CURRENT FILL MASK (for rectangle fill)

	At exit:
		DX:AX = address of the 36-byte long buffer (for return to C).

	Sample assembly code:

		infobuf		label	byte
		curmode		db	?
		defmode		db	?
		dspwidth	dw	?
		dspheight	dw	?
		curpenx		dw	?
		curpeny		dw	?
		curlinetype	dw	?
		curreprule	dw	?
		curpen		dw	?
		curclipminx	dw	?
		curclipmaxx	dw	?
		curclipminy	dw	?
		curclipmaxy	dw	?
		curlogorgx	dw	?
		curlogorgy	dw	?
		curfmask	db	8 dup (?)
				.
				.
				.
		assume	es:dgroup
		lea	di,infobuf
		mov	ah,2		; read current video info into infobuf
		int	5fh
         __________________
        SET LOGICAL ORIGIN

	Sets the logical origin in terms of absolute screen pixels, regardless
	of previous settings of the logical origin or clip region.  The (X,Y)
	of the logical origin may be specified off of the actual physical
	screen (ie, negative values or greater than (239, 127).  All other
	coordinate arguments in this graphics system are relative to the
	logical origin, including those used to specify the clip region.

	SET LOGICAL ORIGIN resets the CLIP REGION to the entire physical
	display (0,0) to (239,127).  So, if clip_region is used, it must be
	set AFTER the set_logical_origin.

	The default logical origin after a mode set is (0,0).

	At entry:

		AH = 3
		CX = x coordinate
		DX = y coordinate

	Sample assembly code:

		mov	ah,3
		mov	cx,120		; move log org to approximately the
		mov	dx,64		;   center of the display
		int	5fh

	_______________
	SET CLIP REGION

	This function sets the coordinates of the upper-left and lower-right
	corners of the clip rectangle.

	All reading/writing of the display in this graphics system is limited
	(clipped) by the current CLIP REGION.

	Default after mode set is (0,0) and (239,127).

	At entry:

		AH = 4 
		CX = x-minimum coordinate
		DX = y-minimum coordinate
		SI = x-maximum coordinate
		DI = y-maximum coordinate

	Sample assembly code:

		mov	ah,4		; clip (limit) all drawing to the
		mov	cx,120		;    right half of the display
		mov	dx,0
		mov	si,239
		mov	dx,127
		int	5fh

         ______________
        DRAW RECTANGLE

	This draws a rectangle which has two diagonally opposite corners at
	the current pen location and (CX,DX).  Hence, you will usually first
	do a MOVE_PEN, then a DRAW_RECTANGLE.  ALL rectangle draws obey the
	current replacement rule.  The pen location is left at the starting
	location (it is not changed).

	If the rectangle drawn is just an outline, it is drawn using the
	current line-type.  If the rectangle drawn is pattern-filled, it uses
	the current fill-mask.  In all cases the current pen color and replace-
	ment rule are used.

	At entry:
		AH = 5
		AL = fill flag	0==outline, current linetype and pen color
				1==solid fill, current pen color
				2==pattern fill, current fillmask and pen color
		CX = x-coordinate of second corner of rectangle
		DX = y-coordinate of second corner of rectangle

	Sample assembly code:

		mov	ah,8		; move pen to (50,74)
		mov	cx,50
		mov	dx,74
		int	5fh

		mov	ah,5
		mov	al,1		; solidfill rectangle to (101, 99)
		mov	cx,101
		mov	dx,99
		int	5fh

	_________
	DRAW LINE

	This draws a line from the current pen location to (CX,DX) using the
	current pen color, linetype, and replacement rule.  The pen location
	is left at the end point.  If another DRAW_LINE is executed after the
	first without an intervening MOVE_PEN, the starting point is not
	plotted.  This is to avoid the problem of drawing connecting lines
	with a replacement rule of XOR.  Since the starting point of the second
	line is the same as the ending point of the first line, it would get
	plotted twice, which in XOR mode is the same as not plotting it at all.

	At entry:

		AH = 6
		CX = x-coordinate of end point
		DX = y-coordinate of end point

	Sample assembly code:

		mov	ah,6
		mov	cx,21
		mov	dx,10		; draw from current pen location
		int	5fh		;   to (21, 10)
         __________
        PLOT POINT

	This moves the current pen location to CX,DX and plots a single
	point there using the current pen color and replacement rule.

	At entry:

		AH = 7
		CX = x-coordinate of point
		DX = y-coordinate of point

	Sample assembly code:

		mov	ah,7
		mov	cx,239		; plot point at (239, 127)
		mov	dx,127
		int	5fh

	________
	MOVE PEN

	This moves the current pen location to (CX,DX).  The default location
	after a mode set is (0,0).

	At entry:

		AH = 8
		CX = x-coordinate
		DX = y-coordinate

	Sample assembly code:

		mov	ah,8
		mov	cx,22		; move pen to (22, 44)
		mov	dx,44
		int	5fh

	_____________
	SET PEN COLOR

	Sets the current pen color to 0 or 1.  The default after a mode
	set is 1 (black).

	At entry:

		AH = 9
		AL = new pen color (0 for white or 1 for black)

	Sample assembly code:

		mov	ah,9
		mov	al,0		; set pen color to white (0)
		int	5fh

         ____________________
        SET REPLACEMENT RULE

	The replacement rule controls how the current pen color is combined
	with the existing color of a pixel on the display when performing
	any plotting function (except WRITE_AREA, which has its own replacement
	rule specified with each call).  If the current replacement rule is
	FORCE then the resulting color of a pixel is equal to the current pen
	color at the time of the plotting action.  For the other three replace-
	ment rules (AND, OR, and XOR), the resulting color is the logical
	operation between the current screen pixel color and the current pen
	color.

	The default replacement rule after a mode set is 0 (FORCE).

	At entry:

		AH = 10 (0Ah)
		AL = new replacement rule	0==FORCE
						1==AND
						2==OR
						3==XOR
	Sample assembly code:

		mov	ah,10
		mov	al,3		; set replacement rule to XOR
		int	5fh

	_____________
	SET LINE TYPE

	This is a 16-bit value that is repeated over and over as each pixel
	of a line or an outlined rectangle is drawn.  0xFFFF will cause solid
	lines to be drawn. The default after a mode set is 0xFFFF (solid line).

	At entry:

		AH = 11 (0Bh)
		CX = new line type

	Sample assembly code:

		mov	ah,11
		mov	cx,0c440h	; set line type to XX000X000X000000
		int	5fh

         __________
        READ POINT

	This returns AX==the color (0 for white, 1 for black) of the requested
	point.  The current pen location is not modified.

	At entry:

		AH = 12 (0Ch)
		CX = x-location of point to read
		DX = y-location of point to read

	Sample assembly code:

		mov	ah,12
		mov	cx,49		; read point (49,57)
		mov	dx,57
		int	5fh

	_____________________
	READ AREA (get image)

	This reads a rectangular area of the display into the specified
	buffer.  There is an 8-byte header at the beginning (specifying
	number of planes, number of bits/pixel, width of image, and
	height of image.  The first two are always equal to 1 on the HP 95LX.
	The size needed for the buffer is:

			8 + ((x2-x1+8)/8) * (y2-y1+1) bytes

	The diagonally opposite corner points (x1, y1) and (x2, y2) are
	included in the read area.  Bits with a value of 0 are added to
	the right end of each row of pixels (if necessary) to fill out an
	integral number of bytes of data for that row.  The image is always
	left justified within the buffer regardless of its byte-alignment on
	the display.

	At entry:

		AH = 13 (0Dh)
		CX = x-coordinate of corner 1
		DX = y-coordinate of corner 1
		SI = x-coordinate of corner 2
		BP = y-coordinate of corner 2
		ES:DI = address of buffer for image

	Sample assembly code:

		tmpbuf	db	56 dup (?)
		.
		.
		.
		assume	es:dgroup
		mov	ah,13
		mov	cx,24
		mov	dx,55
		mov	si,41		; read a rectangular area of the screen
		mov	bp,70		;   from (24,55) thru (41,70) into
		lea	di,tmpbuf	;   'tmpbuf'.
		int	5fh
         ______________________
        WRITE AREA (put image)

	This writes to a rectangular area of the display from a specified
	buffer.  The buffer should have the same eight-byte header described in 	READ_AREA (above).  This call is different from all other "write"-type
	calls in that it specifies its own replacement rule rather than using
	the "current" replacement rule.  It expands upon the replacement
	rule types by allowing the image to be inverted before being combined
	in the usual fashion (according to FORCE, AND, OR, or XOR) with the
	display contents.  This does not modify the contents of the buffer.

	If the entire image doesn't fit on the display, none of it is drawn.

	At entry:

		AH = 14 (0Eh)
		AL = replacement rule	0 FORCE
					1 AND
					2 OR
					3 XOR
					4 invert image and then FORCE
					5 invert image and then AND
					6 invert image and then OR
					7 invert image and then XOR
		CX = x-location of top-left corner of image destination
		DX = y-location of top-left corner of image destination
		ES:DI = address of image

	Sample assembly code:

		tmpbuf	db	56 dup (?)
		.
		.
		.
		assume	es:dgroup
		mov	ah,14
		mov	al,7		; invert, then XOR
		mov	cx,133
		mov	dx,66
		lea	di,tmpbuf	; put image 'tmpbuf' at (133,66)

         __________
        WRITE TEXT

	Writes the specified text (all 256 chars are legal EXCEPT 0)
	to the specified location, horizontally or rotated 90 degrees
	counter-clockwise from horizontal, using the BIOS 6x8 font, the
	current pen color and replacement rule. The specified location (CX, DX)
	is the top-left corner of the text string, or if the rotate flag
	is non-zero, the string is rotated 90 degrees counterclockwise about
	the point (CX, DX) (such that it is now the bottom-left corner of the
	text).

	At entry:

		AH = 15 (0Fh)
		AL = rotate flag.
		CX = x-coordinate of top-left corner of first character
		DX = y-coordinate of top-left corner of first character
		ES:DI = address of null-terminated string

	Sample assembly code:

		txtstr	db	"This is a test",0
		.
		.
		.
		assume	es:dgroup
		mov	ah,15
		mov	al,0		; plot text horizontally
		mov	cx,124
		mov	dx,37		; at (124, 37)
		lea	di,txtstr
		int	5fh

         ___________________________________________________________________
         APPENDIX A: Sample assembly language module of C-callable functions

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
;[ Graphics interface module for calling Jaguar graphics from C programs [
;[ Copyright 1990 Hewlett Packard Company.  All rights reserved.	 [
;[ Author: Everett Kaser  August 14, 1990.				 [
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

	.MODEL	LARGE,C

	.CODE
	assume	ds:nothing

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_Mode(int BiosVideoMode);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_Mode		PROC	BiosVideoMode:word
	mov	ax,BiosVideoMode
	xor	ah,ah
	int	5fh
	ret
G_Mode		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_FillMask(maskptr);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_FillMask	PROC	uses ES DI, maskptr:dword
	les	di,maskptr
	mov	ah,1
	int	5fh
	ret
G_FillMask	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_GetInfo(G_INFO *gp);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_GetInfo	PROC	uses ES DI, gp:dword
	les	di,gp
	mov	ah,2
	int	5fh
	ret
G_GetInfo	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_LorgA(int x, int y);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_LorgA		PROC	x:word, y:word
	mov	cx,x
	mov	dx,y
	mov	ah,3
	int	5fh
	ret
G_LorgA		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_ClipL(int xmin, int ymin, int xmax, int ymax);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_ClipL		PROC	uses SI DI, xmin:word, ymin:word, xmax:word, ymax:word
	mov	cx,xmin
	mov	dx,ymin
	mov	si,xmax
	mov	di,ymax
	mov	ah,4
	int	5fh
	ret
G_ClipL		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_Rect(int x, int y, int fillflag);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_Rect		PROC	x:word, y:word, fill:word
	mov	cx,x
	mov	dx,y
	mov	ax,fill
	mov	ah,5
	int	5fh
	ret
G_Rect		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_Draw(int x, int y);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_Draw		PROC	x:word, y:word
	mov	cx,x
	mov	dx,y
	mov	ah,6
	int	5fh
	ret
G_Draw		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_Point(int x, int y);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_Point		PROC	x:word, y:word
	mov	cx,x
	mov	dx,y
	mov	ah,7
	int	5fh
	ret
G_Point		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_Move(int x, int y);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_Move		PROC	x:word, y:word
	mov	cx,x
	mov	dx,y
	mov	ah,8
	int	5fh
	ret
G_Move		endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_ColorSel(int color);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_ColorSel	PROC	color:word
	mov	ax,color
	mov	ah,9
	int	5fh
	ret
G_ColorSel	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_RepRule(int rrule);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_RepRule	PROC	rrule:word
	mov	ax,rrule
	mov	ah,0ah
	int	5fh
	ret
G_RepRule	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_LineType(int ltype);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_LineType	PROC	ltype:word
	mov	cx,ltype
	mov	ah,0bh
	int	5fh
	ret
G_LineType	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_PointRead(int x, int y);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_PointRead	PROC	x:word, y:word
	mov	cx,x
	mov	dx,y
	mov	ah,0ch
	int	5fh
	ret
G_PointRead	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_ImageGet(int x1, int y1, int x2, int y2, char far *image);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_ImageGet	PROC	uses ES SI DI, x1:word, y1:word, x2:word, y2:word, image:dword
	mov	cx,x1
	mov	dx,y1
	mov	si,x2
	les	di,image
	mov	bp,y2
	mov	ah,0dh
	int	5fh
	ret
G_ImageGet	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_ImagePut(int x, int y, char far *image, int replacerule);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_ImagePut	PROC	uses ES DI, x:word, y:word, image:dword, reprule:word
	mov	cx,x
	mov	dx,y
	les	di,image
	mov	ax,reprule
	mov	ah,0eh
	int	5fh
	ret
G_ImagePut	endp

;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
; G_Text(int x, int y, char far *string, rotflag);
;[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[

G_Text		PROC	uses DS ES SI DI, x:word, y:word, string:dword, rotflag:word
	mov	ax,rotflag
	mov	cx,x
	mov	dx,y
	les	di,string
	mov	ah,0fh
	int	5fh
	ret
G_Text		endp

@curseg	ends
	end
         ______________________________________________________________________
         APPENDIX B: Sample header file for use with C programs and APPENDIX A.

/*[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
  [ Definitions.							[
  [[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[*/

#define	G_ALPHA		0x07
#define	G_GRAPHICS	0x20

#define	G_FORCE		0
#define	G_AND		1
#define	G_OR		2
#define	G_XOR		3
#define	G_NOTFORCE	4
#define	G_NOTAND	5
#define	G_NOTOR		6
#define	G_NOTXOR	7

#define	G_OUTLINE	0
#define	G_SOLIDFILL	1
#define	G_PATTERNFILL	2

#define	MINCOLOR	0
#define	MAXCOLOR	1

/*[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
  [ Structures.								[
  [[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[*/

typedef	struct g_info {
	unsigned char	vidmode;
	unsigned char	defmode;
	unsigned int	xpixels;
	unsigned int	ypixels;
	int		xloc;
	int		yloc;
	unsigned int	linetype;
	int		rrule;
	unsigned int	color;
	int		xclipmin;
	int		yclipmin;
	int		xclipmax;
	int		yclipmax;
	int		xlorg;
	int		ylorg;
	unsigned char	fillmask[8];
	} G_INFO;

/*[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[
  [ Graphics library function definitions.  All x,y locations are rel-  [
  [   ative to the current logical origin unless specified otherwise.	[
  [[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[[*/
void   far cdecl	G_Mode(int);
G_INFO far * cdecl	G_GetInfo(G_INFO far *);
void   far cdecl	G_ColorSel(int);
void   far cdecl	G_RepRule(unsigned int);
void   far cdecl	G_LineType(unsigned int);
void   far cdecl	G_FillMask(unsigned char far *);
void   far cdecl	G_LorgA(int, int);
void   far cdecl	G_ClipL(int, int, int, int);
void   far cdecl	G_Move(int, int);
void   far cdecl	G_Point(int, int);
int    far cdecl	G_PointRead(int, int);
void   far cdecl	G_Draw(int, int);
void   far cdecl	G_Rect(int, int, int);
void   far cdecl	G_ImageGet(int, int, int, int, char far *);
void   far cdecl	G_ImagePut(int, int, char far *, int);
void   far cdecl	G_Text(int, int, char far *, int);

/*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/

/**** G_MODE(mode): mode = {G_TEXT | G_GRAPHICS}
	changes the display mode to text or graphics		*/

/**** G_GETINFO(GraphInfoPtr): GraphInfoPtr is a far pointer to a buffer of
	the programmers choosing where the graphics information will be copied.
	See the typedef for the G_INFO structure in this file for the contents
	of the buffer.	*/
/*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/

/**** G_COLORSEL(color): color = 0 or 1
	sets the current pen to "color"				*/

/**** G_REPRULE(reprule): reprule = {G_FORCE | G_AND | G_OR | G_XOR}
	sets the current replacement rule for all other drawing (except for
	G_ImagePut, which specifies its own replacement rule). */

/**** G_LINETYPE(linetype): linetype = a 16-bit image that is repeated while
	drawing lines and G_OUTLINE'd rectangles.  Bits that are 1 cause the
	current pen color to be plotted using the current replacement rule.
	Bits that are 0 are not plotted and leave the display un-modified. */

/**** G_FILLMASK(buffer): buffer is a far pointer to an 8-byte array which
	specifies the fillmask to use when doing drawings of rectangles
	with a fillflag of G_PATTERNFILL.  Every bit that is a 1 will
	cause a point of the current color to be plotted.  Every bit that is
	a 0 will cause that "point" of the display to be undisturbed. */
/*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/

/**** G_LORGA(x,y): x,y = -32768 to +32767
	sets the logical origin (0,0) to be located at the absolute screen
	coordinate specified by x,y. */

/**** G_CLIPL(x1, y1, x2, y2): x1,y1,x2,y2 = -32768 to +32767
	sets the current clip boundary to the rectangle whose diagonally
	opposite corners are specified by the absolute screen coordinates
	equal to the x1,y1 and x2,y2 offsets from the current logical origin.*/
 /*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/

/**** G_MOVE(x, y): x,y = -32768 to +32767
	causes the logical pen to be moved to "x,y"		*/

/**** G_POINT(x,y): x,y = -32768 to +32767
	plots a point of the current pen color with the current replacement
	rule at "x,y" unless "x,y" is outside the current clip limits	*/

/**** G_POINTREAD(x,y): x,y = -32768 to +32767
	reads the color of the point located at x,y and returns that as the
	value of the function. */

/**** G_DRAW(x,y): x,y = -32768 to +32767
	draws a line of the current pen color with the current replacement rule
	and the current linetype from the current pen location to "x,y";
	only those points lying within the clip limits are actually plotted. */

/**** G_RECT(x,y,fillflag): x,y = -32768 to +32767
	fillflag = {G_OUTLINE | G_SOLIDFILL | G_PATTERNFILL}
	draws a rectangle with diagonally opposite corners at the current pen
	location and at "x,y", using the current pen color and replacement
	rule.  The "type" of rectangle drawn is determined by fillflag.
	if fillflag==G_OUTLINE, the outline of a rectangle is drawn, using the
		current linetype.
	if fillflag==G_SOLIDFILL, a solid, filled rectangle of the current
		color is drawn.
	if fillflag==G_PATTERNFILL, a pattern filled rectangle of the current
		color is drawn, using the current fill mask.	*/
/*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/

/**** G_IMAGEGET(x1, y1, x2, y2, buffer):  x1,y1,x2,y2 = -32768 to +32767
	If both points x1,y1 and x2,y2 are within the current clip boundary,
	the display image bounded by the rectangle whose diagonally opposite
	corners are x1,y1 and x2,y2 is read into the bytes pointed to by
	"buffer". */

   NOTE: for G_ImageGet(), the required size of 'buffer' is (on Jaguar):

	8 + ((x2-x1+8)/8) * (y2-y1+1) bytes          */

/**** G_IMAGEPUT(x, y, buffer, reprule): x,y = -32768 to +32767
	reprule = {G_FORCE | G_AND | G_OR | G_XOR | G_NOTFORCE | G_NOTAND |
			G_NOTOR | G_NOTXOR}
	if x,y and the un-specified bottom-right corner of the image are
	within the clip boundary, the image from "buffer" is drawn on the
	display using reprule as the replacement rule.  (For the "NOT" replace-
	ment rules, the image is color-inverted first, then placed on the
	display using the "rest" of the replacement rule.) */
/*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/

/**** G_TEXT(x,y,buffer,rotflag): x,y = -32768 to +32767, rotflag = 0 or 1
	draws the string pointed to by "buffer" on the display at the specified
	location x,y using the current font. If rotflag = 0, it's drawn
	horizontally, else it's rotated 90 degrees counterclockwise. */
/*\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\\*/