Vivid 2.0      March 14, 1992

                      Copyright 1989-1992 by Stephen B. Coy


                                Table of Contents


            Introduction . . . . . . . . . . . . . . . . . .   2
            Changes for Version 2.0. . . . . . . . . . . . .   3
            Running Vivid. . . . . . . . . . . . . . . . . .   5
            Statistics Display . . . . . . . . . . . . . . .   7
            Legal Stuff. . . . . . . . . . . . . . . . . . .   9
            Acknowledgements . . . . . . . . . . . . . . . .  11
            Input File Format. . . . . . . . . . . . . . . .  13
        	Preprocessor . . . . . . . . . . . . . . . .  15
        	Studio . . . . . . . . . . . . . . . . . . .  17
        	Lights . . . . . . . . . . . . . . . . . . .  24
        	Surfaces . . . . . . . . . . . . . . . . . .  28
        	    bump mapping . . . . . . . . . . . . . .  31
        	    solid texture. . . . . . . . . . . . . .  33
        	    Mandelbrot . . . . . . . . . . . . . . .  36
        	Geometric Primatives . . . . . . . . . . . .  37
        	    sphere . . . . . . . . . . . . . . . . .  37
        	    ring . . . . . . . . . . . . . . . . . .  38
        	    polygon. . . . . . . . . . . . . . . . .  39
        	    triangular patch . . . . . . . . . . . .  40
        	    cone . . . . . . . . . . . . . . . . . .  41
        	Transformations. . . . . . . . . . . . . . .  42
        	Clipping . . . . . . . . . . . . . . . . . .  44
            Support Programs . . . . . . . . . . . . . . . .  46
        	img2gif.exe. . . . . . . . . . . . . . . . .  46
        	paste.exe. . . . . . . . . . . . . . . . . .  50
        	up.exe . . . . . . . . . . . . . . . . . . .  51
        	down.exe . . . . . . . . . . . . . . . . . .  52
            File Formats . . . . . . . . . . . . . . . . . .  53
            Bibliography . . . . . . . . . . . . . . . . . .  54
            Index. . . . . . . . . . . . . . . . . . . . . .  55
        













                                        1





                            Introduction to Vivid 2.0
 
             Surprise!  Yes, 2.0 is finally here.  I'd like to appologize
        to those of you who have been waiting for many months for this to
        come out.  I've been busy doing my Master's thesis and, of
        course, adding "just this one more feature." A few bugs were
        squashed in the process although I'm sure that new ones have been
        breeding in the walls just waiting until this release.  Even with
        the bugs I still consider Vivid to be one of the finest ray
        tracers (I've) ever written. 
 
             In the archive you received should be this document, the
        Vivid executable, some sample input files, and tools for
        processing the image after it has been generated.  Vivid.exe has
        been compiled to run on any MS-DOS based system with a 286 or
        better and a math coprocessor.  Ray tracing can be extremely slow
        and anything less is really not worth it.  If, however, you don't
        believe me feel free to write and I'll send you a copy compiled
        for an bare 8086.  I hope you don't plan on using your PC in the
        next month.  Back to the 286/287 version.  This version also
        contains a DOS extender allowing Vivid to take advantage of any
        extended memory you may have.  For those of you that still want
        something better I also have 386 versions available.  See the
        Legal Stuff section for more info. 
 
             The rest of this document explains the details of how to run
        Vivid and the tools and how to construct an input file.  I
        recommend that you print out this file and a couple of the sample
        input files when first learning Vivid.  An example is worth a
        thousand words, or at least the paper it's printed on. 























                                        2





                      (Most of the) Changes for Version 2.0

 
             I learned to spell Mark VandeWettering's name correctly. 
        Sorry about version 1.0 Mark. 
 
             Inside/outside problems have been resolved eliminating the
        need to have spheres with negative radii or worry about clockwise
        vs counter-clockwise polygons. 
 
             Polygon patches are a lot healthier. 
 
             I plugged my brain back in.  The description of fuzzy
        spheres given in the 1.0 docs is wrong.  But it's better now. 
 
             When using the depth of field option a new "samples"
        parameter has been added to allow you to control the number of
        rays per pixel used. 
 
             Spherical light sources also allow the "samples" parameter
        to determine the number of shadow rays shot toward them. 
 
             There is no longer a limit on the number of lights except
        for memory and your patience.  The limit was 20 but this info
        never made it into the docs for version 1.0.  The limit on number
        of objects has also been removed although due to the operating
        system an effective limit of about 2000 objects still remains. 
        The DOS extender version is limited only by memory. 
 
             The number of objects contained within a bounding box may
        now be specified.  The default, 4, is equal to the prior, fixed
        value.  This can be specified by adding
        	bunching 6
        to the studio structure.  Changing this value will affect the
        performance of the automatic bounding box construction.  Results
        are image dependent but I think that 4 is a good default value. 
 
             A bug in the camera model caused the image to become
        distorted when the up vector given in the studio structure wasn't
        perpendicular to the direction of view.  It has been fixed. 
 
             The traditional flat projection model has been joined by not
        one, not just two, but by three other projection models,
        spherical, othographic and parallax.  See the section on the
        studio structure for details. 
 
             The input file format has been changed to eliminate the need
        for semicolons and equals signs.  In order to be compatable with
        the old file format, they are still accepted but are now treated
        just as a space would be treated. 
 
             A quick-render mode has been added to help speed up

                                        3




        previews. 
 
             Simple math operations are now supported by the parser. 
        These operations are supported on numbers and on vectors (rgb
        triples and xyz coordinates).  The following is a list of the
        operations supported.  Vectors operations supported include cross
        product, addition, subtraction, scaling, and dot product. 
        Numerical operations include multiplication, division, addition,
        subtraction and exponentiation.  Sine, cosine, tangent, arcsine,
        arccosine, arctangent and square root functions are also
        supported. 
 
             Cylinders can now be specified by giving a cone a single
        radius parameter. 
 
             Preprocessor is here.  include files, defines, undefs and
        lack of fixed colors which are now replaced with color.vc. 
 
             Global transformations are now supported.  Together with
        include files this should make scene modeling much easier. 
 
             Primitives can now be clipped by planes, spheres or cone
        allowing easier generation of more complex models. 
 
             The background can have a palette mapped to it rather than
        just having a single color. 
 
             A new bunch of command line switches are now supported. 
        Typing vivid on the command line without any arguements will give
        you a listing of them. 
 
             The keyword "noise" is now "turbulence" to better follow the
        literature. 





















                                        4





                                  Running Vivid
 
             Vivid input files use the extension .v and the output files
        use .img.  With the preproccessor in Vivid, include files are
        also supported.  These may have any extension.  The syntax for
        including a file into your input file is:
        
        	#include filename
        
 
             Include files may have any extension you choose.  The
        following is a list of the file extensions that I regularly use. 
        If we all use the same convention it should make things easier
        for trading input files.  Feel free come up with your own
        conventions if that suits you better. 
        
        	.v      Main input file for an image.  Required.
        	.img    24-bit output file.
        	.map    palette file for img2gif or background mapping.
        	.vc     include file with color definitions.  See color.vc.
        	.vo     include file with object definition.
        	.vs     include file with surface definitions.
        
 
             The .img files produced by Vivid are full 24-bit color.  The
        details of their format are explained later in this document. 
        Since most systems can't display 24-bit graphics I've included a
        tool to convert the .img files into .gif files which can be
        displayed using vpic or cshow.  This tool is called img2gif.  Its
        workings are also detailed later.  In general the procedure for
        generating an image will look like this:
        
        1)  Create an input file, test.v, with your favorite text editor.
        2)  Run Vivid.
        	C>vivid test
        3)  Wait until done.  This can take from a few minutes to a
            couple of days depending on the complexity of the image
            and the speed of your machine.  This is a good time to
            raid the fridge.
        4)  Convert the result, test.img, into a .gif file.
        	C>img2gif -m -d test
            The -m flag tells img2gif to use median cut to determine
            the palette.  The -d flags turns on Floyd-Steinberg
            dithering.
        5)  View the image.
        	C>vpic test.gif
        
        
 
             Because of the way I implemented the preprocessor Vivid
        creates a temporary file on the disk called xyzzy.v.  At this
        time, Vivid does not delete the file after it is done using it. 

                                        5




        The reason I leave this is that it is sometimes useful to look at
        when trying to figure out what the preprocessor is doing with
        your input definition.  Feel free to delete it at any time. 

                                        
 
             Vivid supports a number of command line flags.  These flags
        allow you to change the operation of the program without changing
        the input file.  The following command line flags are now
        supported:
        
        	-s      Run in silent mode, ie no statistics display.
        	-r      Resume.
        	-i x y  Set image size to x by y pixels.
        	-n      No_shadows, same as studio flag.
        	-d #    Set maximum recursion depth value
        	-a mode Set antialias mode.  Valid modes are: none,
        		quick, corners and adaptive.  Since I can't type
        		I've made it so that you only have to give the
        		first letter of the mode for it to work.
        	-p      Don't use the preprocessor.
        
 
             Vivid has the ability to resume the generation of an
        interrupted image.  If during image generation you need to stop,
        hitting ctrl-C or ctrl-BREAK will cause Vivid to stop at the end
        of the next scan line.  This may be up to a few minutes for a
        slow image.  This only works if statistics are enabled (the
        default).  Later, the image generation may be resumed by using
        the -r flag on the command line. 
























                                        6





                                   Statistics

 
             Surprisingly enough some people are curious about the
        statistics that Vivid displays while processing.  Somehow they
        actually got the idea that the numbers may contain useful
        information if only they were documented somewhere.  The secret
        is out.  They don't mean a thing.  I just put them in there
        because I like watching them change while I'm waiting for the
        image to generate.  Sorry to break your bubble.  OK, fine, I'm
        joking, happy now?
 
             When you run Vivid it displays the current version number
        and the copyright notice.  It then displays the filename of the
        input files as the preprocessor digests them.  Next a running
        total of lights and primitives is displayed as the parser reads
        the preprocessed input file.  Once the file is completely read in
        the automagic bounding box code is called.  As it generates
        bounding boxes you see the number of primitives climb.  Upon
        completion of the bounding box generation the scene extent is
        displayed.  This is the minimum and maximum values in each axis
        for all the primitives.  At this time the first scan line is
        starting to be rendered.  When it is done the screen will clear
        and a full display of current statistics will be displayed.  The
        meanings for each of the numbers will now be described in
        glorious detail bereft of all attempts at obfuscation.  I hope
        this makes sense. 
 
             The resolution is the size of the final image in pixels. 
        The line display next to it shows the progress of the ray tracer. 
        For example, if you where generating an image 320 pixels wide and
        200 pixels tall the resolution would display 320x200
        (unbelievable!) and the line value would go from 0 to 200.  In
        quick mode this number will increment by 6 instead of 1. 
 
             The next four lines contain information about the number of
        rays cast.  Eye rays are the rays cast from the viewpoint out
        into the scene.  Reflected rays are those generated by a specular
        surface and refracted rays are those generated by transparent
        surfaces.  The total is just the sum of these rays.  If your
        input file doesn't have any reflective or transparent surfaces
        these numbers will stay 0. 
 
             The next section contains information about shadow rays. 
        Shadow rays are the rays shot from the point of intersection
        toward each light in order to determine if there are any other
        primitives in the scene blocking the light (casting a shadow). 
        Vivid uses a shadow cache to try and speed up this process. 
        Cache hits signify an instance when the cached object was found
        to cast a shadow and no ray was cast.  The cache percentage is
        just the number of hits divided by the number of shadow rays. 
 

                                        7




             The next number is the average number of rays cast per
        pixel.  This number can give you a fair idea of just how hard the
        ray tracer is working to generate the image.  With no
        antialiasing, reflection, or refraction this number should be
        1.0.  Adaptive antialiasing can push this as high as 16 depending
        on the amount of extra work it does.  Reflected and refracted
        rays will make this even higher.  Using the quick mode this
        number may go to as low as .066 or so.  When this number is less
        than 1 that means that the ray tracer is guessing at some of the
        pixels instead of actually casting a ray for them. 
 
             The average queues per ray value has to do with the bounding
        scheme.  The automatic bounding box generator creates a tree-like
        heirarchy of bounding boxes for the system to test each ray
        against.  If a box is intersected by a ray then the objects in
        the bounding box (either other bounding boxes or primitives) are
        entered into the priority queue for further intersection testing. 
        The "bounds checked" number shows how many bounding box
        intersection tests were performed.  The "queue inserts" number
        shows how many object passed the bounds check and were put into
        the priority queue.  The "queue resets" number displays the total
        number of times the priority queue was reset.  This should be
        equal to the total number of rays plus the number of shadow rays
        plus the number of cache hits.  Don't ask why, it just will be. 
        The "max queue size" number shows the maximum number of objects
        in the queue during the rendering. 
 
             The final number, the max recursion depth, shows the maximum
        number of levels deep the ray tracer had to go while rendering
        the image.  The number after the slash is the max depth it is
        allowed to go. 























                                        8





                                   Legal Stuff

        	Vivid is Copyright 1989-1992 by
        	Stephen B. Coy
        	All Rights Reserved.
 
             You are free to redistribute this package in its entirety. 
        In doing so you may charge no more than a nominal fee for
        duplication.  No part of this package may be included as part of
        a commercial package without explicit written permission.  If you
        have any questions about commercial distribution of Vivid or its
        tools I can be contacted at:
        
        	Stephen Coy
        	Vivid Software
        	15205 NE 13th Pl.  #2904
        	Bellevue, WA  98007
        	(206) 641-8615
        
        	INTERNET:    coy@ssc-vax.boeing.com or
        		     uw-beaver!ssc-vax!coy
        	CompuServe:  70413,136
        
 
             Originally I thought of distributing Vivid via shareware but
        I seriously dislike the guilt games most shareware authors
        include.  So, I've decided to try beggarware.  Here's the
        product.  Use it.  If you like it I'd be very happy if you'd sent
        a check for $30.  If you think $30 is out of line, send less (or
        more) or beer.  If you don't think Vivid is worth diddly at least
        send a postcard explaining why you don't like it.  If you want
        the 386 versions you'll have to register at the $50 level.  Sorry
        about that but times are tough and compilers aren't cheap. 
        Anyway that's about the price of an average game lately so I
        don't think it's too far out of line.  As is usual I will also
        accept severe sob stories, beer, software (nothing pirated, thank
        you), barter goods, and young women instead of money.  The 386
        diskette contains versions of Vivid compiled with both the
        Zortech and the Intel compilers giving you a choice of DOS
        extenders to work with.  The Intel version is DPMI compliant and
        has the advantage of supporting virtual memory allowing you to
        allocate up to 128Mb of disk space as memory for those seriously
        huge models.  The Zortech version is DPMI, VCPI and XMS
        compatible and takes up less space.  It also seems to be able to
        find about 500K more memory than the Intel version but doesn't
        directly offer virtual memory support.  If another DPMI host
        which supports virtual memory is active, Windows 3.0 running in
        386 enhanced mode for instance, then the Zortech version can take
        advantage of it. 
 
             Whether you send anything or not I would like to hear about
        any suggestions or bugs.  Of course requests accompanied by money

                                        9




        will tend to get higher priority.  I will answer all mail and
        email even though I may be a bit slow at times.  Email tends to
        get the fastest response.  If you have tried to contact me and
        not gotten a response please try again.  If you still don't get a
        response you might have to resort to US Mail. 
 
             For those of you into BBSing I can be contacted via any of
        the ADEnet nodes.  ADEnet is a network of BBSs primarily
        dedicated to providing professional quality support for AutoCAD
        and other CAD programs.  In addition there is also an animation
        and rendering conference where questions about Vivid, or graphics
        in general, will be answered.  I usually log in on a daily basis
        so turn around is quite quick.  Another BBS I log into a lot is
        TurboTech.  Ray Johnson, TurboTech's sysop and the author of
        TurboCit, has provided a room for ray trace discussions and has
        plenty of disk space for images.  Check out the conversations,
        too.  The BBS attracts some interesting people.  I also frequent
        CompuServe's COMART forum for those of you with deeper pockets. 
 
             Ray Johnson's Turbo Tech BBS can be reached at
        (206)362-6828. 

                 Alacrity Design & Engineering Network (ADEnet)

 
             ADEnet serves the design and engineering communities by
        making information useful to them widely available.  This is done
        in three ways: the ADEnet message conferences, the sharing of
        programs and data files across ADEnet and the dissemination of
        industry news and press releases. 

                              ADEnet Member Listing

 
             The following is a listing of the current ADEnet Member
        BBSs.  Each ADEnet Member is an independant BBS operated by a
        local sysop. 
        Alacrity Software BBS    206-643-5477 Bellevue, WA       DUAL (14.4)
        The Graphics Alternative 510-524-2780 El Cerruto, CA     DUAL (14.4)
        Off Broadway             510-547-5264 San Francisco, CA  V32
        PC-AUG BBS               602-952-0638 Phoenix, AZ        DUAL (9600)
        Mind Image BBS           612-781-1720 Minneapolis, MN    v22, MNP5
        LABB                     717-394-1357 Lancaster, PA      v22, MNP5 [%]
        AEC-ONLINE               818-360-7022 Los Angeles, CA    v22
        The University BBS       908-544-8193 Shrewsbury Twp, NJ DUAL (14.4)
        AZCAD BBS              +61-3-481-6873 Australia          v32bis
        
 
             Each of the listings has the BBS name and it's (primary)
        phone number followed by the location.  At the end of listing is
        the highest allowable bits per second (bps) and protocol. 
        DUAL - US Robotics Dual Standard supporting HST and v.32/v.42bis
        HST  - US Robotics Courier HST

                                        10




        v32  - Industry standard v.32/v.42bis supporting upto 9600 bps
        v32b - Industry standard v.32bis/v.42bis supporting upto 14.4k bps
        v22  - Industry standard v.22 supporting upto 2400 bps
        MNP5 - Indicates support Microcom Network Protocol Class 5
        v42b - Indicates support for CCITT v.42bis
        
        [*] CAD/Engineering Services BBS accepts calls between 22:00-05:00 CST.
        [%] LABB is a multiline system, of which only the main line is listed.
        
 
             The following is a listing of the current ADEnet message
        conferences. 
               Conference  Description
               --------------------------------------------------------
               Autodesk    Autodesk product support
               A/E/C       Architectual, Engineering and Construction
               CAD/CAM     Manufacturing, NC Programming
               Civil       Civil engineering
               CompuGFX    Computer graphics, rendering and animation
               DTP         Desktop publishing
               ForSale     Buy & Sell used equipment, job listings
               Generic     Generic Software product support
               GIS         Geographical information services
               uStation    Integraph Microstation support
               News        Industry news and press releases
               Public      Network wide (ADEnet) general conference
               TechTalk    Technical hardware and software discussions
        


                                 Joining ADEnet

 
             If you are the system operator of a BBS and interested in
        joining ADEnet, please download ADENET.ZIP.  Within is a more
        detailed introduction to ADEnet, an application form, and all of
        the necessary information and data files you'll need. 
 
             ADEnet currently supports PC-Relay, QWK/REP, and FidoNet's
        echomail message networking protocols.  Alacrity Software BBS
        serves as the ADEnet hub for nodes using either PC-Relay or
        QWK/REP.  The University BBS acts as ADEnet's "bridge" to nodes
        using echomail. 











                                        11





                                Acknowledgements
 
             First on the list I must thank Mark VandeWettering for his
        raytracer MTV.  Some pieces of Vivid have been lifted directly
        from MTV's code.  Hopefully, I only took the bug-free ones.  I'd
        like to thank Mike Thompson for his various contributions both
        technical and fermented.  Thanks to Gregor Harrison for a lot of
        help understanding lex & yacc.  I still am somewhat confused but
        I like it that way.  Thanks to Jason Osgood of ADEnet for
        providing a forum for my rantings about Vivid.  Thanks to Drew
        Wells for encouraging me to join CompuServe.  And thanks to all
        those folks who unwittingly helped Vivid through their postings
        to usenet.  Finally, I'd like to thank all of you who took time
        to send comments (and images and beer and money) for version 1. 
        Coming home to a nice letter and a check in the mail rather than
        just bills makes the whole week go better.  Thank you. 
        
        GIF is a trademark of CompuServe
        MS-DOS is a trademark of Microsoft
        
        
































                                        12





                                Input File Format
 
             One thing to keep in mind while creating Vivid input files
        is that Vivid's parser is case sensitive.  Macros (see
        preprocessor section) are also case sensitive. 
 
             Vivid uses a right-handed coordinate system for defining the
        location of objects in space.  A right-handed coordinate system
        can be visualized as having the x axis pointing to the right, the
        y axis pointing into the screen and the z axis pointing up.  Each
        object in a scene file will be defined as having a location in
        space defined by an x, y, z triple in this coordinate system. 
 
             Colors are defined by an r, g, b triple where each component
        generally falls in the range 0..1.  To make picking colors easier
        Vivid includes the file color.vc which contains a few dozen
        predefined colors.  Their names and rgb values can be had by
        viewing or printing color.vc.  If this file is #included at the
        top of you input file these names can be used anywhere an rgb
        triple is called for. 
 
             Simple math operations are now supported by the parser. 
        These operations are supported on numbers and on vectors (rgb
        triples and xyz coordinates).  The following is a list of the
        operations supported.  Vectors operations supported include cross
        product, addition, subtraction, scaling, and dot product. 
        Numerical operations include multiplication, division, addition,
        subtraction and exponentiation.  Sine, cosine, tangent, arcsine,
        arccosine, arctangent and square root functions are also
        supported. 
        
        	Vector ops
        	----------
        	a b c cross x y z       cross product, yields a vector
        	a b c dot x y z         dot product, yields a number
        	a b c + x y z           vector addition, yields a vector
        	a b c - x y z           vector subtraction, yields a vector
        	a b c * n               scale a vector by n
        	a b c / n               scale a vector by 1/n
        	-(a b c)                negate a vector
        
        	Numeric ops
        	-----------
        	sin(x), cos(x), tan(x)  trig functions
        	asin(x), acos(x), atan(x)
        	sqrt(x)                 returns square root of x
        	pow(x y)                returns x to the yth power
        	*, /, +, -              normal mathematical operations
        
 
             It should be noted that these operations introduce some
        ambiguity to the input language.  This problem is aggravated by

                                        13




        the fact that the parser can only look one token ahead when it
        tries to decide how to treat its current input.  I encourage you
        to avoid any such problems by generously using parantheses to
        eliminate any possible ambiguity in your equations.  For example:
        
        	n * a b c can result in either
        	(n*a) b c or
        	(n*a) (n*b) (n*c)
        	depending on how the parser is feeling that day.
        
        
 
             If you really want to I'm sure that you could figure out
        what the parser is doing but that may change in the future so
        save yourself the trouble and just add the parentheses. 
 
             Comments can also be included in the input file.  Like
        comments in computer programs, comments in Vivid input files are
        ignored by the input parser.  Comments in Vivid use the same
        syntax as comments in C++ do.  Multi-line comments start with /*
        and end with */.  Anything between the comment delimeters is
        ignored.  Single line comments start with // and end at the end
        of the line.  For example:
        
        /*      This is a comment
        	which spans multiple lines  */
        
        //      This is a single line comment
        
        
 
             Comments should be used as notes in your input files to help
        remind you or anyone else reading the file what the input is
        trying to do.  Comments can also be used to block out part of the
        input file while you are setting it up to help speed up test
        renderings. 
 
             Normally an input file will be made up of a studio
        definition which describes the image size, antialiasing and
        viewpoint followed by the definitions for lights, surfaces, and
        objects.  Object definitions only deal with the geometry of the
        object.  The surface characteristics (color, shine) of the object
        are taken from the last surface definition preceding the object. 











                                        14





                                  Preprocessor

 
             To make writing input files easier, Vivid's parser also has
        a preprocessor.  Currently, the preprocessor only supports two
        functions, the definition of macros and support for include
        files.  Because of the way I implemented the preprocessor Vivid
        creates a temporary file on the disk called xyzzy.v.  (Didn't I
        already mention this? deja vu) At this time, Vivid does not
        delete the file after it is done using it.  The reason I leave
        this is that it is sometimes useful to look at when trying to
        figure out what the preprocessor is doing with your input
        definition.  Feel free to delete it at any time. 
 
             Macros allow you to associate a name with a string of
        characters.  When the parser sees the name in the input file it
        will substitute the appropriate string before continuing.  A
        simple example of this is the color definitions in the file
        color.vc.  In color.vc the colors white and blue are defined like
        this:
        
        #define blue    (0 0 1)
        #define white   (1 1 1)
        
 
             Once defined you can then use the word "white" wherever you
        would normally have to type (1 1 1).  For example, to create a
        blue surface with a white highlight you could then do this:
        
        surface {
        	diffuse blue
        	shine 20 white
        }
        
 
             Macro names must start with a letter and may contain
        letters, numbers, and the underscore character "_".  Macro names
        are case sensitive.  Note than in the examples I define the
        colors with parentheses around the rgb values.  This is not
        required but helps eliminate any potential parser problems as
        mentioned in the section on the parser's math ability.  You can
        undefine a macro using the #undef keyword. 
        
        #undef blue
        
 
             If you define the same macro more than once the old values
        are put onto a stack and the newest one will always be used.  If
        you then undefine the macro, only the newest one will be deleted
        and the next newest definition will then be active.  If you want
        to define a macro that is longer than one line you have to use
        the backslash, "\", as a continuation character. 

                                        15




        
        #define BLUE_PLASTIC                    \
        	surface {                       \
        		diffuse blue            \
        		shine 20 white          \
        	}
        
 
             Notice that the last line does not have a backslash after
        it.  Once defined you can then just use the name BLUE_PLASTIC in
        the input file wherever you would normally type in the whole
        surface declaration. 
 
             The other preprocessor directive is #include.  This allows
        you to include other files into your input file.  Look at the
        sample input files and notice that almost the first thing in the
        file is a line like:
        
        #include color.vc
        
 
             This causes the parser to read in the file color.vc which
        defines a standard set of colors for use in creating input files. 
        Using Dan Farmer's color editor it is quite easy to create new
        colors to add to this file.  The include command is also useful
        for including objects into your scene.  Combined with the
        transformation commands this will allow you to create objects as
        seperate files and inlcude them into the scene at any location
        and orientation.  You may also inlcude multiple copies of an
        object. 
























                                        16





                                   The Studio
 
             The studio structure in the scene file defines all those
        things that are neither lights, objects or clips.  This includes
        the resolution of the final image, the location of the camera
        (viewpoint), the direction the camera is pointing, the background
        color, and various rendering options.  Some of the options have
        default values.  These are the values these options will take on
        if they are left out of the studio definition.  The studio
        definition looks like this:
        
        studio {
        	from x y z
        	at x y z
        	up x y z
        	angle ang
        	resolution i j
        	start line
        	stop line
        	aspect asp
        	projection mode
        
        	ambient acolor
        	background bcolor
        	haze density
        
        	antialias mode
        	threshold dist
        	jitter
        
        	aperture size
        	focal_length dist
        	samples n
        
        	no_shadows
        	no_exp_trans
        	caustics
        
        	depth max_depth
        	bunching n
        }
        
        "from" is the location of the camera. 

        "at" is where in the scene the camera is pointed. 

        "up" is a vector pointing up, usually 0 0 1.  This can be
                played with to roll the image around the axis of
                the camera. 

        "angle" is the field-of-view angle given in degrees. 


                                    17




        "resolution" is the size of the image in pixels, i pixels
                across and j pixels down.  This can also be
                controlled from the command line using the -i
                switch. 

        "start" and "stop" allow you to start and stop the
                rendering at the specified line numbers.  I use
                this for testing new input files and isolating
                bugs.  Those of you with networks might want to
                consider using this to split up an image for
                rendering on multiple computers.  After the
                sections are done you can then use paste.exe to
                glue them together.  Currently there is a problem
                with using start and the resume (-r) flag.  Avoid
                the combination. 

        "aspect" is the aspect ratio of the screen.  This is the
                ratio of width to height of the screen you are
                rendering your images for.  I've found that my
                Nec 3D has an aspect ratio of about 4/3 and that
                my Amiga 1084 has an aspect ratio of about 1.2. 
                To determine the proper aspect ratio for your
                screen measure the width and height of a screen
                image.  The aspect ratio of your screen can be
                found by dividing the width by the height. 
                Determining the correct aspect ratio of your
                screen will insure that circles come out looking
                like circles instead of ovals.  Remember, aspect
                ratio should the the width/height ratio of the
                displayed image regardless of the image
                resolution.  Together with the resolution these
                are used to determine the aspect ratio of the
                pixels. 

        "projection" controls how the 3d world is mapped onto the
                2d screen.  The default is "flat".  This is the
                standard perspective projection you've all come
                to know and love.  "spherical" projection
                produces an effect somewhat like a fisheye lens. 
                Things can look pretty strange.  Unique to the
                "spherical" mode is the field of view angle can
                be greater than 180 degrees.  Try a 360 degree
                panorama some time.  The "orthographic"
                projection mode produces an image where all the
                eye rays are parallel to each other.  For this
                mode the "angle" parameter has no meaning and is
                replaced with a "width" parameter.  Width defines
                how wide the screen is in the world coordinate
                system.  Generally, I think that this mode is
                useless but it was easy to code so why not? The
                final mode is the "parallax" projection mode. 
                This produces a 2-point projection instead of a
                3-point projection like the "flat" mode.  In the

                                    18




                "parallax" mode, all vertical lines stay vertical
                on the screen.  This was implemented specifically
                for architectural renderings but is sometimes
                useful in other contexts.  Note that "vertical"
                is defined by the direction of the up vector. 

        "ambient" is the color of the light that is everywhere in
                the image.  In "the real world" when light
                strikes diffuse surfaces such as walls, some of
                it is scattered back into the room.  This is why
                you can still see under a desk even though no
                light is shining directly underneath it.  Most
                ray tracers, including Vivid, can't handle this
                diffuse interreflection.  But, all hope is not
                lost.  To fake diffuse interreflection Vivid
                allows you to set an ambient light value.  This
                acts like a light that is shining in every
                direction at once and does not cast any shadows. 
                For an inside scene values of about .2 .2 .2 seem
                to work well.  Outside scenes look a bit more
                realistic with a higher ambient value because of
                the scattering of light the atmosphere does. 
                Most ray traced images that you will see just
                have the ambient value set to 0 0 0 or black. 
                This produces the sharpest contrasts and gives
                the image a super-real effect.  The default value
                for ambient is 0 0 0. 

        "background" is the color that will be returned if no
                objects are hit while tracing a ray.  Popular
                choices are black and sky_blue.  If haze is
                defined then this is the color of the haze.  (see
                below) The background color defaults to black. 
                Alternatively you can do the following:
                
                	background {
                		palette.map
                		up x y z
                	}
                
                 This produces a graduated background using the
                colors in the file palette.map.  The file can
                have any name but is required to have the .map
                extension.  The file is the same format as the
                img2gif palette files.  The first color in the
                file is the color that will appear in the
                direction of the up vector.  If no up vector is
                specified then the up vector from the studio
                structure will be used. 

        "haze" is the density of the fog or haze in the scene. 
                The haze density defaults to 0.  This means that
                there is no haze.  A value of .5 means that for

                                    19




                every unit a ray travels, half of its color is
                determined by the background color.  This
                function is exponential, ie if the haze density
                is given as .5 the color of a ray going 1 unit
                will be .5 times the color of the object it hits
                and .5 times the background color.  A ray going 2
                units will be .25 the color of the object and .75
                times the background color.  For most images this
                parameter can be ignored and the default value of
                0 used. 

        "antialias" determines whether or not antialiasing is
                performed and what type is used.  This can also
                be controlled from the command line using the -a
                switch.  The valid modes are:

            none -- Do one ray per pixel, right through the
                center.  Results are blocky but relatively quick. 
                This is the default. 
            quick -- This does a subsampling approximation of the
                image.  In areas of even color the most speedup
                is gained.  This is the fastest mode but the
                results are not useful for much more than test
                images.  At best (ie on a blank image) this
                should be about 15 times faster than the above
                mode.  In general I notice about a 3-5 times
                speedup.  This is a great mode for doing test
                renderings. 
            corners -- Shoot a ray at each corner of the pixel
                and average the results.  Since the corners are
                shared by adjoining pixels this means about one
                ray per pixel.  The results are almost as quick
                as none but usually have a better look. 
                Effectively this is the same as running a
                smoothing filter over the image. 
            adaptive -- Rays are shot at the corners of the
                pixel.  If they are within a certain threshold of
                each other the program moves on to the next
                pixel.  If they differ by more than the threshold
                value, the pixel is subdivided into four
                subpixels and sampled again.  The corners of the
                subpixels are then compared against the threshold
                and if they are still too far apart the are
                subdivided once more.  The effective result of
                this is that in areas of constant or smoothly
                changing intensity only one ray per pixel is
                shot.  At edges or other sharp color transitions
                up to 25 rays per pixel may be averaged to
                determine the color of the pixel.  The result is
                fairly good antialiasing without too much undo
                overhead. 

        "threshold" is the threshold value used by the adaptive

                                    20




                mode of antialiasing.  The default threshold is
                16.  Valid values are 0..255.  This parameter
                also affects the quick mode.  In general, lower
                values will produce better results but take more
                time. 

        "jitter" is a flag telling the system to add a little bit
                of randomness to the direction each ray is shot. 
                Combined with antialiasing this helps to break up
                the patterns sometimes caused by sampling an
                image on a regular grid.  Images with regular
                patterns such as checkerboards disappearing into
                the horizon will benefit most from jitter. 

        "aperture" is an optional parameter which allows the ray
                tracer to model a more realistic camera.  The
                default aperture is 0 which models a pinhole
                camera.  With an aperture greater than 0 objects
                at the focal length (see below) will appear in
                sharp focus while objects nearer or further from
                the viewpoint will be blurred.  The larger the
                aperture, the more exaggerated the blurring will
                be.  Using this option will greatly increase the
                amount of time needed to generate an image
                because Vivid uses distributed ray tracing to
                model the effects of a camera with a non-zero
                aperture.  This causes the number of rays
                necessary to calculate the color of a pixel to
                increase greatly.  The default is to shoot 8 rays
                instead of one ray whenever aperture is greater
                than zero.  This value can be controlled with the
                "samples" parameter below. 

        "focal_length" determines the distance from the camera to
                the focal plane where objects are rendered in
                focus.  This option is used in conjunction with
                the aperture option.  Objects which are a
                distance equal to the focal length away from the
                camera will be in sharp focus.  The default for
                the focal length is the distance between the
                "from" and "at" points which determine the
                viewpoint and the viewing direction. 

        "samples" controls the number of rays shot when a
                non-zero aperture is used.  The default is 8. 

        "no_shadows" causes all shadow calculations to be turned
                off.  The speed increase gained by turning
                shadows off is especially useful when doing test
                images of a new scene.  The can also be
                controlled using the command line switch -n. 

        "no_exp_trans" is a wonderfully intuitive name for a flag

                                    21




                that turns off the exponential attenuation of the
                rays as they pass through transparent objects. 
                Got that? Let me try again.  Normally when Vivid
                shoots a ray through a transparent object (glass)
                the color of the ray is tinted by the color of
                the glass and is a function of the distance that
                the ray has to travel through the glass.  For
                example if you have two sheets of coke-bottle
                green glass where one is 1/4 inch thick and the
                other is 2 inches thick, light passing through
                the thicker one will be darker.  The relationship
                between the thickness and the amount of tinting
                is exponential.  This causes problems with single
                sided glass because when Vivid tries to compute
                the thickness of the glass the distance
                calculated is from the glass to whatever wall or
                floor the ray hits next.  Hence the windows will
                tend to be way dark.  When you set the
                no_exp_trans flag in the studio structure Vivid
                only uses the transparent color of the surface to
                calculate the tint and totally ignores the
                distance that the ray travels.  This tinting also
                affects shadow rays. 

        "caustics" is an experimental flag which turns on Vivid's
                faked caustics.  Caustics are those neat patterns
                of light that are produced as light passes
                through a transparent object.  I've been playing
                around with a couple of ways to get some of the
                effect without having to spend a few days per
                image doing the real thing.  The effect is pretty
                subtle but does seem to make some images look
                better.  Joe Bob says check it out. 

        "depth" lets you limit the maximum recursion level to
                which rays will be traced.  At a depth of 1 only
                eye rays are traced.  A depth of 2 will trace 1st
                level reflections and refractions.  The maximum
                value allowed is 20.  This is also the default
                value.  This can also be changed using the
                command line switch -d. 

        "bunching" allows you to control the branching factor of
                the tree created by the bounding boxes.  I'm not
                really sure what an optimal value is but the
                default value of 4 seems to work well for most
                cases.  At any rate, values less than two are
                guaranteed to cause grief.  Higher values will
                cause the bounding box tree to branch more at
                each level and therefore be shallower.  Lower
                values will do the opposite.  I find that
                experimenting with takes more time than I ever
                save so the only time I use it is when I am close

                                    22




                to running out of memory.  Using a higher value
                like 8 or 12 will create fewer composite
                (bounding box) nodes in the tree and save soom
                memory.  Feel free not to ignore it without fear
                of missing out on something. 

















































                                        23





                                     Lights

 
             Lights come in four flavors, point, directional, spherical
        and spot.  Just as the name implies a point light is a light
        source occupying a single point in space.  It has position,
        color, and attributes determining how much the intensity of the
        light falls off with distance.  A directional light acts like a
        point light source infinitely far away with no reduction in
        intensity over distance.  A spherical light source actually has a
        radius to it and can provide shadows with penumbra (soft edges). 
        This feature, however, adds a considerable amount to the time
        needed to render the image.  Spot lights produce a cone of light
        that falls off on the edges.  These are quite nice for
        highlighting areas of your model.  In most cases they also
        produce the least number of shadow rays making them quicker than
        just putting a point light inside a cone. 
 
             The definition for a point light source looks like this:
        
        light {
        	type point
        	falloff f            // defaults to 0
        	position x y z
        	color r g b
        }
        
 
             The falloff parameter determines how the intensity of the
        light is reduced over distance(dist).  In the real world the
        light intensity falls off as 1/(dist*dist) (f=2).  Vivid also
        allows the light to fall off as 1/dist (f=1) and not to fall off
        at all (f=0).  Why would you want to use anything except f=2?
        Simplicity is one reason.  With f=0 you can set the light's color
        to 1 1 1 and know that whatever objects the light falls on will
        be illuminated fully regardless of the distance of the light from
        the object.  With f=2 you must take into account this distance. 
        If the object you wish to be illuminated is 3 units away from the
        light then in order to get the same amount of illumination that
        f=0 provides you must set the color to 9 9 9 ie 3^2.  For f=1 the
        color would have to be 3 3 3.  In the real world much of the
        light around us does not come directly from the light source.  It
        often bounces off of other objects on its way to the object we
        are interested in.  Since Vivid, like most ray tracers, does not
        model this interobject diffuse reflection we can achieve much the
        same effect by have the light intensity fall off linearly with
        distance, ie f=1.  The default value is f=0. 
 
             The definition for a directional light source looks like:
        
        light {
        	type directional

                                        24




        	color r g b
        	direction dx dy dz
        }
        
        or the direction can be replaced by a from and at pair:
        
        light {
        	type directional
        	color r g b
        	from x y z
        	at x y z
        }
        
        
 
             The direction vector points along the direction the light is
        travelling.  Since the light is assumed to be at infinity, there
        is no falloff parameter.  If you are having difficulty
        understanding how the direction parameter works is is sometimes
        useful to note that direction x y z is the same as center 0 0 0
        at x y z. 
 
             The definition for a spherical light source looks like:
        
        light {
        	type spherical
        	position x y z
        	radius r
        	color r g b
        	falloff f
        	samples n
        }
        
 
             Spherical lights differ from point lights in that the
        shadows they cast have penumbra.  Normally when a ray hits a
        surface a shadow ray is shot toward each light.  If the shadow
        ray hits any surface on the way to the light then that light is
        blocked and the surface is in the shadow of the blocking object. 
        With spherical light sources multiple shadow rays are shot.  Each
        one is shot to a random point within the radius of the light.  If
        the light is half blocked by an object, approximately half the
        shadow rays will be blocked and half will pass through to the
        light.  The ratio of blocked to not-blocked shadow rays is then
        used to determine how strong the shadow is.  As you might expect,
        the extra shadow rays will add a lot of extra time to the
        rendering.  Some references refer to these light sources as
        extended light sources.  The number of shadow rays shot each time
        is controlled by the samples parameter.  The default value for
        this is 16. 
 
             The definition for a spot light source looks like:
        

                                        25




        light {
        	type spot
        	position x y z
        	direction dx dy dz
        	min_angle angle1
        	max_angle angle2
        	color r g b
        	falloff f
        }
        
 
             Like the directional light, the direction parameter may be
        replaced with the at x y z to specify where the light is shining. 
        Min_angle and max_angle define the shape of the cone of light
        produced by the spot light.  Everything within the min_angle
        angle of the axis of the light will be fully illuminated.  From
        there the light intensity will fall off until max_angle is
        reached.  For example if you want a cone of light 30 degrees wide
        with sharp edges you would define min_angle and max_angle to be
        30.  To get the same size light but one that fades out at the
        edges you would define max_angle to be 30 and min_angle to be 0. 
 
             Each light source can also have a couple of other
        parameters.  They are no_shadows and no_spec.  As you've probably
        guessed, these allow you to turn off shadows and specular
        highlights for each light.  Used together with a directional
        light source of low intensity (.2 .2 .2) this is often a nice
        alternative to global ambient light.  Global ambient light tends
        to make objects appear flat whereas this technique will provide
        subtle shading without the shadows and spots of your "real" light
        sources. 
 
             One thing to note is that even if a light is within the
        viewing scene it will not appear as an object.  If you want you
        lights to be visible you can wrap a transparent shell around them
        using a sphere.  Example:
        
        //      Define a point light at 2 3 4 that shows up in the scene
        //      as a light with radius 1.
        
        light {
        	center 2 3 4
        	type point
        	color white
        }
        
        //      glass shell
        
        surface {
        	ambient white        // same color as the light
        	transparent white    // totally transparent
        }
        sphere {

                                        26




        	center 2 3 4
        	radius 1
        }
        
        For details on spheres and surfaces skip ahead. 

















































                                        27





                                    Surfaces

 
             Surface structures allow you to define the surface
        characteristics of the objects you are rendering such as color,
        reflectivity and texture.  When a surface is defined in the input
        file, it is applied to all the primitives following it until a
        new surface is defined.  This allows multiple objects to be
        entered without having to repeat the surface characteristics.  A
        simple surface structure looks like this:
        
        surface {
        	diffuse r g b        // defaults to 0 0 0 (black)
        	ambient r g b        // defaults to 0 0 0
        	specular r g b       // defaults to 0 0 0
        	shine pow            // defaults to 0
        	transparent r g b    // defaults to 0 0 0
        	ior num              // defaults to 1.0
        	fuzz magnitude       // defaults to 0.0
        	no_antialias         // turn off antialiasing
        }
        
 
             All of these components of the surface are figured in when
        the ray tracer determines the color of an object in the scene. 
        The diffuse color is the actual color of the object as seen when
        illuminated by a full white light.  A value of 0 0 0 signifies a
        black object while a value of 1 1 1 indicates white.  The
        brightness of this component depends on the amount of light
        falling on the surface at that point.  The ambient term is
        sometimes also referred to as the self-luminous component.  This
        is the color the object will appear in a totally dark scene.  The
        specular component specifies the reflectivity of the surface.  A
        value of 1 1 1 will produce a mirror-like reflection.  The shine
        value determines how large the specular spot will appear on a
        surface.  Low values, 1..10, will produce large, soft-edged
        specular highlights while high values, 1000 or more, will produce
        a small, sharp spot.  Traditionally the brightness and color of
        the spot is in direct proportion to the specular component.  The
        problem is that sometimes it would be nice to have a blue object
        with specular highlights without having the extra overhead of
        tracing reflected rays.  Therefore Vivid allows a second form for
        defining specular spots:
        
        	shine pow r g b
        
 
             In this case the color given will be used instead of the
        specular component of the surface.  The transparent component
        allows you to define how transparent the surface is.  A value of
        1 1 1 will appear glass-like because it allows all colors to pass
        through while a value of 1 0 0 will produce a surface like red

                                        28




        glass since it only allows red light to pass through.  A surface
        with a transparent component of .9 .9 .9 will appear partially
        transparent with the amount of light passed through based on the
        thickness of the object the light is passing through.  The index
        of refraction, ior, determines how much the ray is bent as it
        passes into the transparent surface.  In reality this is related
        to the relative density of the surface.  To simulate glass values
        of about 1.1 to 1.3 seem to work best.  The ior of diamond is
        2.6.  Fuzz is a way of adding random noise to the surface normal
        of the object when its color is determined.  Since the diffuse
        color of the object is affected by the angle the light hits the
        surface this randomization can produce a sort of coarse texuture
        to an object.  Applied to mirrored or transparent surfaces this
        produces an affect much like frosted glass.  Generally, small
        values of fuzz, .01 to .3, seem to work best. 
 
             The no_antialias flag tells the adaptive antialiasing to
        effectively turn off for that surface.  In general this is not
        something that you want to do except in a few special cases.  The
        original reason for this parameter was that fuzzy surfaces can
        cause the adaptive antialias option to shoot lots of rays and
        slow down the image generation considerably.  By adding the
        no_antialias flag to the surface definition you still get the
        benefits of the adaptive antialiasing along the edges of the
        objects but you avoid the slowdown that can be caused by any
        large, fuzzy surfaces.  Note, however, that this will change the
        look of the surface.  Try cutting the amount of fuzz in half when
        using this option to preserve the amount of color variation in
        the surface. 
 
             As an aid to those of us that can't type, some keywords may
        be abbreviated: surf, diff, amb, spec and trans.  I trust that
        you'll be able to figure out what goes with what. 
 
             Some examples are probably in order. 
        
        //	simple red surface
        surface {
        	diff 1 0 0
        }
        
        //	self-luminous blue
        surface {
        	ambient 0 0 1
        }
        
        //      mirror with specular highlights
        surface {
        	spec 1 1 1
        	shine 100
        }
        
        //      glass with some reflection

                                        29




        surface {
        	spec .3 .3 .3
        	shine 30
        	trans .7 .7 .7
        	ior 1.2
        }
        
 
             In general, the rule of thumb is that amb+diff+spec+trans
        should be less than or equal to 1 1 1.  Of course since we are
        defining our own universe anything is possible. 











































                                        30





                                  Bump Mapping
 
             Bump mapping is a means of giving a surface some texture
        which enhances the realism of the surface by adding ripples or
        bumps to the surface.  The surface isn't actually distorted but
        its normal is.  This allows a simple surface to appear very
        complicated.  Bump definitions are included inside of the simple
        surface definitions, ie:
        
        surface {
        	diffuse red
        	bump {
        		...
        	}
        }
        
        A sample wave bump map looks like this:
        
        bump {
        	wave {
        		center 1 2 3
        		wavelength 2.0
        		amplitude 0.2
        		damping 0.9          // defaults to 1.0
        		phase 0.0            // defaults to 0.0
        	}
        }
        
 
             Center defines the source of the wave.  Wavelength defines
        the crest to crest distance of the wave.  Amplitude defines the
        maximum amount that the surface normal is bumped.  Values under 1
        are definitely best.  The damping parameter defines how much the
        amplitude falls with distance.  In the example given the
        amplitude will decrease by 10% for each wavelength of distance
        from the source.  The phase is a number between 0 and 1 which
        defines a starting offset for the phase of the wave.  This can be
        used in animations to create a wave which appears to move
        realistically by incrementing the phase by a small amount for
        each frame.  More than one wave may be defined within the bump
        structure.  By defining three or four wave sources at various
        locations with differing wavelengths and amplitudes a very
        realistic rippled surface can be created. 










                                        31




 
             Turbulence can also be used to perturb the normal of a
        surface.  The definition of turbulence looks like this:
        
        bump {
        	turbulence {
        		scale 1 1 1
        		offset 0 0 0
        		amplitude .5
        		terms 4
        	}
        }
        
 
             The turbulence function takes the location of the ray
        intersection and returns a random number in the range +-
        amplitude.  The scale and offset factors are applied to the xyz
        location before the turbulence function is called.  The terms
        parameter allows you to build a fractal-like surface.  When
        terms>1 the turbulence function is summed multiple times.  Each
        successive term in the sum has its scaling doubled and the
        amplitude halved.  This produces the varying levels of
        self-similarity associated with fractals.  The sample file
        vivid1.v uses this feature and a non-symmetric scaling to produce
        the "spun-chrome" look on the large sphere.  Turbulence and wave
        definitions may be included with each other inside a bump
        definition. 



























                                        32





                                Textured Surfaces

 
             Vivid also allows the use of solid texturing to enhance the
        realism of the surfaces rendered.  Textured surfaces are really
        just two surfaces with some definition of which appears where on
        the object and how the two surfaces are blended together.  The
        surfaces can be "layered" in one of three patterns checker,
        spherical or noise.  The checker pattern produces a 3-d checker. 
        The size of the blocks is controlled by the scale factor.  If one
        of the scale parameters is 0 then the pattern is assumed not to
        change along that axis.  An example would be a simple
        checkerboard pattern with checkers 2 units on a side colored
        black and white.  This pattern is defined to extend infinitely
        along the z axis. 
        
        surface {
        	texture {
        		pattern checker
        		scale 2 2 0
        		offset 0 0 0                 // default
        		fuzz 0                       // default
        		blend 0                      // default
        		surface { diff black }
        		surface { diff white }
        	}
        }
        
 
             A scale of 2 0 0 would create a pattern which changes every
        2 units in the x direction but is continuous in the y and z
        directions.  This is equivalent to 2-unit thick slabs of material
        stacked along the x axis.  The spherical pattern produces
        concentric layers of alternating surfaces.  When one of the scale
        parameters is 0 concentric cylinders are formed with the axis of
        the cylinders along the zero'ed axis.  This is useful for wood
        textures.  The spherical pattern also requires 2 radius
        definitions for the layers.  The first radius is used for the
        first surface, etc. 
        
        surface {
        	texture {
        		pattern spherical
        		scale 2 2 0
        		radius 1
        		radius 2
        		surface { diff black }
        		surface { diff white }
        	}
        }
        


                                        33




 
             The noise pattern uses the output of the noise function
        directly to pick between the two surfaces.  This is useful for
        producing textures like granite.  By using unequal scaling values
        in the x y and z directions you can get a streaked looking
        surface.  I've also used this using tan and brown surfaces to
        produce a fine wood-grain look. 
        
        surface {
        	texture {
        		pattern noise
        		terms 4
        		scale x y z
        		surface { diff white }
        		surface { diff black }
        	}
        }
        
 
             The fuzz and blend parameters may be used to soften the
        edges between the two surfaces.  Their values range from 0 to 1. 
        The blend parameter produces a smooth transition between the
        surfaces.  The value of the blend parameter determines the width
        of this transition area.  The fuzz parameter adds noise to the
        point being checked in proportion to its value.  This produces a
        coarse, speckled transition between the surfaces. 
 
             The turbulence function mention in the bump map section may
        also be applied to textured surfaces.  By varying the parameters
        the effect can be made to range from a slight perturbation of the
        pattern, to a marble look, to excessive turbulence.  A simple
        example is presented below. 
 
             Due to the way Vivid's parser works if you want to bump map
        a surface which is also textured the bump definition must appear
        in the surface structure before the texture definition.  Also
        notice that the surfaces defined in a texture definition need not
        be simple surfaces.  They may also be textured.  The following is
        a definition for a checkerboard surface with checks 10 units on a
        side.  Half the checks are black while the other half have a
        red/white marble finish. 
        
        surface {
        	texture {
        		pattern checker
        		scale 10 10 0
        		surface { diff black }
        		surface {
        			texture {
        				pattern checker
        				scale 1 0 0
        				blend 0.7
        				turbulence {

                                        34




        					amplitude 3
        					terms 4
        				}
        				surface { diff white }
        				surface { diff red }
        			}
        		}
        	}
        }
        












































                                        35




 
             Vivid also allows a Mandelbrot pattern as demonstrated in
        the sample input file vivid1.v.  The Mandelbrot pattern was put
        into Vivid as a joke one evening.  Currently the format for
        specifying it is terrible.  The first two parameters of the scale
        value determine the x y scaling of the set while the 3rd
        parameter determines the maximum number of iterations.  The
        result of the iteration calculation is then scaled by the max
        number of iterations to determine the relative percentages of the
        surface parameters for that point. 
 
             OK, the way it works is like this.  The actual point of
        intersection, x y z, is tranlated using the scale and offset
        values before being put into the Mandelbrot calculation. 
 
             new_x = x * scale_x + offset
 
             Like I said, this is about a backwards as I could make it
        and still have it work.  Since the point is multiplied by the
        scale rather than divided the pattern gets bigger as the scale
        value gets smaller.  Normally the Mandelbrot set extends from -2
        to +1 along the x axis (more or less).  If you want to get it to
        fit from -20 to +10 you would have to scale it by 0.1 in the x
        and y axes.  Stupid? Yes.  Now, since the offset is added on
        after the multiplication that makes it work in the Mandelbrot
        coordinate system rather than the world coordinate system. 
        Continuing the example above, if you wanted to move the center of
        the set to world coordinates 300, 100 you would have to give an
        offset of 30 10. 
 
             Using macros I think you can alleviate most of this garbage. 
        	#define ITERATION_LIMIT         (64)
        	#define SCALE                   (10)
        	#define X_OFFSET                (300)
        	#define Y_OFFSET                (100)
        
        	surf {
        		texture {
        			pattern mandelbrot
        			scale (1/SCALE) (1/SCALE) ITERATION_LIMIT
        			offset (X_OFFSET/SCALE) (Y_OFFSET/SCALE) 0
        	      //  etc...
        
        			}
        
 
             Now all you have to do is change the defines and things will
        work much more like you expect. 
 
             Once I figure out a reasonable way of doing this Mandelbrot
        and Julia sets will become a real part of Vivid.  (Yeah, I know I
        said that last time but it's still true.)


                                        36





                                     Sphere
 
             The sphere is the simplest of the primitives supported by
        Vivid and generally the fastest to perform an intersection test
        with.  The format for a sphere is:
        
        sphere {
        	center x y z
        	radius r
        }
        
        where x y z is the location in space for the center of the sphere
        and r is the sphere's radius.  As an example here is the
        definition for two glass spheres, one which is hollow and one
        which is solid. 
        
        //	glass surface
        
        surface { trans 1 1 1 shine 200 1 1 1 ior 1.2 }
        
        //      solid globe
        
        sphere { center 1 0 0 radius .9 }
        
        //      hollow globe
        
        sphere { center -1 0 0 radius .9 }      // outer surface
        sphere { center -1 0 0 radius .8 }     // inner surface
        
 
             Just for laughs vivid also includes a fuzzy spheres option. 
        These spheres appear fuzzy because they have no fixed radius.  To
        define a fuzzy sphere define a normal sphere and add a fuzz
        parameter.  This defines how much larger the radius will randomly
        be.  Each time the ray tracer performs an intersection test with
        the fuzzy sphere, the radius to test against is randomly chosen
        to lie between the radius and radius+fuzz. 
        
        //      fuzzy sphere with radius between 0.5 and 2
        sphere {
        	center 0 1 2
        	radius .5
        	fuzz 1.5
        }
        
        







                                        37





                                      Ring
 
             The ring primitive may also be described as a washer or
        disk.  The definition for a ring consists of a location, a
        surface normal, and a minimum and maximum radius.  The minimum
        radius may be zero producing a disk without a center hole. 
        Because the intersection for the ring is faster than for a
        polygon the ring is a good choice for use as a ground plane
        underneath the objects you are ray tracing.  The format for the
        ring definition is:
        
        ring {
        	center x y z
        	normal a b c
        	min_radius r0
        	max_radius r1
        }
        
 
             The surface normal a b c does not have to be normalized.  If
        you just want a disk without a center hole the min/max radius
        definitions may be replaced with a single radius definition as
        follows. 
        
        ring {
        	center x y z
        	normal a b c
        	radius r
        }
        
        
 
             Whoa, just got a clue that not everyone knows what a surface
        normal is.  A surface normal is a vector that is perpendicular to
        a surface, ie one that points straight out from the surface.  For
        example, the surface normal for the floor in you room would be a
        vector pointing straight up into the air.  The surface normal of
        your monitor is the vector pointing straight out between you
        eyes.  Simple enough? Ok, now a normalized vector is one which
        has been scaled to have its length equal exactly 1.  This is
        usually done by calculating the length of the vector then
        dividing each of the vector's components by the length.  Vectors
        of length 0 cause no end of problems. 










                                        38





                                     Polygon
 
             Polygons may have any number of vertices (well, a minimum of
        three is required).  The vertices must all lie within the same
        plane otherwise the results will be strange.  The order of the
        vertices may be either clockwise or counter clockwise. 
        
        polygon {
        	points 4
        	vertex  1  1 0
        	vertex  1 -1 0
        	vertex -1 -1 0
        	vertex -1  1 0
        }
        

 
             This will produce a square polygon 2 units on a side
        centered at the origin with a surface normal equal to 0 0 1. 


































                                        39





                                Triangular Patch
 
             The triangular patch is useful for building objects with
        complex shapes that you want to appear smooth.  The patch is
        defined by three vertices and explicit surface normals for each
        vertex.  In general, manually entering in patches will probably
        be too tedious to be of much use but when using computer
        generated input files the results will be worth the extra
        programming effort. 
        
        patch {
        	vertex 1 0 0 normal .1 0 1
        	vertex 0 1 1 normal 0 .1 1
        	vertex 0 0 .5 normal -.1 -.1 1
        }
        





































                                        40





                                      Cone
 
             The cones implemented by Vivid are actually truncated cones. 
        They have a radius both at their base and at their apex.  When
        these radii are equal the cone does a fair imitation of a
        cylinder.  To get a pointed cone enter 0 for one of the radii. 
        
        cone {
        	base 1 1 1 base_radius 4
        	apex 0 0 5 apex_radius 1
        }
        
 
             Rings are useful for putting caps on the ends of cones. 
        Even for a cone at an odd angle the position and normal of the
        ring can be easily calculated.  To cap the apex end of the cone
        the ring's center is equal to the apex, the ring's radius is
        equal to the apex_radius and the ring's normal is equal to
        apex-base.  Using the example above the definition for a ring to
        cap the apex end of the cone would look like this:
        
        ring {
        	center 0 0 5
        	radius 1
        	normal -1 -1 4
        }
        


























                                        41





                                 Transformations

 
             Vivid's transformation commands allow you to move and scale
        objects.  Transformation commands apply to all the primitives
        following them until they are "popped" from the transformation
        stack.  The format for a transformation command is:
        
        transform {
        	scale           s
        	rotate          x y z
        	translate       dx dy dz
        }
        
 
             Scale changes the size of the objects.  Scale may also be
        defined as a vector to create objects that are scaled differently
        in each axis.  Unfortunately this doesn't work with all
        primitives, only polygons and patches can be scaled
        non-uniformally.  The rotate command rotates the object the given
        number of degrees around each axis.  The translate command moves
        the object.  Any of these may be left out or used more than once. 
        They can also be used in any order and will be applied to the
        objects in the order that they are given.  It is very important
        that you get the order correct.  An object that is rotated 90
        degrees around the Z axis and translated 10 units along the X
        axis will end up at 10 0 0 with a 90 degree twist whereas if the
        operations are applied in the other order the object will end up
        at 0 10 0.  Sometimes it helps to play around with real objects a
        bit and work through some of the transformations first.  Remember
        that all rotations are done around the axes, not necessarily
        around the center of the object.  This should also be kept in
        mind when building new objects.  Put 0 0 0 at the objects
        "natural" center of rotation.  This will help greatly when
        building scenes with the objects.  For example, the natural
        "center" for a car model would be at ground level in the center
        of the car.  This allows the car to fairly easily be placed in
        the scene where you want it. 
 
             To remove a transformation from the transform stack use the
        "transform_pop" command.  Sometimes you will want to nest
        transform commands.  This is useful for creating multi-part
        objects that move relative to each other but also need to move as
        a whole unit.  For example, say you want to create a tank model
        with a turret that you can rotate.  Assume that the body of your
        tank model is in the file tank.vo and the turret is in turret.vo. 
        To place the tank in your scene, your input file would look like
        this:
        
        #define TURRET_ANGLE    (30)    // rotation for turret
        
        transform { translate x y z }   // move whole tank

                                        42




        #include tank.vo                // include body geometry
        transform { rotate 0 0 TURRET_ANGLE }
        #include turret.vo              // include turret geometry
        
        transform_pop           // clean up transform stack
        transform_pop
        
 
             Using this technique complicated models can be built and
        positioned with relative ease.  There is currently one major
        drawback to using transformations, surface textures don't move
        with the object.  This isn't too big a deal for single frame
        images but will make animating textured objects look very poor. 
        Yes, I'm working on it. 








































                                        43





                                    Clipping

 
             Primitives can also be "clipped" to produce more complicated
        shapes.  Basically the way a clip works is that a primitive is
        defined with a clipping surface which cuts off part of that
        primitive.  For example a sphere can be clipped against a plane
        to produce a hemisphere or a cone can be used to clip a hole
        through another cone.  There are three types of clipping surface:
        planes, spheres and cones.  Clips are defined within a
        primitive's definiton.  You may have more than one clip per
        primitive.  Clips also transform along with their primitives. 
 
             A clipping plane is defined by a point and a normal. 
        	clip {
        		center x y z
        		normal x y z
        	}
        
 
             The part of the primitive on the normal side of the plane
        will be kept while the part on the other side will disappear into
        the Ronald Reagan Memorial Library.  (You may think I'm lying but
        you'll never really _know_ until you go check.) For example, if
        you want to get a hemipshere of radius 1 centered at the origin
        if would look like:
        	sphere {
        		center 0 0 0 radius 1
        		clip {
        			center 0 0 0 normal 0 0 1
        		}
        	}
        
 
             Note that the clip's normal is pointing upward.  This will
        give you the top half of the sphere.  If you change the normal to
        0 0 -1 you will get the bottom half. 
 
             Clipping spheres are defined as:
        	clip {
        		center x y z
        		radius r
        		inside or outside
        	}
        
 
             With a clipping sphere you can choose to either keep the
        part of the primitive inside of the sphere or the part of the
        primitive outside of the sphere.  You may have already guessed
        this but that's why the inside and outside keywords are there. 
 
             Clipping cones look like:

                                        44




        	clip {
        		apex x y z      apex_radius r
        		base x y z      base_radius r
        		inside or outside
        	}
        
 
             Just like the cone primitive you may also just define a
        single radius to get a cylinder. 

                                        
 
             Sometimes you will want to apply the same clips to a group
        of primitives.  To do this define global clips using the
        global_clip keyword:
        	global_clip {
        		clip { ... }
        		clip { ... }
        		clip { ... }
        	}
        
 
             The clip_pop keyword will cause the previous section of
        clips to be popped off the stack much like the transform_pop does
        for transformations. 





























                                        45





                                Support Programs

                                   img2gif.exe
 
             Once vivid has completed an image you need some way to view
        the results.  That's where img2gif comes in.  Img2gif is used to
        convert the raw img file that Vivid outputs into a gif file.  The
        resulting gif file can then be viewed using your favorite view
        program.  My favorite is Brad Montgomery's vpic.  Look for it on
        you local BBS.  In a pinch, even fractint can be used to view
        gifs. 
 
             When running img2gif you have 2 main decisions to make: a)
        how should the program pick the palette and b) should the program
        do any dithering of the output.  Picking the palette is not
        always an easy problem.  Standard VGA allows us to view only 256
        of the available 262,144 colors.  An "average" lores image will
        have about 7000 colors which we need to represent with our
        palette of 256.  A higher resolution image my have tens of
        thousands of colors to represent.  The following algorithms are
        currently implemented in img2gif. 
 
             Palette File -- A palette may be input via a .map file. 
        This uses the same format as .map files created/read by fractint. 
        This option is useful for creating multiple gifs with the same
        palette for animation. 
 
             Popularity -- The popularity algorithm chooses the palette
        by picking the 256 colors which represent then greatest number of
        pixels in the image.  The remaining colors in the image are
        mapped onto the palette using a minimum distance formula.  The
        popularity algorithm tends to work best on images with a lower
        number of colors.  One typical problem of the algorithm is that
        small highlights may not be colored correctly.  Highlights
        generally only cover a few pixels so their color usually doesn't
        have enough representation in the image to be chosen by the
        popularity algorithm.  To help alleviate this problem, img2gif
        forces the corners of the color cube (white, red, green, blue,
        cyan, magenta, yellow, and black) to be selected as the first
        eight palette entries.  Since most highlights are white this
        greatly helps reduce unwanted artifacts in the resulting image. 
 
             Median Cut -- The median cut algorithm tries to choose a
        more well balanced set of colors to represent the image.  The
        general idea of the median cut is to choose a palette in which
        each entry represents about the same number of pixels in the
        image.  This helps to correctly color highlights that a pure
        popularity algorithm might miss.  Img2gif also allows you to
        limit the number of pixels represented by any one color.  This,
        in effect, increases the importance of the colors in highlights
        and other small regions of the image.  With this limit set to
        one, every color in the image is given the same weight without

                                        46




        regard for the number of pixels it covers. 
 
             Fixed Palette -- The fixed palette option uses a
        predetermined palette instead of choosing one based on the
        content of the image.  This has the advantage of being much
        faster.  When choosing by popularity or median cut img2gif must
        first build a tree structure in memory containing every color in
        the image and a count of the number of pixels represented by that
        color.  After choosing the palette the colors in the tree must
        then be mapped onto the colors in the palette.  This can slow
        img2gif down quite a bit.  When using a fixed palette the image
        colors are mapped directly onto the palette colors via simple
        equations eliminating the need for the tree structure and the
        costly remapping of the images colors to an arbitrary palette. 
        Also, the current version of img2gif can only support a tree
        containing about 57,000 colors.  After this my clone runs out of
        RAM.  The fixed palettes supported by img2gif are:
 
             0 : A grey scale image using 256 grey scale tones.  Due to
        VGA limitations this will display as 64 shades on most PC
        systems. 
 
             1 : Divides the color cube into 8 shades of red, 8 shades of
        green, and 4 shades of blue.  Generally produces fairly bad
        images but kept in for nostalgia.  Blue was chosen to get the
        lower resolution because in general the human eye is much less
        sensitive in the blue range and has a harder time focusing on
        edges therefore the loss of color resolution is not missed as
        much. 
 
             2 : Divides the color cube into 6 shades of red, 7 shades of
        green, and 6 shades of blue.  This option gives the best balance
        of speed vs good color representation.  I've found that it works
        best with images that have a large number of colors.  The
        addition of dithering is usually helpful. 
 
             Dithering is the process of displaying pixels of differing
        colors next to each other in such a way as to produce the
        illusion of more colors.  An every day example of this is your
        television.  Stick your nose up to the picture tube and notice
        that the screen is made up of tiny red, green, and blue dots
        which vary in intensity.  These are the only colors your TV
        actually produces but your eye combines them to produce the rest
        of the spectrum.  Well, at least the spectrum according to NTSC. 
 
             Floyd Steinberg dithering is the original error diffusion
        dithering algorithm.  Error diffusion dithering attempts to
        compensate for a limited palette by insuring that the sum of the
        errors in any region of the image is zero even though the colors
        at each individual pixel may contain some error.  At each pixel
        as img2gif scans through the image the nearest color for that
        pixel is chosen.  Generally this color will not be exact.  The
        difference between the chosen palette color and the true color is

                                        47




        then added to the neighboring pixels which have not been scanned
        yet.  Floyd Steinberg dithering has the advantage of having a
        "random" look to it.  Generally, it does not produce noticeable
        patterns in the output image. 
 
             Ordered dithering works by adding a fixed amount to each
        pixel based on its location.  The sum of these additions over a
        region of the image is equal to zero.  Since ordered dither does
        not take into account the values of neighboring pixels it
        produces fixed patterns in the images which may be distracting in
        some cases.  Ordered dithering combined with a fixed palette has
        an advantage if you are using Vivid to produce single fames for
        an animation.  During an animation the background (non-moving)
        regions of the image will stay constant whereas if you use Floyd
        Steinberg dithering the patterns constantly shift around and
        below any moving objects on the screen. 
 
             The random noise option allows you to add white noise to an
        image.  In some cases this may help as much as dithering.  It can
        also be used in conjunction with either of the dithering options. 
        Interesting effects may be obtained by increasing the range of
        the noise.  Images converted with a large amount of noise tend to
        take on a distinctly grainy look.  Interesting, but not overly
        useful.  The default range for the noise is +-8 on a 0..255
        range.  This value was chosen strictly because it seemed to look
        good in most cases.  Random noise has the advantage of being
        constant from image to image.  This means that smooth areas in a
        series of images will not shimmer during animation. 
 
             Ok, fine, now how do I run img2gif? Well, it goes like this:
 
             img2gif [-m #] [-f #] [-p palfile] [-d] [-o] [-r [#]] file
 
             The default palette choosing algorithm is the popularity
        method. 
 
             [-m #] chooses median cut and limits each color to represent
        at most # pixels.  # defaults to 64K. 
 
             [-f #] chooses fixed palette #.  # defaults to 0, grey
        scale. 
 
             [-p palfile] reads the palette out of the file palfile.map. 
        If this file does not exist the palette will be chosen by median
        cut, popularity, or fixed depending on what other flags are set. 
        After the palette is chosen it will then be written to the file
        palfile.map. 
 
             [-d] chooses Floyd Steinberg dithering. 
 
             [-o] chooses ordered dithering. 
 
             [-r #] chooses random noise +- #.  # defaults to 8. 

                                        48




 
             For example:
 
             img2gif -f 2 -d test
 
             will convert test.img to test.gif using fixed palette 2 and
        Floyd Steinberg dithering. 
 
             Assuming that test.map does not exist
        
        img2gif -m -p test test1
        img2gif -m -p test test2
        img2gif -m -p test test3
        img2gif -m -p test test4
        
        will convert test1 using median cut to choose the palette.  The
        palette will then be saved to test.map.  Test2, test3, and test4
        will then be converted using the palette in test.map. 
 
             In general the best results will be obtained by using the -m
        -d flags as in img2gif -m -d test.  For images that tend to be
        fairly monochromatic I've found that -m -d -r 4 works well. 
        Adding the small amount of random noise helps break up some of
        the banding.  On the down side it also adds to the .gif file size
        since it is tough to compress random noise well.  To get nice
        looking grey scale images try -f 0 -r. 




























                                        49





                                    paste.exe
 
             The paste tool will allow you to join together two images in
        raw file format either vertically (one over the other) or
        horizontally (side by side), ie.  two 320x200 images may be
        joined together to form a 320x400 image or a 640x200 image.  In
        order for two images to be joined vertically the images must have
        the same width.  In order for them to be joined horizontally they
        must have the same height. 
 
             The calling sequence for paste is:
 
             paste [-h | -v] in_file1.img in_file2.img out_file.img
 
             In the horizontal case in_file1.img will appear to the right
        of in_file2.img.  In the vertical case in_file1.img will appear
        above in_file2.img. 




































                                        50





                                     up.exe
 
             Up allows you to double an image's size vertically,
        horizontally, or in both directions.  The increase in size is
        done by pixel duplication, no interpolation is used.  The calling
        sequence is:
 
             up [-h | -v] in_file.img out_file.img
 
             If no flag is given, up increases the image's size in both
        directions. 
 
             For example if test.img is a 320x200 image
 
             up -v test.img test2.img
 
             will create test2.img with a resolution of 320x400. 




































                                        51





                                    down.exe
 
             Down does the opposite of up.  (surprise!) When reducing an
        image's size, down averages the appropriate pixels to produce the
        new pixel.  The calling sequence is:
 
             down [-h | -v] infile.img outfile.img
 
             If no flag is given, down reduces the image in both
        directions. 
 
             For example if test is a 320x200 image
 
             down test.img test2.img
 
             will produce test2.img with a resolution of 160x100. 





































                                        52





                                  File Formats

 
             The information included here about the file formats is to
        aid people in writing their own image manipulation utilities
        compatible with the Vivid formats.  I encourage you to experiment
        and share any interesting results with the rest of us. 
 
             img -- This is the format of the files output by Vivid.  The
        images are stored 24-bits per pixel with a simple run length
        encoding scheme to help keep the size down.  The run length
        encoding works by replacing a repetitive string of the same color
        with a count value and that color written only once.  "Runs" of
        the same color are not allowed to continue beyond the end of the
        scanline to make working a scanline at a time easier.  The format
        consists of a 10 byte header followed by the image data.  The
        16-bit numbers in the header are stored most significant byte
        first.  This format is compatible with that used by Alias
        Research.  (I think.)
        
        <2-bytes>	x size of image
        <2-bytes>	y size of image
        <2-bytes>	first scanline, usually 0
        <2-bytes>	last scanline, usually y size - 1
        <2-bytes>	number of bitplanes, always 24
        <image data>
        
        The image data format looks like:
        
        <1-byte>	a repeat count for the following color
        <1-byte>	blue, 0..225
        <1-byte>	green, 0..255
        <1-byte>	red, 0..255
        
        This is repeated as many times as necessary to complete the
        image.  Note: runs do not wrap from one scan line to the next. 
        This helps simplify post-processing.  It has been noted (hi Ray!)
        that in some of Vivid's antialiasing modes an extra scan line is
        output to the file.  This may eventually get fixed but for now
        the best thing to do is to always use the info in the header
        rather than looking for the end of file. 
 
             map -- This is the format used for palette files.  This
        format was chosen to be compatible with fractint.  The file is in
        plain ASCII text and consists of 256 lines each containing the
        red, green and blue value for that palette entry.  The rgb values
        are integers in the range 0..255. 






                                        53





                                  Bibliography

 
             For anyone interested in ray tracing and how it works the
        following books are highly recommended.  Further references may
        be found in the bibliography at the end of Glassner's book. 
 
             "Computer Graphics, Principles and Practice, 2nd Ed.",
        Foley, van Dam, Feiner and Hughes, 1990, ISBN 0-201-12110-7
 
             "An Introduction to Ray Tracing", Andrew S.  Glassner, ed.,
        Academic Press, 1989, ISBN 0-12-286160-4
 
             "Illumination and Color in Computer Generated Imagery", Roy
        Hall, Springer-Verlag, 1989, ISBN 0-387-96774-5






































                                        54





                                      Index

                  #define. . . . . . . . . . . . . . . . . . . . .  15
        	  #include . . . . . . . . . . . . . . . . . . . 5, 16
                  ambient. . . . . . . . . . . . . . . . . . . . .  19
                  angle. . . . . . . . . . . . . . . . . . . . . .  17
                  antialiasing . . . . . . . . . . . . . . . . . .  20
                  aperture . . . . . . . . . . . . . . . . . . . .  21
                  aspect ratio . . . . . . . . . . . . . . . . . .  18
                  at . . . . . . . . . . . . . . . . . . . . . . .  17
                  background color . . . . . . . . . . . . . . . .  19
                  bibliography . . . . . . . . . . . . . . . . . .  54
                  blend. . . . . . . . . . . . . . . . . . . . . .  34
                  bump mapping . . . . . . . . . . . . . . . . . .  31
                  bunching . . . . . . . . . . . . . . . . . . . .  22
                  caustics . . . . . . . . . . . . . . . . . . . .  22
                  changes for 2.0. . . . . . . . . . . . . . . . .   3
                  checker pattern. . . . . . . . . . . . . . . . .  33
                  clipping . . . . . . . . . . . . . . . . . . . .  44
                  clipping plane . . . . . . . . . . . . . . . . .  44
                  colors . . . . . . . . . . . . . . . . . . . . .  13
                  command line flags . . . . . . . . . . . . . . .   6
                  comments . . . . . . . . . . . . . . . . . . . .  14
                  compound surfaces. . . . . . . . . . . . . . . .  33
                  cone . . . . . . . . . . . . . . . . . . . . . .  41
                  coordinate system. . . . . . . . . . . . . . . .  13
                  depth. . . . . . . . . . . . . . . . . . . . . .  22
                  dithering. . . . . . . . . . . . . . . . . . . .  47
                  down.exe . . . . . . . . . . . . . . . . . . . .  52
                  field of view angle. . . . . . . . . . . . . . .  17
                  file extensions. . . . . . . . . . . . . . . . .   5
                  file formats . . . . . . . . . . . . . . . . . .  53
                  fixed palettes . . . . . . . . . . . . . . . . .  47
                  Floyd Steinberg dithering. . . . . . . . . . . .  47
                  focal_length . . . . . . . . . . . . . . . . . .  21
                  from . . . . . . . . . . . . . . . . . . . . . .  17
                  fuzz . . . . . . . . . . . . . . . . . . . . . .  34
                  gif. . . . . . . . . . . . . . . . . . . . . . .  46
                  global clipping. . . . . . . . . . . . . . . . .  45
                  haze . . . . . . . . . . . . . . . . . . . . . .  19
                  img file format. . . . . . . . . . . . . . . . .  53
                  img2gif.exe. . . . . . . . . . . . . . . . . . .  46
                  include files. . . . . . . . . . . . . . . . . .   5
                  input file format. . . . . . . . . . . . . . . .  13
                  jitter . . . . . . . . . . . . . . . . . . . . .  21
        	  lights . . . . . . . . . . . . . . . . . . . . .  24
        		 directional . . . . . . . . . . . . . . .  24
        		 point . . . . . . . . . . . . . . . . . .  24
        		 spherical . . . . . . . . . . . . . . . .  25
        		 spot. . . . . . . . . . . . . . . . . . .  25
                  macro. . . . . . . . . . . . . . . . . . . . . .  15
        	  macro continuation . . . . . . . . . . . . . . .  15

                                        55




                  mandelbrot . . . . . . . . . . . . . . . . . . .  36
                  map file format. . . . . . . . . . . . . . . . .  53
                  median cut algorithm . . . . . . . . . . . . . .  46
                  noise. . . . . . . . . . . . . . . . . . . . . .  34
                  no_antialias . . . . . . . . . . . . . . . . . .  29
                  no_exp_trans . . . . . . . . . . . . . . . . . .  21
                  no_shadows . . . . . . . . . . . . . . . . . . .  21
                  ordered dither . . . . . . . . . . . . . . . . .  48
                  palette file . . . . . . . . . . . . . . . . . .  46
                  paste.exe. . . . . . . . . . . . . . . . . . . .  50
                  polygon. . . . . . . . . . . . . . . . . . . . .  39
                  popularity algorithm . . . . . . . . . . . . . .  46
                  preprocessor . . . . . . . . . . . . . . . . . .  15
                  projection . . . . . . . . . . . . . . . . . . .  18
                  random noise dithering . . . . . . . . . . . . .  48
                  resolution . . . . . . . . . . . . . . . . . . .  18
                  resume . . . . . . . . . . . . . . . . . . . . .   6
                  right-handed coordinate system . . . . . . . . .  13
                  ring . . . . . . . . . . . . . . . . . . . . . .  38
                  samples. . . . . . . . . . . . . . . . . . . . .  21
                  solid texture. . . . . . . . . . . . . . . . . .  33
                  sphere . . . . . . . . . . . . . . . . . . . . .  37
                  spherical pattern. . . . . . . . . . . . . . . .  33
                  start. . . . . . . . . . . . . . . . . . . . . .  18
                  statistics . . . . . . . . . . . . . . . . . . .   7
                  stop . . . . . . . . . . . . . . . . . . . . . .  18
                  studio . . . . . . . . . . . . . . . . . . . . .  17
                  surfaces . . . . . . . . . . . . . . . . . . . .  28
                  threshold. . . . . . . . . . . . . . . . . . . .  20
                  transform. . . . . . . . . . . . . . . . . . . .  42
                  transform_pop. . . . . . . . . . . . . . . . . .  42
                  triangular patch . . . . . . . . . . . . . . . .  40
        	  turbulence . . . . . . . . . . . . . . . . .  32, 34
                  up . . . . . . . . . . . . . . . . . . . . . . .  17
                  up.exe . . . . . . . . . . . . . . . . . . . . .  51
                  viewpoint. . . . . . . . . . . . . . . . . . . .  17
                  wave bump map. . . . . . . . . . . . . . . . . .  31
        	  xyzzy.v. . . . . . . . . . . . . . . . . . . . 5, 15