Get File Server Information

    This function returns information about a server to which a client
    has a service connection; The client need not be logged in.

    Function 23 (17h)
  
    Request Buffer

        Offset  Request Packet Contents         Bytes   Remarks
        ------  ---------------------------     -----   -------
        0       Sub-function Structure Len      2       Length
        2       17 (11h)                        1

    Reply Buffer

        Offset  Reply Packet Contents           Bytes   Remarks
        ------  ---------------------------     -----   -------
        0       Server Name                     48
        48      File Service Version            1       Major NetWare Version
        49      File Service Sub Version        1       Minor NetWare Version
        50      Maximum Service Connections     2
        52      Connections In Use              2
        54      Number Mounted Volumes          2       Max Supported Volumes
        56      Revision                        1       NetWare Revision
        57      SFT Level                       1
        58      TTS Level                       1
        59      Max Connections Ever Used       2
        61      Account Version                 1       Accounting Version
        62      VAP Version                     1
        63      Queue Version                   1       QMS Version
        64      Print Version                   1       Print Server Version
        65      Virtual Console Version         1
        66      Restriction Level               1       Security Restrict
                                                        Version
        67      Internet Bridge                 1       Internet Bridge
                                                        Support Version
        68      Reserved                        60