This README of SBACK1.ZIP is for NetWare v3.1x.  The following files are
included in this revision:

	WANGTEK.NLM         15681     7-18-91     3:37p
	DIBIDAI.NLM         15527     7-23-92     2:14p
	NOVADIBI.NLM        17119     3-31-92    12:08p
	SIDR.NLM            17192     8-21-92    12:03p
	TSA-310.NLM        105836     4-03-92     9:20a
	TSA-311.NLM        106267     4-03-92     9:13a
	TSA.NLM             27047     4-03-92     2:59p
	SBACKUP.NLM        183043     3-05-92     2:00p
	TAPEDAI.DSK         28838     2-08-93     5:08p
	PHYSADDR.DSK          487    12-09-92    16:22p
	SME-SHIM.NLM         1148     3-04-92     8:09a
	SBACKUP.PCL         38199     1-15-92    11:46a(DOCUMENTATION) 
	SBACKUP.NFO        178176     3-12-92     3:38p(DOCUMENTATION)
	SBACK1.DOC          THIS FILE (Revision 1.0)


SBACKUP v3.11b Maintenance Update
	These are some of SBACKUP'S fixes and enhancements. 
	
Documentation
	This update contains revised user documentation (Folioformat).To
	view this documentation simply copy theSBACKUP.NFO file to the
	directory where NFOLIO.EXE is located( usually SYS:PUBLIC).
	Execute Nfolio.exe and select SBACKUPfrom the main menu.

3.10 NetWare support
	A TSA for 3.10 NetWare is now available. Load TSA-310.NLM and 
	SME-SHIM.NLM on the 310 server you are backing up.
 
File location
	The subdirectory structure under the SYS:SYSTEM directory
	is not required to load NLMs. All NLMs may reside in the
	SYS:SYSTEM directory*.  

	The directories SYS:SYSTEM\TSA (for temporary file use) and 
	SYS:SYSTEM\DIBI (for DIBI2$DV.DAT file) must exist. 

	*If the SIDR, DIBI and TSA directories are used, search paths
	must be added to these directories using the SEARCH ADD
	[path]command.

Restore
     New restore option:
	  Include File Server Level - see new user document.

	  Bindery is NOT restored unless specifically included
	  using the "Include File Server Level" options.

Maintenance Improvements
     ¯ It runs faster.  
     ¯ Errors no longer appear when trying to restore a directory 
       that does not exist. 
     ¯ Corrected NameSpace data error on FTAM and NFS.
     ¯ Improved file open modes.
     ¯ Changed SMS to work on a server after the SECURE CONSOLE  command. 
     ¯ Corrected ABEND using SYS:\ as the working directory.
     
To install this new SBACKUP and supported files:
     1. Flag all SBACKUP files SRW in SYS:SYSTEM.
     2. Rename the SBACKUP files to *.old.
     3. Copy all files to the SYS:SYSTEM directory. (In this new
	version of SBACKUP, all NLMs can be loaded from the system
	directory*).

	*If the SIDR, DIBI and TSA directories are used, search
	 paths must be added to these directories using the
	 SEARCH ADD [path]command.
	
     4. Flag the files back to ROS.

Explanation of TAPEDAI and DIBIDAI files:

TAPEDAI.DSK
	
	TAPEDAI.DSK is a NetWare 386 device driver written to control
	certain tape devices.  It is used with DIBIDAI.NLM.

	PHYSADDR.DSK is a support file for TAPEDAI.DSK and must be loaded
	prior to loading TAPEDAI.DSK.

	DIBIDAI.NLM presents a DIBI interface to SBACKUP.NLM, but
	translates the DIBI requests into NetWare DAI calls.  This 
	eventually results in device driver calls getting passed to 
	TAPEDAI.DSK through the same IO request mechanism used byNetWare
	to obtain disk service.

	TAPEDAI.DSK must be loaded prior to loading SBACKUP. If it is
	used often, the user may want to load it from within the
	STARTUP.NCF file.

	In order to use TAPEDAI.DSK and DIBIDAI.NLM the DIBI2$DV.DAT 
	file in SYS:SYSTEM\DIBI must be edited to include DIBIDAI.NLM.  
	The DIBI2$DV.DAT file is a DOS text file and can be edited 
	using EDIT.NLM or with any DOS text editor from a workstation.
	
	Editing the Dibi2$dv.dat file in the system\dibi subdirectory:

	1.  Flag the file as read/write.
	2.  Use a text editor to edit the file. If editing the file 
	    using the EDIT.NLM type: 
		     "LOAD EDIT SYS:SYSTEM\DIBI\DIBI2$DV.DAT" 
	    at the console prompt.
	3.  When the file is brought up it will look like this:
   
	    "Wangtek Tape Drive."       WANGTEK  PORT=280 DMA=3 IRQ=5
	    "HP DIBI-2 Tape Driver."    NOVADIBI
	    "DC00 DIBI-2 Tape Driver."  TAPEDC00

	    A line like the following will need to be added:

	    "DibiDai Driver."           DibiDai

	    The description on the left can be anything.  The DibiDai 
	    on the right refers to the the DibiDai.nlm that comes with
	    Sback.zip.  
	    
	4.  Exit the editor and save changes.   


Dependencies:

	TAPEDAI.DSK targets any ASPI compliant disk drivers.  Check with
	the driver manufacturer to confirm ASPI compliancy.

	Consequently,  the ASPI compliant disk driver must be loaded 
	prior to loading TAPEDAI.DSK. 

Target Devices:
	TAPEDAI only works with the following devices:

	Manufacturer    Product                 

	ARCHIVE         Python
	CIPHER          T826 (half inch - 2.6 Gig)
	CIPHER          T860 (half inch - 6 Gig)
	EXABYTE         EXB-8500                        
	HP              HP35450A                        
	HP              HP35470A*                       
	HP              HP35480A*
	TANDBERG        TDC 3800
	TANDBERG        TDC 4100
	TANDBERG        TDC 4200
	WANGDAT         1300
	WANGDAT         3200
	WANGTEK         5525ES
	WANGTEK         6130
	WANGTEK         WANGTEK_6130_HS 

       *(The HP35470A and HP35480A must be set through its dip switches
       so that the SCSI Valid Bit is set upon crossing Early Warning.
       If this is not done, sessions that span tapes won't be reliable.
       Users should perform a test backup and restore across tapes to
       confirm that the switches are set properly.  The file that
       actually spans tapes is the one to test.)

NOVADIBI.NLM
	
	DIBI-2 interface driver that works with devices and drivers
	that are DIBI-2 compatible.  Controller driver must support
	the DIBI-2 interface.  Contact specific hardware vendor to
	determine DIBI-2 driver compatibility.

SIDR.NLM        
	Storage Independent Data Requester.  Controls transfer of data
	between backup engine and the TSA.

TSA Files
	TSA.NLM
	    Target Service Agent.  Interface used by SIDR.NLM to
	    gather data from the target server.

	TSA-311.NLM
	    Target Service Agent for 3.11 server to be backed up.  
	    Provides link between TSA.NLM and specific 3.11 target 
	    server.

	TSA-310.NLM
	    Target Service Agent for 3.10 server to be backed up.  
	    Provides link between TSA.NLM and specific 3.10 target 
	    server.  Must be used in conjunction with SME-SHIM.NLM.

	SME-SHIM.NLM
		Support file for TSA-310.NLM.


**********************
* A WORD OF CAUTION: *
**********************

At the present time SBackup does NO READ-AFTER-WRITE verification of the
data that is backed up.  Therefore it is important that you verify your
backups manually.  One way of accomplishing this is to follow example 1
in the Commonly Asked Questions section -- "How to Restore a file to a
new location."  Restoring several files to a new location and doing a DOS
compare on the restored files with their originals will verify that files
are being backed up correctly and that they can be restored.  It should
be kept in mind that this in no way represents a complete verification.
It is recommended that you do this with every backup set that you make
and should be made a regular step in your backup procedures.

Driver Implementation
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍ»
ºDriver From              ³Driver From         ³Sbackup Interface   ³Multiple º
ºNovell                   ³Vendor              ³Software            ³Device   º
º                         ³                    ³                    ³Support  º
ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
ºTAPEDAI.DSK &            ³Any ASPI compliant  ³DIBIDAI.NLM (Driver ³YES      º
ºPHYSADDR.DSK             ³Disk Driver*        ³must be added to    ³         º
º                         ³                    ³DIBI2$DV.DAT file   ³         º
º                         ³                    ³-- see above        ³         º
º                         ³                    ³TAPEDAI.DSK         ³         º
º                         ³                    ³explanation)        ³         º
ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
ºB/R Driver Kit NLMs.     ³N/A                 ³DC00 DIBI-2 Tape    ³NO       º
º(Only Adaptec.NLM        ³                    ³Driver              ³         º
ºShips w/3.11 -- see      ³                    ³(TapeDC00.NLM)      ³         º
ºfollowing list for other ³                    ³                    ³         º
ºavailable drivers)       ³                    ³                    ³         º
ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
ºN/A                      ³Any DIBI-2          ³HP DIBI-2 Tape      ³YES      º
º                         ³Compliant Disk      ³Driver              ³         º
º                         ³Driver*             ³(NovaDibi.NLM)      ³         º
ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
ºWANGTEK.NLM              ³N/A                 ³Wangtek Tape Drive  ³N/A      º
º(Support for             ³                    ³(Wangtek.NLM)       ³         º
ºWangtek's QIC-02         ³                    ³                    ³         º
ºcontrollers)             ³                    ³                    ³         º
ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
ºN/A                      ³N/A                 ³CPQSCSIT.NLM Tape   ³YES      º
º                         ³                    ³driver from Compaq. ³         º
º                         ³                    ³(Must be added to   ³         º
º                         ³                    ³DIBI2$DV.DAT file)  ³         º
º                         ³                    ³                    ³         º
º                         ³                    ³                    ³         º
ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
ºPS2OPT.DSK dated         ³N/A                 ³DIBIDAI.NLM (Driver ³YES      º
ºFebruary 4, 1993 or      ³                    ³must be added to    ³         º
ºlater                    ³                    ³DIBI2$DV.DAT file   ³         º
º                         ³                    ³-- see above        ³         º
º                         ³                    ³TAPEDAI.DSK         ³         º
º                         ³                    ³explanation)        ³         º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍ¼
*For verification of ASPI or DIBI-2 compliant disk drivers check with
 driver vendor.

File Implementation:

	Sbackup can control tape devices with the following
	configurations:

	1. B/R Driver Kit NLMs.  Adaptec.Nlm is provided with 3.11.
	   The Adaptec.Nlm driver will control a single tape device
	   off of either an Adaptec 154x , 164x or a 174x in standard
	   mode.
		Limitations:
		¯ Support for only one device connected to
		  controller.
		¯ Controller must be set to port address 330.

	Support is also available for the following controllers with
	the purchase of Novell's B/R Driver Kit (Part #153-000179-001):

	THE B/R DRIVER KIT NLMs ALLOW ONLY A SINGLE DEVICE (I.E.SINGLE
	TAPE DEVICE ONLY -- NO HARD DRIVES) TO BE CONNECTED TO THE
	CONTROLLER.

Host Adapter                            Bus           Interface
----------------------------------------------------------------
3COM SCSI Plus                          ISA             SCSI
Adaptec AHA-1520                        ISA             SCSI
Adaptec AHA-1540                        ISA             SCSI
Adaptec AHA-1542                        ISA             SCSI
Adaptec AHA-1640                        MC              SCSI
Adaptec ASPI SCSI Manager                               SCSI
Archive VP402                           ISA             QIC-02
Archive VP409A                          MC              QIC-02
BusTek BT-542B                          ISA             SCSI
BusTek BT-642B                          MC              SCSI
BusTek BT-742A                          EISA            SCSI
Future Domain MCS-350                   MC              SCSI
Future Domain TMC-845                   ISA             SCSI
Future Domain TMC-850                   ISA             SCSI
Future Domain TMC-860                   ISA             SCSI
IBM SCSI Host Adapter                   MC              SCSI
NetFRAME SCSI Adapter                                   SCSI
Tecmar PC-02                            ISA             QIC-02
Tecmar PC-02                            MC              QIC-02
Tricord IIOP                                            SCSI

		With the B/R driver kit the NLMs can be configured for
		the specific controller settings.

		Implementation:     
			¯  The NLM is loaded prior to loading Sbackup.  
			¯  After loading Sbackup select the Tape DC00
			   driver.
			NOTE:  No other driver should be loaded for the
			       controller when using the B/R driver NLMs.
       
		2. NovaDibi.Nlm provides tape backup support when used
		   in conjunction with a disk driver that is DIBI-2
		   compatible (to verify DIBI-2 compatibility check with
		   disk driver manufacturer).  With the NovaDibi.nlm
		   driver multiple devices can be connected to the
		   controller.
		     Implementation:
			  ¯ Load DIBI-2 compliant disk driver before
			    loading Sbackup.
			  ¯ Load TSA.
			  ¯ Select the HP-Dibi2 Tape Driver option in
			    Sbackup.

		   This driver was developed initially for the HP DAT
		   drives.  Caution should be used when using a
		   "Non-DAT" drive.  Errors could occur when multiple
		   sessions are backed up to a single tape.

		3. TapeDai.DSK and PhysAddr.Nlm provide tape backup
		   support when used in conjunction with an ASPI
		   compliant disk driver (to verify disk driver's ASPI
		   compliancy contact driver manufacturer).

			Implementation:
				¯  Load ASPI compliant disk driver.
				¯  Load PHYSADDR.DSK
				¯  Load TapeDai.Dsk.
				¯  Select DibiDai.Nlm option that was
				   added to DIBI2$DV.DAT file (for
				   instructions on how to edit file
				   see note about DibiDai.Nlm file
				   above).

		       NOTE:  If the tape drive being used is not in the
			      list of tape drives supported by TapeDai.Dsk
			      this configuration will NOT work.

		4. Wangtek.Nlm.  Provides tape backup support for Wangtek's
		   QIC-02 tape devices.  The default setting for the driver
		   is Port=280, DMA=3, IRQ=5.  If the   QIC-02 adapter is
		   set to anything other than these   settings the
		   DIBI2$DV.DAT file will need to be edited (see
		   instructions above for editing the DIBI2$DV.DAT file).

		5. PS2Opt.Dsk dated February 4, 1993 and DIBIDAI.NLM.
		   This driver is included in documentation due to its
		   unique implementation.
				¯ Load PS2Opt.Dsk.
				¯ Load TSA
				¯ Load Sbackup
				¯ Select DibiDai.Nlm option that was
				  added to DIBI2$DV.DAT file (for
				  instructions on how to edit file see
				  note about DibiDai.Nlm file above).

		   Requirements:
			  ¯ PS2OPT.DSK dated 02-04-93 or later.
			  ¯ PS2OPT.DSK has only been tested with the
			    following devices:
			     1.  Exabyte 8200, 8mm
			     2.  Exabyte 8500, 8mm
			     3.  HP 35470, 4mm DAT
			     4.  HP 35480A, 4mm DAT
			     5.  HP 35450A, 4mm DAT
			     6.  WangDat 3200, 4mm DAT
			     7.  WangDat 1300, 4mm DAT
			     8.  Archive Python, 4mm DAT
			     9.  Cipher T860s, 1/2 inch tape

		6. CPQSCSIT.NLM.  Driver can be found on Compaq's Netware
		   Programs diskette or the latest driver can be obtained
		   from Netwire -- CPQTAP.ZIP in library 13.  This driver
		   allows Sbackup to function with the following Compaq 
		   tape drives:

		   Drive Name                           Part Number
		   320-/525-MG Tape Drive               116573-001
		   1.3-/2.0-GB DAT Drive                131162-001

		   In order to use this driver the DIBI2$DV.DAT file in the
		   SYS:SYSTEM\DIBI subdirectory must be editted (see note
		   for editting the DIBI2$DV.DAT file above).  

		   If server is EISA based the following line will need to
		   be added:

		   "Compaq SCSI Tape Driver."              CPQSCSIT

		   If server is ISA base the following line will need to be
		   added:

		   "Compaq SCSI Tape Driver."   CPQSCSIT PORT=xxx DMA=x IRQ=x

		   The x's after PORT, DMA and IRQ should be replaced with
		   the actual setting of the SCSI tape adapter.  CPQSCSIT 
		   should also be lined up with the other driver names in
		   the DIBI2$DV.DAT file.

		   Implementation:
			¯ Load TSA
			¯ Load Sbackup
			¯ Select Compaq Option that was added to the 
			  DIBI2$DV.DAT file.


Commonly Asked Questions:
	
	1.  How to restore a file to a new location.

	 From the Sbackup Restore Options Menu select "Selection List
	 Options."
		With the "Include Directories" Option insert the name
		of the subdirectory that files are to be redirected TO
		(i.e. the destination subdirectory).

		With the "Include and Exclude File" Options select
		specific files to be redirected.

		With the "Destination Paths" Option insert the"Source"
		and "Destination" paths.

		Start the Restore.

		EXAMPLE:

		Files that were backed up in the SYS:FIRST subdirectory
		with the file specification of *.DATneed to be restored
		to the VOL1:SECOND subdirectory.On the Sbackup Restore
		Options Menu select"Selection List Options."

		Set the "Include Directories" Option to VOL1:SECOND --
		the name of the destination subdirectory.

		Set the "Include Files" Option to *.DAT -- the file
		specification to be restored.

		Escape back to the Restore Options Menu and select
		"Destination Paths."

		Press Insert and enter the "Path Source" as SYS:FIRST.
		Enter the "Path Destination " as VOL1:SECOND.

		Start the Restore.


	2.  How to Restore specific files.

		From the Sbackup Restore Options Menu select "Selection
		List Options."

		With the "Include Directories" Option insert the
		directory in which the file to be restored resided when
		it was backed up.  If you don't know leave this option
		blank -- all directories will be searched for the include
		files specified.

		With the "Include Files" Option insert the filenames to be
		restored.  Wild cards (* and ?) can be used.

		Start the Restore.

		EXAMPLE:

		The entire SYS:TEMP subdirectory was deleted and purged.
		The entire subdirectory does not need to be restored only
		spreadsheet files need to be restored.

		On the Sbackup Restore Options Menu select "Selection
		List Options."

		The "Include Directories" option would be set to SYS:TEMP.
		This will prevent Sbackup from restoring all instances of
		the spreadsheet files.

		The "Include Files" option would be set to *.WKS, the
		extension of the spreadsheet files.

		Start the Restore.

	3.  In the "Selection List Options" which takes precedence over
	    the other "Include" or "Exclude"?

		The "Exclude" option takes precedence over the"Include"
		option.  However, whenever the "Include"option is used
		all "Non-included" files are excluded anyway.

	4.  In the "Selection List Options" what is the difference between
	    the Include/Exclude files options and Include/Exclude
	    Path/Files on the "Selection List Options"?

		The Include/Exclude Files options are used to restore
		files that reside anywhere in the directory structure.
		When used in conjunction with the Include/Exclude
		Subdirectories options specific file paths can be restored
		(see #2 above -- Restoring specific files).

		The Include/Exclude Path/Files options are used to restore
		files to the specific location in the directory structure
		from which they were backed up.  Regardless of the paths
		specified the entire directory structure will be scanned.
		Any subdirectories that were on the backup tape and not on
		the server being restored will be created.

***************************************************************** 
		    DISCLAIMER  
  
Novell, Inc. makes no representations or warranties with respect to
any NetWare software, and specifically disclaims any express or
implied warranties of merchant ability, title, or fitness for a
particular purpose.  

Distribution of any NetWare software is forbidden without the
express written consent of Novell, Inc.  Further, Novell reserves
the right to discontinue distribution of any NetWare software.

Novell is not responsible for lost profits or revenue, loss of use
of the software, loss of data, costs of re-creating lost data, the
cost of any substitute equipment or program, or claims by any party
other than you.  Novell strongly recommends a backup be made before
any software is installed.   Technical support for this software
may be provided at the discretion of Novell.
*****************************************************************