NWDOSIPX.DOC           07/10/91
           Copyright 1991, Compaq Computer Corporation.
                                
  NOVELL NETWARE DOS IPX WORKSTATION INSTALLATION INSTRUCTIONS


1. INTRODUCTION
2. FEATURES
3. RELEVANT FILES
4. SYSTEM REQUIREMENTS
5. INSTALLATION
6. SOURCE ROUTING SUPPORT
7. HIGH MEMORY SUPPORT
8. NETWIRE


1. INTRODUCTION

     This file details the installation of the NetWare DOS IPX
     workstation driver for the COMPAQ 32-Bit DualSpeed Token Ring
     Controller.


2. FEATURES

     1. Provides improved performance over previous releases of  
        the driver.

     2. Supports Source Routing.

     3. May be loaded into high memory.

     4. Supports Microsoft Windows 3.0.


3. RELEVANT FILES

  NWDOSIPX.DOC - This file
  SCPQT416.OBJ - NetWare DOS IPX workstation device driver object
  SCPQT416.LAN - NetWare DOS IPX workstation configuration file
  MAC380.BIN   - Controller download program image


4. SYSTEM REQUIREMENTS

  This device driver requires:
      *   Any COMPAQ EISA computer with the COMPAQ 32-bit DualSpeed 
          Token Ring controller installed. The system must have
          been configured using the COMPAQ EISA Configuration
          Utility.  

      *   NetWare workstation generation software. Either shgen.exe
          or wsgen.exe can be used to generate the workstation
          software with this driver. These programs are located on
          the workstation services diskette included with the
          NetWare system software.


5. INSTALLATION

In the following procedures, refer to your NetWare documentation
for information on installing DOS workstation drivers.  To install
the device driver for the token ring controller, follow the
procedure that best serves your needs:

Floppy Diskette Drive Installation Procedure:

     1.   If you are installing NetWare Device Drivers from
          diskettes, format a blank diskette with the volume label
          "LAN_DRV_428".  To this diskette, copy the following
          files:

          scpqt416.obj
          scpqt416.lan
          
          Note:  For more information about the MS-DOS FORMAT,
          LABEL, and COPY commands, refer to your MSÄDOS
          documentation.

     2.   Follow the instructions in the NetWare documentation to
          configure and install a network IPX workstation shell
          onto your workstation(s). At some point in the
          installation you will be prompted to insert the diskette
          labeled "LAN_DRV_???". Insert the diskette you prepared
          earlier.

     3.   The NetWare workstation generation procedure creates an
          IPX.COM file which contains the driver for the 32-Bit
          DualSpeed Token Ring Controller.  This file and the
          NETx.COM file must be copied to your workstation fixed
          disk or diskette.  Refer to your NetWare documentation
          on which files are required for the version of MS-DOS you
          are using.

     4.   COPY THE MAC380.BIN FILE TO THE SAME DIRECTORY ON THE
          WORKSTATION WHERE YOU COPIED THE IPX.COM FILE.

          If you are unable to correctly load the device driver,
          verify your Token Ring Controller(s) configuration by
          running CHKTOK.EXE, found on the OPTION CONFIGURATION
          diskette.  To test your system hardware, run DIAGNOSTICS
          Version 7.02 or later.  Refer to the 32-Bit DualSpeed
          Token Ring Controller Installation Card for more
          information on using these utilities, or contact you
          Authorized COMPAQ Computer Dealer.

     
Fixed Disk Drive Installation Procedure:

     1.   If you are installing the workstation drivers from a
          fixed disk or network drive, create a subdirectory named
          LAN_DRV_.428 on the same directory where the installation
          program is stored. Copy to that subdirectory the
          following files: 

          scpqt416.obj
          scpqt416.lan
          
     2.   The NetWare workstation generation procedure creates an
          IPX.COM file which contains the driver for the 32-Bit
          DualSpeed Token Ring Controller.  This file and the
          NETx.COM file must be copied to your workstation fixed
          disk.  Refer to your NetWare documentation on which files
          are required for the version of MS-DOS you are using.

          Note:  If you are installing NetWare from a fixed disk
          or network drive, the drivers will be automatically
          loaded from the LAN_DRV_.428 subdirectory.

     3.   COPY THE MAC380.BIN FILE TO THE SAME DIRECTORY ON THE
          WORKSTATION WHERE YOU COPIED THE IPX.COM FILE.
          
          If you are unable to correctly load the device driver,
          verify your Token Ring Controller(s) configuration by
          running CHKTOK.EXE, found on the OPTION CONFIGURATION
          diskette.  To test your system hardware, run DIAGNOSTICS
          Version 7.02 or later.  Refer to the 32-Bit DualSpeed
          Token Ring Controller Installation Card for more
          information on using these utilities, or contact your
          Authorized COMPAQ Computer Dealer.

          
6. SOURCE ROUTING SUPPORT

     Source routing is a method of routing data across multiple
     networks through bridges. To enable the workstation to pass
     data through a source routing bridge, the workstation must be
     running the source routing program, route.com from Novell.
     This program is necessary only if external source routing
     bridges are present on the network. The source routing
     program, file route.com, is available on the Novell NetWare
     DOS Workstation Generation diskette. The Novell source routing
     program and installation instructions are also available on
     Compuserve NetWire under NOVA forum in library 8 (Novell
     Patch/Drv'r) in the TRN050.ZIP file.

     See the Novell NetWare documentation for more information on
     source routing.

     The following is an example of how to load source routing. The
     following lines should be placed in the workstation
     autoexec.bat file.

     ipx
     route
     net3


7. HIGH MEMORY SUPPORT

     The driver may be loaded into what is sometimes referred to
     as "high memory". High memory is the memory located between
     640K and 1Meg. The NetWare DOS IPX workstation driver is
     compatible with programs such as COMPAQ runhi, QUALITAS
     386max, or QUARTERDECK QEMM. All of these programs allow the
     driver to be loaded into high memory. The primary advantage
     of loading the driver into high memory is that it will free
     up memory in the base 640K, thus leaving more memory available
     to applications. The following is an example of how to load
     the driver with COMPAQ runhi. 

     config.sys:
     device = c:\dos\himem.sys
     device = c:\dos\cemm.exe NOEMS

     autoexec.bat:
     runhi ipx
     runhi net3

     Notice the NOEMS option is being used on the command line for
     cemm.exe. The NOEMS option will disable expanded memory. The
     NOEMS option frees up more high memory, but its use may not
     be advisable if you are using applications that require
     expanded memory. 


8. NETWIRE

     The NetWare DOS IPX driver files for the COMPAQ 32-Bit
     DualSpeed Token Ring Controller reside on Compuserve NetWire
     under NOVA forum in library 11 (or library 17 for new uploads)
     in the CPQTR2.ZIP file.