NETWORK VIDEO IDENTIFIER
                                   v 1.10 
                      Copyright 1989 by Brad Stephenson
    

  GENERAL
  -------
    
    NETVID is a utility program designed for use on Local Area Networks. 
    Depending on the application programs run by the workstations, NETVID 
    may eliminate the need for hardware configuration files for each 
    workstation.  

    NETVID detects the video adapter hardware and current screen settings 
    in a workstation.  It then places information in the workstation's 
    parent DOS environment.  The environment information can be used to 
    build configuration file names for several popular application 
    programs. 
    
    For example, NETVID's environment information can be used to build a 
    Lotus 1-2-3 .SET filename, dynamically configuring 1-2-3 to match the 
    workstation's current video parameters. 

    NETVID auto-detects the workstation's video hardware adapter, the 
    current number of screen columns, and the current number of screen 
    rows.  It then generates three environment variables: 
    
              NVADP - Video adapter hardware present
              NVCOL - Number of columns on display
              NVROW - Number of rows on display

        
    Some of the new VGA video boards come with a configuration program 
    that allows you to set certain emulations such as CGA, Hercules, etc.  
    NETVID will correctly detect the emulation mode, not simply the VGA 
    hardware presence. 
    
    NETVID's auto-detection of the video adapter can be overridden by 
    command line option switches.  This type of override would be used if 
    the workstation has a single-color display (e.g. an LCD), but has a 
    CGA-compatible video adapter.  The auto-detected number of columns 
    and rows can also be overridden by command line switches.  The Test 
    Mode option ('/t') causes NETVID to display the result of its auto-
    detection and any command line overrides. 
    
    The workstation must have at least 30 bytes of free environment space 
    for the NETVID variables.  See your DOS manual for information 
    regarding the expansion of environment size (look at the /E: option 
    in the COMMAND.COM description). 

    Secondary COMMAND processes (as in a 'Drop to DOS' mode from an 
    application), do not allow expansion of the parent's DOS environment; 
    NETVID won't have enough room to add its variables.  If you plan to 
    run NETVID in a secondary COMMAND process, reserve adequate 
    environment space by executing NETVID in the workstation's 
    AUTOEXEC.BAT. 
    
    A non-zero DOS ERRORLEVEL is returned if problems are detected during 
    NETVID execution.  The return values can be used by a batch file to 
    present custom error messages to network users. 


                                 NETVID 1.10 
                                    Page 2
    
  INVOKING NETVID
  ---------------
        
    To call NETVID from the DOS command line or from a batch file, use 
    the following syntax: 

       NETVID [options] 
        
        Options:
           
           /a - Overrides auto-detection of video adapter.
                Single-color CGA system such as a laptop 
                or Compaq portables should use '/aLCD'.
                Valid override values:

                     MDA       -Monochrome Display Adapter
                     CGA       -Color Graphics Adapter
                     MCGA      -Multi-color Graphics Adapter (PS/2)
                     EGA       -Enhanced Graphics Adapter
                     EGA64     -Enhanced Graphics Adapter (with memory upgrade)
                     EGAMONO   -EGA driving monochrome display
                     8514      -IBM 8514-compatible adapter (PS/2)
                     HERCMONO  -Hercules Monochrome Graphics Card
                     ATT400    -AT&T 400-line Color Graphics Adapter
                     VGA       -Video Graphics Array
                     PC3270    -IBM PC3270
                     LCD       -Single-color CGA compatible
           
           /c - Overrides auto-detection of the number of screen
                columns.  The first 3 digits of the option 
                argument are placed in the environment 
                variable NVCOL.
           
           /r - Overrides auto-detection of the number of screen
                rows.  The first 2 digits of the option argument
                are placed in the environment variable NVROW.

           /t - Test Mode.  NETVID will generate and display
                the three environment variables WITHOUT adding
                them to the DOS environment.

                              
                                
                               ***  NOTE:  ***
             Option arguments must immediately follow options and 
             must be white-space delimited (see examples). 


    EXAMPLES:
    
        NETVID /aLCD /c132 /r43 /t 
    
        NETVID /r50 /c80


                                 NETVID 1.10 
                                    Page 3


  DOS ERRORLEVEL RETURNS
  ----------------------

    1.  If NETVID successfully executed:

                 o DOS Errorlevel of 0
                    
                   - If the /t option was specified, ERRORLEVEL 
                     will always be zero.

                 o DOS Environment variable NVADP set to:
                                                                           
                        00 - MDA
                        01 - CGA
                        02 - MCGA
                        03 - EGA
                        04 - EGA64
                        05 - EGAMONO
                        06 - 8514
                        07 - HERCMONO
                        08 - ATT400
                        09 - VGA
                        10 - PC3270
                        11 - LCD
                 
                 o DOS Environment variable NVCOL set to current number
                   of screen columns (or value from '/c' override).
    
                 o DOS Environment variable NVROW set to current number
                   of screen rows (or value from '/r' override).
                                                                             
    
    2.  If NETVID detected an error while executing:

                 o DOS ERRORLEVEL indicates error condition found:
    
                     1 - DOS not version 2.0 or higher
                     2 - Insufficient room in environment for variables
                     3 - Internal NETVID error (bad environment string built)
                     4 - DOS environment corrupted before variables added
                     5 - Invalid NETVID command line option

        
    The utility RETURN (included in the NETVID distribution archive) allows 
    users to call NETVID and see the resulting DOS ERRORLEVEL return code.  
    Refer to the file RETURN.DOC for program syntax. 


                                 NETVID 1.10 
                                    Page 4



  NETWORK USAGE EXAMPLE
  ---------------------

    In this example, a workstation will be executing Lotus 1-2-3 from a 
    workstation and NETVID will be used to select the correct 1-2-3 .SET 
    file matching the video parameters of the workstation.

    Before attempting to execute 1-2-3 using NETVID variables, the 
    Network System Administrator must set up several 1-2-3 configuration 
    files (.SET files).  One .SET is created for each unique workstation 
    hardware configuration. 
    
    1-2-3 configuration files would use the following naming convention: 

                 aacccrr.SET
                 \/\ /\/
                 |  | |
                 |  | Number of screen rows
                 |  |
                 |  Number of screen columns
                 |
                 Video adapter type

    
    A CGA 80x25 configuration file would, for example, be named 0108025.SET. 
    One for VGA 132x80 would be named 0913280.SET.
 
        
   THE NETWORK LOTUS 1-2-3 BATCH FILE
   ----------------------------------

    The Network System Administrator then sets up a batch file that users 
    call when they want to run 1-2-3.  When the user request for 1-2-3 is 
    detected by the file server, the batch file calls NETVID, then 1-2-3.
    An example batch file named RUN123.BAT follows. 

         ECHO OFF
         CLS
         NETVID %1 %2 %3 %4
         IF ERRORLEVEL 1 GOTO ERR
         123 %NVADP%%NVCOL%%NVROW%.SET
         GOTO END
         :ERR
           .
           .    [We'll cover error handling later]
           .
         :END
    


                                 NETVID 1.10 
                                    Page 5


    For our example, we'll use a workstation that has an EGA video adapter
    driving an EGA monitor.  Although the user wants to use a 132x43 video
    driver, the workstation is currently in DOS (80x25).  NETVID will 
    auto-detect the EGA adapter and set NVADP=03.  Since the current 
    display mode is not 132x43, the user requests a higher resolution 
    mode to override the auto-detection of the current 80x25 mode.

    At the workstation, the user types:

                    RUN123 /c132 /r43

    The file server responds by sending RUN123.BAT down to the 
    workstation for execution.  The batch file executes, calling for 
    NETVID from the server.  NETVID executes at the workstation, 
    receiving the two command line parameters '/c132' and '/r43.'

    NETVID places three environment variables into the parent DOS 
    environment of the workstation.  If we stopped execution of the batch 
    file at this point and typed SET at the DOS prompt, the last three 
    statements would be:

                    NVADP=03
                    NVCOL=132
                    NVROW=43

    After executing NETVID, the batch file calls 1-2-3, using the three 
    environment variables to build a 1-2-3 .SET file name that matches 
    the workstation's video hardware and the user's desired video mode.

    The batch file line:  123 %NVADP%%NVCOL%%NVROW%.SET
    is replaced with   :  123 0113280.SET

    1-2-3 comes up in the video mode that correctly matches the 
    workstation's hardware and the row/column overrides specified by the 
    user.



                                 NETVID 1.10 
                                    Page 6


  ERROR HANDLING
  --------------

    Network batch files calling NETVID should include error handling.  
    NETVID returns DOS ERRORLEVEL codes for several types of errors, 
    allowing customized prompts to be displayed to network users.

    A completed RUN123.SET file may look like this:

         ECHO OFF
         CLS
         NETVID %1 %2 %3 %4
         IF ERRORLEVEL 1 GOTO ERR
         IF NOT EXIST \LOTUS\%NVADP%%NVCOL%%NVROW%.SET GOTO BADSET
         123 %NVADP%%NVCOL%%NVROW%.SET
         GOTO END
         :ERR
         IF ERRORLEVEL 5 GOTO BADOPT
         IF ERRORLEVEL 4 GOTO BADENV
         IF ERRORLEVEL 3 GOTO BADENV
         IF ERRORLEVEL 2 GOTO NOROOM
         ECHO You must boot with DOS 2.0 or higher to run 1-2-3!
         GOTO END
         :NOROOM
         ECHO No room in your workstation's environment!
         ECHO Remove unneccessary environment variables before continuing.
         GOTO HELP
         :BADENV
         ECHO Technical difficulties...
         ECHO Please reboot your workstation and try again.
         GOTO HELP
         :BADOPT
         ECHO You entered an unsupported option.
         ECHO The options you entered: %1 %2 %3 %4
         ECHO Please consult your Network User's Manual.
         GOTO HELP
         :BADSET
         ECHO %NVCOL% columns by %NVROW% rows is not supported by the network.
         ECHO Please consult your Network User's Manual
         :HELP
         ECHO For further assistance, call extension 1234
         :END

    

                                 NETVID 1.10 
                                    Page 7


  REVISION HISTORY
  ----------------

    Version 1.00 
    10/15/89      Original release.

    Version 1.01
    10/18/89      Added check and special environment handling for 3.2x 
                  versions of DOS.  Removed requirement that NETVID be
                  executed from primary COMMAND process only.  NETVID
                  now properly handles secondary COMMAND processes.             

    Version 1.10
    10/22/89      Corrected problem seen in auto-detect of video systems
                  already in a 132-column mode (NETVID was writing garbage
                  to the environment).

                                         

  
    NETVID v1.10 has no registration fees nor does it require a software
    license.  The author reserves all rights to NETVID.  It may not be 
    sold for a profit, but may be included (free of charge) with software 
    that is sold for a profit as long as this documentation file 
    accompanies the program.  

    If using NETVID saves you a lot of time (i.e. money) and you feel 
    generous, send no more than $10.00 to the address listed below.  
    Please feel free to comment on NETVID and/or offer suggestions for 
    other utilities you would like to have!
  
  

                               Brad Stephenson
                                670 Edgeworth
                              Jenison, MI  49428
                          Compuserve ID  71620,1035