The installation process will copy the driver "P4_Flickerfixer" to the
drawer "Devs:Monitors". This driver controls the Picasso IV on-board
flicker fixer.
   The picture timing data the flicker fixer uses can be edited with
"PicassoModeTNG" which will store this data in the icon of the
P4_Flickerfixer driver. After starting the driver the timing parameters
will be made memory resident, so they will survive a reboot; every time you
open the boot menu ("Amiga early startup options") or boot from floppy disk
the flicker fixer will be using the new picture timing parameters. However,
if you switch off the Amiga these parameters will be lost. Before you can
use them again, the P4_Flickerfixer driver must be started again.