SIMPLE INTERNET

ADDRESS BOOK PROVIDER

for

Windows 95 and Windows NT

Version 1.0.1 Alpha

RELEASE NOTE

Boldon James Ltd.

10th February 1997

P5255/001

1. About This Release

- This is Version 1.0.1 alpha of the Boldon James Simple Internet Address Book Provider for Windows 95 and Windows NT (referred to in this release note as EMABLT).

- Introduction

EMABLT is a MAPI compliant Address Book service Provider and allows cc:Mail to retrieve recipient mail addresses from an Internet Directory  accessed via the Lightweight Directory Access Protocol (LDAP).

N.B. Windows 95 and NT4 users should view this document with Wordpad (with Option WordWrap=WrapToWindow), or MS-Word. NT3.51 users without MS-Word should open the file EMABLT.WRI (see below for where this is to be found) using MS-Write.

The release note has the following sections:

1.	About this Release

2.	Environmental Requirements

3.	Installation, Uninstallation and Configuration Instructions

4.	Further Information About this Release

5.	Pre-configuring Network Installations

6.	The Deliverables

7.	Customer Support Issues

Windows, Windows 95 and Windows NT are registered trademarks of Microsoft Corporation.

2.	Environmental Requirements

This release of EMABLT needs the following hardware and software:

2.1	Minimum Hardware Required

- EMABLT needs a personal computer which is capable of running either Windows 95 or Windows NT.

- 1.6MB disk space for the deliverables.

2.2	Internet Directory

EMABLT communicates with the Internet Directory over the LDAP protocol version 2.  The LDAP32.DLL software delivered with EMABLT is built from the version 3.3 of the LDAP source from the University of Michigan with support for T.61 characters included. The standard LDAP32.DLL released from the University of Michigan does not have T.61 included hence the version released with EMABLT must be used if T.61 character support required.

The host machine for your Internet Directory should provide the following:-

- An Internet Directory.

- LDAP server version 3.1 or higher.

2.3	Network Requirements

EMABLT needs the following TCP/IP software:

- Any TCP/IP stack that provides a Windows Sockets interface (WINSOCK). If Windows has been configured to run TCP/IP, this condition will normally be satisfied.

2.4	Other Software Requirements

- Microsoft Windows 95 or Windows NT (v3.51 with Service Pack 3, or v4.0) must be installed.

- The 32 bit MAPI subsystem (standard with Windows 95 and NT4). For NT3.51 MAPI Version 1.0a is required.  Boldon James can supply this on request.

- A 32 bit MAPI Client, e.g. cc:Mail for the Internet.

3.	Installation, Uninstallation and Configuration Instructions

3.1	Installing EMABLT

This release of EMABLT consists of two 3.5in high density (1.44MB) diskettes.

The MAPI subsystem must be installed prior to installing EMABLT. Always uninstall any previous version of the product before re-installing (see section 3.3 for instructions). Use either the Explorer shell, or Program Manager, as appropriate to the Windows version. Other shells may not function correctly.

The EMABLT installation program does the following:

- Copies the driver DLL’s into the Windows system directory.

- Copies support files into a directory of your choice (C:\Program Files\Emablt by default), including this document.

- Stores uninstall information in the Registry

- On NT3.51, creates a Program Manager group “EMABLT” to handle uninstallation.

- Allows you to add EMABLT to a MAPI profile.

3.1.1 Installing on Windows 95 or NT4

To install EMABLT, perform the following:

- Insert the EMABLT disk into drive A:

- Select the Start button, and then Settings, and Control Panel.

- Select Add / Remove Programs.

- Select Install from the first property page.

- Follow the instructions in the wizard, making sure that it locates the file A:\SETUP.EXE

Alternatively:

- Insert the EMABLT disk into drive A:

- Select the Start button, and then Run.

- Enter "A:\SETUP.EXE" without the quotes, and then click OK.

3.1.2 Installing on Windows NT3.51

To install EMABLT, perform the following:

- Move to "Program Manager" or "File Manager".

- Select "File" and then "Run".

- Enter the location of the EMABLT Install files, followed by "\SETUP.EXE".

- Click OK, and then follow the on screen instructions.

Alternatively, perform the following steps:

- From Program Manager, start "Control Panel".

- Select the "Mail & Fax" applet.

- Select a MAPI profile, if one is not already selected, and selected "Properties".

- Select "Add", and then "Have Disk".

- Follow the on screen instructions.

Once installed, the Program Manager group EMABLT will contain icons for uninstalling EMABLT, and for reading this document.

3.1.3 Adding EMAB to a MAPI profile

The installation process above describes how to add EMABLT to the list of available information services on a particular workstation. Before you can actually use EMABLT you must add it to an appropriate MAPI profile.

You can add EMABLT to a profile from the Control Panel Mail and Fax applet as follows:-

- Choose Show Profiles and select the required profile from the list of configured profiles.

- Choose Properties then Add.

- In the Add Service to Profile dialog select 'Internet Directory Access' from the list of available information services and choose OK.

Tip

If, after installation, you find that the Add Service To Profile listbox does not contain the “Internet Directory Access” option, or you want to change the defaults in EMABLT.INF and have them reflected in all future new profiles, switch to the Support directory as chosen above, and run, from a DOS shell:

BJMRGINI EMABLT.INF

This merges the EMABLT.INF file into the MAPISVC.INF file which is used whenever the “Internet Directory Access” provider is added to a MAPI profile.

3.2	Using the EMABLT Service Entry to configure EMABLT

You can configure EMABLT in two ways, as follows :

- Control Panel, using the 'Mail & Fax' applet.

- Cc:Mail, using Services item on the Tools menu which is on the File menu.

3.2.1	General

See your system administrator to gather the information for this sheet.

Server Hostname [required]

The name of the machine which is running your LDAP server. This can be a host name or a TCP/IP address.

Server Port Number[required]

This defines what port number the LDAP server is listening on. Default port is 389.

User Name

The distinguished name of the directory user for binding to the server. If blank, anonymous binding is attempted.  The format is as follows e.g.

cn=Joe Smith,ou=development,o=Lotus,c=us

Password

Password for authentication of the directory user. Leave blank if anonymous binding is permitted.

Search Base [required]

This specifies the level of the Internet Directory to use as the root for any search operations.  The format is as follows  e.g.

o=Lotus, c=us

For more information contact your directory administrator.

3.3	Uninstallation

Close down the cc:Mail client and any other MAPI compliant applications.

Any MAPI profile containing references to EMABLT will not be altered; consequently they will fail when used.  Edit these profiles via the “Mail and Fax Applet” and remove any reference to EMABLT.

The MAPI Profile editor will continue to see EMABLT as a service available to be added to profiles, because the file MAPISVC.INF still contains the EMABLT service. Either edit this file to remove the first line with EMABLT on, or, prior to uninstalling, in a DOS shell, change directory to the directory EMAB was installed in, and run “BJMRGINI EMABLT.INF -R”.

On Windows 95 and NT4, call up the Control Panel and select Add/Remove Programs. The Address Book will be seen in the list. Select with care and press Add/Remove. It will be removed.

On Windows NT3.51, run the Uninstall program from the icon in the EMABLT Program Manager group.

- Further Information About this Release

4.1	Performing a search with EMABLT

The EMABLT search engine uses a set of rules to search through the Internet Directory to find a particular entry. Having entered a name for resolution the EMABLT search engine looks through the Internet Directory structure searching for any entries that contain the component you entered.

The EMABLT help describes searching the Internet Directory for a mail address and displaying the properties associated with a matching entry. This can be found in the support files directory (EMABLT by default).

5.	Pre-configuring Network Installations

This section is for the use of mail administrators and developers. Other users may wish to skip this material.

The following describes how to configure the EMABLT installation disk images so that users can be configured as automatically as possible with company defaults.

5.1	Overview of Network Installation

The files on the release disk #1 include:

EMABLT.WRI/DOC	This release note, in uncompressed form.

EMABLT.INF		The EMABLT configuration file.

The document files can be replaced by corporate versions.

EMABLT.INF contains the default settings for an EMABLT profile. During installation, this file is copied to the support directory, and then merged with MAPISVC.INF - a file that MAPI uses to create profiles. Alter EMABLT.INF to change the default MAPI profile to match the corporate environment and Internet Directory usage.

After customising disk #1, copy both diskettes onto a network server under two folders at the same level , called “disk1” and “disk2”. Instruct users to run SETUP in the “disk1” folder, and then to configure a new profile, or add EMABLT to an existing profile, using the Control Panel applet. (It would be possible to construct a .PRF file from the information below, and run NEWPROF.EXE as an alternative - see the MAPI documentation).

5.2	Customising EMABLT.INF

EMABLT.INF is a standard text file. Use any convenient editor.

The file consists of several sections  - only [EMABLT] is of  interest. Restrict editing to the [EMABLT] entries that begin with numeric digits..

The lines in this section consist of 8-character hexadecimal ‘property tags’, followed by '=', and then the value corresponding to the property.

In each of the 8-digit values the trailing 2 digits indicate the type of data to MAPI:

1e - string (without quotes)

03 - long integer (8 numeric digits)

0b - boolean (value of 0100 means TRUE/ON, 0000 FALSE/OFF)

The remainder of this section will describe the tags and format of the values you need to enter in this section of the file. Default values are applied if the property is not present in the EMABLT.INF file. Section 5.3 contains the released EMABLT.INF file.

Property		Format

6600001e		This is the IP address or host name of the machine containing the LDAP server.  Default server.host.com.

6601001e		The port number that the LDAP server is listening on. Default 389.

6602001e		The distinguished name of the user. This value is not required if you allow anonymous binds. Default none – blank.

6603001e		The Search Base e.g. “o=boldon james limited, c=GB”. Default c=us.

6604001e		The Search Filter in RFC1777 format with %s allowed as a substitution token for the name to be searched for e.g. (|(cn=*%s*)(sn=*%s*)) to perform a contains search on common name or surname. Default cn=*%s*.

6605001e		The address type to be used by MAPI in message submission. Default SMTP.

6606001e		The E-Mail Attribute, e.g. mail, mhsOrAddresses or rfc822Mailbox, which is to be mapped to the MAPI PR_EMAIL_ADDRESS property. Default is mail.

6607001e		LDAP Time Limit for searching (in seconds). The maximum length of time to search the directory. A value of 0 means that the search will not be limited by time. Note that this will not necessarily supersede any system-wide limits defined on the server. Default is 60.

6608001e		LDAP Size limit for searching (in number of “hits”). The maximum number of matches to return. A value of 0 means that there is no limit to the number of matches. Note that this will not necessarily supersede any system-wide limits defined on the server. Default is 30.

6609001e		As 6607001e but for low bandwidth links. Default is 120.

660a001e		As 6608001e but for low bandwidth links. Default is 15.

660b001e		Log File (full pathname). Default None.

660c000e		Error Logging Levels , ON or OFF. Default is OFF.

660d000e		Diagnostic Tracing Levels, ON or OFF. Default is OFF.

660e001e		Boldon James detailed tracing levels.  Default is NONE.

660f001e		Output to debug Window, ON or OFF. Default is OFF.

6610001e		Attribute to be used within an Internet Directory entry for populating the Additional Information filed on the user mail details property sheet. Default is cn.

6611001e		Attribute to be used within the Internet Directory entry for populating the user Display Name. Default is cn.

5.3	An example EMABLT.INF

Items in italics are comments in this section. They should not be included in the EMABLT.INF file.

[Services]

EMABLT=Internet Directory Access		don’t alter this section

[Help File Mappings]

EMABLT Help=EMABLT.HLP		don’t alter this section

[EMABLT]

PR_DISPLAY_NAME=Internet Directory Access

Providers=PRO_EMABLT

PR_SERVICE_DLL_NAME=EMABLT.DLL

PR_SERVICE_SUPPORT_FILES=EMABLT.DLL

PR_SERVICE_DELETE_FILES=EMABLT.DLL

PR_SERVICE_ENTRY_NAME=ServiceEntry

PR_RESOURCE_FLAGS=SERVICE_SINGLE_COPY | SERVICE_NO_PRIMARY_IDENTITY

WIZARD_ENTRY_NAME=WizardEntry

Edit this part below

6600001e=server.host.com			server hostname

6601001e=389				port number

6602001e=						user name

6603001e=c=us				search base

6604001e=cn=*%s*				search filter

6605001e=SMTP				address type

6606001e=mail				email address source

6607001e=60					ldap time limit

6608001e=30					ldap size limit

6609001e=120				ldap time limit – low bandwidth

660a001e=15					ldap size limit – low bandwidth

660b001e=						path to log file

660c001e=OFF				error logging

660d001e=OFF				Diag tracing

660e001e=NONE				Trace Level

660f001e=OFF				output to debug window

6610001e=cn					additional info source

6611001e=cn					display name source

[PRO_EMABLT]				do not alter this section

PR_PROVIDER_DLL_NAME=EMABLT.DLL

PR_PROVIDER_DISPLAY=Internet Directory Access

PR_RESOURCE_TYPE=MAPI_AB_PROVIDER

6.	The Deliverables

EMABLT consists of the following software and documentation:

6.1	Software

Listed below are the files delivered into your Windows System directory and your supporting files directory. An entry of [no info] in the version column means that particular file has no version information. The software is virus checked before release.

6.1.1 Support Files

File				Size		Version			Date

emablt.hlp

emablt.inf

bjmrgini.exe

6.1.2	Windows System Files

File				Size		Version			Date

bjlog32.dll			36,864		3.2.0.0			Feb 10 1997-02-10

emablt32.dll		109,568	1.0.1.0			Feb 10 1997

ldap32.dll			159,232	3.3b1			Feb 10 1997

bjablr32.dll			28,160		1.0.1.0			Feb 10 1997

bjsrch32.dll		30,208		1.0.1.0			Feb 10 1997

mfc42.dll			1,013,520	4.2.6256		Feb 10 1997-02-10

msvcrt.dll			267,536	4.20.6201		Feb 10 1997

6.2 Documentation

EMABLT is released with the following documentation:

EMABLT.WRI - Boldon James MAPI X.500 Address Book Provider Release Note

EMABLT.DOC - The above document in Word 7 format

EMABLT.HLP - Boldon James Simple Internet Address Book Provider Help

- Customer Support Issues

If you have any support issues, or other queries about this product, please contact:

Customer Services Unit

Boldon James Ltd.

Brundrett House

Sandbach Road South

Alsager

Stoke-on-Trent. ST7 2LT

England

Telephone: +44 (0) 1270 844006

Facsimile: +44 (0) 1270 883631

Email:	support@bj.co.uk

X400:	s=support;o=Boldon James limited;p=bj;a=ospmail;c=gb

World Wide Web:	http://www.bj.co.uk