››››                    Atari XL OS RAM Upgrade by Russ Babylon›     ›     Modified for 1200XL by Kyle Dain›     ›     The following article shows how to modify an 800XL or 1200XL computer›     to allow any RAM based operating system to remain resident under any›     situation short of turning off the power to the computer. Not only›     will the RAM operating remain active it will also be uncorruptible,›     that is it can not be changed once it is enabled.  Sound interesting?›     ›     As with any project involving internal modification to your computer›     do not attempt this unless you are familiar with electronic circuits›     and soldering.›     ›     You will need one 74LS00 IC, a SPST subminature switch, a 5K resistor›     and a couple of feet of 30 gauge hook up wire.  At most a cost of two›     or three dollars.›     ›     To start the project first disassemble your XL and remove the metal›     shields from the circuit board.  Next locate the PIA chip, it is the›     40 pin chip marked U23 on both 800XL's and 1200XL's.  The PIA should›     have CO14795 or 6520 somewhere in the jumble of numbers on the top.›     ›     Most, if not all 1200XL's will have socketed chips.  If your chips are›     socketed, carefully remove the PIA from its socket and locate pin 10. ›     Pin 10 corresponds to bit 0 of memory location $D301.  CAREFULLY bend›     up pin 10 slightly so that it will not be in the socket and then›     reinsert the PIA into the socket.  If you have soldered chips then the›     easiest way to do the mod would be to carefully cut pin 10 from the›     circuit board with side cutters so no electrical connection existed›     between pin 10 of the PIA and the foil on the board.›     ›     Make SURE you leave enough of pin 10 to solder to. I do not like the›     idea of cutting traces on the circuit board but if you do and can›     trace them carefully enough more power to you.›     ›     Now solder about a twelve inch piece of hookup wire to pin 10 of the›     PIA.›     ›     On the 800XL, flip the board over and find where pin 10 used to be›     connected and solder another twelve inch length of hookup wire to this›     point.›     ›     On the 1200XL, solder about 8-10 inches of hookup wire to the solder›     pad just above the color adjust pot.  This pad will be at the lower›     right of the CPU chip (CO14806) just below pin 19.  If you can't find›     it, use the top pad of R48 instead.››››››››››››››››››››     Now for the next step; with the board right side up, locate the›     74LS375 chip.  It's U28 on the 800XL, and U11 on the 1200XL.  It is›     used to latch the R/W signal from the 6502 CPU. You need to locate pin›     14 of this chip and then flip the board over and solder about eight›     inches of wire to the back of the board where pin 14 connects.›     ›     On the 1200XL, you will also have to put a jumper from the R/W line to›     pin 15 of the 74LS375.  The best place to get the R/W signal is at the›     middle solder pad below U17 (74LS08).  Make this connection on the›     bottom of the board and make SURE you use the MIDDLE solder pad.  Take›     this jumper to pin 15 of the 74LS375 chip (U11).›     ›     You will notice that pin 14 of the 74LS375 has no foil connections to›     it since it is unused in a standard XL but we are going to make good›     use of it.›     ›     Carefully bend up all pins EXCEPT 7 and 14 on the new 74LS00 chip. ›     Stack this chip on top of another 14 pin 74LS chip (such as 74LS08)›     and solder pins 7 and 14 to the chip.  Don't over heat either chip!›     ›     OK, you have power to the chip and now need to hook everything›     together. Take the wire you have connected to pin 10 of the PIA and›     solder it to pin 1 of the 74LS00 chip.›     ›     Take the wire that was connected to where pin 10 of the PIA used to be›     and connect it to pin 8 of the 74LS00 chip.›     ›     Take the wire that you hooked to pin 14 of the 74LS375 chip and›     connect it to pin 13 of the 74LS00 chip.  On the 74LS00 chip itself›     connect pin 2 to pin 4, pin 4 to pin 5, pin 6 to pin 12, pin 3 to pin›     9 and pin 10 to pin 11.›     ›     You are almost home!  Now take the 5K resistor and trim it down and›     connect one side to pin 2, 4, or 5 of the 74LS00 chip and the other›     end to a +5v source, or to pin 14 of the 74LS00›     ›     Solder a small piece of wire to pin 2, 4, or 5 of the 74LS00 (where›     you put the resistor). The other end of this wire is hooked to one›     side or the other of the SPST switch.›     ›     On the other switch terminal connect a wire to any convenient ground›     point or pin 7 of the 74LS00 if none are to be found.›     ›     That completes the electrical work! Now you have a switch hanging in›     mid air looking for a home.››››››››››››››››››››››     For the 800XL, a good place is between the monitor output jack and the›     RF output.›     ›     For the 1200XL, there are many good places, but I put mine right above›     the channel select switch.  That will only work if your switch is›     small enough.›     ›     Drill a 1/4 inch hole in this area and mount the switch after the›     circuit board is installed in the bottom cover.›     ›     Now all you have to do is put it all back together.  The wires from›     the circuit board can be passed through any circuit board and metal›     shield openings being careful not to short or cut any wires or›     insulation.›     ›     The moment of truth is at hand!  With the SPST switch set so it is›     OPEN power up your computer.  It should act perfectly normally in any›     mode or executing any program.›     ›     Now for some fun load in a translator program and after it is in and›     running flip the SPST switch to close the contacts.  The computer›     should not be visibly affected.  Now push RESET and you will find that›     the translator is still there and operating.  Go into BASIC with the›     translator or other RAM operating system and try pokeing different›     values into the RAM area where your operating system resides and you›     find that you can't once you have closed the SPST switch.›     ›     This project has many possible uses. If you are proficient at machine›     language you can modify a RAM operating system to do all sort of nice›     things.›     ›     It could make an Omni-mon look sick. You can make a copy of your ROM›     based operating system except change the RESET vector at $FFFC and›     $FFFD. Install this system in RAM put the switch back in its normal›     position and boot up some picky piece of software that checks for›     custom or RAM based operating systems and wait until it loads.  Then›     close the switch and hit reset and you can go to and execute some›     utility program.  I have used this technique to get memory dumps of›     loaded programs.›     ›     The things you can do with this modification are only limited by your›     imagination.  This mod gives you almost total control of your›     computer.›     ›     Any questions, comments, or suggestions are gladly accepted.  Russ›     Babylon can be reached at the Ratcom BBS 437-9813 and leave a message›     for Big Russ.  Russ also can be reached from time to time on›     CompuServe 72327,404.  Kyle Dain can be reached on the XEP Net,›     CompuServe 72347,3014, or the S.A.G.E. BBS 814-833-4073›                                                                           ›