Author Bill Earle                                                                                                                 
       364 Eastgate Lane                                                                                                          
       Martinez, Ca 94553                                                                                                         
                                                                                                                                  
The following information describes the OS/2 Application Program                                                                  
Interface (API) calls. I have included information under the API                                                                  
column as follows:                                                                                                                
                                                                                                                                  
 F is a Family API (FAPI) call. This means that this call will also                                                               
   run under DOS 3.3, if assembled with the BIND program.                                                                         
                                                                                                                                  
 R means Restricted function. Refer to the OS/2 Technical Reference                                                               
   Manual for further info.                                                                                                       
                                                                                                                                  
I also have attempted to provide information to assist in porting old                                                             
programs over to OS/2. INT and SUBCODE columns provide the old DOS                                                                
interrupt and subcode functions. In some cases, these are approximations                                                          
of old DOS calls. Again, refer to the OS/2 Technical Reference Manual                                                             
for further information.                                                                                                          
                                                                                                                                  
API  INT  SUBCODE  FUNCTION         DESCRIPTION                                                                                   
 F                 BadDynLink       Called on bad dynamic link                                                                    
 R                 DosAllocHuge     Allocate memory greater than one                                                              
                                    segment                                                                                       
 R   21H  48H      DosAllocSegment  Allocate a segment of memory                                                                  
                   Dos AllocShrSeg  Allocate a shared-memory segment. The                                                         
                                    segment returned has a name that                                                              
                                    each process can access.                                                                      
 F                 DosBeep          Generate a sound frequency for the                                                            
                                    specified duration                                                                            
     21H  0DH,68H  DosBufReset      Flush the disk buffers for the                                                                
                                    requesting process                                                                            
 F                 DosCaseMap       Map a binary string into an ASCII                                                             
                                    string by using a DOS code-page                                                               
 F   21H  3BH      DosChdir         Set the current directory                                                                     
 F   21H  42H      DosChgFilePtr    Move a file's read/write pointer                                                              
 F                 DosCLIAccess     Request CLI/STI privilege before                                                              
                                    performing IN/OUT operations.                                                                 
 F   21H  3EH      DosClose         Close the file associated with the                                                            
                                    specified file handle                                                                         
                   DosCloseQueue    Close the queue specified for use by                                                          
                                    the calling process                                                                           
                   DosCloseSem      Close the semaphore specified for use                                                         
                                    by the calling process                                                                        
 F                 DosCreateCSAlias Create an executable alias descriptor                                                         
                                    (second name) for the data type                                                               
                                    descriptor received                                                                           
                   DosCreateQueue   Create and open the queue specified                                                           
                                    for use by the calling process                                                                
                   DosCreatSem      Create a semaphore for use by the                                                             
                                    calling process                                                                               
                   DosCreateThread  Create an asynchronous execution                                                              
                                    thread for the calling process.                                                               
                                    Threads are the OS/2 CPU scheduling                                                           
                                    entities.                                                                                     
 R   21H  4DH      DosCWait         Wait for a child process termination                                                          
                                    and get return code                                                                           
 F   21H  41H      DosDelete        Delete the file specified by the                                                              
                                    ASCIIZ name.                                                                                  
 F                 DosDevConfig     Return device information about                                                               
                                    attached devices                                                                              
 F   21H  44H      DosDevIOCtl      Communicate with an opened device                                                             
                                    handle                                                                                        
 F   21H  45H,46H  DosDupHandle     Return a duplicate DOS handle for the                                                         
                                    file handle provided                                                                          
                   DosEnterCritSec  Mark the entrance of a critical                                                               
                                    section of code and prevent the                                                               
                                    execution of other threads of code in                                                         
                                    the same process for concurrent                                                               
                                    processing synchronization                                                                    
 R                 DosError         Allow the calling process to receive                                                          
                                    OS/2 hard-error notification as                                                               
                                    Opposed to the OS/2 generation of a                                                           
                                    hard-error signal                                                                             
 R   21H  59H      DosErrorClass    Get extended error information.                                                               
 R   21H  4BH      DosExecPgm       Spawn a secondary program as a child                                                          
                                    process                                                                                       
 R   21H  00H,4CH  DosExit          Complete the current thread of                                                                
                                    information                                                                                   
                   DosExitCritSec   Mark the end of a critical section of                                                         
                                    code and enable other threads within                                                          
                                    the current process to execute again                                                          
                                    in a concurrent fashion                                                                       
                   DosExitList      Maintain the list (add,delete,modify)                                                         
                                    of routines that the current process                                                          
                                    is to execute upon completion                                                                 
 R   21H  5CH      DosFileLock      Lock or unlock a range of bytes within                                                        
                                    a file in support of file-sharing                                                             
                                    operations                                                                                    
 R                 DosFindClose     Close the handle associated with the                                                          
                                    file returned by a DosFindNext API                                                            
                                    service                                                                                       
 R   21H  4EH      DosFindFirst     Find the first file in a group of                                                             
                                    files matching the file specification                                                         
                                    provided                                                                                      
 R   21H  4FH      DosFindNext      Find the next file in a group of                                                              
                                    files matching the file specification                                                         
                                    provided in the call to DosFindFirst                                                          
                   DosFlagProcess   Set an external event flag that other                                                         
                                    processes can access for synchroniza-                                                         
                                    tion of concurrent processes                                                                  
                   DosFreeModule    Release the link to the dynamic link                                                          
                                    module specified by the module handle.                                                        
                                    This service decrements the usage                                                             
                                    for the specified module                                                                      
 F   21H  49H      DosFreeSeg       Release a previously allocated memory                                                         
                                    segemnt                                                                                       
 F                 DosGetCollate    Get the current collating sequence                                                            
                                    based upon the current code-page                                                              
     21H  66H      DosGetCP         Return the code-page in use by the                                                            
                                    current application                                                                           
 R   21H  38H      DosGetCtryInfo   Return country dependent formatting                                                           
                                    information                                                                                   
 F   21H  2AH,2CH  DosGetDateTime   Return the current date and time                                                              
     21H  65H      DosGetDBCSEnv    Return the DBCS vector for the                                                                
                                    specified country code                                                                        
 F                 DosGetEnv        Return the segment and offset address                                                         
                                    of the current process command envir-                                                         
                                    onment                                                                                        
 F                 DosGetHugeShift  Return the shift count used by                                                                
                                    DosAllocHuge to allocate memory larger                                                        
                                    than one segment                                                                              
                   DosGetInfoSeg    Return the address of the OS/2 system                                                         
                                    variables                                                                                     
 F                 DosGetMachineMode Return the current processor mode                                                            
                                    (real or Protected)                                                                           
 F                 DosGetMessage    Obtain the text from the system                                                               
                                    message file for the specified message                                                        
                                    and place it into a user-defined                                                              
                                    buffer                                                                                        
                   DosGetModHandle  Return a handle to a dynamic link                                                             
                                    module                                                                                        
                   DosGetModName    Get the complete DOS path name for the                                                        
                                    dynamic link module associated with the                                                       
                                    file handle provided                                                                          
                   DosGetProcAddr   Return the far address to the procedure                                                       
                                    specified within a dynamic link library                                                       
                   DosGetPrty       Return the priority of the current process                                                    
                   DosGetResource   Return the segment selector for the handle                                                    
                                    to the specified resource                                                                     
                   DosGetSeg        Obtain acces to the memory segment specified                                                  
                                    by the selector provided                                                                      
                   DosGetShrSeg     Obtain access to the shared memory segment                                                    
                                    specified by the name provided. The usage                                                     
                                    count of the segment is incremented                                                           
 F   21H  30H      DosGetVersion    Return the DOS version number                                                                 
                   DosGiveSeg       Allow the process specified by the process                                                    
                                    identification provided to access a shared                                                    
                                    memory segment                                                                                
 R                 DosHoldSignal    Enable/disable signal processing for the                                                      
                                    current process                                                                               
 F                 DosInsMessage    Place a text string into the body of a                                                        
                                    message                                                                                       
                   DosKillProcess   Terminate a process and return a termination                                                  
                                    code to the parent process or OS/2                                                            
                   DosLoadModule    Load the dynamic link module specified and                                                    
                                    return a handle.                                                                              
                   DosLockSeg       Lock a segment of memory marked as discard-                                                   
                                    able                                                                                          
                   DosMakePipe      Create a communications pipe for the calling                                                  
                                    process                                                                                       
                   DosMemAvail      Return the size of the largest block of                                                       
                                    memory available                                                                              
 F   21H  39H      DosMkDir         Create the specified directory                                                                
                   DosMonClose      Close the handle to a serial device that the                                                  
                                    process has been monitoring                                                                   
                   DosMonOpen       Open a handle to a serial device for device                                                   
                                    I/O monitoring                                                                                
                   DosMonRead       Wait for and return the input records to a                                                    
                                    serial device open for I/O monitoring                                                         
                   DosMonReg        Create input and output buffer structures                                                     
                                    for device I/O monitoring                                                                     
                   DosMonWrite      Write a data record to the output monitor                                                     
                                    buffer of a device open for I/O monitoring                                                    
 F   21H  56H      DosMove          Move a file from one location to another                                                      
                   DosMuxSemWait    Suspens the execution of the current thread                                                   
                                    until one or more semaphores have been                                                        
                                    cleared                                                                                       
 F                 DosNewSize       Change the size of the file associated with                                                   
                                    the specified file handle                                                                     
 R   21H  3CH,3DH  DosOpen          Open an existing file (if present) or create                                                  
                                    a file with the name specified by the ASCIIZ                                                  
                                    string provided                                                                               
                   DosOpenQueue     Open the queue specified by the ASCIIZ string                                                 
                                    provided for use by the current process                                                       
                   DosOpenSem       Open the semaphore specified by the ASCIIZ                                                    
                                    string provided for use by the current                                                        
                                    process                                                                                       
                   DosPeekQueue     Examine, but do not remove, an element from                                                   
                                    the specified queue                                                                           
                   DosPFSActivate   Activate the code-page and font specified for                                                 
                                    the printer. This activation only affects the                                                 
                                    calling process.                                                                              
                   DosPFSCloseUser  Notify the font-switching software that the                                                   
                                    process has closed its spool file. The font-                                                  
                                    switching software can release any related                                                    
                                    resources                                                                                     
                   DosPFSInit       Direct the font-switching software to init-                                                   
                                    ialize code-page switching and font-switching                                                 
                                    for the specified printer                                                                     
                   DosPFSQueryAct   Return the current code-page and font for the                                                 
                                    specified printer                                                                             
                   DosPFSVerifyFont Ensure that the code-page and font desired                                                    
                                    are supported by the specified printer                                                        
                   DosPhysicalDisk  Return partitioned disk information                                                           
 F                 DosPortAccess    Request or release access to a hardware port                                                  
                                    or ports                                                                                      
                   DosPtrace        Set a Ptrace buffer that is used in debugging                                                 
                   DosPurgeQueue    Delete all of the elements contained in the                                                   
                                    queue associated with the handle provided                                                     
                   DosPutMessage    Output the message provided to the file or                                                    
                                    device associated with a given file handle                                                    
 F   21H  47H      DosQCurDir       Return the current directory                                                                  
 F   21H  19H      DosQCurDisk      Return the current disk drive                                                                 
 R                 DosQFHandState   Query the state of the file associated with                                                   
                                    tha handle provided                                                                           
 F   21H  57H      DosQFileInfo     Return dat and time specifics about the file                                                  
                                    associated with the file handle provided                                                      
 F   21H  43H      DosQFileMode     Return the attribute byte for a specific file                                                 
 F   21H  36H      DosQFSInfo       Return information about the disk in the                                                      
                                    specified drive                                                                               
                   DosQHandType     Determine if the handle specified references                                                  
                                    a device or file                                                                              
                   DosQueryQueue    Return the number of elements in the specif-                                                  
                                    ied queue                                                                                     
 F   21H  54H      DosQVerify       Determine whether the specified queue is                                                      
                                    active or inactive                                                                            
 F   21H  3FH      DosRead          Read the specified number of bytes from the                                                   
                                    file associated with the file handle                                                          
                   DosReadAsynch    Read the specified number of bytes from the                                                   
                                    file associated with the file handle. The I/O                                                 
                                    operation occurs concurrently with the                                                        
                                    continued execution of the process                                                            
                   DosReadQueue     Read and remove an element from the specified                                                 
                                    queue                                                                                         
 R                 DosReallocHuge   Modify the size of a previously allocated                                                     
                                    huge (larger than 1 segment) section of                                                       
                                    memory                                                                                        
 R   21H  4AH      DosReallocSeg    Modify the size of a previosly allocated                                                      
                                    memory segment                                                                                
                   DosResumeThread  Restart a previously suspended thread of                                                      
                                    execution for the current process                                                             
 F   3AH           DosRmDir         Remove the directory specified by the ASCIIZ                                                  
                                    string                                                                                        
 F                 DosScanEnv       Search a process environment segment for a                                                    
                                    specified variable and return its value if                                                    
                                    found                                                                                         
                   DosSearchPath    Define a search path for data files                                                           
 F   21H  0EH      DosSelectDisk    Set the desired current drive                                                                 
                   DosSelectSession Select the desired foreground session                                                         
                   DosSemClear      Clear the specified semaphore                                                                 
                   DosSemRequest    Obtain a new handle to a new semaphore                                                        
                   DosSemSet        Set the semaphore associated with the handle                                                  
                                    provided                                                                                      
                   DosSemSetWait    Set the semaphore associated with the handle                                                  
                                    provided and suspend execution of the current                                                 
                                    thread until the semaphore is cleared                                                         
                   DosSemWait       Suspend execution of the current thread until                                                 
                                    the semaphore associated with the handle                                                      
                                    provided is cleared                                                                           
                   DosSendCtlC      Send a Ctrl-C signal to the lowest process in                                                 
                                    the tree of processes                                                                         
     21H  66H      DosSetCP         Set the code-page as specified for the call-                                                  
                                    ing process                                                                                   
 F   21H  2BH,2DH  DosSetDateTime   Set the current system date and time                                                          
 R                 DosSetFHandState Set the state of the file associated with the                                                 
                                    handle provided                                                                               
 F   21H  57H      DosSetFileInfo   Set the date information (last read, last                                                     
                                    write, creation, and so on) for the file                                                      
                                    associated with the handle provided                                                           
 F   21H  43H      DosSetFileMode   Set the attribute byte for the file assoc-                                                    
                                    iated with the file handle provided                                                           
 F                 DosSetFsInfo     Sets information for a file system  specified                                                 
                                    device                                                                                        
     21H  67H      DosSetMaxFH      Define the maximum number of file handles (up                                                 
                                    to 255) for the current process                                                               
                   DosSetPrty       Set the priority for the current thread                                                       
                   DosSetSession    Set the status of a child process                                                             
 R                 DosSetSigHandler Define a signal-handling routine for a                                                        
                                    specific signal                                                                               
 F   21H  25H      DosSetVec        Define an exception-handling routine for                                                      
                                    specified exeptions                                                                           
 F   21H  2EH      DosSetVerify     Enable or disable disk verification for the                                                   
                                    current process                                                                               
                   DosSleep         Suspend the current thread for a specified                                                    
                                    interval of time                                                                              
                   DosStartSession  Invoke a second application as an OS/2                                                        
                                    session                                                                                       
                   DosStopSession   Terminate a session previously invoked thru                                                   
                                    the DosStartSession                                                                           
 F                 DosSubAlloc      Allocate memory from within a segment                                                         
                                    previously allocated by DosAllocSeg or                                                        
                                    DosAllocShrSeg                                                                                
 F                 DosSubFree       Free memory previously allocated by                                                           
                                    DosSubAlloc                                                                                   
 F                 DosSubSet        Initialize a segment for suballocation, or                                                    
                                    change the size of a previously suballocated                                                  
                                    segment                                                                                       
                   DosSuspendThread Suspend the current thread of execution until                                                 
                                    a DosResumeThread service is invoked                                                          
                   DosSystemService Request OS/2 to perform a unique function                                                     
                                    (such as system-wide event notification for                                                   
                                    the specific process)                                                                         
                   DosTimerAsynch   Start a timer that runs asynchronously to the                                                 
                                    thread issuing the request. Upon completion                                                   
                                    of the time interval, this service sets the                                                   
                                    specified semaphore                                                                           
                   DosTimerStart    Start a periodic interval timer that runs                                                     
                                    asynchronously to the current thread. Each                                                    
                                    time the interval completes, the service                                                      
                                    clears the specified semaphore                                                                
                   DosTimerStop     Stop a periodic interval timer previously                                                     
                                    started by DosTimerStart or DosTimerAsynch                                                    
                   DosUnlockSeg     Unlock a memory segment previously marked as                                                  
                                    discardable                                                                                   
                   DosWait          Suspend the current process until the child                                                   
                                    process specified by the provided process                                                     
                                    identification terminates                                                                     
 F   21H  40H      DosWrite         Write the specified number of bytes to the                                                    
                                    file associated with the file handle                                                          
                                    provided                                                                                      
                   DosWriteAsynch   Write the specified number of bytes to the                                                    
                                    file associated with the file handle that is                                                  
                                    provided concurrently with the threads                                                        
                                    remaining processing                                                                          
                   DosWriteQueue    Place an element in a specified queue                                                         
 F   16H  00H      KbdCharIn        Return the character scan code from the                                                       
                                    standard input device                                                                         
                   KbdClose         Close a handle associated with a logical                                                      
                                    (unique to a process) keyboard                                                                
                   KbdCustCP        Install a user-definable custom keyborad                                                      
                                    translation table. The table only affects                                                     
                                    the keyboard handle provided                                                                  
                   KbdDeRegister    Remove a previously registered keyboard from                                                  
                                    the current session                                                                           
 F                 KbdFlushBuffer   Clear the keyboard buffer for a specific                                                      
                                    keyboard handle                                                                               
                   KbdFreeFocus     Release the logical-to-physical keyboard                                                      
                                    mapping produced by KbdGetFocus                                                               
                   KbdGetFocus      Join a logical (process unique) keyboard                                                      
                                    to a physical keyboard                                                                        
 F   16H  00H      KbdGetStatus     Return information about a specific logical                                                   
                                    keyboard                                                                                      
                   KbdGetXT         Obtain information from the current keyboard                                                  
                                    translation table                                                                             
                   KbdOpen          Open a logical keyboard and return a                                                          
                                    keyboard handle                                                                               
 R   16H  00H      KbdPeek          Return, but do not remove, a keyboard scan                                                    
                                    code if present in the keyboard buffer                                                        
                                    associated with the keyboard handle provided                                                  
                   KbdRegister      Register a keyboard subsystem for a specific                                                  
                                    session                                                                                       
                   KbdSetFgnd       Increase the priority of the foreground key                                                   
                                    board thread                                                                                  
                   KbdSetStatus     Set the size characteristics for a logical                                                    
                                    keyboard                                                                                      
                   KbdSetXT         Set the keyboard translation table for a                                                      
                                    logical keyboard                                                                              
                   KbdShellInit     Request the shell to identify itself to the                                                   
                                    keyboard routing software                                                                     
 F   21H  0AH      KbdStringIn      Read a character string from a logical keybd                                                  
                   KbdSynch         Synchronize access to the keyboard subsystem                                                  
                   KbdXlate         Translate a scan code into a shift state and                                                  
                                    ASCII code                                                                                    
                   MouClose         Close the mouse device handle for the current                                                 
                                    screen group                                                                                  
                   MouDeRegister    Remove a partially registered mouse subsystem                                                 
                                    for the current session                                                                       
     33H  01H      MouDrawPtr       Notify the mouse device driver that a screen                                                  
                                    area previously restricted from access is now                                                 
                                    available                                                                                     
                   MouFlushQueue    Direct the mouse device driver to purge the                                                   
                                    mouse event queue for the current session                                                     
                   MouGetDevStatus  Return the current mouse device driver                                                        
                                    settings                                                                                      
                   MouGetEventMask  Return the event mask for the current mouse                                                   
                                    device driver                                                                                 
                   MouGetHotKey     Return the specific mouse key used for input                                                  
                                    (left, middle, or right)                                                                      
                   MouGetNumButtons Return the number of buttons that the mouse                                                   
                                    driver supports                                                                               
                   MouGetNumMickeys Return the number of "Mickeys" per centimeter                                                 
                                    for the current mouse driver                                                                  
                   MouGetNumQueEl   Return the status of the event queue for the                                                  
                                    current mouse device driver                                                                   
     33H  03H      MouGetPtrPos     Return the current row and column of the                                                      
                                    mouse pointer shape                                                                           
                   MouGetPtrShape   Obtain the current mouse pointer shape                                                        
                   MouGetScaleFact  Return the current scaling factors for the                                                    
                                    mouse pointer shape                                                                           
                   MouInitReal      Initialize the mouse real-mode pointer                                                        
     33H  00H      MouOpen          Open a mouse device driver for the current                                                    
                                    screen group. Return a device handle                                                          
     33H  05H,06H  MouReadEventQue  Read and remove an event from the current                                                     
                                    mouse driver event queue                                                                      
                   MouRegister      Register a mouse subsystem for use with the                                                   
                                    current screen group                                                                          
     33H  02H      MouRemovePtr     Restrict a screen area from use by the mouse                                                  
                                    pointer                                                                                       
                   MouSetDevStatus  Set the current mouse device driver status                                                    
                                    flags                                                                                         
     33H  0CH      MouSetEventMask  Assign an event mask to the current mouse                                                     
                                    device driver                                                                                 
                   MouSetHotKey     Define which button (left, middle, or right)                                                  
                                    serves as the hot key for the current mouse                                                   
                                    driver                                                                                        
     33H  04H      MouSetPtrPos     Set the mouse pointer screen coordinates                                                      
     33H  09H,0AH  MouSetPtrShape   Set the mouse pointer shape                                                                   
                   MouSetScaleFact  Set the scaling factor for the mouse pointer                                                  
                                    shape                                                                                         
                   MouShellInit     Mouse shell indentifies itself to the mouse                                                   
                                    router                                                                                        
                   MouSynch         Direct mouse subsystems to synchronize access                                                 
                                    to the mouse device driver                                                                    
                   VioDeRegister    Remove a previously registered video subsystem                                                
                                    from a screen group                                                                           
                   VioEndPopUp      Remove a temporary window created by VioPopUp                                                 
                                    that is no longer required                                                                    
                   VioGetAnsi       Specify whether ANSI support is on or off for                                                 
                                    the current video buffer                                                                      
 F                 VioGetBuf        Return the address of the logical (process                                                    
                                    unique) video buffer specified                                                                
                   VioGetCP         Return the code-page used for display by the                                                  
                                    specified handle                                                                              
                   VioGetConfig     Return the current video display configuration                                                
 F   10H  03H      VioGetCurPos     Return the current row and column cursor                                                      
                                    position for the specified logical video buffer                                               
 F                 VioGetCurType    Return the cursor type and attributes for the                                                 
                                    specified logical video buffer                                                                
                   VioGetFont       Return the current font for the specified                                                     
                                    logical video buffer                                                                          
 F   10H  0FH      VioGetMode       Return the current video mode for the specified                                               
                                    logical video buffer                                                                          
 F                 VioGetPhysBuf    Return the address of the physical video buffer                                               
                   VioGetState      Return the current video states, or the palette                                               
                                    registers, the border color, or background                                                    
                                    intensity                                                                                     
                   VioModeUndo      Allow one process thread to cancel a                                                          
                                    VioModeWait service issued by another thread                                                  
                                    in the same process                                                                           
                   VioModeWait      Request that a graphics mode application be                                                   
                                    notified each time it needs to restore its                                                    
                                    video mode                                                                                    
                   VioPopUp         Allocvate a temporary popup display screen for                                                
                                    message display                                                                               
                   VioPrtSc         Print the current screen contents                                                             
                   VioPrtScToggle   The OS/2 session manager invokes this routine                                                 
                                    each time the user presses the Shift-PrtSc key                                                
                                    combination                                                                                   
 F   10H  08H      VioReadCellStr   Read a string of characters and attributes from                                               
                                    the screen starting at a specified row and                                                    
                                    column location                                                                               
 F                 VioReadCharStr   Read a character string from the display start-                                               
                                    ing at ther specified row and column                                                          
                   VioRegister      Register a video subsystem with a specific                                                    
                                    screen group                                                                                  
                   VioSavRedraw     Request that a process be notified when it must                                               
                                    save or redraw its contents                                                                   
                   VioSavRedrawUndo Allow one thread in a process to cancel a                                                     
                                    VioSavRedrawWait service issued by another                                                    
                                    thread within the same process                                                                
 F   10H  07H      VioScrollDn      Scrool the screen contents down as specified by                                               
                                    the row and column numbers and number of lines                                                
                                    to scroll                                                                                     
                   VioScrLock       Lock the screen and prevent I/O operations                                                    
 F                 VioScrollLf      Scroll the screen contents to the left as                                                     
                                    specified                                                                                     
 F                 VioScrollRt      Scroll the screen contents to the right as                                                    
                                    specified                                                                                     
 F   10H  06H      VioScrollUp      Scroll the screen contents up as specified by                                                 
                                    the row and column numbers and number of lines                                                
                                    to scroll                                                                                     
                   VioScrUnlock     Unlock the screen for I/O operations                                                          
                   VioSetAnsi       Enable or disable ANSI support for the                                                        
                                    specified logical video buffer                                                                
                   VioSetCP         Set the code-page for the specified logical                                                   
                                    video buffer                                                                                  
                   VioSetCurPos     Set the cursor position to the row and column                                                 
                                    of the logical video buffer provided                                                          
 F   10H  02H      VioSetCurType    Set the cursor type (attributes) for the                                                      
                                    logical video display provided                                                                
                   VioSetFont       Set the font for the logical video display                                                    
 F   10H  00H      VioSetMode       Set the display mode for the logical video                                                    
                                    display provided                                                                              
     10H  0BH      VioSetState      Set the state for the palette registers, border                                               
                                    color, or background intensity for the                                                        
                                    specified logical video display                                                               
 F                 VioShowBuf       Update the physical display with the contents                                                 
                                    of a logical display buffer                                                                   
 F   10H  09H      VioWrtCellStr    Write a character string (with attributes) to                                                 
                                    the specified video display location                                                          
 F   10H  0AH      VioWrtCharStr    Write a character string to the specified                                                     
                                    vidoe display location                                                                        
 F                 VioWrtCharStrAtt Write a character string using a repeated                                                     
                                    attribute to the specified video display                                                      
 F                 VioWrtNAttr      Write the character attribute to the video                                                    
                                    display at the specified location. This service                                               
                                    provides an optional repeat count                                                             
 F                 VioWrtNCell      Write a character or attribute to the video                                                   
                                    display the specified number of times                                                         
 F                 VioWrtNChar      Write a character to the video display starting                                               
                                    at the specified location and repeating the                                                   
                                    display n times                                                                               
 F   10   0EH      VioWrtTty        Write a character string to the video display                                                 
                                    starting at the current cursor position in TTY                                                
                                    mode