HERE IS THE OLD ROUTINE - DOESN'T PROPERLY SET UP ES FOR SCASB:
check_command_string proc near		
	push di
	cld				;Check for first quotation mark -
	mov al,'"'			; replace with null (20h) if present.
	mov di,82h			;Command tail starts at 82h.
	xor ch,ch
	mov cl,byte ptr ds:[080h]	;Length of command tail stored at 80h
	repne scasb
	jcxz end_check
	mov byte ptr [di-1],20h
			
	std				;Change direction & check for
	add di,cx			; last quotation mark.
	dec di
	dec di
	repne scasb
	jcxz end_check
	mov byte ptr [di+1],20h

end_check:
	cld 
	pop di
	ret
check_command_string endp



HERE IS THE NEW ROUTINE - DOES PROPERLY SET UP ES
;-------------------------------------------------------------------------------;Check_command_string removes first & last quotation marks from command
;string.  This lets xcall pass redirection request to COMMAND.COM. This
;routine saves ES & DI.
;-------------------------------------------------------------------------------
check_command_string proc near		
	push di
	push es
	mov ax,ds
	mov es,ax

	xor ch,ch
	mov cl,byte ptr ds:[080h]	;Length of command tail stored at 80h
	jcxz end_check			;All done if no command tail
	cld				;Check for first quotation mark -
	mov al,'"'			; replace with null (20h) if present.
	mov di,82h			;Command tail starts at 82h.
	repne scasb
	jnz end_check
	mov byte ptr [di-1],20h
			
	std				;Change direction & check for
	add di,cx			; last quotation mark.
	dec di
	dec di
	repne scasb
	cld 
	jnz end_check
	mov byte ptr [di+1],20h

end_check:
	pop es
	pop di
	ret
check_command_string endp