ASPI  Router  for  OS/2

 Daniel Dorau (woodst@cs.tu-berlin.de)

 Version 1.01  June 1997





Licence and Warranty


ASPI Router and the accompaning library are provided to you iAS ISj, without
warranty of any kind. You may use ASPI Router and the accompaning library
for free. The use of ASPI Router and/or the accompaning library implies that
you use it at your own risk and that you agree that the author (Daniel Dorau)
has no warranty obligations and shall not be liable for any damages arising out
of your use of this code, even if they have been advised of the possibility of
such damages. You are allowed to use/modify the library code and use it in your
own code together with the ASPI Router device driver.
   Furthermore you may freely distribute ASPI Router and the library as long
as you distribute it in the original non-modioed state together with this docu-
mentation and without taking any charge other than for making it available to
others.



                                 2





Contents


1  Overview                                                                3

   1.1  Why ASPI Router?   . . . . . . . . . . . . . . . . . . . . . . .   3

   1.2  Why ASPI?  . . . . . . . . . . . . . . . . . . . . . . . . . . .   4

   1.3  What does ASPI Router?   . . . . . . . . . . . . . . . . . . . .   4

   1.4  The ASPILIB library  . . . . . . . . . . . . . . . . . . . . . .   4

   1.5  Current limitations   . . . . . . . . . . . . . . . . . . . . . .  4


2  Interface to ASPI Router                                                4

   2.1  Opening the driver . . . . . . . . . . . . . . . . . . . . . . .   4

   2.2  Semaphore initialization   . . . . . . . . . . . . . . . . . . .   5

   2.3  Buffer initialization    . . . . . . . . . . . . . . . . . . . .   5

   2.4  Host adapter inquiry   . . . . . . . . . . . . . . . . . . . . .   6

   2.5  Get Device Type  . . . . . . . . . . . . . . . . . . . . . . . .   7

   2.6  Abort SRB  . . . . . . . . . . . . . . . . . . . . . . . . . . .   7

   2.7  Reset SCSI device  . . . . . . . . . . . . . . . . . . . . . . .   8

   2.8  Issuing SCSI commands  . . . . . . . . . . . . . . . . . . . . .   8

   2.9  Closing the driver   . . . . . . . . . . . . . . . . . . . . . .   9

   2.10 Summary of ASPI Rounter function codes   . . . . . . . . . . . .  10


3  The ASPILIB library                                                    10

   3.1  Initializing the library   . . . . . . . . . . . . . . . . . . .  10

   3.2  Using library funtions   . . . . . . . . . . . . . . . . . . . .  10

   3.3  Closing the library  . . . . . . . . . . . . . . . . . . . . . .  10


4  Other Information                                                      11

   4.1  People I want to thank   . . . . . . . . . . . . . . . . . . . .  11

   4.2  Contact, Reporting bugs  . . . . . . . . . . . . . . . . . . . .  11



1    Overview



1.1   Why ASPI Router?


In OS/2 it is not possible for Ring-3 applications to call OS2SCSI.DMD or OS2-
ASPI.DMD directly, therefore any application which wants to access the SCSI
bus has to provide its own driver to access the SCSI bus via OS2SCSI.DMD or
OS2ASPI.DMD. Since many users want to write their own SCSI applications but
shy away from writing their own driver, I decided to write a simple driver which
provides access to OS2ASPI.DMD for Ring-3 applications.  Since it only routes
SRBs (SCSI request blocks) to OS2ASPI.DMD I named it iASPI Routerj.



                                 3





1.2   Why ASPI?


Besides ASPI, in OS/2 there also exists the possibility to issue SCSI commands
through OS2SCSI.DMD. So why did I decide to use OS2ASPI.DMD?

I decided to use ASPI because a) it seemed to be easier to use for the
application developer as well as for the device driver developer (me) and b)
I hope that libraries for other platforms using ASPI can be ported more
easily.



1.3   What does ASPI Router?


The interface of ASPI Router merely is an extension of the interface of OS2-
ASPI.DMD which expects a SRB and a callback function to call when the SRB
was processed.  ASPI Router simply takes this SRB from your application via
DosDevIOCtl and calls OS2ASPI.DMD with this SRB after conversion of virtual
to physical addresses.  Additionaly, ASPI Router provides a callback function
for OS2ASPI.DMD. If this function gets called by OS2ASPI.DMD, ASPI Router
posts an event semaphore opened by your application before.  So before ASPI
Router can process the orst SRB, the application has to pass the handle of this
semaphore to the driver. ASPI Router closes its own handle of the semaphore
automatically when the application closes the driver.



1.4   The ASPILIB library


The accompaning library consisting of the oles aspilib.cpp, aspilib.h and
srb.h is intended as an example of how to use the ASPI Router device driver.
You may use this library or parts of it in your own programs or modify parts of
it so that it meets your requirements.



1.5   Current limitations


ASPI Router does not support scatter/gather or SRB linking.  The maximum
size of data transferred per SRB is 64K (=65536 bytes).  Only one applica-
tion can use this driver at a time.  Therefore you need to open it with the
OPEN_SHARE_DENYREADWRITE AEag to prevent other applications from opening
the driver while already in use.



2    Interface to ASPI Router


All functions of ASPI Router can be accessed with DosDevIOCtl after opening
the driver with DosOpen. The name of the driver handle is ASPIROU$.



2.1   Opening the driver


The driver can be opened with the following call:



                                 4





  ULONG rc;                                      // return value
  ULONG ActionTaken;                             // return value


  rc = DosOpen((PSZ) "aspirou$",                // open driver
                &driver_handle,
                &ActionTaken,
                0,
                0,
                FILE_OPEN,
                OPEN_SHARE_DENYREADWRITE |
                OPEN_ACCESS_READWRITE,
                NULL);



2.2   Semaphore initialization


Before any SRBs can be processed, ASPI Router needs a handle of an event
semaphore. ASPI Router will post this semaphore for every SRB which has been
processed. To create this semaphore and to send its handle to ASPI Router, the
following code can be used:


  ULONG  rc;                                   // return value
  USHORT openSemaReturn;                      // return value
  HEV    postSema;                             // event
                                                // semaphore
  unsigned long cbreturn;
  unsigned long cbParam;


  rc = DosCreateEventSem(NULL, &postSema,    // create event
                           DC_SEM_SHARED, 0);  // semaphore


  rc = DosDevIOCtl(driver_handle, 0x92,       // pass
                    0x03,                      // semaphore
                    (void*) &postSema,         // handle to
                    sizeof(HEV), &cbParam,    // driver
                    (void*) &openSemaReturn,
                    sizeof(USHORT), &cbreturn);


If ASPI Router could open the semaphore, openSemaReturn will be set to zero.
Otherwise an error occured.



2.3   Buoeer initialization


After passing the semaphore handle to the driver you still need to do one step
before you can issue SCSI commands. You have to initialize the buoeer. You have
to allocate a buoeer in your application where the driver can access the data to



                                 5





be transferred. The driver has not only to convert virtual to physical
addresses,
it also has to ensure that the virtual address is in physical memory (e.g.  not
swapped out) and that it does not change its position in physical memory. To
achieve this, it calls a helper function which locks the buoeer down in memory.
Another important point is that the buoeer must not cross a 64K-boundary in
physical memory. Your task is to allocate this buoeer and pass its address to
the driver. You can do this as follows:


  PVOID  buffer                                // our buffer
  ULONG  rc;                                   // return value
  USHORT lockSegmentReturn;                   // return value
  unsigned long cbreturn;
  unsigned long cbParam;


  rc = DosAllocMem(&buffer, bufsize,          // allocate the
                    OBJ_TILE | PAG_READ        // buffer at a
                    | PAG_WRITE                // 64K boundary
                    | PAG_COMMIT);
  rc = DosDevIOCtl(driver_handle, 0x92,       // pass buffer
                    0x04, (void*) buffer,      // pointer
                    sizeof(PVOID),             // to driver
                    &cbParam,
                    (void*) &lockSegmentReturn,
                    sizeof(USHORT), &cbreturn);


If DosDevIOCtl returns with a non-zero value of lockSegmentReturn some-
thing went wrong with locking the buoeer.



2.4   Host adapter inquiry


Do determine the number of host adapters available and to retrieve information
about them you can issue the iHost adapter Inquiryj command.  Refer to the
iStorage Device Driver Referencej [1] to get more information about it. Here is
an example:


  ULONG rc;                              // return value
  unsigned long cbreturn;
  unsigned long cbParam;


  SRBlock.cmd=SRB_Inquiry;              // host adapter inquiry
  SRBlock.ha_num=ha;                    // host adapter number
  SRBlock.flags=0;                      // no flags set


  rc = DosDevIOCtl(driver_handle, 0x92, 0x02,
                    (void*) &SRBlock, sizeof(SRB), &cbParam,



                                 6





                    (void*) &SRBlock, sizeof(SRB), &cbreturn);



2.5   Get Device Type


To get the device type there is the iGet Device Typej command. Refer to the
iStorage Device Driver Referencej [1] to get more information about it. Here is
an example:



  ULONG rc;                               // return value
  unsigned long cbreturn;
  unsigned long cbParam;


  SRBlock.cmd=SRB_Device;                // get device type
  SRBlock.ha_num=0;                      // host adapter number
  SRBlock.flags=0;                       // no flags set
  SRBlock.u.dev.target=id;               // target id
  SRBlock.u.dev.lun=lun;                 // target LUN


  rc = DosDevIOCtl(driver_handle, 0x92, 0x02,
                    (void*) &SRBlock, sizeof(SRB), &cbParam,
                    (void*) &SRBlock, sizeof(SRB), &cbreturn);



2.6   Abort SRB


With this command you tell OS2ASPI.DMD to abort the previous SRB. You have
to specify a second SRB with which you pass the address of the SRB to be
aborted to the driver. Aborting a SRB does not have to be successful. Watch
the status values and sense code of the SRB you aborted. For further information
about this command refer to the iStorage Device Driver Referencej [1]. Here is
an example:



  ULONG rc;                               // return value
  unsigned long cbreturn;
  unsigned long cbParam;


  AbortSRB.cmd=SRB_Abort;                // abort SRB
  AbortSRB.ha_num=0;                     // host adapter number
  AbortSRB.flags=0;                      // no flags set
  AbortSRB.u.abt.srb=&SRBlock;           // SRB to abort


  rc = DosDevIOCtl(driver_handle, 0x92, 0x02,
                    (void*) &AbortSRB, sizeof(SRB), &cbParam,
                    (void*) &AbortSRB, sizeof(SRB), &cbreturn);



                                 7





2.7   Reset SCSI device


A SCSI device can be reset with the iReset SCSI devicej command as described
in the iStorage Device Driver Referencej [1]. Here is an example:


  ULONG rc;                               // return value
  unsigned long cbreturn;
  unsigned long cbParam;


  SRBlock.cmd=SRB_Reset;                 // reset device
  SRBlock.ha_num=0;                      // host adapter number
  SRBlock.flags=SRB_Post;                // posting enabled
  SRBlock.u.res.target=id;               // target id
  SRBlock.u.res.lun=lun;                 // target LUN


  rc = DosDevIOCtl(driver_handle, 0x92, 0x02,
                    (void*) &SRBlock, sizeof(SRB), &cbParam,
                    (void*) &SRBlock, sizeof(SRB), &cbreturn);



2.8   Issuing SCSI commands


SCSI commands can be issued by sending ASPI SRBs (SCSI Request Blocks)
to the ASPI Router. The data structure deonition of the SRB and it's constant
deonitions can be found in srb.h. The cdb_st oeld has to be olled with a valid
SCSI command. Refer to the SCSI command reference [2] for a description of
the dioeerent SCSI devices and their commands. An example of sending a SRB
to ASPI Router follows below:


  ULONG rc;                                   // return value
  SRB   SRBlock;


  unsigned long cbreturn;
  unsigned long cbParam;


  SRBlock.cmd=SRB_Command;                   // execute SCSI
                                               // command
  SRBlock.ha_num=0;                           // host adapter
                                               // number
  SRBlock.flags=SRB_Read _ SRB_Post;         // data transfer,
                                               // posting enabled
  SRBlock.u.cmd.target=6;                    // Target SCSI ID
  SRBlock.u.cmd.lun=0;                       // Target SCSI LUN
  SRBlock.u.cmd.data_len=512*transfer;       // # of bytes
                                               // transferred
  SRBlock.u.cmd.sense_len=32;                // length of



                                 8





                                               // sense buffer
  SRBlock.u.cmd.data_ptr=NULL;               // pointer to
                                               // data buffer
  SRBlock.u.cmd.link_ptr=NULL;               // pointer to
                                               // next SRB
  SRBlock.u.cmd.cdb_len=6;                   // SCSI command
                                               // length
  SRBlock.u.cmd.cdb_st[0]=0x08;              // read command
  SRBlock.u.cmd.cdb_st[1]=1;                 // fixed length
  SRBlock.u.cmd.cdb_st[2]=(transfer >> 16)  // transfer
                            & 0xFF;            // length MSB
  SRBlock.u.cmd.cdb_st[3]=(transfer >> 8)   // transfer
                            & 0xFF;            // length
  SRBlock.u.cmd.cdb_st[4]=transfer & 0xFF;  // transfer
                                               // length LSB
  SRBlock.u.cmd.cdb_st[5]=0;


  rc = DosDevIOCtl(driver_handle, 0x92, 0x02,
                   (void*) &SRBlock, sizeof(SRB), &cbParam,
                   (void*) &SRBlock, sizeof(SRB), &cbreturn);


After the SRB is being processed you may read the status oelds out of the SRB
and decide whether the SRB was processed successfully or not.  Notice that
the oeld data_ptr is always set to NULL. Since you initialize the data buoeer
before any SRBs can be processed the driver knows the correct physical address
and inserts it automatically.  Note that the valid bit in sense data does not
always represent its current state. Refer to the target status oeld of the SRB
to determine whether the sense data is valid or not.



2.9   Closing the driver


After you're done you have to close the driver. The driver will close its
semaphore
handle and unlock the buoeer (otherwise you won't be able to free the memory).
Then don't forget to close the semaphore in your app and free the buoeer memory.
This shows how it can be done:



  ULONG  rc;                            // return value


  rc = DosCloseEventSem(postSema);    // close event semaphore
  rc = DosClose(driver_handle);        // close driver
  rc = DosFreeMem(buffer);             // free our buffer


Be careful to close the driver before you free the memory. Attempting to free
locked memory does not work.



                                 9





2.10   Summary of ASPI Rounter function codes


ASPI Router provides the following functions:


   _______________________________________________________________
   |_Category__Function__Description______________________________|

   | 92h       02h       Route SRB to ASPI driver                 |
   |                     The driver expects the address of a SRB. The|
   |                     'Data Buoeer Pointer' oeld needs not to be|olled.
   |                                                              |
   | 92h       03h       Pass semaphore handle                    |
   |                     The driver expects the pointer to an event|
   |                                                              |
   |                     semaphore handle to notify the application|that
   |                     a SRB has be processed.                  |
   |                                                              |
   | 92h       04h       Pass Data Buoeer Pointer                 |
   |                     The driver expects the pointer to a data buoeer.|
   |                     The buoeer must not cross a 64K-boundary.|
   |______________________________________________________________|



3    The ASPILIB library



The ASPILIB library is written as a C++ object to be used with (hopefully) any
C++ compiler. I developed it as an example library that shows how to use the
driver. Since I need it for my tape drive, only functions I need for this
application
are implemented. If you need additional functions, add them.



3.1   Initializing the library


First, create a variable of the object type scsiObj. Then you have to call the
init(ULONG bufsize) function to which you have to pass the size of the data
buoeer you wish to use.  Note that the maximum size supported by the driver
is 64K (=65536 bytes).  If the call returns with TRUE, all went ok, otherwise
something went wrong.



3.2   Using library funtions


After initializing the library you can use any public member functions of your
SCSI object.  Be careful to check if your calls return successful and check the
error codes or sense data if necessary.



3.3   Closing the library


Before you quit your application you have to close the library. This is done by
calling the close() function.



                                 10





4    Other Information


4.1   People I want to thank


Big thanks go to Alger Pike (acp107@psu.edu) who wrote the Hello World Device
Driver. Without this I wouldn't have known where to start.



4.2   Contact, Reporting bugs


If you use my driver and/or the library, please tell me what you think about it.
Furthermore you're welcome to report any bugs to me you encounter. My email
address is woodst@cs.tu-berlin.de.
If you want to use PGP for your email, you can retrieve my public key by sending
me a mail with send pgp key in the subject line.



References


[1] Storage Device Driver Reference, part of IBM's Device Driver Kit (DDK),
    freely available at http://service.boulder.ibm.com/ddk


[2] SCSI command reference, for those who have Internet access: I found one
    in the WWW at http://abekas.com:8080/SCSI2/



                                 11