Trace enhancements for FixPack 35















        

        
        



        July 9, 1998

        
        
        
        
        OS/2 Fix Distribution
        Personal System Products
        Austin, Tx
        
        
        
        
        
        (c) Copyright International Business Machines Corporation, 1997.
        All rights Reserved.

        July 9, 1998 - Warp Debug




                             July 9, 1998 - Warp Debug

        CONTENTS


          1.0 System Trace (SysTrace) facility  . . . . . . . . . . . . . 1
          1.1 Config.sys statements   . . . . . . . . . . . . . . . . . . 2
          1.2 Command Line Interfaces and Utilities   . . . . . . . . . . 4
            1.2.1 TRACE   . . . . . . . . . . . . . . . . . . . . . . . . 4
              1.2.1.1 TRACEPOINT CONTROL  . . . . . . . . . . . . . . . . 5
              1.2.1.2 CONTROL OPTIONS   . . . . . . . . . . . . . . . . . 9
              1.2.1.3 OPTIONAL DATA CONTROL  . . . . . . . . . . . . . . 10
              1.2.1.4 BUFFER CONTROL   . . . . . . . . . . . . . . . . . 10
            1.2.2 TRACE examples   . . . . . . . . . . . . . . . . . . . 11
            1.2.3 TRACEFMT   . . . . . . . . . . . . . . . . . . . . . . 13
            1.2.4 TRACEGET   . . . . . . . . . . . . . . . . . . . . . . 14
            1.2.5 TRSPOOL  . . . . . . . . . . . . . . . . . . . . . . . 15
            1.2.6 DTRACE   . . . . . . . . . . . . . . . . . . . . . . . 15
            1.2.7 MAPTSF   . . . . . . . . . . . . . . . . . . . . . . . 15
            1.2.8 SYSSPLIT   . . . . . . . . . . . . . . . . . . . . . . 18
              1.2.8.1 Trace formatting files - SYSTEM.TFF  . . . . . . . 19
            1.2.9 TDFLST   . . . . . . . . . . . . . . . . . . . . . . . 20
            1.2.10 TFFLST  . . . . . . . . . . . . . . . . . . . . . . . 20
          1.3 Appendix A New Tracepoints Cross-reference.    . . . . . . 21




































        
                                                               Contents  ii


                             July 9, 1998 - Warp Debug

        1.0 SYSTEM TRACE (SYSTRACE) FACILITY

        The system trace facility collects information about specific
        events to be logged into the trace buffer as they occur. While
        there are several uses for this information the main one is to
        assist in problem resolution.

        Enhancements have been made to:

        þ  Select process to be traced by process short name

        þ  Enablement of Dynamic Tracing at interrupt time

        þ  Allow Dynamic Trace to handle forwarded DLLs.

        þ  The 256 major code limit has been removed for Dynamic
           tracepoints. Static tracepoints will retain the restriction to
           maintain compatibility with the rest of the system.

        þ  The buffer can be grown dynamically (and without requiring a
           reboot) up to:

           -  5120 KB - from config.sys (TRACEBUF statement)

           -  Whatever is available - from a command line (TRACE function)

              Note: While not defined the upper limit will be somewhere
              around 384 MB. This is variable and based on the current
              state of the user's system.

        þ  Additional Buffer behavior

               The buffer will continue to be a wrapping buffer but the
               user now has the option to have logging to the buffer
               stopped when the buffer is full.

               A minimum size of 128k is imposed if a buffer is requested.
               The user should request a buffer large enough to avoid loss
               of data but small enough not to impact memory requirements.
               In practice a buffer size no larger than 1Mb should be
               suitable for most tracing requirements. If a larger capacity
               is required the TRSPOOL utility (described later) can be
               used as an alternative to defining a larger buffer.

               The buffer will be comprised of a series of 64KB segments.
               This will be transparent to the user and is done for
               efficiency purposes.

               Each trace record and buffer segment will be time-stamped.
               The buffer segment will contain a starting time-stamp that
               is set when the first record is written and an ending
               time-stamp that is originally allocated to zero and updated
               when:
               1. The system selects the next buffer segment,
               2. When TRACE OFF is entered
               3. When TRACE OFF /P:ALL is entered
               4. When TRACE /S is entered

        
                                        System Trace (SysTrace) facility  1


                             July 9, 1998 - Warp Debug

               5. When no-wrap mode is in effect and the last trace buffer
                  segment fills.

               Defaults for buffer options:
                   Wrapping (/M:W)
                   NonQueued (/M:NQ)
                   Do not use IPI. (/M:NODTI)
                   Buffer size = 128KB (will be set to 128 if anything less
                   than 128 is requested)




        1.1 CONFIG.SYS STATEMENTS

        The SysTrace facility has a config.sys statement (TRACEBUF) that
        allows the user to specify information about the trace buffer.
        While it is a good idea to specify this information so that it is
        available at startup time it is not required since there is a
        command line interface (TRACE ON /B:xxx) that can serve the same
        purpose.

        WARNING: There should be only one (1) TRACEBUF statement in the
        config.sys file. If there are more than one the buffer size from
        the last one will be used. The /M and /D parameters function in a
        cumulative manner so all of the requests in these functions will be
        set as they are processed. An example is:

                        TRACEBUF=128,/M:W,Q,DTI
                        TRACEBUF=512,/M:NW,NQ

                The result of the previous 2 statements would be:
                        TRACEBUF=512,/M:NW,NQ,DTI
                where:
                        512 - came from the last statement
                        NW - came from the last statement
                        NQ - came from the last statement
                        DTI - came from the first statement



        The syntax of this command is:      TRACEBUF=nnn [,/M] [,/D]

        þ  nnn - This mandatory field sets the size of the buffer (in KB).
           The size must be between 1 and 5120.

        þ  /M=<mode> - This specifies the mode of the buffer. There are
           several  acceptable values for <mode>and multiples can be
           provided if separated by a comma. They are:

           -  W or WRAP - Wrapping mode.

                  This specifies that the buffer will wrap when it is full.
                  This will cause the oldest data to be replaced with newer
                  data. While this does cause lost data it is the most
                  efficient way to see a current system activity. This mode
                  (W) will be used unless the non-wrapping mode is

        
                                        System Trace (SysTrace) facility  2


                             July 9, 1998 - Warp Debug

                  specified.

           -  NW or NOWRAP - Non-Wrapping mode

                  This specifies that the buffer will not wrap but will
                  suspend the SysTrace facility when the buffer is full.
                  While this will not overwrite data it also may not show a
                  current view of system activity.

           -  NQ or NOQUEUED - Non-Queued mode.

                  Trace records will be discarded if the trace facility is
                  busy at the time the write is attempted. This is not as
                  bad as it sounds since the SysTrace facility is efficient
                  in writing to the buffer and records are very seldom
                  discarded. This mode (NQ) will be used unless the Queued
                  mode is specified.

                  This option is provided for the case where tracing with
                  Queued Mode would sufficiently alter timing dependencies
                  of device drivers that handle interrupts from slow or
                  asynchronous devices. The recommendation is that QUEUED
                  mode be used unless a problem with I/O time-out or
                  performance occurs.

                  Note: When trace events are lost due to non-queue mode
                  being in effect then a "Lost Events" major code 0, minor
                  code 1 is generated and the next available opportunity.
                  This is done regardless of minor code 0 tracing being
                  active.

           -  Q or QUEUED- Queued mode.

                  This will cause trace records to be queued (held) if the
                  trace facility is busy. They will be written when the
                  facility is available. This will maintain the integrity
                  of the trace file but could have an adverse affect on
                  performance.

           -  DTI - DTI mode

                  Dynamic Trace uses Inter Processor Interrupt (IPI) for
                  single stepping tracepoints. While this may provide more
                  reliable trace data it also locks out all of the other
                  processors on a SMP system. This option should only be
                  used when necessary because of the performance impact.

                  Note: DTI mode only takes affect on SMP systems. It will
                  be overridden for certain tracepoints that occur within
                  Ring 0 code to avoid deadlocks from occurring.

           -  NODTI or NDTI- Non-DTI mode

                  Dynamic Trace does not use IPI. This mode will be used
                  unless the DTI mode is specified.

        þ  /D=<optional data> - This specifies what optional system data

        
                                        System Trace (SysTrace) facility  3


                             July 9, 1998 - Warp Debug

           will be captured, if available. Acceptable values for <optional
           data> are:

           -  PROCNAME - Capture the short name for the process

           -  TID - Capture the Task ID

           -  SLOT - Capture the Thread's Slot

           -  CSEIP - Capture the caller's CS:EIP

              Note: Will not be collected if trace is called directly
              through the kernel interface (K_S_Systrace).

           -  SSESP - Capture the caller's SS:ESP

              Note: Will not be collected if trace is called directly
              through the kernel interface (K_S_Systrace and K_D_SysTrace).

           -  TSC - Capture Pentium High Resolution Time-Stamp counter.
              This will be ignored (no error) if not supported by the
              hardware.

           -  ALL - Capture all of the optional data

           -  NONE - No optional data will be captured. This is the default
              if the /D parameter is not specified.





        1.2 COMMAND LINE INTERFACES AND UTILITIES




        1.2.1 TRACE

        The Trace command line interface has been enhanced to allow the
        user to turn on Trace for a specific module by its shortname,
        allocate or de-allocate the trace buffer, set the type of trace
        buffer that is required (wrapping or non-wrapping), and query the
        trace facility for its current status.

        All existing options will function as they currently do. The format
        of the command with a discussion of the enhancements follows:

         TRACE [ON|OFF] [major_code_spec | (minor_code_spec) | tdf_spec |
         (minor_code_spec) | (event_type_spec) | tdf_keyword |
         (minor_code_spec) | (event_type_spec) | /P:pid_spec |
         /N:<process  name>] [/S] [/R] [/C] [/B:<size of buffer in KB>]
         [/M:<mode>] [/D:<optional data>] [/Q]



        The following sections illustrate parameters that are valid for

        
                                        System Trace (SysTrace) facility  4


                             July 9, 1998 - Warp Debug

        functions provided by the TRACE command.

        Note: If "TRACE" is used without any parameters help information
        will be returned showing the proper syntax of the command.




        1.2.1.1 TRACEPOINT CONTROL

         TRACE ON|OFF {[major_code_spec [(minor_code_spec)]..} [/R|/S] [/C] [/Q]
         TRACE ON|OFF {[module_spec [(event_type_spec)]..} [/R|/S] [/C] [/Q]
         TRACE ON|OFF {[tdf_spec [(event_type_spec)]..} [/R|/S] [/C] [/Q]
         TRACE ON|OFF [KERNEL [(event_type_spec)] [/R|/S] [/C] [/Q]
         TRACE ON|OFF /N:<process name> [/R] [/S] [/C] [/Q]
         TRACE ON|OFF /P:pid_spec [/R] [/S] [/C] [/Q]


        þ  ON - The specified tracepoints are turned ON. This has a
           cumulative effect and does not affect tracepoints that are
           already on.

        þ  OFF - The listed tracepoints (All tracepoints if none are
           listed) are being turned OFF.

        þ  major_code_spec - A tracepoint major code. The following major
           code ranges have been defined.
           -  0 - 244        Static and Dynamic trace for IBM use
           -  245 - 255      Static and Dynamic for User use.
           -  256 - 32767    Dynamic Trace for IBM use.
           -  32768 - 65535  Dynamic Trace for User use.

        þ  minor_code_spec - A list of ranges of minor codes

           Note: More than one major_code_spec with minor_code_spec may be
           specified.

        þ  module_spec - The module name for which an associated trace
           definition file (TDF) exists.

           Note: The associated TDF assumes the same name as the module.
           The TDF file is located by searching in the following order:
           -  in the current directory
           -  in DPATH
           -  in \OS2\SYSTEM\TRACE
           -  in \OS2\SYSTEM\TRACE\SYSTEM.TDF
           -  in the load module directory
           -  for base device drivers also in the root directory of the
              boot drive.

           If the TDF specifies that the DLL is a fowarder DLL then the
           forwarded DLL is searched for in the current directory and
           LIBPATH if not already loaded.

        þ  event_type_spec - A list of minor code ranges, groups and types.

               If TRACE cannot find a module specified in module_spec then

        
                                        System Trace (SysTrace) facility  5


                             July 9, 1998 - Warp Debug

               tdf_spec is assumed and TRACE searches directly for a TDF of
               the name specified in the order specified above.  The module
               name is then derived implicitly from the name specified
               within the TDF.

               If KERNEL is specified then \OS2\SYSTEM\TRACE\OS2KRNL.TDF is
               assumed with module OS2KRNL (or DOSCALLS.DLL).

           Note: More than one module_spec with event_type_spec may be
           specified.

        þ  /N:<process name> - This will allow the user to control tracing
           by the name of a module. More than one name can be entered as
           long as they are separated by a comma. An example is
           /N:name1,name2.

               This provides an alternate method of turning on Trace when
               the PID is not known. This parameter is valid when turning
               Trace ON or OFF but not valid if /P is also specified.

               NOTE: Verification of the name will follow the same method
               as DosExecPgm. They are:

               1. If a path is specified, no search is performed. The name
                  is registered even if it does not exist so that tracing
                  will be started when the process is added to the system.
                  Trace events will be logged only if the process exists
                  when tracing is started.

               2. If a name is specified with an extension but no path, an
                  attempt is made to find the process by searching the
                  current directory. If not found in the current directory,
                  the directories specified in the PATH statement (in
                  config.sys) are searched.

               3. If a shortname is specified (no path, no extension), .exe
                  is assumed as the extension and the method specified in
                  method 2 is used.

        þ  /P:<pid_spec> - This allows the user to specify a PID number.
           By default ALL pids are on.

        þ  /R - This resumes tracing if tracing was previously suspended.

        þ  /S - This suspends tracing.

        þ  /C - This clears the trace buffer.

        þ  /Q -  Returns the state of the Trace facility. Information will
           be returned on all of the tracepoints and will include:

               Suspend command if the Trace facility is currently
               suspended.

               Buffer Size

               Buffer collection mode (W or NW, Q or NQ, etc)

        
                                        System Trace (SysTrace) facility  6


                             July 9, 1998 - Warp Debug

               Optional Data being captured

               PIDs being traced

               Tracepoints currently ON -  No group names will be
               displayed; all tracepoints turned on as a result of using a
               group name will be displayed.

           Note: /Q is valid with or without other keywords.



        Note: If "TRACE OFF" is used without any parameters ALL tracepoints
        will be turned off.


        The TRACE command provides additional flexibility of the previous
        versions in the way it processes TDFs:

            TRACE OFF is now valid with a full tdf_spec or module_spec.
            This allows individual and groups of tracepoints to be
            selectively removed.

            TRACE no longer requires the TDF name to match the module name,
            thus there is no longer a need to rename OS2KRNLD.TDF to
            OS2KRNL.TDF when using the ALLSTRICT kernel. Tracepoints would
            be activated by specifying TRACE ON OS2KRNLD

            The TRACE command will merge tracepoints with those already
            activated when making repeated invocations that apply
            tracepoints to the same load module. Thus in the case of
            PMWIN.DLL, PMGRE.DLL and PMSHAPI.DLL, each of which is a
            forwarder DLL and has its tracepoints located in PMMERGE.DLL,
            their tracepoints may be applied cumulatively with three
            invocations thus:
                TRACE ON PMWIN
                TRACE ON PMGRE
                TRACE ON PMSHAPI.

            Previous versions of the SYSTRACE facility did not permit this.

        For added serviceability: tracepoints definitions have been
        provided for internal kernel interfaces. Each tracepoint records
        32-bytes of stack on entry to the given routine. These definitions
        are mainly intended for service personnel, however the following
        may be of use to developers writing virtual device and file system
        drivers:

            TRACE ON KRNLxFS(FSH) will trace File System Helper calls.
            TRACE ON KRNLxVDM(VDH) will trace Virtual Device Helper calls.

            Note: In the above two commands "x" should be replaced with "R"
            when using the RETAIL kernel, "B" when using the HSTRICT kernel
            and "D" when using the ALLSTRICT kernel.

        Other kernel trace definitions provided are:


        
                                        System Trace (SysTrace) facility  7


                             July 9, 1998 - Warp Debug

           KRNLxTK:     Tasking and Scheduler   TK, SCH, VR, XCPT,
                                                SYSSERV, KM, SCI, SIG
           KRNLxSEM:    Semaphore               SEM, KSEM, MUX, RAM, SYSSEM,
           KRNLxPG:     Page Manager            PG
           KRNLxSM:     Swapper Manager         SM
           KRNLxVM:     Virtual Memory Manager  VM BMP RMP
           KRNLxSEL:    Selector Manager        SEL
           KRNLxTOM:    Timer Manager           TOM TIM
           KRNLxLDR:    Loader                  LDR
           KRNLxVDM:    Virtual Dos Machines    VDH EM86 DEM VDM VPM
           KRNLxFS:     File System             FSH DIR EA FAT FCB FNotify
                                                FSD MFT SF VPB
           KRNLxDEV:    Device and IO           DEV IO DRIVE DSK dh PSD
           KERNEL:      Spin Lock APIs          LOCK (SMP Only)
           DOSCALL1:    Spin Lock APIs          LOCK (SMP Only)
           DOSCALL1:    Quecalls APIs           QUE
           DOSCALL1:    Universal Thunks        UT
                *** Normally this should be turned off if tracing ALL APIs due to the
                    large number of additional trace entries it will cause.
                    So if you do:
                        TRACE ON DOSCALL1
                     you should also do:
                        TRACE OFF DOSCALL1(UT).

        Each of these tracepoints in these TDFs have type specifications
        as follows:

           PRE  - Entry point
           POST - Exit point (currently not defined)
           PRIV - Routines private to a component
                  (name begins with a lower case character)
           PUB  - Routines exported to other kernel components
                  (name begins with an upper case character)


        WARNING: Do not use DTI mode with any of the above KRNLxxxx
        tracepoints on SMP systems that have 3 or more processors. This is
        because there is an exposure to a 3-way deadlock arising from
        tracepoints placed in ring 0 code that owns non-interruptable spin
        locks.

        Note: In general when tracing system APIs it is recommended that
        KERNEL and DOSCALL1 groups be specified together. This is because
        for some APIs, processing is are split between DOSCALL1 and
        OS2KRNL. Some information is traced at the DOSCALL1 interface and
        the rest at the OS2KRNL interface.

        Similarly, TRACE ON DOSCSALL1(QUE) should be used with TRACE ON
        QUECALLS to obtain complete information pertaining to QUECALLS API
        tracing.

        New trace definitions have been added for exported interfaces to
        the following modules:





        
                                        System Trace (SysTrace) facility  8


                             July 9, 1998 - Warp Debug

           Module       Tracepoint Groups

           HPFS.IFS     -
           CDFS.IFS     -
           PMWP.DLL     WIN WP SHL NWI
           PMVIOP.DLL   VDM WIN VIO
           PMVDMP.DLL   VDM DOS

        Each of these tracepoints in these modules have type specifications
        as follows:

           PRE  - Entry point
           POST - Exit point (currently not defined)
           PRIV - Routines private to a component
                  (name begins with a lower case character)
           PUB  - Routines exported to other kernel components
                  (name begins with an upper case character)



        All System API tracepoints have been updated to include the
        caller's return address. To facilitate this, all APIs that have a
        thunking interface in DOSCALL1 have a corresponding tracepoint
        defined their entry module to allow the caller's return address to
        be recorded. This applies to QUECALLS, SESMGR and KERNEL.

        For example: 32-bit programs calling DosSleep enter DOSCALL1 at
        DOS32SLEEP and then the KERNEL at DOSSLEEP, whereas 16-bit programs
        calling DosSleep make a direct call to the Kernel at entry point
        DOSSLEEP. The DOSSLEEP tracepoint in the Kernel records the
        paramters and 16-bit return address. This should be used in
        conjunction with the DOS32SLEEP tracepoint in DOSCALL1 to record
        the return address to an original 32-bit caller.

        The Fast Safe RAMSEM APIs have been enhanced to record parameters
        and details of the semphore.

        From Fix Pack 37, DOS32RAISEXCPETION will record parameters and
        format the Exception Report Record.

        From Fix Pack 37, DOS32R3EXCEPTIONDISPATCHER,
        DOS32EXCEPTIONCALLBACK and XCPTEXECUTEUSEREXCEPTIONHANDLER have
        been added to DOSCALL1's EXMG tracepoint group. These record
        Exception Context, Registration and Report Records during the
        dispatching of user exception handler's.

        For a full list of the new API tracepoints to the KERNEL, DOSCALL1
        and SESMGR, see Appendix A below.



        1.2.1.2 CONTROL OPTIONS

         TRACE [/R | /S] [/C] [/Q]




        
                                        System Trace (SysTrace) facility  9


                             July 9, 1998 - Warp Debug

        These options can be used with the ON parameter.  However, these
        must follow all of the parameters of the ON parameter.

        þ  /R - This resumes tracing if tracing was previously suspended.

        þ  /S - This suspends tracing.

        þ  /C - This clears the trace buffer.

        þ  /Q -  Returns the state of the Trace facility. This is the same
           as previously defined in the "TRACEPOINT CONTROL" section.




        1.2.1.3 OPTIONAL DATA CONTROL

         TRACE ON | OFF [/D:<optional data>]


        þ  ON - The specified optional data will be collected. This has a
           cumulative effect.

        þ  OFF - The specified optional data will no longer be collected.

        þ  /D:<optional data> - This specifies what optional system data
           will be captured.

               This is used with the ON  or OFF keywords and is valid only
               when a buffer has been allocated.  This informational is
               GLOBAL to the trace facility and not set on a per tracepoint
               basis. Multiple entries are separated by a comma.

               Values and behavior will be the same as previously defined
               in the TRACEBUF config.sys statement.

               The data will only be collected if available.




        1.2.1.4 BUFFER CONTROL

         TRACE ON /B:<buffer size in KB> [/M:xxx] [/R | /S] [/D:<optional data>]
         TRACE OFF /B


        þ  ON - The buffer will be allocated using the specified options.

        þ  OFF - The buffer will be deallocated.

        þ  /B:[<buffer size>] - This sets the size of the buffer (in KB) if
           used with the ON keyword and deallocates the buffer (no size
           allowed) if used with the OFF keyword.

               When used with the ON keyword.


        
                                       System Trace (SysTrace) facility  10


                             July 9, 1998 - Warp Debug

                   The buffer size must be numeric.

                       Minimum Value = 1, Maximum value is unlimited (An
                       error will be returned if the buffer can not be
                       allocated. A value of 128 or less will cause a 128KB
                       buffer to be allocated.

                       After the first 128KB, the size will be rounded up
                       to the next multiple of 64KB so that the proper
                       number of buffers can be created.

               When used with the OFF keyword.

                   No size is allowed. The parameter will be simply /B.
                   When the buffer is deallocated the following happens:

                   The buffer is deallocated causing all data to be
                   cleared.



        þ  /M:<mode> - This specifies the mode of the buffer and will be
           accepted if a buffer is allocated. Values and behavior will be
           the same as previously defined in the TRACEBUF config.sys
           statement.

        þ  /R - This resumes tracing if tracing was previously suspended.

        þ  /S - This suspends tracing.

        þ  /D:<optional data> - This specifies what optional system data
           will be captured.

               This is used with the ON  or OFF keywords and is valid only
               when a buffer has been allocated.  This informational is
               GLOBAL to the trace facility and not set on a per tracepoint
               basis. Multiple entries are separated by a comma.

               Values and behavior will be the same as previously defined
               in the TRACEBUF config.sys statement.

               The data will only be collected if available.


        NOTE: The buffer options (/B:, /M:, and /D:) will be used until the
        system is booted. If you want the options to be more permanent they
        can be specified in the config.sys file (TRACEBUF statement).



        1.2.2 TRACE EXAMPLES


        Allocate a wrapping 320KB trace buffer.

            TRACE ON /B:320 /M:W


        
                                       System Trace (SysTrace) facility  11


                             July 9, 1998 - Warp Debug

        Note: An error will be returned if the buffer is already allocated.

        Allocate a wrapping 320KB trace buffer using default values where
        possible (Wrapping mode) and specify what optional data (shortname
        and SS:ESP) to capture.

            TRACE ON /B:320 /D:PROCNAME,SSESP

        Allocate a wrapping 320KB trace buffer and put the Trace facility
        in suspended mode. No tracing will be possible until the user puts
        the trace facility in the resume mode.

            TRACE ON /B:320 /M:W /S

        Deallocate a previously allocated trace buffer.

            TRACE OFF /B

        Note: This command will not affect any optional system data or
        tracepoints that have been previously defined. When the buffer is
        next allocated (TRACE ON /B:xxx) the optional data and tracepoints
        when again be active.


        Change the optional system data that is being collected to be ALL
        possible data.

            TRACE ON /D:ALL

        Change the optional system data that is being collected to NOT
        collect the TID.

            TRACE OFF /D:TID


        Enable for All available major codes. However, major code 1 is used
        for performance testing and will only be enabled if a DEKKO card is
        present in the hardware.

            Trace ON

        Enable for major code 13.

            Trace ON 13

        Enable for doscall1.

            Trace ON DOSCALL1

        Enable for processes (ffst and notes)

            TRACE ON /N:ffst,notes


        The format for the command to stop tracing is the same as enabling
        tracing except for the keyword. The keyword used to stop tracing is
        OFF. The following command would stop tracing for major codes 6 and

        
                                       System Trace (SysTrace) facility  12


                             July 9, 1998 - Warp Debug

        13.

            TRACE OFF 6,13

        Note: If TRACE OFF is used without any other parameters ALL
        tracepoints will be turned OFF.


        Suspend Tracing

            TRACE /S

        Resume Tracing

            TRACE /R

        Clear the Trace buffer. Tracing must be suspended or disabled for
        this option to be valid.

            TRACE /C

        Query the Trace facility.

            TRACE /Q

        If the TRACE facility was ON (for major codes 3,4, and 5) with a
        wrapping buffer of 256K this would return (all parameters will be
        displayed even if they could have been defaulted) the following:

            TRACE ON /B:256 /M:W
            TRACE ON 3,4,5

        The commands will be broken into a series of commands if the
        command goes longer than 80 characters. The first command (no
        longer than 80 characters) will have buffer information and
        tracepoints that are ON while the rest of the commands will only
        have tracepoints. EXAMPLE: If tracepoints 4-30 are on with a 512KB
        non-wrapping buffer the data returned would be:

            TRACE ON /B:512 /M:NW
            TRACE ON 4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,19,20,21,22
            TRACE ON 23,24,25,26,27,28,29,30

        NOTE: If you turn on tracepoints using GROUP names the QUERY will
        return everything that was turned on (not the group name).



        1.2.3 TRACEFMT

        The Tracefmt command starts the trace formatter which provides a
        user interface to the trace buffer. It has been enhanced to:

        þ  Display the System Optional Data

        þ  The Processor ID (CPU ID) has been added to the Select...
           (Search) function (under VIEW action bar item) so that only the

        
                                       System Trace (SysTrace) facility  13


                             July 9, 1998 - Warp Debug

           records for a single Processor can be displayed.

        þ  An option has been added to allow unformatted data to be
           displayed in dump format (Hex and ASCII). This new option
           "Display in Dump Format" is under the VIEW action bar item. It
           will toggle on and off the same as the other display options.
           This will not affect data that is subject to a formatting
           control (except for %U).

        þ  The default display type has been changed to the new Dump
           format. This will be used for data if formatting instructions
           have not been provided.

        þ  There is a new command line switch (/f=output_file_name) that
           allows the formatted output to be directed directly to an output
           file.  When /f is specified TRACEFMT will close as soon as the
           input trace data has been formatted and written to the output
           file.  The full syntax for the TRACEFMT command is:

           TRACEFMT <input> </t=tff_path> </f=output>


           where:

                  <input> specified either a RAW trace buffer (from TRACEGET or
                          TRSPOOL) or an unformatted trace file saved by TRACEFMT.

                  </t=tff_path> specifies the TFF path name. This defaults to
                          \OS2\SYSTEM\TRACE

                  <f=output> specifies the output formatted file name.




        1.2.4 TRACEGET


        The TRACEGET command will extract the System Trace buffer and
        save it in a file. The command syntax is :

        TRACEGET file



        where:

        file    - The name of the file where the buffer will be written.










        
                                       System Trace (SysTrace) facility  14


                             July 9, 1998 - Warp Debug

        1.2.5 TRSPOOL


        TRSPOOL extends the usefulness of the OS/2 system trace facility
        by capturing the system trace buffer and spooling it to a
        cyclically used sequence of disk files (named TRACEBUF.nnn,
        where nnn is a sequential number starting with 000).  The
        captured trace disk files may be later formatted using TRACEFMT,
        by selecting the Open option of the File menu.

        For information about this utility please see the file
        TRSPOOL.DOC in the OS2\SYSTEM directory.



        1.2.6 DTRACE

        DTRACE is a utility that allows an experienced user to define
        dynamic tracepoints where tracepoints were not previously
        located.

        For information about this utility please see the file
        DTRACE.DOC in the OS2\SYSTEM directory.



        1.2.7 MAPTSF

        This utility will generate a TSF from a MAP file. One tracepoint is
        generated for each public code symbol. Optionally a return tracepoint
        may be generated for each public code symbol.
        The syntax is:

                 MAPTSF map_file [/MAJOR=major_code]
                                 [/MODNAME=name]
                                 [/MAXDATALENGTH=max_data_length]
                                 [/MINORSTART=minor_code]
                                 [/TEMPLATE=template_file]
                                 [/LOGSTACK=stack_bytes]
                                 [/EXCLUDE=string[*][,....]]
                                 [/INCLUDE=string[*][,....]]
                                 [/REGISTERS=reg[,reg]...]
                                 [/LOGRETURN]
                                 [/RETEP]
                                 [/CASESENSITIVE]
                                 [/TYPES]
                                 [/GROUPS=string[,.....]]


         The parameters are:

        þ  map_file (only REQUIRED parameter)

        þ  /MAJOR

               Specifies the major code to be used in the MAJOR= statement of the TSF.
               If omitted, TRCUST will select the default major code of 1 when compiling the TSF.

        
                                       System Trace (SysTrace) facility  15


                             July 9, 1998 - Warp Debug

        þ  /MODNAME

               Specifies the module name to be used in the MODNAME= statement of the TSF.
               If omitted, MAPTSF will use the module name that appears in the second line of
               the MAP file.

               Note: The MAP file excludes the module extension. TRCUST will assume an
               extension of DLL if not specified.

        þ  /MAXDATALENGTH

               Specifies the MAXDATALENGTH= statement of the TSF. If omitted, TRCUST will
               assume the default of 512 when compiling the TSF.

        þ  /MINORSTART

               Specifies the first minor code. Subsequent tracepoints have incremental minor
               codes. If omitted, the MINOR= statement is not generated. TRCUST will assume
               an initial minor code of 1 and increment for each tracepoint.

        þ  /INCLUDE

               Specifies a comma delimited list of case insensitive strings used as inclusion
               criteria for public symbols. An optional trailing * signifies a generic match. If
               both /INCLUDE and /EXCLUDE are specified then the logical OR of their criteria is
               used for selection.

               For example:

                   /INCLUDE=dos*,strupr

                       Inludes all public symbols beginning 'dos' or equal to 'strupr'.

                   /EXCLUDE=s* /INCLUDE=strupr

                       Excludes all public symbols beginning 's' except for 'strupr' and includes everything else.

        þ  /EXCLUDE

               Specifies a comma delimited list of case insensitive strings used as exclusion criteria for
               public symbols. An optional trailing * signifies a generic match. If both /INCLUDE and
               /EXCLUDE are specified then the logical OR of their criteria is used for selection.
               See the examples under /INCLUDE.

        þ  /CASESENSITIVE

               Switch that applies to /INCLUDE and /EXCLUDE. If specified then the include and
               exclude strings will be match on a case-sensitve basis.

        þ  /LOGSTACK=n

               Specifies the number of bytes of stack to log for entry tracepoints. This
               causes the following TSF statements to be generated for each entry tracepoint:

                   for 16-bit code:



        
                                       System Trace (SysTrace) facility  16


                             July 9, 1998 - Warp Debug

                REGS=(SP,SS),
                FMT="Stack pointer SS:SP=%A->",
                MEM=(RSS+SP,D,n),
                FMT="1W"


                   for 32-bit code:

                REGS=(ESP),
                FMT="Stack pointer ESP=%F->",
                MEM32=(FESP,D,n)
                FMT="1F"



           If /LOGSTACK is specified without a value then 16 bytes is assumed.

        þ  /LOGRETURN

               Specifies that for each return tracepoint, the return value in AX/EAX should be
               logged. This causes the following TSF statements to be generated:

                   for 16-bit code:

                REGS=(AX)
                FMT="Returns (ax) %W"


                   for 32-bit code:

                REGS=(EAX)
                FMT="Returns (eax) %F"


        þ  /REGISTERS or /REGS

               Specifies one or more processor registers to be logged, each separated by a
               comma. The following register mnemonics are supported:

                AX,BX,CX,DX,CS,DS,ES,FS,GS,IP,SI,DI,SP,BP,FLAGS,
                EAX,EBX,ECX,EDX,EIP,ESI,EDI,ESP,EBP,EFLAGS



        þ  /RETEP

               Specifies that for each public entry-point in the MAP file, a return tracepoint
               should be generated using the RETEP parameter on the TRACE statement in the TSF.

               Note: RETEP is only processed by TRCUST if the module has debugging information
               present. If this is not the case then TRCUST (2.20) will ignore the RETEP
               parameter and a warning message will be issued for the associated tracepoint.

        þ  /TYPES

               pre-defined types:


        
                                       System Trace (SysTrace) facility  17


                             July 9, 1998 - Warp Debug

                   PUB  = Public routines - names the begin upper case (ignoring leading underscores)

                   PRIV = Private routines - names the begin lower case (ignoring leading underscores)

                   PRE  = Entry tracepoint.

                   POST = Exit tracepoint.

        þ  /GROUPT

               Requests that each of the strings listed be used to define a group. Tracepoints
               are assigned to a group according to whether a group name matches the beginning
               of the tracepoint name, ignoring case and leading underscore characters

        þ  /TEMPLATE

               Specifies a file where up to four template tracepoint definitions may be
               specified, one for each of the following categories:
                   16-bit entry points
                   16-bit return points
                   32-bit entry points
                   32-bit return points

               The definitions are in a shortened form of the TRCUST TRACE statement syntax.
               They are appended to each tracepoint of the category to which they apply. All
               parameters other than MINOR and DESC are permissible. TP and RETEP are
               specified as follows:
                   TP=@16           signifies a 16-bit entry-point
                   TP=@16,RETEP     signifies a 16-bit return-point
                   TP=@32           signifies a 32-bit entry-point
                   TP=@32,RETEP     signifies a 32-bit return-point

               Only TP and RETEP may appear on the same line as the TRACE keyword.
               For example:

                TRACE TP=@16
                      MEM=(SS:BP+8,I,0x10)
                      FMT="16-bytes of parameter 1: 1W"


               will append:

                      MEM=(SS:BP+8,I,0x10)
                      FMT="16-bytes of parameter 1: 1W"


               to every 16-bit entry tracepoint definition.




        1.2.8 SYSSPLIT


        If the system trace definitions for a particular module needs to be
        replaced or modified then SYSSPLIT may be used to split SYSTEM.TDF
        into its constituent TDF files. The resultant *.TDF files may be saved

        
                                       System Trace (SysTrace) facility  18


                             July 9, 1998 - Warp Debug

        in OS2\SYSTEM\TRACE. Because of the search order employed by TRACE.EXE
        it is recommended that SYSTEM.TDF be renamed after being split.

        When applying tracepionts to a DLL, TRACE.EXE will search the current path,
        then the DPATH for the dll_name.TDF file. If not found it searches
        OS2\SYSTEM\TRACE\SYSTEM.TDF and finally, OS2\SYSTEM\TRACE\dll_name.TDF.

        The file names of the split *.TDFs will be chosen to be the original
        names used to create SYSTEM.TDF.

        The syntax of the command is:

        SYSSPLIT <input_file>


            <input_file> is the system trace definition files - SYSTEM.TDF


        Note: The Trace definitions for the OS2KRNL may be in OS2KRNL.TDF or
        DOSCALLS.TDF. The TRACE command recognizes the keyword KERNEL as an
        alias for each of the kernel TDF names. TRACE.EXE searches the DPATH
        for DOSCALLS.TDF. Currently, TRACE ON KERNEL will only work
        for OS2KRNL.TDF if a directory from the boot drive is current.


        The TDFLST utility may be used with each of the resultant TDFs to
        format the trace point definitions.




        1.2.8.1 Trace formatting files - SYSTEM.TFF


        When formatting the system trace buffer, TRACEFMT.EXE will search
        OS2\SYSTEM\TRACE\SYSTEM.TFF for the formatting templates for each
        major code encountered in the trace buffer. If a major code is not
        found in SYSTEM.TFF then TRACEFMT will search for a file named
        TRC00xx.TFF, where xx is the major code number in hexadecimal.

        If the formatting templates for a particular module needs to be
        replaced or modified then SYSSPLIT may be used to split SYSTEM.TFF
        into its constituent TFF files. The resultant *.TFF files may be saved
        in OS2\SYSTEM\TRACE. Because of the search order employed by
        TRACEFMT.EXE it is recommended that SYSTEM.TFF be renamed after being
        split.

        The file names of the split *.TFFs will be chosen to be the original
        names used to create SYSTEM.TDF, that is names formed from their major
        codes.

        The TFFLST utility may be used with each of the resultant TFFs to
        format the trace point definitions.

        Note: TRCUST has the ability to combine TFFs for the same major code.
        This is not to be confused with the special SYSTEM.TFF and SYSTEM.TDF
        files that are concatenations of dissimilar major code definitions.

        
                                       System Trace (SysTrace) facility  19


                             July 9, 1998 - Warp Debug




        1.2.9 TDFLST


        TDF list formats a TDF as DTRACE compatible trace program file. The
        output is directed to STDOUT, which may be captured in a file using
        the redirection operator (>).

        Trace definitions may be modified or supplemented using an editor and
        the TDF rebuilt using DTRACE BUILDTDF.

        The syntax is:

        TDFLST <tdf_file>






        1.2.10 TFFLST


        TFF list formats a TFF as TRCUST compatible source. The
        output is directed to STDOUT, which may be captured in a file using
        the redirection operator (>).

        Trace formatting templates may be modified or supplemented using
        an editor and the TFF rebuilt using TRCUST.

        NOTES:

            TRCUST is used for generating TDFs and TFFs. The keyword,
            TP=@STATIC directs TRCUST solely to generate TFFs. Normally this is
            used with static trace but equally valid for dynamic trace where the
            tracepoints have already been defined.

            Large TDF and TFF files may take a few minutes to list.  A
            degree of searching and cross-referencing has to take place before the
            listing is produced.  Consequently there may be a considerable pause
            before the listing is produced.


        The syntax is:

        TFFLST <tdf_file>










        
                                       System Trace (SysTrace) facility  20


                             July 9, 1998 - Warp Debug

        1.3 APPENDIX A NEW TRACEPOINTS CROSS-REFERENCE.


        Those tracepoints flagged with an "*" are full tracepoints and record parameters
        as well as return address. Those not flagged only record the caller's return
        address and have to be used with their corresponding system tracepoint to record
        parameter information.



















































        
                                       System Trace (SysTrace) facility  21


                             July 9, 1998 - Warp Debug

        New "TRACE ON KERNEL" Tracepoints

        Tracepoint                        Minor Group Types    F  Remarks
        DOS32CANCELLOCKREQUEST            494   FS    PRE,API  *
        DOS32CANCELLOCKREQUEST            495   FS    POST,API *
        DOS32SETFILELOCKS                 496   FS    PRE,API  *
        DOS32SETFILELOCKS                 497   FS    POST,API *
        DOS32PROTECTSETFILELOCKS          498   FS    PRE,API  *
        DOS32PROTECTSETFILELOCKS          499   FS    POST,API *
        DOSCREATESPINLOCK                 500   LOCK  PRE,API  *  SMP only
        DOSCREATESPINLOCK                 501   LOCK  POST,API *  SMP only
        DOSACQUIRESPINLOCK                502   LOCK  PRE,API  *  SMP only
        DOSACQUIRESPINLOCK                503   LOCK  POST,API *  SMP only
        DOSRELEASESPINLOCK                504   LOCK  PRE,API  *  SMP only
        DOSRELEASESPINLOCK                505   LOCK  POST,API *  SMP only
        DOSFREESPINLOCK                   506   LOCK  PRE,API  *  SMP only
        DOSFREESPINLOCK                   507   LOCK  POST,API *  SMP only
        DOS32IPROTECTREAD                 508   FS    PRE,API  *
        DOS32IPROTECTREAD                 509   FS    POST,API *
        DOS32IPROTECTWRITE                510   FS    PRE,API  *
        DOS32IPROTECTRWITE                511   FS    POST,API *


        New "TRACE ON DOSCALL1" Tracepoints

        Tracepoint                        Minor Group Types    F  Remarks
        DOS32WAITCHILD                    262   TK    PRE,API     32-bit EP to KERNEL API
        DOS32BEEP                         263   IO    PRE,API     32-bit EP to KERNEL API
        DOS32PHYSICALDISK                 264   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETCP                        265   TK    PRE,API     32-bit EP to KERNEL API
        DOS32SETPROCESSCP                 266   TK    PRE,API     32-bit EP to KERNEL API
        DOS32SLEEP                        267   TK    PRE,API     32-bit EP to KERNEL API
        DOS32DEVCONFIG                    268   FS    PRE,API     32-bit EP to KERNEL API
        DOS32GETDATETIME                  269   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETDATETIME                  270   TIM   PRE,API     32-bit EP to KERNEL API
        DOS32EXECPGM                      271   TIM   PRE,API     32-bit EP to KERNEL API
        DOS32ENTERCRITSEC                 272   TK    PRE,API     32-bit EP to KERNEL API
        DOS32EXITCRITSEC                  273   TK    PRE,API     32-bit EP to KERNEL API
        DOS32EXIT                         274   TK    PRE,API     32-bit EP to KERNEL API
        DOS32KILLPROCESS                  275   TK    PRE,API     32-bit EP to KERNEL API
        DOS32SETPRIORITY                  276   TK    PRE,API     32-bit EP to KERNEL API
        DOS32RESUMETHREAD                 277   TK    PRE,API     32-bit EP to KERNEL API
        DOS32SUSPENDTHREAD                278   TK    PRE,API     32-bit EP to KERNEL API
        DOS32CREATEPIPE                   279   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32CREATEQUEUE                  280   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32OPENQUEUE                    281   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32CLOSEQUEUE                   282   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32PEEKQUEUE                    283   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32PURGEQUEUE                   284   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32QUERYQUEUE                   285   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32WRITEQUEUE                   286   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS32CALLNPIPE                    287   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32CONNECTNPIPE                 288   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32DISCONNECTNPIPE              289   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32CREATENPIPE                  290   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32PEEKNPIPE                    291   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32QUERYNPHSTATE                292   PIP   PRE,API     32-bit EP to KERNEL API

        
                                       System Trace (SysTrace) facility  22


                             July 9, 1998 - Warp Debug

        DOS32RAWREADNPIPE                 293   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32RAWWRITENPIPE                294   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32QUERYNPIPEINFO               295   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32QUERYNPIPESEMSTATE           296   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32SETNPHSTATE                  297   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32SETNPIPESEM                  298   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32TRANSACTNPIPE                299   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32WAITNPIPE                    300   PIP   PRE,API     32-bit EP to KERNEL API
        DOS32RESETBUFFER                  301   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETCURRENTDIR                302   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETFILEPTR                   303   FS    PRE,API     32-bit EP to KERNEL API
        DOS32PROTECTSETFILEPTR            304   FS    PRE,API     32-bit EP to KERNEL API
        DOS32CLOSE                        305   FS    PRE,API     32-bit EP to KERNEL API
        DOS32PROTECTCLOSE                 306   FS    PRE,API     32-bit EP to KERNEL API
        DOS32COPY                         307   FS    PRE,API     32-bit EP to KERNEL API
        DOS32DELETE                       308   FS    PRE,API     32-bit EP to KERNEL API
        DOS32FORCEDELETE                  309   FS    PRE,API     32-bit EP to KERNEL API
        DOS32DEVIOCTL                     310   FS    PRE,API     32-bit EP to KERNEL API
        DOS32DUPHANDLE                    311   FS    PRE,API     32-bit EP to KERNEL API
        DOS32EDITNAME                     312   FS    PRE,API     32-bit EP to KERNEL API
        DOS32FINDCLOSE                    313   FS    PRE,API     32-bit EP to KERNEL API
        DOS32FSATTACH                     314   FS    PRE,API     32-bit EP to KERNEL API
        DOS32FSCTL                        315   FS    PRE,API     32-bit EP to KERNEL API
        DOS32MOVE                         316   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETFILESIZE                  317   FS    PRE,API     32-bit EP to KERNEL API
        DOS32PROTECTSETFILESIZE           318   FS    PRE,API     32-bit EP to KERNEL API
        DOS32QUERYCURRENTDIR              319   FS    PRE,API     32-bit EP to KERNEL API
        DOS32QUERYCURRENTDISK             320   FS    PRE,API     32-bit EP to KERNEL API
        DOS32QUERYFHSTATE                 321   FS    PRE,API     32-bit EP to KERNEL API
        DOS32PROTECTQUERYFHSTATE          322   FS    PRE,API     32-bit EP to KERNEL API
        DOS32PQUERYFSATTACH               323   FS    PRE,API     32-bit EP to KERNEL API
        DOS32QUERYFSINFO                  324   FS    PRE,API     32-bit EP to KERNEL API
        DOS32QUERYHTYPE                   325   FS    PRE,API     32-bit EP to KERNEL API
        DOS32QUERYVERIFY                  326   FS    PRE,API     32-bit EP to KERNEL API
        DOS32DELETEDIR                    327   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SEARCHPATH                   328   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETDEFAULTDISK               329   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETFHSTATE                   330   FS    PRE,API     32-bit EP to KERNEL API
        DOS32PROTECTSETFHSTATE            331   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETFSINFO                    332   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETMAXFH                     333   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETRELMAXFH                  334   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SETVERIFY                    335   FS    PRE,API     32-bit EP to KERNEL API
        DOS32ERRCLASS                     336   FS    PRE,API     32-bit EP to KERNEL API
        DOS32ERROR                        337   TK    PRE,API     32-bit EP to KERNEL API
        DOS32LOADMODULE                   338   LDR   PRE,API     32-bit EP to KERNEL API
        DOS32FREEMODULE                   339   LDR   PRE,API     32-bit EP to KERNEL API
        DOS32QUERYMODULEHANDLE            340   LDR   PRE,API     32-bit EP to KERNEL API
        DOS32QUERYMODULENAME              341   LDR   PRE,API     32-bit EP to KERNEL API
        DOS32QUERYAPPTYPE                 342   LDR   PRE,API     32-bit EP to KERNEL API
        DOS32PFINDNEXT                    343   FS    PRE,API     32-bit EP to KERNEL API
        DOS32SHUTDOWN                     344   FS    PRE,API     32-bit EP to KERNEL API
        DOS32OPENCHANGENOTIFY             345   FS    PRE,API     32-bit EP to KERNEL API
        DOS32RESETCHANGENOTIFY            346   FS    PRE,API     32-bit EP to KERNEL API
        DOS32CLOSECHANGENOTIFY            347   FS    PRE,API     32-bit EP to KERNEL API
        DOS32CREATESPINLOCK               348   LOCK  PRE,API     SMP only, 32-bit EP to KERNEL API
        DOS32ACQUIRESPINLOCK              349   LOCK  PRE,API     SMP only, 32-bit EP to KERNEL API

        
                                       System Trace (SysTrace) facility  23


                             July 9, 1998 - Warp Debug

        DOS32RELEASESPINLOCK              350   LOCK  PRE,API     SMP only, 32-bit EP to KERNEL API
        DOS32FREESPINLOCK                 351   LOCK  PRE,API     SMP only, 32-bit EP to KERNEL API
        DOS32READQUEUE                    352   QUE   PRE,API     32-bit EP to QUECALLS API
        DOS16CREATEQUEUE                  353   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16OPENQUEUE                    354   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16CLOSEQUEUE                   355   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16PEEKQUEUE                    356   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16PURGEQUEUE                   357   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16QUERYQUEUE                   358   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16WRITEQUEUE                   359   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS16READQUEUE                    360   QUE   PRE,API     16-bit EP to QUECALLS API
        DOS32R3EXCEPTIONDISPATCHER        361   EXMG  PRE,API  *  From FP37, Internal DOSCALL1 tracepoint
        DOS32EXCEPTIONCALLBACK            362   EXMG  PRE,API  *  From FP37, Internal DOSCALL1 tracepoint
        XCPTEXECUTEUSEREXCEPTIONHANDLER   363   EXMG  PRE,API  *  From FP37, Internal DOSCALL1 tracepoint
        UT16RETURN                        33028 UT    POST,INT    Internal DOSCALL1 tracepoint
        UT32RETURN                        33029 UT    POST,INT    Internal DOSCALL1 tracepoint


        New "TRACE ON SESMGR" Tracepoints

        Tracepoint                        Minor Group Types    F  Remarks
        DOS32SELECTSESSION                32          PRE,API     32-bit EP to SESMGR API
        DOS32SETSESSION                   33          PRE,API     32-bit EP to SESMGR API
        DOS32STARTSESSION                 34          PRE,API     32-bit EP to SESMGR API
        DOS32STOPSESSION                  35          PRE,API     32-bit EP to SESMGR API