PrintQ - Print Library for OS/2 Presentation Manager Programs
(C) Peter Wansch, 1994
Version 1.31

Contents
========

1. Introduction .............................................................. 1
1.1 What's new? .............................................................. 2
2. Requirements .............................................................. 2
3. Components of the Print Subsystem ......................................... 2
4. Functions ................................................................. 3
5. Compiling, installing and using the library .............................. 11
6. Multithreading considerations ............................................ 11
7. e-mail ................................................................... 12


1. Introduction
===============

The operating system OS/2 Version 2 and its graphical program environment 
Presentation Manager provide outstanding functionality and consistency both 
for the program developer and the user. The programming interface of the 
print subsystem combined with the powerful functions of the Graphic 
Programming Interface (GPI) enable the programmer to create device-independent 
printed output. 

However most books about Presentation Manager programming (even those known 
for their in-depth coverage of PM-Programming like "Programming the OS/2 
Presentation Manager" by Charles Petzold) lack a chapter on printing. A 
possible reason for that could be the fact that programming printing does not 
only require some knowledge about the corresponding functions but also a 
detailed understanding of the print subsystem itself. 

Hence it can be difficult for inexperienced programmers to tackle printing. 
On the one hand the programming references and books lack comprehensible 
examples and the sample print program from the Developers Toolkit is too 
complex to use it as a template.

The dynamic link library PrintQ completely hides the print subsystem from the 
programmer and provides 13 extremely easy to use functions and 4 data
structures to create printed output from your Presentation Manager 
applications. Hence PrintQ substantially reduces the complexity of a 
Presentation Manager application and the time to implement printing because 
the programmer needs no knowledge about the print subsystem. 

I hope this document together with the sample application Hello queue/2 that
uses the PrintQ library provides sufficient and comprehensible documentation 
for programmers. This document is a brief summary of a document about the 
print subsystem and the PrintQ library which I wrote in German. I suggest that 
you read this document first (you don't actually have to read chapter 3) and 
have a look at the sample programs after that.

The code for the PrintQ library as well as the PRINTQ.DLL and PRINTQ.LIB files
can be found in the \PRINTQ directory. The code and the file hello.exe for the
sample program Hello queue/2 can be found in the \HELLOQ1, \HELLOQ2 , \HELLOQ3,
\HELLOQMT and \HELLOQO directories. The sample programs are almost identical but 
Hello queue/2 1.0 uses a cached-micro presentation space for drawing (obtained 
withWinBeginPaint) and obtains a handle to the printer presentation space with 
the function SpoolBeginSpool whereas Hello queue/2 1.1 uses a normal presentation 
space both for drawing and printing. Hello queue/2 1.2 shows how printing from 
a secondary thread is accomplished and Hello queue/2 1.3 shows how to save 
printer settings

                                      -1-
 
1.1 What's new?
===============

When you started a program using the PrintQ library 1.0 or 1.1, all settings
of the printer queues were reset to their default values. Now you can save the
printer settings and restore them when you call SpoolInitialize. This enables
you to save the printer settings with documents or just to save the printer
settings in an initialization file, so that they do not have to be changed
each time you load the program. Hello queue/2 1.3 in the \HELLOQ3 directory
shows how to do that and how to use the printer font dialog.

It is now safe to call PrintQ functions from separate threads in a process 
since they are serialized in the PrintQ library. The sample program Hello 
queue/2 1.2 in the directory \HELLOQMT shows how to implement a secondary 
print thread.

More sophisticated Presentation Manager applications don't use a cached micro 
or a micro presentation space that is obtained with the WinBeginPaint function 
call because of its limited functionality. These programs use normal 
presentation spaces that are created for a display window in response to the 
WM_CREATE message of your main application window (using GpiCreatePS), 
associated with the display device (the handle to that device is obtained with 
the WinOpenWindowDC function) and kept until termination. 
These presentation spaces also have to be destroyed using GpiDestroy. Unlike 
cached-micro and micro presentation spaces, normal presentation spaces can be 
disassociated from the screen device and associated with a printer device 
which makes sense since all the settings are retained. 

PrintQ now supports this type of applications as well and the sample program 
Hello queue/2 1.1 demonstrates the use of PrintQ functions in such a program. You just 
specifiy the handle of your normal presentation space as a parameter in 
SpoolBeginSpool or SpoolBeginInfo and PrintQ automatically makes all the 
associations and disassociations for you. This new feature makes PrintQ usable 
for a broader range of applications while retaining its ease of use. Hello queue/2 1.0
also demonstrate how you can print bitmaps.


2. Requirements
===============

I assume that you have basic experience programming Presentation Manager
applications in C and that you know how to paint in an applications client 
window which comprises a certain knowledge about presentation space and device 
contexts. To compile the source code for the dynamic link library and the sample 
programs you need the IBM C Set/2 for OS/2 2.0 Version 1.0 and the Developer's 
Toolkit for OS/2 2.0 (or higher versions) or any other C compiler for 
OS/2 2.x.


3. Components of the Print Subsystem
====================================

The following chapter provides background information about the print 
subsystem which is not necessarily required to understand the PrintQ library.

The print subsystem comprises the following components:

  * the spooler
  * the user interface of the print subsystem
  * the queue driver (queue processor)
  * the printer driver


                                      -2-

The Spooler is a background process that controls the print subsystem. It
manages print jobs that are submitted by applications in the system. 
Applications do not directly print to a physical printer (device) but to a 
queue. The main purpose of the Spooler is to read print jobs from a queue, 
sort them according to their priority and send them to the corresponding 
physical device i. e. the printer. A spooler can manage more than one queue 
at once. Per default each printer has its own queue. However other 
configurations e.g. for printer sharing where two or more queues are connected 

to a single device or printer pooling where two or more printer devices are 
connected to a single queue are also possible. Each queue can be configured 
individually. A print job in a queue is actually a meta file which is a 
sequence of GPI function calls. 

The user interface of the print subsystem is realised by means of printer
objects on the Workplace Shell desktop. These device objects do not represent
the physical printer devices but queues. Such a queue is connected to a 
logical device that contains the specification of the corresponding physical 
device. The specification comprises the printer driver and the port to which 
the physical device is attached. The settings for the printer objects on the 
desktop are stored in the system initialisation file OS2SYS.INI.

The queue driver (sometimes referred to as queue processor) retrieves the 
print jobs from the queue and sends the corresponding meta files to the 
printer driver.

The printer driver provides a dialog window that allows the user to view and
change the configuration of the physical device (e. g. which forms are 
available and which font cards are installed) and a dialog window that enables 
the user to configure an individual print job (e. g. set the default font or 
form). This configuration data is also referred to as Job properties. Hence a 
print job consists of a meta file and Job properties which are its default 
print settings. The printer driver also translates the device independent GPI 
function calls in the meta file of a print job into a printer specific command 
language like PCL, PPDS or Postscript. After the translation the printer 
driver directly sends the data to the printer via the file system and the 
corresponding port. 


4. Functions
============

The functions that are provided by PrintQ are displayed in the following 
table.

                            {SpoolInitialize
                                    |
                                    |
      {SpoolBeginSetup       {SpoolBeginInfo         {SpoolBeginSpool         
              |                                              |
              |                                              |
  SpoolSetDef, SpoolJobProp                    SpoolNewFrame, GPI functions
              |                                              |
              |                                              |
        SpoolEndSetup}        SpoolEndInfo}   SpoolAbortSpool, SpoolEndSpool}
                                    |
                                    |
                              SpoolTerminate}

Some functions (SpoolInitialize and SpoolTerminate, SpoolBeginSetup and 
SpoolEndSetup, SpoolBeginInfo and SpoolEndInfo, SpoolBeginSpool and 
SpoolEndSpool) form logical brackets.

The use of these functions is shown in the sample programs.
                                      -3-

This dependence also imposes a sequence on the correct use of the library 
functions. For instance SpoolAbortSpool and SpoolNewFrame can only be used 
after a SpoolBeginSpool call. You should be familiar with these logical 
brackets since they are used in Presentation Manager programs all the time 
(e. g. WinInitialize and WinTerminate or WinBeginPaint and WinEndPaint). 
In the following the use of these functions will be described.


BOOL SpoolInitialize(HAB hab, PDRIVDATA pDriverData, PBOOL pfIni)

  Before you can use any function or data structure provided by the library 
  you have to initialise the library for use by your program. The first
  parameter is the anchor block-handle of your application that you obtain by 
  a WinInitialize function call which is normally the first statement in a 
  Presentation Manager application. Hence it is advisable to call 
  SpoolInitialize immediately after WinInitialize. If you have saved the driver
  data you can pass a pointer to a DRIVDATA structure in the second parameter or
  you can pass NULL. In the third parameter you pass a pointer to a flag. If
  the flag is true, SpoolInitialize tries to set the default printer and its
  settings according to the data passed in the second parameter. If that is
  not possible (for instance if a different version of the corresponding printer
  driver has been installed) the flag to which pfIni points will be set to FALSE
  after the call. See Hello queue/2 1.3 in the \HELLOQ3 directory for an
  example, where the driver data is stored in the user ini profile.

  All Library functions  return a value of type BOOL which indicates whether
  or not the function was  successful (TRUE success, FALSE error occurred). 
  If you for instance call  any other library function before initialising 
  the library, this function  will return FALSE. You should always check the 
  return values of the PrintQ functions. In the sample programs the return 
  value is only checked for the SpoolInitialize function to improve the 
  clarity of the sample program.

BOOL SpoolTerminate(void)

  This function terminates the use of the PrintQ library and releases of 
  resources associated with the application. It forms a logical bracket with 
  the SpoolInitialize function like the WinInitialize and WinTerminate 
  functions. Hence it is advisable that this function is the last but one 
  function in your program with WinTerminate being the last function. 

  The File menu of a Presentation Manager application normally contains a 
  Printer setup item. When you choose this command a dialog window is 
  displayed that consists of a list box and several push buttons. The list box 
  displays the printers that are available in the system. The default printer 
  (which can be set in the context menu of any printer object with the command 
  "Set default") is selected. Now you can select a different printer or change 
  the job properties for a printer. The job properties are the settings that 
  are specific for the print job in your application. In your application you 
  have to create a dialog box template for the printer setup dialog and write 
  the dialog procedure. Your dialog box should consist of a list box, an OK 
  button a Cancel button and a Job properties button. If you provide on-line 
  help you should also include a Help button. In response to the WM_INITDLG 
  messages which is sent to your dialog procedure before the dialog window is 
  displayed, you have to call the following function.

BOOL SpoolBeginSetup(HWND hwnd)

  where hwnd is the handle to the printer list box. You can obtain a handle to
  the list box using the WinWindowFromId function. When the user chooses the 
  Job properties button you receive a corresponding WM_COMMAND message and you 
  call the following function. If hwnd is NULLHANDLE, Printq assumes that you
  don't want to display a list box. If you call SpoolJobProp the Jop properties
  dialog window of the currently selected printer is displayed.

                                      -4-

BOOL SpoolJobProp(void)

  This function displays the Job properties dialog window for the currently 
  selected printer. When the user presses the OK button in the Printer setup
  dialog window the default printer settings for your application has to be 
  updated using the following function.

BOOL SpoolSetDef(void)

  sets the hilited printer in the List box your default printer. The data 
  structures that information on the device and form capabilities are updated.

BOOL SpoolEndSetup(void) 

  forms a logical bracket with the SpoolBeginSetup function. It is advisable to
  call the function after the WindDlgBox function call which displays the 
  Printer setup dialog. 


  If you want to obtain a presentation space to the printer currently selected 
  in your application just to retrieve information (e. g. about font metrics), 
  you use the following function.

BOOL SpoolBeginInfo(PHPS phpsPrinterInfo, BOOL fAssocPS)

  The parameter phpsPrinterInfo is a pointer to a HPS variable which is assigned
  the presentation parameter of the currently selected printer if fAssocPS is 
  FALSE. If fAssocPS is TRUE this function expects a pointer to the handle of 
  a normal presentation space which it will associate with the printer device 
  context. This returned presentation space is an information presentation 
  space which is used to query information about a device associated with it. 
  Directing GPI functions to this yields no printed output.

BOOL SpoolEndInfo(void)

  forms a logical bracket with the SpoolBeginInfo function. This function is 
  especially important if you use a normal presentation space in your program 
  since it re-associates the presentation space with the display device 
  context.

  A print job is normally started in response to the user choosing the Print 
  command from the File menu i. e. in response to the corresponding WM_COMMAND
  message. To start a print job you call the following function.

BOOL SpoolBeginSpool(PSZ pszComment, PSZ pszDocName, PSZ pszQueueProcParams, 
                     ULONG ulOptions, PHPS phpsPrinter, BOOL fAssocPS)

  The first parameter pszComment is a zero-terminated comment string 
  describing the print job. This string is displayed in the settings of a 
  print job on the Submission data page and has no further relevance. The 
  second parameter pszDocName is a null-terminated string that is the name 
  (title) of the print job. This string is the document name of the print job. 
  The third parameter pszQueueProcParms is a zero-terminated string that may 
  contain commands for the queue processor separated by one or more blanks. 
  The available commands are:

  COP=n          

  The COP parameter specifies the number of copies that you want printed. The 
  value of n must be an integer in the range of 1 through 999. The default 
  value of n is 1.



                                      -5-

  COL=M|C  

  The COL parameter enables you to specify color output if you have a color
  printer. A value of COL=M creates monochrome output. A value of COL=C creates
  color output. The default value of COL is M for a monochrome printer and C 
  for a color printer.

  MAP=N|A        

  The MAP parameter specifies how neutral colors (colors which were not 
  defined e. g. the background color) are printed. The default value N yields 
  a white background and a black foreground while a value of MAP=A provides 
  the reverse of the normal representation. 

  ARE=C|w,h,l,t  

  This parameter determines the size and position of the output area on the 
  physical printer page. The default value of ARE=C means that the output area
  is the whole page. To size and position the output area at a specific point 
  
  
  on the page use ARE=w,h,l,t where w and h are the width and height of the 
  desired output area and l and t are the offsets of the upper-left corner of 
  the output area from the left and from the top of the maximum output area. 
  These four values must be gives as percentages of the maximum output 
  dimensions.

  FIT=S|l,t      

  This parameter determines which part of a picture is to be printed. The 
  default value of FIT=S causes the output to be scaled until the larger of 
  the height or width just fits within the defined output area. The aspect 
  ratio of the picture is maintained. To print the picture in actual size use 
  FIT=l,t where l and t are the coordinates of the point in the picture that 
  you want positioned at the center of the output area. l is measured from the 
  left edge of the picture and it is measured from the top edge. The 
  coordinates must be gives as percentages of the actual dimensions of the 
  picture.

  XFM=0|1        

  The default value of XFM=1 allows the appearance of the output to be 
  determined by the ARE and FIT parameters. A value of XFM=0 yields output as 
  specified in the picture file.

  For instance the string "COP=2 MAP=A" would result in two inverse copies.

  Default values are used for parameters that are omitted or used incorrectly.
  Bitmaps or image data is not affected by the ARE and FIT parameters.

  The fourth parameter ulOptions determines the scale units for the printer 
  presentation space. If you use 0UL, pixels are used. Other options are 
  PU_LOMTRIC (0.1 mm), PU_HIMETRIC (0.01 mm), PU_LOENGLISH (0.01 inch), 
  PU_HIENGLISH (0.001 inch) or PU_TWIPS (1/1440 inch). If fAssocPS is TRUE, 
  the parameter phpsPrinter is a pointer to a HPS variable which is assigned 
  the presentation space of the currently selected printer. If fAssocPS is 
  TRUE this function expects a pointer to the handle of a normal presentation 
  space which it will associate with the printer device context. 
  Now you can use this presentation space handle as the first parameter for 
  GPI functions like GpiLine. The coordinates are interpreted with respect to 
  the ulOptions parameter.

  Use the following function to start a new page and to eject the old page.

                                      -6-

BOOL SpoolNewFrame(void)

  To end the print job use the following function.

BOOL SpoolEndSpool(PUSHORT pusJobId)

  The parameter pusJobId is a pointer to an USHORT variable which is assigned 
  the id of the submitted print job. This variable can be used to inform the 
  user of the id of the print job if desired. 
 
  If you decide to abort the print job without actually printing after calling 
  the SpoolBeginSpool function (e. g. in response to a user request) you use 
  the following function.

SpoolAbortSpool(void)

  Please note that it is not neccessary to call SpoolEndSpool after 
  SpoolAbortSpool since you either call SpoolAbortSpool or SpoolEndSpool to 
  close the logical bracket with the SpoolBeginSpool function.

  
  The library also provides 4 variables. These variables are only valid after
  initialising the Library using the SpoolInitialize function and before de-
  registering from the library using the SpoolTerminate function. Their use is 
  illustrated in the sample program Hello queue/2. The variable hcInfoDef is
  a structure of type HCINFO and it contains information about the currently 
  selected form of the currently selected printer. It is also described in the 
  PM Reference as follows:

  typedef struct _HCINFO {
    CHAR    szFormname[32];  /* Form name */
    LONG    cx;              /* Width (left-to-right) in millimeters  */
    LONG    cy;              /* Height (top-to-bottom) in millimeters  */
    LONG    xLeftClip;       /* Left clip limit in millimeters  */
    LONG    yBottomClip;     /* Bottom clip limit in millimeters  */
    LONG    xRightClip;      /* Right clip limit in millimeters  */
    LONG    yTopClip;        /* Top clip limit in millimeters  */
    LONG    xPels;           /* Pels between left and right clip limits  */
    LONG    yPels;           /* Pels between bottom and top clip limits  */
    LONG    flAttributes;    /* Attributes of the form identifier  */
  } HCINFO;

  The variable prqInfoDef is a structure of type PRQINFO3 and is described in
  the PM Reference as follows. It provides information about the currently 
  selected printer queue.

  typedef struct _PRQINFO3 {
    PSZ          pszName;        /* Queue name  */
    USHORT       uPriority;      /* Queue priority  */
    USHORT       uStartTime;     /* Time when queue becomes active  */
    USHORT       uUntilTime;     /* Time when queue ceases to be active  */
    USHORT       fsType;         /* Queue type  */
    PSZ          pszSepFile;     /* SeParator-page file  */
    PSZ          pszPrProc;      /* Default queue-processor  */
    PSZ          pszParms;       /* Queue Parameters  */
    PSZ          pszComment;     /* Queue description  */
    USHORT       fsStatus;       /* Queue status  */
    USHORT       cJobs;          /* Number of jobs in queue  */
    PSZ          pszPrinters;    /* Print devices connected to queue  */
    PSZ          pszDriverName;  /* Default device driver  */
    PDRIVDATA    pDriverData;    /* Default queue job properties  */
  } PRQINFO3;


                                      -7-

  The third variable alCaps is an array of LONG values. You access the array 
  elements using the following symbolic names. For instance the number of 
  available physical colors on the currently selected printer (which will be 2 
  for non-color printers) is alCaps[CAPS_PHYS_COLORS]. The following description 
  is copied from the PM Reference.

  CAPS_FAMILY 
    Device type (values as for lType in DevOpenDC). 
  CAPS_IO_CAPS 
    Device input/output capability: 
    CAPS_IO_DUMMY 
      Dummy device 
    CAPS_SUPPORTS_OP 
      Device supports output 
    CAPS_SUPPORTS_IP 
       Device supports input 
    CAPS_SUPPORTS_IO 
       Device supports output and input. 
  
  CAPS_TECHNOLOGY 
      Technology: 
    CAPS_TECH_UNKNOWN 
      Unknown 
    CAPS_TECH_VECTOR_PLOTTER 
      Vector plotter 
    CAPS_TECH_RASTER_DISPLAY 
      Raster display 
    CAPS_TECH_RASTER_PRINTER 
      Raster printer 
     CAPS_TECH_RASTER_CAMERA 
      Raster camera 
    CAPS_TECH_POSTSCRIPT 
      PostScript device. 
  CAPS_DRIVER_VERSION 
    Version identifier of the Presentation driver. The high order word of the 
    version identifier is 0. The low order word identifies the release, for 
    example x0120 is release 1.2. 
  CAPS_WIDTH 
    Media width (for a full screen, maximized window for displays) in pels. 
  CAPS_HEIGHT 
    Media depth (for a full screen, maximized window for displays) in pels. 
    (For a plotter, a pel is defined as the smallest possible displacement of 
    the pen and can be smaller than a pen width.) 
  CAPS_WIDTH_IN_CHARS 
    Media width (for a full screen, maximized window for displays) in default 
    character columns. 
  CAPS_HEIGHT_IN_CHARS 
    Media depth (for a full screen, maximized window for displays) in default 
    character rows. 
  CAPS_HORIZONTAL_RESOLUTION 
    Horizontal resolution of device in pels per meter. 
  CAPS_VERTICAL_RESOLUTION 
    Vertical resolution of device in pels per meter. 
  CAPS_CHAR_WIDTH 
    Default character-box width in pels for VIO. 
  CAPS_CHAR_HEIGHT 
    Default character-box height in pels for VIO. 
  CAPS_SMALL_CHAR_WIDTH 
    Default small-character box width in pels for VIO. This is 0 if there is 
    only one character-box size. 
  CAPS_SMALL_CHAR_HEIGHT 
    Default small-character box height in pels for VIO. This is 0 if there is 
    only one character-box size. 

                                      -8-

  CAPS_COLORS 
    Number of distinct colors supported at the same time, including reset 
    (gray scales count as distinct colors). If loadable color tables are 
    supported, this is the number of entries in the device color table.  For 
    plotters, the value returned is the number of pens plus one (for the 
    background). 
  CAPS_COLOR_PLANES 
    Number of color planes. 
  CAPS_COLOR_BITCOUNT 
    Number of adjacent color bits for each pel (within one plane). 
  CAPS_COLOR_TABLE_SUPPORT 
    Loadable color table support: 
    CAPS_COLTABL_RGB_8 
      1 if RGB color table can be loaded, with a minimum support of 8 bits 
      each for red, green, and blue. 
    CAPS_COLTABL_RGB_8_PLUS 
      1 if color table with other than 8 bits for each primary color can be 
      loaded. 
    
    CAPS_COLTABL_TRUE_MIX 
      1 if true mixing occurs when the logical color table has been realized, 
      providing that the size of the logical color table is not greater than 
      the number of distinct colors supported (see element CAPS_COLORS). 
    CAPS_COLTABL_REALIZE 
      1 if a loaded color table can be realized. 
  CAPS_MOUSE_BUTTONS 
    The number of pointing device buttons that are available. A returned value 
    of 0 indicates that there are no pointing device buttons available. 
  CAPS_FOREGROUND_MIX_SUPPORT 
    Foreground mix support: 
    CAPS_FM_OR 
      Logical OR. 
    CAPS_FM_OVERPAINT 
      Overpaint. 
    CAPS_FM_XOR 
      Logical XOR. 
    CAPS_FM_LEAVEALONE 
      Leave alone. 
    CAPS_FM_AND 
      Logical AND. 
    CAPS_FM_GENERAL_BOOLEAN 
      All other mix modes; see GpiSetMix. The value returned is the sum of the 
      values appropriate to the mixes supported. A device capable of 
      supporting OR must, as a minimum, return CAPS_FM_OR + CAPS_FM_OVERPAINT + 
      PS_FM_LEAVEALONE, signifying support for the mandatory mixes OR, 
      overpaint, and leave-alone. Note that these numbers correspond to the 
      decimal representation of a bit string that is six bits long, with each 
      bit set to 1 if the appropriate mode is supported. Those mixes returned 
      as supported are guaranteed for all primitive types.
  CAPS_BACKGROUND_MIX_SUPPORT 
    Background mix support: 
    CAPS_BM_OR 
      Logical OR. 
    CAPS_BM_OVERPAINT 
      Overpaint. 
    CAPS_BM_XOR 
      Logical XOR. 
    CAPS_BM_LEAVEALONE 
      Leave alone. 
    CAPS_BM_AND 
      Logical AND. 



                                      -9-

    CAPS_BM_GENERAL_BOOLEAN 
      All other mix modes; see GpiSetBackMix. The value returned is the sum of 
      the values appropriate to the mixes supported. A device must, as a 
      minimum, return CAPS_BM_OVERPAINT + CAPS_BM_LEAVEALONE, signifying 
      support for the mandatory background mixes overpaint, and leave-alone. 
      Note that these numbers correspond to the decimal rePresentation of a bit 
      string that is four bits long, with each bit set to 1 if the appropriate 
      mode is supported. Those mixes returned as supported are guaranteed for 
      all primitive types.  
  CAPS_VIO_LOADABLE_FONTS 
    Number of fonts that can be loaded for VIO. 
  CAPS_WINDOW_BYTE_ALIGNMENT 
    Whether or not the client area of VIO windows should be byte-aligned: 
    CAPS_BYTE_ALIGN_REQUIRED 
      Must be byte-aligned. 
    CAPS_BYTE_ALIGN_RECOMMENDED 
      More efficient if byte-aligned, but not required. 
    CAPS_BYTE_ALIGN_NOT_REQUIRED 
      Does not matter whether byte-aligned. 
  
  CAPS_BITMAP_FORMATS 
    Number of bit-map formats supported by device. 
  CAPS_RASTER_CAPS 
    Capability for device raster operations: 
    CAPS_RASTER_BITBLT 
      1 if GpiBitBlt and GpiWCBitBlt supported 
    CAPS_RASTER_BANDING 
      1 if banding is supported 
    CAPS_RASTER_BITBLT_SCALING 
      1 if GpiBitBlt and GpiWCBitBlt with scaling supported. 
    CAPS_RASTER_SET_PEL 
      1 if GpiSetPel supported. 
    CAPS_RASTER_FONTS 
      1 if this device can draw raster fonts. 
    CAPS_RASTER_FLOOD_FILL 
      1 if GpiFloodFill is supported. 
  CAPS_MARKER_HEIGHT 
    Default marker-box height in pels. 
 
  CAPS_MARKER_WIDTH 
    Default marker-box width in pels. 
  CAPS_DEVICE_FONTS 
    Number of device-specific fonts. 
  CAPS_GRAPHICS_SUBSET 
    Graphics drawing subset supported. (3 indicates GOCA DR/3) 
  CAPS_GRAPHICS_VERSION 
    Graphics architecture version number supported. (1 indicates Version 1) 
  CAPS_GRAPHICS_VECTOR_SUBSET 
    Graphics vector drawing subset supported. (2 indicates GOCA VS/2) 
  CAPS_DEVICE_WINDOWING 
    Device windowing support: 
    CAPS_DEV_WINDOWING_SUPPORT 
      1 if device supports windowing. Other bits are reserved 0. 
  CAPS_ADDITIONAL_GRAPHICS 
    Additional graphics support: 
    CAPS_GRAPHICS_KERNING_SUPPORT 
      1 if device supports kerning. 
    CAPS_FONT_OUTLINE_DEFAULT 
      1 if device has a default outline font. 
    CAPS_FONT_IMAGE_DEFAULT 
      1 if device has a default image font. 
    CAPS_SCALED_DEFAULT_MARKERS 
      1 if default markers are to be scaled by the marker-box attribute. 

                                      -10-

    CAPS_COLOR_CURSOR_SUPPORT 
      1 if device supports colored cursors. 
    CAPS_PALETTE_MANAGER 
      1 if device supports palette functions. 
    CAPS_COSMETIC_WIDELINE_SUPPORT 
      1 if device supports cosmetic thick lines  
    CAPS_ENHANCED_TEXT 
      1 if device supports full font file description and text alignment. 
      Other bits are reserved 0. 
  CAPS_PHYS_COLORS 
    Maximum number of distinct colors available on the device. 
  CAPS_COLOR_INDEX 
    Maximum logical color-table index supported for this device. For the EGA 
    and VGA drivers, the value is 63. 
  CAPS_GRAPHICS_CHAR_WIDTH 
    Default graphics character-box width, in pels. 
  CAPS_GRAPHICS_CHAR_HEIGHT 
    Default graphics character-box height, in pels. 
  
  CAPS_HORIZONTAL_FONT_RES 
    Effective horizontal device resolution in pels per inch, for the purpose 
    of selecting fonts. For printers, this is the actual device resolution, 
    but for displays it may differ from the actual resolution for reasons of 
    legibility. 
  CAPS_VERTICAL_FONT_RES 
    Effective vertical device resolution in pels per inch, for the purpose of 
    selecting fonts. 
  CAPS_DEVICE_FONT_SIM 
    Identifies which simulations are valid on device fonts. Valid flags are: 
    CAPS_DEVICE_FONT_SIM_BOLD 
    CAPS_DEVICE_FONT_SIM_ITALIC 
    CAPS_DEVICE_FONT_SIM_UNDERSCORE 
    CAPS_DEVICE_FONT_SIM_STRIKEOUT 
  CAPS_LINEWIDTH_THICK 
    Cosmetic thickness of lines and arcs on this device, when fxLineWidth is   
    LINEWIDTH_THICK. The units are pels.  A value of 0 is interpreted as 2 
    pels.  

  If you select another printer or change the Job properties of the currently 
  selected printer these variables are updated. You use these variables to 
  position graphics on a page (e. g. to determine the boundaries of a page).

The fourth variable hcPrn is a handle to the printer device context. You need
this handle when you want to print bitmaps.


5. Compiling, installing and using the library
==============================================

The source code of the library and the sample programs Hello queue/2 include
makefiles. The makefiles require the include file ibmc.inc which must be 
copied to an include path. (e. g. \IBMC\INCLUDE for the IBM C Set/2 1.0 
compiler). To create the DLL and the import library type NMAKE at the command 
prompt. Then you have to copy the file PRINTQ.DLL to a path that is included in 
the LIBPATH statement of your CONFIG.SYS file (e. g. \OS2\DLL). To use the 
library in an application you have to copy the created import library PRINTQ.LIB 
to a directory where your C compiler searches for libraries (e. g. \IBMC\LIB). 
You also have to copy the file PrintQ.h to a path where your C compiler searches 
for include files (e. g. \IBMC\INCLUDE). In every C source code file that uses 
PrintQ library functions you have to insert the following line

#include <printq.h>

The file PRINTQ.H contains function prototypes and the definition of the 3 
variables. Makes sure that you add the name of the import library file 
PRINTQ.LIB when linking the .obj files. You have to use the system linkage
convention (IBM C Set/2 1.0 compiler option /Ms) instead of optlink.
                                      -11-

6. Multithreading considerations
================================

If spooling a print job in your application takes considerably longer than a 
few seconds you might want to use a secondary thread to print from your 
application so that the system queue is not blocked while you are printing. 
Please note that if you use a normal presentation space and you have started a 
print job the presentation space is not associated with your screen until you 
call either SpoolAbortSpool or SpoolEndSpool so you must think of a way to 
synchronize painting and printing. You could for instance obtain a cached 
micro-presentation space when printing and just paint the window with 
SYSCLR_WINDOW in the meantime. 

The first two samples do not print in secondary threads so if you plan to do so 
in your application, have a look at Hello queue/2 1.2 in \HELLOQMT. 

Here is a short description of the program:

In your primary thread a flag fPrintThreadStarted indicates if there is a 
secondary print thread. This variable is initialised as FALSE. In response to 
a Print-WM_COMMAND message you set this variable TRUE. Then you create a 
thread for the printing function Print(). While the printing flag is set you 
must not allow your primary thread to modify the data that is being printed in 
any way. It's a good idea to gray the menu items that change the data and the 
Print menu item. In our sample application only the Printer setup choice can 
change the data so it is grayed. The Print item has to be grayed because we 
only allow one secondary thread at a time which is not a limitation. It is a 
good idea to include an Abort print job choice in your File menu. This choice 
is enabled when a print job has been started. You can determine whether or 
not a job has been started using the SpoolIsJobStarted() function. We use this 
function when processing the WM_INITMENU function. In response to the Abort 
print job WM_COMMAND message we use the SpoolAbortSpool function to abort the 
printing process. You can also use the SpoolIsJobStarted function in your 
printing function to determine - while calling GpiFunctions - if the job has 
been aborted. If SpoolIsJobStarted returns FALSE then you post a "Job done" 
message to your application window. I think this is quite an elegant 
alternative to the modal dialog box in Windoze. In the secondary thread after 
everything is printed and before it terminates you should as mentioned before 
post a message to your main window procedure to report that the job has been 
done. In response to that you set the printing flag fPrintThreadStarted to 
FALSE. This is a very simple communication pattern that works fine for 
communication with secondary threads. You just have to check the return code of 
WinPostMsg because in the (unlikely) event that your message queue is full your 
printing flag is never reset because you lost the message posted by the printing 
function. Hence I suggest something like this when using WinPostMsg to ensure 
that a message is posted sucessfully:

  while (!WinPostMsg(hwndMain, WMP_PRINT_JOB_DONE, NULL, NULL))
    DosSleep(BACKOFF_TIME);

When your primary window is destroyed (i.e. in the course of processing the 
WM_DESTROY message) you have to wait for the print thread to terminate. 

If you have to use _beginthread to start your printing thread you must use the 
_Optlink keyword to specifiy the oplink linkage convention otherwise the 
compile will report an error if you use the /Ms option for system linkage. 
You must not use the optlink convention for your entire program just for your 
Print thread if started with _beginthread otherwise parameter passing to 
PrintQ functions does not work. You specifiy optlink for a print function 
called Print as follows:
void _Optlink Print(void *arg);



                                      -12-

7. e-mail
=========

Your e-mail is appreciated if you have any comments, suggestions or questions.

Peter Wansch
Vienna, Austria
e-mail p.wansch@ieee.org
























































                                      -12-