*** OS/2 Profiler ***

  These files are the source code for very simple profiler for OS/2.  Yes,
I admit, it's a kludge; but it works.

  The profiler itself runs as a process seperate from the program being
profiled.  It creates a small shared memory segment and runs at a time-critical
priority.  It keeps looking at a SHORT variable in the memory segment and
maintains a histogram of the values found in the variable.  When it finds
an exit code in the variable, or it receives a ^C, it exits and prints out
a frequency distribution of the values it found in the variable.

  The program being profiled must be slightly modified to include the code
at function entry and exit to update the variable, and the code to access
and free the shared memory segment.

  I wrote the profiler to help in speeding up a batch program that ran at
a glacial rate, and it met the objective perfectly.  The profiler can easily
be extended to handle multi-thread programs and recursive function calls.
I release this program to the public domaine.  May it be useful to other
OS/2 programmers.  Comments and suggestions are welcome.

      Andrew Goodman
      Compuserve 72010,3113


                      *** Instructions ***

--- To prepare:

A.  Compile the profiler

    Study the profiler code (PROFILE.C) and the include file (PROFILE.H).
    Compile.  I used the large model.

B.  Modify the target file

    1.  Add the statement "#define PROFILE 1" *before* including PROFILE.H
        in every module.  To turn off the inclusion of profiler code in the
        target functions, comment out this define.

    2.  Include PROFILE.H in every module.

    3.  Add the variable  "PROMESSAGE   *pPM;"

    4.  Add the functions "fnusIPro" and "fnvXPro" to at least one module

    5.  Modify all the functions.  As the first line of each function after
        any local variable declarations, add the line "ENTER(x);", where
        x is a sequential number starting at 1.  Don't add ENTER to main().
        add the line "LEAVE;" at every exit point except in main().  Needless
        to say, be careful: if you miss a function entry or exit, you will
        blow out the profiler stack.

    6.  If needed, modify the target program so that it will run for 3-5
        minutes.  The profiler does not look very often (by machine speeds)
        to see what function is running, so you need a large sample set
        for significant results.

    7.  Compile.  I used the large model.


--- To use:

    A.  Run the profiler in an OS/2 command window.  You will probably want
        to pipe the output to a file.

    B.  Run the target in a seperate session.

    C.  When the target completes, check the profiler output.