These files have been uploaded in response to message #36711 from Steve
Liberty 71450,2341.  Since these are questions of a general interest, the
response has been posted here.

An example program is attached (files CLIENT.C and SERVER.C) that demonstrates
some of the concepts that are outlined in the answers to the following
questions about using queue's in OS/2.

For the sake of convenience, the contents of Steve's original question have
been included here.

>#: 36711 S8/OS/2
>    07-Oct-88  09:55:28
>Sb: Queue questions
>Fm: STEVE LIBERTY 71450,2341
>To: all
>
>I am playing around with Queues, and have several questions. If anyone can
>help me clear up my hazy understanding on this topic, I would greatly
>appreciate it.
>
>First, am I correct that the data being passed from one process to another
>must be passed in shared memory? It appears from the docs that the only data
>that can actually be contained in the queue packet is an unsigned event_code.
>So I assume that the data address field of the packet points into some shared
>memory. Is that right?

** Right; queues only pass the address of the data back and forth. It is
the responsibility of the process to set up a data transfer area- usually
a piece of shared memory.

>Next, if that is correct, what is the best way to handle the shared memory?
>Does it matter whether the reader or writer allocates the memory? Should it
>selector be accessed by the other via a DosGetShrSeg call?

** There are no hard and fast rules for this but the attached example uses
the method that you describe, namely that the client process opens the
shared segment and the server opens this segment using DosGetShrSeg.

>Finally, if all of the above is somewhat on track, once the selector is found
>say by the writer, how does he move a string into the shared memory? For
>example can he simply use strcpy? How is the selector converted into an
>address, and can that address be incremented by the string's length to get to
>the next slot?

** The best way to handle the allocation is to use DosSubAlloc to allocate
space for each object from within the client process and then have the
server process free this block when it is done reading the information.
Doing it this way insures that you will not have any data corruption and
freeing the memory after its use will return the memory to the pool for
subsequent writes (i.e. allocations) by the client process. As for the
actual transfer of information from the client to the shared segment,
memcpy or strcpy work fine for this. The attached example use strcpy
because the information transfered is a string.

Here is how to use the attached example: Compile CLIENT.C and SERVER.C
seperatly with /AL (large model). Detach CLIENT.EXE and then run SERVER.EXE.
Alternately, you can run CLIENT.EXE in one screen group, switch to another
and run SERVER.EXE.

If you have any other questions or problems, let us know.