DOS32  Version  3.0

                    Applications Program Interface (API)
                         
                             10th March 1995

            Copyright (C) 1994  Adam Seychell,  All Rights Reserved.






     This document contains detailed information of the DOS32 API with each
function obeying the following rules.

 1) All services are invoked from software interrupts 31h or 21h.
 2) All parameters are passed through registers.
 3) All services will preserve registers which are not returned with any      
  value. 
 4) Each function listed here has the minimum DOS32 version number needed on  
  the right hand side of it's heading.
 5) Never call a service in a protected mode interrupt handler
    unless otherwise said it is safe to do so.






                 The Interrupt 31h services.

The following list of services are called from a INT 31h with AX containing
the function number. 





                 GET DOS32 VERSION AND SELECTOR VALUES                  V3.0+

  IN:     AX = EE00h

 OUT:     AL = minor version  ( BCD )     currently 00
          AH = major version  ( BCD )        "      03
          DL = system type    1 = raw DOS
                              2 = XMS
                              4 = VCPI
                              8 = DPMI
          BX = Selector of 4GB data segment with zero base address.

  Notes:
        o This function may be called in a protected mode interrupt handler.











                    GET DOS32 ADDRESS INFORMATION                       V3.0+

 IN:    AX = EE02h

 OUT:   EBX = 32bit linear address of the program segment
        EDX = Total size in bytes of the programs .EXE file after linking.
        ESI = Offset address of PSP ( Program Segment Prefix )
        EDI = Offset address of Program Environment
        ECX = Offset address of the programs .EXE file name and path
                    ( in ASCIZ format, i.e. terminates with a zero )

  Notes:
  o   All offset addresses returned are relative to the main program
      segment.
  o   The .EXE file size is generally used for loading extra data
      appended to the original application's .EXE file.
  o   The .EXE file name pointed by ECX is actually the file name contained  
      in the last string of the Environment segment pointed to by EDI.
  o   The PSP address points to the original PSP set up by DOS. Thus pointers
      stored in here still contain real mode (segment:offset) values.
      Also this PSP address may not be the same address returned by DOSs
      Int 21h AH=62h (Get PSP) since DOS32 may of been loaded by a parent
      stub program.
  o   This function may be called in a protected mode interrupt handler.










   GET A REAL MODE CALL BACK ADDRESS WITH IRET OR RETF STACK FRAME      V3.0+

     This service will return a real mode address which when called (in real
mode) will in turn call a protected mode procedure. The real mode address may
either be called with a REFF or IRET stack frame, i.e far CALL or an
interrupt.


  Expects:     AX = EE20h     ( for an RETF frame )
               AX = EE21h     ( for an IRET frame )
               ESI -> Offset address of the protected mode procedure to be
                      invoked when the real mode address is called.
                      The procedure must exit with a FAR return.


  Returns:
               If function was successful:
               Carry flag is clear.
               CX:DX = The real mode far pointer ( SEG:OFFSET ) to
                     call the protected mode procedure.

               If function was not successful:
               Carry flag is set.








Notes:
    o   This function will fail if it's called more than 30 times.
    o   The protected mode procedure must exit with a FAR return instruction.
    o   The procedure is called undefined selectors in all segment register 
        ( ES,DS,FS,GS & SS ) and must preserve any segment registers it       
        modifies.
    o   EAX, EBX, ECX, EDX, ESI, EDI, EBP registers and flags will be
        preserved across the mode switch.
    o   This function can be used to hook a Real Mode interrupt by setting    
        the real mode interrupt vector to point to the real mode address 
        (CX:DX) returned by this function. See examples on how this may be    
        done.










                      TERMINATE AND STAY RESIDENT                       v3.0+

   This service will terminate the application to DOS but leaving it
   resident in memory.

 IN:   AX  = EE30h

 OUT:  Never returns

 Notes:
   o   All memory allocated from functions AX=0EE42h ( memory block ) and
       AX=EE41h ( DMA buffer ) will not be freed and stay allocated.
   o   This service may come in handy. Now....  what could you write with a
       multi megabyte TSR ??





























             UNDO PREVIOUS MEMORY ALLOCATION or DMA BUFFER              v3.0+

        This function will free the previously allocated memory block
( function AX =EE41h ) or DMA buffer ( function AX=EE42h ). If this
function is called multiple times then memory will be deallocated in
reverse order to when allocated. For example, if a memory block was
allocated followed by a DMA buffer then at first time this function
is called the DMA buffer would be freed, a second call to this function
will free the memory block, a third call will return an error ( Carry set )
because at this point no memory is being allocated.

 IN:  AX = EE40h

 OUT:  If function successful carry flag is cleared
       If unsuccessful the carry flag is set

 Notes:
    o   This function will fail if there is no memory allocated.
    o   All memory will automatically be freed when then application
        terminates.





              16KB BLOCK  ALLOCATION  FOR  DMA  CONTROLLER              V3.0+

       This function allocates a DMA buffer allowing the application
       to do DMA transfers of up to 16KB at a time.

  Expects:     AX = EE41h

  Returns:
               If function was successful:
               Carry flag is clear.
               EBX = Physical address of a contiguous 16KB memory block
                     that dose not cross a 64KB boundary and has a
                     physical address in the lower 16MB.
               EDX = Near pointer to the base address of the block
                     relative to the main program segment.

               If function was not successful:
               Carry flag is set.


NOTES: o  The 16Kb block will not cross a physical 64KB boundary and will
          have a base address aligned on a 4 byte boundary. This is just
          what DMA needs!.
       o  If the carry flag is set then there was not enough memory to
          allocate the DMA block otherwise the carry flag is cleared.
       o  If the application needs to do use more than one DMA channel at
          the same time ( e.g reading floppy disk at the same time as
          sending music to a sound card ) then a buffer should be allocated
          for each channel used.
       o  If all the memory was allocated by the Allocate Memory service
          ( AX=0EE42h ) then this function will fail. Your application
          should allocate it's DMA buffers before is tries to allocate large
          blocks with the AX=0EE42h function.







       o  If you need to send large amounts of memory via DMA to a device
          then it will have to be done in 16KB blocks. I know this sounds
          very inefficient but I done tests and found that I could not
          even measure the speed increase between 1Kb blocks to 128Kb blocks.
          Only a noticeable slow down occurred when transferring with blocks
          of 100 bytes or less. In fact the time it takes to program the DMA
          controller and move a 16KB block to the buffer ( using REP MOVSD )
          is under %1 of the DMA transfer time. In other words, it will be
          less than %1 slower using a buffer as opposed to transferring DMA
          directly to/from the data area.






                       ALLOCATE A MEMORY BLOCK                   V3.0+

        The entire application code,data and stack is initially contained in
one large memory block. This service here is used for allocating extra
memory blocks for the application.


 IN:  AX = EE42h
      EDX = Size of the memory block requested to allocate in bytes.

 OUT:
      EAX = The actual allocated size of the memory block in bytes
      EDX = Near pointer to the base address of the block relative
            to the main program segment.

      If the returned size was less than the requested size then the
      Carry flag is set otherwise the carry flag is cleared.

 Notes:
   o  The value expected in EDX will be rounded off to the next 4KB
      boundary.  Example, allocating 51001h bytes will actually allocate
       52000h bytes.
   o  Never call this function in a interrupt handler or after using the 
      terminated and stay resident function ( AX=EE30h ).
   o  If EAX is returned with zero then no memory was allocated and
      contents of EDX are undefined.
   o  The function will fail if the requested size is zero.
   o  If your system happens to have 4Gb of RAM installed then
      only about 4032Mb of it can ever be allocated (sorry for those people:)
   o  No more than 64 allocations can be made.
   o  When not running under a DPMI server ( i.e  Raw,XMS or VCPI ) then
      extended memory is allocated before conventional memory is. For
      example, if there is no more extended memory free then conventional
      memory will be allocated. In either case DOS32 sets up the 386 page
      tables such that the allocated memory is addressed in a straight linear
      block when it may actually be physically scattered throughout RAM.













                The Interrupt descriptor table services


     These services allow the application to get and set vectors of the 
protected mode interrupt descriptor table. The hardware interrupt  vectors
will always be set the default values.  i.e IRQs 0..7 map  onto CPU
interrupts 8..15 and IRQs 8..15 map onto CPU interrupts 70h..77h.
         All protected mode interrupt vectors will initially reflect to the
same interrupt in real mode. In other words a switched to and from real mode  
is automatically made when a protected mode interrupt is called. The
registers EAX,ECX,EDX,EBX,EBP,ESI,EDI and flags will be preserved across the
mode switch. The exception to this rule are protected mode interrupts
0,1,3,4,5,6 and 7. These are exceptions and will terminate the program
reporting with an error on the screen.
     Hardware interrupt handlers will be called with undefined selectors in
all data segment registers. The interrupt handler must preserve all modified
general registers and segment registers before it returns from the interrupt.
     The application is responsible for returning the original interrupt
vectors before the application terminates. It is only necessary do to this
when running under a DPMI server. However, for reliability, ALL modified
interrupt vectors should be restored to their original value.





       GET PROTECTED MODE INTERRUPT VECTOR                              V3.0+

 IN:  AX = 0204h
      BL = interrupt

 OUT: EDX = The 32 bit Offset of the vector
      CX =  Selector of vector





       SET PROTECTED MODE INTERRUPT VECTOR                              V3.0+

 IN:  AX = 0205h
      BL = interrupt
      EDX = The 32 bit Offset of the vector
      CX =  Selector of vector  ( must be a code selector )

 OUT: nothing



















                           Real Mode Call Services

     The following three services are used for calling real mode programs 
(e.g a DOS call or a device driver). Each of these services expects a pointer
to a real mode call structure whish is used to passing all registers to and
from the real mode switch. The format of the structure is defined as:


                              Offset      Register

                                00h         EDI
                                04h         ESI
                                08h         EBP
                                0Ch  Reserved by system
                                10h         EBX
                                14h         EDX
                                18h         ECX
                                1Ch         EAX
                                20h         Flags
                                22h         ES
                                24h         DS
                                26h         FS
                                28h         GS
                                2Ah         IP
                                2Ch         CS
                                2Eh         SP
                                30h         SS



-----------------------------------------------------------------------------
              Simulate a Real Mode interrupt                            V3.0+

IN:
        AX = 0300h
        BL = Interrupt number
        BH = Flags
             Bit 0  = 1 resets the interrupt controller and A20
             line
             Other flags reserved and must be 0
       CX =   Number of  words to  copy from  protected mode to
             real mode stack
       ES:EDI = Selector:Offset of real mode call structure

OUT:

      If function was successful:
      Carry flag is clear.
      ES:(E)DI =  Selector:Offset of  modified real mode call
       structure

      If function was not successful:
       Carry flag is set.












-----------------------------------------------------------------------------
      Call Real Mode Procedure With Far Return Stack Frame              V3.0+

IN:
        AX = 0301h
        BH = Flags
             Bit 0  = 1 resets the interrupt controller and A20
             line
             Other flags reserved and must be 0
       CX =   Number of  words to  copy from  protected mode to
             real mode stack
       ES:EDI = Selector:Offset of real mode call structure

OUT:

      If function was successful:
      Carry flag is clear.
      ES:EDI =  Selector:Offset of  modified real mode call
       structure

      If function was not successful:
       Carry flag is set.








-----------------------------------------------------------------------------
         Call Real Mode Procedure With IRET Stack Frame                 V3.0+

IN:
        AX = 0302h
        BH = Flags
             Bit 0  = 1 resets the interrupt controller and A20
             line
             Other flags reserved and must be 0
       CX =   Number of  words to  copy from  protected mode to
             real mode stack
       ES:EDI = Selector:Offset of real mode call structure

OUT:

      If function was successful:
      Carry flag is clear.
      ES:EDI =  Selector:Offset of  modified real mode call
       structure

      If function was not successful:
       Carry flag is set.













                        The 32 bit DOS type services

     The following services are like a protected mode version of DOS's
services. They are called the same way as in real mode where AH=function and
invoked with INT 21h. These services work exactly the same as calling the
DOS services in real mode except 32bit registers and protected mode far
pointers ( selector:offset ) are used. For a more detailed description of how
the services work please refer to DOS programming documentation. The
description below is only to show the use of 32 bit registers.

NOTE:  If an INT 21h function is called and is not described here then the
       interrupt is done in real mode with all the registers passed to
       from the call. This is also the case for any other protected mode
       interrupt, not just INT 21h!.




 


-----------------------------------------------------------------------------
         WRITE STRING TO STANDARD OUTPUT                                V3.0+
     AH = 09h
     DS:EDX -> '$'-terminated string


-----------------------------------------------------------------------------
         CREATE SUBDIRECTORY                                            V3.0+
     AH = 39h
     DS:EDX -> Selector:Offset of ASCIZ pathname
Return: CF clear if successful
         AX destroyed
     CF set on error
            AX = error code (03h,05h)


-----------------------------------------------------------------------------
         REMOVE SUBDIRECTORY                                            V3.0+
        AH = 3Ah
        DS:EDX -> Selector:Offset ASCIZ pathname of directory to be removed
Return: CF clear if successful
         AX destroyed
     CF set on error
            AX = error code (03h,05h,06h,10h)


-----------------------------------------------------------------------------
         CHANGE SUBDIRECTORY                                            V3.0+
        AH = 3Bh
        DS:EDX -> ASCIZ pathname to become current directory (max 64 bytes)
Return: CF clear if successful
         AX destroyed
     CF set on error
            AX = error code (03h)










-----------------------------------------------------------------------------
         CREATE OR TRUNCATE FILE                                        V3.0+
     AH = 3Ch
     CX = file attributes
     DS:EDX -> Selector:Offset ASCIZ filename
Return: CF clear if successful
         AX = file handle
     CF set on error
            AX = error code (03h,04h,05h)


-----------------------------------------------------------------------------
         OPEN EXISTING FILE                                             V3.0+
     AH = 3Dh
     AL = access and sharing modes
     DS:EDX -> Selector:Offset ASCIZ filename
     CL = attribute mask of files to look for (server call only)
Return: CF clear if successful
         AX = file handle
     CF set on error
            AX = error code (01h,02h,03h,04h,05h,0Ch,56h)


-----------------------------------------------------------------------------
         READ FROM FILE OR DEVICE                                       V3.0+
     AH = 3Fh
     BX = file handle
     ECX = number of bytes to read  ( may be zero )
     DS:EDX -> Selector:Offset buffer for data
Return: CF clear if successful
         EAX = number of bytes actually read (0 if at EOF before call)
     CF set on error
            AX = error code (05h,06h)


-----------------------------------------------------------------------------
      WRITE TO FILE OR DEVICE                                           V3.0+
     AH = 40h
     BX = file handle
        ECX = number of bytes to write
        DS:EDX -> Selector:Offset data to write
Return: CF clear if successful
         EAX = number of bytes actually written
     CF set on error
            AX = error code (05h,06h)


-----------------------------------------------------------------------------
      DELETE FILE                                                       V3.0+
     AH = 41h
        DS:EDX -> Selector:Offset ASCIZ filename (no wildcards )
Return: CF clear if successful

        CF set on error
            AX = error code (02h,03h,05h)










-----------------------------------------------------------------------------
         SET CURRENT FILE POSITION                                      V3.0+
     AH = 42h
     AL = origin of move
         00h start of file
         01h current file position
         02h end of file
     BX = file handle
     EDX = offset from origin of new file position
Return: CF clear if successful
            EAX = new file position in bytes from start of file
        CF set on error
            AX = error code (01h,06h)
Notes:    The normal real mode DOS function uses CX:DX as the position of
          the file to seek and returns DX:AX with the new value of the
          position. This protected mode version uses EDX in place of
          CX:DX and uses EAX in place of DX:AX.




-----------------------------------------------------------------------------
      GET FILE ATTRIBUTES                                               V3.0+
     AX = 4300h
        DS:EDX -> Selector:Offset ASCIZ filename
Return: CF clear if successful
            CX = file attributes

         AX = CX (DR-DOS 5.0)
     CF set on error
            AX = error code (01h,02h,03h,05h)



-----------------------------------------------------------------------------
      SET FILE ATTRIBUTES                                               V3.0+
     AX = 4301h
        CX = new file attributes
        DS:EDX -> Selector:Offset ASCIZ filename
Return: CF clear if successful
         AX destroyed
     CF set on error
            AX = error code (01h,02h,03h,05h)



-----------------------------------------------------------------------------
      GET CURRENT DIRECTORY                                             V3.0+
     AH = 47h
     DL = drive number (00h = default, 01h = A:, etc)
        DS:ESI -> Selector:Offset 64-byte buffer for ASCIZ pathname
Return: CF clear if successful
         AX = 0100h (undocumented)
     CF set on error
            AX = error code (0Fh)










-----------------------------------------------------------------------------
      LOAD AND/OR EXECUTE PROGRAM                                       V3.0+
     AH = 4Bh
     AL = type of load
         00h load and execute
         01h load but do not execute
     DS:EDX -> ASCIZ program name (must include extension)
     DS:EDI -> Program environment to copy for child process (copy caller's
                environment if EDI = zero )
     DS:ESI -> pointer to command tail to be copied into child's PSP
Return: CF clear if successful

        CF set on error
            AX = error code (01h,02h,05h,08h,0Ah,0Bh)

Notes:  Unlike DOS's 4Bh function this does not require a parameter block
        to be set up. The environment and command tail are pointed to by
        DS:EDI and DS:ESI respectively. See the examples distributed with     
        DOS32 on how this function may be used.




-----------------------------------------------------------------------------
      TERMINATE WITH RETURN CODE                                        V3.0+
     AH = 4Ch
     AL = return code
Return: never returns

Notes:
    o   DOS32 applications MUST ALWAYS terminate with this call.
    o   All memory allocated ( including DMA buffers ) will automatically
        be freed when the application terminates with this call.




-----------------------------------------------------------------------------
      FIND FIRST MATCHING FILE                                          V3.0+
     AH = 4Eh
     CX = file attribute mask
        DS:EDX -> ASCIZ file specification (may include path and wildcards)
Returns:   CF clear if successful
           The DTA ( Disk Transfer Area ) is filled with file information.
        CF set on error
          AX = Error code (02h, 03h, or 12h)

Notes:
        The DTA is set to the default area which is at offset 80h in the
        Program Segment Prefix (PSP). See function INT 31h AX=EE02h for       
        obtaining the PSP address.














-----------------------------------------------------------------------------
         RENAME FILE                                                    V3.0+
     AH = 56h
        DS:EDX -> ASCIZ filename of existing file (no wildcards )
        ES:EDI -> ASCIZ new filename (no wildcards)
     CL = attribute mask
Return: CF clear if successful
     CF set on error
            AX = error code (02h,03h,05h,11h)



-----------------------------------------------------------------------------
         CREATE TEMPORARY FILE                                          V3.0+
     AH = 5Ah
        CX = file attribute
        DS:EDX -> ASCIZ path ending with a '\' + 13 zero bytes to receive the
          generated filename
Return: CF clear if successful
         AX = file handle opened for read/write in compatibility mode
            DS:EDX pathname extended with generated name for temporary file
     CF set on error
            AX = error code (03h,04h,05h)





-----------------------------------------------------------------------------
         CREATE NEW FILE                                                V3.0+
     AH = 5Bh
        CX = file attribute
        DS:EDX -> ASCIZ filename
Return: CF clear if successful
         AX = file handle opened for read/write in compatibility mode
     CF set on error
            AX = error code (03h,04h,05h,50h)



                              <END OF API.DOC>