SCSIUtil V2.0 - an utility for doing SCSI low level operations


SCSIUtil (c) 1991,92,93,94 by Gary Duncan and Heiko Rath


	Gary Duncan
	Philips PTS
	23 Lakeside Dr
	Tally-Ho Technology Park
	Burwood East Vic 3151
	Australia

	EMail: gduncan@philips.oz.au


	The Software Brewery
	Dipl. Inform. (FH) Heiko Rath
	Raiffeisenstr.10a
	D-64331 Weiterstadt
	Germany

	EMail: hr@brewhr.swb.de


 BECAUSE THE PROGRAM IS LICENSED FREE OF CHARGE, THERE IS NO WARRANTY
 FOR THE PROGRAM, TO THE EXTENT PERMITTED BY APPLICABLE LAW.  EXCEPT
 WHEN OTHERWISE STATED IN WRITING THE COPYRIGHT HOLDERS AND/OR OTHER
 PARTIES PROVIDE THE PROGRAM "AS IS" WITHOUT WARRANTY OF ANY KIND,
 EITHER EXPRESSED OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE
 IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR
 PURPOSE.  THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF THE
 PROGRAM IS WITH YOU.  SHOULD THE PROGRAM PROVE DEFECTIVE, YOU ASSUME
 THE COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.

 IN NO EVENT UNLESS REQUIRED BY APPLICABLE LAW OR AGREED TO IN WRITING
 WILL ANY COPYRIGHT HOLDER, OR ANY OTHER PARTY WHO MAY MODIFY AND/OR
 REDISTRIBUTE THE PROGRAM AS PERMITTED ABOVE, BE LIABLE TO YOU FOR
 DAMAGES, INCLUDING ANY GENERAL, SPECIAL, INCIDENTAL OR CONSEQUENTIAL
 DAMAGES ARISING OUT OF THE USE OR INABILITY TO USE THE PROGRAM
 (INCLUDING BUT NOT LIMITED TO LOSS OF DATA OR DATA BEING RENDERED
 INACCURATE OR LOSSES SUSTAINED BY YOU OR THIRD PARTIES OR A FAILURE
 OF THE PROGRAM TO OPERATE WITH ANY OTHER PROGRAMS), EVEN IF SUCH
 HOLDER OR OTHER PARTY HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH
 DAMAGES.

 When redistributing this program ALWAYS redistribute the WHOLE
 archive consisting of:

 - DMakefile
 - HISTORY
 - o/SCSIutil.o
 - SCSI_priv.h
 - SCSIutil.c
 - TODO
 - SCSIutil.doc
 - smakefile

 The source is provided, therefore you can make changes yourself. The
 only thing I'm asking is that if you do make changes, please get in
 touch with me (hr@brewhr.swb.de), so that we can coordinate any
 further development.


What is SCSIUtil?
=================

 It is a little utility to do some low level stuff with SCSI devices.
 As I currently don't have too much time to work on it (I finished my
 thesis and am now wasting most of my time with a full time job)
 I release it to the public as it is. It is far from being perfect,
 but it is useful to me. In it's current incarnation it has
 the following features:

  - read the capacity of a SCSI device
  - read 16 bit raw digital audio off an audio CD (works with Sony CDU
    561 & 8003 & Toshiba 3401) (left/right channel and stereo
    reading supported)
  - read 16 bit raw digital audio off an audio CD and convert to 8 bit
    (left/right channel supported)
  - eject/insert a medium via software control
  - display the Inquiry data of a SCSI device
  - read & interpret a CD-ROM data block address header
  - start/stop the motor on a device
  - read pages via MODE SENSE
  - play audio on a CD-ROM drive (tested with Sony CDU 561 = Apple CD-300
    and Tosiba 3401)
  - read sectors
  - seek to a specified sector
  - display table of contents (TOC) of a CD
  - read subchannel information of a CD (tested with Sony CDU 561)
  - allow/prevent medium removal
  - change the output channel volume of a CD-ROM drive


Why SCSIUtil?
=============

 I needed some software to explore my new CD-ROM drive.

 Here is what SCSIUtil displays, if you invoke it without parameters:

SCSIutil V2.0 [Jan  4 1994 : 16:59:03] - written by Gary Duncan
         (gduncan@philips.oz.au) and Heiko Rath (hr@brewhr.swb.de)
Usage: SCSIutil [-dscsi_dev] <scsi_id> <command>
 -c[r]                 : Read capacity [raw]
 -d<l|r|s> sec blks sc : Read 16 bit digital audio(start sector/# blocks)(2)
 -D<l|r> sec blks      : Read  8 bit digital audio(left or right channel)(3)
 -e <0|1>              : Change medium (0=eject, 1=load)
 -i[r]                 : Inquiry [raw]
 -h[r] blk             : Read CD-ROM data block address header
 -l <0|1>              : Allow/Prevent medium removal
 -m <0|1>              : Stop/Start motor {0=stop, 1=start}
 -o[r] contr page      : Mode sense (contr = 0-3))
 -p st si et ei        : Play audio CD track (1-99), index (1-99)
 -r[t] sec_no          : Read sectors [use trackdisk.device]
 -s sec_no             : Seek to sector (5)
 -t[r|l]               : Display TOC of an audio CD [raw|long]
 -u[r] chan fmt track  : Read CD sub-channel information [raw] (6)
 -v [vl0 vl1 vl2 vl3]  : Set output volume channels 0-3 (7)

Note 1: usually scsi_id = (BOARD * 100) + (LUN * 10) + SCSI_TARGET_ID
     2: with 's' returns LRLRLR pairs of stereo audio, 2352 bytes per block
        sc = Apple subcode (0=2352, 1=2368, 2=2448, 3=96 byte/block)
     3: converted to 8 bit audio (-d and -D work with Sony CDU 561 & 8003)
     4: contr 0: current, 1: changeable, 2: default, 3: saved values
     5: to park heads, try sec_no of -1
     6: Q-channel = 64, fmt: 0=Sub-Q Channel data,1=current CD-ROM pos.,
        2=Media Catalog Number (UPC/Bar Code),3=Track ISRC
     7: use -1 to leave volume of channel as it is, without argument shows
        current volume settings

Documentation on the options of SCSIUtil:
=========================================

 -c[r]               : Read capacity [raw]

	This will issue a READ CAPACITY to the device to get the
	highest sector available, the sector size and the capacity
	(= sector size * max sector). With the 'r' option SCSIUtil
	will not try to interpret the returned data.

	BTW, the Apple CD-300 returns different sector sizes,
	depending on the last read size (that means sometimes it is
	96, 2048 or 2352).

 -d<l|r|s> sec blks sc : Read 16 bit digital audio(start sector/# blocks)(2)

	This will read data directly from the specified CD-ROM drive,
	interpreting the information as raw digital input. A value for
	the sector to start reading from is required as well as the
	number of sectors to read. The data will be in 16-bit format
	e.g.  SCSIutil 2 -ds 2 100 0 reads the first 100 blocks
	starting from sector 2 as Stereo 16 bit data. One sector
	corresponds to 1/75 of a second.  The data will be output to
	stdout.  This works with the Sony CDU-8003/541/561 (Apple uses
	the CDU-561 in their Apple CD-300).

	The sc parameter was tested with the Apple CD-300 and tells
	the drive to return 2352/2368/2448/96 bytes/block. If you're
	only interested in digital audio use sc=0 which just delivers
	588 * 16 bit stereo samples per block = 2352 bytes. If you use
	sc=1 the last 16 bytes contain information about the current
	track/index and timeposition of the sample. Sc = 2 adds 96
	bytes to the raw samples which supposedly contain all the
	subchannels except the Q-subchannel. Usually there won't be
	any useful data in these 96 bytes, but on CD+Graphics and
	CD+Midi CDs (pretty rare) the graphics/midi information is
	encoded. If anybody has some information regarding the
	encoding of CD+G / CD+Midi please get in touch with me!

	The digital audio data sent to stdout looks like this (in case
	of sc = 0):

	struct cdda_sector {
	  struct cdda_sample {
	    char left_channel_lsb;
	    char left_channel_msb;
	    char right_channel_lsb;
	    char right_channel_msb;
	  } samples[588];
	};

	With mono, either the left or right channel is skipped.

	BEWARE: sometimes I get SCSI bus lockups while using this
	command. I'm pretty sure that it's not SCSIUtil's fault, but
	either a problem of the WD SCSI chip 33C93A 00-04-PROTO in my
	Amiga 3000 or a firmware bug in the Apple CD-300 (my firmware
	is release 1.8d). The lockups usually occur only if I read
	more than about 150 sectors. When a lockup occurs, don't
	panic! I usually power cycle the Apple CD-300 and everything
	reverts to normal.  BTW, the Apple CD-300 sometimes returns
	the following MODE SENSE errors for no obvious reason:

	SENSE_DATA: 70 00 00 00 00 00 00 0a 00 00 00 00 00 00 00 00 00 00
	Error : err=45 , No error

	Since V1.905b SCSIUtil reschedules the failed SCSI command and
	tries to reread the missing sectors, thus you shouldn't lose
	any data. (When this happens you might notice a little glitch
	in the digital data, this is caused by the CD-ROM drive's
	inability to access a certain block directly - it might start
	reading +- n sectors before/after the requested block).

 -D<l|r> sec blks    : Read  8 bit raw digital audio(left or right channel)(*3*)

	Does basically the same as the '-d' option, only divides every
	16 bit word by 256 before sending it to stdout, which makes
	for a cheap (and suboptimal) conversion to 8 bit. The warning
	about SCSI bus lockups applies also to this command. A better way
	to scale to 8 bit would be to find the min/max values in the
	digital data and scale accordingly. Obviously you'd need another
	program to do this job, as otherwise you'd have to keep the
	whole sample in memory to perform this operation.

 -e <0|1>            : Change medium (0=eject, 1=load)

	By using this command you can eject a removable medium via
	software, e.g. SCSIutil 2 -e 0 ejects the CD-ROM currently in
	the drive with SCSI id 2.

 -i[r]               : Inquiry [raw]

	This command sends the INQUIRY command to the specified
	device. This can be used to get all kinds of information about
	the device. With the 'r' parameter SCSIUtil will not try to
	interpret the information returned.

 -h[r] blk           : Read CD-ROM data block address header

	This will read the address header information of a particular
	CD-ROM block, e.g. SCSIutil 2 -h 100 reads block 100 from SCSI
	device 2 and returns the header information.

 -l <0|1>            : Allow/Prevent medium removal

	This command sends a PREVENT ALLOW MEDIUM REMOVAL to the SCSI
	device.

 -m <0|1>            : Stop/Start motor {0=stop, 1=start}

	Start or stop the device motor of the specified device.
	SCSIutil 2 -m 0 stops a CD that is playing in SCSI device 2.

 -o[r] contr page    : Mode sense (contr = 0-3)) (*4*)

	Reads MODE SENSE control pages from a SCSI device. The contr
	parameter decides what pages to return:

	contr 0: current values
              1: changeable values (not interpreted correctly by SCSIUtil)
              2: default values
              3: saved values

	The page value must be in the range of 0-63. Page 63 usually
	returns all the available MODE SENSE pages.  With the 'r'
	option SCSIUtil will not interpret the returned data.

 -p st si et ei      : Play audio CD track (1-99), index (1-99)

	Allows the playing of a series of audio tracks. Can use index
	marks as well e.g. SCSIutil 2 -p 1 1 8 1 plays an Audio CD in
	SCSI device 5 from Track 1 to Track 8.
	Track and Index should be in the range of 1-99 (according to
	the ANSI SCSI 2 specs). The Apple CD-300 accepts an index of 0
	as play whole track, therefore I allowed the selection of 0 as
	an index, even though the online help states otherwise. To
	play a whole CD type: scsiutil 2 -p 1 0 99 0. To play only
	track 3: scsiutil 2 -p 3 1 3 1.

 -r[t] sec_no        : Read sectors [use trackdisk.device]

	Read data sector off a SCSI device. In case of an audio CD use
	the -d or -D commands to read digital audio data.

 -s sec_no           : Seek to sector (*5*)

	Seek the head of a device to the specified sector.

 -t[r|l]             : Display TOC of an audio CD [raw|long]

	Reads the table of contents of a CD. The TOC can contain
	entries for data/audio tracks.  With the 'r' option SCSIUtil
	won't interpret the returned data. With the 'l' option
	SCSIUtil will display the TOC in a longer form.

 -u[r] chan fmt track: Read CD sub-channel information [raw] (*6*)

	Reads information from the specified sub-channel of a CD.

	Chan = 64 = Q-Sub-channel
	Fmt 0: read Q-sub-channel
	 Doesn't work with the Apple CD-300 drive
	Fmt 1: read current position data
	 Track must be 0
	Fmt 2: read media catalog number (UPC/Bar Code)
	 Track must be 0
	Fmt 3: read track international standard recording code (ISRC)
	 Track must be a valid track

	With the 'r' option SCSIUtil doesn't try to interpret the
	returned data.

 -v [vl0 vl1 vl2 vl3]  : Set output volume channels 0-3 (7)

	Allows you to set the volume of the CD-ROM audio channels.
	Values in the range of 0-255 are allowed. If you use -1 this
	channel won't be affected. If -v is issued without additional
	parameter, SCSIUtil will display the current volume settings.

The future:
===========

 There are several things that I'd like to implement, take a look at
 the TODO file. If you have a need for some additional features you
 can always try to talk me into implementing them (hint: I can be
 bribed ;-)


Acknowledgements:
=================

 Fred Fish for his work for the Amiga community

 Gary Duncan (gduncan@philips.oz.au) for having written the original
	version and releasing the source to the public

 Dave Hassal (dave@ainfo.equinox.gen.nz) for bugging me with questions
	and pushing me into finishing SCSIUtil.

 Stefan Becker (stefanb@yello.adsp.sub.org) for supplying patches to allow
	reading of digital audio with the Toshiba XM3401 and DICE-support.

 Ralph Babel for some _very useful_ hints/tips/tricks.

 Franz-Josef Reichert for his Jukebox.

 Frank Munkert (ln_fmu@pki-nbg.philips.de) for AmiCDROM, PlayCDDA
	and some good suggestions.

 Free Software Foundation, Inc. for the no warranty text and use at
	your own risk texts. Also thanks for some high quality SW.

 My fellow Software Brewers (Christian Balzer & Armin Sparr) for
	support.