A
                                   Comparison
                                       of
    
    
          ===========================================================
          MM   MM  IIIIIII    CCCC   RRRRRR     OOO             CCCC
          M M M M     I      C    C  R     R   O   O           C    C
          M  M  M     I     C        R     R  O     O         C
          M     M     I     C        RRRRRR   O     O  -----  C
          M     M     I     C        R   R    O     O         C
          M     M     I      C    C  R    R    O   O           C    C
          M     M  IIIIIII    CCCC   R     R    OOO             CCCC
          ===========================================================
          
                                     A N D
          
          ===========================================================
           SSSSS   MM   MM     A     L        L                 CCCC
          S     S  M M M M    A A    L        L                C    C
          S        M  M  M   A   A   L        L               C
           SSSSS   M     M  A     A  L        L        -----  C
                S  M     M  AAAAAAA  L        L               C
          S     S  M     M  A     A  L        L                C    C
           SSSSS   M     M  A     A  LLLLLLL  LLLLLLL           CCCC
          ===========================================================
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1990,1991 Dave Dunfield
                              All rights reserved

    MICRO-C .vs. SMALL-C                                             Page: 1


    1. INTRODUCTION
    
          The most common reaction of people hearing about MICRO-C  for  the
       first time is something like "Humph... Another  version  of  the  old
       SMALL-C compiler". This couldn't be further from the truth.
    
                           MICRO-C IS NOT SMALL-C!!!
    
          MICRO-C is a completely  new  implementation  of  a  'C'  compiler
       suitable for use on very small systems. It offers several  advantages
       over SMALL-C:
    
        - It was designed from the  ground  up  to  be  easily  portable  to
          different processors & computer platforms. Sample code  generators
          are included for 8080, 8051, 80x86, 8096, 6809 and  68HC11  cpu's,
          and an entire section of the manual  is  devoted  to  porting  the
          compiler.
    
          Although SMALL-C claims  to  be  easily  portable,  much  of  it's
          arcitecture is oriented toward the original 8080 processor. For an
          example of  how  this  affects  the  compiler,  compare  the  code
          generated by the 8086 version of SMALL-C to reference stack (auto)
          variables to that produced by MICRO-C.
    
        - It is a more complete implementation of the 'C' language, see  the
          features comparison later in this document.
    
        - It produces faster, more compact code. See the  benchmark  results
          later in this document.
    
        - MICRO-C employs  a  fully  tokenized  parser,  allowing  statement
          analysis to be performed  on  16  bit  "tokens"  instead  of  text
          strings as is  done  in  SMALL-C.  This  results  in  MUCH  faster
          compilation.
    
        - Although it is higher in functionality than SMALL-C,  the  MICRO-C
          compiler is much smaller than SMALL-C (Nearly half the size). This
          allows it to run on very small computer systems.
    
    2. DETAILED COMPARISON OF COMPILERS
    
          The following pages contain a detailed comparison of  the  SMALL-C
       version 2 compiler, and MICRO-C.

    MICRO-C .vs. SMALL-C                                             Page: 2


       2.1 'C' Implementation
            =============================================================
            Data types              | SMALL-C V1 | SMALL-C V2 | MICRO-C |
            ------------------------+------------------------------------
            int                     |    Yes     |    Yes     |   Yes   |
            char                    |    Yes     |    Yes     |   Yes   |
            unsigned int            |     No     |     No     |   Yes   |
            unsigned char           |     No     |     No     |   Yes   |
            pointers                |    Yes     |    Yes     |   Yes   |
            pointers to pointers    |     No     |     No     |   Yes   |
            Single dimension arrays |    Yes     |    Yes     |   Yes   |
            Multi dimension arrays  |     No     |     No     |   Yes   |
            arrays of pointers      |     No     |     No     |   Yes   |
            Typecast                |     No     |     No     |   Yes   |
            sizeof                  |     No     |     No     |   Yes   |
            ========================+====================================
            Control Structures      | SMALL-C V1 | SMALL-C V2 | MICRO-C |
            ------------------------+------------------------------------
            if/else                 |    Yes     |    Yes     |   Yes   |
            while                   |    Yes     |    Yes     |   Yes   |
            do/while                |     No     |    Yes     |   Yes   |
            for                     |     No     |    Yes     |   Yes   |
            switch/case             |     No     |    Yes     |   Yes   |
            goto                    |     No     |    Yes     |   Yes   |
            Conditional Expressions |     No     |    Yes     |   Yes   |
            Inline assembler        |    Yes     |    Yes     |   Yes   |
            ========================+====================================
            Pre-processor           | SMALL-C V1 | SMALL-C V2 | MICRO-C |
            ------------------------+------------------------------------
            #define (basic)         |    Yes     |    Yes     |   Yes   |
            #define (Parameterized) |     No     |     No     |   Yes   |
            #define (Multi-line)    |     No     |     No     |   Yes   |
            #undef                  |     No     |     No     |   Yes   |
            #include (single level) |    Yes     |    Yes     |   Yes   |
            #include (nested)       |     No     |    Yes     |   Yes   |
            #ifdef/#ifndef          |     No     |    Yes     |   Yes   |
            ========================+====================================
            Misc features           | SMALL-C V1 | SMALL-C V2 | MICRO-C |
            ------------------------+------------------------------------
            Optimization            |     No     |    Yes     |   Yes   |
            Multiple memory models  |     No     |     No     |   Yes   |
            Make/touch utility      |     No     |     No     |   Yes   |
            Source linker           |     No     |     No     |   Yes   |
            6809 code generator     |     No     |     No     |   Yes   |
            68HC11 code generator   |     No     |     No     |   Yes   |
            8080 code generator     |    Yes     |    Yes     |   Yes   |
            8051 code generator     |     No     |     No     |   Yes   |
            8086 code generator     |     No     |    Yes     |   Yes   |
            8096 code generator     |     No     |     No     |   Yes   |
            ========================+====================================
            Library features        | SMALL-C V1 | SMALL-C V2 | MICRO-C |
            ------------------------+------------------------------------
            Complete standard lib   |     No     |    Yes     |   Yes   |
            Interrupt serial I/O    |     No     |     No     |   Yes   |
            Windowing library       |     No     |     No     |   Yes   |
            TSR support             |     No     |     No     |   Yes   |
            ========================+====================================

    MICRO-C .vs. SMALL-C                                             Page: 3


       2.2 Generated code quality
    
             To test the actual performace  of  code  generated  by  MICRO-C
          against  code  generated  by  SMALL-C,  I  used  this  "Sieve   of
          Eratosthenes" prime number generator program, taken from the  BYTE
          benchmarks:
    
    
    
    
    
    /*
     * The classic "Sieve of Eratosthenes" prime number program.
     * from BYTE, January 1983.
     */
    #include <stdio.h>
    #include "timer.c"          /* The timer subroutines */
    
    #define SIZE  8190
    #define LOOP  100
    #define TRUE  1
    #define FALSE 0
    
    char flags [SIZE + 1];
    
    main()
    {
        int i, prime, k, count, iter;
    
        printf("BYTE Sieve Benchmark - %d iterations\n",LOOP);
    
    /* Start timer and execute loop */
        startimer(timestamp);
        for(iter = 1; iter <= LOOP; ++iter) {
            count = 0;                          /* prime counter */
            for(i = 0; i <= SIZE; ++i)          /* set all flags true */
                flags [i] = TRUE;
            for(i = 0; i <= SIZE; ++i) {
                if(flags [i]) {                 /* found a prime */
                    prime = i + i + 3;          /* twice index + 3 */
    /*              printf ("\n%d", prime);     */
                for(k = i + prime; k <= SIZE; k+= prime)
                    flags [k] = FALSE;          /* kill all multiple */
                ++count; } } }                  /* primes found */
        elapsed(timestamp);                     /* Calculate time taken */
    
    /* Report results */
        printf("%d primes.\n\n", count);        /* primes found on 100th pass */
        printf("Elapsed time: %02d:%02d:%02d.%02d\n",
            timestamp[1], timestamp[0], timestamp[3], timestamp[2]);
    }

    MICRO-C .vs. SMALL-C                                             Page: 4


       2.3 Speed of compilation
    
             To show the relative compilation times,  I  wrote  this  simple
          MICRO-C program, using the timing routines shown below, to execute
          the compilers & report the time taken:
    
    
    
    
    
    #include <stdio.h>
    #include "timer.c"          /* The timer subroutines */
    
    main()
    {
        startimer(timestamp);
        system("CC SIEVE");             /* Execute the SMALL-C compiler */
        elapsed(timestamp);
        printf("Elapsed time: %02d:%02d:%02d.%02d\n\n",
            timestamp[1], timestamp[0], timestamp[3], timestamp[2]);
    
        startimer(timestamp);
        system("MCC SIEVE.C SIEVE.ASM");/* Execute the MICRO-C compiler */
        elapsed(timestamp);
        printf("Elapsed time: %02d:%02d:%02d.%02d\n",
            timestamp[1], timestamp[0], timestamp[3], timestamp[2]);
    }
    
             NOTE: The results from the above program will include the  time
          taken to load the compilers. To minimize this, all tests were  run
          from a RAMdisk. This eliminates disk seek time, and  reduces  load
          time to the speed of a memory to memory copy.

    MICRO-C .vs. SMALL-C                                             Page: 5


       2.4 Timing the tests
    
             These subroutines were used to time  the  programs,  using  the
          MS-DOS internal clock which has a resolution of 1/100 of a second:
    
    
    
    
    
    char timestamp[4];          /* Stores initial timestamp */
    
    /*
     * Record system time for later calculation
     */
    startimer() asm
    {
            MOV     AH,2CH      ; Get time function
            INT     21H         ; Ask DOS
            MOV     SI,4[BP]    ; Get pointer to timestamp
            MOV     [SI],CX     ; Record hours & minites
            MOV     2[SI],DX    ; Record seconds & hundreds
    }
    
    /*
     * Calculate elapsed time since timestamp recorded
     */
    elapsed() asm
    {
            MOV     AH,2CH      ; Get time function
            INT     21H         ; Ask DOS
            MOV     SI,4[BP]    ; Pointer to timestamp
            SUB     DL,2[SI]    ; Convert 100ths
            JNC     ELAP1       ; No borrow
            ADD     DL,100      ; Re-adjust
            DEC     DH          ; Reduce seconds
    ELAP1:  MOV     2[SI],DL    ; Save elapsed hundreds
            SUB     DH,3[SI]    ; Convert seconds
            JNS     ELAP2       ; No borrow
            ADD     DH,60       ; Re-adjust
            DEC     CL          ; Reduce minites
    ELAP2:  MOV     3[SI],DH    ; Save elapsed seconds
            SUB     CL,[SI]     ; Convert minites
            JNS     ELAP3       ; No borrow
            ADD     CL,60       ; Re-adjust
            DEC     CH          ; Adjust hours
    ELAP3:  MOV     [SI],CL     ; Save elapsed minites
            SUB     CH,1[SI]    ; Convert hours
            MOV     1[SI],CH    ; Save elapsed hours
    }

    MICRO-C .vs. SMALL-C                                             Page: 6


       2.5 Test results
    
             After compiling the programs, I ran  the  various  tests  on  a
          standard 8-Mhz IBM PC/AT, with these results:
    
    E:\>dir
    
     Volume in drive E is VDISK  V3.3
     Directory of  E:\
    
    CC       EXE    40626   9-10-90  /* SMALL-C compiler */
    MCC      COM    22316   9-10-90  /* MICRO-C compiler */
    TIMER    C       1094   9-10-90  /* The timer subroutines */
    TIMECOMP C        527   9-10-90  /* The compiler timer */
    SIEVE    C       1149   9-10-90  /* The test program */
    SIEVE-S  EXE    16946   9-10-90  /* SMALL-C produced this */
    SIEVE-M  COM     1651   9-10-90  /* MICRO-C produced this */
    TIMECOMP COM     1924   9-10-90  /* Executable compiler timer */
            8 File(s)    301056 bytes free
    
    E:\>sieve-s     /* The SMALL-C version: 1 min, 28.98 secs */
    BYTE Sieve Benchmark - 100 iterations
    1899 primes.
    
    Elapsed time: 00:01:28.98
    
    E:\>sieve-m     /* The MICRO-C version: 1 min, 4.59 secs */
    BYTE Sieve Benchmark - 100 iterations
    1899 primes.
    
    Elapsed time: 00:01:04.59
    
    E:\>
    
    **NOTE: Before running TIMECOMP, I created a "generic" STDIO.H
            file which was suitable for both compilers.
    
    E:\>timecomp    /* Times to compile the program */
    Small-C Compiler, Version 2.1, (Rev. 75)
    Copyright 1982, 1983, 1985 J. E. Hendrix
    Elapsed time: 00:00:04.72       /* SMALL-C 4.72 secs */
    
    MICRO-C 2.0 Compiler
    Copyright 1988,1990 Dave Dunfield
    All rights reserved.
    Elapsed time: 00:00:01.32       /* MICRO-C 1.32 secs */
    
    E:\>

    MICRO-C .vs. SMALL-C                                             Page: 7


    3. OTHER ADVANTAGES OF MICRO-C
    
          In addition to being a superiour and more portable  compiler,  The
       MICRO-C package also offers these advantages:
    
       3.1 Utilities
    
             MICRO-C Comes with the following utilities (all  with  complete
          MICRO-C source code):
    
        CC      - Command Coordinator, combines pre-processor, compiler,
                  optimizer, assembler and linker into a single command.
                  Command line parameters allow very flexible operation.
    
        MAKE    - Automates building of larger (multi module) programs.
    
        TOUCH   - Set timestamp of file to current or specified date.
                  (Used with MAKEs dependancy checking)
    
        SLINK   - Source LINKer, Allows pre-compiled (assembler) source to
                  be kept in a library and included as needed to resolve
                  external references. Useful when MICRO-C is used as cross
                  compiler for systems not supporting an object linker.
    
        SLIB    - Utility for updating and maintaining a source library.
    
        SINDEX  - Automatically indexes a source library for use by SLINK.
    
        SCONVERT- Converts assembly language source for use by SLINK.
    
        EXE2BIN - Converts MS-DOS EXE files to a binary image, useful for
                  users of later versions of DOS which no longer include
                  this utility.
    
        MCP     - The MICRO-C Pre-processor
    
        MCC     - The MICRO-C Compiler
    
        MCO     - The MICRO-C Optimizer

    MICRO-C .vs. SMALL-C                                             Page: 8


       3.2 Example Programs
    
             MICRO-C comes with the following  example  programs  (all  with
          complete MICRO-C source code):
    
    ASM86.C         An 8086 assembler
    BASIC.C         A simple BASIC interpreter
    CALC.C          A pop-up (TSR) calculator for programmers
    CASTLE.C        A large "adventure" game
    CHATTR.C        Chenges file attributes
    COMEXT.C        Extracts comment from 'C' programs
    CSET.C          A pop-up (TSR) PC character set
    CVTCOM.C        Convert C++ style '//' comments to C's '/* - */'
    DUMP.C          A HEX/OCTAL file dump utility
    EQUIP.C         Displays equipment installed in your PC
    FIBO.C          Calculates a fibonacci series
    FORTUNE.C       Displays a "fortune cookie" message every time it is run
    GREP.C          Unix like "grep" command from DECUS
    HANOI.C         Solves the "towers of hanoi" program on screen
    HELLO.C         Standard 'C' demo program
    HEM.C           Traps hardware fault interrupts
    HEXED.C         A full-screen hex file editor
    HFTEXT.C        Simple Huffman encoded for text files
    INSTALL.C       The Micro-Install program
    LZC.C           Laser Commander - pop-up (TSR) control for laser printer
    MTERM.C         A pop-up (TSR) ANSI terminal with XMODEM
    OBSCURE.C       Makes a 'C' program un-readable (it still compiles)
    PPC.C           Pretty-Printer for C
    PRIME.C         Calculates prime numbers
    RLTEXT.C        Simple Runn Length encoded for text files
    ROBOFACE.C      Draws a robot face on your BC screen
    TEXTNUM.C       Displays text equivalent of numbers
    TIMEIT.C        Time the execution of another command
    TR.C            Unix like "tr" command
    TTT3D.C         Three-Dimensional Tic-Tac-Toe
    TYPE4.C         Display a file with tabs at 4 character intervals
    VALIDATE.C      PD version McAfee's validate program, uses dual CRC's
    WINDEMO.C       MICRO-C window demonstration program




                              MICRO-C .vs. SMALL-C

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1


     2. DETAILED COMPARISON OF COMPILERS                                    1

        2.1 'C' Implementation                                              2
        2.2 Generated code quality                                          3
        2.3 Speed of compilation                                            4
        2.4 Timing the tests                                                5
        2.5 Test results                                                    6

     3. OTHER ADVANTAGES OF MICRO-C                                         7

        3.1 Utilities                                                       7
        3.2 Example Programs                                                8