41

                          CHAPTER 6 - MULTIPLICATION AND DIVISION



             Unlike addition and subtraction, where the result can be in
             either memory or in one of the registers, the multiplication and
             division instructions have a rigid format. 


             MULTIPLICATION

             You can multiply a one byte number by a one byte number and get a
             two byte result, or you can multiply a one word number by a one
             word number and get a two word result. The first number MUST be
             in AL for the byte operation or in AX for the word operation. The
             second number may be a register or a memory location (but not a
             constant). The result is in AH:AL for the byte operation and
             DX:AX for the word operation. Our possibilities are:

                      AL  X  (one byte register or memory)  ->  AH:AL
                      AX  X  (one word register or memory)  ->  DX:AX

             Is there a difference between signed and unsigned numbers? Yes, a
             very big difference. For the byte operation  FFh = -1 signed but
             FFh = 255 unsigned.  -1 X -1 = 1 = 0001h.  255 X 255 = 65025 =
             FE01h. These are two completely different answers. You need to
             tell the 8086 whether you want signed multiplication or unsigned
             multiplication. The 8086 does the rest. Let's look at both signed
             and unsigned multiplication. We'll do byte multiplication for
             unsigned numbers and word multiplication for signed numbers. The
             instruction for unsigned multiplication is MUL. The instruction
             for signed multiplication is IMUL. AX or AL is understood to be
             the register, so it is not in the code. The instructions are:

                 variable1  db ?
                 variable2  dw ?

                      mul  bx             ; unsigned word from a register
                      mul  variable1      ; unsigned byte from memory
                      imul ch             ; signed byte from a register
                      imul variable2      ; signed word from memory

             No AX or AL. It's understood. Here's our program:

             template.asm
             ; + + + + + + + + + + + + + + + START DATA BELOW THIS LINE 
             answer1      dw     ? 
             answer2      dw     ? 
             ; + + + + + + + + + + + + + + + END DATA ABOVE THIS LINE 

             ; - - - - - START CODE BELOW THIS LINE 
              
                    mov     cx, 0               ; clear cx for visual effect 

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                         42
             ______________________

              
             outer_loop: 
                    ; unsigned byte multiplication 
                    mov   ax_byte, 0A2h          ; half regs, unsigned 
                    mov   bx_byte, 0A2h          ; half regs, unsigned 
                    lea   ax, ax_byte 
                    call  set_reg_style 
              
                    mov   ax, 0               ; clear regs 
                    mov   bx, 0 
                    mov   dx, 0 
                    call  show_regs 
                     
                    call  get_unsigned_byte    ; get two unsigned bytes
                    call  show_regs 
                    push  ax                   ; save the first number
                    call  get_unsigned_byte 
                    mov   bl, al 
                    pop   ax                   ; restore the first number
                    call  show_regs_and_wait 
                    mul   bl                   ; unsigned multiplication
                    call  print_unsigned       ; display the result (ax)
                    call  show_regs_and_wait 
                     
              
                    ; signed word multiplication 
                    mov   ax_byte, 01h          ; full reg, signed 
                    mov   bx_byte, 01h  
                    mov   dx_byte, 01h
                    lea   ax, ax_byte 
                    call  set_reg_style 
              
                    mov   ax, 0               ; clear regs 
                    mov   bx, 0 
                    call  show_regs 
              
                    call  get_signed           ; get two numbers
                    call  show_regs 
                    push  ax                   ; save the first number
                    call  get_signed 
                    mov   bx, ax 
                    pop   ax                   ; restore the first number
                    call  show_regs_and_wait 
                    imul  bx                   ; signed multiplication 
                    push  ax                   ; save result
                    mov   answer1, ax          ; display 4 byte result
                    mov   answer2, dx 
                    lea   ax, answer1 
                    call  print_signed_4byte 
                    pop   ax                   ; restore result
                    call  show_regs_and_wait 
              
                   jmp    outer_loop 
             ; - - - - - END CODE ABOVE THIS LINE 

             If the answer for the unsigned byte multiplication is greater
             than 255, it will be difficult to read the answer from the half





             Chapter 6 - Multiplication and Division                        43
             _______________________________________

             registers, so we print out the whole AX register.

             If the answer for the signed word multiplication is greater than
             +32767 or is less than -32768, the answer will be unreadable in
             the DX:AX registers. We move the answer to memory, and then call
             print_signed_4byte. As with set_reg_style, the data is too long
             to be put in AX, so we pass the address of the first byte of
             data with:

                 lea  ax, answer1

             and then call print_signed_4byte. Everything from PUSH AX to POP
             AX is designed to do that.

             Do MUL and IMUL set any flags? Yes. For byte multiplication, if
             AL contains the total answer, the 8086 clears the OF and CF
             flags. If part of the answer is in AH, then the 8086 sets both
             the OF and CF flags.  For word multiplication, if AX contains the
             total answer, the 8086 clears the OF and CF flags. If part of the
             answer is in DX, then the 8086 sets both the OF and CF flags. 

             What do we mean by the total answer? This is simple for unsigned
             multiplication. If AH (or DX for word) is 0, then the total
             answer is in AL (or AX for word). It is more complicated for
             signed multiplication. Consider word multiplication. +30000 X +2
             = +60000. But that's less than 65536, so it is completely
             contained in AX, right? WRONG. The leftmost bit of AX contains
             the sign. If the signed result is out of the range -32768 to
             +32767, information about the absolute value of the number is
             corrupting information about the sign of the number.  AX will
             have the wrong number and the wrong sign. Only by combining AX
             with DX will you get the correct answer. Similarly for byte
             multiplication with AL, if the result is not in the range -128 to
             +127, The leftmost (sign) bit will be corrupted, and only by
             looking at AH:AL will you be able to get the correct result.

             If CF and OF are set, you need to look at both registers to
             evaluate the number. You might want to do error handling, so once
             again, you can have:

                      mul  bx
                      jnc  go_on
                      call error_handler
                 go_on:

             using the same reverse logic as before (if nothing is wrong, skip
             the error handler). We can also use:

                      mul  bx
                      into

             if there is an INTO error handler. 


             DIVISION

             Division operates in the same way as multiplication. Word





             The PC Assembler Tutor                                         44
             ______________________

             division operates on the DX:AX pair and byte division operates on
             the AH:AL pair. There are two instructions, DIV for unsigned
             division and IDIV for signed division. After the division:

                 byte      AL = quotient, AH = remainder
                 word      AX = quotient, DX = remainder

             Both DIV and IDIV operate on BOTH registers. For bytes, they
             consider AH:AL a single number. This means that AH must be set
             correctly before the division or you will get an incorrect
             answer. For words, they consider DX:AX a single number. This
             means that DX must be set correctly before the division, or the
             result will be incorrect. Why did Intel include AH and DX in the
             division? Wouldn't it have been easier to use just AH (or AX for
             word division) and put the quotient and remainder in the same
             place? These instructions are actually designed for dividing a
             long number (4 or 8 bytes). How it works is pretty slick; you'll
             find out about it later in the book. 

             How do you set AH and DX correctly? For unsigned numbers, that's
             easy. Make them 0:

                 mov  al, variable
                 mov  ah, 0
                 div  cl        ; unsigned byte division

             For signed division, set AH or DX to 0 (0000h) if it is a
             positive number and set them to -1 (FFFFh) if the number is
             negative. This is just standard sign extension that was covered
             in the chapter on numbers. Fortunately for us, Intel has provided
             instructions which do the sign extension for us. CBW (convert
             byte to word) correctly extends the signed number in AL through
             AH:AL. CWD (convert word to double) correctly extends the signed
             number in AX through DX:AX. The code is

                 mov  ax, variable5
                 cwd
                 idiv bx             ; signed word division

             Of course with these two instructions you can convert a byte to a
             double word.

                 mov  al, variable6
                 cbw
                 cwd
                 idiv bx             ; signed word division

             first converting to a word, then to a double word.

             For the division program, we are going to use the multiplication
             program and make some small changes. Make a copy of your
             multiplication program:

                 >copy mult.asm  div.asm

             and then make the following changes:






             Chapter 6 - Multiplication and Division                        45
             _______________________________________

                 MULTIPLICATION                     DIVISION

                 ; unsigned byte                    ; unsigned byte
                                                    pop  ax
                 pop  ax                            mov  ah, 0
                 call show_regs_and_wait            call show_regs_and_wait
                 mul  bl                            div  bl


                 ; signed word                      ; signed word
                                                    pop  ax
                 pop  ax                            cwd
                 call show_regs_and_wait            call show_regs_and_wait
                 imul bx                            idiv bx

             The calls to print_unsigned and print_signed_4byte are
             irrelevant, so you may either delete them or ignore the output.
             All we did was change the multiplication instruction to division
             and prepare the upper register correctly (AH for byte, DX for
             word). That's all. 

             Assemble, link, and run it. Try out both positive and negative
             numbers and see what the remainder looks like. Also notice the
             sign extension just before the division. Remember, for division,
             the results are in the following places:

                 byte      AL = quotient, AH = remainder
                 word      AX = quotient, DX = remainder

             Now divide by 0. Ka-pow! You should have exited the program and
             gotten an error message. Unlike the other arithmetical errors
             where you have the option of ignoring them or making an error
             handler for them, the 8086 considers division by 0 a major no-no.
             When the 8086 detects division by zero,{1} it interrupts the
             program and goes to the zero-divide handler (which is external to
             the program). Normally, this just exits the program since the
             data is now worthless.






             ____________________

             1 What it actually detects is that the quotient is too large to
             fit in the lower register (AL for byte or AX for word). As long
             as the upper register is correctly sign extended, the only time
             this can happen is when you divide by 0. If the upper register is
             NOT sign extended correctly, you can have zero divide errors all
             over the place, even though you aren't dividing by 0. As an
             example, if AH:AL contain 3275 and bl contains 10, then:

                 div  bl

             will give a quotient of 327 ( > 255) and will generate a zero
             divide error.





             The PC Assembler Tutor                                         46
             ______________________

                                          SUMMARY

             MUL and IMUL
                 MUL performs unsigned multiplication and IMUL performs
                 signed multiplication. For bytes, the multiplicand is in AL
                 and the result is in the AH:AL pair. For words, the
                 multiplicand is in AX and the result is in the DX:AX pair.
                 If the total result is contained in the lower register, CF
                 and OF are cleared (0). If part of the result is in the
                 upper register, CF and OF are set (1). The multiplier may be
                 either a register or a variable in memory.

                      variable1 db ?
                      variable2 dw ?

                           mul  variable1      ; unsigned byte
                           mul  cx             ; unsigned word
                           imul bl             ; signed byte
                           imul variable2      ; signed word


             DIV and IDIV
                 DIV performs unsigned division. IDIV performs signed
                 division. For bytes, the dividend is the AH:AL pair. For
                 words, the dividend is the DX:AX pair. In byte division, AH
                 must be correctly prepared before the division. For word
                 division, DX must be correctly prepared before the division.
                 The divisor may be either a register or a variable in
                 memory.

                      variable1 db ?
                      variable2 dw ?

                           div  variable1      ; unsigned byte
                           div  cx             ; unsigned word
                           idiv bl             ; signed byte
                           idiv variable2      ; signed word

                 The quotient and remainder are as follows:

                      byte      AL = quotient, AH = remainder
                      word      AX = quotient, DX = remainder

                 No flags are affected. If the quotient is too large for the
                 lower register, or if you divide by zero, a zero divide
                 program interrupt occurs.

             CORRECT SIGN EXTENSION
                 To prepare for division, you must correctly sign extend the
                 lower register into the upper register. For unsigned
                 division, zero the upper register (AH = 0 or DX = 0). For
                 signed division, use CBW and CWD. CBW (convert byte to word)
                 extends a signed number in AL through AH:AL. CWD (convert
                 word to double) extends a signed number in AX through DX:AX