Sefx


               C Language Sound Effects Library

               Version 1.0

               20 Feb 92

               Copyright (c) 1992  Bri Productions







































                                   1

       Table of Contents



       Introduction

               Acknowledgments.........................4

               General Description.....................4

               Disclaimer..............................4

               Registration............................4

               Contacting the Author...................5

               Terminology.............................5

               A typedef...............................5


       Control Functions

               Description.............................6

               SndOpen.................................7

               SndClose................................8

               SndLen..................................9

               SndTbase...............................10

               SndFlush...............................11

               SndHold................................12

               SndTerm................................13


       Sound Generation Functions

               Description............................14

               SndTone................................15

               SndPause...............................16

               SndString..............................17

               SndTrill...............................18

               SndSlide...............................19

               SndPulse...............................20





                                   2

       Miscellaneous

               SndMs..................................21




       Appendix A - Things to look out for............22


       Appendix B - Musical notes.....................23


       Appendix C - Sound queue usage.................24


       Appendix D - Registration form.................25











































                                   3

       Acknowledgments.

       I would like to thank Earl Jensen for technical review and
       advice, James Garcia for musical information and Margaret
       Carlsen for proof reading this documentation.



       General Description.

       Sefx is a C language timer-driven sound effects library for IBM
       and compatible computers. Sefx is compatible with most if not
       all DOS based C compilers.

       All the sound generated by Sefx is generated in the background.
       This fact allows the program to continue with other operations
       while the sound is generated.


       Some of Sefx's features are:

       ù Generates sound simultaneously to other operations
       ù Produces frequencies from 19 to 20,000+ hertz
       ù Time bases of 54.9, 27.5, 13.7 and 6.9 milliseconds
       ù Changes frequency up to 145 time per second
       ù Adjustable sound queue as large as 65532 bytes
       ù Sound queue is handled internally
       ù Written in assembly language for optimum speed and efficiency.



       DISCLAIMER.

       Sefx is provided AS IS. Bri Productions specifically disclaims
       any and all warranties, expressed or implied, including fitness
       for a particular purpose. Use this product at your own risk.



       Registration.

       Sefx is a user supported software product. Distribution of
       this product, unaltered and without charge, is encouraged. If
       you find this product useful, you are encouraged to register
       your copy. This allows Bri Productions to continue to provide
       support low cost, high quality shareware.

       The registration fee is $20.00 US dollars and includes libraries
       for small, medium, compact and large memory models and complete
       source code. A registration form is provided in Appendix D.










                                   4

       Contacting the author.

       Bri Productions may be contacted by any of the following means:

       CompuServe      -       76635,2246
       U.S. mail       -       Bri Productions
                               P.O.Box 7121
                               Fremont, CA 94537-7121

       CompuServe is a trademark of CompuServe Inc.


       Terminology

       This section is intended to define the terminology used in this
       documentation and clarify any ambiguities thereof.

       A 'tone' consists of a single frequency and a 'duration'. A
       'pause' is the same in all respects as a 'tone' except for the
       absents of a frequency. It can also be defined as a 'tone' with
       a frequency of zero.

       A 'sound' is one or more 'tones' and/or 'pauses' put together
       to produce the desired results. ie. trill, slide, string, etc.
       A 'sound' may consist of only one 'tone' or 'pause'. Each Sefx
       sound generation function generates exactly one sound.

       The 'time base' refers to the length of time of one 'tic' which
       is the basic unit of time used by the Sefx sound generating
       functions. A new 'tone' or 'pause' may be loaded as often as
       once per 'tic'. Hence the frequency may be changed as often
       as the value of the 'time base'.

       The 'duration' of a 'tone' is the number of 'tics' (and hence
       the length of time) it will last.

          Examples:

             A 'tone' with a 'duration' of two 'tics', when the
             'time base' is set to MEDium (27.5ms), will last 55
             milliseconds.

             A 'sound' consisting of a 'tone' with a 'duration' of of
             two 'tics', a 'pause' with a 'duration' of one 'tic'
             followed by another tone with a 'duration' of three 'tics'
             when the 'time base' is set to HIGH (13.7ms), will last
             82.2 milliseconds.


       A typedef

       You will see the data type 'TONE' throughout the Sefx library.
       TONE is a structure, defined in sefx.h, used for storing
       frequency/duration pairs. This type is used mainly by the
       function SndString. The fields are defined as follows:

                   typedef struct{
                      int freq;         /* frequency */
                      int durtn;        /* duration  */
                      }TONE;
                                   5

        Control Functions

       Before sound can be generated, a call to SndOpen must be made
       to initialize Sefx. SndOpen will also allocate memory for a sound
       queue. Sounds are then loaded into the sound queue and played in
       sequence

       Prior to program's termination, a call to SndClose must be made
       to undo SndOpen. Failing to call SndClose prior to a program's
       termination will cause the computer to lock up requiring a
       reboot.

       Other control functions are available for manipulating and
       procuring the status of the sound queue. The sound queue can
       be flushed at any time with SndFlush. SndTerm terminates the
       current sound while SndHold will put all sound on hold. The
       number of bytes currently residing in the sound queue is available
       through SndLen.










































                                   6

       ----------------------------------------------------------------
       SndOpen
       ----------------------------------------------------------------

       Function

             Initializes the timer and interrupt handler and allocates
             memory for the sound queue.


       Syntax

             #include "sefx.h"
             int SndOpen(unsigned Qsize, int tbase);


       Parameters

             Qsize - Size of the sound queue in bytes. The number
                     of bytes required for a sound varies depending
                     on the sound. This value will be rounded down
                     so that it is even multiple of 4 bytes.

             tbase - Time base. This value determines the length of
                     time of one tic and subsequently how often the
                     frequency can be changed. Possibilities are:

                        LOW    (3) - 54.9 milliseconds
                        MED    (2) - 27.5 milliseconds
                        HIGH   (1) - 13.7 milliseconds
                        ULTRA  (0) -  6.9 milliseconds


       Remarks

             SndOpen initializes the timer chip, installs the
             timer interrupt handler, allocates memory for the
             sound queue and sets the time base.

             The time base determines how long one tic will be. Since
             a new tone can be loaded as often as once per tic, this
             value also determines how often the frequency can be
             changed.

             After a call to SndOpen, a subsequent call to SndClose
             must be made prior to the program's termination.


       Return value

             SndOpen returns a zero if no errors occur, or non
             zero on an error. Constants are defined in sefx.h
             as follows:

                     NOERR       (0) - no errors
                     OPENED      (1) - Sefx already opened
                     MALLOC_ERR  (4) - queue allocation error



                                   7

       See also

             SndClose SndTbase


       Example

             Initialize Sefx, allocate a 1023 byte sound queue and
             set the time base to MEDium resolution.

             #define  QSIZE     1024
             {
             int rv;

                rv = SndOpen(QSIZE, MED);
                if(rv)
                {

                   ... error handler

                }



       ----------------------------------------------------------------
       SndClose
       ----------------------------------------------------------------

       Function

             Restores the timer and timer interrupt, and releases the
             sound queue from memory.


       Syntax

             #include "sefx.h"
             void SndClose(void);


       Remarks

             SndClose restores the timer interrupt vector and the
             timer chip to normal, and releases the memory allocated
             for the sound queue.

             A call to SndClose is required prior to the program's
             termination.


       See also

             SndOpen







                                   8

       Example

             Restore the interrupt vector and free the sound queue
             prior to termination

             {

                ... closing code

                SndClose();
             }



       ----------------------------------------------------------------
       SndLen
       ----------------------------------------------------------------

       Function

             Determines how many bytes are currently occupying the
             sound queue.


       Syntax

             #include "sefx.h"
             unsigned SndLen(void);


       Remarks

             SndLen determines how many bytes are currently occupying
             the sound queue. The value is a direct representation
             of how full the sound queue actually is and does not
             necessarily represent how much time is left in the queue.


       Return value

             SndLen returns the number of bytes currently residing in
             the sound queue.


       See also

             SndFlush SndHold SndTerm













                                   9

       Example

             Check if there is room for 10 more bytes in the sound
             queue.

             #define THRESH        512
             #define SndThresh()   (SndLen() < THRESH)
             {
                if(SndThresh())
                {

                   ...load more sound

                }
             }



       ----------------------------------------------------------------
       SndTbase
       ----------------------------------------------------------------

       Function

             Sets the time base.


       Syntax

             #include "sefx.h"
             int SndTbase(int tbase);


       Parameters

             tbase - Time base. This value determines the length of
                     time of one tic and subsequently how often the
                     frequency can be changed. Possibilities are:

                        LOW    (3) - 54.9 milliseconds
                        MED    (2) - 27.5 milliseconds
                        HIGH   (1) - 13.7 milliseconds
                        ULTRA  (0) -  6.9 milliseconds


       Remarks

             SndRes sets the time base. This value determines the
             length of time of one tic, the basic unit of time used
             by Sefx. Since a new tone can be loaded as often as once
             per tic, the time base determines how often the frequency
             can be changed.



       Return value

             SndTbase returns the previous time base.


                                   10

       See also

             SndOpen


       Example

             Set the time base to 6.9 milliseconds per tic, later
             restoring the original time base.

             {
             int org_tb;

                org_tb = SndTbase(ULTRA);

                   ... short tones
             }


             {

                   ... later

                SndTbase(org_tb);

             }



       ----------------------------------------------------------------
       SndFlush
       ----------------------------------------------------------------

       Function

             Flushes all sound.


       Syntax

             #include "sefx.h"
             void SndFlush(void);


       Remarks

             SndFlush flushes the sound queue, deleting all pending
             and current sounds. It also terminates the current tone.

       See also

             SndLen SndTerm SndHold








                                   11

       Example

             Play a song after displaying the opening screen until
             the user hits a key.

             {

                ...display opening screen

                SndString(song, 100, 0);

                getch();

                SndFlush();

                ...continue

             }



       ----------------------------------------------------------------
       SndHold
       ----------------------------------------------------------------

       Function

             Puts all sound on hold or releases from hold.


       Syntax

             #include "sefx.h"
             int SndHold(int on_off);


       Parameters

             on_off - hold on/off switch. Possibilities are

                         ON  (1) - put on hold
                         OFF (0) - release from hold

       Remarks

             SndHold puts all sound on hold or releases it from a
             previous hold condition. When a hold is set, the
             current tone as well as the sound queue is immediately
             frozen until it is subsequently released from hold.
             When a hold condition is released, the sounds will
             resume where it left off.


       Return value

             SndHold returns the previous hold condition




                                   12

       See also

             SndFlush SndTerm


       Example

             Make sure the sound is on hold temporarily and then
             restore it to it's previous condition

             {
             int prev_hold;

                prev_hold = SndHold(ON);

                   ... guaranteed quiet time

                SndHold(prev_hold);
             }



       ----------------------------------------------------------------
       SndTerm
       ----------------------------------------------------------------

       Function

             Terminates the current sound.


       Syntax

             #include "sefx.h"
             void SndTerm(void);


       Remarks

             SndTerm terminates the current sound. The sound may be a
             single tone or many tones. In either case all the tones
             that make up the sound are terminated.


       See also

             SndFlush SndHold


       Example

             Terminate the alarm when the user responds

             #define CONTINUOUS   0
             #define Alarm()   SndTrill(1400, 600, 8, 8, CONTINUOUS)
             {
                Alarm();
                   ... wait for response
                SndTerm();
             }
                                   13

       Sound Generation

       Sound generation functions load sounds into the sound queue to be
       played in sequence. Most of the sound generation functions allow
       the sound to be repeated a specified number of times or
       continuously.

       A sounds consisting of a single tone is loaded with SndTone while
       a sound consisting of a string of tones can be loaded with
       SndString.

       Sefx provides sound generation functions for the more common types
       of sounds. This includes trills, pulses and slides created by
       the functions SndTrill, SndPulse and SndSlide respectively.
       These basic sounds can create a multitude of sounds themselves and
       in addition can be used with other sound generation functions to
       create more complex combinations.











































                                   14

       ----------------------------------------------------------------
       SndTone
       ----------------------------------------------------------------

       Function

             Loads a single tone  into the sound queue.


       Syntax

             #include "sefx.h"
             void SndTone(int freq, int durtn);


       Parameters

             freq  - frequency of the tone in hertz.

             durtn - number of tic the tone will last.


       Remarks

             SndTone loads single tone of the specified frequency and
             duration into the sound queue. Specifying a duration of 0
             causes the tone to be played continuously. Specifying a
             frequency of 0 will generate a pause. The single tone is
             considered to be one sound.

       See also

             SndString SndPause SndTbase SndMs


       Example

             Make a two second beep at 2000 hertz.

             {
             int second;

                 ... made an error

                second = SndMs(1000);
                SndTone(2000, 2*second);
             }













                                   15

       ----------------------------------------------------------------
       SndPause
       ----------------------------------------------------------------

       Function

             Loads a pause into the sound queue.


       Syntax

             #include "sefx.h"
             void SndPause(int durtn);


       Parameters

             durtn - number of tics the tone will last


       Remarks

             SndPause loads a pause (no sound) of the specified
             duration into the sound queue. The pause is considered to
             be one sound.

             SndPause is a function macro defined as SndTone(0, durtn).


       See also

             SndTone SndTbase SndMs


       Example

             Insert a three beat pause between two notes

             #define  A     440
             #define  B     494
             {
             int beat;

                beat = SndMs(500);

                SndTone(A, 3*beat);
                SndPause(3*beat);
                SndTone(B, 3*beat);

             }










                                   16

       ----------------------------------------------------------------
       SndString
       ----------------------------------------------------------------

       Function

             Loads a string of tones into the sound queue.


       Syntax

             #include "sefx.h"
             void SndString(const TONE *str, int count, unsigned reps);


       Parameters

             str    - pointer to an array of type TONE were the
                      string of tones are stored.

             count  - number of tones in the array.

             reps   - number of times to repeat the string of
                      tones.


       Remarks

             SndString loads an string of tones, stored in an array
             of type TONE, into the sound queue. The string of tone
             will be repeated as specified. Specifying a repetition of
             0 will cause the string to be repeated continuously.

             The string of tones is considered to be one sound.

       See also

             SndTone SndTbase SndMs SndPause


       Example

             Play the scale of notes one time.

             #define  C     262
             #define  D     294
             #define  E     330
             #define  F     349
             #define  G     392
             #define  A     440
             #define  B     494

             {
             TONE scale[7] = { {C,3},{D,3},{E,3},{F,3},
                               {G,3},{A,3},{B,3}
                             };

                SndString(scale, 7, 1);
             }

                                   17

       ----------------------------------------------------------------
       SndTrill
       ----------------------------------------------------------------

       Function

             Loads a trill sound into the sound queue.


       Syntax

             #include "sefx.h"
             void SndTrill(int freq1, int freq2,
                                      int durtn1, int durtn2, int reps);


       Parameters

             freq1  - frequency of the first tone in hertz.

             freq2  - frequency of the second tone in hertz.

             durtn1 - number of tics the first tone will last.

             durtn2 - number of tics the second tone will last.

             reps   - number of times to repeat the trill sound.
       Remarks

             SndTrill loads a trill sound into the sound queue. The
             trill is repeated as specified. Specifying a repetition
             of 0 will cause the trill to be repeated continuously.

             A trill sound is sometimes referred to as a flip-flop sound.


       See also

             SndSlide SndPulse SndMs SndTbase


       Example

             Make a telephone ring five times.

             {
             int i = 5;

                while(i--)
                {
                   SndTrill(1400, 600, 1, 1, 10);
                   SndPause(22);
                }
             }






                                   18

       ----------------------------------------------------------------
       SndSlide
       ----------------------------------------------------------------

       Function

             Loads sliding tones into the sound queue.


       Syntax

             #include "sefx.h"
             void SndSlide(int start, signed dfreq,
                                               int durtn, int reps);

       Parameters

             start - frequency of the starting tone in hertz.

             dfreq - change (delta) in frequency per tic.

             durtn - number of tic the slide will last.

             reps  - number of times to repeat the slide.


       Remarks

             SndSlide loads sliding tones into the sound queue. The
             frequency is increased (positive 'dfreq') or decreased
             (negative 'dfreq') on each tic by the specified delta
             frequency. The sliding tone will last the specified
             duration and will be repeated as specified.

             To calculate the frequency of the ending tone in the slide
             use: end = start + (durtn - 1) * dfreq.

             Hint: shorter (faster) time bases generate a smoother
             sounding slide while longer (slower) time bases generate
             a more course sounding slide. Both cases can be useful
             for creating the desired effect.

       See also

             SndTrill SndPulse SndMs SndTbase


       Example

             Play a sliding tone from 2000 hertz to 992 hertz


             {

                SndSlide(2000, -28, 37);

             }



                                   19

       ----------------------------------------------------------------
       SndPulse
       ----------------------------------------------------------------

       Function

             Loads a pulsing sound into the sound queue.

       Syntax

             #include "sefx.h"
             void SndPulse(int freq, int durtn,
                                             int pdurtn, int reps);

       Parameters

             freq   - frequency of the tone in hertz.

             durtn  - number of tics the tone will last.

             pdurtn - number of tics the pause will last.

             reps   - number of times to repeat the pulse.


       Remarks

             SndPulse loads a tone of the specified frequency and
             duration, followed by a pause of the specified duration
             The sound is repeated as specified. Specifying a repetition
             of 0 will cause the pulse to repeat continuously.

             SndPulse is a function macro defined as:
             SndTrill(freq, 0, durtn, pdurtn, reps);


       See also

             SndTrill SndSlide SndMs SndTbase


       Example

             Make a wrist watch alarm. (Time base = LOW/54.9)

             {
             int i = 3;

                while(i--)
                {
                   SndPulse(4250, 2, 1, 3);
                   SndPause(9);
                }

             }





                                   20

       ----------------------------------------------------------------
       SndMs
       ----------------------------------------------------------------

       Function

             Converts milliseconds to tics.


       Syntax

             #include "sefx.h"
             int SndMs(unsigned ms);


       Parameters

             ms - number of milliseconds to convert to tics


       Remarks

             SndMs converts a value in milliseconds to the equivalent
             number of tics, rounding off to the nearest tic. SndMs
             takes into account the current time base and adjusts
             the resulting number of tics accordingly. The number of
             tics will always be at least one unless 0 milliseconds is
             specified.

             Shorter (faster) time bases result in a more precise
             conversion than longer (slower) time bases. In most
             applications this is an insignificant limitation. In
             any case the value will never be off more that the length
             of time of one tic.


       Return value

             SndMs returns the number of tics that is approximately
             equal to the specified number of milliseconds.


       See also

             SndTbase


       Example

             Make a one second tone at 100 hertz

             {
             int second;

                second = SndMs(1000);

                SndTone(100, second);

             }

                                   21

        Appendix A


       Things to look out for.

       ù Sefx takes over interrupt 8 and may change the system clock
         rate. If the clock rate is changed, Sefx arbitrates the
         timer chain in order that it's rate remains the same. If
         a program written with Sefx needs to chain into interrupt 8
         it should do so prior to the calling SndOpen.

       ù The functions SndOpen and SndClose make calls to the C
         functions malloc and free respectively.

       ù In the small and medium memory models, the near heap where
         the sound queue is allocated, is limited. The data segment
         (globals etc.) + the stack + allocated memory (sound queue)
         must not exceed 64K bytes. If an extremely large sound queue
         is required the compact or large model, where the sound queue
         can be as large as 65532 bytes, should be used.








































                                   22

       Appendix B

       Musical notes.

       This appendix provides information about frequencies of musical
       notes and octave shifting.


       The Equal Tempered Chromatic Scale (rounded to integer)

          note|freq  |  note|freq  |  note|freq  |  note|freq
        -------------|-------------|-------------|-------------
          C0     16  |  C2     65  |  C4    262  |  C6   1047
          C#0    17  |  C#2    69  |  C#4   277  |  C#6  1109
          D0     18  |  D2     73  |  D4    294  |  D6   1175
          D#0    19  |  D#2    78  |  D#4   311  |  D#6  1245
          E0     21  |  E2     82  |  E4    330  |  E6   1319
          F0     22  |  F2     87  |  F4    349  |  F6   1397
          F#0    23  |  F#2    93  |  F#4   370  |  F#6  1480
          G0     25  |  G2     98  |  G4    392  |  G6   1568
          G#0    26  |  G#2   104  |  G#4   415  |  G#6  1661
          A0     28  |  A2    110  |  A4    440  |  A6   1760
          A#0    29  |  A#2   117  |  A#4   466  |  A#6  1865
          B0     31  |  B2    123  |  B4    494  |  B6   1976
                     |             |             |
          C1     33  |  C3    131  |  C5    523  |  C7   2093
          C#1    35  |  C#3   139  |  C#5   554  |  C#7  2217
          D1     37  |  D3    147  |  D5    587  |  D7   2349
          D#1    39  |  D#3   156  |  D#5   622  |  D#7  2489
          E1     41  |  E3    165  |  E5    659  |  E7   2637
          F1     44  |  F3    175  |  F5    698  |  F7   2794
          F#1    46  |  F#3   185  |  F#5   740  |  F#7  2960
          G1     49  |  G3    196  |  G5    784  |  G7   3136
          G#1    52  |  G#3   208  |  G#5   831  |  G#7  3322
          A1     55  |  A3    220  |  A5    880  |  A7   3520
          A#1    58  |  A#3   233  |  A#5   932  |  A#7  3729
          B1     62  |  B3    247  |  B5    988  |  B7   3951
                                                 |  C8   4186

       Since the frequencies of the octaves increase as a factor of
       two, musical notes of the other octaves are easily accomplished
       by multiplying or dividing by factors of two, or more
       efficiently by shifting left or right. For example to obtain
       the frequency of A5, the value of A4 (440) is shifted left
       once (multiplied by two). To obtain the frequency of A2,
       shift A4 right twice (divide by four).

       Examples:   A5 = A4 << 1

                   A2 = A4 >> 2

       Note: It is better to shift from a higher octave to a lower
       octave since the percent of rounding error, when rounding to an
       integer, is smaller with the larger values.
       Appendix C





                                   23

       Appendix C

       Sound queue usage

       Some of the sound generation functions load instructional
       information as well as frequency and duration information. This
       added information allows Sefx to conserve memory. When the sound
       is initially loaded by the sound generation function, it will
       occupy an 'initial' number of bytes in the sound queue. When the
       next sound is fetched from the sound queue, the instructional
       information is evaluated and then discarded. The remaining bytes
       will continue to occupy the sound queue until the sound is
       terminated. This is referred to in the table below as 'residual'.


                              Initial           Residual
                             ---------         ----------

          SndTone                4                 4

          SndPause               4                 4

          SndString         8 + 4 * len         4 * len

          SndTrill              16                 8

          SndSlide         8 + 4 * durtn       4 * durtn

          SndPulse              16                 8































                                   24

       Appendix D

       Sefx v1.0 Registration Form

       Name: ______________________________________________________

       Company: ___________________________________________________

       Address: ___________________________________________________

       City: ____________________________  State: _________________

       Zip code: _________________  Phone # : _____________________

       CompuServe # : _____________________________________________

       How did you acquire Sefx ? _________________________________

       ____________________________________________________________

       What functions do you find most useful ?____________________

       ____________________________________________________________

       What functions do you find least useful ?___________________

       ____________________________________________________________

       What functions, not in Sefx, would you like to see ?________

       ____________________________________________________________

       What other types of libraries would you find useful ?_______

       __ Serial Communications  __ Expanded Memory  __ IEEE/GPIB

       __ Game Port  Others: ______________________________________

       registration                                      $ 20.00

       California residents add sales tax (  8.25% )     $________

       shipping inside continental U.S.   ( $ 2.00 )
       shipping outside continental U.S.  ( $ 5.00 )     $________


                                                Total:   $________

       All Payments Must be in U.S. Dollars

       Make check or money order payable to:    Bri Productions
                                                P.O. Box 7121
                                                Fremont, CA 94537-7121







                                   25