(*****************************************************************************
 *                                                                           *
 *  ADVCRT - Advanced Screen and Keyboard Manipulation Routines              *
 *           for Borland International's Turbo Pascal Version 5.5            *
 *                                                                           *
 *    Serial Number:  000000 - Released June 19, 1990                        *
 *      Licensed to:  Author                                                 *
 *              For:  Normal use                                             *
 *  Current Version:  9.0                                                    *
 *                                                                           *
 *****************************************************************************
 *                                                                           *
 *                      Description of AdvCRT Routines:                      *
 *                                                                           *
 *****************************************************************************
 *                                                                           *
 *  Procedure FindScreenBase(var ScreenBase: Word);                          *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns type of display adaptor installed in the form of the       *
 *        Video Segment Address.                                             *
 *   PARAMETERS:                                                             *
 *        ScreenBase (out) - Video Segment Address of display                *
 *          Hex B800 - SVGA/VGA/EGA/CGA/MCGA card                            *
 *          Hex B000 - Monochrome card                                       *
 *   NOTE(S):                                                                *
 *        Used primarily for DirectOut procedure.                            *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function QuickScreenBase: Word;                                          *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns the Video Segment Address of the current video             *
 *        display adaptor installed.  Used instead of a global variable      *
 *        and the FindScreenBase procedure.                                  *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function MakeAttr(Fore, Back: Byte): Byte;                               *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Converts given Foreground and Background colors into a             *
 *        single Attribute byte for low level machine calls.                 *
 *   PARAMETERS:                                                             *
 *        Fore (in) - Foreground of Attribute to make                        *
 *        Back (in) - Background of Attribute to make                        *
 *   NOTE(S):                                                                *
 *        Opposite of ExtractAttr procedure.                                 *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure ExtractAttr(Attr: Byte; var Fore, Back: Byte);                 *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Converts machine Attribute (single number) to Compiler             *
 *        specific Foreground and Background colors.                         *
 *   PARAMETERS:                                                             *
 *        Attr  (in) - Attribute byte used in low level machine calls        *
 *        Fore (out) - Foreground color extracted from Attr                  *
 *        Back (out) - Background color extracted from Attr                  *
 *   NOTE(S):                                                                *
 *        Opposite of MakeAttr function.                                     *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure TurnCursor(ONorOFF: Boolean);                                  *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Turns the cursor ON or OFF.  That is, makes it visible or          *
 *        invisble.  Current cursor shape is retained in the global          *
 *        variable SaveCursor.                                               *
 *   PARAMETERS:                                                             *
 *        ONorOFF (in) - Pass in ON to make cursor visible, OFF to hide      *
 *                       cursor                                              *
 *   SYNTAX:                                                                 *
 *        1.  TurnCursor(OFF); - Hide Cursor                                 *
 *        2.  TurnCursor(ON);  - Reveal Cursor                               *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure SetCursor(StartScan, EndScan: Byte);                           *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Sets cursor to a specific size.                                    *
 *   PARAMETERS:                                                             *
 *        StartScan (in) - Start cursor scan line (upper half)   (0-13)      *
 *        EndScan   (in) - Ending cursor scan line (bottom half) (0-13)      *
 *   NOTE(S):                                                                *
 *        If StartScan>EndScan the cursor will become invisible.             *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure Scroll(X1,Y1,X2,Y2, LinesToScroll, BlankLineAttr,              *
 *                   UPorDOWN: Byte);                                        *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Scrolls a particular area of the screen up or down.                *
 *   PARAMETERS:                                                             *
 *        X1, Y1        (in) - Coord. of upper-left area to be scrolled      *
 *        X2, Y2        (in) - Coord. of lower-right area to be scrolled     *
 *        LinesToScroll (in) - Number of lines to scroll                     *
 *        BlankLineAttr (in) - Attribute to fill the blank area with         *
 *        UpOrDown      (in) - Direction to scroll the area - 0=Up, 1=Down   *
 *   NOTE(S):                                                                *
 *        (X1,Y1), (X2,Y2) are related to the coordinates given for          *
 *        Turbo Pascal's standard Window procedure.                          *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure TurnScreen(ONorOFF: Boolean);                                  *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Turns the display ON or OFF software wise.  If OFF, all output     *
 *        to the screen is written, but not shown.  Clearing the screen      *
 *        along with a TurnScreen(ON) will reactivate the display.           *
 *   SYNTAX:                                                                 *
 *        1.  TurnScreen(OFF); - Turn Screen OFF--Software Wise              *
 *        2.  TurnScreen(ON);  - Turn Screen ON                              *
 *   NOTE(S):                                                                *
 *        Note that a DIRECT screen write while the screen is OFF will       *
 *        infact show up on the display.  If you wish to write to the        *
 *        screen while it is "OFF", use Turbo's WRITE and WRITELN.           *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure DirectOut(X,Y: Byte; aStr: String; Attr: Byte);                *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Writes a string of information directly to video display memory.   *
 *        This routine is not the fastest possible, since it actually        *
 *        outputs a character at a time.                                     *
 *   PARAMETERS:                                                             *
 *        X, Y (in) - Coordinates where string should be displayed           *
 *        aStr (in) - String to be displayed on screen                       *
 *        Attr (in) - Attribute to be used when displaying                   *
 *   NOTE(S):                                                                *
 *        See MakeAttr function for information on procedure that need       *
 *        machine level attributes.                                          *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure SetBorder(BordColor: Byte);                                    *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Sets screen border color.  Works on all classes of PC's            *
 *        including PCjr.                                                    *
 *   PARAMETERS:                                                             *
 *        BorderColor (in) - Color to set the screen's border to             *
 *   NOTE(S):                                                                *
 *        Can also be achieved on a PC with a simple Port call. This         *
 *        routine works on all PC's including PCjr.                          *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure GetCursorPos(var X,Y: Byte; Page: Byte);                       *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns the position of the cursor on the screen on a given        *
 *        Video Display Page.                                                *
 *   PARAMETERS:                                                             *
 *        X, Y (out) - Returns the coordinates of the cursor                 *
 *        Page  (in) - The display page to scan for the cursor position      *
 *   NOTE(S):                                                                *
 *        Quite similar to WhereX and WhereY, but can be used on any         *
 *        given display page.  Makes AdvCRT Unit dependant only on           *
 *        the DOS Unit.                                                      *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure GetCRTMode(var Mode, Columns, ActivePage: Byte);               *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns the current mode of the video display adaptor.             *
 *   PARAMETERS:                                                             *
 *        Mode (out) - Current mode of the CRT                               *
 *          0 - 40 column B&W text mode                                      *
 *          1 - 40 column color text mode                                    *
 *          2 - 80 column B&W text mode                                      *
 *          3 - 80 column 16 color text mode                                 *
 *          4 - 4 color med-resolution graphics mode                         *
 *          5 - 4 grey color med-resolution graphics mode                    *
 *          6 - 2 color B&W high-resolution graphics mode                    *
 *          7 - 80 column monochrome mode                                    *
 *          8 - 15 graphics modes for EGA Card                               *
 *        Columns    (out) - Current number of columns on the screen         *
 *        ActivePage (out) - Active display page number                      *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function ActiveDisplayPage: Byte;                                        *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns the active Video Display Page.  Useful for other           *
 *        routines that demand a Page be passed into them.                   *
 *   SYNTAX:                                                                 *
 *        1.  Writeln(ActiveDisplayPage);                                    *
 *        2.  GetCharXY(12,3, ActiveDisplayPage, Ch, Attr);                  *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure SetPage(Page: Byte);                                           *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Sets active display page.                                          *
 *   PARAMETERS:                                                             *
 *        Page (in) - Display page to switch to                              *
 *   NOTE(S):                                                                *
 *        Page is [0-3] in 80 column text mode                               *
 *                [4-7] in graphics modes.                                   *
 *        Can be used in conjunction with ClrPage, WriteStrPage,             *
 *        and WriteChPage procedures to produce "instant" pages of text.     *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure SetCurPosPage(X,Y, Page: Byte);                                *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Sets the cursor position on a give page.  Used primarily by        *
 *        other procedures within this Unit, but can be called               *
 *        separately.                                                        *
 *   PARAMETERS:                                                             *
 *        X, Y (in) - Coordinates on which the cursor should be placed       *
 *        Page (in) - Display page to use                                    *
 *   NOTE(S):                                                                *
 *        Remember that the display page on which you may be positioning     *
 *        the cursor may not be the ACTIVE display page.                     *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure GetCharXY(X,Y, Page: Byte; var Ch: Char; var Attr: Byte);      *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Scans the CRT for the character and its attribute at a given       *
 *        position on a given display page.                                  *
 *   PARAMETERS:                                                             *
 *        X, Y  (in) - Coordinates of position to be scanned                 *
 *        Page  (in) - Display page to scan                                  *
 *        Ch   (out) - Character found at requested position                 *
 *        Attr (out) - Attribute of the character found                      *
 *   NOTE(S):                                                                *
 *        Since a character does exist at every position on the screen       *
 *        on any page, Ch will return a "blank" character (#32) if no        *
 *        other character was found.                                         *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure WriteChPage(X,Y, Page: Byte; Ch: Char; NumReps: Integer;       *
 *                        Attr: Byte);                                       *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Writes a character at screen coordinates X, Y (Column, Row         *
 *        respectively) on a given Display Page with a given                 *
 *        Attribute.                                                         *
 *   PARAMETERS:                                                             *
 *        X, Y    (in) - Coordinates at which to write the character         *
 *        Page    (in) - Display page to write to                            *
 *        Ch      (in) - Actual character to write                           *
 *        NumReps (in) - Number of times to write the character              *
 *        Attr    (in) - Attribute to use when writing the character         *
 *   SYNTAX:                                                                 *
 *        1.  WriteChPage(12,3, ActiveDisplayPage, 'G', 1, MakeAttr(15,1));  *
 *        2.  WriteChPage(13,4, 0, 'a', 2, 7);                               *
 *   NOTE(S):                                                                *
 *        Use with other page routines to create instant pages of text.      *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure WriteStrPage(X,Y, Page: Byte; aStr: String; Attr: Byte);       *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Writes a string at screen coordinates X, Y on a given Display      *
 *        Page with a give Attribute.                                        *
 *   PARAMETERS:                                                             *
 *        X, Y    (in) - Coordinates at which to write the string            *
 *        Page    (in) - Display page to write to                            *
 *        aStr    (in) - Actual string to write                              *
 *        Attr    (in) - Attribute to use when writing the string            *
 *   SYNTAX:                                                                 *
 *        1.  WriteStrPage(1,10, ActiveDisplayPage, 'Turbo', 7);             *
 *        2.  WriteStrPage(2,23, 1, 'Hello', MakeAttr(0,3));                 *
 *   NOTE(S):                                                                *
 *        Use with other page routines to create instant pages of text.      *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure ClrPage(Page: Byte);                                           *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Clears a given Display Page and sets the cursor to the upper       *
 *        left hand corner of that page.  Similar to ClrScr procedure.       *
 *   PARAMETERS:                                                             *
 *        Page (in) - Display page to clear                                  *
 *   NOTE(S):                                                                *
 *        Should be called before writing to a given display page, since     *
 *        that page may have "garbage" from previous applications.           *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure GetKey(var Code: Byte; var Extkey: Boolean);                   *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Gets a key from the keyboard--returns it's ASCII value and         *
 *        whether or not it is "extended".                                   *
 *   PARAMETERS:                                                             *
 *        Code   (out) - ASCII value of key pressed (See Turbo Manual)       *
 *        Extkey (out) - TRUE if key is "extended", FALSE otherwise          *
 *   SYNTAX:                                                                 *
 *        GetKey(Code, Extended);                                            *
 *   NOTE(S):                                                                *
 *        Normal keys return a single code with Extkey set to FALSE,         *
 *        extended keys (Alt-A, F10, Alt-F3, etc) return a single            *
 *        code (See Turbo Manual) with Extkey set to TRUE.                   *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function CapsLockON: Boolean;                                            *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if Caps-Lock key is active--FALSE otherwise.          *
 *   SYNTAX:                                                                 *
 *        If CapsLockON Then                                                 *
 *          WriteLn('Caps-Lock key is currently ENABLED');                   *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function NumLockON: Boolean;                                             *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if Num-Lock key is active--FALSE otherwise.           *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function ScrollLockON: Boolean;                                          *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if Scroll-Lock key is active--FALSE otherwise.        *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function RightShift: Boolean;                                            *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if the Right Shift key is depressed at the time of    *
 *        the call to the function--FALSE otherwise.                         *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function LeftShift: Boolean;                                             *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if the Left Shift key is depressed at the time of     *
 *        the call to the function--FALSE otherwise.                         *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function AltPressed: Boolean;                                            *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if the Alt key is depressed at the time of the        *
 *        call to the function--FALSE otherwise.                             *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function CtrlPressed: Boolean;                                           *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if the Ctrl key is depressed at the time of the       *
 *        call to the function--FALSE otherwise.                             *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function InsertModeON: Boolean;                                          *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns TRUE if the machine global insert mode is active at        *
 *        the time of the call to the function--FALSE otherwise.             *                *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure SaveScreen(var aScreen: ScreenType; Height: Byte;              *
 *                       var Status: Byte);                                  *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Saves the contents of the TEXT screen to memory.  Each screen      *
 *        needs about 4000 bytes (4k) of memory.  You may have as many       *
 *        screens saved to memory as you wish, however one page              *
 *        (VirtualPage, of type ScreenType) is supplied for you at the       *
 *        VARiable declaration of this UNIT.                                 *
 *   PARAMETERS:                                                             *
 *        aScreen (out) - Screen is saved to this varialbe:  All Chars,      *
 *                        their attributes, and the Height of the Screen.    *
 *        Height   (in) - The height of your screen--usually 25, may differ  *
 *                        according to Display Adaptor (VGA/EGA/etc).        *
 *        Status  (out) - Returns 0 if Screen Save was successful, 1         *
 *                        otherwise (lack of memory).                        *
 *   SYNTAX:                                                                 *
 *        SaveScreen(VirtualScreen, 25, Result);                             *
 *   NOTE(S):                                                                *
 *        See also RestoreScreen procedure.                                  *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure RestoreScreen(aScreen: ScreenType);                            *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Restores a text screen stored in variable aScreen to Video         *
 *        Display Memory instantly.                                          *
 *   PARAMETERS:                                                             *
 *        aScreen (in) - "Screen" [variable] to restore.  Will be place      *
 *                       directly to Video Display Memory for an             *
 *                       instantaneous text display.                         *
 *   SYNTAX:                                                                 *
 *        RestoreScreen(VirtualScreen);                                      *
 *   NOTE(S):                                                                *
 *        See also SaveScreen procedure.  It is not necessary to pass in     *
 *        the height of the screen again since it is saved when you make     *
 *        a call to SaveScreen.                                              *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function NumSecsMidNight: Real;                                          *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns the number of seconds elapsed since Midnight.              *
 *   SYNTAX:                                                                 *
 *        1.  Writeln(NumSecsMidNight:0:2);                                  *
 *        2.  r := NumSecsMidNight;                                          *
 *   NOTE(S):                                                                *
 *        Used primarily by CheckTime procedure.                             *
 *  ----------------------------------------------------------------------}  *
 *  Procedure DelaySeconds(NumSecs: Real; KeyIntr: Boolean);                 *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Delays a specified number of seconds.                              *
 *   PARAMETERS:                                                             *
 *        NumSecs (in) - Number of seconds to wait.                          *
 *        KeyIntr (in) - Pass in ON or OFF to specify whether or not         *
 *                       to allow a keypress to bypass the full wait.        *
 *   SYNTAX:                                                                 *
 *        DelaySeconds(5.0, ON);                                             *
 *          - Pauses system for about five seconds.  If a key is pressed     *
 *            before time has expired.                                       *
 *   NOTE(S):                                                                *
 *        Useful for programs which may half to run on various levels        *
 *        of PCs, since Turbo's Delay command produces unpredictable         *
 *        affects.  AdvCRT's procedure uses the system clock to delay.       *
 *        DelaySeconds is a close approximation, but the time will not       *
 *        be exactly NumSecs seconds.                                        *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure CheckTime(Action: Byte);                                       *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Checks the length of time a specific task takes.  Can be used      *
 *        as a programming aid to time procedures, etc.                      *
 *   PARAMETERS:                                                             *
 *        Action       (in) - 0, 1, or 2 are valid parameters.               *
 *                            0 to reset timer                               *
 *                            1 to start timer                               *
 *                            2 to stop timer                                *
 *        ElapsedTime   N/A - Global variable which stores the elapsed       *
 *                            time since the timer was turned on.            *
 *   SYNTAX:                                                                 *
 *        CheckTime(0);                                                      *
 *          - Resets AdvCRT's internal timer.                                *
 *        CheckTime(1);                                                      *
 *          - Turns timer ON.                                                *
 *        CheckTime(2); Writeln(ElapsedTime);                                *
 *          - Turns timer OFF.  Displays the amount of time elapsed since    *
 *            the timer was turned on.                                       *
 *   NOTE(S):                                                                *
 *        AdvCRT's internal "timer" is a real global variable "StoreTime"    *
 *        and may be manipulated if need be.                                 *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure CapsLockKey(ONorOFF: Boolean);                                 *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Sets the keyboard CAPS-LOCK state to Upper Case or Lower Case.     *
 *   PARAMETERS:                                                             *
 *        ONorOFF (in) - Pass in ON to set keyboard to Upper Case state,     *
 *                       or OFF to set keyboard to Lower Case state          *
 *   SYNTAX:                                                                 *
 *        1.  CapsLockKey(ON);  - Turns CAPS-LOCK state ON                   *
 *        2.  CapsLockKey(OFF); - Turns CAPS-LOCK state OFF                  *
 *   NOTE(S):                                                                *
 *        Sets the CAPS-LOCK state regardless of what the current state      *
 *        happens to be.                                                     *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure NumLockKey(ONorOFF: Boolean);                                  *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Sets the keypad to its Cursor Control or Numeric state.            *
 *   PARAMETERS:                                                             *
 *        ONorOFF (in) - Pass in ON to set the keypad to its Numeric         *
 *                       state, or OFF keypad to its Cursor Control state    *
 *   SYNTAX:                                                                 *
 *        1.  NumLockKey(ON);  - Turns NUM-LOCK state ON                     *
 *        2.  NumLockKey(OFF); - Turns NUM-LOCK state OFF                    *
 *   NOTE(S):                                                                *
 *        Sets the NUM-LOCK state regardless of what the current state       *
 *        happens to be.                                                     *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure PrintScreen(var Status: Byte);                                 *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Causes the current text or graphics screen to be printed to        *
 *        printer 0, the default printer.                                    *
 *   PARAMETERS:                                                             *
 *        Status (out) - Status of the Print-Screen procedure                *
 *           00 - OK status                                                  *
 *           01 - A Print-Screen operation is currently in progress          *
 *          255 - An error occured during a Print-Screen                     *
 *   SYNTAX:                                                                 *
 *        PrintScreen(Status);                                               *
 *   NOTE(S):                                                                *
 *        Identical to standard "Shift-PrtSc" key on the keyboard.           *
 *        Note that in order to print graphics screens, it may be            *
 *        necessary to first install the GRAPHICS.COM program found on       *
 *        your DOS distribution diskette.                                    *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Procedure PurgeKBDBuffer;                                                *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Causes a purge of the type-ahead keyboard buffer.  Any characters  *
 *        which may have existed between the HEAD and TAIL of the keyboard   *
 *        buffer [circular] queue are cleared.                               *
 *   SYNTAX:                                                                 *
 *        ClrScr;                                                            *
 *        PurgeKBDBuffer;                                                    *
 *        Write('Press any key to continue...');                             *
 *        GetKey(Code, ExtendedKey);                                         *
 *   NOTE(S):                                                                *
 *        This procedure uses the global addresses KBDBufferHead and         *
 *        KBDBufferTail which point to the PC's internal type-ahead          *
 *        keyboard buffer.                                                   *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *  Function SizeKBDBuffer: Integer;                                         *
 *  {                                                                        *
 *   DESCRIPTION:                                                            *
 *        Returns the size (in bytes) of the type-ahead keyboard buffer.     *
 *        Default size for PCs is 16 bytes.                                  *             *
 *   SYNTAX:                                                                 *
 *        Writeln('Keyboard buffer size: ', SizeKBDBuffer);                  *
 *   NOTE(S):                                                                *
 *        This function is type Integer (instead of Byte) because of the     *
 *        fact that the size of the buffer may indeed be greater than        *
 *        a Byte's maximum value of 255.                                     *
 *  ----------------------------------------------------------------------}  *
 *                                                                           *
 *****************************************************************************)