The LASERPRT.PAS file produces a unit which is used for
printing reports with a HP LaserJet or compatible printer.
Most of the commonly used formatting commands have been
provided as functions.  Each function returns a string
containing the appropriate HP PCL control codes.  It is
anticipated that the function calls would be made within a
"WRITE(lst," or a "WRITELN(lst," statement.

One of the most difficult problems I had in trying to format
my printouts was using the shading feature to shade every
other line.  Ted Dickens, Sysop of the HP Forum (76701,272)
figured out the right way to accomplish this task.  The
following is an edited version of several messages he wrote
explaining how this is accomplished.  In addition, the
sample program included in the LZRTPU.ZIP file
(SHADETXT.PAS) was originally written by Ted to demonstrate
this procedure.  I have modified it to take advantage of the
LASERPRT.TPU functions.

============================================================
There are three different ways to position the cursor on a
LaserJet+ (or later): row/col, dot/dot, and
decipoint/decipoint.  The three are not interchangeable.

For the sake of this discussion, assume the top margin is 0
lines and that the left unprintable margin is 0.25 inches.

The decipoint/decipoint control sequence, <esc>&a720v1440H,
says move the cursor to 1" (720/720) from the top edge and
2.25" (1440/720 + 0.25" unprintable region) from the left
edge.

The dot/dot control sequence, <esc>*p300y600X, does exactly
the same thing.  With either command, the cursor will be
positioned exactly 1" from the top of the paper and 2.25"
from the left edge.  If you were to draw a single dot --
that's where it would appear.

But, even though there are 10 characters per inch and 6 rows
per inch, the row/col control sequence, <esc>&a6r20C, will
NOT leave the cursor at the same position.

The cursor WILL be left 2.25" from the left edge.  But the
vertical spacing will be at 6.75 rows from the top -- not 6
as one might think.

There's a pretty good reason for this.  Think of a character
cell:
       +-------+
       |       |
       |       |
       |       |  /______ Baseline is set to 75%
       |       |  \       of the current VMI setting
       +-------+

This little extra nudge moves the cursor so that the top of
the character cell will fall at the specified location.  In
this example -- the TOP of the first character we print
should appear 1" from the top edge and 2.25" from the left
edge.

In fact, the only time that the difference is even noticed
is when mixing text and graphics.  (Shading is a graphic
function on the LaserJets.)

Therefore, when shading a line of text, the shading
procedure should:

1. move the cursor up 75 percent of the height of the
   current line height;

2. fill the desired area;

3. move the cursor down 75 percent of the height of the
   current line height;

4. print the line of text.

Thus, the up and down cursor movements are:

             Line Height       Movement
   lpi       (decipoints)    (decipoints)
---------    ------------    ------------
    4           180              135
    6           120               90
    8            90               67.5

(line height = (1 inch/X lpi)*(720 decipoints per inch)
============================================================

The principles discussed above are used in three sample
programs.  The first (SHADETXT.PAS) is included in the
LZRTPU.ZIP file.  The other two (SHADE1.PAS and SHADE2.PAS)
are available in Library 0 of the HP forum.  SHADETXT.PAS is
a sample program showing alternating lines of shaded text.
SHADE1.PAS produces a pattern similar to "green bar" paper
in the portrait format while SHADE2.PAS does the same thing
except in the landscape format.

By the way, if you browse the HP library, you will see a
SHADE3.PAS file.  That is the original version of the
SHADETXT.PAS program.