Upgrading your Central Station Laptop_To_Ethernet link 
                       for use with LANtastic V5.0
        ------------------------------------------------------
                    (C) Copyright 1993 Artisoft, Inc.
                            (Edition 1.00)

INTRODUCTION
============
This file provides information to enable you to upgrade your Central Station
Laptop_To_Ethernet (LTE) link for use with LANtasitic V5.0.

Do not perform this upgrade if your network is not running LANtastic V5.0.

How to Determine Your Version of LANtastic
==========================================
If you are running DOS-based LANtastic, look for the version number at the
top of any menu.  If you are using LANtastic from the command line, look
for the version number in the sign-on message when you load the network
software.  If you are running LANtastic Windows Version, pull down the Help
menu from the NET or NET_MGR Main Functions menu, then choose About Net or
About Net Manager.

Upgrading your Central Station
==============================
To upgrade your software:

       1.  Connect the Central Station to a PC (if it is not already).
           Instructions for doing this appear in your StationWare for
           LANtastic User's Manual.

       2.  Make sure the PC is not running CSPPORT.  At the DOS prompt,
           type:  CSPPORT/REMOVE

       3.  Using a diskette containing the upgrade software place it 
	   into your PC's floppy drive.  Type:
                          A: <Enter>
                          CSCONFIG <Enter>
           where "A:" is the floppy drive in which you placed the diskette.
           If you connected the Central Station to the computer's LPT2
           port, type:
                          A: <Enter>
                          CSCONFIG PORT=LPT2 <Enter>

           You can also copy the files from the StationWare diskette to
           your PC's hard drive and upgrade your software from there.

       4.  You may be prompted to reset the Central Station.  If the
           Central Station power is on, turn it off for at least four
           seconds, then turn it back on.

       5.  From the CSCONFIG Main Functions menu, select Central Station
           System Software <Enter>.

       6.  Select Update System Software <Enter>.

       7.  When the upgrade process is finished press Esc to exit to 
	   the Main Functions menu, then press Esc again.

       8.  You are asked if you would like to save the changes.  Press
           Enter to select YES.

        
           Your Central Station LTE system software is now upgraded 
           and ready for use on your LANtastic V5.0 network.


1993 Artisoft, Inc.  All rights reserved.  Central Station and StationWare 
are trademarks, and Artisoft and LANtastic are registered trademarks of 
Artisoft, Inc.  Brand names and product names are trademarks of their 
respective companies.

Artisoft, Inc.
691 E. River Road
Tucson, AZ 85704 USA
Sales/Customer Service:  1-800-TINY-RAM
Technical Support:  1-602-293-6363
Headquarters:  1-602-293-4000
Fax:  602-293-8065


Edition 1.00