XR v1.14 - X10 Report Program
                 Copyright (c) 1991 by Adrienne Cousins
                          All Rights Reserved

                              VersaWare
                30 Jennifer Street, Littleton, MA 01460
                  508-486-9351 (Voice 9am-4pm Eastern)
                   508-486-8507 (24 hour Support BBS)


 This program provides a couple of simple functions for the X10 that I have
 been unable to find in any other X10 program, and have found very useful
 while connecting and reprogramming my X10 computer interface.

 The most useful function is the STATUS report (-S) which requests the
 X10 to return an actual list of currently programmed events.
 XR will translate the data returned from the X10 into an english format
 report using the same "tokens" as the XA program.  This report will
 show ALL events that are programmed in the X10 (many X10 control programs
 do not clear prior events before programming new ones), and will also
 show actual times that were calculated by "tokens" such as SUNRISE and
 SUNSET.

 The other useful function is the WATCH function (-W) which monitors the
 serial port for data received from the X10.  Anytime a rocker switch is
 pressed, or a programmed event occurs, the X10 sends a data packet to
 the PC describing the event that just occurred.  If XR is running in
 WATCH mode when this happens, the event is described on screen using the
 same english "tokens" used by the XA program.

 All output from XR can be redirected to any standard output device or
 disk file.

                  -----------------------------------------

 XR command syntax & functions:

        XR [<cmd>][,<cmd>][,<cmd>] [>>outfile]

 Where <cmd> can be any of the following switches.

 ?      Print a short help text to the screen

 -A     Echo all X10 I/O to the screen in ascii
        Causes all data sent to or received from the X10 to be echoed to
        the screen in ascii.  This can also be redirected to any standard
        output device or file.

 -Bn    Set baud rate of serial port (300-19200)
        Causes the serial port to be set to the specified speed.
        If this switch is not specified, XR will use the serial port at
        the currently initialized speed.
        This is so that XR can also be used with X10s attached via Lawns.

                XR -B600,-W

 -H     Echo all X10 I/O to the screen in hexadecimal
        Causes all data sent to or received from the X10 to be echoed to
        the screen as hexadecimal bytes.  This data can also be redirected
        to any standard output device or file.

                XR -H,-W

 -Pn    Serial port that X10 is connected to (1-4)
        Use this switch to specify a serial port other the default of COM1.
        Multiple -P switches may appear on the line, to send commands to
        multiple serial ports in a single command.

                XR -P1,-S,-P2,-S

 -S     Display status of all events in the X10
        Causes the X10 to be queried for a list of all events currently
        programmed.  The data will be translated into english "tokens"
        and displayed on the screen.  This report can also be redirected
        to any standard output device or file.

                XR -S >X10STS.LOG

 -Tf:l  Change X10 timeout tick counts (first:last)
        The value called FIRST, is the timeout in ticks until the first
        byte is received from the X10.  The value called LAST, is the
        timeout in ticks after the last byte is received from the X10.
        FIRST defaults to 36 (2 secs), and LAST defaults to 18 (1 sec).

 -W     Watch for any data received from the X10
        This monitors the serial port for any data received from the X10.
        It may be used in conjunction with the -A and -H echo switches.
        This mode is terminated on any keystroke.

                XR -H,-W

        -----------------------------------------------------------

 A list of the tokens used by XR are as follows:

        HOUSE, NORMAL, SECURITY
        TODAY, TOMORROW, EVERYDAY, WEEKENDS, WEEKDAYS
        MONDAY, TUESDAY, WEDNESDAY, THURSDAY, FRIDAY, SATURDAY, SUNDAY
        TIME, UNIT, LEVEL, ON, OFF, DIM, An-Pn

 A sample status report follows:

        XR -S
        Status:1 TIME 6:52 pm MONDAY HOUSE A
        Event:0 NORMAL WEEKENDS TIME 4:00 am A8 Level:0 ON
        Event:1 NORMAL WEEKDAYS TIME 7:00 am A8 Level:0 ON
        Event:2 NORMAL EVERYDAY TIME 8:53 pm A2 Level:7 DIM
        Event:3 NORMAL EVERYDAY TIME 9:00 pm A2 Level:3 DIM
        Event:4 NORMAL EVERYDAY TIME 12:00 am A2 Level:0 OFF
        Event:5 NORMAL EVERYDAY TIME 8:53 pm A3 Level:7 DIM
        Event:6 NORMAL EVERYDAY TIME 10:00 pm A3 Level:11 DIM
        Event:7 NORMAL EVERYDAY TIME 4:49 am A3 Level:0 OFF

 A sample WATCH session with HEX echo enabled follows:

        XR -H,-W
        Press any key to exit Watch mode
        <R:FF FF FF FF FF FF 01 62 00 08 60 CA
        Status:1 ON A5
        <R:FF FF FF FF FF FF 01 63 00 08 60 CB
        Status:1 OFF A5