Sounding Board (tm) adapter Test Procedure
        ___________________________________________


     The Sounding Board (tm) adapter can be tested by running
     either a handset test called HTEST.EXE, or a Line-In and
     Line-Out test called LTEST.EXE.  Both of these tests re-
     quire the Sound adapter to be used in full-duplex mode,
     i.e. using both DMA channels 1 and 3.  If you intend to use
     the board in half-duplex mode only, then use SAY.EXE AND
     RECORD.EXE to separately play and record messages to verify
     that the adapter is working.

     Testing the Sound adapter in full-duplex mode:
     -------------------------------------------

     You will need a standard phono plug to phono plug cable to
     perform the Line-In and Line-Out test, and you will also need
     to test the handset provided.

     For running either of the tests verify the following:

     1. Jumpers J1 and J2 are both in the ON position on the
        Sound adapter.  This selects the use of both DMA channels
        1 and 3.
     2. The SOUNDBD.EXE driver is installed using both DMA
        channels.

     To run the handset test:
     -----------------------

     1. Plug the handset into the RJ-11 jack on the Sound adapter.
        Place the handset on a smooth, flat surface such that the
        mouthpiece and speaker are facing downward.  This provides
        an acoustical coupling between the microphone and speaker.

     2. Run the HTEST.EXE program.  You should hear an audible beep
        and then a message will appear indicating the result of the
        test.  A "Handset passed" message will be shown if the
        test passed.  If any other message appears, verify that the
        handset is positioned correctly and that it was not bumped
        during the test.  Run the HTEST.EXE program again to verify
        the results.

     Running the Line-In and Line-Out test:
     -------------------------------------

     1. Remove the handset from the jack on the Sound adapter.
        Insert the phono plugs, one side into Line-In and the other
        side into Line-Out.

     2. Run the LTEST.EXE program.  The result of the test will
        immediately appear.  A "Line-In and Line-Out passed"
        message will be shown if the adapter passed.  If any other
        message appears verify that the cable is plugged in
        correctly and run the LTEST.EXE program again.

     Testing the Sound adapter in half_duplex mode:
     ---------------------------------------------

     Verify the following before testing:

     1. Place either J1 or J2 in the ON position depending on
        whether you are using DMA channel 1 or 3 respectively.
     2. The SOUNDBD.EXE is installed specifying which DMA
        channel is in use.

     The RECORD.EXE program is used to record a message through both
     the handset and the Line-In jack to a file.  The syntax for using
     the program is:

     RECORD[option] filename

     where "option" represents the optional switch /C if you want to
     enable 2-to-1 compression on the file and filename represents the
     name of the file to record data into.  Press any key to abort the
     program.

     The SAY.EXE program is used to play a message from a file to the
     handset and to the Line-Out jack.  The correct syntax is:

     SAY[option] filename

     where "option" represents the optional switch /C if the file was
     recorded with compression and filename represents the name of
     the file to be played.  Press any key to abort the program.

     Once you've successfully recorded and played a message, the Sound
     adapter is fully tested.


Note: You can also run the RECORD.EXE and SAY.EXE programs when using
      the Sound adapter in full-duplex mode.