AHA- 1540A/1542A Technical Reference
                                                                            
Copyright 1989 Adaptec, Inc. All rights reserved. 

No part of this publication may be reproduced, stored in a retrieval system, or 
transmitted, in any form or by any means, electronic, mechanical, photocopying, 
recording, or otherwise, without the prior written consent of Adaptec, Inc. 691 
South Milpitas Blvd., Milpitas, CA 95035. 

TRADEMARKS 

IBM is a registered trademark, PS/2, PC AT, DOS, MS-DOS, OS/2 and Micro Channel 
are trademarks of International Business Machines Corporation. SCO and SCO 
XENIX are trademarks of The Santa Cruz Operation. Unix is a registered 
trademark of AT & T Bell Laboratories. 

CHANGES 

The material in this manual is for information only and is subject to change 
without notice. 
While reasonable efforts have been taken in the preparation of this manual to 
assure its accuracy, Adaptec, Inc. assumes no liability resulting from any 
errors or omissions in this manual, or from the use of the information 
contained herein. 
Adaptec reserves the right to make changes in the product design without 
reservation and without notification to its users. 
Additional information may be obtained from: 
Adaptec Literature Department 691 South Milpitas Blvd. Milpitas, CA 95035 

This equipment generates and uses radio frequency energy and if not installed 
and used properly, that is, in strict accordance with the manufacturer's 
instructions, may cause interference to radio and television reception. It has 
been type tested and found to comply with the limits for a Class B computing 
device in accordance with the specifications of Subpart J of Part 15 of FCC 
Rules, which are designed to provide reasonable protection against such 
interference in residential installation. However, there is no guarantee that 
interference will not occur in a particular installation. If this equipment 
does cause interference to radio or television equipment reception, which can 
be determined by turning the equipment off and on, the user is encouraged to 
try to correct the interference by one or more of the following measures: 
	Reorient the receiving antenna 	Relocate the computer with respect to the 
receiver 	Move the computer away from the receiver 	Plug the computer into a 
different outlet so that computer and receiver are on different branch circuits 

If necessary, the user should consult the dealer or an experienced 
radio/television technician for additional suggestions. The user may find the 
following booklet prepared by the Federal Communications Commission helpful: 
	"How to Identify and Solve Radio-TV Interference Problems" This booklet is 
available from the U.S. Government Printing Office, Washington, D.C. 20402, 
Stock No. 004-000-00345-4. 

Warning: This equipment has been certified to comply with the limits for Class 
B computing device, pursuant to Subpart J of Part 15 of FCC Rules. Only 
peripherals (computer input/output devices, terminals, printers, etc.) 
certified to comply with the Class B limits may be attached to this computer. 
Operation with non-certified peripherals is likely to result in interference to 
radio and TV reception. Also this equipment must be used with shielded power 
cables and shielded I/O cables. 


AHA-1540A and AHA-1542A Industry PC/AT-to-SCSI Host Adapter User's Manual and 
Specification Copyright 1989  Adaptec, Inc. All Rights Reserved 

Reproduction or use, without express written permission from Adaptec, Inc. 
and/or its licensor, of any portion of this manual is prohibited. While 
reasonable efforts have been taken in the preparation of this manual to assure 
its accuracy, Adaptec, Inc. assumes no liability resulting from any errors or 
omissions in this manual, or from the use of the information contained herein. 



1.0  Introduction........................................................1-1 
1.1  Document Scope......................................................1-1 
1.2  Purpose.............................................................1-1 
1.3  Features............................................................1-1 
1.4  Product Specifications..............................................1-2 
1.5  Reference Documents.................................................1-4 

2.0  Host Adapter Architecture...........................................2-1 
2.1    Hardware..........................................................2-1 
2.1.1  Bus Master DMA....................................................2-1 
2.1.2  SCSI Protocol Chip................................................2-1 
2.1.3  8-Bit Memory......................................................2-1 
2.1.4  Block Diagram.....................................................2-2 
2.2    Firmware..........................................................2-4 
2.2.1  Multithreaded Operation...........................................2-4 
2.2.1.1  Mailboxes.......................................................2-4 
2.2.1.2  Command Control Block...........................................2-5 
2.2.1.3  Command Descriptor Block........................................2-6 
2.2.1.4  Principles of Operation.........................................2-6
2.2.1.5  Task Queueing...................................................2-7
2.2.2    Single Threaded Operation.......................................2-7

3.0  Installation........................................................3-1
3.1  Unpacking and Inspecting............................................3-1
3.2  Installation........................................................3-1
3.2.1  System Configuration..............................................3-1
3.2.2  Hardware Setup....................................................3-2
3.2.3  Checklist.........................................................3-4
3.2.4  Operation Using the BIOS under DOS................................3-4
3.3  Jumper Configuration................................................3-5
3.3.1  Jumper Block J1...................................................3-6
3.3.1.1  SCSI Synchronous Negotiation....................................3-6
3.3.1.2  Diagnostic Jumper...............................................3-6
3.3.1.3  SCSI Parity.....................................................3-6
3.3.2  SCSI Address......................................................3-7
3.3.3  DMA Channel.......................................................3-7
3.3.4  AT Interrupt Channel..............................................3-9
3.3.5  DMA Transfer Speeds...............................................3-10
3.3.6  AT BIOS Wait State................................................3-10
3.3.7  AT Port Address...................................................3-11
3.3.8  AT BIOS Address...................................................3-11
3.3.9  Front Panel LED...................................................3-11
3.3.10  LA Enable Jumper.................................................3-12
3.3.11  Auxiliary Jumpers................................................3-12
3.3.12  BIOS Enable/Disable..............................................3-12
3.3.13  SCSI Terminators.................................................3-13
3.3.14  SCSI Terminator Power............................................3-13
3.4.1  Flexible Diskette Controller Secondary Address....................3-13
3.4.2  Flexible Diskette Controller Enable...............................3-13
3.4.3  Flexible Diskette Controller Interrupt Channel....................3-13
3.4.4  Flexible Diskette Controller DMA Request Channel..................3-14 
3.4.5  Flexible Diskette Controller DMA Acknowledge Channel..............3-14 
3.4  Flexible Diskette Controller Jumpers (AHA-1542A Only)...............3-13

4.0  Hardware Functional Description.....................................4-1
4.1  Overview............................................................4-1
4.2 I/O  Port Interface..................................................4-1
4.2.1  Control and Status Port...........................................4-2
4.2.2  Command and Data Port.............................................4-4
4.2.3  Interrupt Flag Port...............................................4-5
4.3  Reset Overview......................................................4-7
4.3.1  Hard Reset Operations.............................................4-7
4.3.2  SCSI Reset Operations.............................................4-7
4.3.2.1  SCSI "Soft" Reset Option........................................4-8
4.3.2.2  SCSI "Hard" Reset Option........................................4-9 

5.0   Firmware Functional Description....................................5-1
5.1  Host Adapter Command Overview.......................................5-1
5.1.1  Host Adapter Operation Codes......................................5-1
5.1.1.1  No Operation....................................................5-2
5.1.1.2  Mail Box Initialization.........................................5-2
5.1.1.3  Start SCSI Command..............................................5-3
5.1.1.4  Start PC/AT BIOS Command........................................5-3
5.1.1.5  Host Adapter Inquiry............................................5-3
5.1.1.6  Enable Mailbox Out Available Interrupt..........................5-4
5.1.1.7  Set Selection Time-out..........................................5-4
5.1.1.8  Set Bus-On Time.................................................5-5
5.1.1.9  Set Bus-Off Time................................................5-5
5.1.1.10  Set Transfer Speed	............................................5-6
5.1.1.11  Return Installed Device........................................5-7
5.1.1.12  Return Configuration Data......................................5-8
5.1.1.13  Enable Target Mode Command.....................................5-8
5.1.1.14  Return Setup Data..............................................5-9
5.1.1.15  Write Adapter Channel 2 Buffer.................................5-11
5.1.1.16  Read Adapter Channel 2 Buffer..................................5-12
5.1.1.17  Write Adapter FIFO Buffer......................................5-12
5.1.1.18  Read Adapter FIFO Buffer.......................................5-12
5.1.1.19  Echo Command Data..............................................5-13
5.2  Mailbox Command Overview............................................5-13
5.2.1  Mailbox-Out Definition............................................5-14
5.2.2  Mailbox-In Definition.............................................5-15
5.3  Command Block Definition............................................5-19
5.3.1  Scatter Gather Definition.........................................5-25
5.4  Description of Operation............................................5-26
5.4.1  Execution of Initiator Mode Operations............................5-27
5.4.2  Execution of Target Mode Operations...............................5-28
5.4.2.1  Target Mode With a Prepared CCB.................................5-28
5.4.2.2  Target Mode Without a Prepared CCB..............................5-28
5.5  DMA Channel Initialization With the Host Adapter BIOS Disabled......5-29
5.6  Interrupt Initialization............................................5-29

 
6.0  Single-Threaded Software Interface..................................6-1
6.1  Single Threaded BIOS Command Interface..............................6-1
6.2  BIOS Command Execution Using Interrupt 13...........................6-2
6.2.1  Physical to Logical  Translation..................................6-2
6.2.2  BIOS Command Return Codes.........................................6-3
6.3  BIOS Disk Commands..................................................6-4
6.3.1  Reset Disk Subsystem..............................................6-5
6.3.2  Read Status of Last Operation.....................................6-5
6.3.3  Read Desired Sectors Into Memory..................................6-6
6.3.4  Write Desired Sectors From Memory.................................6-6
6.3.5  Verify Desired Sectors............................................6-6
6.3.6  Identify SCSI Devices.............................................6-7
6.3.7  Read Drive Parameters.............................................6-7
6.3.8  Initialize Drive Pair Characteristics.............................6-8
6.3.9  Seek..............................................................6-8
6.3.10  Alternate Disk Reset.............................................6-8
6.3.11  Test Drive Ready.................................................6-9
6.3.12  Recalibrate......................................................6-9
6.3.13  Read DASD Type...................................................6-9
 

7.0  Device Drivers......................................................7-1
7.1  PC/AT BIOS..........................................................7-1
7.1.1  Initialization....................................................7-1
7.1.2  System Boot.......................................................7-2
7.1.3  Hard Disk I/O.....................................................7-2
7.2  XENIX/UNIX..........................................................7-2
7.3  DOS Driver..........................................................7-2
7.3.1  DOS Driver Support of Virtual Mode................................7-3
7.4  AHA-1540 On-board Utilities.........................................7-4

8.0  SCSI Features.......................................................8-1
8.1  SCSI Description Initiator Mode.....................................8-1
8.1.1  Linked SCSI Commands..............................................8-2
8.1.2  Zero Latency Read Operation.......................................8-2
8.1.3  SCSI Messages.....................................................8-3
8.2  SCSI Description, Target Mode.......................................8-3
8.2.1  Initiator Conformance Level Requirements..........................8-3
8.2.2  Support of Synchronous Transfer...................................8-3
8.2.3  SCSI Target Operation in Processor Target Mode....................8-4
8.2.3.1  Test Unit Ready.................................................8-5
8.2.3.2  Request Sense...................................................8-5
8.2.3.3  Inquiry.........................................................8-7
8.2.3.4  Send............................................................8-8
8.2.3.5  Receive.........................................................8-9
8.2.4 Incorrect Length Management........................................8-9

9.0  Floppy Disk Interface...............................................9-1

10.0  Problem Determination..............................................10-1
10.1  Self Diagnostic Capability.........................................10-1
10.2  Indicators.........................................................10-2
10.3  Problems Detected During Operation.................................10-2
10.3.1  HA Status Error Indications and Corrective Actions...............10-3
10.3.2  SCSI Error Indications and Corrective Actions....................10-5
10.4  Problems Detected During Installation..............................10-7 

11.0  Glossary...........................................................11-1
 

Appendix A  AHA-1540 System Timing Diagram................................A-1
Appendix B  Connector Pin Out.............................................B-1
Appendix C  Product Comparison and Compatibility..........................C-1 


1.1 DOCUMENT SCOPE 

This manual provides the information required to install and program the AHA-
1540A and the AHA-1542A  Intelligent Host Adapters in  AT bus-based systems. 

1.2 PURPOSE 

The Adaptec AHA-1540A and AHA-1542A provide a powerful  multitasking interface 
between the Industry Standard Architecture (PC/AT compatible) bus and the Small 
Computer System Interface (SCSI) bus. The AHA-1540A/1542A are high performance 
intelligent host adapters supporting a maximum asynchronous SCSI rate of 2.0 
MBytes/second and a synchronous transfer rate of 5 MBytes/second. The AHA-
1540A/1542A support multithreaded I/O operations, allowing simultaneous 
operations on multiple targets/LUNs. Disconnect/Reconnect support maximizes bus 
utilization for multiple target systems. Target mode operation allow the AHA-
1540A and AHA-1542A to receive information from other host adapters. Scatter-
gather allows high-performance even in systems with fragmented memory buffers. 

The Adaptec AHA-1540A/1542A provides a solution for system applications 
requiring very high performance, configuration flexibility and multithreaded 
I/O capability, and system redundancy. The Adaptec BIOS also allows the AHA-
1540A/1542A to be used in place of a standard hard disk controller.  The AHA-
1540A host adapter provides only the high performance host adapter circuitry. 
The AHA-1542A host adapter provides identical host adapter circuitry, but adds 
an IBM compatible flexible diskette controller to the circuit board. 

1.3 AHA-1540A/1542A PRODUCT FEATURES 

	High performance Bus Master DMA with selectable or programmable data rates of 
 up to 10 
	MBytes/second. 
	16- and 8-bit transfers 	Odd and Even starting address 
 transfers and odd or even data lengths 
	Maximum synchronous SCSI transfer rate of up to 5.0 MBytes/second 
	Asynchronous and synchronous peripherals supported simultaneously 
	Programmable AT bus burst transfer on and off time 
	Jumper selectable DMA channel for bus arbitration (channels 0,5,6,7) 
	Jumper selectable interrupt channels (IRQ 9, 10, 11, 12, 14, 15) 
	True multithreaded operation supporting up to 255 tasks simultaneously 
	Programmable mailbox architecture ¥	Adaptec BIOS for standard hard disk 
 emulation 
	Jumper selectable I/O port address 
	Internal and external SCSI connectors 
	Initiator and Target modes of operation fully supported 
	On-board flexible diskette controller (AHA-1542A only) ¥	Scatter-gather 

1.4 PRODUCT SPECIFICATIONS

	Physical Dimensions: 
 	Length : 13.25 "  Width : 4.125"   Height : 0.5" 
 Standard PC/ATª compatible form factor 
Power Requirements:  
 	+5.0 +/- 0.25 Volts at 2.1 Amps maximum. 
Environmental Requirements: 
 	Temperature 0-60 degrees C (operating or storage) 
Reliability Information 
 	Mean Time Between Failures:	15000 hours 			(calculated 
  per Mil Handbook 217E, ground benign, 40 ¡C) 
 	Mean Time Between Failures:	TBD hours 			(experimental) 
 	Mean Time to Repair:				30 minutes 
 	Industry Standard Architecture Interface 
Standard PC/AT bus electronic and physical interface. 
 	Driver output: 
 VOL: min:0 volts max.  0.4 volts IOL:	24 ma. 
 VOH: min:2.4 volt max. 5.25 volts
 IOH:  8 ma. 
Receiver Input 
 VIL: 0.8 volts 
 VIH:	2.0 volts 	

Connector configuration as specified by IBM PC/AT Technical Reference Manual or 
manual of Industry Standard Architecture host computer. 

	SCSI Interface:

Electrical Interface: 

	As specified by ANSI X3.131-1986 for single-ended operation. 
  Minimum driver output:48 milliamps, sinking @ 0.5 volts 
  Signal true:min: 0 volts max:   0.8 volts 
  Signal false:min:2.0 volts max:5.25 volts 
  Input hysteresis:min: 0.2 volts 	
Terminator Power voltage: min:4.25 volts  max:5.25 volts 
Terminator Power current: min:800 ma.  max:1.5 amp (fused) 
Internal connector: Unshrouded 50-pin header, compatible with unshielded 
alternative 1 connector as specified in ANSI X3.131-1986 
Figure 4-1 For connector pin out, see Appendix B. Partial list of 
compatible connector plugs (for reference only): Manufacturer Model Part Number 
3-M	N.A.	3425-6000 T&B Ansley	N.A.	609-5000M Molex	N.A.	15-29-8505 

Cable for internal SCSI connector should be good quality 50 conductor flat 
cable with 26 or 28 gauge conductors and a characteristic impedance (Z0) of 100 
 10. Cable shielding is necessary if extremely noisy circuitry or extremely 
noise sensitive circuitry is present inside the host computer frame. 

External connector: 
Shielded 50-pin connector as specified in ANSI X3.131-1986, Figure D-4. 
For connector pin out, see Appendix B. 
Partial list of compatible connector plugs or cable assemblies  (for reference 
only):Manufacturer Model Part No. Amphenol N.A. 200-1M115-02003(Mates with 57-
BC50B-AM200) AMP Champ Plug 554953-1 Cover 554946-x(1-2) Ferrule	554725-x(1-6) 

Cable for external SCSI connector should be good quality 100% shielded round 
cable with 25 twisted pairs.  Each pair should have a characteristic impedance 
(Z0) between 90 and 135 ½. Wire gauge may be 26 or 28 AWG.  All pairs should 
have the same impedance and should have the same delay per length of cable. 
Cables meeting these requirements will normally operate correctly in any SCSI 
configuration and should normally meet all FCC requirements. 
	Floppy Disk Interface 
  Standard Floppy Disk electronic and physical interface: 
       Driver output:  VOL: min: 0 volts max. 0.5 volts
                       IOL: 60 ma. 
                       VOH: open collector  max. 5.25 volts 
                       IOH:.1 ma. 

      Receiver Input 
Tied to +5 volt supply through 150 ohm resistors. Schmidt Trigger with 0.8 
volts hysteresis VT-:max 1.0 volts  VT+:		min	1.4 volts 	

Connector: Unshrouded 34-pin header. For connector pin out, see Section 9.1 
Partial list of compatible connector plugs (for reference only): 
Manufacturer  Model  Part Number 
3-M           N.A.   3414-6000 
T&B Ansley    N.A.   609-3400M 
Cable for floppy connector should be good quality 34 conductor flat cable with 
28 gauge conductors. Addressing of the second drive may be generated by 
twisting connector signals 10 through 16 or by changing jumpers in the floppy 
disk drives. Meets radiation limits specified for a Class B computing device in 
accordance with the specifications in Subpart J of Part 15 of FCC Rules. See 
FCC Compliance notes and recommendations in preface of this document.
1.5 REFERENCE DOCUMENTS IBM PC/AT Technical Reference Manual 
	Small Computer System 
Interface, ANSI X3.131-1986, American National Standards Institute 
Adaptec AHA-1540A/AHA-1542A Host Adapter Installation Guide 
Adaptec AHA-1540 Programming Guide 


2.1 HARDWARE 


2.1.1 Bus Master DMA 

The AHA-1540A/1542A controls the host AT bus as a master and transfers data 
directly to and from main system memory. This implementation is known as Bus 
Master DMA. Bus Master DMA greatly reduces the host software overhead because 
the host CPU is no longer required to maintain the DMA channel's address 
pointers and word counts. Bus Master DMA also reduces the number of interrupts 
generated per I/O command. The Adaptec AIC-560L is the DMA controller. 
Adaptec's implementation of Bus Master DMA can achieve a 10 MB/second burst 
data rate. This speed is especially valuable in multitasking systems where the 
tasks execute on a time shared basis. Appendix A shows a diagram of the timing 
required to achieve the DMA rates that are supported by the AHA-1540A/1542A. 
The AHA-1540A/1542A DMA hardware will handle both odd-byte and odd-memory 
address data transfers with no performance degradation. 

2.1.2 SCSI Protocol Chip (AIC-6250) 

The AHA-1540A/1542A utilizes the AIC-6250 SCSI protocol chip to maximize the 
SCSI bus utilization. The AIC-6250 is an Adaptec VLSI device which allows the 
AHA-1540A/1542A to achieve greater than 2.0 MBytes/Sec asynchronous SCSI data 
transfer rates, and up to 5.0 MBytes/second synchronous transfer rates. The 
AIC-6250 will also enable the AHA-1540A/1542A to operate as both an initiator 
and as a target device. Through a 16-bit host interface, the AIC-6250 reduces 
bus busy time during data transfer by bursting data across the AT bus at up to 
10 MBytes/second. The AIC-6250 has separate data busses for the local 
microprocessor and for the system data bus. This further increases the 
performance of the AHA-1540A/1542A by reducing the overhead associated with 
SCSI commands. 

2.1.3  8 Bit Memory 

During normal DMA operations, nearly all transfers to and from memory are 16 
bit transfers. At the very end, or the very beginning of an odd address 
boundary, an 8 bit transfer on the upper data bits (D8-D15) will occur 
according to the AT bus architecture. Some memory in the I/O space, such as 
video RAM, is 8 bits only and always transfers data only on the lower data bits 
(D0-D7). The AHA-1540A/1542A will transfer 16 bit or 8 bit memory in the 
address space between 0A0000 hex and 0BFFFF hex depending on the signal line 
MEM16 on the AT bus. If this signal is active, 16 bit memory is assumed, and if 
inactive 8 bit memory is assumed. Outside of this address space 16 bit memory 
is always assumed. 

2.1.4 Hardware Block Diagram(cannot be included because of ASC transmission) 

BLOCK DIAGRAM OF AHA-1540A 
BLOCK DIAGRAM OF AHA-1542A 

2.2 FIRMWARE

The AHA-1540A/1542A supports multithreaded SCSI initiator operation through a 
simple mailbox protocol. The firmware accepts as many Command Control Blocks 
(CCB's) as required and executes them from its local RAM. The firmware controls 
all of the SCSI activity that a task may require. This includes: Arbitration, 
Selection, Disconnection, Reconnection, and Command completion. 

Using the same mailbox protocol, the AHA-1540A/1542A can operate as a Processor 
type device serving as a multitasking target to other initiators. This feature 
allows high bandwidth communication between multiple hosts. 

In addition, the AHA-1540A/1542A firmware cooperates with the BIOS installed on 
the host adapter to emulate the standard DOS BIOS calls. This allows booting 
operations and the execution of standard DOS operations from attached SCSI 
disks, allowing the SCSI subsystem to completely replace the usual internal 
disk functions. 

2.2.1 Multithreaded Operation 

A multiuser, multitasking operating system issues a large number of I/O tasks 
in a rapid sequence. The architecture of the AHA-1540A/1542A makes management 
of this activity very easy and straight forward for the operating system and 
its associated I/O drivers. This section briefly explains the interaction 
between the system and the AHA-1540A/1542A required to accomplish an I/O task. 

2.2.1.1 Mailboxes 

The AHA-1540A/1542A uses a mailbox architecture for task communication between 
the host and host adapter. This allows the host adapter to perform 
multithreaded operations with a minimum of host intervention.The mailboxes are 
located in main system memory . Each mailbox entry is four bytes long. After 
power up sequencing, host initialization procedures, and the boot procedure are 
completed, the host issues an initialization command to inform the host adapter 
of the mailbox location. There are always an equal number of Outgoing Mailboxes 
(MBO) and Incoming Mailboxes (MBI). MBIs are located immediately after the 
MBOs. A typical mailbox structure is shown below: 
Base address 
            +0-CMD----CCB 4 POINTER----MBO 0
            +4-CMD----CCB 2 POINTER----MBO 1
            +8-00-----FREE ENTRY-------MBO 2
           +12-CMD----CCB 3 POINTER----MBO 3
           +16-00-----FREE ENTRY-------MBI 0
           +20-STATUS-CCB 1 POINTER----MBI 1
           +24-00-----FREE ENTRY-------MBI 2
           +28-00-----FREE ENTRY-------MBI 3
In this example there are four MBOs and four MBIs. The first byte of each MBO 
contains the MBO Command byte. The remaining three bytes point to a Command 
Control Block (CCB). The CCB provides all the rest of the information needed to 
complete a task. A MBO is available to accept a new entry if the first byte is 
zero. 

The first byte of each MBI contains the status of a completed task. The 
remaining three bytes point to the CCB of the completed task. An MBI is free if 
the Status byte is zero. Mailboxes may point to CCB's controlling initiator 
tasks, controlling target tasks, or controlling error recovery tasks. 

2.2.1.2 Command Control Block 

A Command Control Block provides the information required to control a SCSI 
command sequence. The block contains pointers to the data area to be used by 
the command. It contains areas for presenting status of both the host adapter 
and the addressed SCSI device. In addition, it contains the SCSI Command 
Descriptor Block defining the action to be taken by the addressed SCSI device. 
An error information buffer area is also provided. 

A Command Control Block is also used to service an operation requested by 
another initiator when the AHA-1540A/1542A is being addressed as a SCSI 
Processor device. 

The CCB is defined completely in Section 5. 

A typical CCB is shown below: 

2.2.1.3 Command Descriptor Block 

The Command Descriptor Block (CDB), a part of the Command Control Block, is a 
standard format command packet that is transmitted to the addressed SCSI 
device. It contains all the command information required by the SCSI device to 
perform the desired operation. The Command Descriptor Block contains the 
command Operation Code followed by a Logical Unit Number (LUN), command 
parameters if required, and a control byte. A typical Group 0 six byte CDB is 
shown below:         BITÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
             BYTE  7     6     5     4     3     2     1     0
              0    ÃÄOÄPÄEÄRÄAÄTÄIÄOÄNÄÄÄÄÄCÄÄOÄÄDÄÄEÄÄÄÄÄÄÄÄÄÄÄ´
              1    ÃLÄÄÄUÄÄÄNÄÄÄÄÄ´ÃÄLOGICALÄBLOCKÄADDRESSS(MSBÄ´
              2    ÃÄÄÄÄÄÄÄÄLOGICAL BLOCK ADDRESSÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
              3    ÃÄÄÄÄÄÄÄÄLOGICAL BLOCK ASDDRESS(LSB)ÄÄÄÄÄÄÄÄÄ´
              4    ÃÄÄÄÄÄÄÄÄTRANSFER LENTHÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
              5    ÃVENDOR´ÃÄÄÄÄÄRESERVEDÄÄÄÄÄÄÄÄÄÄÄ´ÃFLAG´ÃLINK´

Please refer to the SCSI specification  ANSI X3.131, the Common Command Set 
(CCS) revision 4B, and the SCSI 2 draft for additional information on Command 
Descriptor Blocks. 

2.2.1.4 Principles of Operation 

At power-up, the host must inform the host adapter of the location and number 
of mailboxes. To start a task, the host builds a CCB and stores its memory 
address into a free mailbox. A non-zero Mailbox Out command byte is then 
written to indicate that the mailbox entry is full and valid. The host then 
writes to an I/O port (defined in section 4) to indicate that the host adapter 
should scan the MBO area. When a full MBO is found, the host adapter copies the 
mailbox's CCB pointer into its internal RAM and clears the Mailbox entry by 
writing a zero to the MBO command byte. This frees the MBO so that it can be 
used to start another task. 

After completing a task, the host adapter scans the MBI area for a free 
mailbox. When one is found, it is updated with the task's completion status and 
CCB pointer. The CCB pointer identifies the completed task. A MBI Stored 
interrupt is generated to notify the host that a task has been completed. The 
host scans the MBI area searching for a non-zero Status byte. When one is 
located, the host obtains the CCB pointer and frees the MBI by writing a zero 
into the Status byte. The host then examines the contents of the CCB to 
determine that the command was successfully completed. The freed MBI can now be 
used to indicate the completion of another task. The host adapter fills the MBI 
area and scans the MBO area in a round robin fashion. If the host saves the 
position of the last active MBI entry, it can determine the MBI of a new entry 
immediately without searching, since a new entry will be in the next MBI 
location. 

The host adapter transmits a new MBO Available or MBI Full interrupt to the 
host whenever all non-Mailbox interrupts have been cleared and serviced by the 
host. The host should analyze the interrupts and clear them as soon as possible 
so that the host adapter can post any new interrupts quickly. The host adapter 
will not wait until an interrupt can be transmitted to the host before 
processing an MBO entry or creating a new MBI entry. Thus, in processing a 
single MBI interrupt, the host may find several MBI entries waiting by the time 
the interrupt processing is finished. Similarly, a later MBI interrupt for the 
last of the later MBI entries may find nothing to service because the MBI entry 
was examined and processed as a result of the first MBI Full interrupt. If the 
interrupts are reset quickly by the host, the probability of an interrupt 
occurring when no MBI entry is available is much lower, providing an important 
performance improvement. If the MBI entries are emptied by the host in a round-
robin order, the scan for the next full entry is very simple, since it is 
always the next MBI entry in the Mailbox area. 


2.2.1.5 Task Queueing 

Multiple tasks may be started against a target/LUN or against multiple 
targets/Logical Units. Since only one task can be active against any one given 
LUN at a time, all other tasks for the same LUN are queued. Other LUN's may 
have active tasks at the same time. 

The host adapter dequeues on a first in, first out  (FIFO) basis for each 
target/LUN combination. However, due to the optimization algorithm used by the 
host adapter, a task may sometimes be started earlier in spite of it's late 
entrance in the queue on multiple target/LUN systems. Task queueing should not 
be used where changes in the order of command execution may cause data 
integrity failures. 

2.2.2 Single-Threaded Operation 

A host adapter BIOS is provided to emulate the standard  hard disk BIOS and 
boot functions. With this BIOS, the host adapter can be used in lieu of a 
standard hard disk controller on any ISA compatible system. 

The BIOS is compatible with the standard hard disk BIOS. This allows DOS to 
access up to two hard disk devices on the SCSI bus without a driver. All normal 
I/O functions are supported including system booting. Single threaded operation 
and multithreaded operation do not operate simultaneously. Single threaded 
operation cannot be requested until all multithreaded operations are completed. 
Similarly, all multithreaded operations must be complete before a single 
threaded operation can be requested. For most multitasking operating systems, 
such as Xenix and OS/2, single threaded operation is normally used only for the 
early part of the boot operation, after which multithreaded drivers take over 
all control of the SCSI operations. 

3.1 UNPACKING AND INSPECTION 

The carrier is responsible for damage incurred during shipment. In case of 
damage, have the carrier note the damage on both the delivery receipt and the 
freight bill, then notify your freight company representative so that the 
necessary insurance claims can be initiated. 

After opening the shipping container, use the packing slip to verify receipt of 
the individual items listed on the slip. Retain the  shipping container and 
packing material for possible later reuse should return of the equipment to the 
factory  necessary. 

CAUTION: The AHA-154XA is carefully designed to resist the effects of static 
electricity. However, like all electronic equipment , it can be damaged or its 
life can be shortened by unusual static discharges. Please take the proper 
precautions when handling the board. Keep the board in its conductive wrapping 
until it is ready to be installed in your system. Be sure that  the  host 
computer and the personnel handling the board are properly grounded while 
installing the board. 

3.2 INSTALLATION 

The following section details the installation procedure for the Adaptec AHA-
1540A/1542A AT to SCSI host adapter. The installation of the board consists of 
setting the various on-board jumpers, preparing the SCSI devices, installing 
the correct terminations, inserting the board into a full-length AT compatible 
connector, and connecting a SCSI cable from the on-board connector to a SCSI 
target. 

NOTE: The system must be turned off during the installation procedure. 

3.2.1 System Configuration 

The DOS operating system and the standard AT BIOS support two hard disk drives, 
drive C: and drive D:. If two standard hard disk drives are installed, they are 
the only hard disk drives accessible from the operating system. If one standard 
hard disk drive is installed, the AHA-154XA BIOS allows DOS to access the SCSI 
drive with the Target:LUN address of 0:0 as the second of the two supported 
drives (drive D:). If no standard hard disk drives are installed, the AHA-154XA 
BIOS allows DOS to access the SCSI drive with the address of 0:0 as the first 
of two supported drives (drive C:) and the SCSI drive with the address of 0:1 
or 1:0 as the second of the drives (drive D:). System booting is performed from 
the floppy drive if a floppy diskette is installed. If no floppy is installed, 
system booting is attempted from the drive chosen as drive C: through the above 
process, whether the drive is a standard hard disk or a SCSI hard disk. The 
AHA-154XA BIOS fully supports the extended partitioning capabilities of DOS 3.3 
for up to two drives. The AHA-154XA BIOS only supports the AHA-154XA if its I/O 
Port Address is set to 330h. 

Adaptec provides a special DOS driver for the AHA-154XA that allows the support 
of up to 24 physical or logical devices under DOS. Many other operating 
systems, including SCO Xenix and Unix, do not have this limitation and will 
allow the access of any number of attached SCSI devices. 

The term "standard hard disk" refers to the disks attached to the system by a 
standard ISA disk controller. These standard hard disks can be set to the 
"Installed" or "Not Installed" state by the SETUP program that is supplied with 
each ISA host computer. The SETUP program allows the user to select the number 
of standard hard disks that are recognized by the system regardless of whether 
or not they are physically installed. 


3.2.2 Hardware Setup 

Several preparatory steps must be taken to install the host adapter in the host 
computer. The initialization jumpers must be correctly placed in the AHA154XA. 
The SCSI Bus terminators must be installed in the correct SCSI devices. 
Finally, the correct SCSI addresses must be assigned to each peripheral device. 

The Adaptec AHA-1540A/1542A 16-Bit AT bus to SCSI bus Host Adapter has been 
designed to operate as shipped in the majority of AT class computers. The host 
adapter's jumper settings should almost always remain in their original default 
positions. Refer to section 3.3 if conflicting memory or port assignments 
require that the host adapter jumpers be reconfigured. The AHA-1540A/1542A is 
shipped with the following default settings: 

 SCSI Address-7   
 SCSI Parity-Enabled 
 Terminators-Installed 
 Terminator Power-Supplying 
 Synchronous Negotiation-Disabled
 DMA Channel-5 
 Interrupt Channel-11
 AT Port Address-330H
 AT BIOS Address-ODCOOOH
 LA Enable Jumper-Installed 

Termination 

The SCSI bus must be terminated correctly to assure proper operation. The first 
and last physical SCSI devices on the SCSI cable must have terminators 
installed. All other SCSI devices must have terminators removed. The host 
adapter is shipped with terminators already installed at locations RN3, RN4, 
and RN5.   The internal and external connectors connect to the same SCSI bus, 
so both internal and external cabling must be considered in determining where 
terminators are installed. 

If only one cable (either internal or external) is connected to the host 
adapter, the terminators must remain installed in the host adapter. Terminators 
must also be installed on the device at the farthest end of the cable from the 
host adapter. Terminators must be removed from all other attached SCSI devices. 

If both an internal and an external cable are connected to the host adapter, 
remove the terminators on the host adapter and install terminators on the 
devices at the farthest end of each cable. Terminators must be removed from all 
devices except the device at the end of each cable. The instruction manuals for 
each SCSI device will indicate how the terminators can be removed or replaced. 

Addressing 

The SCSI target address for each SCSI device to be attached must be selected by 
setting the proper jumpers or switches on the device. If the SCSI device is a 
hard disk that is to be used as the boot disk, it must have the Target 
Identifier (SCSI Address) set to zero and the Logical Unit Number set to zero. 
SCSI Addresses 0 and 1 should be reserved for SCSI hard disk drives.  SCSI 
Address 2 is often used for tape devices. Each installed peripheral must have a 
different Target Identifier. The host adapter's default address is 7. Duplicate 
SCSI Addresses will cause errors that are extremely difficult to identify. Any 
jumpers that control operating modes must also be properly set. If there is a 
jumper that enables synchronous transfer negotiation, the jumper should be set 
to enable negotiation. Check the SCSI drive or controller to ensure that Parity 
Checking is enabled. If Parity checking on the device is disabled or not 
supported, the jumper at location J8 of the host adapter should be removed. 
Parity checking should only be enabled if all SCSI devices support it. 


Installation Procedure 
  
Now that the host adapter and the devices to be installed have been properly 
prepared, the devices should be installed in the following manner: 

1) Turn OFF the power to the computer system. 
2) Remove the system cover according to the directions of the computer 
   manufacturer. 
3) If only an external SCSI subsystem is to be used, no internal cabling is 
required. If an internal SCSI peripheral is to be used, install a 50 pin SCSI 
ribbon cable to the host adapter. This cable must be oriented correctly. Pin 1 
of the SCSI cable is designated by a red stripe. Multi-color 50 pin ribbon 
cables signify pin 1 with a brown color. Pin 1 on the host adapter 50 pin SCSI 
header is located on the left hand side, farthest from the installation bracket 
and is designated by the words PIN 1 on the board adjacent to the header. After 
locating pin 1 on the host adapter and on the SCSI cable, carefully insert the 
connector located at the end of the long end of the cable into the host adapter 
connector. After ensuring that all pins are lined up and that the pin 1 
orientation is correct, firmly seat the connector to the board. If it is ever 
necessary to remove the cable, gentle prying with a small thin-bladed 
screwdriver may be required. 
4) After installing the SCSI cable, the host adapter can be installed in any 
one of the  adapter slots in the host computer. 
5) If an internal SCSI device is to be used, it should be installed in the 
drive bays in accordance with the directions on the peripheral.  The proper 
power supply must be connected to the SCSI peripheral device. 
6) The 50 pin SCSI ribbon cable can now be attached to each SCSI device. Refer 
to the device's installation instructions to ensure proper pin 1 orientation. 
Pin 1 orientation must be consistent throughout the system. Keep the ribbon 
cable neatly dressed away from the ventilation slots in the computer system. 
Keep the ribbon cable dressed away from possible electrical noise sources or 
noise sensitive components, particularly large microprocessors, memory boards, 
switching power supplies, and analog data acquisition boards. If the internal 
configuration requires the cable to come near noise sensitive circuits , make 
sure that the cable crosses the boards at right angles and is near the noise 
sensitive circuits for the shortest distance possible. 
7) Carefully reinstall the cover of the computer. 
8) If an external SCSI subsystem is to be installed, it can now be cabled to 
the External SCSI Connector projecting from the shielding bracket on the back 
of the AHA-154XA Host Adapter. The proper shielded SCSI cable must be used for 
proper operation. The external connector on the AHA-1540A/1542A is a D shell 
connector that ensures correct pin 1 orientation on the host adapter. The 
subsystem, cables, and SCSI terminators must be installed in accordance with 
the directions provided with the external SCSI subsystem. The addresses 
selected for external SCSI devices must not overlap with the addresses of the 
host adapter or any other SCSI devices attached internally. 

3.2.3 Checklist 

Before applying power to your system, the following items should be completed 
and checked: 

1. 50 pin SCSI ribbon cable is connected to the host adapter with proper pin 1 
orientation. 
2. The host adapter is firmly seated in the host computer's adapter 
slot. 
3. The correct SCSI addresses are selected on all attached SCSI devices. 
Address 0 is reserved for the boot hard disk and address 1 is used for a second 
hard disk. 
4. The correct operating modes are selected on all attached SCSI devices. 
5. Terminators are installed or removed on the drives and host adapter as 
required. 
6. External SCSI devices are properly installed and cabled. 


3.2.4 Operation Using the BIOS Under DOS 

To bring up the system for the first time with the host adapter installed, 
insert a bootable system diskette in drive A:, and close the door. After the 
system initialization and power-up diagnostics have completed, system error 
messages, such as "SYSTEM CONFIGURATION CHANGED, RUN SETUP" and prompts on how 
to continue, may be displayed. After following the instructions displayed on 
the screen, the system will boot from the flexible diskette drive. 

Run your SETUP program to configure the system as required. Remember that a 
SCSI drive can only be used as a boot device if both standard hard disks are 
mapped out. When the SETUP parameters have been defined, follow the directions 
on the screen to re-initialize the system. 

Most SCSI drives are shipped from the factory with a complete low-level format. 
A few SCSI drives and most bridge controllers, including the CCS compatible 
Adaptec ACB-4525Z, require a low-level SCSI format operation before they will 
operate. Section 7.4 describes how the low-level format utility that is 
available in the Adaptec BIOS Utilities should be used to format such SCSI 
devices. 

Run the DOS FDISK program to partition the disk for the number of cylinders to 
be used by DOS. When using DOS 3.2 or under, it is generally a good idea to 
select 1 less cylinder than the maximum allowable per partition according to 
DOS. This eliminates the possibility of exceeding the 32 MB limit. Activate the 
first DOS partition before leaving the FDISK program if it is to be the boot 
partition. If you are not sure if a DOS partition exists, use the menu entry in 
FDISK to display partition data. 

After the DOS partition has been created and activated, the drive is ready for 
a DOS FORMAT. Refer to the DOS manual for the format options that are 
available. If the system is going to boot from a SCSI disk, it is usually 
easiest to transfer the hidden system files to that disk during the FORMAT. 

CAUTION: If the drive you are using was previously formatted or partitioned 
with a different host adapter or disk controller, a DOS partition may already 
exist. If such a partition does exist it should be deleted and re-created using 
this host adapter. If this precaution is not followed, erratic system operation 
may result. 

The host adapter and SCSI disks are now ready for normal operation. The host 
adapter's BIOS performs the necessary initialization procedures during the boot 
operation. This procedure is described in section 6.1.1 

3.3 Jumper Configuration 

All of the jumpers have been preset at the factory to ensure proper system 
operation with the majority of AT bus systems. This  information is provided to 
help the OEM or system integrator to configure the system properly if other 
option boards present conflicts. 

The following diagram shows the approximate location of the various customer 
configurable items on the AHA-1540A/1542A. Listed after the diagram are the 
functions, defaults, and set-up options for each jumper. 

Jumper locations:ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄ
                 ³    j5    j4                       Ãscsi conn.´      ³
                 ÀÄÄ¿     Ãdiskette header´                            ÃÄÄ¿
                    ³                                 j6    j7         ³  ³
                    ³                                           j10    ³  ³
                    ³                                                  ³  ³
                    ³      j9                        j8   j12          ³  ³
                    ³          j11                           j18       ³  ³
                    ³ j13             j14j15 j16    j17      j19       ÃÄÄÙ
                    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿     ÚÄ¿          ÚÄÄÄÄÙ
                                               ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ
3.3.1  Jumper Block J1
Jumper block J1 is shown below: 
              ÚÄÄÄÄÄ¿
      pin 1Í  ³ 0 0 ³ Syncronous transfer
              ³ 0 0 ³ Diagnostics
              ³ 0 0 ³ SCSI parity                             
              ³ 0 0 ³ SCSI address
              ³ 0 0 ³ SCSI address
              ³ 0 0 ³ SCSI address
              ³ 0 0 ³ DMA channelÄÄÄÄÄÄÄÄÄÄÄÄ¿ j14 and j15 must also be set.
              ³ 0 0 ³ DMA channelÄÄÄÄÄÄÄÄÄÄÄÄÙ
              ³ 0 0 ³ Interrupt channelÄÄÄÄÄÄ¿
              ³ 0 0 ³ Interrupt channel      ÃÄÄj16 must also be set.
              ³ 0 0 ³ Interrupt channelÄÄÄÄÄÄÙ
              ³ 0 0 ³ DMA transfer speed
              ³ 0 0 ³ DMA transfer speed           x= jumper installed
              ÀÄÄÄÄÄÙ
Jumper block J1 is the large vertically oriented block of jumpers located near 
the center of the host adapter. Pin pair 1 is the topmost pair of pins. 

3.3.1.1 SCSI Synchronous Negotiation 

Pin-pair 1 of jumper block J1 is the synchronous negotiation enable jumper. The 
AHA-1540A/1542A will initiate SCSI synchronous negotiation during 
initialization, or after a SCSI reset if this jumper is installed. If the 
jumper is not installed, the AHA-1540A/1542A will still support synchronous 
SCSI transfers, but a different SCSI device must initiate the negotiation. 
Default is jumper removed, synchronous negotiation initiation disabled. If any 
attached SCSI devices support synchronous transfer, the initiation of 
negotiation should be enabled by both the AHA-154XA and the attached devices to 
fully implement the SCSI synchronous negotiation protocol. 

3.3.1.2 Diagnostic Jumper 

Pin-pair 2 of jumper block J1 is a factory diagnostic jumper. This jumper is 
reserved for Adaptec use and must not have a jumper shunt installed. If this 
jumper is installed, the firmware will loop through the power on diagnostics, 
preventing normal operation. Default is jumper removed. 

3.3.1.3 SCSI Parity 

Pin-pair 3 of jumper block J1 is the parity enable/disable jumper. The SCSI 
parity checking is disabled if this jumper is installed. The default is parity 
checking enabled. 

3.3.2 SCSI Address

Pin-pairs 4, 5, and 6 of jumper block J1 define the SCSI address. The SCSI 
address is selected according to the following table. The default address is 7. 
      J1      ÚÄÄÄÄÄ¿
      pin 1Í  ³ 0 0 ³                        pin pair  scsi
              ³ 0 0 ³                        4 5 6     address     
              ³ 0 0 ³                        0 0 0       7      default
   pin-pair 4 ³ 0 0 ³ SCSI addressÄ0         x 0 0       6
   pin-pair 5 ³ 0 0 ³ SCSI addressÄ1         0 x 0       5
   pin-pair 6 ³ 0 0 ³ SCSI addressÄ2         x x 0       4
              ³ 0 0 ³                        0 0 x       3
              ³ 0 0 ³                        x 0 x       2
              ³ 0 0 ³                        0 x x       1
              ³ 0 0 ³                        x x x       0
              ³ 0 0 ³ 
              ³ 0 0 ³ 
              ³ 0 0 ³ 
              ÀÄÄÄÄÄÙ    x=jumper installed
          
3.3.3 DMA Channel 

There are three jumper blocks involved in selecting the DMA channel. These are 
J1, J14, and J15. The DMA channel selection jumpers consist of pin pairs 7 and 
8 located in the large block of jumper pins J1. The DMA channel reported to the 
AT during the Return Configuration command is set by these jumpers according to 
the following table. Default is DMA channel 5. 

Jumper set J14 selects the DMA REQ signal to be used by the AHA-1540A/1542A 
according to the following table. This jumper set is located near the bottom 
center of the host adapter. Pin pair 1 is the right most pair of pins. The 
default is DMA Request 5. 

Jumper  set J15 selects the DMA ACK signal to be used by the AHA-1540A/1542A 
according to the following table. This jumper set is located near the bottom 
center of the host adapter. Pin pair 1 is the right most set of pins. The 
default is DMA Acknowledge 5. 	

There are four DMA channels that may be chosen for use by the AHA-1540A/AHA-
1542A, channels 0, 5, 6, and 7. The DMA channel is set up by using the three 
jumper blocks and pin-pairs previously described. The jumper settings for each 
channel are shown below:      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ÚÄÄÄÄÄ¿            ³j1 DMA channel jumpers ³
   pin 1Í  ³ 0 0 ³            ³pin-pair  DMA          ³
           ³ 0 0 ³            ³ 7 8      channel      ³
           ³ 0 0 ³            ³ 0 0        7          ³
           ³ 0 0 ³            ³ x 0        6          ³
           ³ 0 0 ³            ³ 0 x        5          ³
           ³ 0 0 ³            ³ x x        0          ³
pin-pair 7 ³ 0 0 ³ DMA channelÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
pin pair 8 ³ 0 0 ³ DMA channel  
           ³ 0 0 ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³ 0 0 ³ ³ j14-2                ³    ³ j15-2                ³
           ³ 0 0 ³ ³ 0 0 x 0ÄÄpin 1       ³    ³ 0 0 x 0ÄÄpin 1       ³
           ³ 0 0 ³ ³ 0 0 x 0              ³    ³ 0 0 x 0              ³
           ³ 0 0 ³ ³ ³ ³ ³ ÀÄÄÄchannel 0  ³    ³ ³ ³ ³ ÀÄÄÄchannel 0  ³
           ÀÄÄÄÄÄÙ ³ ³ ³ ÀÄÄÄÄÄchannel 5  ³    ³ ³ ³ ÀÄÄÄÄÄchannel 5  ³
                   ³ ³ ÀÄÄÄÄÄÄÄchannel 6  ³    ³ ³ ÀÄÄÄÄÄÄÄchannel 6  ³
x=jumper installed ³ ÀÄÄÄÄÄÄÄÄÄchannle 7  ³    ³ ÀÄÄÄÄÄÄÄÄÄchannle 7  ³
                   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
3.3.4 AT Interrupt Channel

There are two jumper blocks involved in selecting the AT interrupt channel. 
These are J1 and J16. The AT interrupt channel jumpers consist of pin pairs 9, 
10, and 11 in the large block of jumper pin pairs J1. The interrupt channel 
reported to the AT during the Return Configuration Command is set by these 
jumpers according to the following table. The default is interrupt channel 11. 

Jumper set J16 selects the AT interrupt channel to be used by the AHA-
1540A/1542A. This jumper set is located near the bottom center of the host 
adapter. Pin pair 1 is the right most pair of pins. The interrupt channel used 
is set according to the following table. The default interrupt channel is 11. 
                                     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   j1      ÚÄÄÄÄÄ¿                   ³ j1 interrupt channels ³
   pin 1Í  ³ 0 0 ³                   ³ pin-pair    interrupt ³
           ³ 0 0 ³                   ³ 9 10  11   channel    ³
           ³ 0 0 ³                   ³ 0  0   0       9      ³  
           ³ 0 0 ³                   ³ x  0   0       10     ³
           ³ 0 0 ³                   ³ 0  x   0       11     ³
           ³ 0 0 ³                   ³ x  x   0       12     ³
           ³ 0 0 ³                   ³ 0  0   x       14     ³
           ³ 0 0 ³                   ³ x  0   x       15     ³
pin-pair 9 ³ 0 0 ³ Interrupt channel ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
pin-pair 10³ 0 0 ³ Interrupt channel     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
pin pair 11³ 0 0 ³ Interrupt channel     ³ j16   3            ³
           ³ 0 0 ³                       ³ 0 0 0 x 0 0ÄÄpin 1 ³
           ³ 0 0 ³ x=jumper installed    ³ 0 0 0 x 0 0        ³
           ÀÄÄÄÄÄÙ                       ³ ³ ³ ³ ³ ³ ÀÄÄIRQ 9 ³
                                         ³ ³ ³ ³ ³ ÀÄÄÄÄIRQ 10³
                                         ³ ³ ³ ³ ÀÄÄÄÄÄÄIRQ 11³
                                         ³ ³ ³ ÀÄÄÄÄÄÄÄÄIRQ 12³  
                                         ³ ³ ÀÄÄÄÄÄÄÄÄÄÄIRQ 14³
                                         ³ ÀÄÄÄÄÄÄÄÄÄÄÄÄIRQ 15³
                                         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
3.3.5 DMA Transfer Speed Default

Pin-pairs 12 and 13 of jumper block J1 set the default DMA transfer speed. 
Installing jumper shunts as shown below will set any of 4  default DMA transfer 
speeds. (See Appendix A for system timing requirements.) The default speed is 
selected after power on or after a hard reset occurs. This speed may also be 
tuned to allow for the fastest possible transfer (minimum bus on time) for any 
particular system by using the Host Adapter command Set Transfer Speed. The 
Host Adapter Command overrides the jumper settings. This command is detailed in 
section 5. The default is no jumper installed. 
      J1      ÚÄÄÄÄÄ¿                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
      pin 1Í  ³ 0 0 ³                      ³ pin pair   DMA  ³ 
              ³ 0 0 ³                      ³ 12  13     Speed³    
              ³ 0 0 ³                      ³  0   0      5.0 ³ default
              ³ 0 0 ³                      ³  X   0      5.7 ³ 
              ³ 0 0 ³                      ³  0   X      6.7 ³ 
              ³ 0 0 ³                      ³  X   X      8.0 ³ 
              ³ 0 0 ³                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 
              ³ 0 0 ³                       
              ³ 0 0 ³                       
              ³ 0 0 ³                      
              ³ 0 0 ³ 
   pin-pair 12³ 0 0 ³DMA Transfer speed
   pin-pair 13³ 0 0 ³DMA Transfer speed 
              ÀÄÄÄÄÄÙ                        x=jumper installed

3.3.6 AT BIOS Wait State 

Jumper block J7 allows IOCHRDY on the AT bus to be driven not active during 
BIOS reads. The time may be set to 100ns, 200ns, 300ns, or the function may be 
disabled. The default is Wait State Disabled. 

                    ÚJ7ÄÄÄÄÄ¿
                    ³0 0 0 X³pin 1
                    ³0 0 0 X³
x=jumper installed  ÀÅÄÅÄÅ ÀÄÄÄÄÄdisable wait states          
                     ³ ³ ÀÄÄÄÄÄÄÄÄ100 ns
                     ³ ÀÄÄÄÄÄÄÄÄÄÄ200 ns
                     ÀÄÄÄÄÄÄÄÄÄÄÄÄ300 ns

3.3.7 AT Port Address

The starting address of the block of four I/O ports required by the AHA-
1540A/1542A is selected by the jumpers in jumper block J6. Pin pair 1 is the 
right most pair of pins. The default address is 0330H. That port address is 
required by the BIOS. Other valid port addresses are 334H, 330H, 234H, 230H, 
134H, and 130. These port addresses may be used by device drivers and operating 
systems that support multiple host adapters.  The default address is 330H. 
  ÚJ6ÄÄÄ¿                 AT Port Address
  ³0 0 X³pin 1            A9  A8  A2   ADRESS
  ³0 0 X³                  0   0   0    334H
  ÀÅÄÅ ÀÄÄÄA2              0   0   X    330H
   ³ ÀÄÄÄÄÄA8              0   X   0    234H
   ÀÄÄÄÄÄÄÄA9              0   X   X    230H
 x=jumper installed        X   0   0    134H
                           X   0   X    130H

3.3.8 AT BIOS Address 
     ÚÄÄÄÄÄ¿                  BIOS Address
 J10 ³ 0  0³                  Jumpers   BIOS 
     ³ 0  0³ÄÄPin 1            0   1    ADRESS
     ÀÄ³ÄÄ³Ù                   0   0    0DC000H  DEFAULT ADDRESS
       ³  ÀÄÄBIOS Address 0    X   0    0CC000H
       ÀÄÄÄÄÄÄBIOS Address 1   0   X    0D8000H
 x=jumper installed            X   X    OC8000H

The starting address of the block of address space reserved for the Adaptec 
BIOS is selected by the jumper pins located in J10. The default address is 
ODCOOOH. This address must not conflict with any other BIOS or decoded address 
space in the system. 

3.3.9 Front Panel LED Connector 

    J5 ÚÄÄÄÄÄÄÄÄÄÄÄ¿
       ³0  0  0  0 ³ÄPIN 1
       ÀÄÄÄÄÄÄÄÄÄÄÄÙ

J5 is the front panel LED header. Pins 1 and 4 are connected to the same 220 
ohm pull up resistor and pins 2 and 3 are pulled low by the same LED driver 
whenever the on board LED is on. This allows the Front Panel LED cable to be 
plugged in with either orientation. The driver is specified to pull 24 
milliamps through the LED. J5 is located near the top left of the host adapter. 

3.3.10 LA Enable Jumper (AHA-W1542A Only)

Note: This jumper exists only on the early production units. These are easily 
identified by a label on the board that has a model number of AHA-W1542A. 
Standard production AHA-1540A and AHA-1542A boards do not have this jumper. 

When J8 is installed, address drivers LA17 - LA19 are enabled. When not 
installed these address lines are not driven. Some computers, especially 80386 
based machines, short address lines LA17 and SA17, LA18 and SA18, and LA19 and 
SA19 together. If your computer system shorts these lines then remove jumper 
J8. Default is jumper installed. 

CAUTION:   Incorrect installation of this jumper may not result in immediate 
system problems. If it is necessary to change the state of this jumper after 
the system has been configured, the SCSI hard disk must also be re-formatted. 
Contact the computer system manufacturer if there is any doubt on how the 
system implements these address lines. 

3.3.11 Auxiliary Jumpers 

Installation of a jumper shunt on pin pair 4 of jumper block J9 will disable 
the automatic request sense function on the AHA-1540A/1542A. If the automatic 
Request Sense function is enabled, it may additionally be disabled on a command 
by command basis using the Request Sense Allocation Length Field of the CCB 
(see Section 5.3). All other pins-pairs on jumper block J9 are reserved for 
future use. 
       1        4
      ÚÄÄÄÄÄÄÄÄÄÄ¿
   J9 ³0  0  0  0³
      ³0  0  0  0³
      À³ÄÄ³ÄÄ³ÄÄ³Ù
       ³  ³  ³  ÀÄÄDISABLE AUTO SENSE
       ³  ³  ÀÄÄÄÄÄRESERVED
       ³  ÀÄÄÄÄÄÄÄÄRESERVED
       ÀÄÄÄÄÄÄÄÄÄÄÄRESERVED
3.3.12 BIOS Enable/Disable 

Only one host adapter BIOS should be enabled in any host system. That BIOS 
allows DOS to access up to two SCSI drives on the host adapter having a port 
address of 330H. Any other host adapters installed in the system must have 
their BIOS disabled.  In addition, certain operating systems may require that 
the BIOS be disabled. The enabling of the BIOS is controlled by jumper J11, 
near the bottom left of the host adapter. When the jumper is installed on J11 
the BIOS is enabled. When the jumper is removed, the BIOS is disabled and will 
not respond to host reads. The default is jumper installed. 

3.3.13 SCSI Terminators

RN3, RN4, and RN5 are the SCSI terminators. If the AHA-1540A/1542A is not the 
first or the last SCSI device in a string of SCSI devices, or if in-line 
terminators are used, then all of these resistor networks must be removed.  
More information is provided in section 3.2.2 about the proper use of the SCSI 
terminators. The default is terminators installed. 

3.3.14 SCSI Terminator Power 

Fuse F1 controls the terminator power. If another SCSI device is supplying 
terminator power, then F1 may optionally be removed. No more than 5 SCSI 
devices should be configured to supply terminator power to a single SCSI bus. 
The default is F1 installed with the AHA-1540A/1542A supplying terminator 
power. The terminator power is protected with a 1.5 amp fuse to prevent short 
circuits from burning SCSI cables. The terminator power is additionally 
protected from terminator power back-flow with a low voltage-drop diode so that 
the SCSI bus will continue to operate even if one or more SCSI host adapters is 
powered down. 

3.4 Flexible Diskette Controller Configuration Jumpers (AHA-1542A Only) 

3.4.1 Flexible Diskette Controller Secondary Address 

Jumper J12, located near the center right of the host adapter, controls the 
selection of the flexible diskette controller secondary address. When J12 is 
installed, the flexible diskette controller will respond to I/O addresses 370-
377. When not installed, the flexible diskette controller will respond to I/O 
addresses 3F0-3F7. The default is no jumper installed. 	

3.4.2 Flexible Diskette Controller Enable 	Jumper J13, located near the bottom 
left of the host adapter, enables or disables the flexible diskette controller. 
When this jumper is installed, the flexible diskette controller will respond to 
host reads and writes. When not installed, the flexible diskette controller 
will not respond to any signal. The default is jumper installed. 

3.4.3 Flexible Diskette Controller Interrupt Channel 
INTERRUPT CHANNEL 6
     ÚÄÄÄÄÄÄÄ¿                        ÚÄÄÄÄÄÄÄ¿                   
 J17 ³0  X  X³ÄPIN 1             J17  ³X  X  0³ÄPIN 1
     ÀÄÄÄÄÄÄÄÙ                        ÀÄÄÄÄÄÄÄÙ
     
Jumper block J17, located near the bottom right of the host adapter, sets the 
interrupt channel for the flexible diskette controller. The default is 
interrupt channel 6. 

3.4.4 Flexible Diskette Controller DMA Request Channel
DMA REQ CHANNEL 2                DMA REQ CHANNEL 3
     ÚÄÄÄÄÄÄÄ¿                        ÚÄÄÄÄÄÄÄ¿                   
 J18 ³0  X  X³ÄPIN 1             J17  ³X  X  0³ÄPIN 1
     ÀÄÄÄÄÄÄÄÙ                        ÀÄÄÄÄÄÄÄÙ

Jumper J18, located near the bottom right of the host adapter, selects the DMA 
Request channel for the flexible diskette controller. Jumper J19, the DMA 
Acknowledge jumper, must be set to the same position. Default is DMA channel 2. 

3.4.5 Flexible Diskette Controller DMA Acknowledge Channel 
DMA ACK CHANNEL 2                DMA ACK CHANNEL 3
     ÚÄÄÄÄÄÄÄ¿                        ÚÄÄÄÄÄÄÄ¿                   
 J19 ³0  X  X³ÄPIN 1             J19  ³X  X  0³ÄPIN 1
     ÀÄÄÄÄÄÄÄÙ                        ÀÄÄÄÄÄÄÄÙ

Jumper J19, located near the bottom right of the host adapter, selects the DMA 
acknowledge channel for the flexible diskette controller. Jumper J18, the DMA 
Request jumper, must be set to the same position. Default is DMA channel 2. 

4.0 HARDWARE FUNCTIONAL DESCRIPTION 

4.1 HARDWARE OVERVIEW 

This section provides a description of the AHA-1540A/1542A hardware functional 
interface to the PC/AT host software. 

The hardware consists of a custom SCSI protocol chip, the AIC-6250, a FIFO 
buffer, a set of I/O ports, and a controlling microprocessor. 

The DMA control logic on the host adapter controls the AT bus arbitration and 
data transfer hand shaking. During DMA data transfers, the AHA-1540A/1542A 
becomes a bus master. The DMA logic supports both odd and even starting 
addresses. For odd starting addresses, the first transfer will be an 8-bit 
transfer. Thereafter, 16 bit transfers will be used to complete the data 
transfer. Odd-byte transfers, and the the last transfer of an even number of 
bytes to an odd address are treated in a similar manner. 

The SCSI port is controlled by the AIC-6250, an Adaptec SCSI protocol device 
which supports arbitration, selection, and reselection with a minimum of 
processor intervention. This VSLI device also supports target mode and 
synchronous SCSI transfers. 


4.2 I/O PORT INTERFACE 

The I/O port interface consists of three address locations. These three port 
addresses are decoded in the AT I/O address space. They form the primary 
communications channel between the host and the host adapter. The I/O ports are 
8 bits wide. The base port is for control and status, the second port for 
command and data transfer, and the third port for interrupt flags. 

I/O PORT INTERFACE BIT DEFINITION 


PORT ADDRESS = BASE + 0 

WRITE:  Control Register        READ:   Status Register 

Bit 7 Hard Reset (HRST)         Bit 7 Self Test in Progress (STST) 
Bit 6 Soft Reset (SRST)         Bit 6 Internal Diagnostic Failure (DIAGF) 
Bit 5 Interrupt Reset (IRST)    Bit 5 Mailbox Initialization Required (INIT)
Bit 4 SCSI Bus Reset (SCRST)    Bit 4 SCSI Host Adapter Idle (IDLE)
Bit 3 Reserved  (0)             Bit 3 Command/Data Out Port Full(CDF)
Bit 2 Reserved  (0)             Bit 2 Data In Port Full (DF)
Bit 1 Reserved  (0)             Bit 1 Reserved ( Undefined )
Bit 0 Reserved  (0)             Bit 0 Invalid H A  Command (INVDCMD) 

PORT ADDRESS = BASE + 1

WRITE:  Command / Data Out       READ:  Data In 
Bit 7 Command/Data Out Bit 7     Bit 7 Data In Bit 7 
Bit 6           "      Bit 6     Bit 6     "   Bit 6
Bit 5           "      Bit 5     Bit 5     "   Bit 5
Bit 4           "      Bit 4     Bit 4     "   Bit 4
Bit 3           "      Bit 3     Bit 3     "   Bit 3
Bit 2           "      Bit 2     Bit 2     "   Bit 2
Bit 1           "      Bit 1     Bit 1     "   Bit 1
Bit 0           "      Bit 0     Bit 0     "   Bit 0 

PORT ADDRESS = BASE + 2 

WRITE:  Reserved, do not write			READ:	Interrupt Flags 

Bit 7                            Bit 7 Any Interrupt 
Bit 6                            Bit 6 Reserved 
Bit 5                            Bit 5 Reserved
Bit 4                            Bit 4 Reserved
Bit 3                            Bit 3 SCSI Reset Detected (SCRD)
Bit 2                            Bit 2 HA Command Complete (HACC)
Bit 1                            Bit 1 MBO Empty (MBOA)
Bit 0                            Bit 0 MBI Full (MBIF) 


4.2.1 Control and Status Port 

Writing a one to the bits of the Control Port initiates certain special host 
adapter operations.   There is no requirement to return the bits to the zero 
state, since they are reset automatically after the requested operation is 
initiated. Read operations to the Status port address return host adapter 
status information. 

Base+0 Port, Write:  Host Adapter Control Port. 

Bit 7-Hard Reset  (HRST): The setting of the Hard Reset bit to one forces the 
host adapter into a state identical to a normal power on state. Diagnostic 
functions are executed and all status for ongoing SCSI operations is lost. A 
Reset Condition is generated on the SCSI bus. While the reset is being 
processed, the Self Testing in Progress bit (Host Adapter Status Port bit 7) is 
set. When the reset is complete, that bit is reset and the Mailbox 
Initialization Required bit (Host Adapter Status Port bit 5) and the SCSI Host 
Adapter Idle bit (Host Adapter Status Port bit 4) are set, indicating that the 
AHA-154XA mailbox structure must be re-initialized and that no other operations 
are active on the host adapter. See section 4.3, describing the overall reset 
structure. 

Bit 6-Soft Reset (SRST): The Soft Reset bit clears all ongoing SCSI and host 
adapter commands. All Command Control Blocks are abandoned and all queued 
commands are abandoned. Mailbox In and Mailbox Out entries must be cleared by 
the host. No diagnostic functions are executed. No Reset Condition is generated 
on the SCSI bus.  The Mailbox Initialization Required bit (Host Adapter Status 
Port bit 5) and the SCSI Host Adapter Idle bit (Host Adapter Status Port bit 4) 
are set when the reset processing is completed. This indicates that the AHA-
154XA Mailbox structure must be re-initialized and that no other operations are 
active on the Host Adapter. See section 4.3, describing the overall reset 
structure. 

Bit 5-Interrupt Reset (IRST): The setting of this bit clears the interrupt port 
of all bits that have been set and resets the interrupt line. The host adapter 
manages the interrupt presentation to minimize the possibility of incorrectly 
resetting an interrupt. MBOE and MBIF interrupts are presented immediately 
unless an SCRD or HACC interrupt has not yet been cleared. An SCRD or HACC will 
only be presented after any interrupt bit has been cleared and DF is zero, 
indicating an operation is fully completed. The prompt resetting of MBOE and 
MBIF interrupts minimizes the chance of a reset of one also resetting the 
other. Host programs should, however, be aware that there is a small chance of 
falsely resetting a new MBIF reset while clearing an MBOE interrupt. This can 
be resolved by periodically scanning the MBI entries when activity is expected 
on the host adapter or by not enabling the MBOE interrupt. 

Bit 4-SCSI Bus Reset (SCRST):The setting of this bit causes a SCSI Bus Reset to 
be generated on the SCSI bus. The SCSI Bus Reset is triggered at the time the 
SCRST bit is set to one and raises the RST line on the SCSI Bus for the 
architected 25 microsecond period. The reset is managed as a SCSI Soft Reset 
and will allow partially completed operations to continue after the reset 
occurs. See section 4.3, describing the overall reset structure. 

Bits 0-3 -Reserved: Reserved bits must be set to zero to avoid compatibility 
problems with future extensions of the Control Register. 


Base+0 Port, Read: Host Adapter Status Port 

Bit 7-Self Testing in progress (STST): This bit, when one, indicates that the 
host adapter is performing self-initialization and internal diagnostics. The 
bit is asserted after a power-on or hard reset (Control Port Bit 7 HRST = 1). 
When diagnostic operation is complete,  the STST bit is set to zero and bit 5 
or bit 6 is set to indicate the successful or unsuccessful completion of the 
diagnostics. If bit 7 remains on, it indicates that the initialization or 
diagnostic could not be completed. The error condition can be determined as 
described in section 10. In most cases, bit 6 (DIAGF) will be set to indicate 
that an internal diagnostic failure occurred. 

Bit 6-Internal Diagnostic Failure (DIAGF): This bit, when one, indicates that 
the self-testing process has completed and that an error was detected. The host 
adapter must be reset by setting the Hard Reset bit (bit 7 of the Control Port) 
to clear the error. If the AHA-154XA again detects an error, troubleshooting 
procedures must be performed to identify and correct the error condition. The 
diagnostic LED will usually present a flash code that indicates the nature of 
the failure. Section 10 describes the corrective procedures. 

Bit 5-Mailbox Initialization Required (INIT):This bit, when one, indicates that 
the self-testing process has completed successfully and that the AHA-154XA is 
ready for mailbox initialization to be performed. The base memory address of 
the Mailbox area must be established by execution of the Mailbox Initialization 
command. After execution of the Mailbox Initialization command and any other 
desired initialization operations, the AHA-154XA is ready for full operation. 

Bit 4-SCSI Host Adapter Idle (IDLE):This bit, when one, indicates that the host 
adapter is in the idle state. The host adapter has no outstanding Adapter 
Commands or SCSI commands. The host processor must wait for the idle state 
before executing any Adapter Command except the Start SCSI (02) and Enable 
Mailbox Out Interrupt (05) commands. 

Bit 3-Command / Data Out Port Full (CDF): The host uses the CDF bit to 
synchronize command and data transfers to the host adapter. An Adapter Command 
byte or an outbound parameter byte can be placed in the Command / Data Out Port 
when the port is empty, indicated by the CDF bit being zero. When a byte is 
placed in the Command / Data Out Port, the CDF bit is set to one and remains 
one until the host adapter has obtained and processed the byte. When the CDF 
bit returns to zero, the next Command or parameter byte can be placed in the 
port. 

Bit 2-Data In Port Full (DF): The host uses the DF bit to synchronize transfers 
of data from the host adapter to the host. When the DF bit is set to one, the 
host adapter has placed a byte in the Data In Port for the host to remove and 
process. When the host performs a read to the Data In Port address, the DF bit 
is set back to zero automatically and not set to one again until a new data 
byte has been placed in the Data In Port by the host adapter for the host. 

Bit 1-Reserved: This bit is zero. 

Bit 0-Invalid Host Adapter Command (INVDCMD): The Invalid Host Adapter Command 
bit is set to one if an invalid command or parameter byte was received in the 
Command / Data Out Port . After sending a command byte or data byte, the host 
software determines that the next byte is ready to send by waiting for the CDF 
bit to be reset.  If the command byte or parameter byte is not valid, the 
command sequence will instead be terminated by the host adapter. The host 
adapter always terminates a command by raising the Host Adapter Command 
Complete (HACC) interrupt. If the HACC interrupt is set to one and the INVDCMD 
bit is not  set, the command terminated normally. If the INVDCMD bit is also 
set to one, the command or parameter bytes were determined to be invalid and 
the command terminated abnormally. The INVDCMD bit is only valid from the time 
the HACC interrupt is set until the HACC interrupt  is reset. The bit's value 
is not predictable until a new HACC interrupt is set for a new Adapter Command. 

4.2.2 Command/Data Out and Data  In Port 

The second I/O port address is used by the host to write Adapter Command bytes 
and accompanying parameter data bytes to the host adapter. It is also used by 
the host adapter to send parameters back to the host to be read. The Command / 
Data Out Port is used by the host to send host adapter initialization and 
management commands and parameters that cannot be sent by the standard Mailbox 
protocol. Information requested by the Adapter Commands placed in the Command / 
Data Out Port is returned through the Data In Port. The host should understand 
the format and number of bytes to be transmitted for each command so that extra 
invalid bytes are not passed across the interface.  Bytes in addition to those 
required by the particular command are likely to be interpreted as invalid, 
although they may instead cause the execution of valid commands that were not 
supposed to be performed. 

The host should only write to the Command / Data Out Port when CDF is zero. 
This allows time for the host adapter to process a previously written command 
or parameter byte. CDF is automatically set to one when the host writes to the 
port and is reset to zero after the host adapter removes the byte from the 
port. 

If an Adapter Command needs additional data bytes, the host waits until CDF is 
zero before writing the additional bytes to the Command / Data Out Port. Just 
as in the command transfer case, each parameter byte written will set the CDF. 
The host can write additional data bytes only after CDF is again zero. The HACC 
interrupt will indicate when the command has terminated, normally or 
abnormally. If INVDCMD is also set, the host adapter found either the command 
or data bytes to be invalid and terminated abnormally. The use of CDF as a 
hand-shaking bit is required to prevent the transfer of invalid data. 

If an Adapter Command requires data transfer from the host adapter, the host 
adapter will place the data bytes in the Data In Port and set the DF bit 
(Status Port bit 2) to indicate that the requested parameter is ready for the 
host to read. When the host reads the Data port, DF is automatically reset. The 
host should wait until DF is again set before attempting to transfer the next 
parameter byte. The use of the DF bit to control the hand-shaking process is 
required to prevent the transfer of invalid data. After the last data byte has 
been transferred, the HACC interrupt bit will be set indicating command 
completion. If the Adapter Command was invalid, the HACC interrupt will occur 
before all data bytes have been transmitted and the INVDCMD bit will be set. 

4.2.3 Interrupt Flag Port 

The Interrupt Flag Port contains bits that indicate the reason that an 
interrupt was provided to the host from the host adapter. The host adapter uses 
the interrupt to notify the host that the host adapter is ready for immediate 
service from the host. The Interrupt Flag Port is a read-only port. When an 
interrupt bit is set by the host adapter to indicate that the host should 
respond, the Any Interrupt bit and the interrupt line are both also set. When 
the host begins to examine the returned registers and mailboxes to determine 
the cause of the interrupt and to perform the operations needed to service the 
interrupt, the host will first read the Interrupt Flag Port to record which 
interrupts must be serviced. The host will then clear the interrupts by setting 
the IRST bit (Host Adapter Control Port bit 5). The host adapter presents MBOA 
and MBIF interrupts immediately unless there is already an SCRD or HACC 
interrupt present. If the SCRD or HACC is present, the MBOA and/or MBIF 
interrupt will be posted after the SCRD or HACC interrupt is cleared. An SCRD 
or HACC interrupt will only be presented if the Any Interrupt signal is zero 
and the DF signal is zero, indicating the completion of all pending interrupt 
presentation. It is recommended that the MBOA interrupt be enabled only when 
required by the host. This prevents the possible presentation and resetting of 
MBIF interrupts before they are processed. Other reset operations will also 
reset the Interrupt Flag Port and the interrupt line, including the Hard Reset 
bit (HRST), the Soft Reset bit (SRST), and the power on reset issued by the 
motherboard. 

Base+2 Port, Read only: Interrupt Flag Port 

Bit 7-Any Interrupt: This bit, when one, indicates that  the interrupt to the 
host has been established. The actual identify of the interrupting condition is 
provided in bits 0 to 3. 

Bit 6-Reserved: Returned as zero. 

Bit 5-Reserved: Returned as zero. 

Bit 4-Reserved: Returned as zero. 

Bit 3-SCSI Reset Detected (SCRD): This bit, when one, indicates that a SCSI 
Reset has been received on the SCSI bus. The Any Interrupt bit and the AT 
interrupt signal will also be set. The host adapter supports SCSI Soft Reset 
(see section 4.3). Any ongoing target or initiator activities will continue 
normally after first clearing the SCSI bus. In some rare cases, host 
intervention will be required to restart a SCSI command that was aborted by the 
reset operation. The host can convert the SCSI Soft Reset to a SCSI Hard Reset 
by setting the Control Register Soft Reset (Bit 6) to one, clearing all ongoing 
operations in the host adapter. In this case, the host must recognize that any 
operations not yet completed will never be completed and must perform 
appropriate error recovery operations. See section 4.3, describing the overall 
reset protocol. The SCRD bit is not set for host initiated SCSI Reset 
conditions caused by the setting of the HRST bit  or the SCRST bit, since the 
host is already aware of the actions it has requested. If the Any Interrupt 
signal or DF signal is present, the SCRD interrupt will not be presented until 
the interrupts already present are cleared. 

Bit 2-Host Adapter Command Complete (HACC): This bit, when one, indicates that 
an Adapter command has been completed, normally or abnormally. The Any 
Interrupt bit and the AT interrupt signal will also be set. If the command was 
completed normally, only the HACC bit will be on. If the command was completed 
abnormally or was aborted before it was completed, the HACC bit will be one and 
the Invalid Command Bit (Status Register bit 5) will also be one. During 
parameter transfers to or from the host adapter, the HACC bit should be 
examined to verify  that  the command is still being processed and has not been 
ended abnormally. If the Any Interrupt signal or DF signal is set, the HACC 
interrupt will not be presented until the interrupts already presented are 
cleared. 

Bit 1-Mailbox Out Available (MBOA): This bit, when one, indicates that an 
outbound Mailbox entry is now available for use by the host. The Any Interrupt 
bit and the AT interrupt signal will also be set. Most operating systems will 
choose to leave this interrupt disabled to avoid the generation of extra 
interrupts. The host adapter will normally empty Mailbox Out entries to its 
local RAM so rapidly that round robin filling of the Mailbox Out entries will 
assure that a Mailbox Out entry will already be empty by the time that the host 
is ready to fill it again. 

If the host finds that all Mailbox Out entries are full, it can enable the 
Mailbox Out Available interrupt by executing an Enable Mailbox Out Interrupt 
command through the I/O Command Port. The Enable Mailbox Out Interrupt command 
is one of the two commands that can be executed without waiting for the IDLE 
state of the host adapter. As soon as any Mailbox Out entry is cleared by the 
host adapter, an MBOA interrupt will be generated to indicate to the host that 
an MBO entry is available. An MBOA interrupt is generated after that each time 
a Mailbox Out entry is cleared by the host adapter until an Enable Mailbox Out 
Interrupt command is executed to force the reporting of MBOA interrupts to be 
disabled. If the SCRD or HACC interrupts are present, the MBOA interrupt is not 
presented until they are cleared. At all other times, MBOA is presented 
immediately. 

Bit 0-Mailbox In Full (MBIF): This bit, when one, indicates that an entry has 
been placed by the host adapter in the Mailbox In.  The interrupt should be 
reset as soon as possible so that any subsequent interrupts can be detected. 
The host adapter may return information in other Mailbox In entries, so the 
host should check the next entry to determine if more than one set of 
information has been provided. The MBI entries are filled in round-robin order, 
so the host should simply check the next MBI entry after the last one that was 
found when a new MBIF interrupt occurs. 

If an MBIF interrupt is set and other Mailbox In entries are made before the 
interrupt is cleared, then all the entries can be scanned as found. The new 
MBIF interrupt will be presented if the SCRD and HACC interrupts are cleared. A 
new MBIF interrupt will be presented regardless of the state of the MBOA 
interrupt bit. It is important to clear and record each interrupt as soon as 
possible to avoid the possible accidental resetting of a valid interrupt. In 
addition, it is desirable to enable the MBOA interrupt as rarely as possible. 
The host system software must be ready to scan for MBI entries even if no MBIF 
interrupt occurred. 


4.3 RESET OVERVIEW 

The reset functions provided by the AHA-154XA are extensive to allow the 
fullest flexibility and architectural consistency, both with SCSI and with the 
Industry Standard Architecture. 

4.3.1 Hard Reset Operations 

Resets may be generated by the hardware through two mechanisms. The RESET 
signal from the ISA socket is generated by the system board to reset or 
initialize all installed adapters upon power on or during a low line voltage 
condition. The system can also activate this signal under host program control. 
In addition to the RESET signal, the setting of the HRST bit (bit 7 of the Host 
Adapter Control Port) will force a hardware reset to the AHA-154XA. Regardless 
of the source, a Hard Reset forces the following actions on the AHA-154XA. 

	All  internal registers of the AHA-154XA are returned to their reset 
condition. 
	The host adapter's microprocessor returns all internal information 
and parameters to their initial state. 
	The host adapter performs all required internal diagnostics. 
	A standard SCSI Reset condition is generated to all other attached SCSI 
devices. 

During the Hard Reset process, the AHA-154XA will indicate to the attached host 
that self-testing is in process by raising the STST bit in the Host Adapter 
Status Port. After the Hard Reset process is complete, the AHA-154XA will 
indicate that initialization parameters are required from the host by raising 
the INIT bit in the Host Adapter Status Port. 

4.3.2 SCSI Reset Operations 

The SCSI Reset condition is defined in the SCSI Standard, X3.131-1986, section 
5.2.2. A SCSI Reset condition may be forced by any SCSI device on the bus. The 
condition is forced by the assertion of the SCSI Reset signal. 

The AHA-154XA has four mechanisms which may force a SCSI Reset condition. The 
SCSI Reset condition may be invoked from the host software if the software sets 
the SCRST bit (Bit 4 of the Host Adapter Control Port). In this case, the 
normal SCSI Reset operations will be performed by the Host Adapter and the SCSI 
Reset signal will be asserted on the SCSI bus. In this case, the SCRD bit 
(Interrupt Flag Port bit 3) will not be set, since the host itself caused the 
reset. 

The SCSI Reset is invoked if a hard reset is generated, either by the system 
board RESET signal or by the setting of the HRST bit. This reset is described 
in Section 4.3.1. 

The SCSI Reset condition may be invoked by the AHA-154XA as part of the 
recovery mechanism for a bus phase error. Bus phase errors may include 
detection of an invalid information transfer phase or detection of an 
impossible phase sequence (Command Phase after a Data Phase in the same 
command). In this case, the normal SCSI Reset operations will be performed and 
the SCSI Reset signal will be asserted on the SCSI bus. In addition,  the SCRD 
bit (Interrupt Flag Port bit 3) will be set to indicate to the host computer 
that a SCSI Reset condition occurred. The setting of the SCRD bit also causes 
the Any Interrupt bit (Interrupt Flag Port bit 7) and the appropriate interrupt 
signal  to be presented. 

The SCSI Reset condition may be invoked by another SCSI device attached to the 
AHA-154XA as part of the other device's recovery mechanism or initialization 
procedure. In this case, the normal SCSI Reset operations will be performed. In 
addition,  the SCRD bit (Interrupt Flag Port bit 3) will be set to indicate to 
the host computer that a SCSI Reset condition occurred. The setting of the SCRD 
bit also causes the Any Interrupt bit (Interrupt Flag Port bit 7) and the 
appropriate ISA interrupt  signal to be presented. 


4.3.2.1 SCSI "Soft" Reset Option 

The SCSI standard indicates two optional methods of handling the normal SCSI 
Reset operations. The AHA-154XA implements the "Soft" Reset Option, described 
in section 5.2.2.2 of the SCSI specification. The "Soft" Reset Option is 
designed to allow a SCSI Reset signal to correctly clear the SCSI bus, but to 
allow ongoing system operations to continue without any major interruptions. 
When the SCSI Reset occurs, any activity on the SCSI bus is immediately halted 
and all bus lines are cleared from the bus. After the Reset condition ends, any 
operations in progress are again allowed to start up in the normal manner. No 
status or pointer information is destroyed. All disconnected commands are 
allowed to reselect and continue in the normal manner. This "Soft" Reset 
function allows a multiple initiator system to use reset to clear certain types 
of bus failures without damaging ongoing tasks from any initiator. 

The SCSI "Soft" Reset option is useful in multitasking systems that cannot 
tolerate the overhead of a complex reconfiguration and reinitialization after a 
normal reset operation. For the SCSI "Soft" Reset option to operate correctly, 
all SCSI devices that communicate on the SCSI bus must support the "Soft" Reset 
option. If any SCSI devices support the "Hard" Reset option, it is likely that 
operations will be terminated without warning and the system will have to time 
out and monitor the requirement to restart some activities. 


4.3.2.2 SCSI "Hard" Reset Option

The "Hard" Reset Option is designed to restore all attached SCSI devices, 
including both hosts and peripheral devices, to their power on reset state. All 
system activities that have not been recorded on a non-volatile memory device 
or through another SCSI path are completely lost and must be restarted. The 
system must be completely re-initialized. For certain types of systems that 
frequently do back-up or check point their transactions, that re-initialize 
quickly and easily, or that infrequently do resets, the "Hard" Reset Option is 
appropriate. The AHA-154XA responds to a SCSI Reset Condition by executing only 
the "Soft" Reset Option, but it notifies the host whenever a SCSI Reset 
condition has been established by causing an interrupt to the host. The host 
then has the option of converting the "Soft" Reset to a "Hard" Reset by forcing 
the host adapter to clear all the ongoing operations and return to its initial 
state. The host requests this by raising the SRST bit (bit 6 of the Host 
Adapter Control Port). The host must raise the SRST bit within 300 microseconds 
to disable the restarting of operations according to the rules of "Soft" Reset. 
The raising of the SRST bit causes the host adapter to abandon all CCB's and 
prepare itself to begin accepting new instructions from the host. No secondary 
SCSI Reset signals are activated. The Mailbox initialization and all normal 
SCSI initial conditions are reset by the SRST bit, so that reinitialization is 
required to restart the system. Of course the system still has the right at any 
time that the IDLE bit (bit 4 of the Host Adapter Status Port) is on to execute 
any of the Adapter Commands and modify the Mailbox Address or the SCSI initial 
conditions. 

If the host requires that the SCSI be reset according to the SCSI "Hard" Reset 
option, the host raises the HRST bit. The host adapter will then set a SCSI 
Reset Condition on the SCSI Bus and clear all its CCB and status information, 
thus performing a SCSI "Hard" Reset with a single load to the Host Adapter 
Control Port. Reinitialization will be required. 


5.1 HOST ADAPTER COMMAND OVERVIEW 

The AHA-1540A/1542A supports two types of commands: SCSI and Adapter Commands. 
SCSI commands are issued using the mail box protocol and a Command Control 
Block. When SCSI commands are used, the AHA-1540A/1542A is operating in true 
multithreading mode. In this mode of operation, the AHA-1540A/1542A is capable 
of executing multiple commands for multiple targets concurrently. The AHA-
1540A/1542A maximizes the I/O transaction throughput by managing SCSI 
disconnection and reconnection. 

Adapter Commands are issued by writing to the Command / Data Out port. Most 
Adapter commands can not be issued when there are outstanding SCSI commands. 
Adapter commands are used to initialize the host adapter and to establish 
control conditions within the host adapter. Adapter commands are also used to 
transmit the special parameters for communication between the BIOS and the host 
adapter for the execution interrupt 13 operations. 


5.1.1 Adapter Command Operation Codes 

Below is a list of the Adapter Command operation codes. 

00 -- No Operation
01 -- Mailbox Initialization
02 -- Start SCSI Command *
03 -- Start PC/AT BIOS Command 
04 -- Adapter Inquiry
05 -- Enable Mailbox Out Available Interrupt*
06 -- Set Selection Time-out
07 -- Set Bus-On Time
08 -- Set Bus-Off Time
09 -- Set Transfer Speed
0A -- Return Installed Devices
0B -- Return Configuration Data
0C -- Enable Target Mode **
0D -- Return Setup Data **
1A -- Write Adapter Channel 2 Buffer **
1B -- Read Adapter Channel 2 Buffer **
1C -- Write Adapter FIFO Buffer
1D -- Read Adapter FIFO Buffer
1F -- ECHO Command Data 

*Note: This command can be issued when the host adapter is executing a SCSI 
command. 
** These commands are not supported by the AHA-1540. 


All Adapter Commands except Start SCSI (02) and Enable Mailbox-Out Available 
Interrupt (05) must be executed only when the IDLE bit (Status bit 4) is one. 
Many commands require additional parameter bytes which are then written to the 
Command / Data Out I/O port (base + 1). Before each byte is written by the host 
to the host adapter, the host must verify that the CDF bit (Status bit 3) is 
zero, indicating that the command port is ready for another byte of 
information. The host adapter usually clears the Command / Data Out Port within 
100 microseconds. Some commands require information bytes to be returned from 
the host adapter to the host. In this case, the host monitors the DF bit 
(Status bit 2) to determine when the host adapter has placed a byte in the Data 
In I/O port for the host to read. The DF bit is reset automatically when the 
host reads the byte. The format of each Adapter Command is strictly defined, so 
the host adapter and host system can always agree upon the correct number of 
parameter bytes to be transferred during a command. 

All  Adapter Commands except Return Installed devices, Start SCSI, and Start 
PC/AT BIOS typically require less than 200µs to complete. Return installed 
devices will typically complete in less than 3 seconds. Start SCSI and Start 
PC/AT commands completion times will vary with the SCSI device and the command 
issued. 


5.1.1.1 No Operation  (Operation Code 00) 

No host adapter action is taken, but HACC is set indicating command completion. 
No additional information bytes are exchanged. 


5.1.1.2 Mailbox Initialization (Operation Code 01) 

This command is used to specify the number of mailbox locations used by the 
host adapter and to specify the base memory location of the mailbox area. The 
host adapter requires that four bytes of outbound data  follow the command 
byte. The definition of those four bytes is shown below. 

00  Mailbox count  (>0)
01  Mailbox address (MSB)
02  Mailbox address 
03  Mailbox address (LSB) 

Byte 0 Mailbox Count: The Mailbox count must be greater than zero. 

Byte 1,2,3 Mailbox Address: The Mailbox address specifies the location of the
                             first byte of the Mailbox area. Byte 1 is the most
                             significant byte. 


When the Mailbox Initialization command and parameters are received,  the host 
adapter will then assume that the specified number of Mailbox Out entries and 
the same number of Mailbox In entries will be assigned beginning at the Mailbox 
address. The total number of bytes reserved for the Mailbox area will be eight 
times the Mailbox count. If the Mailbox Count is zero, the INVDCMD bit will be 
set with HACC to indicate that the parameter is invalid. 	

At command completion, HACC will be set to one and INIT will be reset to zero. 
HACC will be reset as specified by section 4.2.3. 

5.1.1.3 Start SCSI Command (Operation Code 02)

This command indicates that the host has made at least one Mailbox Out entry 
and that the host adapter should begin to scan for active MBO entries. Once 
scanning has been started, it continues until all MBO entries have been 
serviced, either by beginning the requested operations or by queueing the 
activities for later execution.  Since it is not easy for the host to determine 
that scanning is still taking place, the host should normally issue this 
command every time a Mailbox Out is filled. This command does not require 
additional data bytes. To avoid unnecessary interrupts, HACC is NOT set after 
command completion. HACC will be set with INVDCMD if the mailbox was not yet 
initialized. 


5.1.1.4 Start PC/AT BIOS Command (Operation Code 03) 

This command is used by the Adaptec BIOS to communicate with the host adapter 
firmware. The command is not available for use by programs other than the 
Adaptec BIOS. 


5.1.1.5 Adapter Inquiry (Operation Code 04) 

After receiving this command, the host adapter returns four bytes of data 
describing the host adapter firmware revision level. After completing the 
transfer of the four bytes of inbound data, the HACC interrupt is set 
indicating normal command completion. The bytes contain the following 
information: 

00  Board Identification 
01  Special Options Identification
02  Hardware Revision Level
03  Firmware Revision (ASCII) 

Byte 0 Board ID: The value in this byte allows software supported on both the 
                 PC/AT and on the Microchannel(tm) to distinguish the type of
                 supporting host adapter. 
Value             Meaning
00H- board is an AHA-1540 with 16 Head BIOS
30H- ('0' ASCII) Board is an AHA-1540 with 64 Head BIOS
41H- ('A' ASCII) Board is an AHA-1540A/1542A, 64 Head BIOS
42H- ('B' ASCII)	Board is an AHA-1640, 64 Head BIOS
All Others- Reserved 

Byte 1  Special Options ID: The value in this byte indicates what special
                            options are supported on the AHA-154XA host 
                            adapter. Other host adapters use other values in 
                            this byte. 

Value              Meaning 
41H- ('A' ASCII)	Board is standard model
All Others- Reserved 

Byte 2 Firmware Revision: This value indicates an ASCII value from 0-9,A-Z that
                          indicates the firmware revision installed in the AHA-
                          154XA.

Byte 3 Firmware Revision: This value indicates an ASCII value from 0-9,A-Z that
                          indicates the firmware revision installed in the AHA-
                          154XA. 

After completing this command, HACC will be asserted, indicating normal 
completion. 


5.1.1.6 Enable Mailbox-Out Available Interrupt (Operation Code 05) 

The Enable Mailbox Out Available Interrupt command specifies that a Mailbox Out 
Available Interrupt should be generated whenever a Mailbox Out entry has been 
cleared by the host adapter. One byte of outbound data is transmitted to 
indicate whether the interrupt should be enabled or disabled. 

Byte 0 Enable/Disable Parameter: The Enable/Disable parameter byte must be 
                                 either 00H or 01H. If the Enable/Disable 
                                 parameter byte is 00H, the Mailbox Out 
                                 Available interrupt  is not returned. If the 
                                 Enable/Disable parameter byte is 01H, the 
                                 Mailbox Out Available interrupt is returned as
                                 soon as a Mailbox Out has been cleared by the
                                 host adapter. 

After completing this command, HACC will NOT be asserted to avoid generating 
additional interrupts. If the data byte is neither 00 nor 01, INVDCMD will be 
asserted indicating an invalid command. In this case, HACC will also be 
asserted. 

The Mailbox Out Available interrupt is normally intended to be used by the host 
as an indicator that a Mailbox Out entry is available. This function should 
only be enabled if all Mailbox Out entries have been found full by the host. It 
should be disabled soon afterward. If used in other ways, the interrupt may 
generate a large number of relatively useless interrupt handling activities. 


5.1.1.7 Set Selection Time-out  (Operation Code 06)

This command sets the SCSI selection time out value. The SCSI Selection time 
out value is used to determine whether or not a SCSI selection was successful. 
If the SCSI BSY signal is not returned within the specified time out value, the 
selection will be terminated and an appropriate error message posted with the 
returned CCB. This command expects four outbound data bytes to be provided as 
defined below: 

00 Enable/Disable Selection Time Out	
01 Reserved  (00)
02 Time Out Value (MSB)
03 Time Out Value (LSB)

Byte 0- Enable/Disable Selection Time Out: This parameter byte specifies whether 
or not the Selection Time-out will be used. If the byte is set to 00H,   no 
time-out will be performed. If the byte is set to 01H, the time specified in 
bytes 02 and 03 will be used as the Selection Time Out by the SCSI. The default 
value established by the reset process is 01H, indicating the time out is 
enabled. 

Byte 1-Reserved:	This byte must be zero. 

Byte 2,3-Time Out Value:	This two-byte value specifies the time in milliseconds 
that will be used for the Selection Time Out. The default value is 250 
milliseconds. 

After completing this command, HACC will be asserted, indicating normal 
completion. INVDCMD will be asserted if the data byte 0 is neither 00 nor 01 or 
if byte 1 is not zero, indicating an invalid command. 


5.1.1.8 Set Bus-On Time (Operation Code 07)

This command specifies the time that the host adapter spends on the bus when 
transferring data. The Bus-On duration is adjustable from 2 to 15 microseconds. 
The default setting is 11us. One data byte is passed out to the host adapter to 
indicate the Bus-On duration in microseconds. 

Data Byte 0 -- Bus On-Time (2 to 15 us)

After completing this command, HACC will be asserted indicating normal 
completion. INVDCMD will be asserted, indicating an invalid command, if the 
data byte is greater than 15. The valid range is 2 to 15 decimal. 


5.1.1.9 Set Bus-Off Time (Operation Code 08)

This command sets the time that  the host adapter will spend off the bus during 
a data transfer. The Bus-On duration is adjustable from 1 to 64 microseconds. 
The default setting is 4us. After receiving this command, the host adapter 
expects one byte of data which specifies the bus off time in microseconds. 

Data Byte 0 -- Bus-Off Time ( 1 to 64 us)

After completing this command, HACC will be asserted indicating normal 
completion. INVDCMD will be asserted, indicating an invalid command, if the 
data byte is greater than 64. The valid range is 1 to 64 decimal. The actual 
time implemented by the host adapter is rounded down to the next four 
microsecond step at or below the specified value. The minimum value is 
approximately one microsecond. 

5.1.1.10 Set Transfer Speed (Operation Code 09)

This command adjusts the Bus Master DMA circuitry to a specified maximum AT bus 
transfer speed to and from the host memory. Several speeds may be selected by 
setting the jumper configuration as explained in section 3.3. The selected 
jumper speeds are overridden if the Set Transfer Speed command is executed. The 
single data byte transmitted after the command byte either sets the read and 
write speed together, or establishes separate values for each. Appendix A gives 
the timings that result from the selected values. The default setting is the 
value set by the jumpers. The I/O Channel Ready signal automatically slows the 
system further if required by the host memory. 

Data Byte 0 	-- AT Bus Transfer Speed
                    00 -- 5.0 MB/second
                    01 -- 6.7 MB/second
                    02 -- 8.0 MB/second
                    03 -- 10 MB/second
                    04-- 5.7 MB/second
                    80-FF-- See Table
After completing this command HACC is set indicating normal completion. 

5.1.1.11 Return Installed Devices (Operation Code 0A)

This command returns information about which SCSI Targets and Logical Units 
(LU's) are installed on the SCSI bus. The host adapter issues the SCSI Test 
Unit Ready command to each target/LUN combination and reports the results using 
eight bytes of data returned through the Data In Register. A bit having a value 
of one indicates that the associated LU is installed.  Each byte is associated 
with the  corresponding target. Each bit within a target byte is associated 
with a particular Logical Unit, bit 7 indicating the presence of LU 7 and so 
forth. The state of the target is analyzed using the SCSI TEST UNIT READY 
command, analyzing the returned data to determine if the addressed LU is 
available. 

After receiving this command, the host adapter returns eight bytes of 
information which specify the installed configuration  as shown below: 

Byte 0          Target 0 Configuration:

                Bit 7 LU 7 Installed
                Bit 6 LU 6 Installed
                Bit 5 LU 5 Installed
                Bit 4 LU 4 Installed
                Bit 3 LU 3 Installed
                Bit 2 LU 2 Installed
                Bit 1 LU 1 Installed
                Bit 0 LU 0 Installed

Byte 1 Target 1 Configuration
Byte 2 Target 2 Configuration
Byte 3 Target 3 Configuration
Byte 4 Target 4 Configuration
Byte 5 Target 5 Configuration
Byte 6 Target 6 Configuration
Byte 7 Target 7 Configuration

The byte associated with the SCSI Device Identifier of the host adapter will 
always be zero. After completing the information transfer, the HACC bit will be 
set to indicate normal completion. 

5.1.1.12 Return Configuration Data (Operation Code 0B)

The DMA arbitration priority, the Interrupt channel, and the SCSI ID of the 
adapter are returned by this command. The three bytes of information are 
returned in the following format: 

Byte 0 DMA Arbitration Priority:
Bit 7 Channel 7
Bit 6 Channel 6
Bit 5 Channel 5
Bits 4-1 Reserved (0)
Bit 0 Channel 0

Byte 1 Interrupt Channel:
Bit 7 Reserved (0)
Bit 6 Interrupt channel 15
Bit 5 Interrupt channel 14
Bit 4 Reserved (0)
Bit 3 Interrupt channel 12
Bit 2 Interrupt channel 11
Bit 1 Interrupt channel 10
Bit 0 Interrupt channel 9

Byte 2	SCSI Identifier
Bits 7-3 Reserved (0)
Bits 2-0 Binary value of SCSI Identifier

After completing this command, HACC will be set indicating normal completion. 


5.1.1.13 Enable Target Mode Command (Operation Code 0C)

A special host adapter command  (0C)  enables and disables target mode. The 
host adapter requires that two bytes of outbound information follow the command 
byte. The information bytes contain the following information: 

Byte 0-  Enable/Disable Target Mode:	This parameter specifies which operating 
modes the host adapter will use. If the byte is set to 00H, the AHA-1540A/1542A 
will operate only in Initiator Mode. If the byte is set to 01H, the host 
adapter will operate both as an initiator and as a Processor type Target SCSI 
Device. Any other value is invalid. The default value after  a Hard Reset, Soft 
Reset, or Power On Reset is 00H (Initiator only). 

Byte 1-Logical Unit Mask: This parameter byte contains an eight bit bit-
significant mask indicating the Logical Units which will respond in Target 
Mode.  Bit 7 corresponds to LU 7, and so forth. If the bit is one, the 
corresponding LU will be treated as installed. If the bit is zero, the LU will 
be treated as not installed. 

If the AHA-1540A/1542A does not have the Target Mode feature installed, the 
host adapter will indicate an invalid host adapter command. If an attempt is 
made to change from target mode while there are still target mode CCB's being 
processed by the host adapter, the host adapter will post an invalid host 
adapter command indication. 

If the command disables Target Mode, the Logical Unit Mask byte will be 
ignored. If the command enables Target Mode, the Logical Unit Mask byte must 
contain at least one bit, indicating the presence of at least one Logical Unit. 

The SCSI INQUIRY command will provide an indication to other initiators that 
the Logical Unit is installed or not installed  in byte 1 of the returned 
inquiry data. 

If target mode is not enabled, the host adapter will behave on the SCSI 
interface as if it were an ordinary SCSI initiator. Any attempt to select the 
host adapter will result in a SCSI selection time out. Most Reset Operation, 
including Soft Reset, Hard Reset, and Power-On Reset will return the AHA-
1540A/1542A Target Mode to the disabled state. SCSI Resets, generated either by 
the host or by other SCSI Devices, will not change the previously established 
enabled or disabled state of Target Mode. 


5.1.1.14 Return Setup Data (Operation Code 0D)

This command returns information describing the setup of the host adapter. The 
information returned reflects either the values supplied by previous host 
adapter commands or default values. The command is followed by an outbound data 
transfer and an inbound data transfer. The outbound transfer is a one byte 
parameter indicating the length of the required inbound data transfer. The 
inbound data transfer contains from zero to 255 bytes of information describing 
the setup of the host adapter. The inbound information normally transferred 
will be truncated or padded with zeros as necessary to transfer the requested 
number of bytes. The number of bytes normally transferred by the AHA-154XA is 
16. 

 Outbound Data Byte:

Byte 0     Data In Length: The number of data bytes requested can be from 0 to 
                           255. A value of zero will be accepted and 256 bytes
                           will be returned.

Inbound Data Summary:


00     SDT and Parity Status
01     Transfer Speed
02     Bus On Time
03     Bus Off Time
04     Number of Mailboxes
05     Mailbox Address (MSB)
06     Mailbox Address
07     Mailbox Address (LSB)
08-0F  Synchronous Transfer Agreements
10-FF  Reserved (00)

Inbound Data Bit Assignments:

Byte 0   SDT and Parity Status:

         Bit      Meaning
          0       If this bit is zero, Synchronous Data Transfer negotiation 
                  will not be initiated by the host adapter, but will be 
                  responded to if requested by an attached SCSI Device. If the 
                  bit is one, Synchronous Data Transfer negotiation will be
                  initiated by the host adapter under those conditions which
                  require such negotiation. The state is set from jumper J1.

          1       If this bit is zero, parity checking on inbound SCSI transfers
                  has been disabled. If this bit is one, parity checking on 
                  inbound SCSI transfers is enabled. The state is set from 
                  jumper J1.

         2-7      Reserved (0)

Byte 1 Transfer Speed-This byte returns the value passed in to the host adapter 
                      by the Set Transfer Speed command (See Section  5.1.1.10) 

Byte 2 Bus On Time:Indicates the Bus On Time in microseconds 
                   (See Section 5.1.1.8) 

Byte 3 Bus Off Time:Indicates the Bus Off Time specified by the Bus Off Time 
Value in microseconds. (See Section 5.1.1.9) 

Byte 4- Number of Mailboxes:The number of Mailboxes established by  a previous 
Mailbox Initialization command will be returned in this byte. This number will 
be 00H if the Mailbox Initialization command has not yet been successfully 
completed. 

Byte 5-7 -Mailbox Address:The base address of the Mailbox area established by a 
previous Mailbox Initialization command will be returned in these bytes. The 
Most Significant byte is byte 5. These bytes have no meaning if Mailbox 
Initialization has not yet been successfully completed. 

Byte 8-Sync Neg, Target 0 Returns information about the synchronous negotiation 
with Target 0. The byte will be 00H for the address of the host adapter. 

Bit 7-Set to one if synchronous transfer is negotiated. Set to zero if 
asynchronous transfer is being performed. 

Bits 6-4 -These bits contain a value between 0 and 7 that defines the 
synchronous transfer period according to the following equation. Period =200 +  
50 (value) nanoseconds 

Bits 3-0 -These bits contain the negotiated offset value. The value will 
normally be between 1 and 7. 

Byte 9 Sync Neg, Target 1	Same as byte 8, for target 1 

Byte 10 Sync Neg, Target 2	Same as byte 8, for target 2 
Byte 11 Sync Neg, Target 3	Same as byte 8, for target 3
Byte 12 Sync Neg, Target 4	Same as byte 8, for target 4
Byte 13 Sync Neg, Target 5	Same as byte 8, for target 5
Byte 14 Sync Neg, Target 6	Same as byte 8, for target 6
Byte 15 Sync Neg, Target 7	Same as byte 8, for target 7

If the command completes normally, the HACC interrupt will be set to one. If 
the Mailbox area has not been properly initialized, all 16 bytes are still 
requested by the host. If byte 4, the Number of Mailboxes, is zero, bytes 5-7 
must be ignored. 

5.1.1.15  Write Adapter Channel 2 Buffer (Operation Code 1A)

After receiving this command, the host adapter expects three outbound 
information bytes to be transferred which point to an area of 64 bytes in 
system RAM. The area pointed to will be transferred to the host adapter's 
Channel 2 Buffer using the host adapter's DMA circuitry.  After completing the 
transfer of the 64 bytes from the indicated buffer area to the host adapter, 
the HACC interrupt will be set indicating normal completion. This command is 
used in conjunction with the Read Channel 2 Buffer command for host  adapter 
diagnostics. The Channel 2 Buffer is used for transmission of all information 
except the actual data field between the host adapter and the host system. 

Byte 0       Buffer area address, Most significant byte
Byte 1       Buffer area address
Byte 2       Buffer area address, Least significant byte 	

5.1.1.16  Read Adapter Channel 2 Buffer (Operation Code 1B)

After receiving this command, the host adapter expects three outbound 
information bytes to be transferred which point to an area of 64 bytes in 
system RAM.  The area pointed to will be used as a buffer to receive 64 bytes 
of information transferred from the host adapter's Channel 2 Buffer to the 
host's memory using the host adapter's DMA circuitry. After completing the 
transfer of the 64 bytes from the Channel 2 Buffer to the indicated host memory 
area, the HACC interrupt will be set indicating normal completion. This command 
is used in conjunction with the Write Channel 2 Buffer command for host adapter 
diagnostics. 

Byte 0   Buffer area address, Most significant byte
Byte 1   Buffer area address
Byte 2   Buffer area address, Least significant byte 

5.1.1.17 Write Adapter FIFO Buffer (Operation Code 1C)

After receiving this command, the host adapter expects three outbound 
information bytes to be transferred which point to an area of 54 bytes in 
system RAM. The area pointed to will be transferred to the host adapter's FIFO 
buffer using the host adapter's DMA circuitry.  After completing the transfer 
of the 54 bytes from the indicated buffer area to the host adapter, the HACC 
interrupt will be set indicating normal completion. This command is used in 
conjunction with the Read Adapter FIFO Buffer command for host  adapter 
diagnostics. 

Byte 0   Buffer area address, Most significant byte
Byte 1   Buffer area address
Byte 2   Buffer area address, Least significant byte 	

5.1.1.18 Read Adapter FIFO Buffer (Operation Code 1D)

After receiving this command, the host adapter expects three outbound 
information bytes to be transferred which point to an area of 54 bytes in 
system RAM.  The area pointed to will be used as a buffer to receive 54 bytes 
of information transferred from the host adapter's FIFO to the host's memory 
using the host adapter's DMA circuitry. After completing the transfer of the 54 
bytes from the FIFO to the indicated buffer area, the HACC interrupt will be 
set indicating normal completion. This command is used in conjunction with the 
Write Adapter FIFO Buffer command for host adapter diagnostics. 

Byte 0      Buffer area address, Most significant byte
Byte 1      Buffer area address
Byte 2      Buffer area address, Least significant byte 	

5.1.1.19 ECHO Command Data (Operation Code 1F)

This command is used to test the Command / Data Out Port, the Data In Port, and 
the associated control bits in the other I/O Ports.  After receiving this 
command, the host adapter expects one byte of outbound information to be 
transferred through the Command / Data Out Port. The host adapter then sends 
(Echos) the same data value back to the host through the Data In Port. After 
the host has read the data value provided on the Data In Port, the host adapter 
will generate the HACC interrupt to indicate normal command completion. 

Byte 0, Out   Outbound Echo Value
Byte 0, In    Returned Echo Value

5.2 MAILBOX OVERVIEW

The AHA-1540A/1542A uses a mailbox architecture for task communication between 
the host and the host adapter when executing SCSI commands. This allows the 
host adapter to perform multithreaded operations with a minimum of host 
intervention. The mailboxes are located in main system memory. Each mailbox 
entry is four bytes long. At power up, the host issues an initialization 
command to inform the host of the mailbox location. There are always an equal 
number of Outgoing Mailboxes (MBO) and Incoming Mailboxes (MBI). The MBIs are 
located immediately after the MBOs. Initiator operations and target operations 
use the same mailboxes. Both initiator and target operations may be in process 
at the same time. A typical mailbox structure is shown below. 

In this example, there are four MBOs and four MBIs. The Mailbox Count in the 
Mailbox Initialization command was set to four. The base address is the address 
specified by the Mailbox Address field. 

Note: The Adaptec BIOS initializes the AT DMA controller to accommodate Bus 
Master DMA. If the host adapter BIOS is removed or disabled, the host DMA 
controller must be initialized, via software, for Bus Master DMA operation. See 
section 5.5. 

5.2.1 Mailbox Out Definition

The first byte of each MBO contains the Mailbox status byte. The remaining 
three bytes contain an address pointer to the first byte of a Command Control 
Block (CCB). The CCB provides additional task control information. A MBO is 
free if the first byte is zero. The host can make an entry in any free MBO and 
indicate that it is filled out or completed by placing the proper MBO command 
in the first byte of the MBO. After the MBO has been examined by the host 
adapter and all relevant information obtained by the host adapter, the host 
adapter sets the MBO command byte back to zero to allow the host to fill it 
again. For a multitasking operating system, it is desirable that the number of 
mailboxes be sufficient to allow at least one mailbox for each active 
independent task or activity. 
The MBO format is described in detail below:

Byte 0 MBO Command  This byte specifies the state of the MBO entry.

Value         Definition

00H        Mailbox Out is free
01H        SCSI or Host Adapter command is to be started. CCB pointer 
           indicates location of CCB to be processed.
02H        SCSI or Host Adapter command is to be aborted. CCB pointer indicates
           location of CCB to be terminated.
Byte 1     CCB Pointer (MSB)
Byte 2     CCB Pointer
Byte 3     CCB Pointer (LSB)

The use of Mailbox Out (MBO) entries to pass pointers to CCB's is identical for 
target and initiator modes. The appropriate target mode CCB may be prepared 
early and posted to the host adapter in preparation for an operation that is 
expected to happen. If a SCSI operation occurs before the CCB is prepared, the 
host adapter processes as much of the transaction as possible, then requests a 
CCB from the host through the MBI. The host is fully responsible for preparing 
the correct CCB from the information provided through the MBI. 

In target mode, one CCB may be presented for each unique combination of LUN, 
Initiator, and direction. If a second CCB to the same LUN and initiator with 
the same direction bit is sent to the AHA-1540A/1542A, the CCB will be returned 
with a host status of 19H, Duplicate CCB Received. 

Initiator type CCB's may be queued for an LUN and Target. The host adapter will 
always search for new MBO entries in a round-robin order, beginning with the 
entry after the last MBO entry that was processed. By always placing the MBO 
entries in  the MBO area consecutively, the host can assure that the SCSI 
commands will be started with a minimum scan overhead. Initiator CCB queueing 
must be used with caution, since under some circumstances it is possible for 
CCB's to be executed out of order. 

If the Mailbox Out Available Interrupt is enabled by execution of Adapter 
Command 05 (Enable Mailbox Out Available Interrupt), the host adapter will take 
one of the following actions after each MBO entry is freed by the host adapter: 

1)If the Any Interrupt bit in the Interrupt Flag Port is zero, indicating that 
there are no interrupts pending, the host adapter will set the Mailbox Out 
Available Interrupt and the Any Interrupt bit and indicate a hardware interrupt 
to the host. 

2)If the Mailbox Out Available Interrupt has been set to one by the previous 
clearing of a Mailbox Out entry and the interrupt has not yet been cleared by 
the host, the host adapter will not change the MBOA interrupt bit and will 
continue to scan for other stored MBO entries. 

3)If interrupts other than the Mailbox Out Available Interrupt are pending, the 
host adapter will wait for the pending interrupts to be cleared before setting 
the Mailbox Out Available Interrupt. This guarantees that the MBO Available 
Interrupt will not be cleared accidentally by clearing another interrupt. 


5.2.2 Mailbox In Definition

The Mailbox In entries are used to pass completion information concerning a 
task from the host adapter to the host. In addition, requests for Target Mode 
CCB's are passed to the host using MBI entries. The first byte of each MBI 
contains the MBI Status byte, summarizing the type of information being passed 
from the host adapter to the host. The remaining three bytes contain 
specialized information that provides more detail about the information. In the 
case of a CCB Completed MBI, the bytes contain a pointer to the completed CCB. 
In the case of a CCB Required MBI, the bytes contain the information necessary 
for the host to prepare an appropriate CCB. Only those MBI's with a MBI Status 
that is non-zero have information for the host. When the host returns the MBI 
Status byte to zero, the MBI Free state, the host adapter is allowed to place a 
new set of information in the MBI entry. 
 
When a SCSI command completes or if a new CCB is required, the host adapter 
scans the first byte of an MBI entry to find a free mailbox. If one is found, 
the host adapter will update the MBI's status byte with a non zero value and 
update the following bytes with the appropriate required pointers or 
parameters. The valid MBI formats are defined below: 

Mailbox In Format for CCB Complete

Byte 0        MBI Status-This byte specifies the state of the MBI entry.
Value         Definition
00H           Mailbox In is free
01H           CCB completed without error. CCB pointer indicates location of
              successfully completed CCB. 
02H           CCB aborted by host. CCB pointer indicates location of CCB that
              was aborted.
03H           Aborted CCB not found. CCB pointer indicates the supposed location
              of the CCB that was to have been aborted. It is likely that the 
              CCB was already presented to the host before the Abort  CCB MBO
              entry was completed.
04H           CCB Completed with Error. The CCB fields indicate the details of
              the error condition. This code allows normal CCB completion to be
              processed without bothering to examine the completion codes in 
              the CCB. 
Byte 1        CCB Pointer (MSB)
Byte 2        CCB Pointer
Byte 3        CCB Pointer (LSB)

Mailbox In Format for CCB Required
Byte 0       MBI Status	This byte specifies the state of the MBI entry.
Value        Definition
10H          SCSI Target Command received with no CCB available. The host must
             prepare an appropriate CCB and place it in the MBO to complete the
             SCSI command. The remaining three bytes of the MBI specify the 
             information necessary to prepare a SCSI command.
Byte 1       Initiator and LUN
Bit 7-5      Binary address of initiator that selected the host adapter in 
             Target Mode.
Bit 4        The SCSI Target Command received was a RECEIVE command. A CCB must
             be prepared to transmit data to the Initiator.
Bit 3        The SCSI Target Command received was a SEND command. A CCB must be
             prepared to transmit data from the Initiator.
Bits 2-0     Binary address of the logical unit of the Target Mode host adapter
             that was addressed by the Initiator.
Byte 2-3     Data Length The high order two bytes of the data length specified
             in the SEND  or the RECEIVE command. A CCB must be prepared to 
             transmit this amount of data plus up to 256 more bytes. It is 
             assumed that the data fields are self-defining or of a known length
             in such protocols.

The CCB Required Mailbox In entries are only generated when a command has been 
received by the host adapter in target mode. For the CCB Required Mailbox In 
entries, byte 0 takes on a distinctive value of 10H, indicating both that the 
MBI entry is filled and that the MBI entry is being presented to request a CCB 
appropriate to service a SCSI transaction for which no CCB was available. The 
host adapter will have disconnected on the SCSI after receiving the initiator 
and LU addresses and after having received either a SCSI SEND or a RECEIVE 
command. If the LU address is enabled by the Logical Unit Mask, the MBI will 
provide the addresses in bits 7-5 and bits 2-0 and will indicate by setting 
either bit 3 or bit 4 that a SCSI SEND or RECEIVE command was accepted from the 
initiator. The host system is then expected to prepare a CCB suitable for 
processing the Send or Receive command. The information in bytes 2 and 3 is a 
copy of bytes 2 and 3 of the Send or Receive command CDB. This provides the 
host  an approximation of the length of the requested data transfer. This 
length is used by the host to allocate the correct amount of buffer to accept 
data in a SEND command or to control the maximum amount of data that can be 
transferred in a RECEIVE command. If the LU address received is disabled,  no 
MBI will be presented and a check condition will be posted to the Initiator. A 
subsequent REQUEST SENSE command will recover an Invalid LUN error indication. 

After each Mailbox In entry is stored by the host adapter, it will indicate 
that Mailbox In scanning must be performed in the following manner: 

1)-If the Any Interrupt bit is not set to one in the Interrupt Flag port, 
indicating that no interrupts are pending, the host adapter will set the 
Mailbox In Full interrupt bit, the Any Interrupt bit, and raise the hardware 
interrupt line to indicate that there is at least one Mailbox In entry to be 
examined by the host system. 

2)-If the Mailbox In Full interrupt bit has already been set to indicate that 
an entry was made in the Mailbox In area and if that interrupt has not yet been 
cleared by the host, no further notification is provided by the host adapter. 

3)-If interrupts other than the Mailbox In Full interrupt are pending, the host 
adapter will wait for all pending interrupts to be cleared before setting the 
Mailbox In Full interrupt. 

Note that careful host Target Mode software design is necessary to prevent 
ambiguity in the notification process. If a CCB was just prepared but the MBO 
has not yet been searched by the host adapter at the time the MBI entry is made 
to the host, the host may choose to examine the MBI entry and not act on it, 
having already provided the needed CCB. The host should also examine the entire 
MBI space to be sure that a previously supplied CCB which should have been able 
to service the notification MBI entry was not already used for a previous 
operation that had been posted by the host adapter but not yet serviced by the 
host. Proper care in host system design will prevent these overlapping 
operations from becoming a problem. 

5.3 COMMAND BLOCK DEFINITION

The CCB specifies detailed information about a SCSI command. The format of a 
CCB is shown below. Each of the fields is separately explained following the 
table. 

COMMAND CONTROL BLOCK FORMAT


Byte 0    Command Control Block Operation Code
Value       Definition
00H       SCSI Initiator Command
01H       Target Mode Command
02H       SCSI Initiator Command with Scatter/Gather
81H       Bus Device Reset

Byte 1   Address and Direction Control 
Bits 7-5   CCB Op Code = 00, 02:  SCSI Target Id 
           CCB Op Code = 01:     SCSI Initiator Id
Bit   4    Outbound data transfer, length is checked.
Bit   3    Inbound data transfer, length is checked.
Bit  2-0   Logical Unit Number
Byte 2     SCSI Command Length
Byte 3     Request Sense Allocation Length/Disable Auto Sense
Byte 4-7   Data Length (Byte 4 most significant)
Byte 7-9   Data Pointer (Byte 7 most significant)
Byte 10-12 Link Pointer (Byte 10 most significant)
Byte 13    Command Linking Identifier
Byte 14    Host Adapter Status  (HASTAT)
Byte 15    Target Device Status  (TARSTAT)
Byte 16-17 Reserved (00)
Byte 18-n  SCSI Command Descriptor Block
           (Length specified by byte 2)
Byte n-m   Reserved for REQUEST SENSE information bytes
           (Length of reserved space in byte 3)

The standard format of the Command Control Block is shown in the following 
diagram: 

The bytes of the CCB are defined further below:
Byte 0: Command Control Block Operation Codes
The AHA-1540A/1542A supports four CCB Operation Codes. The valid command values 
are shown below: 

00  SCSI Initiator Command Control Block
01  SCSI Target  Command Control Block
02  SCSI Initiator Command Control Block with Scatter/Gather
81  SCSI Bus Device Reset

If the Operation Code value is 00H, the SCSI command specified in the Command 
Descriptor Block field of the CCB is executed against the addressed Target  / 
LUN. The other fields of the CCB support the required Initiator functions of 
the AHA-1540A/1542A. 

If the Operation Code value is 01H, the CCB is intended to service a SEND or 
RECEIVE command sent to the host adapter as a target from another initiator. 
The values in the other fields are used to service the Target Mode operation. 
If an Operation Code of 01H is specified to a host adapter that has not had its 
Target Mode enabled, the host adapter returns a Host Status indication of 18H, 
Invalid CCB Parameter. 

If the Operation Code value is 02H, the SCSI command specified in the Command 
Descriptor Block field of the CCB is executed against the addressed Target / 
LUN. The definition of the Data Length and the Data Pointer is modified to 
support the Scatter/Gather function. Refer to section 5.2.4. 

If the value is 81(hex) a Bus Device Reset message will be sent to the 
addressed target. This command forces the host adapter to abort all outstanding 
tasks against the selected target. All remaining CCB Bytes are ignored. The 
host adapter will generate a Bus Device Reset message out to the specified 
target. 

Any other command value generates a Host Adapter Detected Error (Host Status 
byte of 16H). 


Byte 1: Address and Control Byte

This byte identifies the address of the devices that will be serviced and 
provides information about the expected direction of data flow. 

If the CCB is an Initiator CCB, this byte identifies the target SCSI device in 
bits 7,6, and 5. If the CCB is a Target CCB, the byte identifies the initiator 
which the CCB will serve. 

Bits 4 and 3 are set to determine the direction of data transfer. For an 
Initiator CCB, if neither bit is set, the direction of data transfer will be 
established by the SCSI command being executed.  For a Target CCB, if neither 
bit is set or both bits are set, the CCB will be returned with an indication of 
Invalid CCB Parameters (18H) in the Host Status field, since each Target CCB 
must be identified as to whether it will service a SEND or a RECEIVE command. 
If both bits are set for an initiator CCB,  the command must perform no data 
transfer. If only bit 3 is active, the data transfer will be to the host 
adapter and from the external SCSI device. If the CCB is a target CCB, the data 
transfer will be required to be a Data Out phase, while if the CCB is an 
initiator CCB, the data transfer will be required to be a Data In phase. If 
only bit 4 is active, the data transfer will be from the host adapter and to 
the external SCSI device. If the CCB is a target CCB, the data transfer must be 
a Data In phase, while if the CCB is an initiator CCB, the data transfer will 
be a Data Out phase. 

If bits 3 or 4 are set for an Initiator CCB, the data length will be checked. 
If the amount of data transferred exceeds the specified amount, the CCB Host 
Status field will contain an indication of Data Over/Under Run (12H). For a  
Processor Target mode CCB, the handling of incorrect lengths is described in 
Section 8.2.4. 

If a data underrun/overrun condition occurs for an operation that accesses the 
drive's media (READ/WRITE, EXTENDED READ/WRITE, WRITE AND VERIFY) and the 
direction bits are set to zero, the host adapter will complete the operation 
without error. However, some or all of the data specified by the host may not 
be transferred. 

CAUTION:  THE APPROPRIATE DIRECTION BIT SHOULD BE SET FOR ALL OPERATIONS THAT 
ACCESS THE DRIVE'S MEDIA. 

If the CCB is an initiator CCB, bits 2,1, and 0 define the target Logical Unit 
which will be addressed. If the target accepts an IDENTIFY message out, the 
value in bits 2,1, and 0 will be provided in the LUN field of the message byte. 
The LUN field in the SCSI Command Descriptor Block (CDB) is expected to be 
zero. If the target does not accept an IDENTIFY message out, the LUN field in 
the SCSI CDB must contain the correct Logical Unit address. SCSI devices with 
conformance level 2, including Common Command Set (CCS) disk drives and all 
SCSI-2 devices will always accept the IDENTIFY message out. The few SCSI 
devices not meeting those requirements must be examined on a case by case basis 
to determine whether the Logical Unit Address should be placed in CCB Byte 1 or 
in the CDB. 

This enables the host adapter to check the length of the data transfer and if a 
data underrun/overrun condition occurs, the CCB will be returned with an 
indication of Data Underrun/Overrun (12H) in the Host Status field. For 
operations that do not access the drive's media, the direction bits should be 
set to zero unless transfer length checking is desired. Setting both direction 
bits to one should be used only when no data transfer is expected or 
suppression of data transfer is desired for READ operations. 

Byte 2: SCSI Command Length

This byte establishes the length, in bytes, of the SCSI Command Descriptor 
Block. 

Byte 3: Request Sense Allocation Length

When a SCSI device terminates an operation with CHECK CONDITION status, it 
means that the device has error or status information as a result of execution 
of the operation. The SCSI specification indicates that a REQUEST SENSE command 
must be executed before any other command is executed in order for the host 
initiator to be sure of obtaining the error information. Since the AHA-154XA 
host adapter has the capability of queueing commands for execution, the host 
adapter itself must take charge of generating the Request Sense command. The 
automatic generation of Request Sense is inconvenient for some specialized 
operating systems, so the function can be disabled by installation of a jumper 
in J9 (See section 3.3.11). If the jumper is not installed, the function can 
also be disabled by specifying a value of 01H for the Request Sense Allocation 
Length. 

This byte indicates the length, in bytes, of the area reserved for information 
that may be obtained by a REQUEST SENSE command. A value of 00H indicates that 
an allocation length of 14 bytes is to be used, sufficient to capture the sense 
key and error code of all normal extended sense type devices. A value of 01H 
requests that no automatic REQUEST SENSE be executed. The values from 02H to 
07H are reserved. Values from 08H to FFH are valid allocation lengths. The 
value is used to notify the host adapter that the specified number of bytes 
have been reserved at the end of the CCB to receive possible Request Sense data 
bytes. The REQUEST SENSE also uses the indicated allocation length as its byte 
count in the Command Descriptor Block generated by the host adapter. 

If an operation that treats the AHA-1540A/1542A as a Target Mode device fails 
and presents a Check Condition status byte,  the Initiator should return a 
REQUEST SENSE command. The AHA-1540A/1542A will return appropriate sense 
information in response to the command. If the command that originally failed 
was a SEND or a RECEIVE command, the same REQUEST SENSE information bytes that 
will later be sent to the Initiator are also sent to the host when the CCB is 
returned. The sense information is placed in the specified Request Sense 
Allocation area with a length not exceeding the Request Sense Allocation 
Length. 

Bytes 4, 5, 6: Data Length

These bytes determine the length, in bytes, of the data transfer. CCB host 
adapter error 12(hex) is posted if a data over run occurs. 

If the CCB specifies a Scatter/Gather operation, the Data Length field contains 
the total number of bytes in the Data Segment List. 

Bytes 7, 8, 9 : Data Pointer

These bytes specify the real address of the first byte of the data area to be 
used during the data phase of the SCSI command. 

If the CCB specifies a Scatter/Gather operation, the Data Pointer field 
contains the pointer to the first byte of the Data Segment List. 

Bytes 10, 11, 12: Link Pointer

These bytes are used when a SCSI command contains a LINK or LINK WITH TAG bit  
in the command. When a Linked command is completed, the host adapter will use 
the contents of this field as a pointer to the next CCB to execute. If the 
Linked Flag bit is set, an interrupt will be generated before the next command 
is started. A completed CCB is always reported back in an MBI, but MBIF 
interrupts are only reported if the linked set of commands is finished or if a 
Link with Flag message is presented. There must be enough MBI entries to 
receive the entire set of linked commands. 

Target Mode does not support the linking function. 

Byte 13 : Command Link ID

This byte is used in conjunction with linked commands. It is set by the host to 
identify commands in a command chain. 

Linking is not supported in Target Mode. 

Byte 14 : Host Status

This byte is used to report the host adapter status (HASTAT). 

HASTAT has the following definitions:

00 H No host adapter detected error-The CCB was completed normally.
0A H Linked command complete without error-The SCSI command 
                                           completed and linked normally.
0B H Linked command complete without error, interrupt generated.-The SCSI
 command completed and linked with a LINKED COMMAND COMPLETE WITH FLAG message.
11 H Selection time out-The initiator selection or target reselection was not 
   complete within the Set SCSI Selection Time-out period. 
12 H Data over run/Under run-The target attempted to transfer more data than 
   was allocated by the Data Length field or the sum of the Scatter / Gather 
   Data Length fields. 
13 H Unexpected bus free-The target dropped the SCSI BSY at an unexpected time. 
14 H Target bus phase sequence failure-An invalid bus phase or bus phase 
   sequence was requested by the target. The host adapter will generate a SCSI 
   Reset Condition, notifying the host with a SCRD interrupt. 
15 H MBO command was not 00, 01, or 02-The first byte of the MBO command was 
   invalid. This usually indicates a software failure. 
16 H Invalid CCB Operation Code-The first byte of the CCB was invalid. This 
    usually indicates a software failure. 
17 H Linked CCB does not have the same LUN-A subsequent CCB of a set of linked 
   CCB's does not specify the same logical unit number as the first. 
18 H Invalid Target Direction received from Host-The direction of a Target Mode 
   CCB was invalid. 
19 H Duplicate CCB Received in Target Mode-More than once CCB was received to 
   service data transfer between the same target LUN and initiator SCSI ID in 
   the same direction. 
1A H Invalid CCB or Segment List Parameter-A segment list with a zero length 
   segment or invalid segment list boundaries was received. A CCB parameter was 
   invalid. 

Byte 15: Target Status 

For an initiator CCB, this byte is used to return the SCSI status byte sent to 
the host adapter from the initiator. If a SCSI command returns with BUSY 
status, the normal recovery process is to execute the command again. The AHA-
154XA takes that burden off the host and periodically restarts the command 
automatically until the command completes with a status other than Busy. 
  
For a target mode CCB, this byte is used to indicate to the host what status 
the host adapter returned to the initiator. 

Target Status may have the following values in target mode 

00 -- Good Status
02 -- Check Status (See REQUEST SENSE byte area)
08 -- LUN Busy

Byte 16: Reserved (must be 0)

Byte 17: Reserved (must be 0)

Byte 18: n: SCSI Command Descriptor Block

This field holds the SCSI Command Descriptor Block (CDB) as described in the 
SCSI specification. The length of this command is described in byte 02. For 
initiator mode CCB's, the CDB provided by the host is transmitted to the 
target. For target mode CCB's, the CDB provided from the initiator is returned 
to the host in this space. 

Byte 18+n - 18+n+m : Allocated for Sense Data

If a Check Status condition is detected by the AHA-154XA as it completes an 
operation on the SCSI bus,  the host adapter automatically executes a REQUEST 
SENSE command with the data length specified by Request Sense Allocation 
Length. The actual bytes returned, up to the maximum indicated by the Request 
Sense Allocation Length, are placed in the area Allocated for Sense Data. If 
the Request Sense Allocation Length was 01h, no REQUEST SENSE command is 
executed. 

If a check condition is detected by the AHA-154XA while it is operating in 
Processor Target Mode, the same information that will later be recovered by the 
initiator that received the Check Status is also placed in the area Allocated 
for Sense Data so that the host processor is also aware of the failure. 


5.3.1 SCATTER/GATHER LIST DEFINITION

Using the normal CCB Operation Codes of 00 and 01 (SCSI Initiator and SCSI 
Target CCB's), the CCB itself contains a pointer to the first byte of a 
contiguous area of data of a specified length. The direction of transfer with 
respect to the data area and the checking of the length of the data transfer to 
the data area are both managed by the AHA-1540A/1542A according to the 
requirements of the particular mode and control bit set-up. 

Using the Scatter/gather Operation Code of 02, the CCB instead contains a 
pointer to a list of data segments and an indication of the length of the list 
of data segments. The data segment list contains pointers to the actual 
location in host memory of the data segments to be transferred as well as a 
precise indication of the length of each data segment. Each data segment list 
entry contains a three-byte pointer to the location of a data segment and 
three-byte length indicator telling how long that particular data segment shall 
be. The data segment list is arranged in the order in which data will be 
gathered or distributed, the first pointer in the list being used first. 

A typical data segment list is shown in the following table. The data segment 
list describes the distribution of 4096 bytes distributed in four separate 
locations within the memory. The beginning of the data segment list is 
indicated by the data segment list pointer. The length of the data segment list 
(24 bytes) will be contained in the data segment list length field of the CCB. 

A data segment list can have from one to sixteen segments. A list with 0 
segments or a list with more than 16 segments causes an Invalid Segment List 
error to be posted in the host status field. 

The AHA-154XA has certain constraints in the data segment address boundaries 
and lengths that are allowed. If these boundaries are violated, an Invalid 
Segment List error will be posted in the host status field of the CCB. The 
simplest way to assure that these boundaries are not violated is to require all 
boundaries between segments to be on even word boundaries. The first segment 
may begin on any boundary and the last segment may end on any boundary. All 
segments but the first and last should have even byte counts. 

The actual boundary limitation is somewhat less restrictive. If the binary 
values of the starting address of a segment, the byte count of that segment, 
and the starting address of the next segment are all exclusive OR'd together, 
and the result of that exclusive or is an even number, the boundary between 
those two segments is valid. Another way to express the limitation is to 
require that the ending boundary of one segment must be the same as the 
beginning boundary of the next segment. If a segment ends on a word boundary, 
the next segment must begin on a word boundary. Similarly, if a segment ends on 
an odd-byte boundary, the next segment must begin on an odd-byte boundary. 


5.4 DESCRIPTION OF OPERATION 

This section describes the interface operations required to invoke the desired 
SCSI behavior. The AHA-1540A/1542A must be properly initialized before any of 
these operations can be performed. 

After system initialization is done, the I/O Command Port initialization 
commands must be executed. The Mailbox Initialization command must be executed 
to assign the Mailbox area. The Enable Target Mode command may optionally be 
executed if Target Mode is to be allowed. 

5.4.1 Execution of Initiator Mode operations 

To begin an Initiator Mode SCSI command, the host first allocates a data buffer 
area. A CCB is then created to perform the desired operation to the correct 
peripheral device and a pointer to the data buffer area is placed in the CCB. 
Once the CCB is completely defined, the host places a pointer to the CCB in an 
empty MBO location, places an MBO full status in the MBO status byte, and 
transmits a Start SCSI Command to the I/O Command Port. If it is not already 
scanning the MBO for an active MBO entry, the Start SCSI Command to the I/O 
Port causes the host adapter to begin scanning for such an entry. 

After finding an active MBO entry, the AHA-1540A/1542A copies the MBO Command 
field contents and CCB pointer into its internal RAM and clears the MBO Command 
byte, freeing the mailbox. Up to 16 initiator CCBs and 16 target CCBs can be 
stored in the host adapter's internal RAM concurrently. The AHA-1540A/1542A 
maximizes the SCSI bus utilization by starting the next available CCB as soon 
as the bus is free. Disconnection  and reconnection on the bus are 
automatically taken care of by the AHA-1540A/1542A. As the host adapter starts 
the SCSI operation, it  will first determine if the addressed target/LUN is 
busy. If the target/LUN is busy, then the command will be placed in the task 
queue to be tried again later. 

Commands are removed from the queue in the order that they were received, 
establishing a (FIFO) first in first out command execution order. Of course, 
the order of task completion may vary due to the different amounts of time 
required to process and complete different commands. If the target/LUN is not 
busy, the new command is started at the next bus free phase. If BUSY status is 
received by the AHA-1540A/1542A, the CCB is placed at the end of the FIFO queue 
to be restarted later. 

If a CHECK CONDITION status is received from the target, the AHA-1540A/1542A 
will issue a Request Sense command to get the sense data. The sense data is 
stored in the CCB after the SCSI command data. The driver software must reserve 
the allocated number of bytes at the end of the CCB to hold the sense data 
which is returned as result of a receiving a check status. Automatic Request 
Sense can be optionally disabled by jumpers or by using the CCB. 

If the MBO Command is to abort a SCSI command, the host adapter first searches 
the active and queued CCBs. If the CCB is found, the task is aborted at the 
earliest possible moment and an MBI entry is made to indicate that the CCBs 
execution was successfully terminated. If the CCB is not found among the active 
or queued CCBs, the AHA-1540A/1542A completes the command and reports that fact 
in the MBI Status byte.  The CCB may not be found because it has previously 
been aborted, because an intervening reset occurred, or because the CCB was 
already finished normally and returned. 

The AHA-1540A/1542A scans the MBOs in a round robin fashion. This is to ensure 
that all of the mailboxes will be scanned with equal probability. A host can 
minimize the AHA-1540A/1542A MBO scan time by using MBO's sequentially. 

When executing a START SCSI command, the AHA-1540A/1542A does not verify that 
the new CCB resides in an unused memory area. Therefore, the host must not 
reuse a CCB location until it has been returned through a Mailbox In entry and 
the host has examined all the pertinent information in the CCB.  CCB addresses 
are used by the AHA-1540A/1542A as task identifiers. 

5.4.2 Execution of Target Mode Operations

5.4.2.1 Target Mode with a Prepared CCB

Typical target operation is managed in the following way by the host software. 
After power-on initialization is complete, the host sends an Enable Target Mode 
command to the host adapter to enable Processor Target mode. After that, the 
host, from previous configuration knowledge, generates a pair of CCB's for each 
likely initiator and for each LUN supported by the host. One CCB is for 
outbound data from the initiator using the SEND command, while the other is for 
inbound data from the target to the initiator using the RECEIVE command. The 
SEND command CCB defines a data buffer for the expected network type command 
from the initiator. The RECEIVE command CCB defines a set of data which is 
known and expected by the initiator, typically a welcome or configuration type 
message packet. The host adapter tests to be sure that duplicate CCBs are not 
provided by the host. 

As the initiator finishes its initialization procedure, it requests 
availability and configuration information using the TEST UNIT READY, REQUEST 
SENSE, and INQUIRY commands. Finally, it may choose to address SEND and RECEIVE 
commands to the targets it has located to transmit or request  information 
packets. 

When the initiator executes a SEND or a RECEIVE command, the target accepts the 
selection on the SCSI bus, accepts the command from the initiator, and executes 
the proper data transfer to or from the area specified by the proper CCB. When 
all SCSI activity is finished successfully, the CCB is posted back to the host 
program by an entry in the MBI. The host adapter updates the CCB byte count and 
CDB field contents to correctly reflect the operation performed. The host is 
notified that there is an entry in the MBI by an interrupt from the host 
adapter.  The host then prepares a new CCB to control the target's next 
activity expected from the initiator. 


5.4.2.2 Target Mode without a Prepared CCB

Alternatively, the processor type device may be addressed by an initiator when 
no CCB has yet been prepared for use by the host adapter. If the host adapter 
command enabling target mode has not yet been executed, the host adapter will 
act like any initiator. It will not accept any selection sequence and any 
attempts to select it by its target ID will cause the initiator to detect a 
selection time-out. 

If the host adapter has been enabled as a Processor Target by a host adapter 
command, any selection to the host adapter's target address will be accepted. 
The availability commands and identification commands (TEST UNIT READY, REQUEST 
SENSE, and INQUIRY) will be executed completely and normally. If a SEND or 
RECEIVE command is received and if a CCB is not active, either because the host 
has not completed its program initialization or because the host has not 
finished analyzing the results of previous data transfers and has not generated 
a new CCB, the Processor Target will accept the selection, obtain the IDENTIFY 
Message Out to determine what Logical Unit has been selected, request the CDB 
from the SCSI, and then disconnect. The CDB will be partially interpreted so 
that the proper MBI can be generated to notify the host that a new CCB with a 
certain address, direction, and data length must be generated. When the new CCB 
is passed to the host adapter by an MBO entry, the CCB is filled up with the 
command information, the SCSI is reconnected, and the command is completed as 
described above. 

5.5 DMA Channel Initialization With the Host Adapter BIOS Disabled

The DMA circuitry must be set to a special state to allow the Bus Master 
operation of the AHA-154XA to operate correctly. This state is normally 
established by the BIOS during initialization so that no other activity is 
required. If a DMA channel other than the default channel is being used or if 
the DMA channel is manipulated by other programs, the circuitry must be 
initialized in the following way before the AHA-154XA can be used. 

For the DMA channel being used, 2 bytes of data must be written to the DMA 
controller port specified to initialize the Host DMA controller for Bus Master 
DMA operation. The following table specifies these values in HEX. 

DMA Channel       DMA Controller Port    Data
 0                       0B               0C
                         0A               00

 5                       D6               C1
                         D4               01

 6                       D6               C2
                         D4               02

 7                       D6               C3
                         D4               03


5.6 INTERRUPT INITIALIZATION

This setup procedure is normally completed by the BIOS during initialization so 
that no other activity is required. If modifications to the interrupt handler 
are required, this information together with the programming information 
provided by the host system should be sufficient to properly set up the 
interrupt vectors. 

The host adapter will drive one of several interrupts in the AT system. The 
particular interrupt used must be set up on power up initialization and be 
properly managed during usage. The AT interrupts of interest to the host 
adapter driver along with their corresponding vector locations are summarized 
below. All these interrupst are handled by a slave interrupt controller. The 
master controller handles all system interrupts such as keyboard, timer, etc. 
and is assumed to be correctly initialized to allow interrupts by the slave 
controller. Upon receiving an interrupt, the processor will be vectored to the 
contents of the corresponding vector location. 

Hardware   Software interrupt
interrupt  vector location (hex)

int 9    --     INT71
int 10   --     INT72
int 11   --     INT73
int 12   --     INT74
int 13   --     INT76
int 14   --     INT77
int 15   --     INT78

The interrupt is initialized by clearing the corresponding interrupt mask bit 
in the slave controller. The mask register is a read/write register, and only 
the bit of interest should be cleared. The port address is A1 hex, and bit 
definitions follow.

Interrupt mask bit definition (port address A1 hex)

bit 0 -- int 8
bit 1 -- int 9
bit 2 -- int 10
bit 3 -- int 11
bit 4 -- int 12
bit 5 -- int 13
bit 6 -- int 14
bit 7 -- int 15

6.1 SINGLE THREADED BIOS COMMAND INTERFACE

The AHA-1540A/1542A BIOS resides on the host adapter board. It provides support 
for up to two SCSI Common Command Set disk drives under DOS. If SCSI devices 
other than CCS disk drives or if support for more than two disk drives is 
required under DOS, the Adaptec DOS Driver, ASW-1110 must be used. The BIOS 
provides a very simple single threaded capability that does not make use of the 
Mailbox Interface used by more sophisticated programs. This capability allows 
the host system to boot from a SCSI disk drive and to support standard DOS 
calls from any standard program. 

The BIOS communicates with the host adapter through a special set of commands 
passed under the I/O Command Port command 02H (Start Bios Command). These 
commands are not available to any programs except the Adaptec BIOS. The Adaptec 
BIOS provides a standard BIOS interface. The DOS interface to the standard BIOS 
is described in this section. 

On an AT compatible machine, up to two hard disks are supported by the BIOS 
resident on the mother board. Any other drives must be managed through the 
Mailbox Interface using an appropriate driver. The operation of the AHA-
1540A/1542A BIOS on attached SCSI devices depends on the number of standard 
hard disks installed directly on the system. 

No standard hard disks installed: 

In this case, two SCSI drives can be supported by the AHA-1540A/1542A BIOS. 
SCSI Device 0 Logical Unit Number 0 is designated as drive 0 (Drive C:). Either 
SCSI Device 0 LUN 1 or SCSI Device 1 LUN 0 may be designated as drive 1 (Drive 
D:). This set of addresses allows the use of two drives with either embedded 
controllers or bridge controllers. Booting is only performed from SCSI Device 0 
LUN 0.  When no standard hard disks are installed, the AHA-1540A/1542A BIOS is 
operating in non-concurrent mode. 

One standard hard disk installed: 

In this case, the internally installed hard disk is designated as drive 0 
(Drive C:). SCSI Device 0 LUN 0 is designated as drive 1 (Drive D:). Booting is 
performed from the internally installed hard disk. This mode of operation is 
called concurrent operation, indicating that the internally installed drive and 
one SCSI drive can operate together under the BIOS. 

Two standard internal hard disks installed: 

In this case, all the disks that can be supported by the BIOS are directly 
installed. The AHA-1540A/1542A BIOS will not support any SCSI drives. Therefore 
a device driver will need to be installed to access the SCSI drives. 

6.2 BIOS COMMAND EXECUTION USING INTERRUPT 13 

On IBM compatible systems, disk I/O requests are passed from the operating 
system to the BIOS through software interrupt 13H. CPU registers are used to 
pass information about the desired operation and the associated parameters. 

The AHA-1540A/1542A BIOS provides SCSI support by intercepting each interrupt 
and managing the request according to the drive address. If the drive is a 
floppy or internally installed fixed disk, the call is managed by the mother 
board BIOS with no changes. If the selected drive is a SCSI disk drive, the 
request is handled by the Adaptec BIOS resident on the AHA-1540A/1542A. For 
concurrent operation, only calls to drive 81H (D:) are handled by the AHA-
1540A/1542A BIOS. For nonconcurrent operation, calls to both drive 80H (C:) and 
81H (D:) are managed by the AHA-1540A/1542A BIOS. 

On each Interrupt 13 call, the correct host microprocessor registers are set by 
the operating system program to provide the required parameters to both the 
Adaptec BIOS and the mother board BIOS. Most commands use the registers as 
indicated in the following table. 

Register Function

AH       BIOS Function Code
AL       Number of Sectors
CH       Low Order Byte of Cylinder Number
CL       Cylinder and Sector Numbers
             Bits 7,6 High Order Cylinder Bits
             Bits 5-0 Sector Number
DH       Head Number
DL       Drive Number
ES:BX    Data Buffer Address

6.2.1 Physical to Logical Address Translation

As shown above, the starting sector address for read, write and verify requests 
is passed as a physical address including a 10 bit Cylinder Number, an 8 bit 
Head Number, and a 6 bit Sector Number. SCSI devices are addressed by logical 
block address without regard to the physical layout of the drive. For this 
reason, all SCSI devices are defined as drives with 64 heads and 32 sectors per 
track and with the appropriate number of cylinders to provide the full capacity 
of the drive using this physical to logical translation. The SCSI logical 
address is formed by the BIOS by concatenating the values as show below: 

Cylinder(10 bits) || Head(6 bits) || Sector(5 bits)=SCSI Logical Block Address

6.2.2 BIOS Command Return Codes

The BIOS command, when complete, returns control to the requesting program at 
the next instruction after the software interrupt. A return code is set in the 
Carry Flag (CF) and a status code is placed in register AH for examination by 
the requesting program.  The expected return codes placed in the Carry Flag are 
shown below. 

CF Contents at Return    Return Code
CF=1                     Status is non-zero. Unusual condition or error 
                         detected.
CF=0                     Status is zero. Normal command completion 	occurred.

AH Contents at Return    Status of Operation
AH = 00H                 No error:The operation completed successfully.
AH = 01H                 Invalid Function Request:	The operation code or  an 
                         associated parameter provided by the Interrupt 13 
                         operation was not valid.
AH = 02H                 Unable to Read Address Mark: One of the following 
                         additional sense codes (SCSI ASC) was presented in the
                         sense information returned by the REQUEST SENSE 
                         command:
                             12H (No AM Found on Data Field) 
                             21H (Illegal Logical Block Address) 
AH = 03H                  Write Protect Error:	Returned SCSI ASC was:
                             27H  (Data Protect)
AH = 04H                Read Error:Returned SCSI ASC during a read operation 
                        was:
                             14H  (No Record Found)
                             16H  (Data Sync Error)
AH = 10H                Uncorrectable ECC Error in Data:  Returned SCSI ASC 
                        during a read operation was:
                              10H  (ID ECC Error)
                              11H  (Unrecovered Read Error)
AH = 11H                ECC Corrected Data Error:Returned SCSI ASC during a 
                        read operation was:
                              17H  (Recovered Read Error w/o ECC)
                              18H  (Recovered Read Error w/ ECC)
AH = 20H                General Controller Failure:A host adapter detected 
                        failure occurred or one of the following SCSI ASC's 
                        was returned:
                              01H 08H 40H 46H
                              03H 09H 41H 47H
                              05H 1BH 42H 48H
                              06H 1CH 43H 49H
                              07H 1DH 44H

AH = 40H               Seek Operation Failed:  Returned SCSI ASC was:
                              15H  (Seek Positioning Error)
                              02H  (No Seek Complete)
AH = 80H               Selection Time-out: A host adapter does not respond to 
                       BIOS.
AH = AAH               Device Not Ready:Returned SCSI ASC was:
                              04H  (LUN Not Ready)
                              28H  (Unit Attention, Ready)
                              29H  (Unit Attention, Power On)
                              2AH  (Unit Attention, Mode Select Change)
AH = BBH               Unknown Target Sense Error Occurred: A SCSI ASC other 
                       than those specified above was returned from the 
                       selected SCSI device.
AH = CCH               Write Error:   Not Returned
H = FFH                Sense Operation Failed:BIOS unable to retrieve sense 
                       information from target.

6.3 BIOS DISK COMMANDS

The commands that can be accepted from the operating system by the BIOS include 
all those commands required for normal DOS operation, for booting of the DOS 
operating system, for the booting of other operating systems, and for basic 
maintenance and verification of normal disk operation. The command set is 
summarized in the following table and each command is described in more detail 
in the sections following. 

AH Register Meaning

00 H Reset Disk System
01 H Read Status of Last Operation
02 H Read Desired Sectors into Memory
03 H Write Desired Sectors from Memory
04 H Verify Desired Sectors
06 H Identify SCSI Devices
08 H Read Drive Parameters
09 H Initialize Drive Pair Characteristics
0C H Seek
0D H Alternate Disk Reset
10 H Test Drive Ready
11 H Recalibrate
15 H Read DASD Type

The Format commands (AH = 05, 06, 07, and 1AH) are not supported by the AHA-
1540A/1542A BIOS. The format operation is performed under a special format 
utility installed in ROM and initiated through the DEBUG program. 

The Diagnostic Reserved commands (AH = 0A, 0B, 0E, 0F, 12, and 14H) are not 
supported by the AHA-1540A/1542A BIOS. 

The Park Heads command  (AH = 19H) is not supported by the AHA-1540A/1542A 
BIOS. 

The Reserved for Diskette commands (AH = 16, 17, 18) and the commands from 1BH 
up to FFH are not supported by the AHA-1540A/1542A BIOS. Any attempt to execute 
any of these unsupported commands will be ended by the BIOS and an error code 
of  01H (Invalid Function Request) will be returned in the AH register. 


6.3.1 Reset Disk System

The BIOS is requested to reset the disk subsystem. A SCSI Reset operation is 
performed on the SCSI bus if the bus is busy at the time the Reset Disk System 
command is received by the host adapter. No other SCSI or host adapter activity 
occurs. The BIOS command is then passed on to the standard BIOS so that any 
internally installed hard disks and floppy disk devices can also be reset. If 
the BIOS is operating concurrently with an internally installed hard disk, the 
drive number is decremented by the AHA-1540A/1542A BIOS so that the standard 
BIOS does not attempt to reset the drive that is not installed. 

Input  Parameters:      AH = 00H
                        DL = Drive Number (80H or 81H)

Output Parameters:      AH = Status of Operation
                        CF =  Return Code

6.3.2 Read Status of Last Operation

The status of the last operation performed to the specified disk is returned. 
No SCSI activity occurs. The disk status is reset to zero. 

Input  Parameters:     AH = 01H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       CF =  Return Code

6.3.3 Read Desired Sectors Into Memory

The sectors requested by the parameters are read from the disk to the system memory. The SCSI command is executed as a READ (EXTENDED) command (SCSI Operation Code 28H). If the operation fails and an error is reported through the BIOS  status byte, the operation should be retried one time. If a 11 Error (ECC Corrected Data Error) is returned,  the data returned has been corrected and may be used with confidence. 

Input  Parameters:	AH = 02H
DL = Drive Number (80H or 81H)
DH = Head
CH = Cylinder
CL = High Cylinder and Sector
AL = Number of Sectors to Read
ES:BX = Address of buffer area

Output Parameters:  AH = Status of Operation
                    CF =  Return Code


6.3.4 Write Desired Sectors from Memory

The sectors requested by the parameters are written from the system memory to 
the indicated disk. The SCSI command is executed as a WRITE (EXTENDED) command 
(SCSI Operation Code 2AH). If the operation fails and an error is reported 
through the BIOS  status byte, the operation should be retried one time. 

Input  Parameters: AH = 03H
                   DL = Drive Number (80H or 81H)
                   DH = Head
                   CH = Cylinder
                   CL = High Cylinder and Sector
                   AL = Number of Sectors to Write
                   ES:BX = Address of buffer area

Output Parameters: AH = Status of Operation
                   CF =  Return Code

6.3.5  Verify Desired Sectors 

The sectors defined by the parameters are verified to be correctly written on 
the SCSI disk. The SCSI command is executed as a VERIFY command (SCSI Operation 
2F) with the Byte Check bit set to zero. If the VERIFY command is not supported 
by the selected disk, the Verify Desired Sectors will perform a SCSI READ 
command (SCSI Operation Code 28H) and throw away the received data. If the 
operation fails and an error is reported through the BIOS  status byte, the 
operation should be retried one time. 

Input  Parameters: AH = 04H
                   DL = Drive Number (80H or 81H)
                   DH = Head
                   CH = Cylinder
                   CL = High Cylinder and Sector
                   AL = Number of Sectors to Verify

Output Parameters: AH = Status of Operation
                   CF =  Return Code

6.3.6 Identify SCSI Devices

This is a special AHA-1540A/1542A BIOS call that is used to return the number 
of the first supported SCSI drive. In the  nonconcurrent case (2 SCSI drives), 
the returned value will be 80H. If only one SCSI drive is installed, the 
returned value will be 81H. 
 

 in the following table and each command is described in more detail 
in the sections following. 

AH Regi

Input  Parameters:	AH = 06H

Output Parameters: AH = Status of Operation
                   AL = First Drive Supported
                         80H Nonconcurrent operation
                         81H Concurrent operation
                   CF =  Return Code

6.3.7 Read Drive Parameters

A SCSI READ CAPACITY command is used to determine the maximum logical block 
of the selected drive. This information is then used to calculate the proper 
number of cylinders to be returned to the host system. The number of heads 
returned will always be 64 and the number of sectors per track will always 
be 32. The number of drives returned will include both internally installed 
drives and SCSI drives. 

Input  Parameters:AH = 08H
                  DL = Drive Number (80H or 81H)

Output Parameters:AH = Status of Operation
                  DL =  Number of BIOS accessible drives attached (1 or 2)
                  DH =  Maximum value for head number (3FH)
                  CH =  Maximum value for Cylinder Range (Low Byte)
                  CL =  Maximum value for Sector, High Cylinder Bits
                          Bits 7,6  	High Order Cylinder Bits
                          Bits 5-0 Sector Number Maximum Value ( 20H)
                  CF =  Return Code

6.3.8 Initialize Drive Pair Characteristics

This command performs no operation, since SCSI CCS drives are self 
configuring. 

Input  Parameters: AH = 09H
                   DL = Drive Number (80H or 81H)

Output Parameters: AH = Status of Operation
                   CF =  Return Code

6.3.9 Seek

A seek to the logical block address defined by the physical parameters is 
performed. The seek is performed using the SEEK (EXTENDED) command (SCSI 
Operation 2BH). The SEEK commands are not mandatory CCS commands and are not 
required for proper functioning of SCSI devices. If the addressed disk drive 
reports an error indicating that the SEEK (EXTENDED) command is not 
supported,  the BIOS command will complete normally anyway. Since the seek 
operation is performed automatically by a Read or a Write operation, there 
is no need to generate a separate seek operation to access data. 


Input  Parameters: AH = 0CH
                   DL = Drive Number (80H or 81H)
                   DH = Head
                   CH = Cylinder
                   CL = High Cylinder. (Sector bits = 0)

Output Parameters: AH = Status of Operation
                   CF =  Return Code


6.3.10 Alternate Disk Reset

The BIOS is requested to reset the disk subsystem. A SCSI Reset operation is performed on the SCSI bus if the bus is busy at the time the Reset

Input  Parameters: AH = 00H
                   DL = Drive Number (80H or 81H)

Output Parameters: AH = Status of Operation
                   CF =  Return Code

6.3.11 Test Drive Ready

The BIOS command determines that the specified drive is available and ready 
by executing a TEST UNIT READY command (SCSI Operation Code 00H) to the SCSI 
device. The command may have to be executed a second time if a Unit 
Attention condition was detected in the first execution of the TEST UNIT 
READY. 

Input  Parameters: AH = 10H
                   DL = Drive Number (80H or 81H)

Output Parameters: AH = Status of Operation
                   CF =  Return Code

6.3.12 Recalibrate

The BIOS command transmits a REZER0 UNIT command (SCSI Operation Code 01H) 
to the specified drive. Since the REZERO UNIT command is not a mandatory 
command and is not required for proper functioning of the SCSI device, the 
BIOS command will complete without indicating an error even if the SCSI 
device indicates that the command is invalid. 

Input  Parameters: AH = 11H
                   DL = Drive Number (80H or 81H)

Output Parameters: AH = Status of Operation
                   CF =  Return Code

6.3.13 Read DASD Type

The AHA-1540 BIOS executes this command by performing an INQUIRY  (SCSI 
Operation Code 12H) and a READ CAPACITY (SCSI Operation Code 25H) to the 
selected SCSI drive. The INQUIRY command is used to verify that the device 
is a Direct Access Storage Device. The READ CAPACITY is used to determine 
the number of logical blocks available. A special return format is used to 
obtain the required information. 

Input  Parameters: AH = 15H
                   DL = Drive Number (80H or 81H)

Output Parameters:AH = Status of Operation (Special Format)
                        00H  Drive not present or DL invalid
                        01H Reserved
                        02H Reserved
                        03H Fixed Disk installed

                  CX,DX  Number of 512 byte blocks available on disk
                  CF =  Return Code


7.1 PC/AT BIOS

The PC/AT BIOS is provided to allow the user to use the AHA-1540A/1542A in 
lieu of, or in addition to, a standard PC/AT hard disk controller. This 
compatibility includes booting from a SCSI device. Hard disk requests are 
sent to the BIOS via an INT 13 software interrupt. CPU register contents 
specify the desired I/O function and associated parameters. The BIOS then 
uses host adapter commands to emulate PC/AT functions. Again, since the 
mailbox architecture is circumvented, PC/AT BIOS functions run in a single-
threaded mode. 

The BIOS consists of three major functional components. These are: 

1. Initialization Routine
2. System Boot Routine
3. Hard Disk I/O Routine


7.1.1 Initialization

The Initialization routine is called at power-up. This routine performs all 
of the necessary initialization functions and will display the following 
message if the system successfully recognizes the AHA-1540A/1542A BIOS. 

ADAPTEC AHA-1540A/1542A HOST ADAPTER BIOS
COPYRIGHT 1987 ADAPTEC, INC.
ALL RIGHTS RESERVED.

If any subsequent initialization of the AHA-1540A/1542A fails, the following 
message is displayed: 

HOST ADAPTER NOT FOUND AT PORT 330H.

otherwise, the AHA-1540A/1542A BIOS chooses a course of action based upon 
the number and types of hard disks already installed. In each case, the 
number of hard disks already installed is displayed along with the ID 
numbers of any SCSI devices that are successfully used by the BIOS. 

Possible Messages:

HARD DISK #0 ALREADY INSTALLED.
HARD DISK #1 ALREADY INSTALLED.
HOST ADAPTER DIAGNOSTIC FAILURE.
SCSI DEVICE 0 : 0 NOT FOUND.
USING SCSI DEVICE 0 : 0 AS HARD DISK #0.
USING SCSI DEVICE 0 : 0 AS HARD DISK #1.
USING SCSI DEVICE 0 : 1 AS HARD DISK #1.
USING SCSI DEVICE 1 : 0 AS HARD DISK #1.

NOTE: No error message is displayed if a second SCSI drive is not available. 
If the system reports an initial number of hard drives greater than 2, the 
following message is displayed: 

SYSTEM CONFIGURATION ERROR.

The AHA-1540A/1542A BIOS allows the use of 0, 1, or 2 hard disks on the SCSI 
bus under DOS without a device driver. 

If 2 hard disks are attached to an internal hard disk controller, and are 
already recognized by the system, the BIOS does nothing. A device driver 
will be needed to access SCSI devices. 

If 1 hard disk is attached to an internal hard disk controller, and is 
already recognized by the system, the BIOS attempts to assign the SCSI 
device (Target : LUN) 0 : 0 as the second drive. (drive D:) If this is 
unsuccessful, an initialization error is reported to the system. 

If there are 0 hard disks attached to an internal controller, the BIOS 
attempts to assign the first SCSI device (Target : LUN) 0 : 0 as the first 
drive. (drive C:) If this is unsuccessful an initialization error is 
reported to the system. If successful, the BIOS attempts to assign another 
SCSI device as the second drive. (drive D:) Device 0 : 1 is tried first, and 
if that fails, device 1 : 0 is tried. There is no initialization error 
reported if a second drive is not available. 

7.1.2 System Boot

System boot is invoked by execution of an Interrupt 19. No interception of 
this interrupt is necessary, as the PC/AT BIOS manages the boot process. 
When the boot procedure attempts to read the boot track from drive C:, the 
AHA-154XA BIOS will respond if drive C: is a SCSI Drive. Only SCSI drive 0:0 
can be assigned as a SCSI C: drive. Mother board BIOS's that use interrupt 
13 to perform booting should boot normally from SCSI drives using the AHA-
154XA. 

7.1.3 Hard Disk I/O

The BIOS enables up to two SCSI drives to be accessed via interrupt 13 as 
described in Section 6. 

7.2 XENIX/UNIX Drivers

SCO Xenix and Unix, Interactive Systems Unix, and Microport Unix all support 
the AHA-1540A/1542A at the time of this publication. Please consult with 
these Operating System companies for more information on their products. 


7.3 DOS Driver

An optional DOS Driver is available that enables the AHA-1540A/1542A to 
access additional SCSI devices on the SCSI bus. When operating under DOS, a 
device driver is needed to access more than two hard disks, tape devices or 
other types of SCSI peripherals. In addition, DOS applications that use the 
virtual memory mode of the 80386 processor require this driver. If you are 
not running DOS programs that operate in the virtual 80386 mode, or if all 
DOS operations will be confined to two SCSI disks or one internal and one 
SCSI disk, a device driver is not needed because of the on-board BIOS. The 
DOS driver is installed by creating a DOS configuration (CONFIG.SYS) file 
that calls the device driver at boot time. Please refer to your DOS manual 
for information on creating a CONFIG.SYS file. At initial system loading, 
the AHA-1540A/1542A device driver will determine the number of hard disks 
attached to the system. The device driver is normally only installed if one 
of the following cases is true. 

1) There are two internal hard disks and one or more SCSI disks.
2) There is one internal hard disk and two or more SCSI disks.
3) There are no internal hard disks and more than two SCSI disks.


The following table shows how hard disks in a system are addressed:

      configuration                 c:           d:           device driver
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³two internal hard drives³  1st int. disk ³ 2nd int. disk ³  SCSI        ³
³                        ³                ³               ³  devices     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
³one internal hard drive ³  int. hard disk³  SCSI 0/0     ³ other SCSI   ³
³                        ³                ³               ³  devices     ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
³no internal hard drive  ³  SCSI 0/0 disk ³  SCSI 0/1     ³ other SCSI   ³
³                        ³                ³   or 1/0      ³  devices     ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The SCSI disk drives that are accessed by the device driver are divided into 
32 MB logical disks. There can be multiple logical disks on one physical 
SCSI disk drive. A utility program is also provided that performs the 
functions of the DOS FDISK and FORMAT utilities. This utility will perform 
FDISK and FORMAT to SCSI disks that can only be accessed through the device 
driver. These utility programs partition the disks and create file 
directories so that DOS files may be copied and accessed from SCSI drives. 
Please refer to your DOS manual for details of FDISK and FORMAT. 

SCSI 2 compatible and QIC 104 command set  1/4" tape drives are also be 
supported by the DOS device driver. The user accesses a SCSI tape drive by 
building a CCB as described in Section Five. The device driver passes the 
CCB to the AHA-1540A/1542A and instructs the AHA-1540A/1542A to complete the 
command. Software products such as Sytron Corporations SYTOS Tape Operating 
System automatically interface to the Adaptec AHA-1540A/1542A DOS driver. 

To install the driver into your boot routine, you must create, or edit the 
DOS configuration file named CONFIG.SYS. You can use any file editor to do 
this, or you can create it through the "COPY CON: CONFIG.SYS" DOS command. 
Refer to your  DOS manual for more information on this command. Once 
installed, the driver operates transparently to the user. 

7.3.1 DOS Driver Support of Virtual Mode

The use of high performance 16-bit Bus Master DMA on the AHA-1540A/1542A 
SCSI host adapter may result in incompatible operation with application 
programs that use the 80386 virtual memory mode of operation. 

In real mode, the host adapter BIOS is passed a physical address. This is 
necessary since the host adapter controls all SCSI I/O without CPU 
intervention. This physical address may not be passed to the host adapter 
when the system is in the V86 mode. Programs that use the V86 mode can only 
be run on 80386 machines. 

The AHA-1540A/1542A DOS driver also allows this type of application program 
to run under DOS. 

7.4 AHA-1540A/1542A On-board Utilities

The AHA-154XA BIOS contains a utility program that allows the user to 
perform the several important functions. The utility programs are accessed 
using a self explanatory menu. 

The utilities are accessed using the DOS Debug function. To access the 
utilities, boot using a standard DOS system disk or diskette. When the DOS 
prompt symbol appears on the screen, enter the debug program by typing debug 
and pressing Enter. The debug program will load and present a new cursor, 
the - symbol. Enter the following line and press enter to invoke the On-
board Utility program. 

          G=dc00:6

If a BIOS base address other than DC000H is being used on the adapter to be 
tested, replace the dc00 parameter with the actual BIOS base segment. The 
segment is the upper 16 bits of the 20 bit BIOS base address. 

The menu options include the following items which are selected by pressing 
the index number of the menu function. 

(1)  A list of all devices installed on the SCSI bus may be requested. This 
information is retrieved via a RETURN INSTALLED DEVICES host IOCP command, 
followed by INQUIRY commands to all available targets. 

(2) A device may be selected for execution of the following two functions. 
Pressing the '2' key toggles the selection from one installed device to the 
next. 

(3) A low level, or primary, format of the selected Target/LUN can be 
requested. A MODE SELECT is issued first to set the block size at 512 bytes 
per sector. Then a FORMAT command is issued which will format the drive with 
factory as well as grown defects.  Only one SCSI drive can be formatted at a 
time. 

(4) Integrity of a target can be checked by verifying an entire drive. Any 
correctable errors found will automatically be handled through the SCSI 
Reassign Blocks Command. If any uncorrectable errors are found the user will 
first be asked via a screen prompt if reassignment of the effected block 
should be performed. 

(5) The user can leave the AHA-154XA On-board Utility functions and return 
to normal DOS operation. 


In addition to the On-Board Utilities, a DMA channel test also resides on 
the AHA-154XA BIOS. The test verifies that all DOS-available memory can be 
accessed correctly from the host adapter using first party DMA. The test 
takes from 2 to 10 minutes to execute, depending on the CPU speed and the 
amount of memory available. The test is invoked by entering the debug 
program as above and entering: G=DC00:9 

The program then is activated and verifies each segment of the memory, 
indicating with screen messages as each segment is verified. The test runs 
indefinitely or until an error is detected. In most cases of error, the 
error information cannot be presented since the host operating system is 
likely to be compromised. The error symptom is usually a system crash. The 
test is halted by rebooting. 


8.0 SCSI FEATURES

8.1 SCSI DESCRIPTION, INITIATOR MODE

The AHA-1540A/1542A provides a very high performance SCSI interface 
connection. The host adapter meets the ANSI Standard X3.131-1986, describing 
the SCSI. The host adapter additionally meets conformance level 2 of the 
specification by implementing the following SCSI options: 

Accepts or manages the following messages:

  Command Complete
  Disconnect	
  Message Reject
  Identify
  Save Data Pointer

 Performs arbitration

The following alternatives are selected for the AHA-1540A/1542A SCSI 
interface connection from those described by X3.131-1986. 

Single-ended SCSI driver/receivers are used. 

The Termination Power is supplied through a removable fuse, allowing the 
user to select whether or not termination power is provided by the host 
adapter at installation time. 

Parity is always generated. Parity checking can be disabled through the 
jumper selection. 

The "Soft" Reset option is always performed by the AHA-1540A/1542A. If the 
user desires the "Hard" Reset, an interrupt servicing program that detects 
the SCSI Reset Detected interrupt in the Interrupt Flags Port must set the 
Soft Reset bit in the Control Port. This bit forces the host adapter to 
clear all SCSI related operations, but does not require execution of the 
diagnostic functions. If the Soft Reset bit has been set, the host software 
must re-initialize the AHA-1540A/1542A. 

Synchronous data transfer is supported. Negotiation for the synchronous 
transfer initiated by another SCSI device will be accepted by the AHA-
1540A/1542A at any time. If the jumper has been set to allow it, the AHA-
1540A/1542A will also initiate synchronous data transfer negotiation when it 
has detected that  such negotiation may be required. 

Multitasking is fully supported. 

Modify Data Pointers is supported to allow Zero Latency Read operations. 
In addition to these SCSI functions, the SCSI Common Command Set at level 4B 
is also supported. While this document was never made a standard, it 
describes a widely available set of disk drive functions which are supported 
by the host adapter. The Host Adapter BIOS commands are all mapped in to 
SCSI CCS commands to allow the proper support of all the most common SCSI 
disk drives. The Adapter Command "Return Installed Devices" also uses CCS 
commands to determine which devices are available. 

The draft ANSI standard for SCSI-2 has been used as a reference for the 
implementation of all SCSI functions with the expectation that the host 
adapter will be fully compatible with the final version of the SCSI-2 
standard. In particular, the Processor type device command set has been 
selected from the SCSI-2 manual for Target Mode operation. 


8.1.1 Linked SCSI Commands

The AHA-1540A/1542A supports linking of SCSI commands in initiator mode. 
When the link bit in the SCSI command control byte is set, the target will 
present either a 0A or 0B message at command completion. The AHA-1540A/1542A 
uses the the link pointer in a CCB to fetch another CCB. At the same time, 
the completed CCB status and address are stored in an MBI. If the target 
returns a 0B or 00 message, the AHA-1540A/1542A generates an interrupt to 
inform the host of the full MBI. If the target returns a 0A message, the 
MBIF interrupt is not posted until all linked commands are completed. The 
linked CCBs must address the same target and LUN since the target is not re-
selected. 

8.1.2 Zero Latency Read Operation

The AHA-1540A/1542A implements Zero Latency operation through the use of 
modify data pointer messages. Zero Latency can eliminate rotational latency, 
depending on the length of the data transfer, by supporting out of order 
data transfers. This advanced feature is currently only implemented on the 
ACB-4525Z SCSI to ESDI controller, and is supported transparently to the 
user. 

Since the Adaptec host adapter family is the first to support Zero Latency 
Read operation, this section is intended to briefly explain the required 
target support. Please refer to the Adaptec ACB-4525Z SCSI to ESDI 
controller manual for complete details of Zero Latency Read operation. 

After seeking to the target track, the ACB-4525Z (ACB-4525Z is assumed since 
it is the first SCSI controller to implement this feature) will begin 
reading block IDs. If the first block ID is within range of the data 
transfer, but not the last block of the the data transfer, the ACB-4525Z 
will begin reading the subsequent blocks into its buffer. Before 
transferring data the ACB-4525Z will issue a MODIFY DATA POINTER message to 
the AHA-1540A/1542A. This supplies a positive argument that is added to the 
value of the current data pointer. The ACB-4525Z will now send this portion 
of the data transfer to the host. The ACB-4525Z will resume reading data 
into its buffer as soon as the first block of the data transfer is detected. 
Before sending this data to the host, the ACB-4525Z will issue a second 
MODIFY DATA POINTER message to the AHA-1540A/1542A which supplies a negative 
argument. This returns the data pointer to its original position. This 
guarantees that a data transfer of one track or less will never require more 
than a single revolution since data can now be transferred out of order. 

8.1.3 SCSI Messages 

The AHA-154XA host adapter supports a number of special messages in addition 
to the messages required by meeting conformance level 2. Those messages are 
described in detail in the SCSI specification, X3.131-1986, and in this 
section where they are used. The messages are summarized in this table: 

FUNCTION                MESSAGE                   CAUSED BY

 Standard Messages      Command Complete          Normal Sequencing

 Error Management       Message Reject            Invalid Messages
                        Bus Device Reset          Special CCB
                        Abort                     Special MBO

Disconnect / Reconnect  Identify                  Normal Sequencing
                        Disconnect                Normal Sequencing
                        Save Data Pointer         Normal Sequencing
                        Restore Pointers          Special Sequencing/ZLR

Synchronous Transfer    Synchronous Data Transfer Initialization Sequencing
                        Request

Zero Latency Operation  Modify Data Pointers      ZLR Sequencing

Linked Commands         Linked Command Complete   Command Linking
                        Linked Command Complete   Command Linking
                        With Flag


8.2 SCSI DESCRIPTION, TARGET MODE


8.2.1 Initiator Conformance Level Requirements

Initiators that  execute commands against an  AHA-1540A/1542A operating in 
Target Mode are required to have the following conformance levels, as 
described in Appendix E of the SCSI  Specification, ANSI  X3.131-1986. 
Conformance must be present  with respect to each of the following items: 

The  initiator must use single-ended drivers. 

Termination power may optionally be provided by the initiator, but must meet 
the SCSI specification  in both its over-current protection and its  reverse 
current diode protection.  The terminators may be  installed on the AHA-
1540A/1542A board or  installed as in-line terminators at the cable 
connectors. 

The implementation of parity is optional, but desirable. The  initiator may 
support either "hard" reset or "soft" reset. All attached devices must 
support the same type of reset. 

The initiator must meet the requirements of conformance level two. In 
particular, all LUN addressing must be performed by the IDENTIFY message, 
not by the  LUN field in the CDB. Disconnection and reconnection must be 
supported. 

The initiator and target functions have the same SCSI ID. 


8.2.2 Support of Synchronous Transfer

Synchronous transfer is supported by the AHA-1540A/1542A in target mode 
without any instruction or support from the system processor. If an 
initiator  invokes a synchronous transfer negotiation, the AHA-1540A/1542A 
will complete the negotiation of the required transfer offset and period. If 
the proper jumper has been set, the AHA-1540A/1542A will also attempt to 
negotiate synchronous transfer during the initial selection period of the 
first command after an initialization or after a SCSI reset. 


8.2.3 SCSI Target Operation in Processor Target Mode

When the AHA-1540A/1542A has been set to respond in Processor Target Mode, 
the host adapter appears on the SCSI bus as a normal processor type device 
as defined by the SCSI specification. From one to eight LUN's may be 
supported, depending on the LUN mask byte in the Enable Target Mode command.  
Five SCSI commands are accepted: 

    TEST UNIT READY	
    REQUEST SENSE	
    INQUIRY	
    SEND
    RECEIVE

All other commands are rejected with CHECK CONDITION status. The sense 
information will indicate a Sense Key of 05H (Illegal Request) with a Sense 
Code of  20H (Invalid Command Operation Code). 

The commands that do not perform data transfer to or from the host are 
handled completely by the AHA-1540A/1542A with no CCB communication with the 
host system. Those commands are the TEST UNIT READY, REQUEST SENSE, and 
INQUIRY commands. The SEND and RECEIVE commands must have a CCB from the 
host with the proper direction bits, the proper initiator address, and the 
proper LUN number to complete the SCSI operation. The SEND and RECEIVE CCBs 
may be provided to the host adapter before a command is received on the SCSI 
or may be requested after the command is received. 

Each time an initiator activates a command to the AHA-1540A/1542A, an 
internal sub-channel is activated to manage the command. The sub-channel is 
dedicated to that particular LUN-Initiator transaction until all operations 
associated with the command are completed. Such operations include 
disconnection to obtain a CCB,  pending error conditions, and linked 
operations. If all sub-channels are busy, a selection to the AHA-1540A/1542A 
will result in the AHA-1540A/1542A accepting the command and then generating 
BUSY status immediately. If this occurs, the initiator must re-issue the 
command later.  

8.2.3.1 TEST UNIT READY
     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³  Ãtest unit ready code(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃLUN(unused=0)ÄÄ´ÃÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  4  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  5  ³  ÃÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÃflag´Ãlink´³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


The TEST UNIT READY command follows the SCSI specification in all respects. 
If the AHA-1540A/1542A has been initialized by the Enable Target Mode 
command to the Processor Target Mode, the command will finish normally with 
GOOD status and a COMMAND COMPLETE message. The host adapter supports the 
normal definition of UNIT ATTENTION on the first operation after power on, 
after a SCSI Reset, or after a BUS DEVICE RESET. 

If a TEST UNIT READY command is executed against an LUN which was not 
allowed by the Enable Target Mode command, then CHECK CONDITION status will 
be presented with sense data of Sense Key 5 (Invalid Request) and an Error 
Code of 25H (Invalid LUN). 


8.2.3.2 REQUEST SENSE

     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³  Ãrequest sense operation code (03h)ÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃLUN(unused(00)Ä´ÃÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  4  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  5  ³  ÃÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÃflag´Ãlink´³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


If the AHA-1540A/1542A has returned CHECK CONDITION status to a previous 
command, the REQUEST SENSE command will obtain the sense information 
associated with the error. The sense information will be sent in the 
extended sense format according to the SCSI standard. The data format is 
given in the following figure: 


     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³  Ãerror code(07h orf0h)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄ00ÄÄÄÄ´Ãilf´ÃÄÄ0ÄÄ´ÃÄÄsense keyÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3- ³  ÃÄÄÄÄÄÄÄÄÄÄÄinformation bytesÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ³                                              ³
  6  ³  ÃÄÄÄÄÄÄÄÄÄÄÄ(residue)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  7  ³  ÃÄÄÄÄÄÄÄÄÄadditional sense bitsÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  8- ³  ÃÄÄÄÄÄÄÄÄÄreserved(00000000h))ÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ³                                              ³
 11  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
 12  ³  ÃÄÄÄÄÄÄÄÄÄadditional sense codeÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
 13  ³  ÃÄÄÄÄÄadditional sense code qualifier(00h)Ä´³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


The following errors are detected and presented by the AHA-1540A/1542A while 
operating in Processor Target Mode: 

Error                         Sense      Additional Sense
                               Key               Code

No Sense Data                   00                00
Invalid Command Operation Code  00                20
Invalid LUN                     05                25 
Invalid Command Parameter       05                26
Power Up Attention              06                29
Reset  Attention                06                29
Interface Parity Error          0B                47
Initiator Detected Error        0B                48
Dumb Initiator                  05                2B


One set of error data may be buffered for each initiator - LU association 
possible, up to a total of 56 sets of sense data. No Contingent Allegiance 
or Extended Contingent Allegiance state is established. 

The Error Code (Byte 0) will be F0h if the residue field is valid and 70h if 
the residue field has no information. 

The Incorrect Length Indicator (ILI) will be set if an incorrect data 
transfer length is executed as described in Section 8.2.4. 

The residue is set equal to the transfer length requested in the initiator 
CDB minus the target host's specified data length specified as a four-byte 
two's complement number. 

8.2.3.3 INQUIRY

     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³  ÃInquiry Operation code(12h)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃLUN(unused=00)Ä´ÃÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  4  ³  ÃÄÄÄÄÄÄÄÄÄÄÄAllocation lenthÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  5  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÃflag´Ãlink´
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


The INQUIRY command provides the information necessary to uniquely identify 
the Adaptec AHA-1540A/1542A as a Processor-type device. The information is 
returned in the SCSI-2 format. The following information is returned to any 
selecting initiator from any selected AHA-1540A/1542A Logical Unit: 

     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³Peripheral qual'er´Ãprocessor device type(03h´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄ´Ã ansi ver(02)Ä´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3  ³  ÃÄÄÄÄÄÄÄÄResponse data format(02h)ÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  4  ³  ÃÄÄÄÄÄÄÄÄÄÄÄAdditional lenth(1Dh)ÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  5  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  6  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  7  ³ ÃÄ0ÄÅÄÄ0ÄÄÅÄÄ0ÄÄÄÅsyn=1³lnk=1ÃÄ0ÄÅÄÄ0ÄÄÅÄÄ0Ä´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  8- ³  ÃÄÄÄVendor Identification(ascII)ÄÄÄÄÄÄÄÄÄÄÄ´³
     ³                                              ³
 15  ³  ÃÄÄÄÄÄÄÄÄÄAdaptec bbbÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
 16- ³  ÃÄÄÄÄProduct identification(asc11)ÄÄÄÄÄÄÄÄÄ´³
     ³                                              ³
 31  ³  ÃÄÄÄÄÄÄÄÄAHA-1540bbbbbbbbÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
 32- ³  ÃÄÄÄÄProduct Revision level(asc11)ÄÄÄÄÄÄÄÄÄ´³
     ³                                              ³
 35  ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

If the INQUIRY command is attempted against a Logical Unit that has not been 
enabled as a target, byte 0 is returned as 23h, indicating that the LUN is 
not installed, but would be a Processor Device if it were installed. The 
remaining bytes are returned normally. 

If a length shorter than the required 36 bytes is specified by the INQUIRY 
command, the number of bytes specified by the command is transferred. If a 
length longer than 36 bytes is specified, the command will only transmit 36 
bytes. 


8.2.3.4 SEND


     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³  ÃÄÄÄÄSend Operation code 0A)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃLUN(unused=00)Ä´ÃÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄÄÄÄTransfer lenth(msb)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3  ³  ÃÄÄÄÄÄÄTransfer lenthÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  4  ³  ÃÄÄÄÄÄÄTransfer lenth(lsb)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  5  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÃflag´Ãlink´
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The SEND command has the format specified by the SCSI standard. 

The SEND command transfers data from the initiator to the target. The 
information is placed in the area specified by the appropriate CCB. If an 
appropriate CCB has not already been provided to the host adapter by the 
host software, an MBI entry requesting the appropriate CCB is sent to the 
host from the host adapter. In this case, the target host adapter 
disconnects from the SCSI until the CCB is made available to the host 
adapter through the MBO protocol. An appropriate CCB must have the same 
initiator address, target LUN, and direction as is required to complete the 
command. 

The transfer length  in the SEND command specifies the length in bytes of 
data that is sent during the DATA OUT phase. A transfer length of zero 
indicates that no data is sent.  Management of incorrect length transfers is 
described in Section 8.3.2.6. 

The CDB information is included in the returned CCB so that the receiving 
host programming can determine whether or not the information transmitted by 
the SEND command was application data or asynchronous event notification 
data. 

8.2.3.5 RECEIVE

     bit 7     6     5     4     3    2    1    0
 byteÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  0  ³  ÃÄÄÄÄReceive Operation code(08h)ÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  1  ³  ÃLUN(unused=00)Ä´ÃÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  2  ³  ÃÄÄÄÄÄÄAllocation lenth(msb)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  3  ³  ÃÄÄÄÄÄÄAllocation lenthÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
  4  ³  ÃÄÄÄÄÄÄAllocation lenth(lsb)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´³
     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´     
  5  ³  ÃÄÄÄÄÄÄÄÄÄÄÄreserved(00)ÄÄÄÄÄÄÄÄÄÃflag´Ãlink´
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The RECEIVE command has the format specified by the SCSI standard 

The RECEIVE command transfers data from the target to the initiator. The 
information is taken from the area specified by the appropriate CCB. If an 
appropriate CCB has not already been provided to the host adapter host 
software, an MBI entry requesting the appropriate CCB is sent to the host 
from the host adapter. In this case, the target host adapter disconnects 
from the SCSI until the CCB is made available to the host adapter through 
the MBO protocol. An appropriate CCB must have the same initiator address, 
target LUN, and direction as is required to complete the command. 

The transfer length  in the RECEIVE command specifies the length in bytes of 
data that is sent during the DATA IN phase. A transfer length of zero 
indicates that no data is sent. Management of incorrect length transfers is 
described in section 8.3.2.6. 


8.2.4 Incorrect Length Management for Target Mode Operation

The messages transmitted using the SEND and RECEIVE commands are normally 
expected to have a length that has previously been agreed to by the 
initiator system software and by the target system software. If the transfer 
length specified by the command is equal to the transfer length specified by 
the CCB,  normal operation takes place and no errors are posted. 

If the transfer length specified by the initiator's command is shorter than 
the space defined by the target CCB, all data bytes expected and required by 
the initiator will be transmitted. The target AHA-1540A/1542A will indicate 
GOOD status on the SCSI at the end of the transfer. The target system's 
software however must be notified that the entire area of data defined by 
the CCB was not transmitted. A  Target Status of GOOD will be presented in 
the returned CCB. At the same time,  the Incorrect Length Indication bit  
(bit 5 of byte 2) will be set in the CCB Request Sense data area. Bytes  3 
through 6 of the Request Sense data area will contain the residue in two's 
complement notation of the length requested in the initiator command minus 
the length of the data area defined by the CCB. In this case, the residue 
will be a negative number, since the requested length was less than the area 
specified by the CCB. The HA status stored in the CCB will be 12h, 
indicating a Data Over/Under Run. The MBI Status Byte will be set to 04 to 
indicate that the CCB was completed with an error. If the transfer length 
specified by the initiator's command is longer than the space defined by the 
target CCB, only those bytes contained within the CCB's data transfer area 
will be transmitted. The target AHA-1540A/1542A must indicate with an error 
condition to the initiator that not all the requested bytes could be 
transferred. The target AHA-1540A/1542A presents a SCSI status of CHECK 
CONDITION at the end of the data transfer. The Request Sense information 
transmitted to the initiator as a result of an immediately following REQUEST 
SENSE command indicates that an Incorrect Length Indication is present by 
setting bit 5 of byte 2. Bytes 3 through 6 of the Request Sense information 
transmitted to the initiator will contain the residue in two's complement 
notation of the length requested in the initiator command minus the length 
of the data area defined by the target CCB. In this case, the residue will 
be a positive number, since the requested length was greater than the 
available area. The target system's software must also be notified that the 
transfer length requested by the initiator exceeded the assigned buffer 
area. A Target Status of CHECK CONDITION will be presented in the returned 
target CCB. A Host Status of '12'h will be returned indicating a Data 
Over/Under Run. At the same time, the information that will later be posted 
to the initiator by the REQUEST SENSE command will be posted to the target 
system in the CCB Request Sense data area. This includes both the Incorrect 
Length Indicator and the Residue. The MBI Status Byte will be set to 04 to 
indicate that the CCB was completed with an error. 


9.1 FLOPPY DISK INTERFACE

The floppy disk controller allows the attachment of any standard IBM 
compatible floppy disk drive to the AHA-1542A. The floppy disk controller is 
accessed by the standard IBM compatible BIOS through the standard IBM 
compatible floppy diskette program interface. The floppy disk controller 
section of the host adapter is completely independent of the host adapter 
function. The floppy disk controller section can be disabled by removing 
jumper J13 as described in section 3.4.2. The base address and interrupt and 
DMA channels can be modified by jumpers as described in section 3.4. 

A floppy disk is attached to the host adapter using a 34 pin ribbon cable 
connector as specified in section 1.4. The pin out of the cable is described 
here, although that is usually not necessary, since all standard floppy disk 
drives have the same pin out. Some systems choose to use the same address 
for all floppy disk drives and to twist the cable, pins 10-16, to switch the 
address lines at the drive. 


Signal Name       Pin      Pin      Signal Name        

Ground             1        2           -LD
Ground             3        4        Reserved
Ground             5        6        Reserved
Ground             7        8        -INDEX
Ground             9       10        MOTOR ENB DRIVE A

Ground             11      12        DRIVE SELECT B
Ground             13      14        DRIVE SELECT A
Ground             15      16        MOTORO ENB DRIVE B
Ground             17      18        -DIRECTION
Ground             19      20        -STEP

Ground             21      22        -WRITE DATA
Ground             23      24        -WRITE ENABLE
Ground             25      26        -TRACK 0
Ground             27      28        -WRITE PROTECT
Ground             29      30        -READ DATA

Ground             31      32        -HEAD SELECT
Ground             33      34        -DSKCHNG


10.0 PROBLEM DETERMINATION


10.1 Self Diagnostic Capability

The AHA-1540A/1542A executes self diagnostics upon power up or after a hard 
reset. These diagnostics test the CPU operation, perform a sum check on the 
EPROM, and check the data transfer paths on the board. The host system has 
the option of exercising more extensive diagnostics involving reads and 
writes to memory. 

The red light emitting diode (LED) on the host adapter indicates the result 
of the self diagnostic process.  When power is first applied to the board, 
the LED turns on. If the board is operating normally, the light will soon go 
off and stay off until SCSI or I/O port activity is requested by the host. 
If the board is not operating correctly,  a flash code number is flashed on 
the LED to indicate which test failed. The flash code number is indicated by 
a series of 1 to 6 closely spaced flashes followed by a longer pause. The 
flash code is repeated continuously until the board is powered off, reset, 
or repaired.  The SCSI interface should be disconnected if these diagnostic 
tests are being run for fault isolation purposes. At least one set of 
terminators must remain installed or the LED will stay on, indicating that 
the AHA-154XA is receiving an active RST signal. Continuous execution of the 
diagnostics can also be forced by inserting the diagnostic jumper (pin-pair 
2 in jumper J1). The flash code and associated failure modes are indicated 
in the following table. 


TABLE OF FLASH CODES


FLASH CODE    POSSIBLE MEANINGS OF FLASH CODE

LED           Remains On Host Adapter Control Processor 
              inoperative/terminators missing or not powered. 

1 Flash       Firmware EPROM check sum failed.

2 Flashes     RAM test failed.

3 Flashes     AIC-6250 SCSI protocol chip verification failed

4 Flashes     FIFO read data path test failed.

5 Flashes     FIF  write data path test failed.

6 Flashes     Channel 2 test failed.

If any of these failure conditions is identified, the host computer should 
be powered down, the host adapter removed, and the host adapter inspected 
for physical damage. Such damage can include EPROM's that are not correctly 
installed or not firmly seated, broken wires, missing or damaged components,  
or conductive debris on the board. If no such physical damage is found, the 
AHA-154XA should be returned for repair. 

All boards are fully tested, burned in,  cleaned, and inspected before they 
are shipped. Care should be taken to keep the board in its protective 
conductive wrapping until it is installed. With these simple precautions, 
mechanical damage can normally be avoided. 


10.2 INDICATORS

The red light emitting diode (LED) on the AHA-154XA is used to provide the 
fault isolation information described above. In addition, the LED indicates 
when the host adapter is performing activities on the host interface and the 
SCSI interface. The LED is such a useful activity indicator that a connector 
is made available on the host adapter to allow the cable to an externally 
visible LED to be attached. (See Section 3.3.9). 

As an activity indicator the LED is turned on from the time that an Adapter 
Command is transmitted to the host adapter until the HACC interrupt is 
generated to indicate that the Adapter Command is complete. In addition, the 
LED will be turned on whenever SCSI bus activity is occurring. This is 
roughly the same period of time that the SCSI BSY signal is present on the 
SCSI bus. If the light stays on when no activity is expected to be present 
on the bus, it is possible that the bus is hung, the processor has failed, 
that unexpected activity is occurring, or that the SCSI cables are 
incorrectly installed. If the SCSI cables are installed reversed, the host 
adapter is forced in to a solid SCSI reset state which halts normal 
operation. 


10.3 PROBLEMS DETECTED DURING OPERATION

The information in section 10.3 is not intended for routine users of the 
AHA-1502A/1542A. It is intended to provide a reference for programmers 
preparing device drivers, error recovery procedures, and error information 
presentation programs. 

Operation of the I/O Port interface is controlled and monitored by host 
system software. Two bits in the Status Port (Base + 0), described in 
section 4.2.1, are provided to indicate unusual conditions in the host 
adapter. 

Internal Diagnostic Failure (Status Port, bit 6): This bit indicates that 
the self testing process after either a hard reset or a power on operation 
was terminated by an error condition. The error indicates that a critical 
failure was found in the AHA-154XA control circuitry or data paths.   The 
error should be presented to the host video display to indicate that 
diagnostic actions are required. The diagnostic action uses the host adapter 
diagnostic flash codes to determine if the AHA-154XA is failing. The host 
system should be powered off, then opened so that the LED can be observed. 
All SCSI cables, both external and internal, should be removed from the host 
adapter. The system should then be powered on. If the LED flashes once and 
turns off, the host adapter has passed its diagnostics and should be 
accessible again. If the LED flashes one of the error flash codes, the AHA-
154XA  should be replaced. If the LED remains on and does not turn off, the 
host adapter is not able to begin operation at all. The host system may be 
holding the AHA-154XA in the reset state or the host adapter may have 
failed. To distinguish these two cases, the AHA-154XA should be replaced and 
the new host adapter operation should be verified. Be sure to power down the 
host system when removing or replacing the host adapter. If the diagnostics 
indicate that the AHA-154XA must be replaced, it should be sent to an 
authorized service facility for repair. 

Invalid Host Adapter Command (Status Port, bit 0):  This bit is set to 
indicate that a command or parameter transmitted to the host adapter was 
invalid.  This is an indication that the host software, usually an operating 
system, special application program, or device driver, has generated an 
invalid request. The responsible programming organization should be notified 
so that the invalid sequence or parameter can be corrected. 


10.3.1 HA Status Error Indications and Corrective Actions

The Host Adapter Status indications, in addition to indicating several 
normal completion states, indicate three general groups of errors. One set 
describes software errors in the requests made to the host adapter. Even 
though most of these errors are caused by software design problems, the AHA-
154XA may need to be replaced as an isolation step, since there exists a 
small chance that hardware failures in the AHA-154XA cause the appearance of 
a software error. 

A second set describes errors detected by the host adapter firmware in the 
host adapter hardware. The most likely failing component in this case is the 
AHA-154XA, although certain system or cable failures may generate the 
appearance of a host adapter hardware error. 

A third set describes the appearance of unexpected or incorrect sequences 
executed by the attached SCSI devices. In this case, the cables are the most 
likely failure point, with the peripheral device second and the AHA-154XA 
third. The host adapter status code should be returned to the host video 
display to indicate to the operator what errors have occurred and under what 
conditions the errors occurred. The following section describes those Host 
Adapter Status indications that indicate an error. 

NUMBER TYPE ERROR   DESCRIPTION AND CORRECTIVE ACTION

11     SCSI NO      Selection Time Out: The SCSI attempted to select a 
                    device that was not installed or that did not respond to 
                    selection due to a power, parity or addressing failure. 
                    Verify correct address values set to SCSI devices. 
                    Verify that SCSI cable routing includes the required 
                    devices. Verify  SCSI cable integrity by replacement of 
                    cables. Verify that SCSI Selection Time Out value has 
                    been correctly established by Adapter Command. 

12     HOST NO      Data Over Run / Under Run: Data length or direction 
                    specified by CCB did not agree with the data length 
                    actually provided by the attached peripheral device. 
                    Often a normal error or accompanied by a check condition 
                    indicating transfer truncation. Verify program requested 
                    correct length or direction. Verify peripheral provided 
                    expected data length, number of blocks, or block length. 

NUMBER TYPE ERROR   DESCRIPTION AND CORRECTIVE ACTION


13     SCSI  YES    Unexpected Bus Free: The target dropped BSY without 
                    executing the proper messages first. This normally 
                    indicates that the BSY and/or other portions of the SCSI 
                    bus failed or that the target encountered such an 
                    invalid sequence that no recovery was possible. Some 
                    targets may have sense information available to qualify 
                    the error condition. Verify SCSI cable integrity. Verify 
                    SCSI cables are all properly connected. Replace SCSI 
                    cables. Replace peripheral. Replace AHA-154XA. 

14     SCSI  YES    Target bus phase sequence failure:	The initiator detected 
                    an invalid phase or an invalid phase sequence. If this 
                    occurs, it is likely that the host adapter forces a SCSI 
                    reset on the bus as the first phase of the recovery 
                    process. Verify SCSI cable integrity. Verify SCSI cables 
                    are all properly connected. Replace SCSI cables. Replace 
                    peripheral. Replace AHA-154XA 

15     HOST  YES    MBO Command Byte invalid:	This indicates a software 
                    failure or bug in the host's development of the MBO 
                    entry. Generally, this indication will only occur during 
                    initial debug processes of new operating systems. 
                    Replace the AHA-154XA. Replace the host computer system. 
                    Contact the software developer for design support. 

16     HOST  YES    Invalid CCB Operation Code:	This indicates a software 
                    failure or bug in the host's development of the CCB. 
                    Generally, this indication will only occur during 
                    initial debug processes of new operating systems. 
                    Replace the AHA-154XA. Replace the host computer system. 
                    Contact the software developer for design support. 

17     HOST  YES    Linked CCB does not have same LUN:  This indicates that 
                    the host software generated an invalid combination of 
                    link commands. Generally, this indication will only 
                    occur during initial debug processes of new operating 
                    systems. Replace the AHA-154XA. Replace the host 
                    computer system. Contact the software developer for 
                    design support. 

NUMBER TYPE ERROR    DESCRIPTION AND CORRECTIVE ACTION

18     HOST  YES    Invalid Target Direction Parameters received from Host:  
                    This indicates that the host software generated an 
                    invalid Target Direction Parameter. Generally,  this 
                    indication will only occur during initial debug 
                    processes of new operating systems. Replace the AHA-
                    154XA. Replace the host computer system. Contact the 
                    software developer for design support. 

19     HOST YES     Duplicate CCB Received in Target Mode: This indicates 
                    that the host system was not keeping correct management 
                    information for target mode operation and incorrectly 
                    generated a second CCB identical to one already active. 
                    Generally,  this indication will only occur during 
                    initial debug processes of new operating systems. 
                    Replace the AHA-154XA. Replace the host computer system. 
                    Contact the software developer for design support. 

1A     HOST YES     Invalid CCB Parameter or Segment List: A segment list 
                    was presented to the host adapter with a zero length 
                    segment or invalid segment boundaries. An invalid CCB 
                    parameter was presented to the host adapter. 
                    Generally,this indication will only occur during initial 
                    debug processes of new operating systems. Replace the 
                    AHA-154XA. Replace the host computer system. Contact the 
                    software developer for design support. 


10.3.2 SCSI Error Indications and Corrective Actions

Error conditions detected by SCSI peripherals usually cause a CHECK 
CONDITION Status byte to be presented. When this is presented, the host 
adapter automatically retrieves the sense information from the SCSI 
peripheral by executing a REQUEST SENSE command according to the SCSI 
standard. The information returned is mapped for single-threaded BIOS 
operation into the categories of error conditions described in section  
5.2.2. For multitasking (mailbox) operation, the information returned is 
made available in the area allocated for Sense Data. In either case, an 
intelligent attempt is made by most operating systems to retry the operation 
at least one time. Such retry operations may require the management of 
queued operations that have already started execution. This attempt to retry 
the operation is rarely successful, since SCSI peripheral devices have very 
extensive automatic retry and correction mechanisms designed to be executed 
before the error information is returned in the first place. 

Since it is rare that such an operation is successful, the host software and 
operating systems should make every attempt to make available key 
information about the error which can be analyzed by the system operator or 
customer engineer. In small systems, it may be sufficient to present the 
important Sense Data together with the command that created the error. Some 
simpler systems may perform a preliminary analysis of the error information 
and generate a code or descriptive text that describes the error and 
indicates the corrective action. In very complex systems, a logging process 
may take place, allowing a customer engineer to analyze the data at some 
future time. In all systems, such information is very important for host 
program verification and for system integrity verification, even if the 
designers choose not to make the information available to any system users 
other than the design and maintenance engineers. 

The SCSI Sense Data is generally self descriptive. The errors can be mapped 
in to four major categories, each category with its own diagnostic 
procedure. 

The first category includes those errors caused by incorrect command or 
parameter bytes or by incorrect sequences of commands. These errors 
typically are presented only during the early development stages of an 
operating system or device driver, since a properly operating program will 
not generate invalid commands. 

The second category includes those sense codes associated with peripheral 
status presentation. Such  sense codes are not truly errors, in that they 
inform the host program of an unusual but not unexpected condition. Such 
sense codes include indications that a device is not ready, that the device 
has just become ready, that a device has reached the end of its media (End 
of Tape or Blank Check),  or that the expected data length and actual data 
length differed. These sense codes are normally used by the device driver to 
execute the correct operation in response to the condition. Such sense codes 
are not normally presented to the system user except as text that requests 
some action. As one example, an End Of Tape condition may require the system 
user to replace the tape cartridge. 

The third category of errors points to a particular hardware failure in the 
peripheral device or its supporting electronics. Such error conditions 
usually require the adjustment, repair, or replacement of the peripheral 
device or some of its components. In some cases, the error condition may 
also indicate possible cable or host adapter failures. These errors must be 
exposed to the system user so that the proper actions can be taken. 

The fourth category  of errors points to a media failure in the peripheral 
device. Such errors include bits that cannot be recovered from magnetic 
media and imperfections in the surface of optical media. Most such errors 
are recovered using the extensive retry and correction algorithms programmed 
into the peripheral device. In some peripheral device technologies, the 
errors may be caused by noise conditions or by marginal electronic failures 
in the read or write path. Those rare errors that cannot be recovered 
usually indicate that some data important to the operating system or 
application has been lost. The system must make this error information 
available to the system user so that the system user can replace the media 
or recover the data from a back up copy as required. In addition, logging of 
errors that were successfully recovered by the peripheral device is often 
useful as an indicator of the overall reliability of the device or of the 
requirement for periodic maintenance. 


10.4 PROBLEMS DETECTED DURING INSTALLATION

This section may be useful to correct problems related to installation. The 
information in this section is included in the Host Adapter Installation 
Guide. 

If the system will not boot from the flexible diskette drive after initial 
hardware installation the following items should be checked: 

	AHA-1540A/1542A internal diagnostics: The LED on the AHA-1540A/1542A should 
come on briefly at  system power up. If the LED begins to blink at regular 
intervals then the host adapter has detected an internal failure and should 
be returned for repair or replacement to the place of purchase. A message 
may also be posted to the screen. 

	If the AHA-1540A/1542A LED and the SCSI drive LED are always on, the SCSI 
cable's pin 1 orientation has probably been reversed between the host 
adapter and the drive. See section 3.2. 

	Is the AHA-1540A/1542A BIOS message displayed on the screen? If not, the 
AHA-1540A/1542A BIOS is not being recognized by the system. 

a) Check for BIOS address conflicts between the AHA-1540A/1542A and other 
   option boards. 
b) Try a different BIOS address. See section 3.3.
c) Change the BIOS wait state jumper. See section 3.3.

	If the HOST ADAPTER NOT FOUND AT PORT 330H message is displayed check the 
AT port address jumper setting. Also verify that the SCSI cable is correctly 
installed. A forced SCSI reset caused by an inverted or displaced internal 
SCSI cable may cause the problem. See Section 3.3. 

Problems Booting the System from a SCSI drive: 

	Make sure that both standard hard disks are mapped out of the system by 
using the AT SETUP program. 

	Make sure that the SCSI boot drive address is set to SCSI ID 0:0. Check the 
drive installation manual for information about setting the SCSI ID for that 
device. The Return Installed Devices utility in the Onboard Utilities can 
also be used to determine the SCSI addresses of peripherals on the SCSI bus. 

	Make sure that SCSI parity is consistently enabled or disabled on all 
devices on the SCSI bus. 

	Verify that the host adapter and the SCSI devices are properly configured 
and installed by referencing Section 3. 

	Power should be cycled off and on after changing any values on a HA, Setup 
program, or SCSI device to be sure that a DOS format operation has been 
successfully completed. 

	Make sure that the SCSI bus is properly terminated. 

	Make sure that the intended boot disk has an active DOS partition and a DOS 
format. See section 3.0 and the DOS manual for more information. 

Problems using a SCSI drive as drive D: with a standard hard disk as drive C:

	Make sure that the second hard disk is mapped out of the system with the AT 
SETUP program. 

	Make sure that the SCSI drive to be used as drive D:  is set to SCSI ID 
0:0. Check the drive manual for information on setting the SCSI ID for that 
device. The Return Installed Devices utility in the Onboard Utilities can 
also be used to determine the SCSI addresses of peripherals on the SCSI bus. 
 
	Make sure that SCSI parity is consistently enabled or disabled on all 
devices on the SCSI bus. 

	Verify that the host adapter and the SCSI devices are properly configured 
and installed by referencing Section 3. 

	Power should be cycled off and on after changing any values on an HA, Setup 
program or SCSI device to be sure that the new initial values are loaded. 

	Make sure that the SCSI bus is properly terminated. See Section 3. 

	Make sure that the disk has a  DOS partition and a DOS format. See section 

5.0 and the system DOS manual for more information. 

Problems using a SCSI drive as drive D: with another SCSI drive as drive C:

	Make sure that both standard hard disks are mapped out of the system with 
the AT SETUP program. 

	Make sure that the SCSI drive to be used as drive D:  is set to SCSI ID 0:1 
or 1:0. Check the drive manual for information on setting the SCSI ID for 
that device. The Return Installed Devices utility in the Onboard Utilities 
can also be used to determine the SCSI addresses of peripherals on the SCSI 
bus. 

	Power should be cycled off and on after changing any values on an HA, Setup 
program or SCSI device to be sure that the new initial values are loaded. 

	Make sure that SCSI parity is consistently enabled or disabled on all 
devices on the SCSI bus. 

	Verify that the host adapter and the SCSI devices are properly configured 
and installed by referencing section 3. 

	Make sure that the SCSI bus is properly terminated. See section 3. 

	Make sure that the disk has a  DOS partition and a DOS format. See section 
3.0 and the DOS manual for more information. 

System works erratically. Hangs or the host adapter can't always find the 
drives. 

	Check SCSI parity for consistency. 

	Check Termination.

	Check cable length and integrity.

	If host adapter and drive light remain on during a hang condition, make sure 
that the SCSI  drive conforms to the Common Command Set revision 4B. (CCS 
4B) 

	If only the host adapter LED remains on during a hang, it is probably a host 
adapter, system interface problem. The system may not be capable of First 
Party DMA transfers. Check with the System manufacturer for information. 

Adapter Command-A command transmitted to the host adapter using the 
Command/Data Out Port and the Data In Port. The commands are sequenced using 
the Control Port, the Status Port, and the Interrupt Flag Port. Abbreviated 
as IOCP command. 

AEN-See Asynchronous Event Notification

AHA-AHA-1540A-Adaptec Host Adapter for connecting SCSI devices to the PC/AT 
backplane bus. The AHA-154XA is an enhancement of the AHA-1540 (see Appendix 
C) 

AHA-1540A-The enhanced high performance Adaptec Host Adapter for connecting 
SCSI devices to the PC/AT backplane bus. 

AHA-1542A-The enhanced high performance Adaptec Host Adapter for connecting 
SCSI devices and standard IBM compatible floppy disk devices to the PC/AT 
backplane bus. 

AHA-154XA-Either the AHA-1540A or the AHA-1542A or both. 

AHA-1540A/1542A-Either the AHA-1540A or the AHA-1542A or both. 

Asynchronous Event Notification-A process by which a target can send 
unsolicited sense information to an initiator using the SEND command in 
order to inform the initiator about the occurrence of an important unusual 
occurrence. 

Asynchronous Data Transfer-Data transfer performed by the SCSI interface 
involving the interlocking of a signal to the initiator (REQ) and a signal 
to the target (ACK) such that each step of the data transfer protocol must 
occur before the next step can begin. Characterized by a low data rate and 
independence of external timing constraints, including cable length and 
circuit response times. 

AT Bus-The Industry Standard Architecture bus. 

Bus Device Reset-A SCSI message that clears all activity in the target to 
which it is addressed. 

Byte-An 8 bit unit of data. An octet. A byte is normally the smallest 
addressable unit of a memory and the unit of transfer on the SCSI. 

CCB-See Command Control Block 

CCS-See Common Command Set 

CDB-See Command Descriptor Block 

Command Control Block-A software object prepared by the host microcomputer 
software for the host adapter to provide it all the control information it 
needs to execute a SCSI command.  Abbreviated CCB. 

Command Descriptor Block-A block of information passed across the SCSI bus to 
provide the command, parameter, and address information necessary for the 
target to execute the desired functions. Prepared by the host software and 
placed in the CCB to be passed to the target by the host adapter. 
Abbreviated CDB. 

Common Command Set-A defacto standard SCSI command set for communication with 
hard disk drives. The Common Command Set (CCS) is the basis for the SCSI-2 
command set for all types of peripheral devices. 

Control Microprocessor	An integrated circuit computer used to execute the 
software that controls the host adapter's operation. 

Device Driver-A program that is linked with or attached to an operating 
system to map the software interface of the operating system to the 
requirements of attached peripheral devices and host adapters. 

DMA-See Direct Memory Access

Direct Memory Access-A mechanism that allows hardware control of the 
transfer of streams of data to or from the main memory of a computing 
system. The mechanism may require set up the host software. After 
initialization, it automatically sequences the required data transfer and 
provides the necessary address information. 

EPROM-Erasable Programmable Read Only Memory.  An integrated circuit used to 
store the host adapter firmware and the host adapter BIOS. 

FIFO-First In / First Out.- 

A queueing order in which items are removed from the queue for execution in 
the same order in which they are placed in the queue. 
An integrated circuit that buffers data in such a manner that the each byte 
placed in the buffer is removed from the buffer in the same order. 

Firmware-The software that controls and manages the host adapter. It is 
'firm' as opposed to 'soft' because it  is designed in to the host adapter 
and cannot be modified by the user. 

IBM PC/AT Compatible-Any computer system that emulates exactly the IBM PC/AT 
and that uses an ISA backplane bus. 

ISA-The Industry Standard Architecture


Industry Standard Architecture-The IBM PC/AT functions have been duplicated 
by a number of manufacturers. All the IBM PC/ATª compatible machines use a 
backplane bus that very closely emulates the function of the backplane bus 
of the PC/AT. Because of the broad usage of this bus structure, it has 
become known as the Industry Standard Architecture bus, even though there is 
no presently accepted standard for the bus. 

initiator-A SCSI device that requests an operation to be performed by another 
SCSI device (the target). The initiator provides all the command information 
and parameters required to perform the operation, but the details of the 
operation are actually sequenced by the target. 

host-A microcomputer in which a host adapter is installed. The host uses 
software to request the services of the host adapter in transferring 
information to and from peripheral devices attached to the SCSI bus 
connector of the host adapter. 

host adapter-A hardware printed circuit board that installs in a standard 
microcomputer backplane and provides a SCSI bus connection so that SCSI 
devices can be connected to the microcomputer. A host adapter is 
"intelligent" if it has a simple high-level software interface to the 
microcomputer. A host adapter is "dumb" if the microcomputer must directly 
manage the SCSI protocol using the microcomputer processor. 

Logical Unit-A physical or virtual device addressed through a target. 

Logical Unit Number-An encoded three-bit identifier for a logical unit. 

LU-See Logical Unit 

LUN-See Logical Unit Number 

Mailbox In-An area in main memory assigned by the host microcomputer software 
for communication with the host adapter. The host adapter places status and 
pointer information in entries in the Mailbox In (MBI) to indicate to the 
host microcomputer what operations have been completed or what information 
must be obtained from the host microcomputer. 

Mailbox Out-An area in main memory assigned by the host microcomputer 
software for communication with the host adapter. The microcomputer software 
places commands and pointer information in entries in the Mailbox Out (MBO) 
to indicate what operations should be started by the host adapter. 

MBI-See Mailbox In. 

MBO-See Mailbox Out. 

Multi-tasking Operation-The execution of commands in such a way that more 
than one command is in progress at the same time, allowing the system to 
take advantage of overlapping activities by using resources that are 
temporarily not required for other operations. More than one program or more 
than one portion of a program may be operating in parallel. 

PC/AT-A family of small computers sold by IBM, also called the Personal 
Computer /AT family of computers. The name is trademarked by IBM. 

RAM-Random Access Memory. Memory of which any byte can be accessed directly 
in a single memory cycle. Information can be read from and written to the 
memory. 

SCSI-Small Computer System Interface. 

SCSI ASC-SCSI Additional Sense Code. Byte 12 of the extended sense 
information. Provides a standardized description of the condition described 
by the sense information. 

SCSI Device-A device attached to a Small Computer System Interface bus 
cable. The device may be an initiator, a target, or capable of both types of 
operation. The device may be a peripheral device, a host device, or a device 
mixing both roles. 

Single Threaded Operation-Operation of the computing system such that only 
one program can be operating or active at a time. The computing system must 
wait until all resources are available before starting an operation and 
cannot start another operation until the first one is completed. No 
overlapping of latencies or program operation occurs. 

Synchronous Data Transfer-A method of data transfer on the SCSI bus 
involving clocking data on to the bus with a fixed-length fixed-frequency 
strobe pulses. The acknowledgements may be delayed several clock periods 
from the data requests. Synchronous Data Transfer can be used only for data 
transmission on the SCSI bus. It is prohibited for command, message, and 
status transmission. 

Synchronous Data Transfer Negotiation-The message exchange between the 
initiator and the target  that allows the negotiation of the data transfer 
frequency and delay between requests and acknowledgements required for 
synchronous data transfer. Once negotiated, synchronous data transfer 
parameters remain unchanged until certain reinitialization activities occur. 

Target-A SCSI device that performs an operation requested by an initiator. 
The target may be  a peripheral device performing a service for an 
initiator. The target may also be a host adapter performing a Processor type 
device service for an initiator. 

Word-A two byte (16 bit) unit of data. 

AHA-1540A/1542A MEMORY CYCLE TIMING

to see this diagram send for manual.  


STANDARD   tRR   TIMING
SPEEDS     tWW
	
5.0 MB     250     A      tARS Address Setup to MEMR Leading Edge
5.7 MB     200     A      tARH Address Hold from MEMR Trailing Edge
6.7 MB     200     A      tBRS SBHE Setup to MEMR Leading Edge
8.0 MB     150     A      tDRS Data Setup to Trailing Edge of MEMR
10.0 MB    100     B      tDRH Data Hold from MEMR Trailing Edge
                          tRW	Read Pulsewidth

SPEED   TIMING A    TIMING B  tAWS Address Setup to MEMW Leading Edge
                              tAWH Address Hold from MEMW Trailing Edge
tARS    73           23       tBWS SBHE Setup to MEMW Leading Edge
tARH    55           55       tDWS Data Setup to MEMW Leading Edge
tBRS    73           23       tDWH Data Hold from MEMW Trailing Edge
                              tWW  Write Pulsewidth
tDRS    32           32
tDRH    26           26       Note: I/O Channel Ready may slow the actual 
tAWS    73           23             transfer rate

tAWH    55           55
tBWS    73           23
tDWS    13           13
tDWH    60           60

Appendix B CONNECTOR PINOUT

Internal Connector Pin Assignments

Signal Name   Pin   Pin  Signal Name        

Ground         1     2    -DB(0)
Ground         3     4    -DB(1)
Ground         5     6    -DB(2)
Ground         7     8    -DB(3)
Ground         9    10    -DB(4)

Ground        11    12    -DB(5)
Ground        13    14    -DB(6)
Ground        15    16    -DB(7)
Ground        17    18    -DB(P)
Ground        19    20    Ground

Ground        21    22    Ground
Ground        23    24    Ground
Open          25    26    Term Power (Fused)
Ground        27    28    Ground
Ground        29    30    Ground

Ground        31    32    -ATN
Ground        33    34    Ground
Ground        35    36    -BSY
Ground        37    38    -ACK
Ground        39    40    -RST

Ground        41    42    -MSG
Ground        43    44    -SEL
Ground        45    46    -C/D
Ground        47    48    -REQ
Ground        49    50    -I/O

External Connector Pin Assignments

Signal Name   Pin   Pin   Signal Name
Ground         1     26    -DB(0)
Ground         2     27    -DB(1)
Ground         3     28    -DB(2)
Ground         4     29    -DB(3)
Ground         5     30    -DB(4)

Ground         6     31    -DB(5)
Ground         7     32    -DB(6)
Ground         8     33    -DB(7)
Ground         9     34    -DB(P)
Ground        10     35    Ground

Ground        11     36    Ground
Ground        12     37    Ground
Open          13     38    Term Power (Fused)
Ground        14     39    Ground
Ground        15     40    Ground

Ground        16     41    -ATN
Ground        17     42    Ground
Ground        18     43    -BSY
Ground        19     44    -ACK
Ground        20     45    -RST

Ground        21     46    -MSG
Ground        22     47    -SEL
Ground        23     48    -C/D
Ground        24     49    -REQ
Ground        25     50    -I/O

Appendix C	AHA-1540/1640 FAMILY COMPATIBILITY INFORMATION

Brief summary of board characteristics:

AHA-1540:

High performance SCSI to ISA Bus Master host adapter. Most revisions support 
synchronous data transfer. Separate user's manual. Subset of AHA-154XA 
Adapter Commands available. 

W AHA-1542A:	

High performance SCSI to ISA Bus Master host adapter. Supports synchronous 
data transfer. Supports floppy disk drives. Higher level of host adapter 
integration. 

AHA-1542A:

High performance SCSI to ISA Bus Master host adapter. Supports synchronous 
data transfer. Supports floppy disk drives. Higher level of host adapter 
integration. Improved SCSI connection pattern and jumper controls. Supports 
Target Mode operation. 

AHA-1540A:

High performance SCSI to ISA Bus Master host adapter. Supports synchronous 
data transfer. Does not support floppy disk drives. Higher level of host 
adapter integration. Improved SCSI connection pattern and jumper controls. 
Supports Target Mode operation. 

AHA-1640:

Very high-performance SCSI-to-Micro Channel Bus Master host adapter. 
Supports synchronous data transfer. Does not support floppy disk drives. 
High level of host adapter integration. Supports Target Mode Operation. See 
Adaptec's AHA-1640 User's Manual for details, including POS management, 
differences in interrupt presentation, differences in reset management and 
improvements in Adapter commands. 

COMPATIBILITY CHART

Function                  1540      W1542A      1542A      1540A      1640
Floppy Disk Controller      No        Yes        Yes         No         No
Synchronous Transfer        No        Yes        Yes        Yes        Yes
Selectable DMA Speeds       No        Yes        Yes        Yes        POS
Programmable DMA Speeds    Yes        Yes        Yes        Yes        Yes
Internal SCSI Connectors Straight    Rt Angle   Rt Angle   Rt Angle   Straight
Scatter Gather              No        Yes        Yes        Yes        Yes
64 Head BIOS              Option      Yes        Yes        Yes        Yes
16 Head BIOS               Yes         No         No         No         No
LED Connector               No        Yes        Yes        Yes        Yes
Target Mode                 No         No        Yes        Yes        Yes
LA 17-19 Jumper            Yes        Yes         No         No         NA
Micro Channel               No         No         No         No        Yes
PC/AT                      Yes        Yes        Yes        Yes         No

NG B  tAWS Address Setup to MEMW Leading Edge