AHA-1540/42B INSTALLATION GUIDE


HARDWARE INSTALLATION

The Adaptec AHA-154XB AT-to-SCSI Host Adapter has been designed to operate 
as shipped in the majority of AT class computers.  The Host adapter's 
factory default settings should remain in their original positions.  The 
AHA-154XB is shipped with the following settings:

SCSI Address                    7
SCSI Parity                     Enabled
Terminators                     Installed
Terminator Power                Supplying
Synchronous Negot.              Disabled
DMA Channel                     5
Interrupt Channel               11
AT Port Address                 330h
AT Bios Address                 DC000H, Enabled
Bios Wait State                 0, Disabled
FD Controller                   Enabled (AHA-1542B)
DMA Transfer Speed              5 MB/second
Auto Sense                      Enable

TO PERFORM INSTALLATION:

TURN OFF POWER TO THE SYSTEM AND EXTERNAL EQUIPMENT.

Remove the cover of your AT personal computer to expose the AT bus slots.

Locate an unused AT expansion slot in your AT system.  AT type slots can be 
recognized by the fact that they have 2 edge connectors, one 62-pin and the 
other 36 pin.

Remove the corresponding system expansion slot cover by turning the screw 
that secures it from the top counter-clockwise.

Align the AT I/O Bus Connector on the bottom of the AHA-154X into this AT 
slot.  Use the screw from the corresponding expansion slot cover to secure 
the AHA-154X's bracket to your AT system frame.

The SCSI bus must also be terminated correctly to ensure proper operation.  
The first and last physical SCSI devices on the SCSI cable must have 
terminators installed.  All other SCSI devices must have terminators 
removed.  

The SCSI factory-installed Bus terminators on the AHA-154X should be removed 
if and only if you attach SCSI devices to both an internal and external cable
since the internal and external cable SCSI connectors are the same SCSI Bus.
                                                             
Attach the SCSI Bus to the host adapter and the peripherals, using either 
the internal or external connector, making sure that pin 1 orientation is 
maintained throughout the bus.

If the host adapter is not the first or the last unit on the cable, remove
the SCSI terminators from the board.

Reassemble the system in the reverse order.

JUMPER CONFIGURATION REFERENCE 

Five sets of jumpers are located on the board to configure user-selectable 
options.  Jumpers installed at the factory are shown as "(x)".  Those not 
installed are shown as "o".  It should not be necessary to change the
jumper settings.

J5-GENERAL CONTROL
Pin  1  2  3  4  5  6  7  8  9  10  11  12  13
     o  o  o  o  o  o  o (x) o  (x)  o   o   o

o  1 - Synchronous Transfer negotiation enable.
o  2 - Diagnostics (used only at Adaptec).
o  3 - SCSI Parity disable.

o  4  o   (x)   o   (x)   o   (x)   o   (x)  - SCSI Address ID 
o  5  o    o   (x)  (x)   o    o   (x)  (x)    (SCSI disks should be
o  6  o    o    o    o   (x)  (x)  (x)  (x)    set for ID 0 and 1)
   ----------------------------------------
      7    6    5    4    3    2    1    0 

o  7  o  (x)   o   (x) - DMA Channel Select
x  8  o   o   (x)  (x)   See also jumper J9 
   -------------------
      7   6    5    0                       

o  9  o   (x)   o   (x)   o   (x) - Interrupt Channel Select.
x 10  o    o   (x)  (x)   o    o    See also jumper J9
o 11  o    o    o    o   (x)  (x) 
      ---------------------------
      9   10   11   12   14   15                             

o 12   o   (x)   o   (x) - DMA Transfer Speed
o 13   o    o   (x)  (x)   in MB/sec. 
       ------------------                    
      5.0  5.7  6.7  8.0                       


J6-BIOS/Auto Sense Control
Pin  1  2  3  4  5   
    (x) o  o  o  o   

1 - BIOS Enable.
2,3,4 - Not Used.
5 - Auto Sense disable

J7-ADDRESS SELECTION
Pin  1  2  3  4  5  6  7  8
     o (x) o  o  o  o  o  o

o  1 - Floppy Secondary Address select (AHA-1542B only).

x  2   o   (x)   o   (x)   o   (x) -  AT I/O Port Address Select
o  3   o    o   (x)  (x)   o    o    in Hexadecimal
o  4   o    o    o    o   (x)  (x)   
      ----------------------------
      334  330  234  230  134  130 
     (Note: The host adapter bios is "hard coded" to 330H)

o 5   o   (x)   o   (x) - BIOS Wait State Select
o 6   o    o   (x)  (x)   in nanoseconds 
       ------------------                       
      0   100  200  300

o 7   o    (x)    o    (x)   - BIOS Base Address Select
o 8   o     o    (x)   (x)   in Hexadecimal 
    -----------------------
    DC000 CC000 D8000 C8000

J8-FLOPPY DISK SELECTION (AHA-1542B only)
Pin  1   2   3   4   5   6   7  8 
    (x) (x)  o  (x)  o  (x)  o  o

1 - Floppy enable
2,3 - DMA Request 2 or 3 select
4,5 - DMA ACK 2 or 3 select
6,7 - INT Request 6 or 10 select
8 - Dual Speed enable

J9-DMA/INTERRUPT SELECTION
Pin  1  2  3  4  5  6  7  8  9  10  11  12  13  14
     o (x) o  o  o (x) o  o  o   o  (x)  o   o   o

o  1 - DMA Request 0 Select
x  2 - DMA Request 5 Select
o  3 - DMA Request 6 Select
o  4 - DMA Request 7 Select

o  5 - DMA ACK 0 Select  
x  6 - DMA ACK 5 Select
o  7 - DMA ACK 6 Select
o  8 - DMA ACK 7 Select
 
o  9 - INT Request 9 Select
o 10 - INT Request 10 Select
x 11 - INT Request 11 Select
o 12 - INT Request 12 Select
o 13 - INT Request 14 Select
o 14 - INT Request 15 Select

                                                                               
SOFTWARE INSTALLLATION 

Copy the files from the ASW-1410 Program diskette to the root directory of 
drive C using the MS-DOS COPY command.  In order for the ASPI MS-DOS Manager
files to be loaded whenever the system is booted, the CONFIG.SYS file must 
contain the following DEVICE=commands:

DEVICE = ASPI4DOS.SYS
DEVICE = ASPIDISK.SYS

Using any ASCII file editor, add the individual device driver commands to an 
existing CONFIG.SYS file, or follow the Instructions in the MS-DOS Operations
Reference Manual to create a new CONFIG.SYS file.  FAILURE TO LOAD ALL THE
DEVICE DRIVERS IN THE CORRECT ORDER, CAUSES THE PROGRAM TO NOT BE INSTALLED. 
The following command line options may be added to the device drivers in the
CONFIG.SYS file.  (Refer to the User's Manual for details).

DEVICE = ASPI4DOS.SYS (/D) (/P<port address) (/L) (/V) (/W) (/X<speed>)
(/N<bus on time>) (/F<bus off time>) (/I).

MS-DOS provides access to physical hard disk drives C and D.  You must use 
the MS-DOS FDISK and FORMAT programs for drives C and D.  DO NOT use AFDISK
with drive C and D.  To use a hard disk partitioned by AFDISK as drive C or 
D, you must use AFDISK to delete the partitions, and then use MS-DOS FDISK
to create new partitions.

When starting AFDISK program, it must be run from the root directory of 
drive C or the AFDISK directory if an AFDISK directory was created.  When
ready, type:
                  
             AFDISK (at the DOS prompt)

and press ENTER.  The AFDISK utility is menu driven.  Follow the directions 
on the screen to partition and format the selected SCSI devices.  The AFDISK
utility also includes an on-line HELP file which is accessed by pressing the 
F1 key.  The AFDISK may be exited at any time without executing by pressing 
the ESC key and being careful to choose the selections that do not write to 
or format the disk.

When the SCSI device(s) are successfully partitioned and formatted, reboot 
the system.  This saves any changes made and allows use of the newly 
installed disk(s) or partition(s).
  
                           
TERMINATION
 
The SCSI bus must be terminated correctly to ensure proper operation.  The 
first and last physical SCSI devices on the SCSI cable must have terminators
installed.  All other SCSI devices must have terminators removed.  The AHA-
154XB host adapter is usually the first device on the SCSI Bus and has 
terminators installed at the factory.
  (x)  - SCSI Address ID 
o  5  o    o   (x)  (x)   o    o